PRINTBUF - Version 1.12

                            RepoWare Associates
                         Jeff Howe and Dana Nowell
                                  12/9/86


    Introduction
    ------------

    PrintBuf is a simple resident program that may be used to intercept
    characters bound for the printer via the BIOS printer interrupt, and
    forward them to the printer in the background.  It is intended for
    use with programs that do not implement background printing on their
    own, and we have found it to be particularly useful when used with
    editors and word processors.  Most programs use the BIOS
    interrupt, and PrintBuf has been tested with IBM's Personal
    Editor II, the Smart Wordprocessor, DOS print command and
    programs that use DOS LPT1 or PRN drivers.

    PrintBuf was designed for operation on MS-DOS and PC-DOS computers.
    It is distributed with its assembly language source for the
    edification of anyone foolish enough to want to muck around in it.


    History
    -------

    We consider PrintBuf to be essentially a Q-and-D hack that got out
    of hand.  The guts of the program were taken from a background
    printer program used in conjunction with a commercial package, with
    the intent of providing our editor (IBM's Personal Editor II) with
    the ability to print documents in the background without having to
    drop to DOS to use DOS's print.  Much to our surprise, the program
    (nearly) worked the first time out; and as a bonus, did not degrade
    system performance as DOS's print does on most 8088/8086 machines.
    In the true spirit of code-flinging, more features were added
    gradually and haphazardly.  In its current incarnation, we consider
    PrintBuf to be far from perfect; however, we (and the rest of our
    development staff) use it every day and find it to be quite useful.


    Description
    -----------

    PrintBuf, when installed, sits on BIOS interrupt 17h, intercepts
    any characters bound for the printer and buffers them in its own
    internal buffer.  On each timer tick (BIOS interrupt 1Ch), the
    print buffer code gains control and attempts to send a fixed
    number of characters to the printer via the BIOS code.  This fixed
    number is called the burst count.  Each character so sent will be
    attempted a fixed number of times per timer tick (retry count).
    If a character may not be successfully sent in that many retries,
    the interrupt handler code will relinquish control until the next
    timer tick.

    All three of the critical parameters (buffer size, burst count and
    retries count) may be during installations, and burst count and
    retries can be set after installation.  In addition, several
    additional operations may be performed after installation.  These
    are:

         - the ability to kill the print buffer's current contents

         - the ability to turn on and off the print-screen function

         - the ability to temporarily pause forwarding of characters
           to the printer


    Operation
    ---------

    PrintBuf may be installed using the following command lines
    (Minus signs may be used in place of slashes in the switches):

         PrintBuf /i

    or

         PrintBuf [/s<size>] [/b<burst count>] [/r<retries>] [/p]

    where the command switches mean the following

         i           = install, using defaults of buffer size = 32K,
                       burst count = 20, retries = 10, print screen OFF
         size        = number of bytes to reserve for print buffer
                       (max = 63000 approx.)
         burst count = number of chars to print per timer tick
                       (max = 100)
         retries     = number of times to retry printing a single char
                       (max = 200)
         p           = print screen toggle (disable shift-prtsc on/off)


    Default values will be used for any parameter not explicitly stated:

         - buffer size = 32K

         - burst count = 20

         - retries = 10

         - print screen is OFF

    These defaults are generally reasonable; if you run into slow system
    response during printing, try setting the burst count or the retries
    to lower values.

    If PrintBuf is run with no arguments before installation,
    instructions will be printed to the console.

    We suggest that you install PrintBuf in your autoexec.bat file, and
    note that PrintBuf will work well with DOS's print only if you
    install PrintBuf before you install print.

    After installation, PrintBuf may be run using the following command
    line:

         PrintBuf [/b<burst count>] [/r<retries>] [/k] [/h] [/p]

    where the command switches mean the following

         burst count = number of chars to print per timer tick
                       (max = 100)
         retries     = number of times to retry printing a single char
                       (max = 200)
         p           = print screen toggle (allow shift-prtsc on/off)
         k           = kill data in print buffer
         h           = on/off print buffer hold status

    PrintBuf will print a report to the console that includes current
    parameter settings, as well as the current count of characters in
    the print buffer.


    Problems
    --------

    PrintBuf only works with LPT1 (at least for the present)

    The print-screen interrupt is a particurlarly nasty one, and
    PrintBuf does not interact very well with it.  We suggest that you
    disable it using the /p switch on installation.  If you can't live
    without it, wait until there are no characters in the print buffer
    before using it.

    For situations where the print buffer gets filled, a printer timeout
    is simulated by the printbuf interrupt 17h handler, which will
    probably result in a message something like

                    "Printer not ready. (Retry/Abort)?".

    If the printer is still printing characters at this point, just wait
    awhile and retry the operation.  Usually the print buffer will have
    emptied enough to resume taking in characters.


    Source Code Features
    ------ ---- --------

    PrintBuf illustrates the use of several (possibly) interesting
    MS-DOS coding techniques which could be applied to other
    applications, both resident and non-resident:

         - interception and handling of system interrupts

         - set up of a terminate and stay resident program

         - user of a DOS user interrupt (int 69h) to provide
           communication between installed code and a currently
           running process

         - use of the BIOS timer tick

         - assembly language command line parsing


    Distribution and Support
    ------------ --- -------

    PrintBuf is provided to you as a freebie - use it as you will,
    distribute it to others - just don't sell it.  Feel free to modify
    or cannibalize the code for your own use, but be aware that the
    authors will be releasing upgrades as time permits - do us the
    courtesy of letting us keep our own version numbering sequence (i.e.
    don't go releasing Version 1.13 on us).

    Because this is a public domain package, we will not provide
    substantial support for PrintBuf.  However, the authors have been
    known to frequent the following BBS systems:

         Northern Lights BBS : 202-766-2467
         DataBit BBS         : 703-370-9832

    and if you leave either of us a message on one of these boards, we
    will do our best to get back to you.  We welcome your comments and
    suggestions.