E&l0O(0U(s0p12h10v1s0b8T


                                     CLASER
                                  Version 2.03

                                 GRAHAM SYSTEMS


                             Hewlett Packard LaserJet

                             RESIDENT CONTROL PROGRAM



















                         Table of Contents

                   CHAPTER                           PAGE

                        CLASER                         i
                   1.   Installing Cartridge Control   1
                   2.   Starting CLASER                4
                   3.   CLASER Main Menu               7
                   4.   CLASER Help                    9
                   5.   Primary and Alternate Fonts   10
                   6.   Selecting Cartridge Fonts     12
                   7.   Selecting Font Attributes     14
                   8.   Resetting the LaserJet        15
                   9.   Graphic Print Screens         16
                   10.  Translation Functions and
                        Epson FX Emulation            18
                   11.  Switching Fonts In Text       23
                   12.  Port Redirection              25
                   13.  Miscellaneous Functions       27
                   14.  Exiting CLASER                29
                   15.  Things That Can Go Wrong      30






















                                         CLASER
                                 Hewlett Packard LaserJet
                                 Resident Control Program

                           CLASER is a control program written for
                   the IBM PC and PC compatible machines to
                   control the Hewlett Packard LaserJet printer.
                   It overcomes some of the problems of using the
                   LaserJet and allows users to get their money's
                   worth out of a fine machine. CLASER was written
                   in an attempt to make use of some of the
                   features of the LaserJet and to make selection
                   of these features convenient. It also was
                   designed to make existing software written to
                   support the Epson FX printer series compatible
                   with the LaserJet without modifying software or
                   patching complicated printer tables.

                           CLASER is a resident program, which
                   means that it attaches itself to DOS and in
                   effect becomes an extension of DOS. Since it is
                   resident, the program only has to be executed
                   once at the beginning of a session and it will
                   continue to be available as long as the PC is
                   left on and the the PC is not re-booted. CLASER
                   is accessible by pressing the Alt and the left
                   shift key and holding them down and tapping the
                   L key. (L for LaserJet).



                                    <i>







                           CLASER is a pop-up screen program which
                   allows you to stop an ongoing program and call
                   up the CLASER menus. The menus disappear when
                   you are finished with them and the program you
                   were in restarts as though it never heard of
                   CLASER. The CLASER pop-up menus are always
                   accessible to you, even when in a LOTUS 1-2-3
                   spreadsheet. You can control you LaserJet and
                   thereby maximize your investment.

                           CLASER offers several different
                   features. It offers font selection supporting
                   15 font cartridges through the use of the
                   CLFONT program. CLASER gives control over your
                   printer ports allowing you to direct printer
                   output from LPT1: and LPT2: to any other port
                   or the serial ports. This feature allows you to
                   shift easily from any printer attached to your
                   PC to the LaserJet and back again. CLASER
                   allows control over such features as lines per
                   inch and margins. It allows the LaserJet to
                   print in 66 lines per page mode. CLASER allows
                   you to access the Raster Graphics built into
                   you LaserJet by giving you the ability to
                   perform graphics screen dumps much faster than
                   the DOS GRAPHICS.COM program could dump to an
                   Epson printer.

                           One of the most important features of
                   CLASER is its ability to emulate an Epson
                   printer. The LaserJet is a good printer, but
                   most software was written first for the Epson
                   printers. Getting software to work with any
                   other printer very often involves making
                   complicated patches to the printer tables or
                   buying expensive printer driver upgrades. If


                                    <ii>







                   you own a LaserJet you need CLASER even without
                   the Epson emulation, but the Epson Emulation
                   feature can save many times over the price of
                   CLASER in software upgrades. CLASER will allow
                   your Epson based software to work immediately
                   and without fuss with the LaserJet.

                           An important feature of CLASER is the
                   abaility to include a font change flag in any
                   text file using ordinary editors or word
                   processor systems. This is done through the
                   use of the tilde character (~) in combination
                   with a font number.

                           The manual which follows goes into
                   detail on how to use CLASER. I would suggest
                   you read chapters 1 and 2 and save the other
                   chapters for later. Try out CLASER and
                   experiment with the menus. I think that you
                   will find it easy enough to use that you will
                   not need 30+ pages of documentation to make it
                   work. If you are unclear as to what a certain
                   function does, then you can read the
                   appropriate chapter in the manual. There is a
                   built in Help function in CLASER that should
                   give a good quick answer to most questions. The
                   manual is pretty much the same as the help
                   screens except that the manual goes into quite
                   a bit more detail.


                                    <iii>



                            CLASER NOW AND THEN

                   CLASER was written when I received an early
                   version of the first LaserJet. It is written
                   for this version and not any LaserJet models
                   which followed. There are still alot of older
                   LaserJets out there so CLASER is still useful.
                   CLASER was sold with moderate success from
                   mail order ads for about a year and then sat on
                   the shelf for about a year. I recently dusted
                   it off and fixed a few things that I didn't like
                   and I am putting it out as a user supported
                   product, hoping to extend its life. It represents
                   about 3 man-months of work so I hope that it
                   will be appreciated. If I receive any support
                   I will go back and enhance it. I would like to
                   add soft font support and EGA support. These
                   are very easy to add, but I will need some
                   indication that it is worth the effort. If you
                   use CLASER, please send in the registration fee.
                   If you would like to see CLASER improved, drop
                   into PC-Rockland with your modem at (914) 353-2176
                   and leave a message for Keith Graham. Shareware
                   authors have support from fewer than 1% of their
                   users. Leave me a message to let me know you are
                   out there even if you can't pay for registration.
                   Your ideas and comments are as valuable as the
                   registration fee (although I'd like both).

                                Thanks,

                                Keith P. Graham
                   


                                    <iv>








                                     CHAPTER 1
                             Installing Cartridge Fonts

                        CLASER.COM comes with Cartridge 92286B
                   installed, but most users will require another
                   cartridge option than the B cartridge. There is
                   a program included on the CLASER disk which
                   will allow the installation of any one of
                   cartridges A-H, J, L-N, P, Q, and T. These
                   cartridges are the only cartridges supported as
                   of the publication of this manual. Any other
                   cartridges can be supported by updates to the
                   system or by selecting individual font
                   characteristics.

                   * note: CLFONT.COM is available to registered
                   users of CLASER for $10.00.

                           Before installing any cartridge data a
                   backup copy of the CLASER disk should be made
                   following the instructions for using DISKCOPY
                   in the IBM PC-Dos manual. You should put the
                   original of CLASER away in a safe place.

                           Installing the font cartridge data is the
                   process of creating a new version of CLASER.COM
                   with a different name. The new version will
                   have the proper commands and the screen menu
                   for the chosen cartridge. Although you can name
                   a program anything you want it is convenient to
                   name the newly created program CLASERn.COM
                   where n is the cartridge letter of the
                   cartridge installed. For instance a CLASER
                   program with cartridge T installed could be
                   called CLASERT.COM. Instead of using the CLASER
                   command to start up LaserJet control you would
                   use CLASERT.



                                         <1>







                           To install a cartridge you would boot
                   the PC from IBM PC-Dos and put the CLASER disk
                   in drive A:. From the A> prompt you would enter
                   the command:

                     CLFONT

                   followed by a carriage return.

                           When the CLFONT program is loaded in it
                   asks three questions. It wants to know first
                   the name of the program to use as a model for
                   making the new program. Normally this would be
                   the CLASER.COM program. (If you hit enter it
                   will take CLASER.COM automatically, saving you
                   some typing.) Next the CLFONT program needs to
                   know what cartridge you will be installing. You
                   would type a T if you were installing the T
                   cartridge. Then you press enter. Last of all,
                   CLFONT needs to know the name of the new
                   program it is creating. If you like the
                   convention of adding the extra letter to the
                   end of CLASER then you would just hit enter.
                   CLFONT will then work a few seconds installing
                   the menu into the program and making a copy of
                   the program. When the DOS prompt returns CLFONT
                   is finished. If you use the DIR command on the
                   a disk you will see the program CLFONT has just
                   created.

                           CLASER is not copy protected in any way,
                   so you can copy the programs from the CLASER
                   disk anywhere you like and use them. Don't pass
                   copies out to your friends. If someone can
                   afford to pay for a LaserJet printer they can
                   spring for the cost of their own copy of
                   CLASER.

                                         <2>







                           Here is a sample CLFONT session for the
                   installation of the J cartridge.


                     A>CLFONT
                     CLFONT.COM Laserjet cartridge installation
                     Version 1.1 November 1, 1987
                     Copyright 1987 by
                     Keith P. Graham

                     ENTER PROGRAM TO COPY [CLASER.COM]:
                     ENTER FONT LETTER [A-T]:J
                     ENTER PROGRAM TO BE CREATED [CLASERJ.COM]:
                     CLFONT COMPLETE, PROGRAM SUCCESSFULLY CREATED
                     A>























                                         <3>








                                     CHAPTER 2
                                  Starting CLASER

                        CLASER is installed by typing the CLASER
                   command followed by certain parameters. CLASER
                   checks to see if it has been previously loaded
                   into memory (you can't load CLASER twice). If
                   CLASER is not already resident it then checks
                   the command line parameters. CLASER expects
                   certain things to follow the CLASER command. If
                   CLASER accepts the command line it will load
                   itself into memory and quietly wait for any
                   data destined for the printer and ship it off
                   to the LaserJet.

                           It is best to start CLASER when the PC is
                   booted up. This is done by putting the CLASER
                   command in the AUTOEXEC.BAT file. CLASER.COM is
                   about 30,000 bytes and should fit on a IBM
                   PC-Dos backup disk for booting purpose for
                   floppy based systems. If you have a hard disk
                   the CLASER program should be either on the
                   root, or preferably in a Dos or utility
                   subdirectory which is on the path. CLASER does
                   not have to be present on the current
                   subdirectory in order to install itself in
                   memory, just on the path. If Sidekick is to be
                   used it must be installed after CLASER.

                   NOTE: CLASER requires IBM PC-Dos 2.0 or better
                   to run.






                                         <4>







                           The command line containing the CLASER
                   command must have either a 1, 2, or an N
                   corresponding to the serial port where the
                   LaserJet is installed. The command line CLASER
                   1 would indicate that CLASER will redirect
                   LPT1: to COM1:. CLASER 2 indicates that CLASER
                   will redirect LPT1: to COM2:. CLASER N
                   indicates that the CLASER program will do no
                   redirection of serial ports. you must have
                   either a 1 2 or n or CLASER will give you an
                   error and not install itself in memory.

                           If the CLASER sound effects become
                   annoying they can be turned off by including
                   the character q on the command line after the
                   port number.

                           Here are examples of two AUTOEXEC.BAT's
                   which install CLASER (among other things).

                           For a floppy based system with 2 disk
                   drives:

                       ECHO OFF
                       CLS
                       REM 2 disk drive autoexec.bat
                       PATH A:\;B:\
                       DATE
                       TIME
                       REM install CLASER with no redirection
                       CLASER n







                                         <5>







                           For a Hard disk based system with
                   subdirectories for DOS, Batch files, Utilities
                   and Sidekick.

                     ECHO OFF
                     CLS
                     REM Hard disk based autoexec.bat
                     PATH C:\DOS;C:\UTIL;C:\BATCH
                     REM install all memory resident utilities
                     REM before Sidekick
                     REM resident program for clock card
                     SETCLOCK
                     REM make the print spooler resident
                     REM CR is a file created with EDLIN which
                     REM has nothing but one blank line.
                     PRINT <CR
                     REM install CLASER for COM1: quiet mode
                     CLASER 1 Q
                     REM initialize COM2: for another serial printer
                     MODE COM2:1200,E,7,1
                     REM install Sidekick last
                     CD \SK
                     SK
                     CD \
                     CLS
                     ECHO AUTOEXEC.BAT COMPLETE
                     VER













                                         <6>








                                      CHAPTER 3

                              CLASER and the Main Menu

                        After CLASER has been made memory resident
                   it is possible to access the functions of
                   CLASER by pressing the key combination of
                   Alt-Left Shift and the letter L. Press the Alt
                   key and the left shift key (the left shift key
                   is on the left and for the purposes of CLASER
                   is different from the right shift). Hold both
                   the keys down and tap the L key. The CLASER
                   menu should appear with a cheery bloop sound.
                   Sometimes CLASER will not appear and the reason
                   is, either it isn't installed, or the program
                   that you are running is using the Alt-L
                   sequence for its own purposes. Some programs
                   such as MultiLink do not recognize the
                   combination of Alt and Shift and will not allow
                   CLASER to start. If you exit the program you
                   can use CLASER. In most word processors which
                   use Alt-L you can usually exit to one of the
                   menus and use CLASER there. CLASER's main menu
                   will normally appear whenever the Alt-Left
                   Shift-L sequence is pressed no matter what
                   program is running at the time.

                        Almost all CLASER functions are controlled
                   by using the function keys. The function keys
                   are listed down the left of the menu and the
                   function they control are on the right. Many
                   function keys will give a sub-menu from which
                   to select a function by use of the function
                   keys. The function keys always apply to the
                   most recent screen, even though new menus


                                         <7>







                   appear, the most recent one is the one that
                   applies.

                         If you select an option, an asterisk (*)
                   appears next to the function. In many cases the
                   asterisk will go away if you leave CLASER or
                   select another option. For instance, that
                   cheerful bloop is annoying to many people (I
                   can't imagine why) and can be toggle off. If
                   you press F6 from the CLASER main menu, the
                   sound will no longer be heard, and an asterisk
                   will appear next to the F6 indicating that the
                   sound is toggled off. If you hit F6 again, the
                   sound will come back and the asterisk will
                   disappear.

                         Hitting the Esc key or F10 will exit you
                   back to your program.




















                                         <8>








                                      CHAPTER 4

                                    CLASER HELP

                           Pressing the F1 key from the CLASER
                   main menu gives a series of help screens. The
                   help screens cover in a very brief way some of
                   the information contained in this manual and
                   the Hewlett-Packard LaserJet manual. The help
                   is not designed to be a replacement for the
                   hard copy documentation, but it acts instead as
                   a quick reference and a tutorial on certain
                   topics. In addition to general help, the help
                   screens have a listing of the LaserJet error
                   codes that you may encounter. It does not
                   include the error codes that are written on the
                   front of the LaserJet itself and it does not go
                   into detail as to possible causes or fixes for
                   error codes.

                           Help screens are too big to fit on 40
                   column displays and will not appear on them. If
                   you are in 40 column mode and wish to have help
                   you must return to an 80 column mode before
                   help will work.












                                         <9>







                                      CHAPTER 5

                            Primary and Alternate Fonts

                         On main menu options F2 and F3 a window
                   will come up and ask your preference as to
                   which font the selections will apply to,
                   primary or alternate. This question applies to
                   the LaserJet's ability to use 2 fonts a once
                   and shift back and forth between them without
                   resetting any of the other characteristics of
                   the printer. The main font is called the
                   primary font and the font that you can switch
                   to is called the alternate font. You usually
                   will want to make changes apply to the primary
                   font.

                         You can switch between primary and
                   alternate fonts (after they have been set) by
                   using characters shift-in and shift-out (SI and
                   SO). These characters are usually imbedded in
                   the text to be printed by the word processor.
                   On the Epson SI will start condensed print
                   mode. (in Lotus 1-2-3 it is the setup string
                   015). On the Epson SO will start enlarged print
                   mode.

                         On the LaserJet the SI and SO characters
                   are used to flip back and forth between
                   selected fonts. SO begins the alternate font
                   and SI returns to the primary font.







                                        <10>







                         There is one warning concerning the
                   selection of fonts. If you select 2 fonts which
                   are incompatible with one another (eg. primary
                   font landscape and alternate font portrait)
                   then one font will default out. The LaserJet
                   tries to make the best fit of the attributes
                   you want to the attributes it can give you, and
                   some of the attributes must be the same for
                   both fonts (such as orientation). If the
                   LaserJet cannot give the combination of
                   characteristics which you requested, it will
                   cause the incompatible characteristics to
                   default to the last valid selection.

                          The following are the various ways of
                   encoding SI and SO.

                       CHARACTER       HEXADECIMAL   DECIMAL
                          SI              0F          015
                          SO              0E          014

                   SO is can usually be entered as a Ctrl-O. SI
                   can usually be entered as Ctrl-N. Your word
                   processor, however, may have decided to use
                   these control codes for other purposes. You
                   must consult you word processor documentation
                   to determine the best way to enter SI and SO.

                   (Note: the LaserJet Manual will refer to the
                   alternate font as the secondary font.)








                                        <11>







                                      CHAPTER 6

                             Selecting Cartridge Fonts

                        Choices F2 and F3 from the main menu allow
                   you to choose primary or secondary font
                   attributes, the difference is that the F2
                   screen can be customized using the CLFONT
                   program specifically for the cartridge that you
                   plan on using. F2 allows the selection of any
                   of the fonts on the cartridge you selected when
                   you installed CLASER. If you see the Cartridge
                   B menu when you press F2 and you have any other
                   cartridge then you must read chapter 1:
                   Installing CLASER.

                        Only one version of CLASER can be loaded
                   into memory at one time, this is to prevent
                   memory from being loaded up with LaserJet
                   control programs to the exclusion of any other
                   program. This means that you can only specify
                   one cartridge using the F2 function. If you
                   have more than one LaserJet cartridge you can
                   only control one of them using the F2 function.
                   You must re-boot and load another version of
                   CLASER to get convenient control over another
                   cartridge. Re-booting is not practical for most
                   users. My suggestion is to install the
                   cartridge most often used as the CLASER
                   cartridge. You can then use F3 (see chapter 7)
                   to select the attributes of other cartridges
                   when you find it necessary to switch
                   cartridges. It will not be necessary to select
                   all of the attributes of the required font, and
                   most selections will take no more than four



                                        <12>







                   extra keystrokes. F3 may be slightly less
                   convenient yet the cost in terms of memory
                   usage in adding extra screens makes up for the
                   inconvenience.

                       If you have no cartridges there is no
                   reason to install a cartridge screen. The B
                   cartridge screen (which is the default) has the
                   options for selecting between the two LaserJet
                   internal fonts. Just ignore all options except
                   the landscape and portrait courier fonts.

                       Use the Escape key (Esc) to exit from the
                   font selection screen.
























                                        <13>







                                      CHAPTER 7

                             Selecting Font Attributes

                         Pressing function key F3 from the CLASER
                   main menu allows the selection of fonts by
                   attribute. This function is useful for
                   selecting very quickly a certain attribute
                   without selecting a whole font. For example, if
                   you want to use the font which is currently
                   active, but you would like to switch to a
                   landscape orientation then you could use this
                   menu rather than the font selection menu.
                   Another reason for using F3 would be to select
                   fonts which are in a different cartridge than
                   the cartridge supported by F2.

                          Font characteristics should be set in
                   the order in which they appear in the menu. The
                   LaserJet tries to give a font which is the best
                   fit to the characteristics currently selected.
                   The LaserJet's best fit is based on priorities.
                   The F3 menu is listed according to the
                   LaserJet's priorities with the most important
                   items first. Always select the font attributes
                   in the order shown working from F1 down.

                         Another reason for using the F3 function
                   would be in the cases where a font cartridge
                   overrides the default internal courier font. In
                   this case it is easy to return to the internal
                   font just by specifying the USASCII character
                   set.





                                        <14>







                                      CHAPTER 8

                               Resetting the LaserJet

                           Pressing F4 from the main menu results
                   in sending the Esc @ string to the printer. In
                   the Epson, this results in a reset of all of
                   the selected options. If CLASER is emulating an
                   Epson, Esc @ will be translated to the LaserJet
                   Esc E reset command. The two forms of reset do
                   different things to the Epson and to the
                   LaserJet.

                          When you reset an Epson it reverts to
                   its power on characteristics such as normal
                   font and 6 line per inch. When the LaserJet is
                   reset, it also reverts to its power on state.
                   The problem is that a LaserJet will also print
                   the current page if there is one and then issue
                   a page eject. The Epson does not eject the
                   page. Remember emulation does not mean that all
                   things will be the same.
















                                        <15>







                                      CHAPTER 9

                        Selecting Graphic Print Screen Modes

                         CLASER allows you to do graphic screen
                   dumps to the LaserJet. This feature can be
                   disabled, or redirected by using choice F7 from
                   the main menu. Normally pressing the PrtSc key
                   and the shift key will result in the text
                   characters on the screen being dumped to the
                   printer on LPT1:. In addition to this built in
                   feature of the PC, CLASER will allow you to
                   dump graphic output to either LPT1: or LPT2:.

                         When graphic screen dumps are enabled,
                   CLASER will sense the screen mode of the PC's
                   color graphics adaptor. If the PC is in a valid
                   graphics mode, the screen will be dumped, using
                   LaserJet raster graphics to the printer port
                   specified in the F7 menu. If the PC is not in a
                   valid graphics mode or the graphics print
                   screen function is disabled then the normal
                   print screen function takes over. (This is the
                   function which comes with your PC that only
                   goes to LPT1:.)

                         There are times when programs either
                   disable the PrtSc key or they use a
                   nonstandard way of developing graphics. If a
                   program has turned off the print screen
                   function and Shift PrtSc no longer works it is
                   still possible to dump screens, graphic or
                   text, through the us of Alt-Left Shift-P. This
                   does the same thing as pressing Shift PrtSc
                   with the exception that programs can't turn it
                   off as easily as they can turn off the Print
                   Screen function.

                                        <16>







                         Lotus 1-2-3 graphics screens are
                   developed in a nonstandard way and the print
                   screen function is disabled. Pressing the
                   Alt-Left Shift-P key combination results in a
                   text screen dump which is a because CLASER can
                   not sense that the screen is in a graphics
                   mode. In the Lotus 1-2-3 graphics screens (and
                   only Lotus 1-2-3 graphics screens!) you may
                   press the Alt-Left Shift-G combination to force
                   a screen dump. Forcing a graphics screen dump
                   allows you to dump graphic screens which were
                   not previously accessible to you. Alt-Left
                   Shift-G is not discriminating! It will force a
                   graphics dump of non-graphics screens which
                   will result in a garbled mess, both on the
                   screen and on the paper. Do not use Alt-Left
                   Shift-G unless you are certain that the screen
                   you are looking at is a color graphics screen.

                           If you use the Alt-Left Shift-G
                   combination on a text screen, be patient.
                   CLASER will return the screen to its original
                   condition when it is finished. If you just wait
                   and watch. It will be done in a few minutes.
                   Save the LaserJet output as a reminder of what
                   happens when you don't read the instructions.












                                        <17>







                                     CHAPTER 10

                                 EPSON FX Emulation

                        Option F5 on the main menu allows you to
                   toggle Epson FX emulation on and off. CLASER
                   emulates many of the functions of an EPSON FX
                   (see limits below), but assumes that only one
                   LaserJet is attached to the PC at one time. For
                   this reason, emulation takes place on LPT1:.
                   You must specify to your software that the
                   LaserJet is on LPT1:. If you have need to hook
                   up some other printer to the port normally
                   assigned to LPT1: you may use function F8 to
                   swap ports (see chapter 11).

                        The LaserJet and the Epson Fx series of
                   printers are very different pieces of hardware
                   and deep down are not compatible in many of
                   their features. CLASER tries to iron out some
                   of the very obvious differences between the two
                   types of printers, but it cannot change the
                   hardware. Certain things that the Epson
                   printers do a LaserJet cannot be forced to do.
                   Some of the functions of an Epson are
                   impractical to try and duplicate on the
                   LaserJet.

                         CLASER will try its best to duplicate the
                   functions of an Epson Fx printer, including
                   graphics with the following exceptions: CLASER
                   does not attempt to emulate the Epson's ability
                   to redefine characters. CLASER does not attempt
                   to emulate nine pin graphics. It was felt that
                   the LaserJet has much better character sets
                   than the matrix graphics characters of the
                   Epson and to have the LaserJet emulate these

                                        <18>







                   functions would be to a step backwards. CLASER
                   would have to be nearly 3 times the size that
                   it currently is, just to have room to remember
                   the combinations of characters that it could be
                   sent. Nine pin graphics is rarely implemented
                   because it is awkward to manipulate the 9 bits
                   of data. Most users will never miss this
                   function.

                         On the following pages is a list of all
                   of the Epson Functions. An X next to the
                   function means that the function is emulated,
                   an I means that the function is captured and
                   not acted upon. A P means that CLASER passes
                   the function to the LaserJet unaltered.























                                        <19>







                       CLASER        EPSON FUNCTION
                    ===========================================

                          X          Carriage return
                          P          Line feed
                          P          Form feed
                          X          Tentative n/216 line spacing
                          X          Reverse feed
                          I          Set Elite character set
                          I          Set Pica character set
                          P          Shift out
                          I          Cancel enlarged mode
                          I          Set enlarged mode
                          P          Shift in
                          I          Condensed mode cancel
                          X          Escape shift out
                          X          Escape shift in
                          X          Underline mode
                          I          Emphasized mode
                          I          Cancel emphasized
                          I          Double strike
                          I          Cancel double strike
                          I          Superscript/subscript
                          I          Superscript/subscript cancel
                          I          Mode selection
                          P          Backspace
                          X          Alternate character selection
                          X          Alternate character cancel
                          I          Internat. character Selection
                          X          1/8 line spacing
                          X          7/72 line spacing
                          X          1/6 line spacing
                          X          n/216 line spacing
                          X          n/72 line spacing
                          X          Horizontal tab
                          X          Horizontal tab set


                                        <20>







                       CLASER        EPSON FUNCTION
                    ===========================================
                          I          Vertical tab
                          I          VFU channel selection
                          I          Set vertical tab
                          I          VFU position setting
                          X          Form length setting
                          I          Skip over perforation
                          I          Skip over perforation cancel
                          X          Right Margin
                          X          Left Margin
                          I          Select printer
                          I          Deselect printer
                          I          Delete
                          I          Cancel
                          I          MSB  0
                          I          MSB  1
                          I          MSB control sequence
                          I          Download character definition
                          I          CG select
                          I          ROM cg copy
                          I          Expand printable code
                          I          Cancel expand printable code
                          I          Control code select
                          P          Bell
                          I          Paper end detector disable
                          I          Unidirectional printing
                          I          Half speed printing
                          I          Incremental printing
                          X          Initialize
                          X          Normal density graphics
                          X          Dual density graphics
                          X          Quad density graphics
                          X          Bit image selection
                          I          Bit image mode assignment
                          I          9 pin graphics


                                        <21>







                                   CHAPTER 11

                                  Port Redirection

                         Choice F8 from the CLASER main menu gives
                   you control over printer ports LPT1: and LPT2:.
                   Ports LPTn are normally assigned to the
                   parallel ports. These are the ports on the IBM
                   monochrome printer adapter and the IBM printer
                   adapter. With CLASER you can capture
                   information before it gets to the printer port
                   and send it out one of the serial ports. Serial
                   ports are usually used for communications, but
                   they can be used for printers with serial
                   interfaces. The LaserJet has a serial interface
                   and requires that the serial port communicate
                   at a speed of 9600 baud. When you start up
                   CLASER using option 1 or 2 the appropriate
                   serial port is initialized to the correct
                   speed.

                         F1 through F4 control printer port
                   reassignment to serial ports. You may reassign
                   the normal printer assignments of LPT1: and
                   LPT2: and have them go to either the COM1 or
                   COM2 serial ports. You can have both LPT1: and
                   LPT2: going to the same serial port if you
                   like.

                        F7 and F8 allow you to initialize the
                   serial ports. If you assign a printer to a com
                   port it is likely that the com port is not
                   correctly initialized to 9600 baud so that the
                   LaserJet can recognize the data being sent to
                   it. If you are using CLASER and try to print



                                        <22>







                   something and the LaserJet gives an error code
                   40 it means that the serial port was not
                   correctly initialized and the LaserJet can't
                   read the information being sent to it. You must
                   always initialize the serial port that the
                   LaserJet is attached to when you select that
                   the printer will be redirected to the serial
                   port.

                         In order to test the printer you may use
                   option F9 from the port control screen to print
                   a test line out LPT1:.

                         Option F9 and all CLASER control commands
                   expect to talk to the LaserJet using LPT1:.
                   CLASER always assumes that it is talking to
                   LPT1:. Sometimes it is necessary to have
                   another printer on LPT1: and use the LaserJet
                   on LPT2:. In these case you can use F6 to swap
                   port assignments. All that this does is
                   whenever CLASER sees data going to LPT1: it
                   makes the data go to LPT2: and vice versa.
                   (This can be used to have the PC's normal
                   screen dumps go to printer on LPT2:).

                          It should be noted that CLASER will not
                   recognize any control function, including Epson
                   emulation, on LPT2:. Use F6 to swap printers if
                   the LaserJet is to be attached as LPT2: before
                   issuing any control commands.








                                        <23>







                                     CHAPTER 12

                              Miscellaneous Functions

                         Option F9 from the main menu allows the
                   control of several diverse but handy items.
                   Normally you would use the setup abilities of
                   you word processor to control margins and lines
                   per inch using the Epson emulation features of
                   CLASER, but sometimes it is necessary to issue
                   a command to the CLASER directly to override
                   the word processing options or to do things
                   such as print ascii text files. F9 allows for a
                   a few commonly needed functions.

                         F1 sets 66 lines per page. This is useful
                   because an Epson is normally set to 66 lines
                   per page. This function is not automatically
                   set when Epson emulation begins and must be
                   specified from this screen. Since a LaserJet
                   cannot print 66 lines per page at 6 lines per
                   inch and normal margins, the lines per inch is
                   changed and the top and bottom margins are
                   reduced. This should be rememberd if any
                   subsequent printing is to be done where it is
                   expected that the printer be set at 6 lines per
                   inch.

                         F2 sets 6 lines per inch.

                         F3 sets 8 lines per inch.

                         F4 sets 12 lines per inch.





                                        <24>







                         Font selection (F2 from the main menu)
                   does not change the lines per inch, and some of
                   the smaller fonts will look much better at 8
                   lines per inch. 12 lines per inch is for when
                   you use very small fonts, but can be handy if a
                   double spaced document is to printed as single
                   spaced without altering the document.

                         F5, F6 and F7 give you three common
                   options for setting the left margin. The
                   LaserJet normally prints a document too far to
                   the left to allow room for punching holes for
                   putting documents in binders. F6 or F7 should
                   leave room for punching holes in pages without
                   ruining the document.

                         F8 gives a line feed.

                         F9 gives ejects the page. F9 is handy to
                   eject the last page of documents that get left
                   in the printer without getting up and pressing
                   the buttons on the LaserJet. I find I use this
                   function very often so I made it easy to get
                   to. Press Alt-Left Shift L, press F9 twice and
                   F10 twice and you are back to where you started
                   and the page is ejected. Use F9 when printing
                   Lotus 1-2-3 spreadsheets before using the 1-2-3
                   align option on the 1-2-3 print menu.










                                        <25>







                                     CHAPTER 13

                                   Exiting CLASER

                   Once you get into CLASER, as much fun as it is,
                   you may want to escape from the windows. Escape
                   will always get you out of any situation. Hit
                   escape a few times and you will exit CLASER.
                   You must back out the way you got in. CLASER is
                   3 screens deep at the deepest so you would have
                   to hit escape for each menu that you passed
                   through to get where you are. F10 will
                   sometimes work to exit you from the current
                   menu, but some menus require that F10 be used
                   for control functions and in these cases you
                   must use the escape key to exit CLASER.

                      REMEMBER: Don't Panic - Escape

                   It is also possible, beginning with version 2.03
                   to uninstall CLASER. This is done by pressing
                   the key combination of CTRL and K when at any of
                   the CLASER menus (not help screens). CLASER will
                   restore DOS to the condition it was in when CLASER
                   was started. This will kill any programs running
                   as well as any memory resident programs which were
                   installed after CLASER. You may want to be careful
                   about uninstalling CLASER while in another program.
                   Some files may not be closed correctly if you do
                   this. It is best to exit a program and uninstall
                   CLASER from the DOS prompt.







                                        <26>







                                     CHAPTER 14

                              Things That can Go Wrong

                         From time to time there will be problems
                   as a result of using CLASER. Most problems come
                   from compatibility problems of CLASER with
                   other software or misunderstandings as to how
                   CLASER works. Here is a list of some of the
                   common problems.

                      PROBLEM: The computer stops or "hangs up"
                   when a package is loaded in. The package never
                   hung the system before and still works fine
                   when CLASER is not loaded.
                      SOLUTION: Some packages are not very careful
                   about how they use the various methods to
                   capture characters from the keyboard. The main
                   place where this can be a problem is when
                   CLASER is run alongside of Borland's Sidekick.
                   CLASER should be loaded in before other
                   keyboard type resident programs. Sidekick
                   should be loaded in last. Check the memory
                   requirements of your program. CLASER takes up
                   about 30k of memory. Your program may be
                   bumping its head against the top of memory. If
                   you have 256K of memory or less I would suggest
                   that you buy a memory expansion board for you
                   PC.

                       PROBLEM: The Alt-Left Shift-L sequence does
                   nothing, yet I know CLASER is there.
                       SOLUTION: Some programs grab the keyboard
                   for their own uses, but they give it back when
                   they are done. Multi-Mate and some other word
                   processors use Alt-L in their program.


                                        <27>







                   CLASER is always benign and will allow all
                   other programs to have first crack at a key
                   that is typed. These programs get the Alt-L
                   first and don't pass it on to CLASER. The
                   CLASER menus will be accessible from the menus
                   in these programs and should always be
                   available from IBM PC-Dos.
                       Another possible problem is that CLASER may
                   be busy printing. CLASER will not interrupt
                   itself in the middle of Epson emulation. If you
                   interrupted a program that was printing by
                   using the Ctrl-Break key you may have confused
                   CLASER and CLASER will be waiting for some more
                   data. The Solution is to try a PrtSc an see if
                   the printer works. If it does not, try again.
                   You should not interrupt CLASER and a print or
                   graphics program while they are working
                   together.
                       CLASER will not display its main menu on a
                   graphics screen. If you are in graphics mode,
                   CLASER will know it and ignore the Alt-Left
                   Shift L sequence. Return to Text mode and
                   CLASER will work.

                        PROBLEM: When I press Alt-Left Shift-L I
                   get a clock like tick.
                        SOLUTION: The click is Sidekick getting
                   upset about CLASER. Make sure that CLASER is
                   always loaded in before Sidekick.

                        PROBLEM: I get the CLASER Main menu but F1
                   Help does not work.
                        SOLUTION: Help screens contain too much
                   information to fit on a 40 column screen.
                   CLASER will show all the other menus, but Help
                   will not work in 40 column mode. Change to an


                                        <28>







                   80 Column mode and F1 will give you the help
                   you need.

                         PROBLEM: I get graphics but they are
                   distorted. Circles look like eggs.
                         SOLUTION: The HP LaserJet is not an Epson
                   and was not designed to be Epson compatible. By
                   trying to make it Epson compatible certain
                   compromises had to be made. The differences in
                   the density of the Epson and LaserJet graphics
                   results in differences in aspect ratios. Most
                   good graphics packages allow you to adjust the
                   aspect ratio. To get good graphics out of your
                   LaserJet you will have to determine the density
                   of the graphics, the page size and the aspect
                   ratio. The vertical density of the dots on the
                   LaserJet will be the same as the Epson, that is
                   48 dots per inch. The horizontal density will
                   be different from the Epson. The LaserJet will
                   give either 50, 75, 150 or 300 dots per inch.
                   The corresponding Epson densities are 60, 80,
                   120 and 240. The Epson normal density yields
                   graphics on the LaserJet that are 20% wider.
                   CRT graphics are 6% fatter. Double density
                   graphics and high resolution graphics are 20%
                   thinner than Epson graphics. You must adjust
                   your page size, density and aspect ration until
                   the graphics looks good. This may require
                   experimentation.

                       PROBLEM: The LaserJet waits for graphics
                   but after a few minutes flashes a 20 or 21.
                       SOLUTION: The LaserJet has limited ability
                   to do graphics, especially in high density
                   modes. You have exceeded the amount of graphics
                   that the LaserJet can handle at once. You must


                                        <29>







                   use a lower density graphics or clean up the
                   graphics page. CLASER intercepts white space
                   and does not send it out to the LaserJet. You
                   will find that graphics with more white space
                   look better and print faster. One thing that
                   has cleared up a lot of the error 20 problems
                   is not using page borders in you graphics. The
                   page borders are useless and I find that it
                   limits the impact of graphics if you put them
                   in a box.
                       New LaserJets with more memory and memory
                   upgrades for the older LaserJets are becoming
                   available, and you may consider getting the
                   upgrade if you do much graphics.
                       For the time being you can press the
                   continue button on the LaserJet and continue
                   with the graphics on the next page.

                       PROBLEM: Alt-Left Shift-G gives very
                   strange results. The screen goes all screwy and
                   the LaserJet prints strange bars and lines.
                       SOLUTION: Alt-Left Shift-G is only used for
                   graphics screens such as the Lotus 1-2-3
                   graphics where Shift-PrtSc does not work. It is
                   an override type of function and will attempt a
                   graphics dump of any screen. But Alt-Left
                   Shift-G has no conscience and does not care if
                   you really do have a text screen, it treats it
                   like a graphics screen. If you wait it will
                   finish all by itself in about a minute. Please
                   don't press the Alt-Left Shift-G again unless
                   you are sure that you have a graphics screen.

                       PROBLEM: I have a text with imbedded
                   LaserJet Escape codes. When I print it I see
                   strange combinations of characters where the


                                        <30>







                   codes were placed, but the LaserJet does not
                   change fonts as I have asked it.
                       SOLUTION: When CLASER is emulating an Epson
                   it does not recognize LaserJet escape sequences
                   (just as your Epson would not recognize them).
                   You must use menu option 5 to turn off Epson
                   emulation.

                       PROBLEM: I am using a word processor that
                   works very well with my LaserJet without
                   CLASER, but prints garbled data at the top of
                   each page when I am using CLASER.
                       SOLUTION: The word processor is using
                   LaserJet escape sequences to control the page
                   and print options of the LaserJet, but CLASER
                   is trying to convert these commands and getting
                   confused. Either turn off Epson emulation using
                   CLASER menu option 5 or tell your word
                   processing package that you are attached to an
                   Epson.

                       PROBLEM: I have a graphics program which
                   works with the Epson which sends garbage to the
                   LaserJet or does not work at all.
                       SOLUTION: CLASER does not emulate 9 pin
                   graphics (which is rarely used) or downloadable
                   characters (which is used in packages such as
                   Lettrix, Sideways and a few other packages).
                   The Epson downloadable fonts feature was not
                   supported for three reasons. First, they do not
                   look good on the LaserJet and I can't imagine
                   anyone preferring them to the LaserJet
                   cartridge fonts. Second, Hewlett-Packard is
                   supporting its own downloadable fonts on the
                   new model LaserJets which are not compatible
                   with Epson type fonts. Third, supporting


                                        <31>







                   downloadable Epson fonts would have added more
                   than 60K to CLASER's size making it too large
                   for a memory resident program. I would suggest
                   that you rely on the LaserJet font cartridges
                   for extra character sets.

                       PROBLEM: Graphics come out with ragged
                   edges and broken lines.
                       SOLUTION: CLASER is trying its best to
                   emulate Epson Quad density graphics and is
                   failing. The LaserJet cannot position a dot to
                   the precision that is necessary to perfectly
                   emulate Epson Quad density graphics. The ragged
                   edges are accumulated rounding errors from from
                   your graphics package sending out multi-strike
                   lines to the LaserJet. The solution is to
                   always use low or medium resolution graphics
                   when given a choice. Packages such as
                   Select-A-Font can produced fuzzy looking
                   results in high resolution modes.

                   PROBLEM: IBM DisplayWrite 3 will not work with
                   CLASER. It gives a message telling me that it
                   doesn't have enough free memory.
                   SOLUTION: IBM DisplayWrite 3 needs all of 256K
                   to run. If you have DisplayWrite, I would
                   suggest that you buy a memory expansion board
                   for your PC.

                   PROBLEM: The CLASER menu is not available from
                   within IBM DisplayWrite word processing
                   packages.
                   SOLUTION: It's not DisplayWrite's fault, but
                   the KQE.COM keyboard enhancer. Try running
                   DisplayWrite without the KQE command (look at
                   the DW3.BAT file and make the KQE commands into
                   remarks).

                                        <32>

E