HP LaserJet Tools
                                    Rip Toren
                                     POB 674
                                Columbia MD 21045



    This is a collection of programs that have developed over time to assist
    in working with the HP LaserJet printer.  My HPLJ has no font cartridges,
    and I quickly learened it could not do the PC line drawing symbols.  

    HPFILTER
    This is a TSR (terminate and stay resident) program that I use to produce
    line drawing characters on my printer that does not have any FONT
    cartridges.  It is tied into the interrupt to the printer (17).  It looks
    for ASCII codes 179 through 223.  When these are found, a command string
    is sent to the HPLJ to produce those line grawing characters.  It will
    also BOLD (fatten) characters between an ESC 'G' and ESC 'H'. ESC 'G will
    start it, while ESC'H' or ESC'E' will terminate it. It will definitely
    screw up any output to anything other that the HPLJ if these characters
    are sent.  To turn off the filtering, simply run it a second time.

    >HPFILTER

    HPXFER
    While trying to develop the strings that HPFILTER would use, it became
    apparent that it was a pain to modify and rec assemble.  This drove the
    development of HPXFER.  

    This program will read in a standard Ascii file and send part of it to
    the printer. The file name is the only argument. If it is not found, the
    extension '.HPX' will be appended, and the open tried again. The data
    found on each line is sent until a tilde ('~') is located. Every thing
    following the tilde is treated as comment.  If the end of the line is
    found without finding a tilde, the CRLF is also sent to the printer.

    If a line is read that starts with '@' in character 1, the rest is
    assumed to be a file name. That file is opened in BINARY mode, and its
    entire content is sent to the printer.  This is usually a bit graphic
    image.

    >HPXFER LOGOSET.HPX

    ** WARNING **   It is generally a bad idea to send binary data to the
                    printer while HPFILTER is active. It will garble (transl-
                    ate) any binary values that fall within its range.
                    Probably with very poor results.








    CPAINT


    Now that there is a way to send single command lines, and binary files,
    all that is needed is a way to obtain those binary files. CPAINT (See
    PAINT) is one way to do that. CPAINT will read a PC Paintbrush
    (Zsoft/Microsoft) file (PCX or PCC) and produce up to four data files.
    Each data file corresponds to one level or plane in the image.  They are
    usually RED, GREEN, BLUE, and INTENSITY.  Each output file starts with
    the HPLJ code to begin graphics ('ESC *r1A'), with the current cursor
    location as the left margin. The file ends with an end of graphic code
    ('ESC *rB').  Each graphic line is also setup with the proper HPLJ code
    for the number of bytes of binary data. 

    The program does one special thing. As it is scanning the input, it does
    not transfer any data to the output files until a scan line has been
    located that contain a set bit.  This means that your resulting file will
    not contain white space above the image.  You position the cursor prior
    to printing for exact registration.

    >CPAINT RTLOGO.PCX YNNN

    Since the amount of information is rather massive that can be produced, a
    second argument is checked for flags. This argument will allow you to
    suppress the production of any of the planes.  The output files are named
    "PLANEx.DAT" where 'x' is a number 1 through 8. If you wish to produce
    only planes 2 & 3, the second argument would by "NYYN".  This says '(N)o'
    to planes 1 & 4, and '(Y)es' to planes 2 & 3.  When using an EGA adaptor,
    you currently get only 4 planes, so you needn't worry about the last
    four. Only enough data file are use to cover the number of planes in the
    file.

    If you draw your image in Black lines on a White background, you will
    find that all four planes conatin the same pattern.  If you use patterns,
    are different colors, you may find data in some planes, and not in
    others.

    READY - SET - GO

    Draw your image using PC Paintbrush. Crop, cut and save only the part you
    want to appear on the page. Run CPAINT to extract the planes you want to
    print. Build the rest of the commands that you want for positioning and
    line drawing, as well as any included image files into a an Ascii file.
    Run HPXFER to send that file to your HPLJ. Ta-Da. If the lines look OK,
    but the image is real trash, check to insure that HPFILTER is de-
    activated or not installed at all.

    NOTES
    HPFILTER was originally designed to work with WordPerfect 4.1. I have
    been using it now for 3 months with no problems. I have my HPLJ attached
    to LPT1.  I had to create my own character definition using the "PRINTER"
    program supplied with WP 4.1. I copied one of the character sets into my
    own name, the modified it to send the simpla Ascii for characters 179






    through 223. I also was able to obtain "BOLD" ouput by doing it on a
    second pass, and having the start string offset the printer cursor up and
    over one dot. At the end of the pass, the cursor is offset back and down
    one dot.