PRO-SET
                   An IBM Proprinter Configuration Utility
                         Version 3.3 - April 7, 1986
    
                              by Fred Willshaw
                                 207 Oak Lane
                                 Cranford, NJ  07016
                                 CIS 73075,321

PRO-SET is a utility program which may be used to send control strings to the
IBM PROPRINTER without the necessity of exiting the program you are currently
using.  It is distributed at no cost and may be freely copied and used.
Should, however, you alter the program code in anyway it is forbidden to pass
this program on to others.  If you would like to see modifications to the
current program please contact the author.

I will attempt to keep the current version on the following Bulletin Boards in
the New York/New Jersey area.  The program will be named PROSETxx.ARC where xx
will indicate the latest version number.

                 Bulletin Board          Telephone#
               ------------------      --------------
               The POLICE              (201) 963-3115
               CFONJ                   (201) 486-2956
               The GOD'S               (201) 277-6522
               Omegammon               (201) 653-3893
               The BOSS                (201) 568-7293
               Software Society        (201) 729-7410
               Wolves Den              (212) 874-6319
               Invention Factory       (212) 431-1194
               Manhattan South         (212) 432-7288 

                           PRO-SET PARAMETERS           
                           ------------------

You may either execute the program as a stand-alone DOS batch program or you
may load it into resident memory.  Both modes are accomplished by placing the
desired parameter(s) after the program name, then executing the program. These
optional parameters are:

                    PRO-SET [R=x C=x V=x K=x S=x A=xxx]

Where R=x indicates the type run you wish to perform, the two options are:

           "R" for Load into low memory and remain resident.  The program
               may be accessed by depressing the Hot-Key/Control-Key
               combination you assigned, simultaneously.  This is the default.
	   "B" indicates that you want to run as a batch DOS job and not
               remain resident.  You may also use this option even if the
               program is currently resident.

Where C=x indicates the Color mode you wish to use, the two options are:

           "C" for using the IBM C/G Adapter colors. This is the default.
           "N" for no colors, the NO COLORS option is primarily for users
               of Amber and Green High Res monitors.
            
                  Note: If you are using a Monochrome Adapter the program
                        will automatically detect this.

Where V=x is the Sound On/Off indicator for the program, the two options are:

           "Y" to get Sound warnings of input errors and invalid Drive/
               Path/File Names during the Font Load procedure.  This is the
               default.
           "N" for no sound.

Where K=xx indicates the Hot-Key to be used along with the Control-Key
           key(s) to activate the Memory Resident version.  Enter the
           hexidecimal scan code value.  If you do not assign your own Hot-Key
           PRO-SET will use the letter "P".  A partial list is shown below:

           KEY  SCAN      KEY  SCAN     KEY  SCAN     KEY  SCAN     KEY  SCAN
           =========      =========     =========     =========     =========
            A    1E        G    22       L    26       Q    10       V    2F
            B    30        H    23       M    32       R    13       W    11
            C    2E        I    17       N    31       S    1F       X    2D
            D    20        J    24       O    18       T    14       Y    15
            E    12        K    25       P    19 *     U    16       Z    2C
            F    21                                  * = default

Where S=xx indicates the Control-Key key(s) to be used along with the
           Hot-Key to activate the Memory Resident Version.  The default used
           by PRO-SET is the <CTRL><ALT> combination. Enter the hexidecimal
           total value from the following table, always enter as a two digit
           value:

                  KEY       VALUE TO ADD       EXAMPLE (using the Default)
              ===========   ============       ===========================
              Right Shift        01                           CTRL  04
              Left Shift         02                           ALT   08 
              CTRL               04                                 ==
              ALT                08                Enter total -->  0C

Where A=xxx indicates the drive, path and file name of the file you wish
            loaded as the return address, this is optional.  Construct the
            file using COPY CON: XXX, or any commonly used ASCII file editor,
            with 1 to 4 lines of up to 33 characters each.

                   Example parameter:   A=C:\SUB1\SUB2\RETURN.DAT
  
                            Installing Pro-set
                            ------------------

In order to install the program, have PRO-SET.COM in the root library or a
sub-directory in the PATH command. Then include the line PRO-SET, along with
your parameter(s), if any, in your AUTOEXEC.BAT file or issue the DOS command
PRO-SET with your requested parameter(s), if any.

When loaded as memory resident, you may gain access to the program from any
other program by depressing the Hot-Key/Control-Key combination.  The program
will then intercept the keyboard interrupt (09H) and display the program menu.

                             The Program Menu's
                             ------------------

Depressing the appropriate key(s) will send the appropriate character string
and highlight the option on the menu or present a sub-menu for additional input.
Depressing the <ESC> key will return you to the Original Program, Pro-Set Main
Menu or DOS as appropriate.

The first line, [1] LPT1: -- 3:, is used to indicate which line printer port
you want the control information send to.  The default is LPT1:.  If the port
selected is not ready an error message will be displayed.

OPTION    COMMAND FUNCTION                    WHAT HAPPENS
------  --------------------  --------------------------------------------
[A]     Set Condensed Mode    Sends <ESC> 15
[B]     Stop Condensed Mode   Sends <ESC> 18
[C]     Set 12 CPI            Sends <ESC> 58
[D]     Set Emphasized Mode   Sends <ESC> 69
[E]     Stop Emphasized Mode  Sends <ESC> 70
[F]     ONE Direction Print   Sends <ESC> 85 01
[G]     TWO Direction Print   Sends <ESC> 85 00
[H]     Set Double Wide       Sends <ESC> 87 01
[I]     Stop Double Wide      Sends <ESC> 87 00
[J]     Character Set 1       Sends <ESC> 55
[K]     Character Set 2       Sends <ESC> 54 02
[L]     Format/Reset/Envelope Displays sub-menu

   [A]  Reset Printer         Sends 24             Empty Buffer
                                    18             Cancel Condensed/Set 10 CPI
                                    <ESC> 45 00	   Cancel Underscore
                                    <ESC> 53 00    Cancel Auto Linefeed
                                    <ESC> 55       Select Character Set 1
                                    <ESC> 61 00 00 Clear Download Buffer
                                    <ESC> 65 12    6 Lines to Inch
                                    <ESC> 67 66    Set 66 Lines to Page
                                    <ESC> 67 00 11 Set to 11 Inches to Page
                                    <ESC> 70       Cancel Emphasized Print
                                    <ESC> 72       Cancel Doublestrike
                                    <ESC> 73 00     Standard Print Mode
                                    <ESC> 82       Cancel Tab Settings
                                    <ESC> 84       Cancel Sub/Superscript
                                    <ESC> 85 02    Set Bidirectional Print
                                    <ESC> 87 00    Cancel Double Wide Print
                                    <ESC> 95 00    Cancel Overscore
   [B]  Set Top of Form       Sends <ESC> 04
   [C]  Form Length (Inches)  Sends <ESC> 12 00 ## (Where ## is the value
   [D]  Form Length (Lines)   Sends <ESC> 12 ##     is the value you entered)
   [E]  Print an Envelope     Displays input screens

                                 Enter up to four lines of 33 characters for
                                 a return address, depress the <ENTER> key
            Return Address       after each line even if there is no entry.
                                 Pressing <ESC> will return you to the Main
                                 Menu.  The return address entered will be
                                 stored and displayed the next time you enter
                                 this function.  If you have no changes,
                                 depress the <ENTER> key four (4) times.  You
                                 may also preload a return address using the
                                 initial paramters outlined above (A=).

                                 Enter up to four lines of 33 characters for
                                 a mailing address, depress the <ENTER. key
            Mailing Address      after each line even if there is no entry.
                                 Pressing <ESC> will return you to the Main
                                 Menu.

                                 Next, insert an envelope into the printer,
                                 see directions below if not certain, then
            Select Size          select the envelope size type by depressing
                                 the appropriate size type - F1=Standard Size
                                 F2=Legal Size or <ESC> to return to the Main
                                 Menu.

                                 Proper placement of the envelope into the
                                 Proprinter - Slide the envelope face up,
            Positioning          top first and left side against the 
                                 LEFT EDGE GUIDE, see manual page 1-10 bottom,
                                 into the FRONT OPENING until you feel the
                                 envelope stop moving.  At this point you are
                                 ready for PRO-SET to print your envelope.

[M]     1/8" Spacing          Sends <ESC> 48
[N]     7/72" Spacing         Sends <ESC> 49
[O]     Set Normal Quality    Sends <ESC> 73 00
[P]     Set Normal Download   Sends <ESC> 73 04
[Q]     Set NLQ Normal        Sends <ESC> 73 02
[R]     Set NLQ Download      Sends <ESC> 73 06
[S]     Set NLQ Doublestrike  Sends <ESC> 71
[T]     Stop NLQ Doublestrike Sends <ESC> 72
[U]     Font Processing       Displays sub-menu

   [1]  FONTGEN Created       Indicates that file to be downloaded was
                              created by the FONTGEN program. The next sub-menu
                              is then displayed with which you indicate the
                              Drive/Path/Data Set Name of the file to be
                              downloaded.  After completion of this sub-menu
                              the file is downloaded to the active printer.
   [2]  IBM Format            Indicates that file to be downloaded was
                              created to appear as in the IBM Proprinter Manual.
                              The next sub-menu is then displayed with which
                              you indicate the Drive/Path/Data Set Name of the
                              file to be downloaded.  After completion of this
                              sub-menu the file is downloaded to the active
                              printer.
   [3]  Create a Character    Indicates that you wish to construct a download
                              character of your own.  The subsequent input
                              screen is processed as follows:
        Char Code =           Enter the character code to be downloaded in the
                              range decimal 33 to 126.
        Attribute =           Indicate the ascend/decender code 0 or 1
        <arrow keys>          Move around the grid with the arrow keys, they
                              will automatically wrap-around.
        <ENTER>               Depressing <ENTER> will reverse the pin printing
                              by toggling this pin position On or Off.
        F1 = Download         Depressing the <F1> key will download the
                              character to the active printer.
        F2 = Save to file     Depressing F2 will display a sub-menu with which
                              you indicate the Drive/Path/Data Set Name of the
                              file the character is to be saved in.  If the
                              file exists, the character will be added to the
                              end of the file, if not, a new file will be
                              created.  This file may be subsequently down-
                              loaded using the IBM file format download option.
        F3 = Clear            Depressing <F3> will clear the pin map,
                              character code and attibute from the input screen.
        <ESC>                 Escape will return you to the Primary Menu. 

>> IMPORTANT NOTE <<     After you have downloaded a font file you must
                         instruct the printer how to process the downloaded
                         font be using either option <P> SET NORMAL DOWNLOAD
                         or <R> SET NLQ DOWNLOAD.  Selection of the <U> option
                         does NOT establish the mode you wish to print in.
                         It should also be noted that if you download a single
                         character to the buffer only that character code will
                         print for character codes in the decimal 33 to 126
                         range.

                             IT WON'T WORK WITH
                             ------------------

PRO-SET will not execute, and will lock up, on a PC 3270 or PC/AT 3270 running
with the 3270 Control Program.  The Control Program simply doesn't care for
other programs taking over interrupts.  Not a friendly program at all. PRO-SET
will run properly with the Control Program in batch (R=B) mode.

If you have problems in making PRO-SET function properly, a careful examination
of the memory resident programs you are using may be in order.  Certain
combinations and sequences may cause improper execution of PRO-SET or your
other programs.  Try loading these programs in a different sequence until they
produce the proper results.  A leading offender with PRO-SET are Print Spoolers
and Keyboard Enhancers.

                      UPDATES/MODIFICATIONS/CORRECTIONS
                      ---------------------------------

Version 1.1 (01/07/86) - Added support for graphics modes 320X200 and
                         640X200.  Note that this is determined by BIOS
                         Interrupt 10H.  Some programs do not properly
                         set this value, i.e. 1-2-3 in Graphics mode.
                         Since the configuration screen cannot fit in 40
                         column modes, a beep will sound if you attempt
                         to use the program in 40 column mode.

Version 2.0 (01/21/86) - Added support for download fonts.  Depressing
                         option U will present a sub-menu requesting the
                         download font file format.  The first FONTGEN,
                         is created using the FONTGEN utilities found
                         on many Bulletin Boards.  It is well worth the
                         download to get a copy of this program series.
                         The second file format is the IBM standard
                         layout as described in the PROPRINTER Manual.
                         Another sub-menu will be displayed requesting
                         the location and name of the font file to be
                         loaded.
                         A new sub-menu has taken the place of TOP
                         OF FORM.  This is option L and will present a
                         sub-menu offering TOP OF FORM, Form length in
                         inches, Form length in lines and a Reset of the
                         printer.  The Reset is taken from the Technical
                         Reference Manual and issues an interrupt 17H
                         with AH set to a 1.  This option does not seem
                         to work on my Proprinter and as there is no
                         discussion in the Proprinter Manual of such a
                         feature, your helpful assistance is requested.
                         When changing the LPTx: option the selected
                         printer is now checked to ensure that it is
                         online.  If the printer is not available, i.e.,
                         turned off or offline, the program will notify
                         you when selecting the printer.  However, if
                         you are sending a command string and the printer
                         is unavailable, the program will sit patiently
                         and wait for you to turn on the device.

Version 2.1 (01/27/86) - Moved save of current path, FCB and DTA to Font
                         routine in order to speed up execution for 
                         non-font requests.

Version 3.0 (02/21/86) - Added ability to run as a batch program.  Allowed
                         selection for color or black/white for users of
                         amber/green high res screens.  Rewrote documentation.
                         Added screen to show how parameters are entered in
                         the event they are incorrectly entered. Converted
                         all DOS Interrupt (21H) calls to ROM BIOS calls
                         as the DOS calls were destroying the DOS stack
                         when called from a resident program.  See the small
                         print in the DOS manual !  Added ability to turn
                         sound on and off.  Fixed cursor mode on Monochrome.
                         Added ability to select the Hot-Key Combination to
                         activate the memory resident version.  Gave ability
                         to run as a DOS batch program.  Changed Printer
                         Reset routine to pass individual parameters.  Added
                         ability to set the internal drive table to specific
                         configuration requirements.

Version 3.1 (03/04/86) - Added code to determine 12 or 16 bit fat based on the
                         cluster size comments on page 122 of Peter Noton's
                         book PROGRAMMER'S GUIDE TO THE IBM PC (c) 1985. Fixed
                         problem where initial address of LPT1: was hard coded
                         and not from printer base table.  Added routine to
                         print envelopes while in PRO-SET.  Routine supports
                         Standard and Legal size envelopes.  Many thanks to
                         Ed Feins of CFONJ for putting up with my feeble
                         attempts at programming and making this update
                         possible.

Version 3.2 (03/11/86) - Deleted all references to BIOS routines, now using
                         Interrupt 21H functions 3D, 3E and 3F.  This
                         includes the drive location table parameter (D=)
                         which was removed.  Added ability to preload a return
                         address via the parameters, see A=.  While the BIOS
                         routine worked fine on Floppies and 10 Meg hard disks,
                         it had serious problems with DOS 3.1 and hard disks
                         in the 16 bit FAT category.  If and when decent
                         documentation is available on these problems BIOS
                         may reenter the PRO-SET world.  Again thanks to
                         Ed Feins and Eric Rintell for their cooperation and
                         spirit of adventure !

Version 3.3 (04/07/86) - Added ability to create, download and/or save
                         font characters you have created.  Fixed bug in
                         data set processing of drives other than current
                         drive.  Tested the INIT line reset technique shown
                         in the current issue of PC Tech Journal for reset
                         of the Proprinter.  Since it does not do a complete
                         reset the previous routine was retained.