PSU
                           Printer Setup Utility

                                Tom Peters

This document describes PSU, Versions 1.0, 1.1, and 1.2.

Version  1.1  doubled the buffer size to 2048 bytes (0800h) and  version  1.2 
does a directory of *.PSU and lists any such file on the screen.

PSU IS NOT PUBLIC DOMAIN SOFTWARE! BUT:

PSU  may  be freely distributed PROVIDED 
1. that all copyright notices are left intact, and that 
2. it is distributed with all documentation and other files included, and that
3. no charge is made other that normal media costs (<$10). 
4. all PSU datafiles (*.PSU) contain the copyright notice included with the
   sample files,  either in the ID line or the test pattern.  

The  easiest  way to implement item 4 above is to build  any  PSU 
files using the enclosed SAMPLE.PSU as its basis.

If  you find PSU usefull (I'm sure you will) please send a contribution  ($20 
suggested) to me. This will enable me to continue to write software.

Tom Peters, 2811 W. Green Tree, Glendale, WI  53209

                                  Using PSU

In order for PSU to work, you must be already able to talk to the printer. If 
it is a serial printer, you may need to issue a command like the ones below:

SETUP LPT1:=COM1
SETUP COM1:baud,parity,databits,stopbits,P

Where baud, parity, databits, and stopbits are the values appropriate to your
printer, and P is always specified. (P means "continuous retry on error").

Your computer may use a MODE command similar to the SETUP command; see your
DOS manual.

Under Concurrent DOS or CP/M-86, you may need to issue the 
appropriate PRINTER n command, where n is the printer number you will be 
using.  Also  insure that your LPRS file is set up correctly;  the LPRS  file 
accomplishes the same task as the MODE or SETUP commands. 

                                PSU datafiles

PSU ignores case in filenames.  You may enter the name of a file in all caps, 
all lowercase, or any combination.

Case IS significant in the menu,  though.  Items "c" and "C" may perhaps both 
appear, and they are different. 

You  may have one or more PSU files on a drive.  They all end in .PSU and all 
have a similar structure.  PSU must be told which file to use,  which you can 
do in any of 3 ways.





                                1



1.  DEFAULT: Copy  the  PSU file you use most often  into  DEFAULT.PSU.  The 
command to do this would look something like that below:

A>COPY OKI192.PSU DEFAULT.PSU

If PSU can find DEFAULT.PSU,  and if you invoke PSU without any filename, PSU 
will  use the data in DEFAULT.PSU without further input from  you.  The  menu 
that appears in this case will tell you what printer the DEFAULT file assumes 
you have.  Henceforth, you could enter the command below to run PSU using the 
DEFUALT data:

A>PSU

2.  SPECIFIED ON COMMAND LINE:  If you know that the file TALLY160.PSU exists 
on the current disk, you may specify that file on the command line:

A>PSU TALLY160
     -or-
C>PSU A:TALLY160

In this case, PSU will use the file TALLY160 without further input from you.

3.  SPECIFIED AT PROMPT:  If DEFAULT.PSU is not available, or you type a name 
on  the command line that doesn't exist or has something wrong with  it,  PSU 
will prompt you for the name of the file you wish to use. PSU reports that it 
couldn't  find  DEFAULT.PSU.  It  then checks to see if any other  PSU  files 
exist, and lists any it finds, and asks you to enter one of them.

Note  that PSU doesn't understand paths under MS-DOS (tm).  PSU.EXE may exist 
in any directory or drive you have a path to,  but the datafiles (*.PSU) must 
be in the current directory.

                                  THE MENU

The menu consists of the FILE ID,  the MENU CHARACTERS, and the DESCRIPTIONS. 
The FILE ID appears at the top.  It just tells you what model(s) printer this 
file is appropriate for. 

The MENU CHARACTERS are single letters/numbers/symbols along the left edge of 
the menu. Below is a line from the middle of an average menu:

C Set compressed print (16 CPI)

The  menu character above is "C",  so entering C will cause Compressed  print 
(16  characters  per  inch) to be activated.  The DESCRIPTION  in  the  above 
example  is of course "Set compressed print (16 CPI)" and describes what  the 
function does.

                                  WHEN DONE

PSU always presents the option "(CR to quit)" at the bottom of the  menu.  CR 
is  shorthand for "Carriage Return" and means press the RETURN or ENTER  key. 
This  takes you out of PSU.  If you enter the PSU menu and see that the ID at 
the  top is for a printer other that the one you have,  press CR right  away, 
rather than confuse your printer with control codes it won't understand.







                                2



                              TECHNICAL STUFF
                              ===============

                         MAKING YOUR OWN PSU FILES

1. The file is 2048 bytes long or less.
2. All data is plain ascii text. Case matters, BUT hex values may be upper or
   lower case. All hex characters are TWO characters, lead zeros if required.
3. The high bit is not ignored, so if the PSU file was created in Wordstar's
   Document mode it probably WON'T WORK. ***Fixed in version 1.2: Only menu
   descriptions need have the hi-bit clear. Hex values will evaluate correctly.
4. Item 1 in the file is a label or identifier detailing printers applicable
   and the last revision date of that particular PSU file. The label is ascii
   text and ends with "$". Example:
OKIDATA 192 & 193 PRINTERS revised 03/08/86
$
   Note  that  in  the above example,  there is an  extra  cr/lf  before  the 
   terminating   dollar-sign. If the menu gets to big for 1 screen, place the 
   "$" on the same line as the ID.
5. All remaining items are function entries, except the terminator entry.
6. A function entry consists of a backslash, the menu option letter, <SPACE>, 
   the function description, '$',hex codes, '$'. Example function entries:

\A 10 Characters/Inch$1E$
\B 12 Characters/Inch$1C$
\C 17 CPI$1D$
\D Draft Quality mode$1B 30$
\Q Correspondence Quality mode$1B 31$
7. The last item is a terminating entry: 
\$

The hex codes can be separated by any non-alphabetic character,  (except $ or 
\) or not separated at all. All of the examples below will work:

\T Short test pattern$41 42 43 44 45$
\T Short test pattern$41,42,43,44,45$
\T Short test pattern$41-42-43-44-45$
\T Short test pattern$4142434445$

Example setup file:

OKIDATA 192 & 193 PRINTER SETUP FILE 03/08/86$
\P Set 10 pitch$1E$
\E Set 12 pitch$1C$
\C Set 16 pitch$1D$
\D Go to Draft  quality$1B 30 79$
\L Go to Letter quality$1B 31 79$
\H Start Enhanced   print$1B 48$
\Z Start Emphasized print$1B 54$
\C Cancel Emphasized AND Enhanced print$1B 49$
\0 Skip no lines at bottom of page$1B 25 53 00$
\4 Skip  4 lines at bottom of page (for performation)$1B 25 53 04$
\Q Start Underlining$1B 43$
\N Stop  Underlining$1B 44$
\U Print Unidirectionaly (left-to-right only)$1B 2D$
\B Print Bidirectionaly$1B 3D$
\T Set top-of-form to current position$1B 35$
\F Feed to top of next page$0C$
\# Print a Test Pattern$41 42 43 44 45 46 47 48 49 4A 4B 4C 4D 4E
4F 50 51 52 53 54 55 56 0D 0A$


                                3



\$

In the example above, there are too many lines to fit on one screen. One line 
is saved by making the Identifier Line one line instead of two. This is done
by placing the terminating "$" on the same line. 

Setup file names all end with .PSU and are 1-8 characters long. You should make
the names as descriptive as possible. Some conventions to follow: 

1. Make the name a abbreviation of the make followed by the model number.
2. Name the file with the lowest common denominator model number. For example,
   the control codes for the Okidata 192 printer apply the the 193 as well; 
   name the file OKI192.PSU

A few notes about the content of the file:

1. Menu letters: Use all capital letters and minimize the use of symbols, if
   possible. 
2. Always include a test pattern.
3. If the file contains more than 2048 bytes (characters) of date, only the
   first 2048 bytes will be read. If options near the end of the file don't
   appear on the menu, the file may be too long.
4. It is often convenient to have \F Form feed$0C$ in the file.

PSU cares little about where carriage returns and linefeeds are. 
The only place you can't sprinkle them in is in the middle of a hex value.

                          PATCHING PSU

Those  of you who are adventurous and know how to use DEBUG can make a  few 
patches. The structure of the data area of PSU is shown below.

                   (The prompts and strings appear here)

          BUF_SIZE  EQU  0800h
read_buf       db       BUF_SIZE dup (0) ; 2048 byte disk read buffer
read_buf_end   db       0                ; address for the end of the buffer
; DEFAULT FCB- TRY TO OPEN IF NO DATA ON COMMAND LINE
DEF_FCB         db      00      ; drive code: 0=default, 1=a:, 2=B:, 3=C:, 4=D:
DFCB_NAME       DB      'DEFAULT '      ; FILENAME
DFCB_TYPE       DB      'PSU'           ; FILETYPE

You  could,  for example,  patch the byte at DEF_FCB to 01 to force PSU  to 
always look on drive A: for DEFAULT.PSU rather than the default drive.

You  should not attempt to run any of the code in PSU if you are  going  to 
patch it.  PSU plays games with CS,  DS,  and ES, so you may not be able to 
find the data. Use the default DS that DOS gives you when debug is started.

Here is a list of approximate locations in the DS. The relationship between 
them shouldn't change, tho the adresses may.

0000 PSP
0100 Stack
039E Strings
0A07 File read buffer
1208 Drive and Name of default PSU file





                                4


039E Strings
0A07 File read buffer
1208