WD1002S-WX2 Hard Drive Controller




The following information on the Western Digital Controller is for
the WD1002S-WX2 taken from the Western Digital Installation Guide.
If you need help doing a low-level format on the drive, please
leave a message in the Hard Drive Conference, Sparta PCBoard
(201) 729-7056.


The BIOS ROM is used to define individual disk drive parameters.
Currently there are two varieties of BIOS ROMs available. The
standard BIOS ROM contains a selection of four sets of drive
parameters that can be used with most existing disk drives.

In addition to this same selection of parameters, another BIOS
ROM, called Auto Config BIOS ROM, allows manual assignment and
modification of these drive parameters; has the ability to load
a drive defect list; and lets the user logically format one disk
drive as two virtual drives.

Both versions of the BIOS ROM contain four drive configuration
tables or BIOS tables as listed below:

BIOS Drive Tables contained within the following BIOS ROMS
Standard - WD62-000042-013
Auto Config - WD62-000043-010

                            Table 0
Specifications                          Drive Types
Drive Capacity  20MB                    Microscience HH725/HH325
Cylinders       612                     Tandon TM262/362
Heads           4
RWC             613(none)
WPC             613(none)
Step Rate       Option 5

                            Table 1

Drive Capacity  10MB                    Miniscribe 3012/3212
Cylinders       612             
Heads           4
RWC             128
WPC             128
Step Rate       Option 5

                            Table 2

Drive Capacity  20MB                    CDC 9415-525AT/9415-528
Cylinders       612                     Miniscribe 3425
Heads           4                       Mivil M125/M225/M325
RWC             613(none)               Seagate ST225
WPC             128
Step Rate       Option 5

                            Table 3

Drive Capacity  10MB                    Fujitsu m2233
Cylinders       306                     LaPine 3065/3512/3522
Heads           4                       Microscience HH612/HH312
RWC             306(none)               Miniscribe 2012
WPC             0 (all)                 Rodime 252/352
Step Rate       Option 5                Seagate ST412



                        SW1 Jumper Positions 1 - 4

BIOS Table      Drive 1                 Drive 0
                SW 1-1  SW 1-2          SW 1-3  SW 1-4
0               Close   Close           Close   Close
1               Open    Close           Open    Close
2               Close   Open            Close   Open
3*              Open    Open            Open    Open

*Shipping Configuration

                        SW1 Jumper Positions 5 - 8

SW 1-8  Open    Reserved for BIOS ROM
SW 1-7  Open    Reserved for BIOS ROM
SW 1-6  Open    Reserved for BIOS ROM
SW 1-5  Open    Reserved for BIOS ROM


The following jumpers cover the W1 - W7 jumper positions 

Jumper  Pin Connects    Status
W1      2-1             Normal*
        2-3             Factory Test Only

W2      2-1             Normal*
        2-3             Factory Test Only

W3      Closed          BIOS ROM Enabled*
        Open            BIOS ROM Disabled

W4      2-3             Device Address 320H*
        2-1             Device Address 324H

W5      2-1             BIOS ROM Size 32K or 64K**
        2-3             BIOS ROM Size 16K

W6      2-3             Reduced Write Current (8 heads)*
        2-1             Head Select 3 (16 heads)

W7      2-1             INTRQ to INTRQ 5 on host connector** 
        2-3             INTRQ to INTRQ 2 on host connector

* - As Shipped - Jumper is installed
** - As Shipped - Jumper is installed, Pins 1 and 2 are joined via an
                  etch on the PCB. To change, the etch must be carefully
                  cut and a jumper installed.


Step Rates 
The WD1015 Control Processor uses the CCB Option Byte to establish
the actuator step rate.  This step rate is defaulted to either 70 or
75 microseconds on the installed version of the Control Processor. It
can be modified by the Auto-Config BIOS ROM.  The control processor
is the chip located at U11 on the circuit board.

An older version of the control processor, P/N WD1015-14, supports a
maximum of 8 heads and is completely suitable for the lower capacity
ST506 type disk drives.  The default step rate is 70 microseconds.

Today's control processor, the WD1015-24, supports up to 16 heads. It
includes controller support to the DMA and Syquest removable drives.
Other differences include: it no longer performs the unnecessary
controller self-test after power-on or soft resets; the processor allows
faster step rates; and the default step rate is 75 microseconds.

The Auto-Config BIOS ROM can be used to change the step rate of either
the WD1015-14 or -24 control processors.  Table 5 lists the available
step rates for both the WD1015-14 and the WD1015-24.  Overall system
performance will be enhanced by selecting the fastest possible step rate
supported by the attached drive.

                            Table 5

WD1015-14 Step Rates
DEC     BIN     Step Rate       Comments
0       000     3 ms
1       001     3 ms
2       010     3 ms
3       011     3 ms
4       100     200 us
5*      101     70 us           Standard Buffered Seek Rate
6       110     3 ms
7       111     3 ms

WD1015-24 Step Rates
0       000     3 ms
1       001     45 us
2       010     60 us
3       011     18 us
4       100     210 us
5*      101     75 us           Standard Buffered Seek Rate
6       110     30 us
7       111     18 us

* Default value in WD BIOS ROMS