Last week I posted an erroneous copy of the following to
comp.sys.ibm.pc.  I hope the cancellation I sent out caught up
with most of the copies before they were widely received.  I
have corrected the file and I am including the original 
"cover" along with the updated file.  (The corrected version
of the source file can be identified by the comment "Corrected
version, 9/2/87, DF" on the very first line.)  A bad mail feed
prevents me from sending this to the moderator of comp.sources.
misc where it should rightfully be posted.

--------------- beginning of original posting ---------------

A couple of weeks ago Jim Margeson distributed a copy of TIME-
PARK.ASM which apparently caused a little bit of controversy.

The TIMEPARK assembly file Jim posted was originally distributed
last spring by Sandy Zelkovitz who developed it for use on his
Pro-Tech BBS.  While Sandy ostensibly placed TIMEPARK in the
public domain, he did so with some very non-public domain usage
restrictions attached (non-commercial, no money charged, etc).

While I assume Sandy would not mind TIMEPARK being distributed over
the net (he placed it on several public access bulletin boards
himself), I am sure he would be disappointed that his document
file, restrictions on use, and identifying program banner managed
to get lost somewhere along the way.

The problem I have with TIMEPARK is not its genesis--but that it
commits a cardinal sin:  it causes two end-of-interrupt codes to
be sent to the 8259A interrupt controller during the processing of
a single timer interrupt--one EOI from TIMEPARK and one from the
bios time-of-day routine.  This can cause one of those bugs that,
when it goes off, is damn near impossible to find!

As I was pondering all of this, I came to realize that what the
free-world needed was an honest-to-goodness public domain timed
head parking program that was fully commented and reasonably
understandable.  (Jim Margeson made a valiant attempt at commenting
Sandy's TIMEPARK.ASM, but he was just a wee bit off in spots! *8-)
                                        ---

So this past weekend I started thinking about all of the attributes
I would want in good timed head parking program.  Saturday night
it was written, Sunday afternoon it was tweaked unmercifully, and
Sunday night it was sanitized and commented.

TA DAAAA!!!!  Introducing . . . .  P D T I M P R K  ! ! ! ! !