ANSI.MOD Documentation 


                                  January 1989
                                  Version 1.12


                       Copyright 1988 by John H. Brooks.
                              All rights reserved.
                       Permission is granted to quote or 
              distribute copies of this documentation separately,
                 and the entire, unaltered POWERKIT II package.


    DISCLAIMER: This software is sold "as is."  No warranty is given, either 
    express or implied, that any specific POWERKIT feature will work on any 
    particular machine.  The manufacturer will not be liable for any damage 
    caused by the use of POWERKIT. 
    
    The names of hardware and software products, and companies mentioned in 
    this document are trademarks or service marks of the respective companies.

FORWARD: Welcome, let me tell you what this ANSI.MOD documentation does NOT 
    contain.  Although ANSI.MOD supports most of the ANSI X3.64 and VT100 
    "escape" sequences, not all of them will be described here.  Just remember 
    that ANSI.MOD will do the job for you, should you have an application pro-
    gram that requires VT100 emulation, or ANSI.SYS be loaded.  Also, ANSI.MOD 
    has many helpful routines that can be used by other programs, and these 
    will not be mentioned here either.  Instead, for those of you who might 
    wish to write your own "module", or to delve into the esoteric mysteries of 
    ANSI "escape" sequences, there is a technical reference manual available to 
    all registered users of POWERKIT II. 

    I have placed the "module" format for executable TSR (and device driver, 
    ANSI.MOD is the console device driver *) files in the public domain, and 
    any software developer, commercial or shareware, may use it, free of royal-
    ties.  You may also take advantage of ANSI.MOD's superior routines in your 
    programs.  There are some restrictions, and you MUST contact me for 
    approval, and for the specifics of this offer. 

WHAT IS ANSI.MOD?  ANSI.MOD performs three major tasks (the keystroke buffer, 
        with view-port, is a separate program).  First, it is a replacement for 
        the rather inadequate MS/PC-DOS console that controls your screen and 
        keyboard.  The DOS console's inadequacies are the reason every major 
        application package handles its own I/O to/from the screen and key-
        board.  Since each program handles this I/O a bit differently, you can

* - For you "techies", ANSI.MOD (when active, and it's simple to turn it on and 
    off) is the highest "CON" link in the device driver chain, is carried in 
    the "list of lists" as the console driver, takes over INT 29h duties, and 
    is the "file" that answers to "handles" 0, 1, and 2. 


Page 2 
        
        blame the poorly designed DOS console for the fact that some of your 
        favorite pop-up TSR's (terminate, but stay resident programs) don't 
        work inside some of your applications, and why some TSR's don't work 
        very well with other TSR's.  Thus, a major goal of the POWERKIT II 
        design is, at least, to get a special class of TSR's, called "modules", 
        to COEXIST amicably.  To this end, ANSI.MOD provides a set of keyboard 
        handling and screen updating routines, that are quite simply the best 
        in the business.  ANSI.MOD can replace an entire 80x25 screen, 40 times 
        a second, on a standard 4.77 Mhz PC. 

        Second, ANSI.MOD is a replacement for the equally laughable ANSI.SYS 
        that came in your DOS package.  It has a far larger set of the ANSI 
        X3.64 and VT100 escape sequences, plus a few that ANSI never heard of.  
        The commands represented by the escape sequences work under much more 
        diverse conditions than do the corresponding ANSI.SYS commands, and in 
        many instances, the same command does many more things than its ANSI-
        .SYS counterpart. 

        To cite an example, the old ANSI "keyboard redefine" sequence did 
        indeed replace one character by one or more other characters, giving 
        ANSI.SYS a "MACRO" capability, sort of.  But, the key redefinition 
        acted ONLY at the DOS prompt (well OK, in DEBUG and EDLIN too).  When 
        you entered an application, the key reverted to its former self.  ANSI-
        .MOD produces true MACROS that are available at the touch of a key, all 
        the time. 

        Furthermore, you can attach a comment or description to each of your 
        MACROS, to remind you of some important fact about them.  There is a 
        way provided to show this comment, and also a means to move this MACRO 
        to a different key (you'll see why later).

        Another feature unique to ANSI.MOD's MACROS is that ANSI escape 
        sequences can be embedded in them.  Thus, MACROS can be used to com-
        mand your communications port (dial the phone, for example), or 
        printer, or even to define (or delete!!, even themselves) other MACROS. 

        Finally, MACROS can be defined at any time, because ANSI.MOD pro-
        vides "hot" key access to the ANSI sequence parser, replacing "PROMPT 
        $e [" (ALT-ESC is the default, and FYI, all hot keys for POWERKIT II 
        modules are just special types of MACROS, the help screens for the mod-
        ules are the above-mentioned comments, and the hot key can be moved 
        just like any other MACRO).  The old, unhandy "PROMPT $e [ ... " method 
        is still available for batch file use, etc. 

        Oops, I almost forgot, an ANSI.MOD MACRO can contain sub-macros 
        (to 10 levels deep), and these are expanded when the outer MACRO is 
        being called, not when the outer MACRO is being defined.  This not 
        only saves space in the MACRO buffer, but the sub-macro(s) can be 
        ALTERED between calls to the outer MACRO.  I'm sure you will discover 
        many uses for this sophisticated capability.

        Speaking of space, ANSI.MOD MACROS use only a single byte for most key-
        strokes, except "extended" ASCII codes (these are two byte codes whose 
        first byte is 0, or E0h).  "Problem" codes (such as control codes) are 
        handled in software.  This results in a significantly larger program, 
        but the reward is, ANSI's buffer will hold almost twice as much inform-
        ation, in the same space, as some other "KEY" or "ANSI type" programs. 


Page 3

        This brings us to a second important goal of POWERKIT II, STANDARD-
        IZATION!!!.  All good word processors, spreadsheets, data "basers", 
        provide many of the same helpful operations, like SEARCH, REPLACE, 
        COPY, MOVE, DELETE, to name a few.  The only trouble is, they each use 
        different keystrokes to accomplish these tasks, and YOU have to REMEM-
        BER which keystroke combination goes with which program.  NO MORE, just 
        create a batch file for each of your programs.  The batch file will 
        create MACROS that move these operations to the same keys in all the 
        programs -- call the program -- then "uncreate" the MACROS (yep, I 
        forgot that too, you can delete MACROS) after exiting the program. 

        Lastly, ANSI.MOD is the traffic cop that mediates potential conflicts 
        between POWERKIT II modules, recognizes hot keys and calls the associ-
        ated module, disables one when another pops up on top of it (to 4 lev-
        els deep), interprets their "command" keys for them and calls the 
        proper routine, sends them keystrokes when asked, pops up their help 
        screens when F1 is pressed, provides many other useful routines (PKII-
        .MOD is several hundred bytes smaller because of these routines). 

        Now for perhaps THE most AMAZING fact about ANSI.MOD.  In its smallest 
        configuration, with a 256 byte MACRO / ANSI sequence buffer, ANSI.MOD 
        requires slightly over 5k bytes! and this leads us naturally to a third 
        important goal of the POWERKIT II design, SAVING SPACE !!!  The space 
        savings provided by the remarkable module design is described in 
        PKIIMOD.DOC, but ANSI.MOD also plays its part. 

        The three goals mentioned above are intermediate to the FINAL goal, 
        which is to SAVE MS/PC-DOS!!! (from itself, mainly).  It's just too 
        LOUSY an operating system not to need a great deal of help to survive.  
        And survive it SHOULD; consider the alternatives; multi-megabyte, 
        multi-user, multi-tasking UNIX and OS/2!  Sure, they're powerful oper-
        ating systems, but I question whether even most "power users" need 
        them.  What I believe IS needed is a communications program, a smallish 
        one, that will operate in the background, to process your Email, and 
        such (for $32, Mirror II does a decent job of that); a print spooler to 
        drive your printer in the background (PRINT comes with DOS, and is one 
        of the best I've ever seen); a small, not too sophisticated foreground/ 
        background dual-tasker that will handle a compute-intensive process 
        (like a spreadsheet re-calc) in the background, and an I/O intensive 
        task (like a word processor) in the foreground; ANSI.MOD, PKII, and a 
        few other, tiny, inexpensive, indispensable, POWERKIT II modules to 
        help you cope with DOS. 

        Well, I've spoken my piece, now let me hear from YOU (please send money 
        too).  Does this approach to Personal Computing make any sense at all 
        to you? 

INSTALLATION: Though it is far from being "just another module", ANSI.MOD can 
        be loaded (and unloaded) like all other modules, by typing:

          LOAD C:\PKII\ANSI.MOD (instructions to ANSI.MOD may go here) 


Page 4

        Of course, this assumes you have previously created the \PKII directory 
        on the "C" (or "A") drive, and copied ANSI.MOD into it.  The easiest 
        way to do this is to run POWERKIT II's "INSTALL" program (see the in-
        structions in README.1ST). 

IMPORTANT NOTE:  ANSI.MOD MUST BE LOADED BEFORE MOST OTHER MODULES !!!

        ANSI.MOD has one switch that may be set at load time (if you don't like 
        the default value, otherwise don't do a thing).  For example: 

          LOAD C:\PKII\ANSI.MOD /m100
                               ^ blank space
        
        will set aside 25,600 bytes for MACROS and ANSI sequence parsing 
        (the default is 4096 bytes). 

        * /Mn, n = 1 to 237 (approx.), tells ANSI how many 256 byte sections of
          memory to reserve for MACROS and ANSI escape sequence parsing.

    NOTE: You must reserve space, in ANSI.MOD's MACRO buffer, for module help 
        screens.  If the screen for PKII.MOD is attached, in /Mn, n must be 4, 
        or higher.  ANSI comes to you with the default set at 16 (i.e., 4k of 
        MACRO buffer space), so there's no need to worry when you first load 
        ANSI.MOD and PKII.MOD. 

ANSI COMMANDS: All ANSI escape sequence commands begin with the "escape" char-
        acter, which is a decimal 27.  The next character is almost always a 
        left bracket (a "[").  The real "meat" of the command then follows 
        those preliminaries.  As was stated earlier, ANSI commands can be ac-
        tivated from the keyboard, at any time (not just at the DOS prompt), by 
        pressing ALT-ESC (press the "ESC" key, while holding down the "ALT" 
        key).  ALT-ESC acts as the "27" and the"[".  The "meat" is either a 
        series of numbers, separated by semicolons (like 1;2;33;44), or a se-
        ries of characters, enclosed by single or double quotes (like 'abc' or 
        "abc"), plus a final upper or lower case character (must be outside of 
        any quote marks).  That final character of the sequence tells the ANSI 
        command interpreter (hereafter referred to simply as ANSI) what to do.  

MACRO RELATED COMMANDS: To a Greek (and a select few others), "macro" means 
        "large".  In computerese, a MACRO is a string of one or more charac-
        ters, that are sent to a display, a file, printed on a printer, or sent 
        to a modem, after a (single) key is pressed.  At this very moment, I'm 
        using MACROS to enter the words "ANSI.MOD" (I press ALT-2), "ALT-ESC" 
        (I press ALT-3), and "MACRO" (I press ALT-4), into this document. 

    CREATE A MACRO: The final character (mentioned above) that tells ANSI to 
        create a MACRO is lower case "p" (upper case "P" means something en-
        tirely different to ANSI).  Creating a MACRO with ANSI.MOD is almost as 
        easy as (or easier than) it is with those well-known (and costly, in 
        PRICE and MEMORY) "KEY" and "ANSI" programs: 

        The "quote" key is the key between the semicolon/colon key, and the 
        ENTER (RETURN) key. 


Page 5

        1. Press ALT-ESC (you should hear a beep)
        2. Press the "quote" key (shifted or not)
        3. Press the key to which the MACRO will be attached
        4. Press the sequence of keys you wish the redefined key to represent
        5. Press the "quote" key again (shifted or not, but the same as in step 
           two above)
        6. Press lower case p

        That's all there is to it.  You will notice ANSI's view-port will open 
        to show you the keystrokes you are typing (well not quite, it cannot 
        show non-printing codes). 

        If you need one or the other of the "quote" keystrokes in your MACRO, 
        use the other 'quote' as the delimiter.  If you need them both, end 
        one "quote" sequence, press ";", press the other 'quote', press the 
        "quote" you need, and continue. 

        If you wish an ANSI escape sequence to be part of your redefinition, 
        press ALT-ESC, followed by the ANSI sequence.  Make sure you are 
        inside the "quote" delimiters (see note below). Outside "quote" 
        delimiters, you must use "0;1" to represent "ESC [". 

    IMPORTANT NOTE: Pressing ALT-ESC a second time ABORTS an ANSI escape 
        sequence, but not if you are inside the "quote" delimiters. 

    DELETE A MACRO: To delete a MACRO, press ALT-ESC, "quote", the key to 
        which the MACRO is attached, "quote", then lower case p.  This causes 
        the key to revert to its original function.   Sorry, the only way to 
        delete all MACROS, is to UNLOAD, then re-LOAD, ANSI.  The reason for 
        this, is that all module "hot" keys are MACROS too (including ANSI.-
        MOD's), and it wouldn't be wise to delete them. 

    MOVE A MACRO: To move a MACRO to a different key, press ALT-ESC, "quote", 
        the "old" key, the "new" key, "quote", then lower case k.  Since module 
        hot keys are MACROS, this procedure will also move a module's hot key.

    MACRO DESCRIPTION: You can include a description of what the MACRO does, 
        when you define the MACRO, if you wish.  After defining the MACRO, and 
        pressing the "quote" key, but before pressing "p", press the "left 
        single quote" key, enter your description, press the "left single 
        quote" again, then press "p".  Include carriage returns (the ENTER or 
        RETURN key), when you want to start a new line, in your description. 

    SHOW DESCRIPTION: To look at this description, press ALT-ESC, "quote", the 
        MACRO's key, "quote", then lower case q.  The description will pop-up 
        on the screen, then disappear as soon as you press another key (the 
        SHIFT key, for example). 

    TURN MACROS OFF/ON:  Press ALT-ESC, "0", lower case "t" to disable all MAC-
        ROS, except ANSI.MOD's hot key.  ALT-ESC, "1", "t", turns them back on. 

    IMPORTANT NOTE: The fact that ANSI.MOD waits until an outer MACRO is being 
        called, before expanding sub-macros, creates a problem for which there 
        is no completely satisfactory solution.  Consider this: Suppose you at-
        tached the MACRO "a" to "a".  In other words, define the key "a" to be 
        itself.  When "a" is pressed, ANSI.MOD will look at it, decide that it 
        was redefined, and look up its redefinition.  The characters in the re-


Page 6

        definition will then be checked to see if any are themselves redefini-
        tions, AND DISCOVER THAT "a" IS.  What has been created, is an infin-
        ite loop.  To stop this, ANSI.MOD checks the stack of sub-macros cur-
        rently being expanded, and if it finds a sub-macro lower down on the 
        stack that is the same as the one being checked, it will NOT expand the 
        one being checked. 

FAST SCREEN MODE: ANSI.MOD is far from being a slow poke in putting characters 
        on your screen.  But sometimes, it can be even faster.  DOS does some 
        checking between sending characters to the screen.  For instance, DOS 
        checks for CTRL-C, which tells DOS to stop doing whatever it is doing.

        This checking can be turned off, thus speeding up screen writes.  True, 
        you will lose CTRL-C and CTRL-BREAK, but PKII's KEYPAD 5, ESC will 
        still get you out of trouble. 

        To enable ANSI.MOD's fast screen update mode, press ALT-ESC, then 1, 
        then lower case "r".  To disable this mode, press ALT-ESC, 0, lower 
        case "r". 

CHANGE TEXT AND GRAPHICS MODES: Press ALT-ESC, n, lower case h.  Where n is the 
        number of the text or graphics mode you wish to use.  I use this mostly 
        when some ignorant programmer has decided he knows more than I, about 
        what mode I want MY display in, puts MY display into 80x25 color mode, 
        when I want it to be in 80x25 Black & White.  

        Note that n = 7 is not a text or graphics mode, but rather a "wrap" 
        mode.  If you don't wish characters to "wrap" at the end of a line, 
        press ALT-ESC, 7, lower case L (l looks like 1).  The option, n = 43, 
        is not part of ANSI, but if you have an EGA (or VGA), it will put your 
        display into an 80x43 (50 for VGA) text mode. 

        The possible values for "n" are: 
        
               0 - 40x25 black & white
               1 - 40x25 color
               2 - 80x25 black & white
               3 - 80x25 color
               4 - 320x200 color graphics
               5 - 320x200 black & white graphics
               6 - 640x200 black & white graphics
               7 - Automatic CR LF at end of line
               8 - 160x200 color graphics (PCjr and Tandy 1000)
               9 - ?
              10 - ?
              11 - ?
              12 - ?
              13 - 320x200 color graphics for EGA
              14 - 640x200 color graphics for EGA
              15 - 640x350 monochrome graphics for EGA
              16 - 640x350 black and white graphics for EGA


Page 7
                    
              17 to 42 - ?   

              43 - 43 (50) line TEXT mode for EGA (VGA) (text modes only, sorry)

        ? - Means "perhaps" that number does something nice to your machine.  
            If not, entering it may cause your machine to LOCK UP. 

CHANGE SCREEN COLORS, ETC.: Press ALT-ESC, P1;P2; ... ;Pk, lower case m, where 
        the Pi's are numbers listed below.  In other words, you are able to 
        select more than one of the attributes listed below, in the same call 
        to ANSI.  Put semicolons between each number.  Again, this is used when 
        some stupid application messes up your screen.  It always works after 
        you exit the program, but some programs won't permit you to change 
        colors while inside them.  Note that option 9 lets you supply an attri-
        bute byte, thus can do the work of (almost all of) the other options. 

        no param - makes current screen (low intensity) White, on Black
               0 - return to White on Black background, no Bold, no Blink
               1 - high intensity (foreground and border only)
               2 - normal intensity, no color change, just dimmer foregrnd
               4 - underline (monochrome adaptors only)
               5 - blinking (in graphics modes, characters are XOR'ed)
               7 - reverse video (XOR background & foreground, blink, bold
                   unchanged) 
               8 - concealed characters (foreground = background, in color)

               9 - The number entered after the 9 replaces current attribute
                   byte (background & foreground colors, blink, and intensity)

        *     10 - Turn off cursor in graphics modes (this is the default)
        *     11 - Turn on cursor in graphics modes (VERY SLOW, use sparingly)
        *     12 - Turn off (detach) ANSI.MOD.  MACROS, and many other things, 
                   still work.  ANSI.MOD can still support the other modules.
        *     13 - Turn ANSI.MOD back on.

              21 - Remove boldness
              22 - Remove blinking and boldness (like option 0, but it works
                   on color screens)
              24 - Remove underlining (MDA only)
              25 - Remove blinking
              27 - Reverse video (same as option 7)
              28 - Remove concealed characters (restore foreground)

        foreground colors
              30 - black
              31 - red
              32 - green
              33 - yellow
              34 - blue
              35 - magenta
              36 - cyan
              37 - white
              38 - ERROR
              39 - ERROR

* - NOTE: At release time (1/31/89), options 10 through 13 sometimes had to be 
    entered twice before they "took". 


Page 8

              40-47 - Background colors (in same order as 30-37)
              48 - ERROR
              49 - ERROR

              50-81 - Border colors (in same order as 30-37, except 51-blue,
                      53-cyan, 54-red, 56-yellow.  58-65 are high intensity.)
    
COPY TO PRINTER OR MODEM: Use ALT-ESC, n, i, where n is a number listed below.  
        These commands will usually be used in MACROS.  For example, suppose 
        your boss is too cheap to buy you a demon dialing telephone, and you 
        MUST call your stockbroker quickly and often.  If your modem has auto-
        dial capability, you can set up a MACRO to do this.  Let's attach this 
        MACRO to F10.  Press ALT-ESC, "quote", F10, ALT-ESC (again), 2, i, 
        ATDT5551212 (or whatever your broker's number is), ALT-ESC (yes, 
        again), 6, i, "quote", p.  Note: If your boss is too cheap even to 
        install touch tone lines, change the "ATDT" to "ATDP". 

        What did we do here?  The first ALT-ESC gets ANSI's attention.  The 
        "quote" mark says that characters, rather than numbers, are to follow.  
        F10 is the MACRO's key.  The characters before the next "quote" will be 
        explained later.  The "quote" marks the end of the characters, and the 
        "p" tells ANSI to attach those characters to the F10 key. 

        Now here's what happens when you press F10.  ALT-ESC starts the ANSI 
        sequence to turn on copy to the modem.  The "2" selects the modem.  The 
        "i" completes the ANSI sequence.  From here on, everything that would 
        normally go to the screen, goes to the modem instead.  Thus, the "ATDT-
        5551212" is sent to the modem, and the modem dials the number.  The 
        final ALT-ESC alerts ANSI again; the "6" deselects the modem; the "i" 
        completes the command, and ANSI directs output back to the screen. 

        The possible values for "n" are: 

               0 - Copy to printer (LPT1)
               2 - Copy to modem (COM1)
               3 - Copy from modem (COM1)
               4 - Turn off copy to printer
               6 - Turn off copy to modem
               7 - Turn off copy from modem

STANDARDIZATION: Suppose you have two word processors, one named "EDITOR", and 
        one named "ED".  One you use to dash off notes and memos, the other, 
        for more serious work (not that your memos aren't serious).  For the 
        sake of simplicity, suppose the two have identical command structures, 
        except that ED uses F8 to call up the "search" capability, while EDITOR 
        uses F9.  To get both programs to use the same keys for the same opera-
        tions, you must call one using a batch file.  Let's call ED using the 
        batch file, EDIT.BAT.  Use either ED or EDITOR to create the following 
        EDIT.BAT, batch file: 

        prompt $e[0;67;0;66p
        ed
        prompt $e[0;67p
        prompt $n$g


Page 9

        Now, when you wish to use ED, just type EDIT, and the F9 key will call 
        the search facility.

        Right now, some of you are thinking "what's this screwy `prompt $e[' 
        notation?"  Well, it's the screwy way DOS has provided you to access 
        ANSI.  I'll bet you recognized the "p" at the end of the first line, 
        and guessed that a MACRO was being defined there.  The "prompt $e[" is 
        DOS's way of sending an escape (27, remember?),and a "[", to ANSI.  The 
        "0;67" is the (extended) ASCII code for the F9 key, and "0;66" the 
        ASCII code for the F8 key.  They have to be represented in this awkward 
        manner (when using the PROMPT command only), because they are nonprint-
        ing characters (for printing characters, you would simply put in a 
        "quote", then the characters, then another "quote").   Thus, the first 
        line of EDIT.BAT turns F9 into F8.  The second line calls ED.  The 
        third line isn't executed until you have exited ED, and it deletes the 
        MACRO attached to F9.  The fourth line tells DOS to make a prompt 
        consisting of the current drive letter, followed by the symbol ">" 
        (look familiar?). 

        I hope this (admittedly oversimplified) example gives some idea of how 
        to lessen the memory circuit overload many of us endure, because every 
        program we own does the same thing differently.  Most DOS manuals have 
        a table of ASCII codes in the back, for you to refer to in this endeav-
        or.   Yes, these ANSI sequences are kind of tough to construct, but you 
        only have to create a batch file once, for each of your most-used 
        programs.