--------------------------------------------------
	  HIGHUMM.SYS: Programmer'S Interface to High Memory
	  --------------------------------------------------

HIGHUMM.SYS is a device driver that lets application programmers
access the memory between 640k and 1Meg.  It requires that LASTBYTE
be installed first.  HIGHUMM may itself be loaded into high memory
with HIGHDRVR.

HIGHUMM provides two methods of accessing high memory:

1. XMS Upper Memory Blocks:
---------------------------

If an Extended Memory Specification (XMS) driver (such as HIMEM.SYS)
has already been loaded, HIGHUMM will link into it, providing an
implementation of the two XMS functions for accessing what the XMS
specification refers to as "Upper Memory Blocks" (UMB's).  Although
described in the spec, the UMB functions have not been implemented in
the current (June 1990) and previous versions of HIMEM.SYS.

Upper Memory Blocks (UMBs) are blocks of memory available on some
80x86 based machines which are located between DOS's 640K limit and
the 1MB address boundary.  The number, size, and location of these
blocks vary widely depending upon the types of hardware adapter cards
installed in the machine.  By definition, this memory is
DOS-accessible, but does NOT include the Bank-Switch memory supported
by LASTBYTE.

On 80286 and 80386 based machines, XMS allows DOS programs to utilize
Extended Memory in a consistent, machine independent manner.  With
some restrictions, XMS adds almost 64K of Extended Memory to the 640K
which DOS programs can access directly.  Depending on available
hardware, XMS may provide even more memory (UMB's) to DOS programs.
XMS also provides DOS programs with a standard method of storing data
in extended memory.

The XMS Specification version 2.0 for MS-DOS was jointly developed by
Lotus, Intel, Microsoft, and AST Research.  The specification was
published on July 19, 1988 and released to the public domain and is
not confidential or proprietary, but the specification is still the
copyright and property of these companies.  You may obtain a copy
from Microsoft Corporation, 16011 NE 36th Way, Box 97017, Redmond, WA
98073, or by calling Microsoft at (800) 426-9400.

Access to the UMB's through XMS is a four step process:

	1.  Test for the existence of the XMS driver.
	2.  Obtain the address of the XMS control function.
	3.  Invoke the Request UMB or Release UMB function.
	4.  Check for success or failure.

This is best explained by an example:

	...
	mov	ax,4300h	; XMS driver installed?
	int	2Fh
	cmp	al,80h
	jne	NoXMSDriver
	...
	mov	ax,4310h	; Get adrs of XMS Control Function
	int	2Fh
	mov	WORD PTR [XMSControl],bx	; XMSControl is a DWORD
	mov	WORD PTR [XMSControl+2],es
	...
	mov	ah,10h		; Request a UMB memory block
	mov	dx,size_in_paragraphs
	call	[XMSControl]
	cmp	ax,1
	jne	Request_Failed

	; If request was successful:
	; --------------------------
	; AX = 1
	; BX = Segment address of allocated block
	; DX = Actual size of block (same as requested size)

	; If request failed:
	; ------------------
	; AX = 0
	; DX = size of largest available in paragraphs
	; Error Codes:	BL = 80h (Not implemented - HIGHUMM not installed)
	;		BL = B0h (Smaller UMB available)
	;		BL = B1h (No UMB available)

	mov	ah,11h		; Release a UMB memory block
	mov	dx,segment_address_of_umb
	call	[XMSControl]
	cmp	ax,1
	jne	Release_Failed

	; If request was successful:
	; --------------------------
	; AX = 1

	; If request failed:
	; ------------------
	; AX = 0
	; Error Codes:	BL = 80h (Not implemented - HIGHUMM not installed)
	;		BL = B2h (DX contained invalid segment number)


HIGHMEM lists such UMB memory blocks as "MS-DOS XMS UMB".


2. Bank-Switch Memory:
----------------------

The second method of accessing high memory is by opening the device
"KSP$UMM" and performing an IOCTL Read of four bytes.  This obtains
the offset and segment address of an extended UMB control function
that provides access to Bank-Switch memory as well as normal UMB
blocks.  Using HIGHUMM.SYS in this manner does not require that an
XMS driver such as HIMEM.SYS be loaded.  For example:


Device_Name	db	'KSP$UMM',0	; HIGHUMM.SYS device name
HIGHUMM_Ctl	dw	0,0		; offset,segment of control function

	...
	mov	ax,3D00h	; open file or device
	mov	dx,OFFSET Device_Name	; DS:DX => device name string
	int	21h
	jc	Open_Failed	; (HIGHUMM.SYS not installed)
	mov	handle,ax	; save handle

	mov	ax,4400h	; ioctl: get device attributes
	mov	bx,handle
	int	21h
	jc	Attb_Failed	; (HIGHUMM.SYS not functioning)
	test	dl,80h		; is this a device or a filename
	jz	Not_Device	; There's a file called "KSP$UMM"

	mov	ax,4402h	; IOCTL Read (BX = handle from open)
	mov	bx,handle
	mov	dx,OFFSET HIGHUMM_Ctl	; DS:DX => read buffer
	mov	cx,4		; read *EXACTLY* four bytes
	int	21h

	pushf
	mov	ah,3Eh		; Close device (BX = handle from open)
	mov	bx,handle
	int	21h
	popf

	jc	IOCTL_Error	; (HIGHUMM.SYS not functioning)

	; offset of control function is in "adrs"
	; segment of control function is in "adrs+2"


Once you have the address of the extended control function from
HIGHUMM.SYS, you can invoke any of five functions by placing the
corresponding function number in register AH:  (Note that these
function numbers are different than those used with XMSControl!)

	AH = 00h	Request a UMB memory block
	AH = 01h	Release a UMB memory block
	AH = 02h	Request a Bank-Switch memory block
	AH = 03h	Release a Bank-Switch memory block
	AH = 04h	Transfer data to/from high memory

The register conventions for functions 00h and 02h are identical to
function 10h of XMSControl, and those for functions 01h and 03h are
identical to function 11h of XMSControl.  HIGHMEM will list allocated
Bank-Switch memory blocks as "Bank-Switch UMB".

Function 04h enables Bank-Switch Memory (e.g., from behind the video
buffer), copies the data between the specified source and
destination, then disables the Bank-Switch memory.  This function
performs no check for argument validity, and returns no indication of
success or failure.  The required operands are:

	AH = 04h
	CX = Number of bytes to transfer
	DS:SI = Segment:Offset address of source
	ES:DI = Segment:Offset address of destination

NOTE: The only valid use of Bank-Switch memory is to store data!
Never load a program into Bank-Switch memory and then reference it
via a JMP or CALL - it won't be there!  For example, you may NOT load
a TSR into Bank-Switch memory and expect it to be accessible when
it's activating interrupt occurs.

--------------------- End of file HIGHUMM.DOC ---------------------