WINCC

                     A Small Window Library For C Written In C

                                   Version 1.0








                                  User's Manual





























                          Copyright (c) 1987 by Doug Lieu.
                                All Rights Reserved.








                             Table of Contents



            I.  INTRODUCTION

           II.  FUNCTION DESCRIPTION

          III.  ERROR MESSAGES AND USER DEFINED TABLES







      I. INTRODUCTION

      WINCC (Window for C in C) is a small screen-handling library including
      more than 50 functions that provide direct screen I/O to open pulldown
      or popup window, to move window, to zoom window in any direction to
      different sizes and some basic I/O functions similar to those in the
      standard C library. It tries to provide an easy way to view many files
      at the same time and is intended as informational display entity with
      no data entry capability. The data which appears in a window is simply
      text. The basic design of WINCC is very simple: an array to hold the
      windows and a stack to store its number. It writes the string directly
      to the video buffer to gain the speed.

      One thing is unusual about WINCC: All functions are written in C
      (Lattice 3.1) without losing too much speed and they currently work
      with Lattice C only.

      There are two window operation modes: control mode and browse mode. In
      control mode, the application can move window, activate window, zoom
      window and etc. In browse mode, a window can browse up to 64K per file,
      and its attribute and border can be changed directly.

      To use the WINCC function is very easy and straight forward. No
      predefined structure are required. e.g. To open a window just calls
      wopen(pop up window) or wfopen(pulldown window) and to move or zoom a
      window just calls wmove or wzoom. You can open as many as 100 windows
      (if you have enough memory) at the same time, but you can operate
      only on the top window i.e. current window. The window number returned
      by the wopen or wfopen is the only thing to be tracked by the
      applications.

      A function is named with prefix "w" if it will operate on the top
      window or it required a window number as an argement. The other
      functions are either for video I/O or applications of windows. The
      routines used internally are named with prefix "_". The WINCC library
      is created on an AT clone under MS-DOS v3.1 using Lattice C compiler
       v3.1 and Object Module Librarian(OML).

      The WINCC has been tested on the IBMPC/XT/AT equipped with monochrome
      and EGA video boards.

      The WINCC requires an IBM-PC or compatible with at least 256K of
      memory, MS-DOS 3.0+, Lattice C compiler v3.0+.


      





      Followng are the terms and their definitions used in the WINCC
      environment:

      Video and Screen
           Two pages of video buffer are used, the first is for displaying
           and the second is used as a temparary buffer. The address
           (segment) of video buffer must be either 0xb000(mono) or 0xb800
           (color). The screen is an area that hold 25 x 80 of characters.

      Attribute
           The attributes are logical defined for both monochrome and color.
           An attribute is a number associated with an attribute byte which
           define background attribute in the upper 4 bits and foreground
           attribute in the lower 4 bits. Their definitions can be found in
           win_vd.h and the following macro definition in win_vd.h set the
           physical attribute:

           #define s_att(bg, fg)        (((bg % 8) << 4) + fg)
                   where fg is foreground and bg is background

           Total of 5 monochrome attribues and 16 color attributes are used
           to define the logocal attributes. 40+ predefined logical
           attributes have been provided. User can change the attributes or
           add more attributes by changing the attribute table in win_tab.c.
           Physical attributes should not be used at anywhere else.

      Border Type
           10 predefined boder types. All these can be changed by simply
           modifing the border table.

              BDR_DLN ----- double line
              BDR_SLN ----- single line
              BDR_SGDB ---- single line for top and bottom, double line for
                            two sides
              BDR_DBSG ---- double line for top and bottom, single line for
                            two sides
              BDR_PUNC ---- '#'
              BDR_STAR ---- '*'
              BDR_DOT ----- '.'
              BDR_DOLLAR -- '$'
              BDR_AT ------ '@'
              BDR_SPACE --- ' ' (space)

      Cursor
           Physical and logical cursor positioning are both proveded.
           Cursor type(mono & EGA) can be changed by a function call.

      Keyboard
           Most of the keys defined by BIOS are included in win_kb.h.

      





      5 STEPS TO DO WINDOWS

           1. Include header files

              Four header files for different operations
                   win_kb.h   -- keyborad definition.
                   win_fct.h  -- declaration of window function.
                   win_op.h   -- macro definition of window operations.
                   win_vd.h   -- video definition.

              They are all collected in "win_hd.h" for convience.


           2. Initialize the environment

              The function winitial must be the first statement in the main
              program. It initializes the global variable, the tables, video
              mode, debug flag, logical attribute and some user defined
              parameters. Although the first opened window will call it, it
              is always safe to make winitial the first statement in the
              main program.


           3. Open the window

              wopen(top,bottom,left,right,attr,bdr,bdr_attr,title,fname)
              wfopen(top,bottom,left,right,attr,bdr,bdr_attr,title,fname)

                   where the dimensions top, bottom, left and right are
                   physical location(0-24, 0-79) on the screen.


           4. Window operaton

              Basic operations are wmove, wzoom, wactive, wz_shift,
              wz_offset, wz_pos and wz_move.


           5. Close the window.

              wclose will remove the window block from sreen and restore the
              context underneath it.


      





      Following is the list of all the library functions in three groups
      according to their operation function:


      FUNCTIONS FOR WINDOW CONTROL

           wactive(win)
           wcenter()
           wcheck(win)
           wchg_attr(attr, bdr, bdr_attr)
           wclose(win)
           wcloseall()
           wcls()
           wfopen(top, bottom, left, right, attr, bdr, bdr_attr, title, fname)
           wfullzoom()
           wgetch()
           wgets(s, len)
           wget_cursp(rwop, colp)
           winitial()
           wmode(opt)
           wmove(top, left, coordi)
           wopen(top, bottom, left, right, attr, bdr, bdr_attr, title, fname)
           wputch(attr, c)
           wputs(attr, s)
           wrefresh(key)
           wscroll(line)
           wset_ctype(type)
           wset_cursp(row, col)
           wshift(dir)
           wstatus(win)
           wwalk()
           wz_move(top, bottom, left, right)
           wz_offset(t_ofst, b_ofst, l_ofst, r_ofst)
           wz_pos(top, bottom, left, right)
           wzoom(opcode)


      FUNCTIONS FOR WINDOW BROWSE

           get_cursor(rowp, colp)
           get_key()
           get_kstat()
           get_vchar(vc)
           get_vmode()
           put_vchar(attr, c)
           set_cattr(attr)
           set_cursor(row, col)
           vputs(attr, s)
           vscroll(line)
           wcls()
           wget_cursp(rowp, colp)
           wgetch()
           wgets(s, len)
           wprintf(attr, fmt, arg_lst)
   





      UTILITY AND APPLICATION FUNCTIONS

           ask(row, col, prompt, len)
           clear_video(page);
           cls()
           dbgprt(fmt, arg_lst)
           delay(sec)
           getfn(row, col, prompt, fname, mdoe)
           getyesno(row, col, prompt)
           message(title, message, opcode)
           put_vchar(attr, c)
           show_attr()
           show_bdr()
           stackmap()
           to_dos()



      WINCCS.LIB -- s model
      WINCCD.LIB -- d model






      II. FUNCTION DESCRIPTION

      This section presents all the functions of the library in alphabatic
      order of function name. It uses similar convention and format as in
      the Lattice C document. All functions are of "int" type except ask.
      "win_hd.h" is the only include file required for using the library, it
      is a collection of four include files.

      All function are compiled with "-n" option only.






      FUNCTION
              ask - ask a question and get the answer string

      SYNOPSIS
              #include "win_hd.h"

              ans = ask(row, col, prompt, len);

              char    *ans;           answered string
              int     row, col;       prompt starting position
              char    *prompt         promt string
              int     len;            maximum length of answer string

      DESCRIPTION
              This function displays the prompt and the field for a single-
              line entry with maximum length len. The prompt and the field
              answered should be in the same line. An error message will be
              displayed and returned with a NULL if the right margin of the
              window exceed the screen border, and no window will be opened.

      RETURNS
              ans == NULL if no answer entered or error
                  == pointer to the answered string

      NOTES
              The function should be delared as "char *".

      SEE ALSO
              getfn, getyesno







      FUNCTION
              clear_video - clear video buffer

      SYNOPSIS
              #include "win_hd.h"

              ret = clear_video(vpage);

              int     ret;            return code
              int     vpage;          page of video buffer to be cleared

      DESCRIPTION
              This function clears video buffer by blanking out the specified
              page of video buffer directly with attribute REGULAR.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid video page number.

      NOTES
              It is used to clear a video buffer when the buffer is used for
              debugging window.







      FUNCTION
              cls - clear the entire screen

      SYNOPSIS
              #include "win_hd.h"

              ret = cls();

              int     ret;            return code

      DESCRIPTION
              This function clears the entire screen and set cursor to home
              position (0, 0).

      RETURNS
              OK -- Successful process.

      NOTES
              None.

      SEE ALSO
              wcls







      FUNCTION
              dbgprt - debug print

      SYNOPSIS
              #include "win_hd.h"

              ret = dbgprt(fmt, arg1, arg2,...);

              int     ret;            return code
              char    *fmt;           format string
              ...     arg1, ...       list of argument to be formatted

      DESCRIPTION
              This function works exactly the same as printf. To turn on the
              debug print at run time, say "SET WDEBUG=1" at DOS prompt or
              add the statement to a batach file. Toturn off the debug print,
              say "SET WDEBUG=" at DOS prompt. All the debug output will be
              written to a file named by "SET WDBGFILE=filename.ext", the
              default debug output file is "WIN_DBG.OUT"

      RETURNS
                 OK -- Successful process.
              ERROR -- A bad format string is detected, error ignored and
                       process continued.

      NOTES
              Please refer the Lattice C manual for detail description.

      SEE ALSO
              dbgprt, printf, wprintf, wputs

      EXAMPLES
              c:>SET WDEBUG=1
              c:>SET WDBGFILE=test.out






      FUNCTION
              delay - delay n seconds

      SYNOPSIS
              #include "win_hd.h"

              ret = delay(n);

              int     ret;            return code
              int     n;              n seconds delay

      DESCRIPTION
              This function delays n seconds before the next statement is
              executed. It calls time function in a loop util the difference
               between starting time and ending is equal to n.

      RETURNS
              OK -- Successful process.

      NOTES
              None.







      FUNCTION
              get_cursp - get physical cursor position

      SYNOPSIS
              #include "win_hd.h"

              ret = get_cursp(rowp, colp);

              int     ret;            return code
              int     *rowp;          pointer to row position
              int     *colp;          pointer to column position

      DESCRIPTION
              Get physical cursor position of physical screen.

      RETURNS
              OK -- Successful process.

      NOTES
              rowp and colp must be pointers.

      SEE ALSO
              set_cursp, wget_cursor, wset_cursp







      FUNCTION
              get_key - wait and get next keystroke

      SYNOPSIS
              #include "win_hd.h"

              c = get_key();

              int     c;              key entered

      DESCRIPTION
              This function waits and gets next key entered, including
              extended character. Any key(s) not defined in the BIOS will
              be ignored.

      RETURNS
              Refer to win_vd.h for detail description.

      NOTES
              None.

      SEE ALSO
              get_kstat







      FUNCTION
              get_kstat - check keyboard status and return the key if the
                          keybord buffer is not empty

      SYNOPSIS
              #include "win_hd.h"

              c = get_kstat();

              int     c;              key buffered

      DESCRIPTION
              This function works similar to get_key, except it does not
              wait for an input.

      RETURNS
              c     -- buffered characters
              ERROR -- no key has been buffered

      NOTES
              When the process is in a loop, some of the WINCC function will
              ignore Ctrl-C or Ctrl-break. With this function in a loop, a
              Ctrl-C will be detected and process can be terminated properly.

      SEE ALSO
              get_key

      EXAMPLES
              #include "win_hd.h"

              while (1) {
                      if (get_kstat() == CTRL_C)
                              break;
                      ....
              }






      FUNCTION
              get_vchar - get a video char

      SYNOPSIS
              attr = get_vchar(vc);

              int     attr;           attribute number
              char    vc[2];          video char

      DESCRIPTION
              This function gets a video character (a character and its
              attribute) at cursor position and retrun the logical attribute
              number.

      RETURNS
              attr -- logical attribute number

      NOTES
              It will return 0, if no attribute matched.

      SEE ALSO
              put_char, win_vd.h







      FUNCTION
              get_vmode - get video mode

      SYNOPSIS
              mode = get_vmode();

              int     mode;           video mode

      DESCRIPTION
              This function gets current video mode.

      RETURNS
              Mode  Description

                  0 -- 40 x 25 B/W
                  1 -- 40 x 25 Color
                  2 -- 80 x 25 B/W
                  3 -- 80 x 25 Color
                  4 -- 320 x 200 Color
                  5 -- 320 x 200 B/W
                  6 -- 640 x 200 B/W

      NOTES
              None.







      FUNCTION
              getfn - get a filename and its accessibility

      SYNOPSIS
              #include "win_hd.h"

              ret = getfn(row, col, prompt, filename, mode);

              int     ret;            return code
              int     row, col;       prompt starting position
              char    *prompt;        prompt string
              char    *filename;      file name
              int     mode;           file mode to mask

      DESCRIPTION
              This function displays the prompt and the filename input field
              within a box, then forces the operator to type a valid file-
              name. The prompt and response are erased prior to return to
              the calling function. It call access to do the validation.
              Refer to Lattice C manual for the detail of file mode.

      RETURNS
                 OK -- Successful process.
              NO_OP -- No filename entered.
              ERROR -- If the file not exist, is not readable or the file
                       mode can not match the specified mode.

      NOTES
              This function is designed to make it easy to obtain a valid
              filename with the specified mode.

              The maximum length of filename is 22, driver symbol is allowed.

      SEE ALSO
              ask, getyesno







      FUNCTION
              getyesno - to ask a question and get a 'Y' or 'N' response

      SYNOPSIS
              #include "win_hd.h"

              ret = getyesno(row, col, prompt);

              int     ret;            response value
              int     row, col;       prompt starting position
              char    *prompt;        prompt string

      DESCRIPTION
              This function displays the prompt and get a one-character
              input field on the screen within a box, then forces the
              operator to type Y/y or N/n to specify his choice. The
              question and response are erased before returning to the
              calling function.

      RETURNS
              YES - if Y/y is entered
               NO - if N/n is entered

      NOTES
              This function is designed to make it easy to ask a simple
              Yes/No question and get a response from the operator. No
              return or enter key is needed after enter Y(y) or N(n).

      SEE ALSO
              ask, getfn







      FUNCTION
              message - to display a message

      SYNOPSIS
              #include "win_hd.h"

              ret = message(title, msg, opcode);

              int     ret;            return code
              char    *title;         message title
              char    *msg;           message to display
              int     opcode;         STAY or PAUSE

      DESCRIPTION
              Displays a message window at the bottom of the screen. If
              opcode is STAY, it will return the message window number,
              otherwise it will wait for a keystroke, then close the window
              and return to the calliing function. The max len of msg is 77.

      RETURNS
              OK -- Successful process.
              w  -- Window number.

      NOTES
              The message window will wait for a keystroke before it is
              closed. This will give user a chance to read the message.

              If the message string contains "\007", the bell will be
              sounded to indicate an error has occurred.







      FUNCTION
              put_vchar - put a video char

      SYNOPSIS
              #include "win_hd.h"

              ret = put_vchar(vc);

              int     ret;            return code
              char    *vc;            video char

      DESCRIPTION
              This function puts a video character (a character and its
              attribute) directly to the video buffer at the cursor
              position.

      RETURNS
              OK -- Successful process.

      NOTES
              The cursor stays at the same position after the execution.

      SEE ALSO
              get_vchar







      FUNCTION
              set_cattr - set the attribute of cursor position

      SYNOPSIS
              #include "win_hd.h"

              ret = set_cattr(attr);

              int     ret;            return code
              int     attr;           logical attribute number

      DESCRIPTION
              This function sets or changes the attribute at cursor position.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid attribute number.

      NOTES
              None.

      SEE ALSO
              wset_ctype







      FUNCTION
              set_cursp - set cursor position

      SYNOPSIS
              #include "win_hd.h"

              ret = set_cursp(row, col);

              int     ret;            return code
              int     rwo, col;       row and column

      DESCRIPTION
              This function sets the physical cursor position.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid row or column specified.

      NOTES
              None.

      SEE ALSO
              get_cursp, wget_cursp, wset_cursp







      FUNCTION
              show_attr - show attribute table

      SYNOPSIS
              #include "win_hd.h"

              ret = show_attr();

              int     ret;            return code

      DESCRIPTION
              This function displays all the attributes in the attribute
              table either mono or color.

      RETURNS
              OK -- Successful process.

      NOTES
              It is embeded in wgetch and activated by the attr_key defined
              in the win_tab.c

      SEE ALSO
              show_bdr, stackmap, wstatus







      FUNCTION
              show_bdr - show border type

      SYNOPSIS
              #include "win_hd.h"

              ret = show_bdr();

              int     ret;            return code

      DESCRIPTION
              This function displays border types defined in the border
              table.

      RETURNS
              OK -- Successful process.

      NOTES
              It is embeded in wgetch and activated by the bdr_key defined
              in the win_tab.c

      SEE ALSO
              show_attr, stackmap, wstatus







      FUNCTION
              stackmap - display the map of window stack

      SYNOPSIS
              #include "win_hd.h"

              ret = stackmap();

              int     ret;            return code

      DESCRIPTION
              This function browses some window's information in the order
              of window stack.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid option.

      NOTES
              It is embeded in wgetch and activated by the bdr_key defined
              in the win_tab.c. It is useful when many windows are opened
              and a window is to be acitvated.

      SEE ALSO
              show_attr, show_bdr, wstatus







      FUNCTION
              to_dos - escape to dos tempararily

      SYNOPSIS
              #include "win_hd.h"

              ret = to_dos();

              int     ret;            return code

      DESCRIPTION
              This function uses the video buffer page 2 to restore current
              screen and escape to dos by calling DOS command.com. Also
              restore the original screen when exit from DOS.

      RETURNS
                 OK -- Successful process.
              ERROR -- Command call failed.

      NOTES
              The program will stay in the memory and the process will be
              in sleep until an "EXIT" is entered at DOS prompt.







      FUNCTION
              vputs - put a string to video buffer

      SYNOPSIS
              #include "win_hd.h"

              ret = vputs(attr, s);

              int     ret;            return code
              int     attr;           logical attribute number
              char    *s;             output string

      DESCRIPTION
              This function puts a string to video buffer. It works similar
              to puts(), plus the handling of attribute. For char less than
              32 only the bell, newline and tab will be processed. Since it
              writes string directly to the screen buffer, it works mush
              faster than puts().

              If ths string s has attribue embeded in the string already,
              set attr to ATTR_STR to use the whole string.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid attribute number.

      NOTES
              None.

      SEE ALSO
              wputs, put_vchar







      FUNCTION
              vscroll - scroll the screen up or down

      SYNOPSIS
              #include "win_hd.h"

              ret = vputs(n);

              int     ret;            return code
              int     n;              scroll n lines

      DESCRIPTION
              This function scrolls the full screen up or down n lines. The
              attribute at cursor position will be assigned to the blank
              lines. It will scroll screen UP if n > 0 else it will scroll
              down.

      RETURNS
              OK -- Successful process.

      NOTES
              The line scrolled over the svreen border is not buffered.

      SEE ALSO
              wscroll






      FUNCTION
              wactive - activate a window to be the top window

      SYNOPSIS
              #include "win_hd.h"

              ret = wactive(win);

              int     ret;            retur code
              int     win;            the number of window to be activated

      DESCRIPTION
              This function surfaces specified window to the top as it is
              the current window.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              Activation processes a lot faster if no window overlaps the
              window to be activated.

      SEE ALSO
              wopen, wfopen







      FUNCTION
              wcenter - move current window to the center of the screen

      SYNOPSIS
              #include "win_hd.h"

              ret = wcenter();

              int     ret;            return code

      DESCRIPTION
              This function moves current window to the center of the
              screen. It is a special case of wmove.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              None.

      SEE ALSO
              wmove, wshift, wz_move.






      FUNCTION
              wcheck - check the window number

      SYNOPSIS
              #include "win_hd.h"

              ret = wcheck(win);

              int     ret;            return code
              int     win;            window number

      DESCRIPTION
              This function validates the window number.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              None.







      FUNCTION
              wchg_attr - change window's attribute

      SYNOPSIS
              #include "win_hd.h"

              ret = wchg_attr(attr, bdr, bdr_attr);

              int     ret;            return code

      DESCRIPTION
              This function changes the attribute and border type of the
              window interactivaly.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              Only the valid attribute or valid border type will be
              processed.







      FUNCTION
              wclose - close a window

      SYNOPSIS
              #include "win_hd.h"

              ret = wclose(win);

              int     ret;            return code
              int     win;            window number

      DESCRIPTION
              This function frees the space allocated when opened and
              restores the screen contents underneath it. The window stack
              is also ajdusted.

      RETURNS
                 OK -- Successful process.
              ERROR -- If win is not opened.

      NOTES
              None.

      SEE ALSO
              wopen, wfopen, wcloseall







      FUNCTION
              wcloseall - close all the windows

      SYNOPSIS
              #include "win_hd.h"

              ret = wcloseall();

              int     ret;            return code

      DESCRIPTION
              This function works like wclose except it closes all the
              windows.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window is currently opened.

      NOTES
              None.

      SEE ALSO
              wopen, wfopen, wclose







      FUNCTION
              wcls - clear the window(inside the border)

      SYNOPSIS
              #include "win_hd.h"

              ret = wcls();

              int     ret;            return code

      DESCRIPTION
              This function clears the area inside the border of current
              window.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window is currently opened.

      NOTES
              None.

      SEE ALSO
              cls







      FUNCTION
              wfopen - fast open of a window (pull down)

      SYNOPSIS
              #include "win_hd.h"

              wn = wfopen(top,bottom,left,right,attr,bdr,bdr_attr,title,fname);

              int     wn;             window number
              int     top;            top row of window
              int     bottom;         bottom row of window
              int     left;           left most column of window
              int     right;          right most column of window
              int     attr;           attribute of window
              int     bdr;            border type
              int     bdr_attr;       attribute of border
              char    *title;         title of window
              char    *fname;         input file name

      DESCRIPTION
              This function does exactly the same work as what wopen does,
              except it pulls down a window instead of popping it up and it
              processes much more faster than wopen.

      RETURNS
                 OK -- Successful process
              ERROR -- If open window failed. The window number should fall
                       between 0 and 99 (0 <= wn <= 99).

      NOTES
              Calling function should always check the return window number.
              The maximum size of window is 25 x 80 and the minimum size is
              2 x 2. Invalid window size, memory not enough or 100 windows
              have already opened will cause an error message displayed.

      SEE ALSO
              wopen, wclose, wactive

      EXAMPLES
              #include "win_op.h"
              #include "win_vd.h"

              int     wn;

              winitial();
              wn = wfopen(10,20,10,70,NORMAL,BDR_DLN,NORMAL,NULL,NULL);
              if (wn == ERROR)
                      exit(0);







      FUNCTION
              wfullzoom - zoom current window to the full of screen

      SYNOPSIS
              #include "win_hd.h"

              ret = wfullzomm();

              int     ret;            return code

      DESCRIPTION
              This function first moves the window to the center of the
              screen, then zooms it to the full of screen.

      RETURNS
                 OK -- Successful process
              ERROR -- If no window opened.

      NOTES
              The content will be redisplayed after zoomed.

      SEE ALSO
              wcenter, wz_move, wzoom







      FUNCTION
              wget_cursp - get virtual cursor position of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wget_cursp(rowp, colp);

              int     ret;            return code
              int     *rowp;          pointer to row position
              int     *colp;          pointer to column position

      DESCRIPTION
              Get logical cursor position of current window.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              rowp and colp must be pointers.

      SEE ALSO
              get_cursp, set_cursp, wset_cursp







      FUNCTION
              wgetch - get a character at cursor position of current window

      SYNOPSIS
              #include "win_hd.h"

              c = wgetch();

              int     c;              return character

      DESCRIPTION
              This function gets a character from current window just like
              getchar() of standard C library. It always processes attr_key,
              bdr_key, bbrow_key, smap_key and tggl_key first before
              processing anything else. Then if it is in Control mode, it
              will return whatever is entered. If it is in Browse mode, it
              will return key between 32(space) and 126(~) plus CR, TAB and
              BACKSPACE, the rest of keys will be passed to wrefresh for
              browse of the content, and then return it to the calling
              function.

              Following are six keys defined in the table(win_tab.c):

                  attr_key          to show attribute table.
                  bdr_key           to show border type.
                  brow_key          to browse window's contents.
                  smap_key          to show map of window stack.
                  stat_key          to browse window's status.
                  tggl_key          to toggle the window operation modes.

              These keys can be changed by modifing their definitions in
              win_tab.c and recompiling.

      RETURNS
              See above.

      NOTES
              Character will not be echoed.

              Since many window operations are embeded in this routine, it
              is very convient to put the statement after window is opened.
              It is alos called by wwalk which will move and zoom the window
              through some combination keys.

      SEE ALSO
              show_attr, show_bdr, stackmap, wgets, wrefresh, wstatus, wwalk







      FUNCTION
              wgets - get a string from current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wgets(attr, s, len);

              int     ret;            length of string entered
              int     attr;           attribute of string to be entered
              char    *s;             string buffer
              int     len;            maximum length of string to be entered

      DESCRIPTION
              This function works like gets in the C library, except it
              requires an attribute and its maximum length of the string to
              get. It calls wgetch, to get a character.

      RETURNS
              ERROR -- If no window opened else
                len -- it return the length of the string entered.

      NOTES
              None.

      SEE ALSO
              wgetch







      FUNCTION
              winitial - initialize the window environment

      SYNOPSIS
              #include "win_hd.h"

              ret = winitial();

              int     ret;            return code

      DESCRIPTION
              This function initializes the global variables, the tables,
              window array, window stack, video mode, debug flag and some
              user defined parameters. If the screen mode is not BW80 or
              CO80, it will abort the process and return to DOS prompt.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              This function should always be the first statement in the
              main program, otherwise window will act unexpectly. The
              init_status defined in win_tab.c can be modified when
              required.

      SEE ALSO
              win_tab.c







      FUNCTION
              wmode - set, get or toggle current window operation mode

      SYNOPSIS
              #include "win_hd.h"

              ret = wmode(opt);

              int     ret;            return code
              int     opt;            options

      DESCRIPTION
              There are two window operation modes: Control mode and I/O
              mode. All the windows opterate under these two modes. The I/O
              mode is on whenever the Control mode is off. The options are:

                  CTRL_ON --- set to Control mode
                  CTRL_OFF -- set Control mode off i.e. set to I/O mode
                  GET_MODE -- get operation mode
                  TG_MODE --- toggle the operation between Control mode
                              and I/O mode

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid option.



              and left corner of of the window if it is in Control mode.

      SEE ALSO
              None.







      FUNCTION
              wmove - move current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wmove(row, col, coordi)

              int     ret;            return code
              int     row;            new row position
              int     col;            new column position
              int     coordi;         coordinate associateed with the new
                                      row and col
      DESCRIPTION
              This function will move the window to a new position specified
              as row, column and coordinate type. It uses the second page of
              video as a temparary buffer to increase the speed of moving and
              save some memory space.

              The row and col should be in the range of (0, 24) and (0, 79).
              The coordinate should be one of following:

                   TOP_LEFT:       /* move the window to top and left */
                   TOP_RIGHT:      /* move the window to top and right */
                   BTM_LEFT:       /* move the window to bottom and left */
                   BTM_RIGHT:      /* move the window to bottom and right*/

      RETURNS
                 OK -- Successful process.
              ERROR -- if the row, col or coordinate are invalid or the
                       window has hit the screen boundary.

      NOTES
              None.

      SEE ALSO
              wshift, wz_move







      FUNCTION
              wopen - open a window (pop up)

      SYNOPSIS
              #include "win_hd.h"

              wn = wopen(top,bottom,left,right,attr,bdr,bdr_attr,title,fname);

              int     wn;             window number
              int     top;            top row of window
              int     bottom;         bottom row of window
              int     left;           left most column of window
              int     right;          right most column of window
              int     attr;           attribute of window
              int     bdr;            border type
              int     bdr_attr;       attribute of border
              char    *title;         title of window
              char    *fname;         input file name

      DESCRIPTION
              This function opens a window and display the input file if
              specified or display the input from console. The input is
              stored in the memory and an attribute is assigned to each
              character for a regular text file. The maximum size of input
              is limited to 30K.

      RETURNS
                 OK -- Successful process.
              ERROR -- If window open failed. The window number should fall
                       between 0 and 99 (0 <= wn <= 99).

      NOTES
              Calling function should always check the return window number.
              The maximum size of window is 25 x 80 and the minimum size is
              2 x 2. Invalid window size, memory not enough or 100 windows
              have already opened will cause an error message displayed.

      SEE ALSO
              wfopen, wclose

      EXAMPLES
              #include "win_op.h"
              #include "win_vd.h"

              int     wn;

              winitial();
              wn = wopen(10,20,10,70,NORMAL,BDR_DLN,NORMAL,NULL,NULL);
              if (wn == ERROR)
                      exit(0);







      FUNCTION
              wprintf - window format print

      SYNOPSIS
              #include "win_hd.h"

              ret = wprintf(attr, fmt, arg1, arg2,...);

              int     ret;            return code
              int     attr;           attribute number
              char    *fmt;           format string
              ...     arg1, ...       list of argument to be formatted

      DESCRIPTION
              This function provides a faster output of formatted string for
              the window. It works exactly the same as printf. All the
              format options can be applied.

      RETURNS
                 OK -- Successful process.
              ERROR -- A bad format string is detected, error ignored and
                       process continued.

      NOTES
              Please refer the Lattice C manual for detail description.

      SEE ALSO
              dbgprt, printf, wputs







      FUNCTION
              wputch - put a character to current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wputch(attr, c);

              int     ret;            return code
              int     attr;           attribute number
              int     c;              output character

      DESCRIPTION
              This function writes a character at the current logical cursor
              position with the specified attribute. The logical cursor
              position is advanced.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              None.

      SEE ALSO
              wputs







      FUNCTION
              wputs - write a string to current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wputs(attr, s);

              int     ret;            return code
              int     attr;           attribute number
              char    *s;             output string

      DESCRIPTION
              This function writes a string at the current logical cursor
              position with the specified attribute. The logical cursor
              position is advanced.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened or invlaid attribute number.

      NOTES
              None.

      SEE ALSO
              wputch







      FUNCTION
              wrefresh - display and refresh window's content

      SYNOPSIS
              #include "win_hd.h"

              ret = wrefresh(key);

              int     ret;            return code
              int     key;            return code

      DESCRIPTION
              This function displays and browses window's content. Following
              are six keys for different ways to display the content:

                   UPARW:               /* up arrow key: scroll down one line */
                   DOWNARW:             /* down arrow key: scroll up one line */
                   PGUP:                /* PgUp: scroll up one page */
                   PGDN:                /* PgDn: scroll down one page */
                   HOME:                /* Home: display first page */
                   END:                 /* End: display last page */
                   ESC:                 /* Esc: redisplay */

              where page equals window's depth - 2.

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened or invlaid key.

      NOTES
              A line content is wrapped around if the length of a line is
              longer the window's width - 2. Whatever the shape of the
              window is, it can only display up to 4000 lines.







      FUNCTION
              wscroll - scroll window's content

      SYNOPSIS
              #include "win_hd.h"

              ret = wscroll(n);

              int     ret;            return code
              int     n;              scroll n lines

      DESCRIPTION
              This function scrolls the window's content up or down n lines.
              The attribute of at cursor position will be assigned to the
              blank lines. It will scroll screen UP is n > 0 else it will
              scroll down.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              The line scrolled over the window border is not buffered.

      SEE ALSO
              vscroll







      FUNCTION
              wset_attr - set the attribute of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wset_attr(attr);

              int     ret;            return code
              int     attr;           attribute number

      DESCRIPTION
              This function changes the attribute of current window. The
              attribute is given when the window is opened by wopen or
              wfopen.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              None.

      SEE ALSO
              wset_bdrattr







      FUNCTION
              wset_bdrattr - set the border attribute of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wset_battr(attr);

              int     ret;            return code
              int     attr;           attribute number

      DESCRIPTION
              This function changes the border attribute of current window.
              The attribute is given when the window is opened by wopen or
              wfopen.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              None.

      SEE ALSO
              wset_attr, wset_bdrtype







      FUNCTION
              wset_bdrtype - set the border type of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wset_battr(type);

              int     ret;            return code
              int     type;           type number

      DESCRIPTION
              This function changes the border type of current window. The
              type is given when the window is opened by wopen or wfopen.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              None.

      SEE ALSO
              wset_battr







      FUNCTION
              wset_ctype - set cursor type of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wset_ctype(type);

              int     ret;            return code
              int     type;           type number

      DESCRIPTION
              Following are the definition of cursor type:

                   C_TOP ----- a dash at the top
                   C_THALF --- half block at the top half
                   C_FULL ---- full block
                   C_MIDDLE -- half block in the middle
                   C_BHALF --- half block in the bottom half
                   C_QUARTER - quarter block in the bottom half
                   C_NORMAL -- double dash at the bottom
                   C_QUOTE --- a dash at the top and a dash at the b
                   C_DASH ---- a dash at the bottom
                   C_BLANK --- no cursor

              If there is no window opened, it will set the cursor type at
              DOS prompt.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid cursor type number.

      NOTES
              It may not works properly in CGA mode.

      SEE ALSO
              win_tab.c, wset_cattr







      FUNCTION
              wset_cursp - set the virtual cursor position of current window

      SYNOPSIS
              #include "win_hd.h"

              ret = wset_cursp(row, col);

              int     ret;            return code
              int     row;            row position
              int     col;            column position

      DESCRIPTION
              This function set the position of the virtual cursor to the
              specified row and column within current window. Any text
              subsequently written to the window with wprintf will be
              written beginning at the virtual cursor location. Cursor will
              not change its position, if return(ret) is ERROR.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid cursor position or no window opened.

      NOTES
              This function is generally used to position the cursor prior
              to a wprintf, so that formatted output may be placed anywhere
              within the window.

      SEE ALSO
              get_cursp, set_cursp, wget_cursp







      FUNCTION
              wshift - shift current window in 8 different directions

      SYNOPSIS
              #include "win_hd.h"

              ret = wshift(dir)

              int     ret;            return code
              int     dir;            direction

      DESCRIPTION
              This function uses the offset defined in the direction table
              (dir_tab) and then call wmove() to move the window. It
              provides a simple way to move the window and the table can be
              modified by adding more directions and different offsets.

      RETURNS
                 OK -- Successful process.
              ERROR -- If the dir is an invalid direction or the window has
                       hit the screen border.

      NOTES
              None.

      SEE ALSO
              wmove







      FUNCTION
              wstatus - display window status

      SYNOPSIS
              #include "win_hd.h"

              ret = wstatus(win)

              int     ret;            return code
              int     win;            window number

      DESCRIPTION
              This function displays the status of specified window, inlcud-
              ing location, size, attribute, title, input filename, position
              in the stack and etc.

      RETURNS
                 OK -- Successful process.
              ERROR -- Invalid window number.

      NOTES
              None.

      SEE ALSO
              showmap






      FUNCTION
              wwalk - walk a window

      SYNOPSIS
              #include "win_hd.h"

              ret = wwalk()

              int     ret;            return code

      DESCRIPTION
              This is an application to simplify the window operations. It
              uses the function keys, key pad and some combination keys to
              operate current window. Any key not defined will terminate
              this function, retrun to the calling function with the key
              entered which gives the calling function more control.

              Following are the key and their function:

                                 INCREASE       DECREASE
                                 ----------     --------
                   top side      Shift & F1     Alt & F1
                   bottom side   Shift & F2     Alt & F2
                   left side     Shift & F3     Alt & F3
                   right side    Shift & F4     Alt & F4
                   all sides     Shift & F5     Alt & F5

                   Zoom the window to full:    Alt-Z
                   Execute DOS commands:       Alt-D
                   Display window stack map:   smap_key
                   Display border types:       bdr_key
                   Display attributes table:   attr_key
                   Toggle Ctrl & Browse mode:  tggl_key
                   Display window status:      stat_key

                   smap_key, bdr_key, attr_key, tggl_key and stat_key are
                   all defined in win_tab.c

      RETURNS
                 OK -- Successful process.
              ERROR -- If no window opened.

      NOTES
              A help screen will pop up when F1 is pressed.

      SEE ALSO
              wgetch, wshift, wmove, wzoom







      FUNCTION
              wz_move - zoom and move current window simultaneously

      SYNOPSIS
              #include "win_hd.h"

              ret = wz_move(top, bottom, left, right)

              int     ret;            return code
              int     top;            top row
              int     bottom;         bottom row
              int     left;           left column
              int     right;          right column

      DESCRIPTION
              This function zooms and moves current window simultaneously
              in a quick and smooth phase.

      RETURNS
                 OK -- Successful process.
              ERROR -- If invalid position specified.

      NOTES
              This function creates an imaginative movement of window.

      SEE ALSO
              wmove, wzoom







      FUNCTION
              wz_offset - zoom current window by offset specified with the
                          function arguments.

      SYNOPSIS
              #include "win_hd.h"

              ret = wz_offset(t_ofst, b_ofst, l_ofst, r_ofst)

              int     ret;            return code
              int     t_ofst;         top offset
              int     b_ofst;         bottom offset
              int     l_ofst;         left offset
              int     r_ofst;         right offset

      DESCRIPTION
              This function zooms current window by specified offset.

      RETURNS
                 OK -- Successful process.
              ERROR -- If invalid offset specified.

      NOTES
              None.

      SEE ALSO
              wz_move, wz_pos, wzoom







      FUNCTION
              wz_pos - zoom current window by position specified with the
                       function arguments.

      SYNOPSIS
              #include "win_hd.h"

              ret = wz_pos(top, bottom, left, right)

              int     ret;            return code
              int     top;            top row
              int     bottom;         bottom row
              int     left;           left column
              int     right;          right column

      DESCRIPTION
              This function zooms current window by specified position.

      RETURNS
                 OK -- Successful process.
              ERROR -- If invalid position specified.

      NOTES
              None.

      SEE ALSO
              wz_move, wz_offset, wzoom







      FUNCTION
              wzoom - zoom window

      SYNOPSIS
              #include "win_hd.h"

              ret = wzoom(opcode)

              int     ret;            return code
              int     opcode;         zoom operation code

      DESCRIPTION
              This function zooms current window in two basic ways: by offset
              and by position. It used the value in the zm_table to zoom
              the window. Following are the macro definitons:

                   ZOFFSET        zoom by specified offset
                   ZPOS           zoom to specified position
                   ZFULL          zoom to full size of screen
                   ZLARGE1        zoom larger, 1 line more on each side
                   ZLARGE2        zoom larger, 1 line more on two sides, 3
                                  lines more on top & bottom
                   ZSMALL1        zoom smaller, 1 line less on each side
                   ZSMALL2        zoom smaller, 1 line less on two sides, 3
                                  lines less on top & bottom
                   ZTOP_U         zoom top line up
                   ZTOP_D         zoom top line down
                   ZBTM_U         zoom bottom line up
                   ZBTM_D         zoom bottom line down
                   ZLEFT_L        zoom left line left
                   ZLEFT_R        zoom left line right
                   ZRIGHT_L       zoom right line left
                   ZRIGHT_R       zoom right line rignt

              Both ZOFFSET and ZPOS are adjustable at run time by modify the
              zm_tab in win_tab.c

      RETURNS
                 OK -- Successful process.
              ERROR -- If current window is not in Control mode.

      NOTES
              None.

      SEE ALSO
              wz_move, wz_offset, wz_pos







      III. ERROR MESSAGES AND USER DEFINED TABLES


      ERROR MESSAGES

      When an error occurs, a message will be displayed at the bottom of the
      screen. If it is a fatal error, the control will return to DOS after a
      key is pressed.

         Cannot access input file (ACCESS_ERR)

         Cannot free the window. Hardware failure, Fatal ! (FREE_ERR)

         Cannot open debug output file (DBGF_ERR)

         Cannot open the window, memory not enough (ALLOC_ERR)

         File open error (FOPEN_ERR)

         File too big to hold(64K max) (TOO_BIG)

         Invalid row and column (INV_RC)

         Invalid window number (WIN_ERR)

         Invalid window size (INV_SIZE)

         Memory not enough (NO_MEMORY)

         No room for another window, can open up to 100 windows (NO_ROOM)

         Read input file failed, Fatal ! (FREAD_ERR)

         Specified position will move the window out of the screen (INV_POS)

         The file has size 0 (EMPTYFILE)

         fseek() error, Fatal ! (FSEEK_ERR)







      KEYBOARD DEFINITION - See win_kb.h


      LOGICAL ATTRIBUTES -

      WINCC uses logical display attributes instead of physical ones. This
      allows the software to be written independently of the actual hardware.
      The physical display attributes to be selected at run time based upon
      the mode of the display adapter. Logical attributes are integers which
      are indexes to the attribute table defined in win_tab.c and win_vd.h.
      To change logical-physical mapping, modify win_tab.c and recompile it.
      See win_vd.h for detail definition.







      WINCC is copyrighted by Doug Lieu. You are welcome to use it and
      distribute it. No fee may be charged for such copying and distribution
      in its original, unmodified state.

      If you are using it and find it to be of value, a contribution of $15
      (suggested) would be appreciated with a dikette of the source code.

                      Doug Lieu
                      26B Warren Dr.
                      Edison, NJ 08820

      Please be advise, no warrant that WINCC will not do anything harmful
      although it has not for me.