Instructions for Patrick Swayne's
                      SummaSketch ADI Driver for AutoSketch

        ** Introduction

        This  collection contains a device driver that uses the  Autodesk
        Device Interface (ADI) specification to let you use a Summagraph-
        ics  MM961,  MM1201, or SummaSketch graphics  tablet  with  Auto-
        Sketch.   The  driver makes AutoSketch a more  powerful  drafting
        tool  because a graphics tablet allows more  precise  positioning
        than a mouse, joystick, or Koala pad.  Support utilities for  the
        driver  are included that let you test your graphics  tablet  and
        alter the X,Y resolution.

        ** Distribution

        These copyrighted programs are provided free of charge.  They may
        be  distributed freely as long as no charge is made for the  pro-
        grams  themselves,  or any software package with which  they  are
        included.  The programs and all related documentation files  must
        be  distributed  together, and may not be  modified.   A  nominal
        charge may be made for the disk containing these programs.

        ** Warranty

        These programs are provided AS IS without any warranty, expressed
        or implied, including but not limited to fitness for a particular
        purpose.

        ** Disclaimer

        In no event will Patrick Swayne be liable to you for any damages,
        including any lost profits, lost savings, or other incidental  or
        consequential  damages arising out of the use of or inability  to
        use  these programs, even if Patrick Swayne has been  advised  of
        the  possibility of such damages, or for any claim by  any  other
        party.

        ** Preparation and Testing

        If you have a hard disk, copy the files ADISUM.COM,  TESTSUM.COM,
        and SETSUM.COM from this collection to your AutoSketch directory.
        If you have a floppy only system, you can copy the files to  your
        AutoSketch startup disk if there is room, or you can copy them to
        your system disk.

        The  file ADISUM.COM is the SummaSketch tablet driver.  It  is  a
        TSR (Terminate and Stay Resident) program that installs itself in
        memory  when you run it and remains there after it exits back  to
        DOS.   TESTSUM.COM  is the program that  tests  your  SummaSketch
        tablet,  and SETSUM.COM is the program that allows you  to  alter
        its resolution.  SETSUM is also used to set up the driver for use
        with the particular model of SummaSketch tablet you have.

        To  test  the operation of your SummaSketch tablet  with  ADISUM,


                                        1




        first  connect  the tablet to your computer as described  in  the
        SummaSketch  User's Guide.  Make sure that the stylus or puck  is
        plugged  into the tablet, and that the power supply is  connected
        and plugged into an AC outlet.  Make the drive/directory contain-
        ing ADISUM.COM and TESTSUM.COM the default.  If your  SummaSketch
        tablet is connected to serial port COM1, type

          ADISUM

        at the DOS prompt, and press Enter or Return.  If your tablet  is
        connected to COM2, type

          ADISUM 2

        and press Enter or Return.  After ADISUM signs on, type

          TESTSUM

        and  press  Enter or Return.  If the driver and your  tablet  are
        working correctly, TESTSUM will print

          SummaSketch tablet tests ok.

        and exit to DOS.  If you see the message

          Unable to communicate with tablet.

        it may means that you have specified the wrong COM port, or  that
        your SummaSketch tablet is not getting power, or that your serial
        port  is not functioning correctly.  If the problem is  that  you
        specified the wrong COM port, unload ADISUM from memory by enter-
        ing

          ADISUM U

        and reinstall it using the correct command.

        If  your  tablet  is connected properly, but it  is  not  working
        properly, you will see the message

          SummaSketch tablet did not initialize properly.

          Analog circuitry test:
          Digital circuitry test:
          Cursor/stylus operation:

        Beside  each of the last three lines above you will see the  word
        "Passed" or "Failed", indicating the result of each test.  If the
        cursor/stylus operation fails, it probably means that your stylus
        or puck (cursor) is not plugged in.  If you plug in the stylus or
        puck while the tablet is powered up, and then run TESTSUM, it may
        report  that all three tests have failed.  If that  happens,  run
        TESTSUM  again.  If either the analog or digital test fails  con-
        sistently when you have run TESTSUM a number of times, it  proba-
        bly  means  that you have a serious problem in  your  SummaSketch


                                        2




        tablet, and you should contact Summagraphics Corporation.

        ** Configuring AutoSketch

        Before you can use ADISUM and your SummaSketch tablet with  Auto-
        Sketch,  you will have to configure AutoSketch to work  with  the
        tablet.   If you have already configured AutoSketch for use  with
        another  pointing device, there will be a file called  SKETCH.CFG
        in  your AutoSketch disk/directory.  It is a good idea to  rename
        this file so that it will be available if you should decide to go
        back  to  the other pointing device.  For example,  if  you  have
        configured  AutoSketch  for  use with a  mouse,  you  can  rename
        SKETCH.CFG to SKETCH.MOU.  Note:  either renaming or deleting the
        file SKETCH.CFG will cause AutoSketch to enter the  configuration
        mode the next time it is run.

        After  you have renamed SKETCH.CFG, or if you  have not yet  con-
        figured  AutoSketch,  make  sure that ADISUM  is  installed,  and
        configure  AutoSketch  as directed in its manual.  When  you  are
        prompted  to "Select pointing device", enter 1  (Autodesk  Device
        Interface Pointer).  When you see the prompt "Interrupt number in
        hex  <79h>", just press Return or Enter.  Continue with the  rest
        of the configuration as required for your equipment.

        ** Operation

        To use AutoSketch with the SummaSketch tablet and ADISUM,  follow
        these steps.

        1.   Load ADISUM into memory.  To do this, type ADISUM or  ADISUM
             2  at the DOS prompt, and press Enter or Return.   You  only
             need  to do this once each type you boot up  your  computer,
             but no harm is done if you do it more than once.  If  ADISUM
             detects  that  it has been already installed in  memory,  it
             will display "ADISUM is already installed" and exit.

        2.   Configure ADISUM for your tablet.  ADISUM is  pre-configured
             for a 12 x 12 inch tablet, so you can skip this step if  you
             have  that type.  If you have a 6 x 9 inch tablet, you  must
             use  SETSUM.COM to configure ADISUM to work with it.  To  do
             that, enter

               SETSUM M9

             at the DOS prompt, and press Enter or Return.  You can  also
             use  SETSUM  to alter the resolution on both  tablet  types.
             This will be explained later.

        3.   Run  AutoSketch.  Using the graphics tablet with  AutoSketch
             is a lot like using a mouse, except that the position of the
             stylus  or  puck on the tablet corresponds  to  an  absolute
             position  of the pointer on the screen.  In other words,  if
             the stylus or puck is moved from anywhere to the lower  left
             corner  of your tablet, the pointer will move to  the  lower
             left  corner of your screen.  The pointer will move even  if


                                        3




             the  stylus or puck is picked up and placed at the new loca-
             tion.

        4.   When you are through using AutoSketch, you can remove ADISUM
             from memory by entering

               ADISUM U

             at  the  DOS prompt, and pressing Enter or  Return.   ADISUM
             uses  less  than 1 k of memory, but if things are  tight  on
             your system, every little bit of memory freed can help.

        ** Altering the X,Y Resolution

        A little explanation of how the ADISUM driver works is  necessary
        in order to explain what you will be up against if you decide  to
        alter  the X,Y resolution of the driver.  The  ADI  specification
        divides the screen up into 20480 units in both the horizontal (X)
        and vertical (Y) directions.  This is true even if the screen  is
        wider  than  it is high, as is usually the case.   Therefore  the
        vertical and horizontal ADI units are usually not the same  size,
        and the driver or tablet must compensate for this.

        The SummaSketch and MM series graphics pads are capable of having
        their horizontal and vertical resolutions set independently,  and
        so they can, in themselves, compensate for a screen divided  into
        different  horizontal and vertical units.  However,  the  maximum
        resolution in this mode is 508 units per inch.  If you have a  12
        x 12 tablet, you can see that means 6096 units across the tablet,
        which is far less than the 20480 units that the screen is divided
        into.   To compensate for this, the ADISUM driver multiplies  the
        reports  from the graphics tablet by a factor of 6 if it  is  set
        for a 12 x 12 tablet, or by 8 if it is set for a 6 x 9 tablet.

        My  goal in choosing the default resolutions used by  the  ADISUM
        driver was to have a given movement of the puck or stylus in  the
        X  direction  produce a certain movement of the  pointer  on  the
        screen, and the same movement in the Y direction produce the same
        movement on the screen.  Screen movements were determined by  how
        many  drawing units the pointer moved (with the grid  turned  on)
        rather  than  by actual movement on the screen as measured  by  a
        ruler.   Just about every screen will have a  slightly  different
        height to width ratio.

        When  a  resolution is specified for the graphics tablet,  it  is
        specified as the number of units across the whole tablet,  rather
        than the number of units per inch (while keeping in mind that the
        resolution cannot exceed 508 units per inch).  When ADISUM is set
        up  for  the 12 x 12 tablet, it sets it up with a  resolution  of
        3420 units in the horizontal (X) direction, and 4956 units in the
        vertical  (Y) direction.  These settings ensure equal  horizontal
        and vertical movement, and they also ensure that the entire width
        of the drawing tablet is used.  You must move the puck or  stylus
        from one side of the tablet drawing surface to the other in order
        to move the pointer from one side of the screen to the other.  In


                                        4




        the vertical direction, a portion of the tablet at the top is not
        used,  because  the screen is not as tall (in  terms  of  drawing
        units) as it is wide.

        When ADISUM is set up for a 6 x 9 tablet, it sets the  resolution
        to 2655 units in the horizontal (X) direction, and 2562 units  in
        the  vertical  (Y) direction.  With this tablet,  all  of  tablet
        surface is used in the vertical direction, put a small portion at
        the right edge is not used in the horizontal direction.  This  is
        because the width to height ratio of the tablet (in terms of even
        units) is greater than that of the screen.  Note:  I do not  have
        a 6 x 9 tablet, and the default values I used are based on calcu-
        lations, and have not been verified.

        If  you  would  like to experiment with setting  your  tablet  to
        different  X and Y resolutions than the default values,  you  can
        use the SETSUM program with this syntax

          SETSUM x,y

        Where  x and y are decimal numbers in the range 100 to 6000.   If
        you  have a 6 x 9 tablet, do not supply an X value  greater  than
        4572,  or  a  Y value greater than 3048.  When  you  are  through
        experimenting,  you  can  return the settings  to  their  default
        values by entering

          SETSUM M12

        if you have a 12 x 12 tablet, or

          SETSUM M9

        if you have a 9 x 9 tablet.

        ** Drawing One to One

        If you would like to adjust things so that one inch, for example,
        equals one drawing unit on the screen, I recommend that you  make
        AutoSketch  Zoom an appropriate amount rather than  messing  with
        the  graphics tablet resolution.  If you have a 12 x 12  graphics
        tablet,  you can turn the grid on and then use the Zoom Box  com-
        mand to zoom to a box 11.7 units wide (the tablet drawing surface
        is  actually 11.7 x 11.7 inches) by 8 or less units high.   After
        the zoom, a one inch movement on the tablet will equal a one unit
        movement on the screen.  If you have a 6 x 9 inch tablet, zoom to
        a  window 6 units high by 8 or fewer inches wide to get the  same
        result.

        In  metric  measure, the 12 x 12 tablet is 29.7 x  29.7  cm.   By
        setting the grid to a fractional unit size, it should be possible
        to zoom to a setting where one centimeter of movement on the  pad
        equals one grid unit on the screen.





                                        5