************************************************
                *                                              *
                *               L A B L P L O T                *
                *                                              *
                *                 Version 1.0                  *
                *                                              *
                *      A labeling progaram for use with a      *
                *        Hewlett-Packard 7470A plotter.        *
                *                                              *
                ************************************************
         
         

         
                                      by:
                                Philip Gilbert
                               9743 Sundew Drive
                             Houston, Texas  77070
         

         
         
       
         
                           
         
         
         
       
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
               
    
    

         
         
                         
                               TABLE OF CONTENTS
                 
                Introduction ............................. 1
                  
                Selecting Serial Port .................... 2
         
                Defining Character Height ................ 2
         
                Selecting Print Direction ................ 3
         
                Selecting Letter Slant ................... 4
         
                Selecting Horizontal Alignment ........... 4
                                       
                Selecting Vertical Alignment ............. 5
         
                Selecting Legend Boxes ................... 6
         
                Selecting Pen Locating Method ............ 7
                                
                Entering Labels .......................... 8
         
                Disclaimer ............................... 9
                Permission to Copy

                User Supported Concept .................. 10
         

         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         

         
         
                                     (1)   

                                  INTRODUCTION
          
         
         This program was originally designed to fill a gap in the 
         graphing capabilities of "1-2-3" by Lotus Development Corp.  
         It does that, but also provides a tool for generating text
         only graphics with a Hewlett-Packard 7470A 2-pen plotter.  
               
         The program begins with a main menu where the desired options 
         and the previous configuration are displayed.  To change an 
         option, simply press the number for that option.  It is not 
         necessary to press the ENTER key after the selection.  Any 
         time a choice is a single keystroke letter or number, it is 
         not necessary to press the ENTER key to initiate the choice.  
         
         When a selected option has been changed, the program returns 
         to the main menu with the exception of the option to begin 
         entering the labels.  An option can be changed as many times 
         as desired prior to selecting option 9: Entering Labels.  
         
         Options 7 & 8: Legend Boxes & Pen Locating, merely define 
         which questions the program will ask at a later point.  This 
         is explained further in the respective sections.
         
         The selected options are saved on a file called "LABLPLOT.CON" 
         when option 9 is selected.  This file must be copied along 
         with the program file for smooth operation.

         The program currently only plots the labels in the Block 
         character font.  Additional character fonts will be supported 
         in a future version.

         This program can be copied and shared with other people.  If 
         you find the program useful, you are encouraged to make a 
         contribution and to register in order to be notified of 
         future updates and enhancements.  The first enhancement being 
         planned is generation of legend boxes with hatching and 
         additional character fonts such as Roman and italics. 
 
         Even if a contribution is not made, I would be interested in 
         hearing any comments or suggestions you might have to make 
         the program more useful. The program is written in Basic so 
         it should be easy to make modifications for your particular 
         needs.  I only ask that modified versions of the program NOT 
         be distributed.  This is so that I will be able to help 
         someone with the program if they should contact me with a 
         problem.  If they have a modified version, I may not be able 
         to help them. 
       
         
         
         
         
         
                                        (1)

                             
    
    


         
         
                                           
                                      (2)
         
                             SELECTING SERIAL PORT
         
         This is option 1 of the main menu.  It gives you the choice 
         of directing output through COM1 or COM2 serial ports.  The 
         program is set up for the handshaking protocol for an IBMúPC.
         
         You must also select the baud rate that the plotter is set 
         to.  You have the choice of 75, 110, 150, 300, 600, 1200, 
         1800, 2400, 4800, or 9600 baud.  Refer to the plotter 
         instruction manual for the proper switch settings on the 
         plotter.
         
         This program has not been tested with other computers but it 
         should work properly with all IBMúPC compatibles.  If you 
         have any problem making it work, please let me know and I 
         will try to straighten things out.
         
         

                           DEFINING CHARACTER HEIGHT
         
         This is option 2 of the main menu.  It gives you the 
         opportunity to define the height of the characters.  The 
         width and the spacing between lines are automatically set.  
         The width will be about 2/3 the height.  The spacing between 
         lines will be approximately one character height.  
         
         The height is to be entered in whole or decimal inches.  For 
         your reference, the following are the heights of standard 
         type styles:
                   ELITE               .08
                   PICA                .10
                   ORATER              .16
         
         The height must be greater than .01 inch and less than 
         7úinches.  After typing in the desired height, you must hit 
         the ENTER key to return to the main menu.  If no value is 
         typed in before hitting the ENTER key, the computer will 
         beep, display a message that says the value is out of the 
         allowable range and will prompt you to type in an acceptable 
         height. 
                             
    

         
         
         
         
         
         
         
         
         

                                      (2)
         
         
         


         
         
                                      (3)

                           SELECTING PRINT DIRECTION 

         This is option 3 on the main menu.  It gives you the option 
         of selecting which direction you want the labels to be 
         printed in.  
         
         Typing an X (uppercase or lowercase) will cause the labels to 
         be printed in the lengthwise direction as shown on the sheet 
         below.
          
                 __________________________________________
                 |                                        |
                 |                                        |
                 |    This is a label printed in          |
                 |                                        |
                 |         the X direction.               |
                 |                                        |
                 |                                        |
                 |                                        |
                 |                                        |
                 |________________________________________|
              


         Typing a Y (uppercase of lowercase) will cause the labels to 
         be printed in the width direction as shown on the sheet 
         below.

                        _____________________________
                       |                            |
                       |                            |
                       |                            |
                       |       This is a label      |
                       |                            |
                       |       printed in the       |
                       |                            |
                       |        Y direction.        |
                       |                            |
                       |                            |
                       |                            |
                       |                            |
                       |                            |
                       |                            |
                       |                            |
                       |                            |
                       |____________________________|
                              
         
         
         
         
         
         
         
         
         
         
                                      (3)
      
                             


         
         

                                      (4)
         
                             SELECTING LETTER SLANT
         
         
         This is option 4 of the main menu.  It gives you the option 
         of having the letters printed upright or slanted forward 
         slightly.  The amount of slant is predefined and this option 
         is only to select whether the letters will be slanted or not.
         
         The Y or N response can be typed in either uppercase or 
         lowercase.  It is not necessary to hit the ENTER key after 
         typing in the desired letter.        

                                     
         
                         SELECTING HORIZONTAL ALIGNMENT
         
         
         This is option 5 of the main menu.  It gives you the option 
         of having the labels left aligned, right aligned or centered 
         on the initial pen location.  The desired alignment is chosen 
         by typing either an L, R or C (uppercase or lowercase).
         
         Selecting left alignment causes each line of the label to be 
         left aligned with the position of the pen when plotting 
         begins.
         This is an
         example 
         of a left aligned label.
         
         Selecting right alignment causes each line of the label to be 
         right aligned with the position of the pen when plotting 
         begins.
                                                     This is an
                                                        example
                                      of a right aligned label.
                                     
         Selecting center alignment causes each line of the label to 
         be centered about the position of the pen when plotting 
         begins.  It should be noted that the initial pen position is 
         the reference point for the alignment.  When center alignment 
         is chosen, only the first line is actually centered about the 
         initial pen position.  The other lines are centered below 
         this point.  In the example below, the initial pen position 
         was at the bottom of the space between the words "This" and 
         "is".
                                   This is an
                                    example
                              of a centered label.
                          
    
         
         
         
         
                                      (4)
         
         
                             

         
         

                                      (5)
         
                          SELECTING VERTICAL ALIGNMENT
         
         
         This is option 6 on the main menu.  It gives you the option 
         of having the labels printed above, below or centered on the 
         initial pen position.  Actually, the first line of the label 
         will be printed above, below or centered on the pen position, 
         the following lines will be spaced accordingly.
          
         Here is an example to
         demonstrate vertical alignment.
         
         In the above left aligned example, if you had selected 
         printing above the pen position, the pen would have been 
         positioned at the lower left point of the "H".
         
         If you had selected printing below the pen position, the pen 
         would have been positioned at the upper left point of the 
         "H". 
         
         If you had selected printing centered vertically, the pen 
         would have been positioned at the point where the crossbar 
         intersects the left upright of the "H". 
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
                                        
         

                                      (5)


         
         
         
                  
         

                                      (6)
         
                             SELECTING LEGEND BOXES
         
         
         This is option 7 on the main menu.  It is currently not 
         operational but will be very soon.  It gives you the 
         opportunity to have a legend box drawn to the left or right 
         of any or all lines of the label.  The legend box will be 
         hatched, crosshatched, or colored-in as you choose.  This 
         feature corresponds to the hatching scheme used in "1-2-3". 
         
         At this option you will be asked whether you want legend 
         boxes or not.  If you choose not to have legend boxes, you 
         will not have to answer certain questions when you are 
         entering the labels.  You will also be asked whether the 
         legend boxes are to be colored-in solid or hatched.
         
         If you choose to have legend boxes, you will be given the 
         opportunity to select which lines of the label will get 
         legend boxes and which will not.  This allows you to define 
         your data with more than a one line description. 
         
         You do not have the option of selecting which type of 
         hatching goes with which line of the label. The boxes will be 
         hatched as shown below which corresponds to the convention 
         used in "1-2-3": 
                   / / / / /      First Box
               
                   \ \ \ \ \      Second Box
         
                   /////////      Third Box
         
                   \\\\\\\\\      Fourth Box
         
                   X X X X X      Fifth Box
                    
                   XXXXXXXXX      Sixth Box
         

         You will be given the opportunity to change the pens before 
         every legend box is drawn so you can change the pen color if 
         you want.  The label will also be plotted in the same color as 
         the legend box.  
         
         Legend boxes can only be used if the labels are left aligned 
         or right aligned.  If they are left aligned, the legend boxes 
         will be aligned to the left of the labels.  The labels will 
         also be aligned one space to the right of the legend boxes.  
         If the labels are to be right aligned, the legend boxes will 
         be right aligned, one space to the right of the labels. 
         
         
         
         
         
                                      (6)

         
         
         
         

         
         

                                      (7)
         
                         SELECTING PEN LOCATING METHOD
         
         
         This is option 8 on the main menu.  It gives you the choice 
         of locating the pen position for the first line of the label 
         with the plotter arrow buttons or by inputing coordinates 
         into the computer.
         
         Positioning the pen with the plotter arrow buttons is simply 
         a matter of manually positioning the pen with the buttons on 
         the plotter until the pen is where you want it to be. This 
         will depend on whether the labels are to be left aligned, 
         right aligned, etc.  If placement is critical, it is 
         suggested that you place a transparent sheet over the good 
         sheet and put the pen down to ensure proper placement.  Be 
         sure to raise the pen before removing the transparent sheet 
         or moving the pen. 
         
         Positioning the pen by inputing the coordinates requires that 
         you know how many inches from the reference corner you want 
         the initial pen position to be.  The X coordinate must be 
         greater than 0.5 and less than 10.5 inches.  The Y coordinate 
         must be greater than 0.5 and less than 8.0 inches. You must 
         hit the ENTER key after typing in each coordinate. 
         
         If the Y coordinate is outside of the acceptable range, you 
         must reenter the X coordinate and the Y coordinate.
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         

                                      (7)
         
                             


         
         
          

                                      (8)
         
                                ENTERING LABELS 

         
         This is option 9 on the main menu.  This is where the current 
         configuration is saved, the pen is located, the labels are 
         input, the legend boxes are assigned to particular lines and 
         the labels are plotted.
         
         If you decided to position the pen by coordinates, you will 
         be given the opportunity to input the coordinates now.  See 
         the section SELECTING PEN LOCATING METHOD for more 
         information.
         
         Each line of the label that you want to be printed is entered 
         at this point.  After entering each line of the label, hit 
         the ENTER key.  You may enter up to 20 lines per label.  The 
         only limitation is that the label cannot contain any commas.  
         Commas must be put in by hand later.  Simply leave a space 
         where the comma is supposed to go.
         
         If you chose to have legend boxes printed, you will be given 
         the opportunity after each line is entered to specify whether 
         a legend box is to be printed beside the label or not.  This 
         gives you the capability to assign legend descriptions that 
         are more than one line long.  You then specify which type 
         of hatching you want to have plotted in the legend box.  The 
         program will pause before each line that is to have a legend 
         box to give you the chance to change the pen if you want to. 
         
         You are instructed to install a pen in the left pen stall at 
         this time and make sure the plotter is on.  If you decided to 
         position the pen by the plotter control buttons, you will be 
         instructed to position the pen at the proper position for the 
         first line of the label.  It is a good idea to place a 
         transparency over the sheet you will be plotting the label 
         on, and put the pen down to ensure it is exactly where you 
         want it to be.  Always raise the pen before moving it to 
         prevent accidental marking.
         
         The program will plot the label when you are ready and you 
         can sit back and watch it work.  You will be given the 
         opportunity to change the pen before each line of the label 
         is plotted.  The only thing you have to do is change the pens 
         when instructed to do so or hit a key to continue plotting. 
         
         
         
         
         
         
         
         
         
         

                                      (8)

                             


         
         
             
                                      (9)

         DISCLAIMER
         
         In no event shall the author be liable for any damages, 
         including any lost profits, lost savings or other incidental 
         or consequential damages arising out of use of or inabliity 
         to use this program, even if the author has been advised of 
         the possibility of such damages, or for any claim by any 
         other party.
                           

         PERMISSION TO COPY
          
         Individuals are granted permission by the author to freely 
         copy the LABLPLOT program and documentatin for their own use 
         or to share with others, so long as no price or other 
         consideration is charged.
         
         Computer clubs and other non-profit orgnizations are granted 
         permission by the author to freely copy the program and 
         documentation and share it with their members, so long as:
         
         1.   No price or other consideration is charged with the 
              exception of a distribution charge to cover the cost of 
              the diskette and computer copying time.
               
         2.   Club members are informed of the user-supported concept 
              and are encouraged to support it with their donations.
         
         3.   The program and documentation are not modified in any 
              way and are distributed together.
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
         
             
                                      (9)
 
         
                             


         
             
                                      (10)
                                         

         THE USER-SUPPORTED CONCEPT
         
         You are encouraged to copy and share this program with 
         others.  If after evaluating this program, you find it to be 
         useful, I trust you to send a contribution($15.00 suggested).  
         The contribution should be sent to:
         
                                 Philip Gilbert
                                9743 Sundew Dr.
                              Houston, TX   77070
         
         User-supported software is an experiment in distributing 
         computer programs based on the following beliefs:
               
         1.   The value and utility of software is best assessed by 
              the user on his/her own system.  Only after using a 
              program can one really determine whether it serves 
              personal applications, needs, and tastes.
         
         2.   The creation of independent personal computer software, 
              can and should be supported by the computing community.
         
         3.   Copying and networking of programs should be encouraged, 
              rather than restricted.  The ease with which software 
              can be distributed outside traditional commercial 
              channels reflects the strength, rather than the 
              weakness, of electronic information. 

                                                                     
         Please join the experiment.
         
         If you believe in these ideals, your contribution will be 
         appreciated to help make them work. 
         
         Whether or not you send a contribution, please write me with 
         any suggestions or comments you have about the program.  If I 
         hear from you, I will put your name on my mailing list to 
         notify you of future updates.  Contributing users will 
         recieve the upgrades free of charge.
         
         Thank you for your support.
         
         
         
         
         
         
         
         
         
         
         
                                         
         

                                      (10)