QUICKEYS                                   Leo Forrest
          Command                        PC Magazine Vol 5, No 5
		Copyright 1985 Ziff-Davis Publishing Company
          ______________________________________________________

          Purpose:  Accelerates the "typematic" repeat rate of a
                    PC or XT keyboard.  A built-in subprogram is
                    included that instantly clears the keyboard
                    buffer to prevent sending excess accumulated
                    keystrokes to the display.

          Format:   QUICKEYS     (loads memory-resident program)
                    <Alt-Shift>         (clears keyboard buffer)

          Remarks:  While the keystroke repetition rate of the PC
                    AT is adjustable, that of the XT and the PC
                    is fixed at approximately nine keystrokes per
                    second.  When QUICKEYS is loaded (normally
                    through your AUTOEXEC.BAT file), the
                    repetition speed is approximately doubled.
                    Successive loadings of QUICKEYS (each
                    requires about 672 bytes of memory) can be
                    used to increase the keyboard speed still
                    further, if desired.

                    Notes:

                    1.   QUICKEYS is a memory-resident program
                         that inserts itself both into the timer
                         tick and keyboard interrupt routines.
                         It is not compatible with some other
                         memory-resident software and with
                         programs that appropriate the keyboard
                         interrupts.