Documentation for Loci ver 1.1



  Summary:
     Loci  is a public domain program by Greg Jackson for  doing  Root
     Locus  design.   Loci runs on IBM and compatible.  It  does  not
     require graphics capability but will make use of it if available.
     All  major graphics systems are supported including Hercules  and
     AT&T monochrome graphics.

  Commentary:
     Root locus design is fundamental to control theory and is used by
     Chemical,  Electrical,  and Mechanical engineers.   Basically  it
     solves for the roots of the characteristic equation in a transfer
     function  and  plots them in the complex plane.  If  this  sounds
     like absolute nonsense then you might as well quit right here.

  Features:
           * Transfer function descriptions can be stored to disk,
             read from disk, and edited.
           * Menu driven, very simple for first time use.
           * Solutions in the form of calculated poles, zeros, and
             loci can be stored in ASCII format for use with other
             programs.
           * Hardcopy of root locus plots is available for Epson or
             IBM dot matrix printers.
           * Plotter interface through TPLOT (another public
             domain program).
           * It's free!

  Limitations:
           * Maximum order of the polynomial is 20.
           * Maximum number of loci is 100 x order (70 for 8087).

  Legal Stuff:
     This  program cannot be sold for profit other than  a  reasonable
     reproduction  cost.  The author is not responsible for damage  to
     property, profit, or reputation which may result from use of this
     program.  If your high performance controlled system  experiences
     `crash and burn' don't come crying to me.

  Technical Stuff:
     Root  Locus  analysis was developed by W.R. Evens in  1950.   The
     program  uses  Laguerre's method and linear  deflation  for  root
     calculations.   The root calculation code is taken directly  from
     Borland's Numerical Method toolbox.

     The  program  is written in Pascal using Borland's  Turbo  Pascal
     v4.0  and  makes  use of Borland units  CRT,  PRINT,  and  GRAPH.
     Source code is available to anyone less the numerical code  which
     is copyrighted to Borland.  For source code contact....

       mail: Greg Jackson            modem: CIME-ISE BBS
             1616 Capital Ave.              (608) 233-3378
             Madison, WI 53705              8/N/1  24 hrs

     Comments, questions, and suggestions are welcome.  This is public
     domain, not  shareware. Money  is not requested.  However, if you
     want to ship me a 12-pak, I  like  Special Export.  Please report
     any  problems  with  the  program.   Program  output  of transfer
     function description and loci should  be sent along with  problem
     description.

  History
     Ver 1.1  (2/13/88)
      - Speed increase of 400% by better implementation of 8087.
      - Unit circle added and transfer function error checking is
        relaxed for use with Z-transforms & discrete systems.
      - A bug in the printout was fixed.

  General operation:
     The  menu driven program is generally self apparent.  This  brief
     documentation  should  be read in full because it  describes  the
     details of the program which are not self apparent.

  Main Menu:
     Rather  than  selecting the "Quit" command you can  quit  at  any
     place by pressing the ESC key.

     The  default  command is automatically  incremented  through  the
     logical  progression  of "Enter Function", "Calc  &  Plot",  then
     "Plot only".

  Entering a transfer function:
     The values displayed in dim video are default values.  To  accept
     defaults simply press <ENTER> at the prompt.  If you already have
     a transfer function entered or loaded from disk you can review or
     edit it by accepting or changing the defaults.

  Hardcopy:
     When the plot is on the screen you can initiate a graphic printout
     by  pressing 'p'. Pressing any other key will return you  to  the
     main menu.  The printout is pretty slow.  If you decide you  want
     to cancel in the middle just press ESC.

  File Menu:
     File  operations  are limited.  There is  no  default  extension.
     Directory listings are not available from the menu.  Remember the
     file names you want before you start the program.

     The  files  output are ASCII.  You can create  transfer  function
     description  files  with  any text editor if  you  like  but  the
     easiest  way is to enter the function in LOCI and then  save  it.
     The numbers must be in the same sequence but the comments are not
     necessary.    The  pole/loci/zero  files  are  the   results   of
     calculations  and can be used for plotting with  other  programs.
     Each pair of numbers is a point on the complex plane (ie: a+bs is
     an  x,y   pair).   The  poles are  noted in the file.  In general
     the  pairs that  come after a pole  correspond to the same  root.
     If you use  this  file with a pen plotter  do NOT take this as  a
     rule.   The  numerical  estimation technique  will sometimes find
     alternate roots in  conjugate  pairs.   This  switching  back and
     forth will make  a mess if  you try  to connect points  with  the
     plotter, so plot points, not lines. The file will also reveal the
     location  of far  zeros.   The scale of the plot is determined by
     the loci.  If a zero is  outside of the scale it will not be seen
     on the screen  but it  will appear  in the file as a point on the
     complex plane.

  Using the 8087:
     This  is  a numerically intensive program.   The  program  cannot
     recognize  the  presence  of a math  chip  and  act  accordingly.
     Rather  you  should  use the right version.   LOCI.EXE  does  all
     floating point calculations in software and LOCI87.EXE makes  use
     of  a  math chip. Using a math chip will make  things  very  much
     faster.   The  difference is particularly  noticeable  on  higher
     order  equations.  Both  versions  should  be  included  in   the
     distribution package.

  There are six adjustable defaults:
     Gain exponent:  The loci calculated tend to pile up near poles or
     zeros.   To  get them spread out somewhat the gains used  in  the
     closed  loop  calculations  are stepped  exponentially.   A  gain
     exponent  of 1.0 indicates a linear gain distribution.   Using  a
     gain  exponent less than 1.0 will make the gain  increments  much
     smaller  at the higher gain values.  This will tend to  make  the
     loci pile up toward zeros.  Using a gain exponent larger than 1.0
     will  make  the gain increments much smaller at  the  lower  gain
     values.  The result is a distribution of loci shifted toward  the
     poles.  A gain exponent of 2.0 provides a parabolic  distribution
     of gain.  To get a feeling for this vary the exponent between 0.1
     and 5.0 for the same transfer function.

     Axis  line type:  This determines the line type for the real  and
     imaginary axis.  A solid line generally looks best.

     Number  of  Loci:  The total number of  characteristic  equations
     calculated.  With n roots to each polynomial the total number  of
     points is  n x NumLoci.  Larger numbers give nicer plots but take
     longer for calculations.

     Print  Mode:   There  are  4 different  print  modes.   The  main
     difference  in  each  one is the number of dots  per  inch  on  a
     horizontal  pass.   Each  printer pin is a  representation  of  a
     screen pixel.  Since a number of screen types are supported, each
     with  a  different aspect ratio, the print mode that  works  best
     will vary with both the video type and hardcopy orientation.

     Orientation:   This  refers to the orientation  of  the  hardcopy
     printout.   Horizontal is as it appears on the screen.   Vertical
     is turned +90 degrees.

     Loci Size:  The size of the point plotted in pixel units.

     Unit  Circle:   The  unit  circle  is  put  on  the  Z-plane  for
     determination  of stability of discrete systems.  This  will  not
     show up on the Tplot plotter output.








  Problems with LOCI:
     The  calculation part of LOCI has been very dependable.   If  you
     appear  to  get garbage on the graphic display don't  assume  you
     have faulty numerical values.  LOCI graphic output was tested  on
     a  number of typical systems.  Very unstable systems,  very  fast
     systems, and very slow systems may not display well.  If you  get
     problems  like that use the file output function to get the  data
     onto  disk.  You can then verify the data in any of a  number  of
     ways.



**************** The following details plotter interface *******************
                If you don't use a plotter just quit here.




  Plotter Interface:
     While  LOCI will not run a plotter directly, it will  create  data
     files  and  command  files that are directly  usable  by  another
     public  domain  program,  TPLOT  by  Dr.  Dudley  Benton.   TPLOT
     supports  a number of graphics devices including Hewlett  Packard
     graphics terminals, Tektronix terminals, IBM color graphics,  and
     the  7470, 7475, 7550, & 9872 HP pen plotters.  I use it with  an
     Epson plotter that emulates the HP graphic language (HPGL) and it
     works fine.

     LOCI  does this by creating data files and a TPLOT command  file.
     The TPLOT command file is necessary since TPLOT will only receive
     instructions  from an instruction file specified on  the  command
     line  (ie:  the  DOS prompt A>).  The  TPLOT  command  file  will
     include scaling commands for the plot which are calculated on the
     basis of the calculated data.  It also contains the names of  the
     data  files.  It is critical that you provide the  proper  format
     for  command  file by making available a  working  TPLOT  command
     file.  LOCI will read your working command file, find the  places
     to  make  changes,  and  then write out a  new  command  file  of
     whatever  name  you  specify.  The reason for  the  original,  or
     template,   is  that there needs to be much more in  the  command
     file than scaling and name commands.  The command file also needs
     to have titles, pen colors, type of plotter, baud rate, and  lots
     of other things specified.  The command file template must be  in
     the  default  directory and must have the name  ROOTLOCI.PLT.

     A  typical  template should be included among the  files  in  the
     distribution package of LOCI.  The distribution package DOES  NOT
     include   TPLOT.   TPLOT  is  almost  300K  and  is   distributed
     separately.   You  should be able to find it on  bulletin  boards
     which have an engineering/scientific slant.










     The  command template included is for an HP 7475 plotter  set  to
     run at 9600 baud through COM1.  It uses pen 1 for the axis, pen 2
     for  poles,  pen  3 for loci, and pen 4 for zeros.   The  strings
     @XAXIS,  @YAXIS, @POLE, @ZERO, and @LOCI which are in the  sample
     command file are not seen by TPLOT which only looks at the  first
     few  characters  of  each line.  The @ strings  must  be  in  the
     ROOTLOCI.PLT  file  for successful creation of  the  new  command
     file.   These  key words must be upper case.   The  LOCI  program
     looks for those strings to know what lines to replace in the  new
     command  file.  When you select TPLOT output in the LOCI  program
     the following things happen....


     1)  LOCI  will  look  for the file ROOTLOCI.PLT  in  the  default
         directory.

     2)  LOCI  will  ask  you for a filename for  your  output.   Lets
         assume you call it `servo'.

     3)  LOCI  will copy ROOTLOCI.PLT to a new file SERVO.PLT.  As  it
         does  this it modifies certain lines marked in  the  original
         file with the @ signifier.

     4)  LOCI will create SERVO.POL, SERVO.ZRO, and SERVO.LOC.   These
         are the datafiles that are used in plotting.

  What Happens next ?
     If  the original ROOTLOCI.PLT template was  correctly  configured
     for  your  system (baud rate, plotter type, etc.), then  the  new
     file will work with the newly created datafiles.  After you  exit
     the LOCI program a simple call on the command line...

      A>TPLOT SERVO.PLT  <cr>

     will call up TPLOT and your plotter should start chugging away.







  In Summary :
     When calling the TPLOT output from the FILE function in the LOCI
     program, LOCI will...

          read in   : ROOTLOCI.PLT
          write out : *.PLT
                      *.POL
                      *.LOC
                      *.ZRO

     Then the  TPLOT  program can read the  instructions  in *.PLT to
     plot the data found  in  *.POL,  *.LOC, and *.ZRO where the * is
     specified by the user.



  Problems in plotting
     Most of the problems involve configuration of the original  TPLOT
     command  file (ROOTLOCI.PLT).  TPLOT can be a bit tricky to  use.
     The  best way to approach this is to modify the  sample  included
     rather  than  creating a new command template.   Don't  let  this
     discourage  you, once you get it working each run  usually  works
     perfectly.

     TPLOT will only work with integer scale factors.  This means that
     if  your root locus plot goes from -1.2e-2 to 0 on the real  axis
     you  will get a plot with a scale from -1 to 0.  This limits  the
     output when doing analysis of very slow systems.  LOCI will  take
     care to provide only integer values in the command file but  this
     does  not do much good  since  the minimum  integer scale of  0-1
     fails to display very small values correctly.

     You  will often get error messages from zeros out of range.   The
     scaling  is done on the basis of the loci and poles.   Often  you
     will get zeros that are a long way off the scale.

     If  you have problems getting the TPLOT interface going don't  be
     shy to contact me or to contact Dudley Benton.  I can be  reached
     through  the BBS  listed near  the  top of this file.  Dr. Benton
     often calls the BBS as well.