VMiX 286 Version 1.20
                         ---------------------

                                   By
     
                     Commercial Software Associates
                     P O B  241863, Village Station
                      Westwood, California  90024
                            (213)  649-0369



This is the First official (non BETA) release of VMiX, VERSION 1.20.

New commands have been added which enhance the multitasking abilities
of VMiX, at the console or at a serial port terminal.  Multiuser is
still fully supported, but the utility of VMiX for single station
users is increased.  The new 'dosjob' command and the keyboard
reassignment hot key, Alt-w, automatically manage background jobs
and multiple screen windows.

We appreciate the comments and help of all the users, who through
various BBS's helped debug VMiX versions 1.1X. Thanks!

You may copy VMiX freely for non-commercial distribution,
provided you follow the restrictions in the LIMITED SHAREWARE LICENSE
below:



             ***  COPYRIGHT NOTICE  ***

      Copyright (c) 1987 by: J. Anthony Borras
                All rights reserved


              LIMITED SHAREWARE LICENSE

      - VMiX 286  may be  copied for others to
      tryout, subject to the following copying 
      restrictions   specified  by  this  time 
      limited license:

          All  copies   distributed to  others 
        must  include a copy of the  Copyright 
        Notice, the Limited Shareware License, 
        Disclaimer   of  All  Warranties   and 
        Liabilities,  and the Software License 
        Agreement. These documents are ALREADY
        incorporated into  file  MANUAL.DOC in
        the distribution archive VMIX.ARC.

        A registration fee of $49 is solicited
        from personal users (up to 3 CPU's) as 
        a condition  of continued  use of  the 
        program beyond a trial usage period of 
        30 days.

      - The  party  agrees  that  unauthorized 
      usage  under this  agreement will  cause 
      great damage to the licensor, Commercial 
      Software Associates.




      REGISTRATION fee .................   $49.

      SOURCE license ...................   $99.
      (+ $50, if upgrade from registration fee)

      UPGRADE Version 1.XX  ............   $20.




        VMiX files are stored in binary in file VMIX.ARC
        Download load with protocol and use ARC to extract.

This is a one person effort.  If you are interested in registering,
pricing for support, the programming interface documentation, the new
full printed manual, the source code, or contributing in a team
effort to come up with something more useful, please contact me.

                                  Enjoy exploring VMiX,

                                       Tony Borras



* VMiX is not presently a full operating system.  It provides the
services of a multiuser operating system supervisor.  The VMiX kernel
ties tightly between the host operating system I/O services and the
user applications.  The functional goal of the VMiX kernel is to
arbitrate the use of system resources by individual tasks with either
or both UNIX I/O or MSDOS I/O.

* VMiX release 1.20 incorporates enhanced multitasking support.
The console screen can be automatically partitioned into up to four
windows, for a total of 4 tasks executing from the console.  The active
task controls and responds to the console keyboard.  The active task
can be switched, at any time, by pressing the hot key, Alt-w.

* VMiX provides concurrent multiprocess capabilities to the host
operating system, which will still service most of the low level
interface to the computer hardware.  NOTE:   MSDOS disk driver
reentrancy problems are not addressed by this release.  If two tasks
are requesting disk I/O,  one is placed in IOWAIT by VMiX, while the
other completes.

* VMiX release 1.20 does not operate in 286 protected mode at all
times.  Hence, it can be used in 8088 PCs.  System services are
provided in sysgate.asm to execute your own functions in protected
mode.   The debugger "assign gdt" method allows entries to the VMiX 
GDT.  This can also be done with the memory manager system service.

* REMOTE permits a user to call a remote PC running VMiX, and
teleoperate, as if he were at the console of the remote PC.  Useful 
for remote customer support of application programs,  offsite login
and operations. 

* With VMiX you can run programs  like Microsoft's  WINDOWS at the
console and BASIC, DEBUG, TURBO PASCAL, WORDSTAR 3.2, WORDSTAR 4.0,
or DBASE II at a COMM terminal.  Multiple BASIC interpreter sessions
are supported.

* Supports a maximum of five users (only because of COMM limitations),
each with multiple processes up to a maximum of 16.

* SPAWN or '&' permits a script of VMiX shell commands to be submitted
to a background process executing the VMiX shell.  This allows for  
background jobs like compiling or printing by a concurrent child
process.

* Loadable character fonts, 33 line CGA display and 43 line EGA
display.  EGA support not included in this release.

* Console operator status line and passive fault-tolerance.

* Built-in debugger (more like a VMS Monitor, right now).

* Memory manager and memory mapper.

* User specified windows in both alphanumeric and hires graphics modes,
  at either the console or VT-100 COMM terminal.

* Assembly and C language interface.

* Interrupt 15h System Services.

Today VMiX is 94K of code and 16K of Kernel data.
80% Microsoft C and 20% MASM.
--------------------------------------------------------------------

The VMiX 286 System consists of the fifteen files described below:


MASTER DISK CONTENTS

- VM_BOOT.EXE -
The VMiX start-up program.  To start, type VM_BOOT from MSDOS's  A> 
prompt and press <RETURN>.

- DSTAT.EXE -
Utility executed by user to view device and channel status.

- PS.EXE -
Utility executed by user to view processes status.

- SYSGATE.OBJ -
Link object file for VMiX programming interface.



   SOURCE FILES              DOCUMENTATION FILES

SYSGATE.ASM               MANUAL.DOC
DSTAT.C
PS.C
C_BIOS.H                 |you need   GEM DRAW   and a |
$_KERNEL.H               |CGA to print Appendix A and |
$_CONFIG.H               |Appendix C figures.         |
$_MEM.H
$_PROC.H                  VMBOOT.GEM
IO_CHAN.H                 VMIOOBJ.GEM
IO_IRP.H                  VMIX.GEM
IO_OBJ.H                  VMNAMES.GEM
                          VMOBJS.GEM
                          VMSCHED.GEM
                          VMSHELL.GEM
                          VMSTATUS.GEM
                          VMSTRUCT.GEM
                          VMSYNC.GEM



              I N S T R U C T I O N S
              -----------------------

      1)   Upon  receipt  of   your   SHIPPING 
           Diskette, copy the three files:

           VM_BOOT.EXE, DSTAT.EXE, PS.EXE, 
           onto your own System Diskette.

      2)   Using your  editor, create  a  file 
           named   CONFIG.SYS.    Include  the 
           following two lines:

           BUFFERS=20
           FILES=20

           and, save the file to  your  system 
           boot disk.

      3)   To  execute  the VMiX  286  program 
           requires   MSDOS  Version  2.10  or 
           above, and 256K of memory.  A color 
           graphics  card,  CGA is recommended 
           for  the console  display.

           If  you have a Monochrome  Adapter, 
           VMiX will sense it.

           Release  1.20  does not operate  in 
           286 protected mode at all times, so 
           it  will  execute properly  in  PCs 
           with 8088 processors.   Start  VMiX 
           by typing:

           A> VM_BOOT <RETURN>

              When VMiX starts, pressing <RETURN>
              will display the available commands.

              Try:    debug <RETURN>
              (note the prompt will change to - )
              then, try 'set' or 'exam' and VMiX
              will display how to complete the
              command (ie., help, VMiX style).
              VMiX will prompt for most command
              arguments, if not included in the
              command line:
                 (ie., type 'set video -m')
              Try:    set term -t <RETURN>
              to see the terminals supported.

      4)   The  RS232 cabling for COM1  and/or 
           COM2    should    be    constructed 
           depending  on whether the  host  PC 
           will   be   connected  to  a   dumb 
           terminal or to another PC acting as 
           a terminal.


             PIN                         PIN

      H      1                           1
      O
      S      2 -- - _           _ _ - -- 2
      T               -_ __ - - 
             3 __ _ -         - - - _ __ 3    T
      S                                       E
      e      4                           4    R
      r                                       M
      i    --5                           5    I
      a  -|                                   N
      l |  --6                           6    A
        |                                     L
      P |    7 ------------------------- 7
      o |
      r |  --8                           8
      t  -|
           --20                          20



         See  Part II,   Using VMiX 286,  for 
      detailed  instructions regarding the use 
      of VMiX 286 commands and options.
----------------------------------------------------------------------------

                          VMiX COMMAND LOOK-UP QUICK REFERENCE

              |ROOT   |DEBUG                                               |
              |LEVEL..|LEVEL...............................................|
              |   0   |   1   |   2                                        |
               ------------------------------------------------------------
              |debug                                                       |
              |       |read                                                |
              |       |write                                               |
              |       |set                                                 |
              |               |video                                       |
              |                  -b, " sets video background color"        |
              |                  -c, " sets window color attribute"        |
              |                  -f, " sets video foreground color"        |
              |                  -m, " sets video mode (1 - 7)"            |
              |                  -s, " toggles status line display ON/OFF" |
              |                  -w, " sets root window size:              |
              |                        y0, x0, y1, x1"                     |
              |                  -W, " auto partitions (1 - 4) task windows|
              |                        (Alt-w toggles kbd)"                |
              |               |remote                                      |
              |                  -c, " selects remote channel"             |
              |                  -l, " sets polled terminal login channel" |
              |               |baud                                        |
              |                  -c, " sets communications:                |
              |                        chan, baud, parity, word, stop"     |
              |               |debug                                       |
              |                  -m, " toggles manager's message           |
              |                        displays ON/OFF"                    |
              |                  -t, " toggles scheduler clock tick        |
              |                        processing ON/OFF"                  |
              |                  -w, " sets shutdown wait delay: seconds"  |
              |               |font                                        |
              |                  -t, " sets font type (0 - 3)"             |
              |               |terminal                                    |
              |                  -t, " selects terminal type (0 - 9)"      |
              |               |process                                     |
              |                  -p, " sets process priority (0 - 31)"     |
              |                  -b, " sets process shell buffer           |
              |                        size (0 - 127)"                     |
              |                  -m, " sets process maximum MSDOS          |
              |                        nesting level"                      |
              |               |pool                                        |
              |                  -a, " adjusts transient program memory:   |
              |                        MCB(seg), nusize(para)"             |
              |                  -l, " sets exe image memory allocation    |
              |                        limit (0 - 1024K)"                  |
              |                  -o, " sets transient program memory owner:|
              |                        MCB(seg), nuPSP(seg)"               |
              |       |init                                                |
              |               |baud                                        |
              |                  -c, " sets communications:                |
              |                        chan, baud, parity, word, stop"     |
              |       |examine                                             |
              |               |memory                                      |
              |               |mcb                                         |
              |               |pool                                        |
              |               |process                                     |
              |       |assign   [gdt]                                      |
              |       |deassign [gdt]                                      |
              |       |quit                                                |
              |remote                                                      |
              |  -c, " selects remote channel"                             |
              |  -l, " sets polled terminal login channel"                 |
              |exec                                                        |
              |  -a, " adjusts transient program memory:                   |
              |        MCB(seg), nusize(para)"                             |
              |  -l, " sets exe image memory allocation                    |
              |        limit (0 - 1024K)"                                  |
              |  -o, " sets transient program memory owner:                |
              |        MCB(seg), nuPSP(seg)"                               |
              |       |dstat.exe                                           |
              |              " utility displays all device(s) status"      |
              |          -a, " selects only assigned objects"              |
              |          -r, " selects only free objects"                  |
              |       |ps.exe                                              |
              |              " utility displays all process(es) status"    |
              |       |'MSDOS command...'                                  |
              |chprio                                                      |
              |spawn                                                       |
              |  -c, " selects spawn i/o channel and script"               |
              |kill                                                        |
              |quit                                                        |
               ------------------------------------------------------------