CoreView(tm)

                     A Window Into Your PC Memory


                             Version 1.0

              Copyright (c) 1989-1991 RolySoft, Denmark




What is CoreView?
-----------------

CoreView is a small but fast memory  viewer.  With help of CoreView you
may  look through  the  memory of  your  computer.   CoreView also  has
facilities  for   searching  memory  for   specific  strings   or  BIOS
extensions.

CoreView is  particular a great  tool if you  are going to  install new
hardware in your computer.  Often you have to set jumbers on the add-on
card to install its BIOS into the right address space.  But WHAT is the
right address space? With CoreView you  may browse through ROM at C000h
thru F000h and look for empty slots.

CoreView is also  capable of viewing memory  in real time.  What  do we
mean with  that? You  may enable  a function  we call  "timed display".
While this function is on, CoreView continously updates the screen with
data from memory.  If  any bits change, you will see  it immediately on
the screen.


Q quick tour through the CoreView functions
-------------------------------------------

CoreView has many functions.  As all functions are easy to use, we will
only use little  space to explain them.   You may call the  help screen
inside  CoreView by  hitting Alt-H  from  the main  screen.  This  help
screen summarises most of the functions.

First of all  you may scroll through  memory.  To do this,  you use the
arrow keys, Home, End etc.  All PCs  are capable of addressing at least
1 Mb of memory.  With CoreView you may inspect this 1 Mb address space.
By using the arrow  keys, PgUp, PgDn, Home, End and  many control keys,
you may browse through  this 1 Mb address space.  At  the bottom of the
PC  memory there  is  always  RAM installed.   When  you  go to  higher
addresses,  the PC  has  ROM installed.   RAM is  memory  which may  be
changed by the CPU.  ROM is Read Only memory, which means it may NOT be
changed.  If CoreView  encounters a ROM area,  you will see a  star (*)
right after the  address.  This star tells you, that  you are currently
looking at ROM locations.

If you are using a colour monitor, you may have noticed that some bytes
are high-lighted while others aren't.  All standard figures and letters
are shown in a  bright colour by CoreView to make it  easier for you to
recognize human-readable strings.

If you  want to  search for a  specific string, you  may do  that.  Hit
Alt-S to enter the  search input screen.  Enter the string  you want to
search for.   In the upper  input window  you may enter  all characters
between 20h  and FFh.  If  you also need to  search any of  the control
characters, you should  hit the Tab key once, and  enter the characters
as two-digit hex numbers.  Hit Enter to  begin the search or hit Esc to
abort.

You may choose  to search for an exact  match, or you may  search for a
match, which is case-insensitive, eg.  upper- and lowercase letters are
treated equal.  Use Alt-C in the main screen to change the search case.

If CoreView finds your search string, and you want to repeat the search
for the next copy, then hit Alt-R to repeat.

CoreView displays  a search message  in the  lower right corner  of the
screen, while it's searching.  The  actual search is NOT interruptable.
On 386s a 1 Mb search takes  approximately 2 seconds.  On XTs and other
relatively slow  computers, the search may  take 15 seconds or  more to
finish.

If you want to jump to a total different address, you may enter it into
the address window.   When you hit Enter,  CoreView is set to  this new
address.  You may also pick up the  current address you are looking at,
and put it into the input box.  Hit Ctrl-Enter to read the address from
the current  window position.  If you  want to normalize  this address,
just  hit  Alt-N.   What  do  we  mean  with  'normalized  address'?  A
normalized address,  is an address  with an  offset part always  in the
range 0000  thru 000Fh.

CoreView provides you with two functions to specify how data are shown.
If you press Alt-W memory is displayed in wide format.  This allows you
to see more  data on a single  screen.  To switch back  to the standard
hex display,  hit Alt-W  once more.  Alt-A  acts as  a filter.   If you
press Alt-A (ASCII), only ASCII  characters are displayed.  This filter
is useful  when you are  looking into text  strings and don't  want the
code displayed.  Most code contains opcodes outside the ASCII range.


A final word...
---------------

The CoreView program and its documentation have been donated the public
domain.

Please report  any problems to ROLAND  LYNGVIG at the  Josti-BBS, phone
+45 47 38 05 24 (DANE TECH 2:230/31 or SDNet/Work: #551.13).


Thank you for using CoreView...

RolySoft, Denmark