SECTION 5 
                    - Exploring a PRINT-SAY* .PRG file -
 
 
       [This section and the next are intended as reference material for 
     later interactions with PRINT-SAY and should probably be skipped if 
     you are reading through for the first time.] 
 
     5.1. FIRST THOUGHTS: 
       As mentioned above, PRINT-SAY is primarily a programmer's tool. In 
     a professional environment we expect our computers and software to 
     adapt to our designs and not vice versa. 
       A program which would generate virtually any possible report would 
     be at least as large and complicated as dBASE itself and has yet to 
     be written.  In the meantime the dBASE programming language provides 
     the minimum necessary tools to create more sophisticated reports than 
     LIST and REPORT FORM can provide.  PRINT-SAY is intended to alleviate 
     most of the routine drudgery of such programming for the programmer. 
     The programmer will take the .PRG output file created by PRINT-SAY 
     and customize it to suit the demands of a more complicated report. 
       Non-programmers with a modicum of dot-prompt expertise can also 
     customize the PRINT-SAY .PRG files in many ways which require no 
     understanding or experience with programming.  The reason for this 
     is that a dBASE program is to a large degree simply a batch of dot- 
     prompt commands grouped together to function as one task.  The pur- 
     pose of this section of the manual, then, is to provide a second 
     guided tour of a more advanced nature.  A tour which examines the 
     details of the PRINT-SAY .PRG file and illustrates some customization 
     changes you may want to use at some point in the future. 
 
     5.2. HOW TO PROCEED: 
       I strongly recommend that the following material be read with 
     your dBASE manual in hand.  It would also be highly useful for the 
     novice programmer to read the really excellent chapters provided in 
     the dBASE III Plus manual on how to program; or one of the many ex- 
     cellent books on the subject, if you are still using non-Plus, such 
     as Alan Simpson's Understanding dBASE III from SYBEX. 
 
     5.3. STEP-BY-STEP: 
       I will presume you are using PRINT-SAY from within dBASE itself by 
     using the RUN command explained in the first manual.  I will also 
     presume (as an example) that you have already created the PRINT-SAY 
     .PRG file called REPORT-A.PRG. from Section 3, A Guided Tour, in the 
     first manual. 
 
     5.3.1. STEP ONE: 
       The first step is to copy REPORT-A.PRG and work with the copy in 
     case there are any mishaps: 
 
               1. Type  RUN COPY REPORT-A.PRG NEWREPRT.PRG 
 
     5.3.2. STEP TWO: 
       Next, you need a way to view and change NEWREPRT.PRG.  (dBASE 
     provides a primitive editor MODIFY COMMAND; many people use WordStar 
     (tm); for my part, I find that the notepad of SideKick (tm) is by 
     far the handiest tool for this task.)  However, for the sake of the 
     example let's stick to the lowest common denominator. 
 
               2. Type  MODI COMM NEWREPRT.PRG 
 
       Now you should see a new screen filled with programmer-ese.  In 
     fact, there is little mystery here.  Most lines of a program are 
     dBASE commands, which could be typed in at the dot-prompt: 'set 
     margin to 0', 'set device to print', 'PageNo = 1', etc.  Some lines, 
     such as: 'do while .not. eof()', however, are valid only in programs. 
       To see more of the program the [PgDn], [PgUp], arrow keys, etc. of 
     the numeric keypad will move you through the file.  The key combin- 
     ations [Ctrl-A] and [Ctrl-F] move left and right from one blank space 
     to the next to speed up left/right motion.  (To exit use the [Esc] 
     key.) 
      [Note that you can also get a print-out of NEWREPRT.PRG (or any .PRG 
     file) with the dBASE command 
 
                       TYPE NEWREPRT.PRG TO PRINT 
 
     This allows you to see more of the code at a glance, which in turn 
     to clarify relations between various parts of a program.  (To see even 
     more of the code at a glance use the Cotton-Ware utility, Prim - with 
     which, incidentally, you can also print this manual.)] 
       Let's read through the program - whether via screen or print-out - 
     to see what some of the more cryptic lines do: 
 
     ***  Program: REPORT-A.PRG 
     ***  Called from: 
     ***  Property of: MOOSE FALLS CLUB OF VERY IMPORTANT PERSONS 
     ***  Programmer: A. PROGRAMMER 
     ***  Created on: 10/11/87 
     ***  Last Update: 
     ***  Purpose: 
     *** 
     ***               (This report is in Compressed pitch) 
     *** 
 
       5.3.3. THE TITLE BLOCK: 
       '***  Program: REPORT-A.PRG' -  This is the program title. Every 
       line in a dBASE program which starts with an asterisk is ignored 
       by the computer and is purely for human consumption.  These lines 
       are called comments or documentation; the computer has no need 
       for a title. 
 
       '***  Called from:' you may insert the name of another .PRG file 
       if it calls this file in the course of its execution. 
 
       '***  Programmer: A. PROGRAMMER' this line identifies you as the 
       author. 
 
       '***  Purpose:' insert a brief explanation of exactly what this 
       report is supposed to report on.  It may be obvious to you now; 
       6 months from now this brief statement will save you some aggra- 
       vation. 
 
 
     ** --------------------- Initialize Environment --------------------- ** 
     set talk off 
     set echo off 
     use CLIQUE 
     set index to CLIQNAME 
 
 
       5.3.4. INITIALIZE ENVIRONMENT: 
       '** --- Initialize Environment --- **' - since this line starts 
       with an asterisk it is ignored by the computer.  This is what is 
       technically known as a comment, and its purpose it both to explain 
       the code which follows it and to section off that code into a 
       logical group to make program reading easier.  All the in-code 
       comments created by PRINT-SAY take this form of two asterisks fol- 
       lowed by dashes, but this is purely an arbitrary artifact. 
 
       'set talk off' and 'set echo off' are commands which tell dBASE 
       not to send anything to the monitor which isn't specifically re- 
       quested by the programmer.  Note: if your report is intended to 
       be called from another .PRG program, be sure to delete these two 
       lines and both other pairs of 'set talk on' and 'set echo on' lines 
       farther down in the code. 
 
       'use CLIQUE' and 'set index to CLIQNAME' - these lines are the 
       familiar dot-prompt commands you are hopefully accustomed to 
       using every day. 
 
 
     ** ---------------------- Initialize Variables ---------------------- ** 
     ResetCode = chr(27)+chr(64) 
     PicaCode = chr(27)+chr(80) 
     CompCode = chr(15) 
     CompOffCode = chr(18) 
     DbleOnCode = chr(27)+chr(71) 
     DbleOffCode = chr(27)+chr(72) 
     Bar = "=============================================================; 
     ====================================================" 
     PageNo = 1 
     store 0 to Sub_1, Sub_2 
 
 
       5.3.5. INITIALIZE VARIABLES: 
       'ResetCode = chr(27)+chr(64)' - "ResetCode" is NOT a dBASE func- 
       tion or command.  Instead it is a dBASE MemVar (memory variable), 
       which is a way of getting the computer to store a certain number, 
       letter, or phrase and recall it each time the MemVar name is used. 
       This is exactly like saying X = 1 in algebra; it's just that 
       programmers prefer to use more descriptive variable names than 
       X, Y, and Z.  In this case, however, ResetCode is not even being 
       assigned a numerical value but that of a group of characters 
       treated as a whole - a "string".  Once a MemVar has been assigned 
       a value, the programmer may change that value at whim but dBASE 
       won't let him change the TYPE of that value.  In this case Reset- 
       Code may become any single character or group of characters, as 
       long as they are bunched together between quotes, but never a 
       numeric (non-quoted digit) type. 
         The 'chr(27)+chr(64)' phrase is what is being stored for future 
       use.  More on MemVars below at PageNo. 
         Almost all printer manuals explain these chr() codes in more 
       detail than I care to go into here.  The dBASE chr() function sends 
       a (hopefully) non-printable instruction to the printer which modi- 
       fies all further activities of the printer in a specific fashion. 
       Most of these instructions start with the character chr(27) 
       (Escape) which tells Epson printers that what follows is a command 
       and not for printing.  (Incidentally, if your non-Epson printer 
       starts each PRINT-SAY report with an unwanted '@' character, 
       remove this line.) 
         If your printer is totally non-Epson compatible, as for example 
       a Hewlett-Packard LaserJet, you will have to change each of these 
       codes to the 'escape sequences' in your manual which perform the 
       equivalent task. 
 
       - Let's skip down a few past the rest of the printer codes: 
 
       'Bar = "======...==' - this MemVar will be used further along to 
       create the double line which separates the header of the printed 
       report from its body.  The long row of characters repeats whatever 
       character you entered as the answer to Question 8 in the Re-Usables 
       Mode. 
 
       'PageNo = 1' Reading this line a programmer knows that the value 
       stored under the name of the MemVar 'PageNo' will only be used 
       for assigning a page number to the report, and that the variable 
       will stay at the value '1' until the next time the MemVar is as- 
       signed a value.  Because the 1 is not in quotes we know it is a 
       numeric variable and arithmetic may be performed with it. 
 
       'store 0 to Sub_1, Sub_2' - this line creates two new MemVars 
       in one stroke using the dBASE STORE x TO command.  Obviously, 
       one could create as many MemVars as wanted with one command - 
       as long as you wanted them all to have the same value. 
 
 
    ** ---------------------- Create Screen Display --------------------- ** 
    clear 
    Begin = " " 
    @ 5,19 say "MOOSE FALLS CLUB OF VERY IMPORTANT PERSONS" 
    @ 7,26 say "STATEMENT OF BALANCE OF DUES" 
    @ 16,34 say "To proceed:" 
    @ 18,17 say '1. Start printer  2. Insert 8 1/2"-wide paper' 
    @ 20,17 say "3. Scroll to start of new page or perforation" 
    @ 22,17 say "4. Press A to Abandon; any other key to begin. . ." get Begin 
    read 
    if Begin = "A" 
      set talk on 
      set echo on 
      return 
    endif 
    @ 12,35 say "PRINTING..." 
 
 
       5.3.6. CREATING THE SCREEN DISPLAY: 
       @ 5,19 say "MOOSE FALLS CLUB OF VERY IMPORTANT PERSONS" - 
       - this line is an example from this group of messages to the 
       monitor.  The '@ say' combination is explained in detail in 
       each dBASE manual.  In brief, '@ say' says: 
 
                   'at row X, column Y say the following'. 
 
       X and Y are the addresses of a point on the monitor screen (or 
       the printed page) exactly like the X,Y co-ordinates on graphs we 
       so tediously studied in algebra many years ago.  Normally, you
       may be used to using the "?" character to write a message to the 
       screen; @ SAY allows more control of message placement. 
 
 
    ** ----------------------- Set-up For Printing ---------------------- ** 
    set device to print 
    set console off 
    @ prow(),pcol() say ResetCode 
    do while .not. eof() 
 
 
       5.3.7. SETTING-UP FOR PRINTING: 
       'set device to print' sends all following commands to the printer 
       instead of the monitor. 
 
       'set console off' tells dBASE not to send any further messages to 
       the monitor or repeat out-put there. 
 
       '@ prow(),pcol() say ResetCode' this cryptic line sends the 
       printer code defined in the MemVar command described above to 
       the printer which tells it to clear all previous format settings 
       from its memory. 
         As in the monitor '@ say' commands above, the formula is also: 
       at row X, column Y say the following.  But in this line X and Y 
       are not directly specified as numbers; instead two dBASE FUNCTIONS 
       are used which tell dBASE to ask the printer for the present row 
       address [prow()] and the present column address [pcol()] and to 
       substitute whatever numbers it receives from the printer into the 
       program at this point. (See the Functions section of your manual.) 
       When the computer is forced to look up an address like this, 
       we are said to be using RELATIVE ADDRESSING. 
         Now that was a pretty technical discussion: you should be pleas- 
       antly surprised that you nearly understood it the first time 
       through. 
 
       5.3.8. CONTROL STRUCTURES: 
       'do while .not. eof()' - this is the beginning of what programmers 
       call a LOOP.  Loops are the most powerful tool in the programmer's 
       arsenal.  Near the end of the program you will see another command: 
       'enddo'.  Everything between the words 'do while' and 'enddo' are 
       repeated over and over by the computer.   
         Notice that all the lines which are enclosed between each pair 
       of 'do while' and 'enddo' commands are indented by two characters. 
       The indentation makes the program hugely more understandable for 
       human beings (the computer ignores it).  Because of the indentation 
       we can see at a glance all the lines which are part of the loop and 
       which are therefore to be repeated. 
         The '.not. eof()' part of the line is the CONDITION which deter- 
       mines when the computer will STOP repeating the loop.  In this case  
       the condition reads: "DO what follows, WHILE you are NOT at the end  
       of the database file which is currently opened".  Eof() is another  
       dBASE function, which returns a True or a False, depending on whether  
       or not the database has been opened to the point just after the last  
       record - the END-OF-FILE point.  This end-of-file point is reached 
       after every SUM or TOTAL and after every LOCATE, SEEK, or FIND which  
       fails to find its target.  The SKIP command below will also finally  
       reach the eof() point.  Eof() is also True if the file is completely  
       empty - contains zero records. 
         After reading this line the computer will first check to see if 
       eof() is true or false.  If true (hopefully not) it has nothing to 
       do and skips down to the matching 'enddo' and proceeds from there. 
       If false (in other words, the record pointer is pointing to a 
       record) it proceeds to execute each of the following commands 
       until it reaches a matching 'enddo'.  When it reaches the 'enddo' 
       it then LOOPS up to the beginning of the 'do while' loop, checks 
       on eof() and repeats the same steps over and over, as long as the 
       function eof() does not return a true. 
         The periods around the not in '.not.' tell dBASE that the word 
       enclosed is a CONDITIONAL word and not a MemVar.  '.and.', '.or.', 
       and '.not.' are the three logic conditional words.  While '.t.' 
       and '.f.' mean True and False to dBASE. 
 
 
  ** ---------------- Code For Printing Page Header ----------------- ** 
  set margin to 0 
  @ 2,0 say CompOffCode+PicaCode+DbleOnCode 
  @ prow()+1,21 say "MOOSE FALLS CLUB OF VERY IMPORTANT PERSONS" 
  @ prow()+2,6 say date() 
  @ prow(),28 say "STATEMENT OF BALANCE OF DUES" 
  @ prow(),71 say "Page" + ltrim(str(PageNo)) 
 
 
       5.3.9. PRINTING THE HEADER LINES: 
       'set margin to 0' - set margin is a normal dBASE command which is 
       often issued from the dot-prompt.  This is also the first of the 
       repeated commands in this 'do while' loop. 
 
       '@ 2,0 say CompOffCode+PicaCode+DbleOnCode' - for this report, 
       PRINT-SAY has chosen to use Compressed pitch to squeeze all the 
       fields in we asked for; in other reports this may be PicaCode or 
       EliteCode. However, in every report PRINT-SAY starts with PICA pitch 
       so that the banner lines of each report will have the same visual 
       format and since compression simply isn't needed at this point in 
       the printout. 
         Note also that this the one of the few lines in which the X,Y 
       co-ordinates in an '@ say' command are simply given straight 
       out - without forcing the computer to perform a prow() or pcol() 
       calculation.  The technical term for sending actual numbers as an 
       address is ABSOLUTE ADDRESSING.  This line tells the printer to 
       move its print head to the first character of the 2nd row down 
       from its initial position; the chr() values mean: switch to pica 
       pitch. 
 
       '@ prow()+2,6 say date()' - this @ SAY uses the other type of 
       addressing, relative, again for the row value, and an absolute 
       (non-look-up) value for the column.  When it gets there it is 
       commanded by the 'date()' function to ask the computer for the 
       current date from its clock and put the answer at this location 
       on the printed page. 
         More importantly, the '+2' phrase tells the computer it is time 
       to cease printing on the previous line and skip down to rows to 
       start a new line of print. 
 
         Two more mixed-address commands list your report title (if any) 
       and the page number, completing the banner or header portion of 
       the printed page. 
         Because these commands are all inside the initial 'do while' 
       loop, they will be executed as many times as dBASE fills a page 
       with records and starts a new one.  Towards the end of the code we  
       see another statement containing PageNo which reads: 'PageNo =  
       PageNo + 1'.  This happens when a full page is printed, causing 
       the value '1' to be added to the memory variable called PageNo, 
       so that the next page will have one higher number than the one 
       previous.  This sort of formula, X = X + 1, is called a COUNTER 
       by programmers and is used frequently. 
 
 
  ** ---------------- Code For Printing Column-Titles --------------- ** 
  set margin to 9 
  @ prow()+1,0 say CompCode 
  @ prow()+1,0 say "Title" 
  @ prow(),12 say "Last Name" 
  @ prow(),31 say "First Name" 
  @ prow(),54 say "Street Address" 
  @ prow(),78 say "Phone No." 
  @ prow(),89 say "Dues Paid" 
  @ prow(),99 say "Dues Owing" 
  @ prow(),111 say "Date Rec'd" 
  @ prow()+1,0 say Bar + DbleOffCode 
 
 
       5.3.10. PRINTING THE FIELD TITLES: 
         This group of code, all starting with '@ prow()' change the 
       print style to Compressed pitch and list the field titles across 
       the paper.  Because each of these commands starts with a plain 
       'prow()' they are all sent to the same row on the page. 
 
 
  ** ------------------- Code For Printing Records ------------------ ** 
  do while .not. eof() .and. prow() < 60 
    @ prow()+1,0 say TITLE 
    @ prow(),7 say SURNAME 
    @ prow(),29 say FIRST 
    @ prow(),46 say STREET 
    @ prow(),78 say PHONE 
    @ prow(),89 say DUES_PAID picture "999.99" 
    Sub_1 = Sub_1 + DUES_PAID 
    @ prow(),101 say 100 - DUES_PAID picture "999.99" 
    Sub_2 = Sub_2 + 100 - DUES_PAID 
    @ prow(),113 say DATE_PAID 
    skip 
  enddo 
  PageNo = PageNo + 1 
  @ prow()+1,0 say DbleOnCode + Bar 
 
 
       5.3.11. THE WORK-HORSE LOOP: 
       'do while .not. eof() .and. prow() < 60'.  The code lines fol- 
       lowing this one until the "enddo" line all work together to write 
       a single line of field-data across the page then they skip down 
       and repeat the process until either the end of the file or the 
       end of the current page is reached.  The result of all this is a 
       loop within a loop!  This is a very powerful tool in the pro- 
       grammer's repertoire; and it is by no means unheard of to have 
       a loop within a loop within a loop, etc.  When loops come inside 
       other loops they are called nested; with the first loop being 
       referred to as the outer and the second the inner loop. 
         While this may seem a bit mind-boggling, it becomes easy to fol- 
       low if you simply keep in mind that each line of the outer loop is 
       executed once. . .until the first line of an inner loop is up to 
       bat.  At that point the inner loop is executed over and over again 
       as long as its condition holds true.  This may be zero times, once, 
       or ten thousand - but eventually something changes which makes its 
       condition (not end-of-file and not printing past row 61 in this 
       example) untrue.  When that happens the outer loop takes control 
       back, any further of its lines are executed until the last line when 
       an 'enddo' line is reached.  At that point control is looped back to 
       the start of the loop; its condition (not end-of-file, in this case) 
       is checked for true and false again; and, if eof() says false, the 
       loop is run through a second time.  Eventually, the beginning of the 
       inner loop is reached - its condition is checked for true or false, 
       and, if true, it is executed any of number of times again. 
         What happens when we apply this theory to the particular case 
       in this program is that the outer loop prints a banner section 
       at the top of a page.  Then it prints the underlined field-titles. 
       Then it meets the inner loop which goes to database, grabs a 
       handful of fields from that file, and spreads them across the 
       next row on the printed page under the field-titles.  Then the 
       program comes to the single word 'skip'.  This DOESN'T mean 'skip 
       a line on the page'; it means 'skip' down to the next record in 
       the database.  It is entirely because of this line that the con- 
       dition at the start of the outer loop can ever come to the answer 
       'false' - and therefore end the print job.  The inner loop is more 
       touchy: it will knock-off whenever end-of-file is reached, like the 
       outer loop, but also whenever the bottom of a page of paper is 
       reached. 
         We might think of the computer as bouncing frantically back and 
       forth between two walls - 'do while' and 'enddo' for each loop it 
       gets snared into by the program.  Each bounce moves a little farther 
       along the walls between the entrance and the exit - though frequent- 
       ly there may be an inner entrance in one of the walls into which the 
       computer pops when it gets that far along the wall.  Then it finds 
       itself in an inner room with an inner wall it must bounce its way 
       along, hoping to avoid yet a deeper trap, before it can exit back to 
       outer room to complete its work-out. . .and very likely be zapped 
       right back to the beginning of the trap again. 
 
 
       5.3.12. ACCUMULATING SUB-TOTALS: 
         Also intermingled in the lines of code sandwiched into this do 
       while loop are two lines using the Sub_1 and Sub_2 MemVars. Because 
       of the "formula" used here, in both cases these MemVars act as ac- 
       cumulators, successively accumulating each value of Dues_Paid and 
       100 - Dues_Paid as the program writes each new line.  At the end of 
       a page the total number accumulated into these MemVars is shown as 
       a sub-total. 
         Notice the single PageNo = PageNo + 1 line sandwiched between 
       the two 'enddo' lines.  This is the only work the computer needs 
       to do after completing the inner loop before bouncing back to 
       the top of the outer loop. 
         Next, the loop which draws a line of equal signs across the 
       page is repeated. 
 
 
    ** ----------------- Code For Printing Sub-Totals ----------------- ** 
    @ prow()+1,86 say Sub_1 picture "99,999.99" 
    @ prow(),98 say Sub_2 picture "99,999.99" 
    @ prow(),pcol() say DbleOffCode 
  enddo 
  eject 
 
 
       5.3.13. DISPLAYING THE SUB-TOTALS: 
         Next, the sub-total MemVars are displayed at the appropriate rows 
       and columns on the printed page.  After these four lines a lone 
       'enddo' closes the largest, outside loop which started with 'do 
       while .not. eof()'.  Therefore, all the lines which follow this line 
       are outside all loops and will only be executed once. 
 
 
  ** ----------------------- Restore Environment ---------------------- ** 
  @ prow(),pcol() say ResetCode 
  set console on 
  set device to screen 
  set talk on 
  set echo on 
  clear 
  return 
 
 
       5.3.14. RESTORING THE ENVIRONMENT: 
       'eject' - the line following both loops - tells the printer to eject 
       the final page of printout so you can tear it off. 
 
         The 'chr(27)+chr(64)' code sent by the second ResetCode MemVar, 
       politely clears the printer of all the other chr() codes left 
       over from the print job. 
 
         The remaining lines simply undo the work of the first several 
       by restoring control of the monitor screen to dBASE and turning 
       the printer back over to itself. 
 
 
 
 
                                 SECTION 6 
                             - Making Changes - 
 
 
       [Note: as in Section 5, in Section 6 we will be using MODIFY 
     COMMAND to examine and change REPORT-A.PRG.  See the beginning 
     of Section 5 for details if you're unclear on how to proceed.] 
 
     6.1. HEADER BLOCK: 
       Drop down a few lines from the top of REPORT-A to enter a sentence 
     or two giving a general description of what this report does.  What 
     may be obvious today may be mysterious next year.  Also the logo line 
     which follows 'Property of:' may or may not be accurate.  To change 
     it merely position the cursor at the beginning of the logo phrase then 
     start typing, what you type will over-write what PRINT-SAY wrote.  To 
     get rid of any excess hold down the space bar.  To delete this line 
     altogether simply position the cursor anywhere on that line and press 
     [Ctrl-Y]. 
 
     6.2. INITIALIZE ENVIRONMENT BLOCK: 
       New lines further controlling the environment might be inserted 
     here, such as 'set status off' for dBASE III Plus.  In that case, 
     drop all the way down to the second-last line and insert a corre- 
     sponding 'set status on'.  To insert a line press enter at the 
     beginning of the following line or the end of the preceding line. 
       If more than one database needs to be opened simultaneously to 
     provide all the fields your report needs insert the appropriate 
     "SELECT 1" (or "SELECT A"), "SELECT 2", etc. lines with appropriate 
     USE and INDEX commands following each area.  For example, NEWREPRT 
     currently reads: 
 
                use CLIQUE 
                set index to CLIQNAME 
 
     But a different report might have needed the lines 
 
                select 1 
                use CLIQUE 
                set index to CLIQNAMES 
                reindex 
                select 2 
                use OLMEMBRS 
                set index to OLDNAMES 
                reindex. 
 
 
     6.3. INITIALIZE VARIABLES BLOCK: 
       If your printer uses some non-Epson compatible codes, you would 
     of course need to change those provided here accordingly.  In some 
     cases it may be possible to enter a Near Letter Quality code as 
     well.  Most printers will not allow simultaneous pitch control and 
     draft/NLQ control but yours may.  In any case, it can't hurt to try 
     adding a line such as "NLQCode = #27#110" in this group, then below 
     (See 6.5.) another line to call the code. 
       Technical users please note: Many printer manuals offer a detailed 
     description of what Epson calls the Master Select command, chr(27)+ 
     '!'+chr(x).  Unfortunately, you can write this off: dBASE makes  
     mincemeat out of Master Select codes on any printer I've tried. 
 
     6.4. CREATE SCREEN DISPLAY BLOCK: 
       Quite possibly you may want to delete this altogether or change 
     the text it presents to the screen.  You can do no harm I can think 
     of by changing any of the text between the double-quotes, changing 
     the numbers which show which row and column each line will appear 
     at, or even by inserting new lines.  The lines involving the MemVar 
     `Begin' and the verb `read' illustrate only one way of gathering 
     the all-important fact that the user has turned on the printer and 
     gotten it adjusted for printing.  See the dBASE manual for an ex- 
     lanation of the WAIT verb for another alternative. 
 
     6.5. SET-UP FOR PRINTING BLOCK: 
       Neither the 'set console off' nor the '- say ResetCode' lines 
     are absolutely necessary.  In particular if the ResetCode is missing 
     from your printer's bag of tricks you may want to delete this line 
     (position the cursor anywhere on its length then press [Ctrl-Y]) and 
     change a line in the Screen Display section prompting the user to 
     turn the printer off then on again before printing. 
       The reset code clears the printer of any previous format commands 
     such as a margin setting or a different pitch; simply turning the 
     printer off then back on accomplishes the same function as the reset 
     code used here. 
       If you are attempting to use an NLQ code, tag your MemVar name on 
     to the ResetCode line here to send your NLQ code to the printer. For 
     example this line might become: 
 
                  '@ prow(),pcol() say ResetCode+NLQCode'. 
 
     6.6. PAGE HEADER BLOCK: 
       Just about anything in this block is game for easy customization: 
 
     6.6.1. USING EXPANDED PRINT: 
     One cute trick would be to add an expanded print code to the logo 
     display line.  Chr(14) starts expanded print; chr(20) cancels it. 
     Because each character between these commands will occupy twice the 
     number of spaces as normal pica text, the number after the comma 
     in the prow()+1,xx segment will have to be reduced accordingly. 
     This number shown here by "xx" is the column address - the left-most 
     point on the line at which the say portion of the command will be 
     displayed. 
       A typical expanded logo might be: 
 
           @ prow()+1,23 say chr(14)+"Metro Police Dept."+chr(20) 
 
       Since the logo is 17 characters long, it will consume 34 chars. 
     of space in expanded print; presuming normal paper which gives us 
     80 characters of space in Pica, we're left with 46 blanks: 23 on 
     each side of the logo to centre it. 
 
     6.6.2. ADDING AN ADDITIONAL LOGO LINE: 
       Nothing could be simpler.  Immediately after the logo line add 
     a new line with exactly the same format, changing only the number 
     after the comma and the string of characters in quotes.  An example: 
 
         @ prow()+1,20 say 'Homicide, Suicide, and Ax-Murders Division'. 
 
     Since this text is 41 characters long, centering it would require 
     20 spaces on one side and 19 on the other, therefore, the number 
     following the comma can be either 19 or 20. 
 
     6.6.3. OTHER CHANGES: 
       The page number and date positions may be changed within the report 
     title line to suit your taste by simply modifying the column number 
     following the '@ prow(),' portion of these lines. 
       A second report title line may be added above or beneath the one 
     PRINT-SAY created simply by following the same procedure described 
     above for adding a second logo line. 
 
     6.7. COLUMN-TITLES BLOCK: 
       The whole body of the report may be moved left or right by chang- 
     ing the margin numeral. 
 
     6.7.1. RE-LOCATING INDIVIDUAL TITLES: 
       Any of the column titles may be moved are left or right of the 
     centre of their fields by changing the column address numbers on 
     their lines.  Often a field for a name of an address needs to be 
     kept as long as the longest name or address, while the vast major- 
     ity of the names or addresses are much shorter, leaving an unsightly 
     gap in the report.  A further consequence of this situation is that 
     the titles appear to be too far to the right of the names or addres- 
     ses below them. 
 
     6.7.2. ADDING A SECOND TITLE LINE: 
       Occasionally it is desirable to break a field title into two 
     phrases one above the other, especially if the title needs to be 
     significantly longer than the width of the field itself.  Perhaps 
     this is a little more complicated than what we've done so far, but 
     it is far from being difficult.  Let's use the titles section from 
     REPORT-A.PRG, created in section 4 of this manual as an example. 
 
 Last Name  First Name  Street Address  Phone No. Received  Owing  Date Rec'd 
 
     Here again is the section of code which generated these titles 
     (I had to leave the first title off, above): 
 
          @ prow()+1,0 say CompCode 
          @ prow()+1,0 say 'Title' 
          @ prow(),12 say 'Last Name' 
          @ prow(),31 say 'First Name' 
          @ prow(),54 say 'Street Address' 
          @ prow(),78 say 'Phone No.' 
          @ prow(),89 say 'Received' 
          @ prow(),99 say 'Dues Owing' 
          @ prow(),111 say "Date Rec'd" 
 
     The first one starts the ball rowing by turning on compressed pitch 
     after dropping down one line (row) from the date/report title/page 
     number line.  The second statement drops down yet another row and 
     prints the first column title, 'Title'.  All the rest of the commands 
     stay on the same line (whatever line number prow() refers to in this 
     case) but move to a different COLUMN address: 0, 12, 31, 54, etc. When 
     that much is clear read on: 
       Now, suppose we wanted to change the field titles to look something 
     like this: 
                                                    Dues    Dues 
 Last Name  First Name  Street Address  Phone No. Received  Owing  Date Rec'd 
 
     which is a fairly common practice.  What we need to do is to insert 
     a row with three titles between the date/report title/page number 
     line and the current titles line.  So, between the first two lines of 
     the block of code shown above we need to insert a new line which 
     will print the word "Dues", then a second new line which will also 
     print the word "Dues" (but in a farther-right location).  We can 
     steal a lot from the code PRINT-SAY generated to do this.  Since the 
     first "Dues" is going above the word "Received" we can borrow "Re- 
     ceived"'s address and add two to it to get the location for the first 
     "Dues", and borrow the exact address from the word "Owing" for the 
     second "Dues".  Like so: 
 
          @ prow()+1,0 say CompCode 
          @ prow()+1,91 say 'Dues'    { - new line 
          @ prow(),100 say 'Dues'     { - new line 
          @ prow()+1,0 say 'Title' 
          . 
          . 
          . 
 
     - It's as simple as that! 
 
     6.8. PRINTING RECORDS BLOCK: 
       In the last fraction of the line `do while .not. eof() .and. prow() 
     < 60' - the `60' is the last row of print the printer will write 
     before starting a new page.  Change this to any value you like less 
     that the maximum which will fit on one page. 
       Any fields which you've entered as being numeric have a dBASE 
     picture statement added to them.  Occasionally,  you may want to 
     modify this picture in one of the multitude of variations shown in 
     your dBASE manual. 
 
     6.9. CLOSING OFF: 
       When using MODI COMM to edit a file, always remember to exit with 
     [Ctrl-W] or [Ctrl-End]: NEVER use [Esc] unless you have consciously 
     decided to abandon the changes you've made. 
       A true programmer will possibly make countless other modifications 
     to this code to handle any number of special situations.  The above 
     represent changes which can be easily controlled by the average dot- 
     prompt user. 
     
 
 
                            - SECTION 7: INDEX - 
 
      @ say - 5.3.6 
      APPSGEN - 1.2 
      ASSIST - 1.2, 2.2 
      Addressing, Absolute - 3.1.2, 4.2, 5.3.9 
      Addressing, Relative - 3.1.2, 5.3.7 
      Asterisk - 5.3.3 
      Chr() - 5.3.5, 6.6.1 
      Clique.dbf - 4.1 
      Code generators - 1.1 
      Column address - 5.3.6, 5.3.7 
      Comments - 5.3.3, 5.3.4 
      Compatibilities, Printer - 1.1, 1.2 
      Compressed pitch - 3.1.3, 4.8 
      Contents, field - 3.2.2, 4.5 
      Ctrl-C - 2.3 
      Ctrl-A - 5.3.2 
      Ctrl-F - 5.3.2 
      Ctrl-W - 5.3.5, 6.11 
      Ctrl-End - 5.3.5, 6.11 
      DO <PRG> - 2.2 
      DO WHILE - 5.3.8, 5.3.11, 5.3.12 
      Databases - 3.1.9 
      Decimals - 3.2.5 
      Default - 3.1.2 
      DrawLineChr - 5.3.5 
      Eject - 5.3.14 
      Elite pitch - 3.1.3 
      Enddo - 5.3.8, 5.3.12 
      Eof() - 5.3.8 
      Epson - 1.1 
      Esc - 5.3.2, 6.11 
      Exiting PRINT-SAY - 2.3; MODI COMM - 5.3.2 
      Expanded print - 6.6.1 
      Field titles - 3.2.1, 4.5, 5.3.10; re-locating - 6.7.1, adding - 6.7.2 
      Field contents - 3.2.2, 4.5 
      Field size - 3.2.4 
      Generator, Code - 1.1, 1.2 
      IF - 3.1.11 
      Indexes - 3.1.10, 4.3 
      Installation (of PRINT-SAY) - 2.1 
      LIST - 1.1 
      LIST STRUcture - 2.2, 3.2.2, 4.1 
      Length of paper - 3.1.5 
      Licensing, Site - 7.1 
      Logo - 3.1.1, 6.1; additional - 6.6.2 
      Loops - 5.3.8, 5.3.11, 5.3.12 
      MEMO fields - 1.5 
      MODIFY COMMAND - 4.8, 5.3.2 
      MemVars - 5.3.5 
      Memory Variables - 5.3.5 
      NLQ - 6.3, 6.5 
      Naming files - 3.1.7, 4.3 
      Number of fields - 3.1.12 
      Numeric, fields - 3.2.3, 4.7 
      Out-put file - 3.1.7  
      PageNo = 5.3.5 
      PCOL() - 5.3.6, 5.3.7 
      Pica pitch - 3.1.3 
      Printers - 1.1
      PRINTSAY.DAT - 3.3, 4.8 
      PROW() - 5.3.6, 5.3.7  
      PRNTCODE.PRG - 3.1.7 
      REPORT FORM - 1.1 
      RUN PRINTSAY - 2.2, 4.1 
      RUN DEL <filename> - 4.1 
      RUN COPY <Filename> <Filename> - 5.3.1 
      Re-Usables - 3.1, 4.2 
      Relative addressing - 3.1.2, 5.3.7 
      ResetCode - 5.3.5, 6.5 
      Revision Mode, Initial Questions - 4.4 
      Revision Mode, Field Questions - 4.8 
      Row address - 5.3.6, 5.3.7 
      SELECT - 1.3, 6.2 
      SET MARGIN TO - 5.3.9 
      SET DEVICE TO PRINT - 5.3.7 
      SET CONSOLE OFF/ON - 5.3.7, 6.5 
      Separators - 3.1.6 
      Size, fields - 3.2.4 
      Skip - 5.3.12 
      Sub-totals - 3.2.6, 5.3.13, 6.10 
      TRIM() - 3.2.2 
      Throw-aways - 3.1.7, 4.3 
      Title, report - 3.1.8 
      Titles, Field - 3.2.1, 4.5, 5.3.10; re-locating - 6.7.1, adding - 6.7.2 
      USE <database> - 3.1.9 
      Underline - 5.3.11 
      Variables - 5.3.5 
      Width of paper - 3.1.4
 

       * PRINTSAY.COM, PRINTSAY.DOC and CUSTMIZE.DOC are (c) Copyright 
                     1988, by Dale Cotton, Toronto, Canada.
                              All Rights Reserved.