ERRMON

                              By Robert J. Newton

       After experiencing a variety of problems with the hard disk on
       my AT, I decided that I wanted a more informative report of disk
       I/O errors than that provided by DOS.  ERRMON is the result.

       ERRMON is a resident program which inserts itself in the INT 13
       chain.  It then sits quietly watching for any error condition
       returned by the disk driver.  When an error is detected, it
       springs to life and prints an error message on the screen.  This
       message is in most cases far more informative than that provided
       by DOS.  It then gracefully returns to the caller to let it do
       what it wishes with the error.

       Under the proper conditions ERRMON will let you know when DOS is
       making retries.  However, ERRMON does not scroll the screen.
       This means that it is possible that a second message will overlay
       the first and you would not be aware of the retry unless the
       calling program causes a scroll.

       A word of caution.  ERRMON has been written to respond to the
       error codes returned by the IBM BIOS disk drivers on the PC, XT
       and AT as shown in the various BIOS listings.  Results with
       other drivers are totally unknown although it might be assumed
       that they map their error codes the same in order to achieve
       compatibility.  There are no checks for machine or drive type.

       In addition, the errors defined for the PC/XT and AT fixed disk
       drivers are not the same in all cases.  ERRMON responds to the
       codes for both.  It is possible, but not likely, that say the AT
       could through some glitch return an error code that is not
       defined on the AT, but is on the XT.  Instead of displaying an
       "Undefined error" message, ERRMON would display the message
       defined for the XT.  This possibility was considered so remote
       that it was not trapped.

       The only error that ERRMON does not respond to is applicable
       only to the AT.  Its floppy disk driver reports an error when a
       disk is changed.  This is not a true i/o error and is ignored by
       ERRMON.

       ERRMON's overhead is essentially nil, only four instructions
       when there is no error.  Approximately 1K of memory will be used,
       mostly for the message text.

       The video attribute for the error messages has been set to 0F,
       intense white.  The messages will print in the lower right
       corner of the screen.  You may change both of these by using
       DEBUG.  The attribute byte is at offset 02EE and the screen line
       is at offset 02E2.  Note that the screen line is relative to 0

                                       1






       so that the last line is hex 18, decimal 24.  For those with
       MASM, you may change the EQUATEs at the beginning.  You may also
       change the message text, perhaps to shorten it so that less
       memory will be needed.

       Installation is simple, just type errmon.  A successful
       installation will return ERRORLEVEL 0, unsuccessful will return
       255.  It can be installed by an AUTOEXEC.BAT, preferably after
       anything else which might place itself in the INT 13 chain.  You
       can use >nul to avoid the sign on message.



                                Error messages

       Sense failure (PC/XT only)

       Status error (AT only) - The controller status register returned
       an error condition, but the error register did not contain an
       error code.

       Write fault (AT only) - Indicates a hardware problem with the
       drive.

       Undefined error - An error code was returned for which BIOS has
       not defined an error.

       Drive not ready (AT only)

       No response - What DOS calls Drive not ready.

       Seek failure - An attempt to seek to the requested track was
       unsuccessful.

       Controller failure - Probably indicates that the controller could
       not successfully complete the requested command within the
       alloted time.

       EEC corrected data error - An information report that the
       controller's EEC algorithm successfully corrected a soft data
       error.  You should copy the file and delete the original if this
       happens frequently.

       Bad CRC/EEC on read - The sector could not be successfully read.
       Retries should be made and if successful the file should be
       rewritten or copied which will usually cure the situation.
       Otherwise, use RECOVER.

       Bad track (PC/XT only) - An operation was attempted on a track
       flagged bad by the low level formatter.  Such areas should have
       been marked bad in the FAT.


                                       2






       Bad sector (AT only) - Similar to Bad track.

       Data crosses DMA boundary - This indicates a software problem;
       DMA cannot operate with more than 64K of data.

       DMA overrun - The controller could not get DMA access; a retry
       should succeed.

       Drive init failure - Probably indicates an attempt to initialize
       an invalid drive number.

       Drive reset failure - An attempt to reset the drive system
       failed.

       Sector not found - Bad news.  The requested sector could not be
       found.  Assuming the values were valid, this indicates a flawed
       disk.  Absent a very capable disk zapper and the knowledge of its
       use, the only cure is a low level format.  It is also possible
       that a disk made in one drive cannot be read in another because
       one of them is out of alignment.

       Diskette write protected - Take the tab off.  If there is no tab
       the drive's sensors are probably bad.

       Address mark not found - Very bad news.  See sector not found.

       Bad controller command - An invalid command was sent to the
       controller.


       ERRMON is (C) Copyright 1985 by Robert J. Newton, but hereby
       released to the public domain for private non-commercial use.  It
       may be freely copied and distributed, but no consideration may be
       requested other than any customary handling fees charged by
       recognized user's groups.  No warranties of any kind are provided
       and by using the program the user assumes all risk.