Using the Drop to Dos Command with Wildcat v 1.03

     When I first started trying to get the drop to dos command to work
properly I really didn't think there would be much of a problem, just a
lot of redundant testing for security reasons. (Wouldn't want to loose
carrier while at the Dos prompt and have the next caller come in at the
C> prompt and erase the HD).  Not so easy as I had planned.

     It was no problem to write the first batch files to accomplish the
simpler tasks needed (no professional programmer here either) but the
worst was yet to come. 

     I knew it was necessary to monitor the carrier detect line so I
could have the computer reboot if I lost the connection from remote
and carrier dropped. I tried Watchdg1.com with no luck, kept locking up
the system when I used Watchdog, found the culprit was the AUTOPARK.COM
in my autoexec.bat file, it wanted the aux1 timer interrupt that Watchdog
needed to work properly. 

     The rest seemed easy until I discovered that as of yet WILDCAT does
not Shell to Dos during drop to Dos.  When you drop to dos from remote, 
Wildcat terminates, no way to get back into Wildcat from Dos other than
executing your Cat.Bat again.  This leaves you on line until the Modem
initialization strings reset the modem (I am using a Qubie' Basic Time 2400),
this was not acceptable because that meant Wildcat couldn't reset thinking
a session was still going on until I would hang up from remote.

     It meant that I was going to have to provide all functions from
the Dos Level.  The following list needed to be accomplished:

     1. Creat Batch files allowing exit to Dos from my Batch 
        files.
     
     2. Provide adequate protection from loss of carrier,
        someone calling in between the time I hung up and
        Wildcat was back in control again, whether carrier
        was lost or I had finished with what I was doing 
        while at Dos.
 
     3. Return to the batch file that had released me to
        the Dos level and start Wildcat running again.
   
     

     The first step was to set up the modem initialization strings
within MAKEWILD.  Using the Qubie 2400 the sample screen below worked
fine.

IN MAKEWILD FRAME 3


                              MODEM INFORMATION                    Frame 3
   1.  Which Communications Port do you want to use [ 1 or 2 ]  ? 1
   2.  Maximum # of seconds to wait for carrier [ S7 Register ] ? 30
   3.  Enter the string to reset your modem: ATZ
   4.  Enter Modem Startup String #1:
        ATZ
   5.  Enter Modem Startup String #2:
        ATB1E1M1V0
========
B1 = Bell Answer Tone
E1 = Command Character Echo Enabled
M1 = Speaker on During Autodialing (probably not necessary)
V0 = Result Messages Sent in Numeric Format
========

   6.  Enter Modem Startup String #3:
        ATS0=1S7=30&C1&D2&S1&W
========
S0=1    = Answer After 1st Ring (enable auto answer)
S7=30   = Maximum Wait Time for Carrier Detect
&C1     = DCD Indicates On-Line Data Carrier Detected
&D2     = Disconnect & Return to Command Mode After Loss of DTR &
          Disable Autoanswer Until DTR is Reactivated
======>   (problem with this one, when system is rebooted by
NOTE!!!    Watchdog program, I used CDMON, DTR goes high so
           this would re-enable Modem Auto Answer)
&S1     =  DSR Indicates On-Line in Data Mode
&W      =  Write to Modem Memory  (no switches on Qubie')


   7.  Enter the string to reinitialize your modem after every call:
        ATV0M1Q0S0=1S7=30
========
V0      =  Result Messages Sent in Numeric Format
M1      =  Speaker on During Autodialing (probably not necessary)
Q0      =  Result Codes Sent to DTE
S0=1    = Answer After 1st Ring (enable auto answer)
S7=30   = Maximum Wait Time for Carrier Detect
========

   8.  Modem Delays in Milliseconds:
          #1: 2000      #2: 750      #3: 2500
   9.  Initialize your modem port at which baud rate [ 300..19200 ] ? 2400
  10.  Lock the DTE setting at the initialized baud rate [Y/N] ? N
  11.  Answer Phone By <R>ing or <A>uto Answer [ R or A ] ? R
  12.  Determine Baud rate by <C>/r's or <R>esult Codes [ C or R ] ?  R
       If By Result codes enter your numeric result codes for:
             300 : 1    1200 : 5    2400 : 10   9600 : 13



     The next step, writing the batch files, well the ones I used
are below:

C>TYPE AUTOEXEC.BAT
PROMPT=$P$_$N$G   'DIRECTORY PROMPT AT DOS LEVEL
WAITN 3           'WAIT 3 SECONDS BEFORE RUNNING (WAITN.COM IN DIRECTORY)
CLS               'CLEAR SCREEN
CD\WILDCAT        'CHANGE INTO WILDCAT DIRECTORY
CAT               'CALL CAT.BAT (RUN BOARD)

C:\WILDCAT
C>TYPE CAT.BAT

CTTY CON:         'BE SURE INPUT IS FROM KEYBOARD
DTR OFF           'DROP DTR (DISABLE MODEM, DTR.COM)
AT S0=0           'SET MODEM NOT TO AUTOANSWER (AT.COM)
WILDCAT           'RUN BULLETIN BOARD
REM The next line is invoked using the [D]rop to DOS choice, if allowed
IF ERRORLEVEL 40 DROPDOS.BAT
IF ERRORLEVEL 0 GOTO END    'BRANCH TO END IF SHUTTING BOARD DOWN
WAITN 3           'WAIT 3 SECONDS (ABORT WITH CONTROL-C)
CAT.BAT           'START BATCH FILE AGAIN
:END              'QUIT       
ECHO ALL DONE


C:\WILDCAT
C>TYPE DROPDOS.BAT                                 'T/100= 6 sec delay
CDMON C/1 M/128 T/100   'Watch Carrier using Com1, Carrier Detect Flag 128,
CTTY COM1:              'Redirect input to Com Port 1
COMMAND /S              'Shell From Batch file (command.com must be present)
DTR OFF                 'after typing Exit, Hangs up Modem
RESET                   'Reboots Computer, Batch files run Board Again.
CAT                     'In Case Reset.Com Fails or Gets Erased



      When I was at Dos and typed EXIT to run the batch file again,
DTR OFF and RESET did the job fine.

      If I would simulate loss of carrier by hanging up at Dos Prompt,
CDMON would reboot the computer then DTR OFF in Cat.bat would hang up
on any caller that might have called in immediately. I have tested these
files and utilities which seemed to work fine for me but at this point I
cannot emphasize strongly enough,

IF YOU MUST HAVE THE DROP TO DOS COMMAND, GET ANOTHER COMPUTER AND TEST
YOUR SYSTEM FOR ALL POSSIBLE CONDITIONS.  EVERY MODEM IS DIFFERENT, 
MEMORY RESIDENT UTILITIES CAN ADVERSELY AFFECT NORMALLY GOOD PROGRAMS
SUCH AS WATCHDG1, CDMON, RESET, DTR, AT, etc.  TEST UNTIL YOU ARE ABSOLUTELY
POSTIVE NO ONE ELSE CAN GET ACCESS TO YOUR SYSTEM AT THE DOS PROMPT.
IF YOU ARE NOT SURE, DON'T USE THE DROP TO DOS COMMAND!!!!!!!!!

If anyone has found a better way, suggestions, or questions regarding 
an easier way to use the DROP TO DOS command I would appreciate knowing
about it.  I can be contacted on my BBS,

                                          Thanks, Stan Chiles

                         
                           The Brick City BBS
                              314-581-0563
                              300/1200/2400
                               Mexico, Mo