Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11

















           Universal Version of Geographic Clock Program

           Copyright 1988,1989 (C) Joseph R. Ahlgren

           Version 3.3    89/06/11

           GEOCLK33.ARC - EGA version
           GEOMNO33.ARC - CGA/HGC/MCGA/ATT400/PC3270 version

           Computer Bulletin Board -  703-241-7980



                              Joseph R. Ahlgren
                              2218 N. Tuckahoe St
                              Arlington, VA  22205-1946


















                                        - 1 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11




                                  Table Of Contents

     A.  Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . . .   3

     B.    Getting Started . . . . . . . . . . . . . . . . . . . . . . . . .   3
          B.1.  EGA/VGA version (GEOEGA) . . . . . . . . . . . . . . . . . .   3
          B.2.  CGA/HGC/MCGA/ATT400/PC3270 version (GEOMNO)  . . . . . . . .   3
          B.3.  Mouse  . . . . . . . . . . . . . . . . . . . . . . . . . . .   4
          B.4.  Upgrading from version 2.x . . . . . . . . . . . . . . . . .   4

     C.    Operation . . . . . . . . . . . . . . . . . . . . . . . . . . . .   5
          C.1.  Single key functions . . . . . . . . . . . . . . . . . . . .   5
          C.2.  Commands . . . . . . . . . . . . . . . . . . . . . . . . . .   6
          C.3.  Command line parameters  . . . . . . . . . . . . . . . . . .   9

     D.    Customizing . . . . . . . . . . . . . . . . . . . . . . . . . . .   9
          D.1.  Time zone data . . . . . . . . . . . . . . . . . . . . . . .   9
          D.2.  Cities in GEOCLOCK.DAT and GEO<n>.DAT  . . . . . . . . . . .  10
          D.3.  Default parameters in GECONFIG.DAT . . . . . . . . . . . . .  10
          D.4.  Example GECONFIG.DAT and GEOCLOCK.DAT files  . . . . . . . .  11

     E.    Functions for registered users only . . . . . . . . . . . . . . .  12
          E.1.  Zoom . . . . . . . . . . . . . . . . . . . . . . . . . . . .  12
          E.2.  Distance . . . . . . . . . . . . . . . . . . . . . . . . . .  13
          E.3.  Time display for cities  . . . . . . . . . . . . . . . . . .  13

     F.    Files . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  14
          F.1.  GEOCLKnn.ARC . . . . . . . . . . . . . . . . . . . . . . . .  14
          F.2.  GEOMNOnn.ARC . . . . . . . . . . . . . . . . . . . . . . . .  14

     G.    Technical Information . . . . . . . . . . . . . . . . . . . . . .  14
          G.1.  Ephemeris Data . . . . . . . . . . . . . . . . . . . . . . .  14
          G.2.  Use of Color . . . . . . . . . . . . . . . . . . . . . . . .  15
          G.3.  Software structure . . . . . . . . . . . . . . . . . . . . .  16
          G.4.  VGA and 8514A support  . . . . . . . . . . . . . . . . . . .  16
          G.5.  Map Generation System  . . . . . . . . . . . . . . . . . . .  16

     H.    Changes from previous versions  . . . . . . . . . . . . . . . . .  17

     I.    Bulletin Board  . . . . . . . . . . . . . . . . . . . . . . . . .  21

     J.    Upgrades and Enhancements for Registered Users  . . . . . . . . .  21

     K.    Registration and License  . . . . . . . . . . . . . . . . . . . .  21



                                        - 2 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     A.  Introduction

          GEOCLOCK shows the current time (based on the system clock) with a map
     of the earth.  The current sun position is displayed with a crossed circle,
     and the part of the earth in sunlight is highlighted.  This display is
     automatically updated every 1 second (for an 8 MHz AT with an 80287) to 20
     seconds (for a 5 MHz PC without an 8087).  Local sunrise, sunset, and the
     sun's azimuth and elevation are also displayed.  A variety of map
     backgrounds and other options are available.

        GEOCLOCK is distributed as SHAREWARE.  If you use and enjoy the product,
     you must register and obtain a license for the program.  The license
     includes a few extra features and more maps.  See section K.  The
     unregistered version of the program may be distributed freely, provided
     that the entire unmodified ARC file is included and no fee is charged other
     than a nominal amount for media and handling.

     B.    Getting Started

          There are two versions of GEOCLOCK.  The first is contained in
     GEOCLK33.ARC and is designed to support computers with a 256k EGA or VGA
     board with a compatible color monitor.  The second is contained in
     GEOMNO33.ARC and is design to support CGA, Hercules, MCGA, AT&T 640x400,
     and PC3270 graphics, all in the highest resolution monochrome mode
     available for that card.   Un-ARC the required file to the directory you
     will run from, and proceed to section B.1 or B.2 respectively.  
          If you are a registered user, you need to run the REGISTER program to
     enable the special features.  You will also want to use a mouse - see
     section B.3.  If you have been using GEOCLOCK version 2.x and are updating
     to version 3.x, see section B.4.

     B.1.  EGA/VGA version (GEOEGA)

          The EGA/VGA version of GEOCLOCK requires an EGA, VGA, or close
     compatible with 256k memory, and an EGA, VGA, or multiscanning color
     monitor.  The program uses 640x350 16 color graphics.  The distribution
     GEOCLK33.ARC file contains all the required programs and data bases.  The
     main program file is named GEOEGA.EXE.  It will automatically determine
     whether or not you have a math co-processor (8087,80287, 80387), and use it
     if you do, or emulate it if you do not.  Simply execute this file, and you
     are on your way!  F1 is a help key.

     B.2.  CGA/HGC/MCGA/ATT400/PC3270 version (GEOMNO)

          This version of GEOCLOCK is compatible with a wide variety of graphics
     boards, including all those two color modes supported by the Turbo Pascal
     5.0 GRAPH unit.  In particular, 640x200 CGA, 720x348 HGC, 640x480 MCGA,
     640x400 ATT, and 720x350 PC3270 mode are supported.  The 640x350 EGA

                                        - 3 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     monochrome mode is NOT supported (this is a four color mode), although the
     EGA emulation of HGC is supported provided your EGA board permits this. 
     The distribution GEOMNO33.ARC file contains all the required programs and
     data bases.  

          After Un-ARCing the program, the files configuring the system for your
     graphics adapter must be built.  The installation program GEOCONVT builds
     these files, installs the proper drivers, and converts the maps to the
     required format.  This program in started by:

          GEOCONVT <board type> [map file spec] [switches]

     where board type is CGA, HGC, MCG, ATT, or 327.  The [map file spec]
     specifies which map files are to be converted to the format for your
     adapter.  If omitted, MAP*.EGA is assumed.  The switches are zero or more
     of /D (which specifies that files not required for your particular adapter
     are to be deleted) and /C (which specifies that map files are to be
     converted, but no other conversions are to be done).  By default, neither
     option is selected.  Specifying /D saves space on your disk, but be sure
     that you have kept a backup or the original ARC file before selecting this
     option.  You should specify /C is you are already running GEOMNO and only
     need to convert a new map file.  

          After this program has run, simply execute GEOMNO.EXE, and you are on
     your way!  F1 is a help key.

     B.3.  Mouse

          Several GEOCLOCK functions require a graphics cursor for input.  These
     operate from both a mouse and the keyboard.  To use the mouse, the INT 33
     driver must be loaded.  This driver, which comes with most mice, is usually
     called MOUSE.COM or MOUSE.SYS.  The mouse buttons and functions are
     emulated on the keyboard as follows:

         Left Mouse Button           Control (CTRL) Key
         Center Mouse Button         Escape (ESC) Key
         Right Mouse Button          Alternate (ALT) Key
         Mouse Motion                Arrow keys and Shift-Arrow keys

          All the keyboard equivalents work whether or not a mouse is available. 
     In particular, the arrow keys may be used to finely position the cursor
     after the mouse has moved the cursor to the vicinity of the desired point,
     and the Escape key can be used if your mouse does not have a center button.

     B.4.  Upgrading from version 2.x

          Version 3.x contains many new features which require changes in some
     of the 2.x files for optimum operation.  Existing 2.x data files will work

                                        - 4 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     but cannot take advantage of these new features.  The conversion process
     effects four types of files.
            a.  MAP<n>.EGA.  This only effects the EGA/VGA version of GEOCLOCK. 
     The map format was changed to reduce the sizes of the map files.  While
     GEOCLOCK 3.x will display both file formats, processing of the new format
     is faster.  The program CVTMAP.EXE, available on the GEOCLOCK bulletin
     board, will convert the old to new format.  To convert your existing maps,
     follow this procedure:
         DEL *.BAK
         COPY MAP*.EGA MAP*.BAK
         CVTMAP MAP*.BAK *.EGA
         DEL *.BAK
            b.  GECONFIG.DAT.  This file was required only for GEOMNO in version
     2.x.  In version 3, this file optionally contains a list of command line
     parameters (one per line).  In addition, two new commands are of particular
     interest: ZONE, which defines time zone characteristics; and PCZONE, which
     defines which time zone the PC's local clock is in.  The GECONFIG.DAT file
     provided should be used until you feel the need to change it.  GEOCONVT
     appends any existing GECONFIG.DAT file (including the one provided in
     GEOMNOnn.ARC) to the one it produces while setting up GEOMNO.  See section
     D.
            c.  GEOCLOCK.DAT and GEO<n>.DAT.  The format of these files has been
     enhanced to take advantage of the time zone data.  The old first line,
     which specifies the displayed zone and its relationship to the PC clock, is
     now optional.  If it is omitted, it is assumed that PC local time is to be
     displayed, as specified by the PCZONE command.  If a zone code is named,
     that is the local time displayed.  On the subsequent lines, for registered
     users, the time offset (specified by +n or -n after the !) may be specified
     as <space><zone code> or <space>*<zone code>, in which case the city time
     is displayed in the time zone specified by the zone code.  If * is
     included, the time zone name is also displayed.  See section D.
            d.  *.BGI files must be replaced with new versions, since version 3
     was compiled under Turbo Pascal 5.0.  These are included in GEOMNOnn.ARC.  

     C.    Operation

          To run GEOCLOCK, simply enter "GEOEGA" or "GEOMNO".  The initial
     display is built, and then this display is updated continuously.  The
     program recognizes a variety of functions while running.  Each of these is
     activated by pressing a letter key.  These functions are summarized below. 


     C.1.  Single key functions

            Function Key 1 - activates the help system.  The first screen is a
     menu listing all the GEOCLOCK parameters and keys.  Selecting a menu item
     by pressing the indicated letter displays additional information.  You exit
     the additional information screen and display the main menu by pressing any

                                        - 5 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     key.  You exit the help system and return to GEOCLOCK display or parameter
     entry by pressing any non-letter key.

            F - speed up the rate of change of time per display update. A prompt
     asks for the number of hours (possibly fractional or negative) for the
     displayed clock to be incremented during each cycle, e.g., 0.25 for 15
     minutes every 1 to 20 second cycle.

            U - set the interval between screen updates.  A prompt asks for the
     update interval in seconds.  When this value is entered, the display is
     immediately drawn.  Subsequently, the screen in updated at the specified
     interval and synchronized with the clock.  Thus, if 15 is specified, the
     screen will be updated at 0, 15, 30, and 45 seconds past the minute.  If
     your computer is not fast enough to achieve this update interval, the
     smallest integer multiple of this interval which works will be used.

            T - change the display time according to prompts in yy/mm/dd
     hh:mm:ss format.  This does not change the system clock.  Any missing data
     will revert to the current local time.  Thus "///12:0:0" sets the time to
     today at 12 noon, while 88 01 01 0 0 0 sets the time to midnight, January
     1, 1988.  All times in GEOCLOCK use the 24 hour format.

            R - restore the display time to the current time, and the display
     update rate to real time.  R undoes F, T, and U.

            P - allows changes to the command line parameters.  These commands
     are listed in section C.2 below.  Entering "?" or "HELP" at the prompt will
     activate the help system.

            S - select a map.  When this key is pressed, a list of available
     maps is displayed with their coordinates, title, and North-South distance. 
     The highlighted line corresponds to the current map.  The cursor keys can
     be used to scroll through this list.  When the <ENTER> key is pressed, the
     highlighted map will be displayed.  Some very early GEOCLOCK maps did not
     have titles.  If you have any of these maps, the FIXMAP program, available
     on the GEOCLOCK RBBS (703-241-7980) will add the proper titles.

            X - return to DOS.

            Escape - return to DOS.

     C.2.  Commands

            GEOCLOCK allows several command line parameters which control the
     display.  These parameters may also be entered in response to prompts from
     the "p" function above, included on the DOS command line, or included in
     the GECONFIG.DAT file.  An * indicates the default value.


                                        - 6 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


            ? - displays list of commands.
            HELP - displays list of commands.
            REM - remark.  The rest of the parameter is ignored.

            NOMAP - does not display any background map.
            MAP1..MAPn - displays appropriate map.  Map1 is the default.  The
     GEO*.ARC files include two maps.  MAP1 is a rectilinear projection of the
     entire Earth.  MAP2 is a map of the 48 states.  The EGA/VGA version also
     includes MAP2000, which is a North Polar projection map.  Other maps are
     available as detailed in section K.  Polar projection maps work only with
     the EGA/VGA version of GEOCLOCK.

            MARK - displays markers for the cities in geo*.dat.  See section D.3
           *NOMARK - does not display city markers or city names.
           *NOCITY - does not display city names for the cities in geo*.dat.
            CITY - displays city names.

           *QUIET - does not beep on screen update.
            SOUND - beeps each time the screen is updated.

           *NOLINE - does not display any latitude/longitude lines.
            LINEnn - displays latitude/longitude lines every nn degrees, unless
     that would result in more than 40 lines.  If nn is 0 or missing, the
     current latitude and longitude line intervals are not changed but lines are
     enabled, and thus LINE undoes NOLINE.
            TLINCnn - same as LINEnn, except only affects Latitude lines.
            GLINCnn - same as LINEnn, except only affects Longitude lines.
            TLSPECnn - displays one latitude line at nn.
            GLSPECnn - displays one longitude line at nn.  Up to 20 TLSPEC and
     GLSPEC lines may be specified.
            CLINE - removes all TLSPEC and GLSPEC lines.
           *HIDELL - does not label latitude/longitude lines
            SHOWLL - labels latitude/longitude lines

           *NORM - highlights sunlit area.
            REV - highlights area not sunlit (appropriate for LCD displays)
            LIGHT - highlights entire screen, and does not show sun symbol.
            DARK - highlights no area, and does not show sun symbol.

           *SHOWCH - (EGA version only) display screens as they are built
            HIDECH - (EGA version only) displays screens only after they are
     completed.
            PS2BUG - (EGA version only) use if, with SHOWCH set, the display
     goes blank during GEOCLOCK operation or after GEOCLOCK termination.  This
     works around an error in the PS/2 VGA BIOS.
           *NORAM - (EGA version only) use if map display is trashed.  This
     option adds approximately 25K to the memory required to execute GEOEGA.


                                        - 7 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


            USERAM - (EGA version only) use if there is insufficient RAM to run
     GEOCLOCK.  This option moves the disk buffer to an area within the VIDEO
     RAM.  Some EGA boards, including the ATI EGA wonder, are not compatible
     with the DMA-s of some computers, and this option will cause the display to
     be trashed or will cause disk errors.

            SHOWMN - displays the map number and name in the upper right hand
     corner.  This data may overlap the latitude/longitude display.
           *HIDEMN - does not display map name and number.

           *FULL - displays local location, time, and full ephemeris data.
            SUN  - displays location, time, and sunrise/sunset data
            TIME - displays local date and time at bottom of screen.
            NONE - displays no text data.
            SUNANGLEx - sets the elevation angle of the sun used to compute
     sunrise and set.  The default is -0.8333 degree, corresponding to the sun
     just breaking the horizon considering refraction effects.  SUNANGLE-6.0
     sets this angle to -6 degrees, which defines civil sunrise and set.  -12 is
     Nautical sunrise and sunset, while -18 is Astronomical sunrise and sunset. 
     This parameter does not effect the terminator line calculations.

            ZONE - defines a time zone.  See section D.2
            PCZONE - defines the time zone the PC's clock is in.  See D.2.
            EQUINOX - allows the exact GMT of an equinox to be specified (e.g.,
     EQUINOX 88/09/22 17:29).  This data is used to calibrate the sun position
     calculation to improve the accuracy near the equinoxes (while degrading it
     far from the equinoxes).  Personally, I do not think this is a very good
     idea, but I am tired of defending my position.  The current system computes
     equinoxes within a few minutes.

            CSET - (EGA version only) allows the screen colors to be changed
     interactively.
            COLORnxxyy - (EGA version only) changes screen color without
     interaction.  "n" specifies the feature number (0- 7) to be changed. 
     Feature number n will display color xx, and feature n+8 will display color
     yy.  Thus COLOR56262 will cause feature numbers 5 and 13 to display as 62
     (bright yellow).  See Section G.2 for a explanation of how color is used in
     GEOCLOCK.

            FAST - Forces GEOCLOCK to use a faster but slightly less accurate
     algorithm for drawing the sunlit area.  This is the default for systems
     without an 80x87.
            SLOW - Forces GEOCLOCK to use the high accuracy algorithm for
     drawing the sunlit area.  This is the default for systems with an 80x87. 
     On systems with an 80x87, the difference in speed between SLOW and FAST is
     negligible, while on those systems without an 80x87, FAST is approximately
     twice the speed of SLOW.  These options do not effect polar projection
     maps.

                                        - 8 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11



     C.3.  Command line parameters

          Any of the commands (other than ZONE, PCZONE, and CSET) in section C.2
     above may be entered on the command line that invokes GEOCLOCK.  These
     commands will be in effect when GEOCLOCK begins, and override commands
     placed in the GECONFIG.DAT file.

     D.    Customizing

          After the program has been extracted and is operating, you may wish to
     customize it for your computer.  The primary ways to customize the program
     is through some special text files.  These files can be customized with any
     text editor.  GECONFIG.DAT describes your graphics system, defines the time
     zones, and gives the default setting for the program.  The GEOCLOCK.DAT and
     GEO<n>.DAT files specify the cities and time zones to be displayed with
     each map.

     D.1.  Time zone data

          Time zones are user defined in GEOCLOCK.  Each zone (e.g., Eastern) is
     specified by giving its code name (e.g., ET), the names of summer and
     standard times (e.g., EDT and EST), the number of hours the time is ahead
     of GMT (e.g., -4 and -5), and the times between which summer time is in
     effect (e.g., 88/04/24 8:00:00 GMT and 88/10/30 8:00:00 GMT).  The zones
     are referenced by their code names, and thus the zone data need only be
     updated once per year (sometime during the winter) and in only one place
     (where the zones are specified).  It is most convenient to include the zone
     specifications in the GECONFIG.DAT file.

         The ZONE command takes 7 parameters: 1) a code name for the time zone
     (referenced by PCZONE, and GEO<n>.DAT files), 2) the name of the standard
     time, 3) the number of hours standard time is ahead of GMT (thus negative
     for US locations), 4) the name of the summer (daylight) time, 5) the number
     of hours summer time is ahead of GMT, 6) the date and time (GMT) to switch
     from standard to summer time, in the format yy/mm/dd:hh:mm:ss, with
     trailing data optional (e.g., 88/10/30:8), 7) the date and time (GMT) to
     switch from summer time to standard time.  If a zone does not change during
     the year, the last four parameters may be omitted.  This command is best
     used in the GECONFIG.DAT file.

          The PCZONE command sets the relationship between the local time on the
     PC's clock and GMT, i.e., declares which time zone the PC's clock is in. 
     It takes one parameter - a time zone code, as defined in the ZONE command. 
     This command is best used in the GECONFIG.DAT file, and it must follow the
     ZONE command that it references.



                                        - 9 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11



     D.2.  Cities in GEOCLOCK.DAT and GEO<n>.DAT

          Cities may be overlaid on the maps.  They are specified in GEO<n>.DAT
     files.  For map number n (e.g., 2, the 48 states map), these cities are
     read from GEOn.DAT (e.g., GEO2.DAT) if that file exists.  If the file does
     not exist, cities are read from GEOCLOCK.DAT.
          The first entry in a GEO<n>.DAT file specifies the time zone code to
     be used for the standard time display.  It consists of a line with a single
     zone code.  If this line is omitted, the code for PCZONE is used. 
     Ordinarily, this code should match the time zone code for the first city in
     the file.
          Following this time zone entry, command line parameters may be
     optionally included.  The command line parameters will be processed after
     both the command line and the GECONFIG.DAT file parameters, and thus will
     override entries there.  The command REM may be used to add comments to the
     file.  
          Subsequent entries in the file specify the name and locations of
     cities to be displayed.  Each entry consists of the latitude, longitude,
     and name of the city.  Latitude and longitude are in degrees and fractions
     (NOT degrees, minutes, and seconds), with North and East positive.  Thus,
     most US locations have positive latitude and negative longitude.  The first
     city specified is used for calculating the sunrise, sunset, and the azimuth
     and elevation angles for the sun.

     D.3.  Default parameters in GECONFIG.DAT

          The GECONFIG.DAT file may be used to specify default setting and time
     information.  If you are using GEOMNO, the first four lines must be as
     written by the GEOCONVT program.  They give specification data for your
     graphics system.  Subsequent lines contain command line parameters.  There
     should be no leading spaces on these subsequent lines.  This file is
     processed BEFORE the command line parameters are executed, so the command
     line will override parameters specified here.















                                        - 10 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     D.4.  Example GECONFIG.DAT and GEOCLOCK.DAT files

          The GECONFIG.DAT file supplied with GEOCLOCK looks like this:

     ZONE   ET     EST    -5    EDT    -4     89/04/02:7   89/10/29:7
     ZONE   EST    EST    -5
     ZONE   CT     CST    -6    CDT    -5     89/04/02:8   89/10/29:8
     ZONE   CST    CST    -6
     ZONE   MT     MST    -7    MDT    -6     89/04/02:9   89/10/29:9
     ZONE   MST    MST    -7
     ZONE   PT     PST    -8    PDT    -7     89/04/02:10  89/10/29:10
     ZONE   +3A    MZ     +3    MSZ    +4     89/03/26:1   89/09/24:1
     ZONE   +2     GMT+2  +2
     ZONE   +2A    OEZ    +2    MZ     +3     89/03/26:1   89/09/24:1
     ZONE   +1A    MEZ    +1    OEZ    +2     89/03/26:1   89/09/24:1
     ZONE   +0A    GMT    0     MEZ    +1     89/03/26:2   89/09/24:2
     ZONE   UKT    GMT    0     MEZ    +1     89/03/26:1   89/10/29:1
     REM
     PCZONE ET
     REM        The PCZONE command should be set to reflect
     REM         the time zone your PC's system clock runs
     LINE30
     SHOWLL
     FULL
     MARK
     CITY


          The first 13 lines start with the keyword ZONE.  These define some of
     the time zones around the world.  For example, the first line defines the
     Eastern time used in the US.  Line 15 (PCZONE ET) declares that the system
     clock in your PC is set to Eastern Time.  If your clock is not on Eastern
     Time, you will want to change it.  For example, if you are on the west
     coast of the US, you will want to change the line to PCZONE PT.  The next 5
     lines set the default values to be used in GEOCLOCK display.  This file
     sets the program to show latitude and longitude lines every 30 degrees, to
     show the full time display including sun rise and sun set times and sun
     azimuth and elevation data, and to display city names and locations on the
     maps.  You may wish to change these values to your own preferences.










                                        - 11 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


          The GEOCLOCK.DAT file supplied with GEOCLOCK looks like this:

     ET
     REM
     REM You should change the above time zone code
     REM  to reflect the time zone you want to display
     REM  at the bottom of the screen.  The time zone
     REM  code are contained in the GECONFIG.DAT file.
     REM
          38.90   -77.03 Washington
     REM
     REM The first city in this file is the city that
     REM  will be displayed at the bottom of the screen
     REM  You may want to change it.
     REM
          61.17  -150.00 Anchorage
          38.00    23.73 Athens
          13.73   100.50 Bangkok
          30.05    31.25 Cairo
          21.31  -157.83 Honolulu
         -26.17    28.03 Johannesburg
          51.50     0.00 London
          34.00  -118.25 Los Angeles
          55.75    37.70 Moscow
          28.62    77.22 New Delhi
         -22.88   -43.28 Rio de Janeiro
          41.88    12.50 Rome
         -33.92   151.17 Sydney
          35.67   139.75 Tokyo
     REM All the above cities will be displayed if
     REM  they fit on the map and the CITY and
     REM  MARK commands are on.

          The first line specifies the time zone that will be displayed on the
     bottom of the screen.  This is usually set to your local time, or to the
     local time for the primary city.  The first city in the file, in this case
     on the eighth line (Washington), specifies the primary city.  This city
     will be displayed on the bottom of the screen with sun rise, set azimuth,
     and elevation data.

     E.    Functions for registered users only

          The following functions are available to registered users only.  See
     section K for details on how to register.

     E.1.  Zoom



                                        - 12 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


          This function allows the user to change the map background using the
     cursor.  A mouse or the arrow keys can be used.  To invoke the function,
     press the letter Z.  The screen will be stabilize without any time or
     sunlight information, and an Iron-Cross type cursor will appear.  Use the
     mouse and/or arrow keys (shift-arrows move 8 times faster than non-shifted
     arrows) to locate a position on the map.  Each press of the right or left
     button on the mouse, or CONTROL or ALTERNATE keys on the keyboard, will
     switch to a new map containing that point.  The left button "zooms in"
     while the right button "zooms out."  The cursor will remain at the
     specified latitude/longitude during the switch.  When the desired map is
     displayed, press the middle button or the ESCAPE key to return to time
     display.  This function is available only to registered users.

     E.2.  Distance

            This function provides a display of the coordinates of three
     selected points, and the distances between them, as controlled by a mouse
     or the keyboard.  The function is invoked by pressing the letter D.  Point
     1 is selected by the left button of the mouse or the CONTROL key on the
     keyboard.  Point 2 is selected by the right button or the ALTERNATE key. 
     Point 3 is the current cursor position.  To return to the time display,
     press the middle button or ESCAPE.  To maintain smooth cursor movement, the
     distance and coordinate displays are updated only when the cursor is not
     moving.  This function is available only to registered users.

     E.3.  Time display for cities

          For registered users only, additional control over city placement,
     color, size, and local time display is possible.  All are marked by
     characters appearing after an exclamation point (!) on a city line in
     GEO<n>.DAT.  This new data consists of an optional string of  characters as
     follows:

          A - show city name Above mark
          B - show city name Below mark
          L - show city name Left of mark
          R - show city name Right of mark (if none of above specified, use
     best)
          Y - show city name in color 5 (Yellow by default)
          E - show city name in 8x14 font (8x8 by default)

          After these optional codes, the line may be optionally followed by a
     space and a time zone code.  If included, this specifies that the local
     time for that city is to be displayed to the right of the city name.  If a
     "*" is included, the name of the time zone will be displayed in addition to
     the time.  For example:



                                        - 13 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


                       ET
        38.90   -77.02  Washington !E
        42.65   -73.75  Albany NY !Y
        35.08  -106.65  Albuquerque NM ! *MT
        42.28   -83.75  Ann Arbor MI !A
        33.75   -84.39  Atlanta GA 
        44.30   -69.76  Augusta ME 
        33.52   -86.81  Birmingham AL ! CT
        46.80  -100.78  Bismarck ND !B *CT

     F.    Files

     F.1.  GEOCLKnn.ARC

         GEOCLOCK.DOC   This file.
         GEOCLOCK.DAT   An example of a customization file for GEOCLOCK.  See
     section B.3 for the details of the contents of this file.
         GECONFIG.DAT   A starter for the configuration file for GEOCLOCK.  See
     section D for details.
         GEOEGA.EXE     GEOCLOCK version for EGA.
         MAP1.EGA       EGA database for MAP1 (world).
         MAP2.EGA       EGA database for MAP2 (48 states).
         MAP2000.EGA    EGA database for MAP2000 (North Polar Projection).
         MAILER.        Printer file to aid registration.

     F.2.  GEOMNOnn.ARC

         GEOCLOCK.DOC   This file.
         GEOCLOCK.DAT   An example of a customization file for GEOCLOCK.  See
     section D for the details of the contents of this file.
         GEOMNO.EXE     GEOCLOCK version for two color graphics.
         GEOCONVT.EXE   Installation program to select drivers and font files,
     write configuration file, and convert maps to specific graphics format. 
     See section B.2 for instructions on the operation of this program.
         MAPA.EGA       Universal MAP1 (whole Earth).
         MAPB.EGA       Universal MAP2 (48 states).
         *.BGI          Various graphics drivers (Turbo Pascal 5.0).
         *.FON          Various font files.
         MAILER.        Printer file to aid registration.

     G.    Technical Information

     G.1.  Ephemeris Data and Accuracy.

         The ephemeris data in GEOCLOCK was derived by fitting data from
     "Interactive Computer Ephemeris" (ICE) to two twelfth order polynomials. 
     One polynomial computes the sun's latitude, while the other computes the
     sun's longitude at noon GMT.  Both assume a 365.242199 day year.  They were

                                        - 14 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     made by a least squares fit to 400 points around 1989 data.  In this
     interval, the maximum and RMS latitude errors are 0.016845 and 0.004049
     degrees, while the maximum and RMS longitude errors are 0.059805 and
     0.016630 degrees.  The fit has been tested against 1986 sun rise and set
     data, and with 1985 through 2000 spring equinox times, and is within a few
     minutes in time, but obviously there are no guarantees of the accuracy. 
     ICE is available on many astronomy bulletin boards, or from:

               Nautical Almanac Office
               Code FA
               U. S. Naval Observatory
               Washington, DC 20392

         The terminator is shown as the locations where the horizon bisects the
     sun without regard to atmospheric effects, so the sunrise occurs earlier
     and the sunset occurs later than the terminator indicates.  The sun rise
     and sun set times are computed as the times that the sun's center is a
     specified angle above or below the horizon, without regard for atmospheric
     effects.  The default value, -0.8333, corresponds to civil sun rise and
     set, where the visible edge of the sun just breaks the horizon.

     G.2.  Use of Color

          The EGA/VGA version of GEOCLOCK does not use the standard relationship
     between the color displayed on the screen (screen color) and the 4 bit code
     (feature number) stored in the adapter's display memory.  The use of the 16
     feature numbers is as follows: 

         feature       use            feature+8        use

            0    Political Bdy (dark)    8       Political Bdy (light)
            1    Water (dark)            9       Water (light)
            2    Land (dark)            10       Land (light)
            3    Land/Water Bdy (dark)  11       Land/Water Bdy (light)
            4    Text Background        12       Text Foreground
            5    Aux Text Color (dark)  13       Aux Text Color (light)
            6    Lat/Long Lines (dark)  14       Lat/Long Lines (light)
            7    Frame and Text         15       Frame and Text

           The display colors are determined by the formula:
      color = B + 2*G + 4*R + 8*b + 16*g + 32*r, where   
            B  bright blue              b dim blue
            G  bright green             g dim green
            R  bright red               r dim red





                                        - 15 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


          Some typical colors are:
        name              RGBrgb      color value

        black             ------         0
        white             RGBrgb        63
        dark blue         -----b         8
        blue              --B---         1
        light blue        --Brgb        57
        dark green        ----g-        16
        green             -G----         2
        light green       -G-rgb        58
        brown             R---g-        20
        light yellow      RG-rgb        62      
        red               R-----         4
        bright red        R--rgb        60

     G.3.  Software structure

          GEOCLOCK is written entirely in Turbo Pascal version 5.0, except for
     the mouse interface routines and a few inline sections required for speed. 
     It has approximately 5300 lines of executable code.  It uses 8 byte reals
     for most calculations, and thus relies on the 80x87 emulation package for
     systems without a math co-processor.  The EGA/VGA version uses a custom
     graphics package which provides access to special hardware features (such
     as independent control of screen planes, disk I/O directly to the video
     memory, and preserving the graphics memory during text display) that are
     not available in the EGAVGA.BGI driver.  The monochrome version uses the
     GRAPH unit, and builds a screen image in RAM before copying the image in
     its entirety to video memory.  The GRAPH unit functions other than PUTIMAGE
     are not used except for a few special applications, such as drawing the
     graphics cursor, and updating the position and distance displays in the
     distance function.

     G.4.  VGA and 8514A support

          Many users have asked for a VGA version of GEOCLOCK (other than using
     the VGA as an EGA emulator).  Unfortunately, this is not possible.  One of
     the keys to the smooth screen updates and speed of operation is building
     the next display screen while displaying the current screen.  The display
     and work screens are swapped when the update is complete.  The VGA in
     640x480 mode does not have enough memory to support two separate screen
     images.  (640x480x4/8x2=307200 bytes)  The 8514A overcomes this problem,
     but until the standard becomes clear I am unwilling to invest the time and
     energy in producing a version for this adapter.

     G.5.  Map Generation System



                                        - 16 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


          The maps used for the GEOCLOCK program were produced by a custom data
     base and software system.  This system consists of a highly compressed
     vectorized map data base and a set of programs to convert the data into
     custom maps.  The data base is a PC conversion of World Data Bank II.  It
     contains approximately 5.7 million vectors covering coastlines, islands,
     lakes, rivers, and similar geologic features, together with political
     boundary data.  It covers the entire earth, and included features are
     accurate to approximately 600 meters.  World Data Bank II was converted to
     this custom PC format by an ad hoc program which took advantage of specific
     features of both data bases.  In its operational form, the PC data base
     uses approximately 0.84 bytes per data point, and in archival form takes
     approximately 0.5 bytes per data point.  The data base is therefore easily
     stored and manipulated on an AT class PC.

          Custom maps are generated by using two programs.  The first, MAPGEN,
     reads the appropriate parts of the map data base and produces separation
     files of the required feature data as EGA or VGA raster images. 
     Rectangular, polar, or Lambert projections may be used in forming these
     separation files.  Depending on complexity and scale, this process takes
     between 30 and 300 seconds on an AT with a co-processor.  The second,
     MOVIE, allows the user to process the separation files to select the
     features and colors for the final map, including filling areas.  This
     program also writes the map in a rasterized compressed format with headers
     and trailers so that it may be easily used as background data for other
     programs (for example, the GEOCLOCK program).

          Both these programs, and the converted data base, are proprietary and
     not yet available to the general public.  World Data Bank II is available
     from National Technical Information Center, Springfield, VA, for about
     $1000 on 5 reels of tape.

     H.    Changes from previous versions

     H.1.  Version 2.3 to version 2.4

          CSET, Zoom, and Distance functions were added.
          If GEO<n>.DAT exists, it is used for city and time zone information
     when displaying MAP<n>.EGA, otherwise GEOCLOCK.DAT is used, e.g., GEO2.DAT
     is used while displaying MAP2.EGA.
          If the system detects hardware incompatibility, a prompt for
     proceed/abort is given.  A few EGA boards, and apparently the IBM VGA
     board, are not properly detected by this program.  However, they do  appear
     to work.

     H.2.  Version 2.4 to version 2.5

          The two color graphics version of GEOCLOCK was made compatible with
     EGA version and will be distributed as GEOMNOnn.ARC.

                                        - 17 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


           Offset from local PC time to display time added.
          Latitude and Longitude Lines were added with the LINE parameter.  MAP1
     has been modified to remove the lines so that all maps are under the
     control of this feature.
          Graphics hardware detection software removed.  As opposed to most
     software changes, this "feature" has proven to be only an annoyance.  If
     you do not have proper graphics hardware to support the version, the
     results are unpredictable.  A fatal message is still issued if the version
     requires an 80x87 but your system does not have one. 

     H.3.  Version 2.5 to version 2.6

          Version 2.5 was not distributed correctly.  Version 2.6 corrects this
     error.  The version 2.5 code does not execute correctly on systems without
     a Numeric Co-Processor.

     H.4.  Version 2.6 to version 2.7

          The code which generates latitude and longitude lines was improved to
     give additional control over line colors.
          An option to label the latitude and longitude lines was added.  The
     latitude lines are drawn from North to South.
          The function "CSET" was added to the non-registered version of the
     program.
          The registration of the markers and the location names was improved
     for the EGA version.  Cities whose names would overlap cities already
     displayed are suppressed.
          The processing of Longitudes was generalized so that maps with 180
     degrees in as an interior longitude can be processed.  The processing for
     the zoom function was generalized to preserve cursor locations for these
     maps.
          The DARK and LIGHT options were added to the display control.
          The SHOWCH and HIDECH options were added.  The use of the display
     buffer was improved in the EGA version.     
          A function giving a help screen when function key F1 is pressed was
     added.

     H.5.  Version 2.7 to version 2.8

          The TIMEB command was added to display time and time zone name at the
     bottom of the screen.
          The COLOR command was added to change the palette without interacting
     with CSET.
          The implementation of city name was changed to allow longer city
     names.
          Users can control the position, font size, and color of city names
     (registered users only).  These features were extended to include the
     monochrome version.

                                        - 18 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


          Local time for each city may be displayed (registered users only).    

          Precision of the cursor used for zoom and distance improved.
          The SHOWMN and HIDEMN commands were added to display the map name and
     number on screen.
          The PS2BUG command was added to help users work around a bug in the
     PS/2 VGA BIOS.  Some changes in screen handling were made to minimize the
     effect of this problem even when PS2BUG is not selected.
          The speed of the non-80x87 version was substantially improved
     (approximately 1/3 faster) by reorganizing the terminator line
     calculations.

     H.6.  Version 2.8 to version 3.0

          The handling of time zones was completely revised.  The GECONFIG.DAT
     file contains the descriptions of all world time zones, including the names
     of summer and standard times, their offsets from GMT, and the times of the
     year that summer time is in effect.  The GEO<n>.DAT file formats were make
     consistent with this standard.  Therefore, all time zone information can be
     concentrated in one place, and the GEO<n>.DAT files can refer to this
     information symbolically.  The old format is still accepted, but mixing the
     two is not recommended.
          The map file format, and the display palette, were changed to reduce
     map file size and drawing time.  The program CVTMAP was developed to
     convert the old map file format to the new map file format.  Conversion is
     not required but is recommended.
          A problem affecting the distance measuring function, and use of the
     mouse, for the hercules and ATT 400 versions was fixed.
          A problem which sometimes caused city name and time data to overwrite
     the legend data at the bottom of the screen was fixed.
          The control of the "zoom" feature was improved so that the left button
     "zooms-in" and the right button "zooms-out".
          A serious error in GEOCONVT affecting the MCGA mode was fixed.  That
     is problem was not noticed earlier tells me that the MCGA is not exactly
     widely used!
          The format of the GECONFIG.DAT file was extended so that the default
     command line parameters can be set and time zone characteristics can be
     defined.
          The separate versions for systems with and without math co-processors
     were eliminated.  The program automatically detects the math co-processor,
     and uses it or emulates it as appropriate.  This slows the program slightly
     but reduces the size of the distribution file dramatically.  The FAST and
     SLOW parameters were added to control the method used to draw the
     terminator (the FAST method is much faster on systems without an 80x87).
          The EQUINOX parameter was added to optionally improve the accuracy of
     GEOCLOCK near the equinoxes, although this degrades the overall accuracy of
     the program.


                                        - 19 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     H.7.  Version 3.0 to 3.1

          The NORAM and USERAM command line parameters were added, and the
     default was changed to NORAM.
          The calculation of sun rise and sun set times was improved, especially
     in areas in extreme latitudes.  The display uses "Dark all day" or "Light
     all day" when the sun never rises or sets.  The parameter SUNANGLE was
     added to allow the definition of sun rise and set to be changed.
          Support for polar projection maps was added to the EGA/VGA version. 
     It is not available in the MNO version.
          The response time for a key press during the generation of the next
     display frame was greatly decreased.  Except during a fill operation on the
     polar projection maps, the response to a key press should be less than 0.3
     seconds.
          A larger marker for the two fixed points in the distance function was
     incorporated, replacing the almost invisible symbols.

     H.8.  Version 3.1 to 3.2

          The accuracy of the sun position calculations was improved.  It is now
     within about 5 minutes (time) in both latitude and longitude for the rest
     of the 20th century.  Section G.1 gives details.
          The accuracy of the distance calculation was improved.  Distances are
     calculated on a sphere with the same volume as the Earth, i.e., with radius
     6371.22 kilometers.
          The control over latitude and longitude line placement was greatly
     enhanced with the addition of the GLINC, TLINC, GLSPEC, TLSPEC, and CLINE
     commands.  See section C.2.
          The symbols used in the distance function now blink.
          The help system was completely revised.  Pressing F1 or ? or "H"
     during GEOCLOCK display brings up a menu.  Selecting a menu item brings up
     more detailed information.
          The REM command was added to allow users to document their GEOn.DAT
     files, and commands will be processed from GEOCLOCK.DAT and GEOn.DAT files
     in addition to GECONFIG.DAT.
          A bug that sometimes caused ZOOM and DISTANCE to ignore cities in the
     GEOn.DAT files was fixed.
          The GEOCONVT program was improved to allow map file conversions,
     control file deletion and GECONFIG.DAT processing from the command line,
     and another MCGA problem was fixed.  The speed of the map conversion
     process was doubled.

     H.9.  Version 3.2 to 3.3

          The tab character is now treated as a space in the input files.
          The map select (S) function was added.
          The update interval (U) function was added.


                                        - 20 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11



     I.    Bulletin Board

         A free Remote Bulletin Board System (RBBS) provides support for users
     of the GEOCLOCK sunlight clock program.  It always has the latest and
     untainted version of GEOCLOCK available for downloading.  In addition, it
     provides a forum for all interested parties for program and information
     exchange concerning GEOCLOCK, high quality graphics for the IBM PC, high
     quality mapping for the IBM PC, and Turbo Pascal.  Information on potential
     applications and needs is as important as information on techniques and
     software.  The board is intended to help identify and solve real problems.
         Registered GEOCLOCK users have access to certain special files and
     higher access limits.  Please have your registration number handy when you
     log on for the first time.  Otherwise, the messages and files on the board
     are available to everyone.
         I also solicit comments and suggestions.  I am especially interested in
     including position and phase data for the moon and perhaps other planets.
         The RBBS number is 703-241-7980.  This is a Washington DC metro area
     number.

     J.    Upgrades and Enhancements for Registered Users

         The GEOCLOCK bulletin board always has the latest version of GEOCLOCK,
     and a variety of extra map files and utilities available.  In addition,
     many other bulletin boards and shareware distribution services also carry
     the latest version of GEOCLOCK.  Registered users may obtain the latest
     version from any of these sources.  When a new version is released, replace
     the files you originally received with the new versions.  The REGISTER
     program, supplied on your distribution disks, must be rerun to enable the
     special features such as ZOOM and DISTANCE that are available only to
     registered users.  If you have customized any of the GE*.DAT files, you may
     want to use the old versions of these files, or to edit the new versions to
     reflect your specific requirements.

     K.    Registration and License

         The GEOCLOCK program is distributed as Shareware.  This means that
     prospective users may use the program for a short evaluation period before
     deciding whether to purchase it.  A license must be obtained to use any
     copy after this evaluation period.  By sending $25 to the address below, a
     user will receive a single copy license, the latest version of the program,
     a registration program which will enable a few special features in the
     GEOCLOCK program not available in the evaluation version (see section E), a
     file with the name, latitude, and longitude of many world cities for
     building GEOCLOCK.DAT files, a "starter set" of GEO*.DAT files, and the
     following 28 maps:



                                        - 21 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     MAP1    World                     MAP2    48 States
     MAP3    Eastern US                MAP4    SouthWestern US
     MAP5    Western Europe            MAP6    Alaska
     MAP7    New York City Area        MAP8    Finer Scale NYC
     MAP9    SouthEastern US           MAP10   NorthWestern US
     MAP11   Chicago Area              MAP12   Texas
     MAP13   Washington DC             MAP14   Carolinas
     MAP15   Pennsylvania              MAP16   New England
     MAP17   Central America           MAP18   South America
     MAP19   Africa                    MAP20   Australia
     MAP21   India                     MAP22   Middle East
     MAP23   Micronesia                MAP24   Japan
     MAP25   China                     MAP2000 North Polar Map           
     MAP2001 North Polar Map 45        MAP2002 South Polar Map

     The polar maps work with the EGA/VGA version of GEOCLOCK only.

          The prices for the GEOCLOCK program are:

           1 copy              $25
           2-9 copies          $20/license
           10-20 copies        $18/license
           21-40 copies        $15/license
           41+ copies          $12/license
           site license        $500 for unlimited use at a single site.

          These prices assume that the purchaser will produce the authorized
     copies from a single master copy.

          GEOCLOCK is normally shipped on two 360K 5.25" floppy disks.  It is
     available on a 720K 3.5" floppy disk for an additional $5.00.  

          For an additional $15, a set of at least 15 supplemental maps will be
     included, and the next major release of the program will be mailed when it
     becomes available.  All these items are available for downloading at no
     charge from the GEOCLOCK support RBBS.  See section I.

          Please add $5.00 for shipping and handling for destinations outside
     the US and Canada.  Cash or checks in US funds draw on US banks only.

          The file MAILER can be printed to give both a registration form and an
     envelope.

          Additional custom rectangular maps can be produced from my existing
     database for $25 per map.  Simply specify the latitude and longitude of the
     center point, and the north to south distance on the map (the map will be
     scaled so that distances and azimuths are correct in the center of the
     map), or the latitude and longitudes of the corner points.  Custom maps

                                        - 22 -













     Joseph R. Ahlgren           GEOCLOCK version 3.3                   89/06/11


     based on user supplied feature data or other projections (the GEOCLOCK
     program only uses flat rectangular and polar projections, but Lambert and
     perspective projections are available) are possible but must be negotiated
     on a case-by-case basis.



                              Joseph R. Ahlgren
                              2218 N. Tuckahoe St
                              Arlington, VA  22205-1946







































                                        - 23 -