(File HANDLES.DOC)

HANDLES.ARC contains the source, object, and documentation of a method of 
increasing the number of files that can be open simultaneously using Clipper
up to 255, as limited by buffer memory.

Author:  Hugh Coomes
         Vericom Systems, Inc.
         19 Old Mamaroneck Road
         White Plains, NY 10605
         Source ID: NAN891

Placed in the public domain by Vericom Systems, Inc.  December 28, 1986

Requirements:  DOS 3.x  and  Clipper Autumn 86.

Directory of Files in HANDLES.ARC

HANDLES.DOC     -  This file

HANDLES.ASM     -  Source file for user defined function to increase the 
                   number of files.
HANDLES.OBJ     -  Object module assembled for 40 file handles.

HANDPROC.ASM    -  Some utility functions useful for testing.
HANDPROC.OBJ    -  Object module of above.


                            I N S T R U C T I O N S

To increase the number of file handles to <n> in a Clipper program, perform the 
following four steps:

   (1)  Change the HTABLEN equate in HANDLES.ASM to  HTABLEN equ <n> and 
        assemble it.

   (2)  Change the value of the FILES = <n> statement in CONFIG.SYS.  (HTABLEN
        is the optimum value.)
        
   (4)  Place the statement
        
                intvar = handles()
        
        in the Clipper program.   The variable intvar will have value 0 if
        the DOS version is prior to 3.0.  Otherwise the value will be equal
        to HTABLEN.  The above statement need NOT preceed all file IO.

   (5)  Link the module HANDLES.OBJ with the Clipper program.  HANDLES.OBJ
        must be linked before the Clipper library is searched in order to
        include the revised _UFBS module (discussed below).


If there is an internal restriction on the number of work areas or open indices
in Clipper Autumn 86, I was not able to reach it within the available buffer
space in 640K of memory. 



The module HANDPROC.ASM contains the following three functions which may be
useful for testing:

handcnt()   -  Returns the number of used file handles.
handval(n)  -  Returns the DCB number for file handle n. (discussed below)
handsiz()   -  Returns the size of the handle table.

At any time during program execution, the number of available file handles is
       
                    min(handsiz(), <n>) - handcnt()

where <n> is the value of the FILES=<n> statement in CONFIG.SYS.  If anyone
knows a way of obtaining that value within a program, please send me a message
on The Source.


                   T E C H N I C A L   D E T A I L S

Much of the following information was extracted from a CompuServe file of
Randy Forgaard, CompuServe ID 70307,521, filename: EXTEND.PAS.  Most of the
information is not documented in the DOS Technical Reference manual.

Under DOS 1.0 and 1.1, all files were accessed via File Control Blocks (FCB's).
There was no limit to the number of FCB's that a program could use, so there
was no limit to the number of files open simultaneously.

Under DOS 2.x, an alternate (and preferable) method of accessing files
was introduced, using a 2-byte integer called a "handle" to refer to a
file.  A "handle" file is described using a data structure called a Device
Control Block (DCB).  However, DOS provides the storage space for all DCB's,
rather than having the application program store the DCB's, so the number of
available DCB's is limited to the amount of space that DOS has set aside for
them.  The maximum number of files/devices that can be open simultaneously, on
the whole computer, is the number of slots available in the DCB Table created
by DOS.  The DCB's in the DCB Table are consecutively numbered, starting with
0.  DCB's 0, 1, and 2 are predefined by DOS to correspond to the AUX, CON, and
PRN devices, respectively.  All remaining DCB's in the DCB Table are available
for files or devices used by application programs.

So that I/O redirection can be supported, the DCB numbers are not used directly
when accessing files.  Instead, a file "handle" is used.  A "handle" is an
index into a 20-byte array, called the Handle Table, located at offset 18H of
the Program Segment Prefix (PSP) for a program (for a general discussion of the
PSP, see the DOS Technical Reference manual).  Each element of the Handle Table
is the DCB number of a file or device.  The value at index "handle" in the
Handle Table is the DCB number of the file or device that implements that file
handle.  Thus, if the value 8 is in the 6th byte of the Handle Table, the
handle "6" refers to the file (or device) described by the DCB in slot 8 of the
DCB Table.  If a handle is not currently being used, its entry in the Handle
Table is FFH.  DOS predefines the first 5 handles to be primary input, primary
output, error, auxiliary, and printer, so the first 5 entries in the Handle
Table are 1, 1, 1, 0, and 2, corresponding to the DCB numbers for the CON (1),
AUX (0), and PRN (2) devices.  This leaves only 15 available handles for
opening files (or new devices).



Every time a new handle file is opened, a new handle gets used.  Since there
are only 20 slots available in the Handle Table for a program, DOS only allows
a "process" to have a maximum of 20 file handles in use simultaneously (and the
first 5 entries are predefined, as just noted, unless those handles get closed
and reused).  Every new handle file requires a unique handle, so only 20
files/devices can be open at the same time by a single process (unless FCB's
are used).  (A "process" is any program spawned using the DOS EXEC function
call.  A process can be invoked by COMMAND.COM, or by another program.)  There
can be many more than 20 DCB's in the DCB Table, so the real limitation is in
the size of the Handle Table in the PSP.

In DOS 3.x additional information on the Handle Table was added to the PSP, but
was not documented in the DOS Technical Reference Manual.

At offset 32H of the PSP is a word containing the length of the Handle Table.
At offset 34H of the PSP is a double word containing a pointer to the Handle
Table.  DOS 3.x uses the pointer and the length to access the handle table. 
Thus the handle table can be moved in memory and its size increased.

The size of the DCB Table (i.e., the maximum number of files/devices that can
be open simultaneously in the whole computer) is controlled by the FILES=XXX
entry in the CONFIG.SYS file.  The minimum number of slots is 8.  Under DOS
2.0/2.1, the maximum number is 99, and under DOS 3.0 and higher, the maximum is
255.  As previously mentioned, the first three of these DCB slots are occupied
by the AUX, CON, and PRN devices.  

Thus under DOS 3.x a process can have more than 20 files open simultaneously if
its Handle Table is replaced by a larger one and an appropriate value of
FILES= is specified in the CONFIG.SYS file.

However, the application must not be internally restricted to the use of only 20
file handles.  Clipper Autumn 86, as released, is restricted to 20 files by
the module _UFBS in the Clipper Library.  This module contains the only 
restriction.  It contains only data definitions and can easily be replaced.

File HANDLES.ASM contains a function, handles(), which replaces the Handle Table
and also provides a replacement for the library module _UFBS.

                                  (eof)