REDEFINING KEYS WITH KERMIT

                         Mark Zinzow

 In a recent article, the basics of file transfer  with  Ker-
 mit,  including  what Kermit is, were covered.  This article
 will cover the commands for, and the uses of, key  redefini-
 tion  in Kermit-MS.  Future articles will cover other ameni-
 ties available in Kermit such as color definitions and  auto
 logon  script files, and new features in Kermit-MS 2.29A and
 CMS Kermit 3.1 that allow local printing  of  VMD  files  on
 your PC.

 Key redefinitions in Kermit-MS have a number of  uses.   One
 is  to  customize  your keyboard to your taste, a particular
 host, or host  application.   An  example  of  this  is  the
 7171KEYS.DEF  file  that is used by the MSKERMIT.INI file on
 our campus.  Another is to cut down on typing of  repetitive
 character  strings  such as the sequence of information used
 to login to a particular host.

    (NOTE: In the following article, Kermit prompts appear in
    regular  Roman  type; commands, parameters, etc. that are
    to entered by the user (as shown) are in upper case bold;
    parameters,  variables,  etc.  that the user must replace
    are in lower case bold.)

 Keys are defined with the SET command and displayed with the
 SHOW command.  In general the syntax of the SET command is:

      SET parameter [parameter] [value]
 For example the MSKERMIT.INI file contains a SET  BAUD  1200
 line which specifies the communications speed.  Here BAUD is
 the parameter and 1200  is  the  value  of  that  parameter.
 Those  people connecting to a host via a LocalNet port would
 edit this line to read SET BAUD 9600 to change  the  default
 setting,  rather  than  typing in the SET BAUD command after
 the Kermit prompt appears.

 When SET is used to define keys in Kermit-MS the syntax is:

      SET KEY {SCAN number | Fn | BACKSPACE} <Enter>
      value
 where number is a decimal scan code for the key you wish  to
 define,  n  is  the number of the function key, and value is
 the string you wish assigned to that key.   Characters  that
 are not easily typed may be included by typing their numeric
 equivalents as three octal (base eight) digits preceded by a
 backslash, e.g., \015 for a carriage return.

 For example, to define F1 (function key one) to generate the
 string  hi  there  when pressed, the command would look like
 this:

      Kermit-MS>SET KEY F1
      Definition string: HI THERE
 Unlike the backspace and functions keys, most  keys  do  not
 have a special name that can be used in the SET KEY command.
 For this reason most key  redefinitions  are  done  by  scan
 code.   There  are tables of the scan codes generated by all
 the keys on the keyboard in the manuals included  with  most
 systems;  however, the easiest way to find out what the scan
 code is for a particular key is to use the SHOW KEY  command
 in  Kermit.   Simply type SHOW KEY (can be abbreviated to SH
 K) at the Kermit-MS> prompt and  you  will  be  prompted  to
 press the key.  The scan code for the key and a redefinition
 (if the key is redefined) will be displayed.  If the key has
 not  been  defined  with the SET KEY command, the definition
 will be blank rather than a display of the actual  character
 sent  to  a  host  by  Kermit  (by  default) when the key is
 pressed.

 Here's how to look at, and then program, F1 for our 7171:

      Kermit-MS>SHOW KEY
      Press key:
        Scan code: 59
        Definition:

      Kermit-MS>SET KEY F1
      Definition string: \0331
      Kermit-MS>SH K
      Press key:
        Scan code: 59
        Definition: \033
        1
 The command SET KEY SCAN 59 would be the same as SET KEY  F1
 in  the above example.  Most keys have a different scan code
 when combined with the SHIFT, CTRL, and ALT keys.  With  the
 various  combinations  of one or more of these modifier keys
 it is possible to assign 80 different  strings  to  the  ten
 function keys alone!  (For those with the new keyboards with
 F11 & F12 keys, current  versions  of  Kermit-MS,  including
 test  releases  through  2.29B, do not recognize these keys;
 however,  release  2.30  will  support   these   keys   when
 released.)

 Obviously it is far too cumbersome to type  in  key  defini-
 tions  manually every time Kermit is run.  That is why there
 are three ways to store these  commands  in  files:  command
 files, macros, and the initialization file.  Any simple text
 editor can be used to create a file of Kermit  commands  and
 then  such  a  file  can be executed by Kermit with the TAKE
 command.  If this file has a special name  (MSKERMIT.INI  in
 MS-DOS,  userid  KERMINI  in  CMS) Kermit will automatically
 TAKE it when it starts up.

 In CMS the following are commands that would be  appropriate
 to  be placed in a userid KERMINI file (e.g., CMS user MARKZ
 would call this file MARKZ KERMINI A):

      SET BLOCK 3
      SET RECEIVE PACKET-SIZE 1000
      SET WARNING ON
 (None of these commands are necessary; they are  given  here
 only  as an example of an initialization file.  See HELP CSO
 KERMIT for an explanation that will allow you  to  determine
 the desirability of these commands for you.)

 Macros are defined with the DEFINE command and executed with
 the DO command.  The syntax of the DEFINE command is:

      DEFINE macro-name [command [, command [, ...]]]
 All commands associated with a macro name are  placed  after
 the  macro name, separated by commas.  For example, here are
 some define commands that might  be  typically  found  in  a
 MSKERMIT.INI file:


      DEFINE 96 SET BAUD 9600
      DEFINE NO SET PARITY NONE
      DEFINE E SET PARITY EVEN
      DEFINE BA SET KEY BACKSPACE,\010
      DEFINE VM TAKE VM
      DEFINE UNIX TAKE UNIX

 The first four DEFINE commands create macros that  are  just
 shortcuts for longer commands, i.e., it is easier to type DO
 NO than SET PARITY NONE.  The last two TAKE files (named  VM
 and  UNIX) that might have more commands than would fit in a
 macro definition.  They would contain commands to  customize
 the  keyboard  for the host operating systems for which they
 are named (UNIX and VM/CMS).

 For instance, here is a file  (called  VM  in  our  example,
 stored in the PC Kermit directory on disk) of commands suit-
 able for modifying Kermit for use on VMD:
      ; Modifications to default INI's for VM
      SET PARITY EVEN
      SET RECEIVE PACKET 1000
      SET SEND PACKET 1000
      ; personal enhancements to the standard key definitions follow
      ; correcting backspace assigned to backspace key
      SET KEY SCAN 14
      \033OD\177
      ; fast Left assigned to ctrl left key
      SET KEY SCAN 1139
      \033OD\033OD
      ; fast Right assigned to ctrl right key
      SET KEY SCAN 1140
      \033OC\033OC
      ; Home assigned to keypad -
      SET KEY SCAN 74
      \010
      SET TERM COLOR 33,40

 Probably the most useful of these definitions is the one for
 the  backspace  key.   Since  Kermit-MS is emulating a VT102
 terminal, which is very similar to a DEC VT100 terminal, the
 ASCII  control  codes  used with Kermit on the 7171 protocol
 converter  are  those  for  the  VT100.   These  codes  were
 designed  for a keyboard layout different from that of a PC.
 Normally the backspace key  generates  the  ASCII  backspace
 control  code  eight  (010 in octal).  The 7171 performs the
 HOME function when it receives this code and places the cur-
 sor in the upper left hand corner of the screen.

 Since this is generally not what one expects when the  back-
 space key is pressed, it is convenient to make that key per-
 form in the usual manner.  However, there is no code  avail-
 able  on  the 7171 to perform this function.  The trick lies
 in realizing that a backspace  involves  two  other  simpler
 functions: moving the cursor left and deleting the character
 then under the cursor.  These functions  are  available,  so
 the  backspace  key  is assigned both the ESC O D left arrow
 sequence and the DEL  (ASCII  127,  177  in  octal)  control
 codes.

 Another common function on many systems  is  a  line  delete
 (e.g.,  kill  in UNIX) used to erase an entire line of input
 when one wishes to start over.  Again the 7171 does not per-
 form  this  function,  but  it  can  be  simulated using two
 simpler functions: field back tab and erase to end of field.
 The  7171KEYS.DEF file defines the Del key to be the charac-
 ter delete DEL.  To define shift Del to  be  a  line  delete
 (which  doesn't  alter  the  unshifted  Del)  the  following
 commands could be added to the VM file (referenced above):
      SET KEY SCAN 595
      \033\011\033\177

 Remember that the backslash introduces octal codes.  In this
 case,  it is for ESC (\033) TAB (\011) ESC (\033) DEL (\177)
 where ESC TAB is the 7171 field back  tab  and  ESC  DEL  is
 erase to the end of the field.

 When creating key definitions it is useful to have  a  table
 of ASCII codes and a copy of the VT100 control codes used by
 our 7171.  ASCII tables are included in the  system  manuals
 of  most computer systems and terminals, and are also avail-
 able as Reference Guide RF-0.5 at CSO  Sites.   VT100  codes
 used  by  the  7171 may be read on VMD with the command HELP
 7171 VT100, and printed with WRITEUP 7171  VT100.   Some  of
 the  comments  in  the 7171KEYS.DEF file supplement the 7171
 VT100 help file with the actual  ASCII  character  sequences
 generated  by VT100 keystrokes such as ESC O M which is gen-
 erated by the VT100 numeric keypad enter key and used by the
 7171 to clear the screen.

 Some keys provide special functions when using the  terminal
 emulator in Kermit-MS.  These functions would be lost (until
 the next release of Kermit) if  those  keys  are  redefined.
 Some  of  these  keys  are:  Home,  End, PgUp, PgDn, and the
 keypad + (grey).  All of the  special  functions  are  docu-
 mented  on page 210 of the Kermit User Guide (Sixth Edition,
 Revision 2) and are well worth exploring.  Two of  the  more
 interesting  ones  are  PgUp and PgDn.  PgUp is used to view
 the last page of text that has scrolled off the screen,  and
 PgDn  scrolls  back down the buffer.  This is very handy and
 simple to use on a UNIX system, but more difficult  to  make
 use  of  in  a  full  screen environment where the screen is
 always cleared before it has a chance to scroll.

 This feature can be used on VMD, for example, by filling the
 screen  buffer  before  beginning  a  7171 terminal session.
 This could be accomplished simply by holding down the  enter
 key  at the LocalNet (Sytek) # prompt and letting the # sym-
 bols scroll off the screen, or by logging into a UNIX system
 prior  to  your session on VMD.  Now if you see a screen you
 think you might wish to refer back to later, you  could  hit
 the  PgUp  key and redraw the screen with the reset (Ctrl G)
 or the reshow (Ctrl V) commands, and then continue your ses-
 sion.   The  saved  screen  could  then be quickly viewed by
 pressing PgDn, and then the current screen could be returned
 to by pressing PgUp.  With a little experimentation this can
 be a very handy feature of Kermit-MS, as several screens may
 be held in the screen buffer.

 The cursor (arrow) keys are also special and might not  work
 on  all hosts if redefined.  The VT100 terminal can generate
 two different sets of cursor motion  control  codes.   Which
 code  is used by Kermit-MS depends on whether the VT102 emu-
 lator is in cursor/numeric or application mode.  Usually the
 host will tell the emulator which mode it expects the keypad
 to be in when the terminal is initialized.  This happens  on
 VMD  when  you  enter  the  VT100 (or KERMIT) terminal type.
 Kermit-MS defaults to numeric mode and the 7171 uses  appli-
 cation  mode.  Should your PC have missed the command to set
 application mode, your arrow keys either won't work at  all,
 or  will  produce  codes that will be interpreted as strange
 function keys.  This situation can also occur  if  noise  on
 your  communications line causes the set cursor/numeric mode
 command to be sent to Kermit-MS, or if you  hit  the  Alt  =
 reset  emulator  command.  If  this happens, simply type the
 7171 reset command Control G. The 7171 will then  reinitial-
 ize  your  emulator and redraw the screen.  In UNIX this may
 cause your arrow keys to stop  working  in  the  vi  editor;
 again you must reinitialize your terminal.

 Scan codes are not affected by the status of the Caps  Lock,
 Num Lock, and Scroll Lock keys.  This can lead to unexpected
 problems.  For example, the 7171KEYS.DEF file redefines  the
 Ins key.  Normally when Num Lock is depressed the Ins key is
 the number zero; however, when the key is redefined the  new
 definition  supersedes  the Num Lock function and the insert
 codes are generated by  this  key.   To  work  around  this,
 remove the insert key definition from your 7171KEYS.DEF file
 if you wish to use your keypad in numeric mode, or hold down
 a shift key when typing numbers on the keypad.

 The 7171KEYS.DEF file redefines only those  keys  which  are
 not  normally used on most hosts, such as the function keys.
 If it included a definition such as the one mentioned  above
 for  the backspace key, that key would not function properly
 on a UNIX-based host.  When logging off a VM/CMS  system,  a
 user with all the example files above would type:
      CTRL-] C
      DO UNIX
      C

 (where C is the abbreviation  for  connect)  before  logging
 onto  a  UNIX  system.   Here  are a few lines that might be
 found in the file UNIX:
      SET KEY BACKSPACE
      \010
      SET PARITY NONE
      SET TERM COLOR 37,44

 Since there are many keys not normally  used,  they  can  be
 assigned  strings  for  tasks  in which the same sequence of
 commands are typed day after day.  A common example  is  the
 sequence  used to log into a host.  Here is a set of defini-
 tions a CMS user with a userid of MARKZ might use to stream-
 line logging in to VMD from an office LocalNet port:
      SET KEY SCAN 2092  ; ALT-Z
      CALL 4500\015
      SET KEY SCAN 2093  ; ALT-X
      KERMIT\015
      SET KEY SCAN 2094  ; ALT-C
      \015l MARKZ\015\015

 With these definitions all MARKZ would type to login to  VMD
 would  be  Enter  until the # prompt appeared, Alt-Z, Alt-X,
 Alt-C, his password, and another Enter.  A variant  of  this
 for users that share a single machine would be to place each
 person's userid on the Alt letter of a first initial.



                          References


 Kermit: A File Transfer Protocol,  Frank  da  Cruz,  Digital
 Press, Bedford, Massachusetts 01730, 1987
      Although more expensive than other sources, this is the
      best  information  available on every aspect of Kermit.
      This book  assumes  no  prior  computer  knowledge  and
      explains  every  aspect of Kermit in very simple terms.
      The book  ends  with  a  thorough  explanation  of  the
      implementation of all the features of the Kermit proto-
      col with numerous programming examples.  This  book  is
      highly  recommended  for  anyone  who  wants a detailed
      understanding of Kermit.

 Kermit User Guide, Sixth Edition, Revision 2, Frank da Cruz,
 editor, Columbia University Center for Computing Activities,
 New York, New York 10027, May 26, 1985

      This is the primary reference guide for Kermit and  its
      major versions.  It includes sections on Kermit in gen-
      eral and chapters on the  major  implementations.   The
      general  sections  are on the high density distribution
      versions of the Kermit disk for the IBM AT and compati-
      bles.   It  is also on VMD in the file KUSER DOC.  This
      may be ordered directly from CUCCA,  but  is  available
      for $3.00 from the CSO Distribution Center at 1208 West
      Springfield Avenue in Urbana.

 Kermit Protocol Manual, Fifth Edition, Frank da Cruz, Colum-
 bia  University  Center  for Computing Activities, New York,
 New York 10027, April 5, 1984
      This manual contains all of the  information  necessary
      to write your own version of Kermit for a computer that
      may not already have it.  This is on VMD in  the  files
      KPROTO  DOC and KPROTO UPD.  It is replaced by the Ker-
      mit book Kermit: A File Transfer Protocol.  See  Kermit
      Info-Digest, Volume 5, Number 13.

 Kermit: A File-Transfer Protocol for Universities, by  Frank
 da Cruz and Bill Catchings
   Part 1: Design Considerations and Specifications, BYTE the
   Small Systems Journal, p. 255, June 1984, Vol. 9, No. 6
   Part 2: States and Transitions, Heuristic Rules, and Exam-
   ples,  BYTE  the Small Systems Journal, p. 143, July 1984,
   Vol. 9, No. 7

      These  articles  provide  interesting  background   and
      technical  information on Kermit.  They are combined on
      VMD in BYTE DOC.

 Info-Kermit Digest
      A series of InterNet note discussions on  all  versions
      of  Kermit  and  enhancements  to the general protocol.
      These may be viewed on  some  UNIX  systems  by  typing
      notes  comp.protocols.kermit  and on other UNIX systems
      under a recently  changed  newsgroup  name  with  notes
      mod.protocols.kermit.  These are available on most sys-
      tems that carry net news or  notes  and  will  soon  be
      available on VMD.

 In addition to these resources, each implementation of  Ker-
 mit  for any specific computer is usually accompanied by one
 or more documents specifically for that version.