LAN-LINK VERSION 1.58 PAGE 1  


                LAN-LINK Copyright (c) 1988, 1989, 1990 by G3ZCZ
                               All Rights Reserved 

                                Joe Kasser G3ZCZ
                                    POB 3419
                                  Silver Spring
                               Md., 20918, U.S.A.
                                 (301) 593 6136

                       U.S.A. Packet BBS Routing G3ZCZ @ N4QQ

                 World Packet BBS Routing G3ZCZ @ N4QQ.MD.USA.NA
                                  _______
                             ____|__     |                  (tm)
                          --|       |    |-------------------
                            |   ____|__  |  Association of
                            |  |       |_|  Shareware
                            |__|   o   |    Professionals
                          -----|   |   |---------------------
                               |___|___|    MEMBER

        LAN-LINK  is  a Personal Packet Terminal Program  for  the  TNC1, 
        TNC2, KPC-2 and most of all a smart multimode digital  communica-
        tions controller for the KAM, MFJ1278 and the PK-232.

             LAN-LINK is written and supported by Joe Kasser, G3ZCZ.

        The program is distributed as a Shareware product. You may freely 
        copy  and  share  the product for noncommercial  use,  with  your 
        friends,  associates and other radio hams. If you decide  to  use 
        the  product, you are asked to become a registered user  by  com-
        pleting  the  registration  form and sending it,  and  $35.00  or 
        equivalent in foreign currency to the author.

        Upon  receipt  of your registration, you will  receive  one  free 
        update disk, telephone and mail (electronic and regular) support. 

        This product may not be sold or distributed with another  product 
        without the express written permission of Joe Kasser, G3ZCZ. 

        Joe  Kasser,  G3ZCZ will only support unmodified copies  of  this 
        software.  Your comments and suggestions for changes are  however 
        welcome.  If you are the first to suggest a change that is imple-
        mented,  you will be sent a complimentary copy of the  disk  with 
        the change incorporated.

        Potential Commercial Users please contact Joe Kasser directly for 
        modifications and/or details of Site licensing.






        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 2  


                                TABLE OF CONTENTS

        1.0  INTRODUCTION
                  1.1  PROGRAM HIGHLIGHTS
                  1.1.1  Packet Radio
                  1.1.2  AMTOR
                  1.1.3  Morse/BAUDOT/ASCII

        2.0  Getting Started
             2.1 Bringing LAN-LINK Up the First Time
             2.2 Using the Quick Menu
             2.3 Connecting to Other Stations
             2.4 Upgrading from YAPP
             2.5 Using Different TNCs
             2.6 Using Different HF and VHF Configuration Files
             2.7 Using the AMTOR/PACKET Robot/Automatic Contest Station

        3.0  Things You Should Know
             3.1 Memory Requirements
             3.2 PC to TNC Communications 
             3.3 Open Loop
             3.4 Problems
             3.5 The Contents of the Status Window
             3.6 Logbooks

        4.0  Function Keys
             4.1  Capture to Disk Toggle
             4.2  Send Brag Tape
             4.3  Transmit Callsign Sequence
             4.4  Send/talk Brag Tape
             4.5  Show Packet MHlist and Point and Shoot Connect
             4.6  Auto CQ Call
             4.7  Activate Type Ahead Buffer/AMTOR Relink
             4.8  Disconnect/Receive
             4.9  Put TNC in CMD Mode
             4.10 Put TNC in CONVERSE /Transmit Mode /AMTOR FEC
             4.11 Alternate Function Keys
             4.12 Shift Function Keys
             4.13 Control Function Keys

        5.0  Main Menu
             5.1 Quick Menu
             5.2 Auto CQ
             5.3 Send Brag Tape
             5.4 Call Someone
             5.5 Log Menu
             5.6 Change Mode
             5.7 Call CQ
             5.8 Send/Talk File
             5.9 QRZ
             5.10 Send/Talk LAN-LINK files 001..010



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 3  


        6.0  BBS Menu
             6.1 Download Text Files

        7.0 Call Menu
             7.1  Alert Call/ARQ Call
             7.2  Connect/Call
             7.3  Enter Call
             7.4  reMember Path
             7.5  Packet Cluster
             7.6  Call CQ
             7.7  Retry
             7.8  Show Directory
             7.9  Target Call
             7.10 aUto CQ
             7.11 Toggle DX Flag
             7.12 Zap BBS
             
        8.0 Edit Menu
             8.1   Edit Brag Tape
             8.2   Edit Call Directory File
             8.3   Edit any other file
             8.4   Answer Ctdsk File (Split Screen)
             8.5   Answer Incoming Messages (Split Screen)
             8.6   Leave Note for Someone
             8.7   Edit Capture-to-Disk File
             8.8   Edit Two files (Split Screen)
             8.9   Edit LAN-LINK.SYS File
             8.10  Edit LAN-LINK.001 through LAN-LINK.010 files
             8.11  Pick Capture-to-disk to Edit
             8.12  Pick Message file to Edit

        9.0 Event/Clock Menu
             9.1  Set Alarm
             9.2  Connect
             9.3  Display Event
             9.4  Periodic Event
             9.5  Turn Robot ON/OFF
             9.6  Turn Contest Mode ON/OFF
             9.7  Time Display ON/OFF
             9.8  Cancel Event
             9.9  Zap BBS

        10.0 Files Menu
             10.1  Send Brag Tape
             10.2  File Directory
             10.3  Erase File
             10.4  Rename File
             10.5  Send File
             10.6  Send/Talk File
             10.7  Send Uppercase File
             10.8  View File
             10.9  View Runfile


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 4  


             10.10 View Incoming Messages

        11.0 Help Menu

        12.0 Jump to Dos

        13.0 LAN-LINK Menu
             13.1 :QBU: External Protocols
             13.2 :QBM: File
             13.3 :QSM: File
             13.4 :QSP: Message
             13.5 :QDB: File
             13.6 :QRU: Messages
             13.7 :QRA: Who is "ON-LINE"
             13.8 :QTA: Messages

        14.0 Log Menu
                  Log Mode Function Keys
                  14.0.1 Alt-A   Append Entry 
                  14.0.2 Alt-E   Edit Log Entry 
                  14.0.3 Alt-F   Find an Entry 
                  14.0.4 Alt-S   Scan Log by Call 
                  14.0.5 Alt-U   Toggle Delete Mark 
                  14.0.6 Alt-Z   Pack Log 
                  14.0.7 Ins     Toggle Insert Mode 
                  14.0.8 End     Show Last Page 
                  14.0.9 Home    Show First Page 
                  14.0.10 PgUp   Move Up One Page 
                  14.0.11 PgDn   Move Down One Page 
                  14.0.12 Up Arrow   Move Up One Entry
                  14.0.13 Down Arrow Move Down One Entry
             14.1 Append Entry
             14.2 Scan Log by Band
             14.3 Change Log
             14.4 Find Date
             14.5 Edit Log Entry
             14.6 Find an Entry
             14.7 Import-Convert Log
             14.8 Help Function Keys
             14.9 Scan Log by Mode
             14.10 Print Log
             14.11 Scan Log by Call
             14.12 Update from Old data
             14.13 Exit From Log Menu
             14.14 Fuzzy Scan

        15.0 Message Menu
             15.1 BBS Command Files
             15.2 Current Messages
             15.3 View Message
             15.4 Leave Note
             15.5 Old Messages


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 5  


             15.6 Time Tag

        16.0 TNC Menu
             16.1 Set TNC Date/Time
             16.2 Flush TNC Buffer
             16.3 Initialize TNC
             16.4 Show Calls Monitored List
             16.5 Show Connect Status
             16.6 Change CTEXT
             16.7 Acitivate TNC Mailbox
             16.8 Deactivate TNC Mailbox

        17.0 AMSAT-OSCAR Menu
             17.1 UoSAT ASCII Beacon
             17.2 Phase 3 RTTY Beacon
             17.3 SAREX Menu
                  17.3 1 Attack Mode ON/OFF
                  17.3.2 Change SAREX Call
                  17.3.3 SAREX Packets Capture to Disk ON/OFF
             17.4 SAREX Orbiter Features 

        18.0 Parameter Menu
             18.1  Turn Beacon Mode ON/OFF
             18.2  Clear Connect Count         
             18.3  Turn Digipeat Detect ON/OFF
             18.4  Turn Beacon Control ON/OFF
             18.5  Turn Command Echo ON/OFF       
             18.6  Change Keyboard Beep Count  
             18.7  Set Message Count           
             18.8  Turn NODE Drop Link ON/OFF     
             18.9  Turn Printer ON/OFF             
             18.10 Turn QTC Snatch ON/OFF         
             18.11 Turn :QSP: Relay Flag ON/OFF  
             18.12 Turn Sound ON/OFF             
             18.13 Turn Contest Mode ON/OFF
             18.14 Turn DCD Flag ON/OFF          
             18.15 Turn BBS Snatch ON/OFF        
             18.16 Turn Time Id. ON/OFF         
             18.17 Turn Automatic Capture-to-Disk Flag ON/OFF         
             18.18 Change BBS Parameters      
                  18.18.1 Local BBS Callsign
                  18.18.2 Mail-Snatch Trigger Word
                  18.18.3 Read Request Command
             18.19 Change Callsigns           
                  18.19.1 Callsign
                  18.19.2 The SELCAL
                  18.19.3 The PacketCluster Call
             18.20 Change Directories         
                  18.20.1 QBM Download Directory
             18.21 Enter Common Calls         
             18.22 Change File Names          
                  18.22.1 VHF Logbook File (VHF.DBF)


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 6  


                  18.22.2 HF Logbook File (HF.DBF)
                  18.22.3 Path Directory File (LAN-LINK.DIR)
                  18.22.4 Brag Tape (LAN-LINK.TXT)
                  18.22.5 QBU Upload File Name (QBU-TX.BAT)
                  18.22.6 QBU Download File Name (QBU-RX.BAT)
             18.23 Change LAN-LINK Parameters 
                  18.23.1 Change CQ Text
                  18.23.2 Set the Default Band
                  18.23.3 Set the Default Transmitter Power
                  18.23.4 Set CQ Delay Time Seconds
                  18.23.5 Set CQ Delay Time Minutes
                  18.23.6 Set Number of Lines in a Non Contest CQ Call
                  18.23.7 Set Shut Down Mode (QRT Flag)
                       18.23.7.1 QRT 
                       18.23.7.2 QRV
                       18.23.7.3 QRV + CTEXT TOGGLE
                       18.23.7.4 BBS
                       18.23.7.5 SOLO
                       18.23.7.6 BBS+SOLO
                  18.23.8 Set Default Users
             18.24 Change PC Communications Parameters
                  18.24.1 The Communications Port
                  18.24.2 The Terminal Baud Rate
                  18.24.3 TNC Data Bits
                  18.24.4 TNC Parity
                  18.24.5 Number of TNC Stop Bits
             18.25 Change Colors
                  18.25.1   OutWindow Color
                  18.25.2   StatusWindow Color
                  18.25.3   PromptWindow Color
                  18.25.4   LogWindow Color
                  18.25.5   InWindow Color
                  18.25.6   ScrollBackWindow color
                  18.25.7   MHWindow Color
                  18.25.8   Alarmwindow Color
                  18.25.9   BottomWindow Color
                  18.25.10  Emphasis Color
                  18.25.11  Prompt Color
                  18.25.12  Option Color
                  18.25.13  Connected Text Color
                  18.25.14  Computer Color
                  18.25.15  VHF Header Color
                  18.25.16  HF Header Color
                  18.25.17  Alert Call Color
                  18.25.18  Outgoing Text Color
                  18.25.19  Multi I/O Stream Color[1]
                  18.25.20  Multi I/O Stream Color[2]
                  18.25.21  Multi I/O Stream Color[3]
                  18.25.22  Multi I/O Stream Color[4]
                  18.25.23  Multi I/O Stream Color[5]
                  18.25.24  Multi I/O Stream Color[6]
                  18.25.25  Multi I/O Stream Color[7]


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 7  


                  18.25.26  Multi I/O Stream Color[8]
                  18.25.27  Multi I/O Stream Color[9]
                  18.25.28  Multi I/O Stream Color[10]
             18.26 Change SAREX Parameters    
                  18.26.1 SAREX CallSign
                  18.26.2 Change SAREX Capture to Disk File
             18.27 Update LAN-LINK.SYS        
             18.28 Verify Changes             
             18.29 Change Scan Words          
             18.30 Turn Misc. Flag ON/OFF
                  18.30.1 All Modes:- Debug or state-sequence numbers
                  18.30.2 BAUDOT Mode:- Navy MARS Protocol Verify
             18.31 Change Band/Mode
             18.32 Zap BBS on Next Mail Beacon
             18.33 BBS Zap, Don't Disconnect After Sequence

        19.0 Q Codes [NC/L]

        20.0 Communications Modes
             20.1 VHF PACKET
             20.2 HF PACKET
             20.3 ASCII (RTTY)
             20.4 BAUDOT (RTTY)
             20.5 MORSE (CW)
             20.6 AMTOR (STANDBY RECEIVE)
             20.7 AMTOR (ALIST [CHIRPCOPY])
             20.8 SIGNAL
             20.9 NAVTEX

        21.0 Terminal Mode Menu
             21.1 Packet Terminal Menu
                  21.1.1 Change Packet Baud Rate
                  21.1.2 CQ/Beacons
                  21.1.3 Everything
                  21.1.4 Read the Mail
                  21.1.5 Just My Station (Solo)
                  21.1.6 All Traffic
                  21.1.7 Single User Connects
                  21.1.8 Multiple User Connects
                  21.1.9 Conference
                  21.1.10 Conference Bridge On/Off
             21.2 AMTOR Terminal Menu
                  21.2.1 Force Break [ACHG]
                  21.2.2 Start Mode B [FEC]
                  21.2.3 Force LETTERS case
                  21.2.4 Read the Mail [ALISTEN]
                  21.2.5 Override ROBOT/Mailbox
                  21.2.6 Standby Receive [ARQ]
                  21.2.7 Set ROBOT/Mailbox
                  21.2.8 CW Identification
                  21.2.9 Set ROBOT infinite Delay



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 8  


             21.3 Baudot Terminal Menu
                  21.3.1 Set Baud Rate
                  21.3.2 Select Shift
                  21.3.3 NAVY MARS Message Protocol
                  21.3.4 USOS On/Off
                  21.3.5 SELCAL set/reset
                  21.3.6 CW Identification
             21.4 ASCII Terminal Menu
                  21.4.1 Set Baud Rate
                  21.4.2 Select Shift
                  21.4.3 SELCAL On/Off
                  21.4.4 CW Identification
             21.5 CW Terminal Menu
                  21.5.1 Lock to Receive Signal
                  21.5.2 Set Morse Speed
                  21.5.3 Unlock Morse Speed

        22.0  eXit to DOS

        23.0 Hot Key Combinations
             23.1  Alt-A - Alert Call (Packet)/ARQ Call/Talk (AMTOR)
             23.2  Alt-B - Send Break/AMTOR Changeover
             23.3  Alt-C - Call/Connect to
             23.4  Alt-D - Disconnect or Receive
             23.5  Alt-E - Enter Call
             23.6  Alt-F - Flush TNC Buffer
             23.7  Alt-J - Jump to DOS Shell
             23.8  Alt-K - Jump to DOS Shell with Quick Return
             23.9  Alt-L - Edit Log
             23.10 Alt-M - Message Scan
             23.11 Alt-N - Multi Connect Stream Next
             23.12 Alt-O - Turn Robot On
             23.13 Alt-P - Turn Printer ON/OFF
             23.14 Alt-Q - Call QRZ
             23.15 Alt-R - Retry Call/Connect
             23.16 Alt-S - Scan Log
             23.17 Alt-X - Exit to DOS
             23.18 Alt-Y - Zap Packet Cluster
             23.19 Alt-Z - Zap BBS
             23.20 Alt-= - Toggle Miscellaneous Flag
             23.21 End   - > +?  [Over]
             23.22 PgUp  - Scrollback (Scrolls back incoming text)
             23.23 The HOME Key
             23.24 The DOWN ARROW Key
             23.25 Shift/Baudrate Control keys
             23.26 Control-Z (Ctrl-Z  or ^Z)

        24.0  LAN-LINK Disk files
             24.1  LAN-LINK.EXE
             24.2  LAN-LINK.SYS
             24.3  *.RUN (YYMMDD.RUN)
             24.4  *.DBF (VHF.DBF and HF.DBF)


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 9  


             24.5  LAN-LINK.DIR
             24.6  CONFIG.SYS
             24.7  *.MBX
             24.8  *.BBS
             24.9  LAN-LINK.001 .. LAN-LINK.010
             24.10 QBU-RX.BAT
             24.11 QBU-TX.BAT
             24.12 LAN-LINK.QTA

        25.0 Mailbox features
             25.1 Answering Machine
             25.2 Mail Beacon (Annunciator)
             25.3 How to leave a message
             25.4 Remote Beacon shutdown

        APPENDIX 1. Anomalies and Bugs
             A1.1  Command/Converse Mode anomalies
             A1.2  Buffer messages in AMTOR Beacon CQ Mode
             A1.3  FEC +? responses in AMTOR Beacon CQ Mode
             A1.4  Using a CGA card with a monochrome monitor
             A1.5  The Packet Conference Mode
             A1.6  Packet Conference Mode disconnects
             A1.7  Strange Events
             A1.8  *** DISCONNECTED
             A1.9  *** CONNECTED
             A1.10 Greek Characters on Incoming Screen
             A1.11 Dumb TNC
             A1.12 Intermittent Lockup

        APPENDIX 2. Local Area Network Capability
             A2.1 LAN Protocol (G3ZCZ Version)
             A2.2 Message Format
             A2.3 File Uploading/Downloading
             A2.4 Path Determination to a DX Station

        APPENDIX 3. NC/L Dictionary
             A3.1  :QBM: File Download
             A3.2  :QDB: File Upload
             A3.3  :QMH: Monitor Heard List
             A3.4  :QSM: Send Repeat of Message
             A3.5  :QSP: Send Message
             A3.6  :QRA: Who is About?
             A3.7  :QRT: Shut Up
             A3.8  :QRU: Upload Messages in Batch
             A3.9  :QNO: Negative Response
             A3.10 :QJG: Task Completed Response
             A3.11 :QRV: Ready Response
             A3.12 :QSL: Confirmation Response
             A3.13 :QTA: Messages
             A3.14 :QTC: List of Messages
             A3.15 :QYU: YAPP Binary File Transfer Upload
             A3.16 :QYD: YAPP Binary File Transfer Download


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 10  



        APPENDIX 4. USING OTHER TNCs
             A4.1 TNC2 (MFJ 1270) Version 1.1.2
                  A4.1.1 Default Commands
                  A4.1.2 Program differences
             A4.2 TNC1 (HD-4040)
                  A4.2.1 Default Commands
                  A4.2.2 Program differences
             A4.3 Kaypro KPC-2
                  A4.3.1 Default Commands
                  A4.3.2 Program differences
             A4.4 KAM 
                  A4.4.1 Default Commands
                  A4.4.2 Program differences
             A4.5 PK-232 EPROM Versions JUN 1987 and later 
             A4.6 MFJ1278 EPROM Version 3.3
                  A4.6.1 Default Commands
                  A4.6.2 Program differences
             A4.7 Heath HK-21

        APPENDIX 5. UPDATES/REVISION HISTORY

        APPENDIX 6. Registration Form

        APPENDIX 7. Problem Reporting Form

        APPENDIX 8. Other PC Software by Joe Kasser G3ZCZ

        APPENDIX 9. How Shareware Works


                                ACKNOWLEDGMENTS

        Thanks to Milt, 4X1AA.  If it wasn't for Milt, Version 1.00 would 
        never have been written.  

        Thanks  to  Jim, WB8QJL, who loaned me his  MFJ1278  for  several 
        months but died in a plane accident before he got to use LAN-LINK 
        on his MFJ1278.















        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 11  


        1.0  INTRODUCTION

        LAN-LINK  is a Personal Digital Communications  Terminal  Program 
        for a Packet Radio TNC.  The program is designed to optimize  the 
        configuration  of  the  TNC in each communications  mode  and  to 
        provide some smart terminal features.  It takes advantage of  the 
        extra   features  of  the  PK-232  which  is  made  by   Advanced 
        Electronics  Applications Inc. It is designed to allow anyone  to 
        use and get the most out of their packet TNC as well as from  the 
        PK-232,  the MFJ1278 and the KAM for Morse, ASCII, BAUDOT,  AMTOR 
        as well as Packet Radio communications without having to keep the 
        manual handy.   

        LAN-LINK  is  a  sophisticated program.  In its  basic  state  it 
        allows  you to use the TNC in an optimal manner.   It  configures 
        the  TNC  (it  types  the  commands)  for  you  to  maximize  the 
        communications  efficiency  in the communications  mode  of  your 
        choice.   That means, for example, when working Packet on HF  you 
        need  to program the TNC parameters to different values than  you 
        would  use  on  VHF  to  make  maximum  use  of  the  mode.   One 
        significant  difference is the length of the packet  itself,  for 
        the  longer it is, the greater the probability of QRM  destroying 
        it. This program will adjust the packet parameters for you.

        Since  the  computer is now involved, other  features  have  been 
        added  to  simplify  operation, and several  features  have  been 
        automated.   All these operations are performed using  menus  and 
        function keys as documented below.  It will take a while to learn 
        how  to  use this program in a manner that suits you,  read  this 
        document and have fun, after all, isn't that one of the  purposes 
        of Amateur Radio.

        This manual is organized by menu.  It describes the operation  of 
        each  menu option and function key in each  Communications  Mode.  
        It is not organized in a how to do something manner.

        Any  Terminal  Node  Controller  (TNC)  is  a  complex  piece  of 
        equipment.   It can operate in a Command Mode, in which you  tell 
        it to do something, or in a Converse Mode in which you are  using 
        it  to talk to other stations.  Many people confuse the two  when 
        first  getting on Packet.  If you monitor the channels  you  will 
        recognize Command Mode TNC instructions on the air, and when  you 
        use  the  TNC you will receive the "error" reply  when  you  type 
        something  thinking  that you are in the Converse  Mode  but  are 
        really in the Command Mode.  LAN-LINK is designed to make  Packet 
        operation simple using Menus and high level (Function and Hot key 
        combinations) commands.

        Morse,  ASCII, BAUDOT communications modes are HALF DUPLEX.   One 
        station  is transmitting at any time.  You thus have to  use  the 
        Transmit/Converse  and Receive/Disconnect function keys  to  turn 
        the transmitter on and off respectively. 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 12  



        AMTOR is also HALF DUPLEX but has some of the attributes of  full 
        duplex.   In  this  Mode  you  control  who  is  talking  through 
        software,  only one station can send data at a time, but you  can 
        type  characters  in to the buffer and they will  be  transmitted 
        automatically  when the other station turns the QSO over to  you.  
        Once   you  have  linked  with  someone,  you  do  not  use   the 
        Receive/Disconnect function UNTIL THE QSO IS OVER.  Both stations 
        are  communicating automatically thanks to the TNC.  If you  want 
        the  other operator to respond type the +? key sequence  (or  use 
        the 'End' Key).  

        Packet  Radio communications  on the other hand is a full  duplex 
        mode  of communications.  Once you have connected  with  someone, 
        you  do not use the Receive/Disconnect function UNTIL THE QSO  IS 
        OVER.   Both stations are communicating automatically  thanks  to 
        the  TNC.  If you want the other operator to respond type  the  > 
        key followed by the 'Enter' Key, better yet, use the 'End' Key.  

        Note  that  Morse,  AMTOR, ASCII and BAUDOT  are  character  mode 
        communications  in  that each character you type is sent  as  you 
        type them.  In Packet Communications, the TNC stores them up  and 
        sends out a burst or packet when you type the 'Enter' Key or  you 
        type  enough characters to fill up a packet.  Studies have  shown 
        that the human attention span when sitting at the keyboard is  of 
        the  order  of 2 seconds. If you are in a  keyboard  to  keyboard 
        packet  radio connect, remember this and don't forget to use  the  
        'Enter' Key frequently, especially before you stop to think about 
        what to send next.

        Note   that   AMTOR  and  PACKET  are  full   duplex   modes   of 
        communications.  When you connect with someone, there is no  need 
        to use the transmit and receive function keys.  In fact you  will 
        have  problems  if you do.  Do not disconnect or break  the  link 
        until the QSO is over.

            1.1  PROGRAM HIGHLIGHTS

            Function key and Menu driven.

            Automatic logbook entries for Packet and Mailbox/Beacon  Mode 
            AMTOR  Connects,  semiautomatic  logbook  entries  for  other 
            modes.  

            Logbook file is dBASE compatible and can be processed by  the     
            LOGBOOK  Package  of PC-HAM by G3ZCZ  for  indexed  listings,     
            tracking of DXCC and other AWARDS, etc.

            Contest  operation, sends standard message and  automatically 
            increments QSO count.

            Automatic  optimized configuration of the TNC for  each  com-


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 13  


            munications mode.

            All mode Function key  'OVER' feature (End).

            There  are  10 files with fixed names  (LAN-LINK.001  through 
            LAN-LINK.010) which may be viewed and transmitted by means of 
            function keys.  They may also be edited from the Edit Menu.

            Set up of TNC for AMSAT-OSCAR Telemetry reception.

            Time display and event scheduler.

            ASCII Text Editor.

            Customizable Colors.

            Access  to the TNC Command Mode is provided in case the  user 
            wishes to override any defaults.

            1.1.1     PACKET RADIO

            Automatic  capture  to  disk of all  packet  radio  connects. 
            Automatic indication of the number of Packet connects.  

            Local   Area   Network  (LAN)  message  store   and   forward 
            capability.   

            Capable of automatic connect attempts to download a QTC  from 
            another station in the LAN.  

            Capable  of  automatic connect attempts to a  packet  BBS  to 
            download  your incoming messages, when your callsign  appears 
            on the BBS mail beacon annunciator.

            Capable  of  automatically requesting Bulletins  on  subjects 
            that interest you from your local packet BBS.

            Digipeat monitoring and capture. 

            Alert signal to let you know when a predetermined call  shows 
            up in a packet header on frequency.  

            Conference Mode in multiconnect situations. 

            Bridge Mode in multiconnect situations.

            Path determination to DX station via :QMH:. 

            Indicator that a specific station designated as the  'target' 
            call   connected   in  Packet  Mode,  or  linked   to   AMTOR 
            Beacon/Mailbox while you were away.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 14  


            Automatic  NET/ROM and KA Node path set up from  LAN-LINK.DIR 
            call/path directory file.

            Selective  answering machine and MAILBOX using  NC/L  command 
            dialogue.

            Screen  indication  of  connect by  desired  station  (target 
            call).

            Automatic Beacon Mode CQ caller  

            Automatic contest (DX-pedition) mode

            Will  call  CQ repetitively and either work the  connect  and 
            keep  going  after disconnect or signal you when a  reply  is 
            received.

            SAREX special features

            :QRA: trigger to determine who else is on channel

            Single keystroke Packet Cluster connect

            1.1.2     AMTOR

            Automatic SELCAL determination.

            Automatic  CQ caller.  Will call CQ repetitively  and  signal 
            you when a reply is received. 
            
            Local   Area   Network  (LAN)  message  store   and   forward 
            capability.   

            Selective  answering machine and MAILBOX using  NC/L  command 
            dialogue.

            Function  key  change from monitoring FEC CQ's  to  QSO's  in 
            progress (chirpcopy).

            Automatic Beacon Mode CQ caller

            Automatic contest (DX-pedition) mode

            Color changes between incoming and outgoing (echoed as  sent) 
            text.

            1.1.3     MORSE/BAUDOT/ASCII

            Automatic  CQ caller.  Will call CQ repetitively  and  signal 
            you when a reply is received. 
            
            RTTY SELCAL


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 15  



            NAVY MARS RTTY file transmitting protocols for the PK-232.

        2.0  Getting Started

        MAKE  A  BACK UP COPY OF THIS DISK, BEFORE YOU REMOVE  THE  WRITE 
        PROTECT TAB.      

        If  you don't have a PK-232 then rename the LAN-LINK.SYS file  to 
        PK232.SYS  and  rename your TNC.SYS file  as  LAN-LINK.SYS.   For 
        example,  if  you  are  using  a  TNC2,  perform  the   following 
        operations in DOS.

                          RENAME LAN-LINK.SYS PK232.SYS
                          RENAME TNC2.SYS LAN-LINK.SYS   

        For details of the rest of the customization possibilities in the 
        'LAN-LINK.SYS' file, read Section 23.2.  YOU WILL NOT BE ABLE  to 
        change  the TNC Type from within LAN-LINK.  YOU MUST  rename  the 
        SYS files BEFORE you begin the customization sequence.

             2.1 Bringing LAN-LINK Up the First Time.

             2.1.1    Turn on the TNC.

             2.1.2   If  the date and time in the PC are not set  to  UTC 
                     (GMT),  set  them  using  the  DOS  date  and   time 
                     commands.

             2.1.3   Load the program by typing LAN-LINK in the way  that 
                     you normally load a program.

             2.1.4   WAIT until the program says that it has  initialized 
                     the  TNC and shows the band and power in the  status 
                     window at the top of the screen.

             2.1.5   If  there is no battery in your TNC do what the  TNC 
                     manual  tells you to do to synchronize the  TERMINAL 
                     baud rate to 1200 baud.  In the case of the  PK-232, 
                     LAN-LINK will send the PK-232 three * characters  to 
                     set the PK-232 to 1200 baud.

             2.1.6   After  LAN-LINK has loaded, use the Parameters  Menu 
                     option  "2" to replace G8BTB with your callsign  and 
                     Selcal  information.  If your TNC does  not  support 
                     AMTOR  you  still need a dummy entry  in  that  line 
                     (which  is  taken care of automatically).   You  may 
                     also  change the colors at this time.  Use  the  "U" 
                     option to save the updated file.  After reading  the 
                     rest  of this manual, you may want to  change  other 
                     defaults to set up LAN-LINK the way you like it.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 16  


             2.1.8   Use  the  "N"  and "I" options in the  TNC  Menu  to 
                     configure the TNC.  Then select the desired mode  of 
                     operation  from the displayed menu by  pressing  the 
                     appropriate key. 

             2.1.9   Exit from LAN-LINK by using the Alt-X Key or the Esc 
                     Key followed by the X Key.

             2.1.10  Reload  LAN-LINK the same way you did before.   This 
                     will load the edited LAN-LINK.SYS file with the  new 
                     settings.   You are now ready to use  LAN-LINK.   If 
                     this  is  your first time, try the Quick  Menu  (See 
                     Sections 2.2 and 5.1).

             NOTE:  If you have batteries in the TNC, make sure that  the 
             TNC is set for a terminal baud rate of 1200, and try to  run 
             the  program.   If you see Greek characters  or  it  doesn't 
             work, remove the batteries and try again (Refer to  Appendix 
             1.10).  You can then replace the batteries and from then  on 
             the program will be correct. Make sure you leave the TNC on   
             when  you replace the batteries or your initialization  will 
             revert to the TNC default settings - the batteries are there 
             to power the TNC RAM while your primary power is off.

             2.2 Using the Quick Menu

             The  Quick Menu is designed for new users and  provides  the 
             most commonly used functions in a single Menu. You bring  up  
             the Quick Menu be touching the Escape key to access the Main 
             Menu and then selecting the 'A' option.

             The Quick Menu is described in Section 5.1.
             
             2.3 Connecting to other stations

             LAN-LINK  treats  incoming connects  and  outgoing  connects 
             differently.  To connect to another station, Use  the  Alt-C 
             hot  key, Function key 5, or bring up the Quick  Menu  using 
             the 'Esc A' character sequence as described in Section  5.1, 
             or  by bringing up the Call Menu via the 'Esc  C'  character 
             sequence  as described in Section 7.  DO NOT TYPE  'C  Call-
             sign'  in  the command mode.  If you do,  the  connect  will 
             still  take  place (the TNC won't know if  you  or  LAN-LINK 
             issued the command) but LAN-LINK will treat it as an  incom-
             ing connect and issue the "[ZCZ] LAN-LINK 1.58>" handshaking 
             signal  (if the LAN-LINK flag is in its default, or  enabled 
             state) as described in Section 18.  If you connect to a  BBS 
             or a Node this way, you will get an error message back  from 
             the  BBS  or node, since it does  not  recognize  LAN-LINK's 
             handshake.

             When  you  use the menu, Alt-C or F5 approach you  can  also 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 17  


             make  use of the 'path memory' feature in  the  LAN-LINK.DIR 
             file.

             2.4 Upgrading from YAPP

             A  YAPP.CNF file is provided to facilitate  conversion  from 
             YAPP to LAN-LINK. YAPP.CNF is a configuration file for  YAPP 
             Version  2 that will configure the PK-232 for YAPP and  then 
             back to LAN-LINK.

             If you are currently using YAPP, replace your YAPP.CNF  file 
             with this one and load YAPP.  Then terminate the program  in 
             the  normal manner by using the Alt-X Key.  You should  then 
             be able to load and run LAN-LINK without any problems.  Each 
             time you subsequently want to run YAPP, YAPP will set up the 
             PK-232,  execute  and then reconfigure the PK-232  back  for   
             LAN-LINK.

             If you are using a YAPP.DIR file, rename it to LAN-LINK.DIR.

             2.5 Using Different TNCs

             There  are differences  between the  command  dialogue and the 
             features  offered by the PK-232, KAM and MFJ1278.   LAN-LINK 
             makes  use of many of them.  For example, as the  KAM  shows 
             the  HF  and VHF packets as if they ware  separate  streams, 
             LAN-LINK detects them and displays the different headers  in 
             different  colors.   As this feature is not present  in  the 
             PK-232,  LAN-LINK does not offer it.  From time to time,  as 
             each  manufacturer updates the firmware (EPROM) in the  TNC, 
             LAN-LINK may be updated and incorporate them.

             LAN-LINK  is normally loaded by typing LAN-LINK followed  by 
             the  'Enter'  key.   In  this  instant,  LAN-LINK  gets  its 
             configuration information from the LAN-LINK.SYS file.   LAN-
             LINK.SYS  is the default SYSTEM or configuration  file.   If 
             you have more than one TNC you may want to set up  different 
             configuration files for each TNC.  

             You must set up your different configuration files with  the 
             filetype ".SYS", examples being TNC1.SYS, TNC2.SYS, KAM.SYS, 
             PK232.SYS  as  well as the default LAN-LINK.SYS.   Edit  the 
             sample  files on the distribution disk to customize them  to 
             your requirements.

             To load LAN-LINK with the optional configuration file,  type 
             'LAN-LINK'  followed  by the name of the file  (without  the 
             filetype)  on the command line then press the  'Enter'  Key.  
             For   example,  if  you  have  a  PK-232  and  a  TNC2   and 
             occasionally use the TNC2, set up the LAN-LINK.SYS file  for 
             the  PK-232.   Then  type  'LAN-LINK'  to  run  the  program 
             normally.   On the rare occasions when you want to  use  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 18  


             TNC2, you may type 'LAN-LINK TNC2' to run LAN-LINK with  the 
             TNC2.SYS configuration file.  

             2.6 Using Different HF and VHF Configuration Files

             You  can  also  use two SYS files, one for HF  and  one  for 
             VHF/UHF.  If you name them HF.SYS and VHF.SYS you can  bring 
             the relevant one up by typing 

                          'LAN-LINK VHF' or  'LAN-LINK UHF'

             as desired.  You can also use a different one for a contest, 
             or for any reason you wish.

             2.7 Using the AMTOR/PACKET Robot/Automatic Contest Station

             In  order  to use the Robot in the AMTOR Mode, you  need  to 
             have  a  Brag Tape file. The default name for this  file  is 
             LAN-LINK.TXT.  If this file does not exist, you will not  be 
             able to activate the Robot.

             You   activate  the  Robot  by  using  the  Alt-O  hot   key 
             combination.  The  Robot will then call CQ and  wait  for  a 
             reply.   If  no reply is received, it will call  again.   It 
             will  continue to call at preset intervals until a reply  is 
             received  (you  may change the interval via  the  Parameters 
             Menu).  In AMTOR, the Brag Tape will be transmitted and  one 
             (and  one  only)  transmission  accepted  from  the  linking 
             station,  unless the linking station uses a NC/L command  on 
             the  same  line  as the +?.  In that case,  the  Robot  will 
             respond  to it.  All incoming text will be captured to  disk 
             in the Capture-to-disk file (LAN-LINK.RUN).  The Robot  will 
             then  sign off and drop the link.  If it has not managed  to 
             recognize a valid call from the linking station it will  ask 
             for a retransmission of the callsign.

             In  the Packet Communications Mode, the CTEXT will  ONLY  be 
             transmitted  if you have set CMSG to ON (in the TNC  Command 
             Mode),  the Brag Tape will not be transmitted. NC/L will  be 
             active.  When the connecting station disconnects, the  Robot 
             will restart the CQ cycle.

             In AMTOR turn the answerback off if the Robot is on. In this 
             way  other  stations  will  not  be  able  to  mess  up  the 
             sequencer.

             When  you touch the F8, F3, Alt-D, Alt-Q or 'End' keys,  you 
             turn the Robot off.

             The  PK-232's  flush command is used before  each  robot  CQ 
             message is transmitted to synchronize the text to the  Robot 
             software.  The KAM however, does not have a way to flush its 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 19  


             internal  transmit buffer.  Under QRM conditions or if  sta-
             tions do not sign on correctly, the sequence can get out  of 
             order due to the wrong text being transmitted.  

             To  use the Automatic Contest mode, enable the contest  mode 
             from  the Parameter menu, then activate the Robot using  the 
             Alt-O function key.  To turn the Automatic Contest Mode off, 
             deselect  (turn  off) the contest mode  from  the  Parameter 
             Menu.

        3.0  Things You Should Know 

             3.1 Memory Requirements

             LAN-LINK  1.58 requires a minimum of 450k of RAM.  You  will      
             need  more  RAM if you wish to use the Editor.   The  Editor      
             files  will each take a maximum of 64K additional  RAM.   If      
             your  memory is marginal, you may get an error when you  try      
             to log a station or edit a file/message.

             3.2 PC to TNC Communications 

             All communications between the computer and the TNC normally 
             use  the 8 BIT NO PARITY and 1 stop bit RS-232  Serial  Port 
             configuration. You CAN THUS SEND FOREIGN LANGUAGE CHARACTERS 
             FROM THE KEYBOARD OR FILES.  If you want to limit the  char-
             acter  set  to the 7 bit ASCII set, set the  TNC  parameters 
             accordingly.   The baud rate defaults to 1200, but  you  may 
             set it to 2400, 4800 9600 or even 19200 if your CPU clock is 
             fast enough and the TNC will respond correctly.  

             3.3 Open Loop

             IF YOU USE THIS PROGRAM, YOU STILL MUST READ THE TNC MANUAL.

             WARNING  ....  THIS PROGRAM OPERATES IN AN OPEN  LOOP  MODE.  
             IT REMEMBERS WHAT INSTRUCTIONS OR COMMANDS IT GAVE THE  TNC.  
             IF  FOR  SOME  REASON, THE TNC IS NOT  SYNCHRONIZED  TO  THE 
             PROGRAM YOU WILL NOT GET CORRECT DISPLAYS ON THE SCREEN.

             3.4 Problems

             In case you have problems, always check the default settings 
             using  the 'Verify Changes' option of the  Parameters  Menu.  
             Further  information is contained in Appendix  1.   Problems 
             can  be caused by incorrect settings of the TNC  parameters. 
             If all else fails, (hard) reset the TNC. Make sure XFLOW and 
             FLOW are OFF.  

             3.5 The Contents of the Status Window

             The indicators in the status line depend on the state of the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 20  


             LAN  Link and are described in the sections that  deal  with 
             the functions they area associated with.  This section is  a 
             summary of the displays in the Status Window.

             Some typical status window displays are shown below.

                  2  Meters 2 Watts      PACKET 1200 W [R] TRFC ->N4QQ
                  20 Meters 100 Watts    MORSE TEST[4]
                  20 Meters 100 Watts    PACKET 300 N TRFC
                  CAPTURE TO DISK        PACKET 300 N [C1][Z] TRFC ->N4QQ

             If the automatic Capture-to-disk is turned off, a yellow bug 
             will be flashing on the left side of the line.

             If the Printer Flag is set, a yellow [P] will be flashing on 
             the left side of the line.

             If  the miscellaneous flag is set, an asterisk '*'  followed 
             by  two  numbers  and a ']' will be  displayed.   The  first 
             number is the BBS Sequence State, the second is the  Connect 
             Sequence State.  These numbers reflect the internal state of 
             LAN-LINK and should be quoted when describing problems.

             If  a message transfer is taking place, the callsign of  the 
             station involved will be displayed.

             When  the Capture-to-Disk is turned on, a 'CAPTURE TO  DISK' 
             will  be  shown,  if it is turned off,  the  operating  band 
             (Meters) and power (Watts) will be shown.  If a ZapBBS is in 
             operation, the Bulletin Request Count will then be shown  in 
             square brackets ('[]').

             The communications mode will be shown next, it may be one of 
             the following;

                  PACKET    AMTOR     AMTOR-(MAIL)   AMTOR-FEC
                  BAUDOT    ASCII     MORSE          NAVTEX
                  SIGNAL    ????      DEFAULT {boot up}

             A flashing yellow musical note following the  Communications 
             Mode indicates that the sound has been inhibited.

             The  next  number to be displayed is the  RF  communications 
             baudrate.   The  letter 'W' or 'N' indicates that  the  Wide 
             shift or the Narrow shift has been selected.  A 'down arrow' 
             will  be shown if the shift is normal. If the shift  is  re-
             versed a flashing yellow 'up arrow' will be displayed.

             In   the   BAUDOT  mode,  'USOS'  will   be   displayed   if 
             'Unshift-on-space' is selected.

             If  the Contest Mode is selected, the word 'TEST' will  then 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 21  


             be displayed followed by the Contest QSO number in '[]'.

             In certain Robot and AutoCQ states, namely while the comput-
             er  is waiting for a reply, a flashing cumulative  CQ  count 
             will be displayed next.

             If  the  RTTY  SELCAL is active the word  'SELCAL'  will  be 
             displayed next.

             If  the Navy MARS BAUDOT RTTY protocol is enabled,  a  '[n]' 
             will be displayed.

             In the packet and AMTOR Robot modes, if at least one station 
             has  connected  or linked, a flashing yellow '[C]'  will  be 
             displayed next.  The number in the square brackets with  the 
             'C'  is the number of stations that  have  connected/linked.  
             If the target call station was one of those station, a happy 
             face will also be displayed in the square brackets.

             If at least one QTC snatch has taken place a flashing yellow 
             '[Q]'  will  be displayed next.  The number  in  the  square 
             brackets  is  the  number of QTC Snatches  that  have  taken 
             place.
             
             In the packet communications mode, if a ZapBBS, a QTC Snatch 
             or a PacketClusterZap is in progress a flashing yellow '[Z]' 
             will be displayed next.  However, if LAN-LINK is set to stay 
             connected  when  the sequence ends, the  flashing  indicator 
             will be a {Z} instead of a [Z].

             In the packet or AMTOR communications mode, a '[R]' will  be 
             displayed  next  if LAN-LINK is configured  for  'store  and 
             forward' (:QSP:).

             In the packet and AMTOR communications modes, if the  beacon 
             mode is enabled a '[B]' will be displayed next.  if  someone 
             has  connected and sent a :QRT: sequence, the '[B]' will  be 
             flashing.   The '[B]' will be followed by a '[M]'  if  there 
             are  messages  pending.  The number in the  square  brackets 
             with  the  '[M]'  is the number of  messages  (*.OUT  files) 
             pending.

             In  the  packet communications mode, if the  SAREX  mode  is 
             enabled,  a  '[S]' will be shown next.  The  '[S]'  will  be 
             flashing  while  capture to disk is in progress.   If  SAREX 
             packets  have been copied a happy face will be displayed  in 
             the square brackets together with the 'S'. 

             In  the packet communications mode, if the  digipeat  Detect 
             mode is enabled a '[D]' will be displayed next.

             In  the packet communications mode, the  terminal  sub-modes 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 22  


             (see Section 21) are then displayed as follows;

             SOLO      This lets you only see messages addressed to you.
             CQ/B      This lets you see beacons and CQ calls as well.
             TRFC      This  lets you see packets containing messages  as 
                       well.
             EVRY      This lets you see everything on channel, including 
                       the link control packets.
             MAIL      This  lets  you monitor packets  from  a  specific 
                       station.   In the PK-232,  you can do  it  without 
                       displaying the headers.

             The  next  item  to be displayed is a  callsign,  under  the 
             following  conditions;   the call of the  station  connected 
             with,  will be prefixed by a '*>' when connected, and  by  a 
             '->' when a connect request is in progress.  if a disconnect 
             is  in progress, the callsign will be replaced by a  '$$$$'.  
             The  callsign will be seen as flashing when a connect is  in 
             progress.

             In  the MAIL mode, the callsign of the station that you  are 
             "reading the mail" on will be displayed, otherwise the  call 
             sign displayed will be that of the one you are connected to.

             If  an  Alert Call has been entered, it  will  be  displayed 
             next,  similarly  for a target call.   The display  will  be 
             slightly different of the calls have been heard/worked.

             The  next  items to be displayed are the packet  multi  user 
             mode  displays.  If the conference bridge is up, a  flashing 
             yellow bridge will be shown.  If only the conference mode is      
             set,   the  word 'C will be flashing, if the   basic   multi      
             user  mode is set, the word 'M will be seen.  The   callsign 
             will  be  prefixed by the I/O  channel  number/letter,   and      
             will  be  in  the color allocated to  the  traffic  on  that  
             channel.  The number shown after the flashing letter is  the 
             number  of  streams  that  LAN-LINK  thinks  that  you   are 
             connected on.

             In the non packet modes, the callsign displayed will be that 
             of the station being worked (entered by the AMTOR robot, the 
             automatic CQ call recognition, or by the operator using  the 
             Alt-C  or  Alt-E keys).  In AMTOR, the SELCAL of  the  other 
             station  will  also be displayed sometimes, usually  if  you 
             entered the call.

             An  '[L]' will be displayed in the non packet modes  when  a 
             callsign is entered.  The '[L]' will flash to remind you (to 
             log it) until the QSO is logged.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 23  


             3.6 Logbooks

             LAN-LINK  uses two dBASE 3 compatible logbook files. One  is 
             used for VHF packet logging (VHF.DBF), the other for all  HF 
             modes (HF.DBF).  See Section 14 for more information.

        4.0  Function Keys

        Function  keys  are  used to perform  operations  common  to  all 
        communications modes, or to allow fast performance of a  function 
        without having to go through several layers of menus.  The action 
        of  each  of  the function keys is  described  in  the  following 
        sections.   The function key number corresponds to the  paragraph 
        number, namely 4.1 refers to Function Key 1 (F1), etc.

             4.1 Capture to Disk Toggle (F1)

             This  key toggles the "capture-to-disk" command.   When  the 
             "capture-to-disk"  is active, all incoming  text  (including 
             'Echo as sent' outgoing text) is stored on a disk (floppy or 
             hard) in a file called 'YYMMDD.RUN' where YY is the last two 
             digits  of  the  year,  MM the month and  DD  the  day  (EG. 
             900824.RUN).   If  this file does not exist the  first  time 
             that LAN-LINK is loaded, it is created.  From that time  on, 
             for the rest of that day, successive activations append  new 
             data to the contents of the file.

             Each time the command is activated a datestamp (or  timetag) 
             will be written to the file.

             When  a  Packet station connects "capture-to-disk"  will  be 
             activated automatically unless you instruct LAN-LINK not  to 
             do so with the Capture-to-disk flag (Section 18.17).  Packet 
             connects  will thus be recorded in their entirety  automati-
             cally  unless you turn off the "Capture-to-disk" during  the 
             course  of  the QSO. "Capture-to-disk" will  be  stopped  at 
             disconnect time.

             You  may later edit the file at your convenience  with  your 
             favorite word processor or the included Editor.  However, if 
             your word processor can only handle files smaller than  64k, 
             make  sure that the 'capture-to-disk' file remains  smaller.  
             You can do this by renaming the file to something like 'LAN- 
             RUN.001'.     LAN-LINK   will   automatically   close    the 
             "capture-to-disk"  file when you terminate the  program  and 
             return to DOS.

             Capture-to-disk is active when you scroll back.  You can use 
             this  feature to save data that has already scrolled by  the 
             window. 




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 24  


             4.2 Send Brag Tape and Talk (F2).

             This  command lets you transmit the Brag Tape (Default  LAN-
             LINK.TXT. In the non packet modes, it will leave the  trans-
             mitter  on  after sending the file.  In the packet  mode  it 
             will send a ^Z after sending the file to notify the  recipi-
             ent that the file is complete.

             4.3 Transmit Callsign Sequence (F3)

             This command lets you transmit the following sequence <other 
             call> DE <your call>.  For example if you are 4X6AA and  you 
             are  working  G3ZCZ  then this command  would  transmit  the 
             sequence  'G3ZCZ de 4X6AA'.  You use this at the  start  and 
             end of a transmission in any mode except Packet.

             4.4 Send Brag Tape (F4)

             This  command lets you transmit the Brag Tape (Default  LAN-
             LINK.TXT.  In the non packet modes, it will turn the  trans-
             mitter off after sending the file.

             4.5 Show Packet 'MH' list and Point and Shoot Connect (F5).

             This  command  lets  you see what calls the  TNC  has  heard 
             recently on the Packet channels.  You can see up to 18, with 
             the  data and time they were last logged by the TNC.   Refer 
             to the 'MH' command in the TNC manual for the particulars of 
             the display.

             The  MH list shows up in a special window and freezes  until 
             you depress any key.  While the list is frozen, LAN-LINK  is 
             not monitoring received data, so don't freeze it too long.  

             If  the MH list is blank, or information comes in  from  the 
             TNC  between the time you entered the command and  the  time 
             the  list is sent back,  subsequent text from the  TNC  will 
             show up in the MH window until the next 'Cmd:' appears or 18 
             lines of text have been received.

             You  can also use this command in a point and  shoot  method 
             for  attempting  a connect with a station  you  have  heard. 
             Bring  up the MH Window and move the cursor to  the  desired 
             callsign.  When the cursor is positioned on any character in 
             the  call,  press  the 'Enter' Key and  that  call  will  be 
             recognized  as the callsign.  If the call is joined  to  the 
             word "Cmd:" or the cursor is positioned on a space or blank, 
             the connect attempt will be inhibited.

             This command does not work on the TNC1.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 25  


             4.6 Auto CQ Call (F6)

             This  command will send a CQ sequence, wait a  preset  delay 
             and then repeat the CQ sequence until it receives your  call 
             back from someone else.  When it does so, it will alert  you 
             with  a  Connect  Alarm signal, reset the  delay  timer  and 
             revert  to the normal or listening mode.  In AMTOR  it  will 
             revert  to the mode in which it is waiting for an  ARQ  call 
             and is able to copy FEC signals on frequency.

             When   the  Automatic  CQ  sequence  is  in  operation,   an 
             indication  will  be  shown  in  the  status  window.    The 
             indicator  will be steady while the transmitter  is  sending 
             the CQ text, and will blink while the receiver is  listening 
             for a reply.

             The time delay between calls is set using the 'Q' command in 
             the Parameters Menu (Set CQ delay time).  It is also set  as 
             a  defined default by you when you setup  your  LAN-LINK.SYS 
             file.

             The  automatic  CQ  command will only work in  the  TNC  non 
             packet  modes if the 'Echo as Sent Mode' is set to 'ON'  per 
             the LAN-LINK.SYS file.  In other words, you must be able  to 
             see  the CQ  text slowly echo in the incoming window for the  
             command  to work.  The reason for this is that the "K  K  K"  
             (or  "+?" in AMTOR) sequence is used to arm the software  to 
             look for a reply.

             In  AMTOR  you  will get the connect  alarm  only  when  the      
             replying station transmits the '+?' character combination.

             The check for the detection of your callsign and the connect 
             alarm  sequence only occur after a line feed  character  has 
             been received.

             Under  most conditions in AMTOR, many in RTTY, and  some  in 
             MORSE,  LAN-LINK will recognize the callsign of the  station 
             answering  your CQ and display it in the status window.   In 
             the  event  that it fails completely, the  sequence  '--?--' 
             will  show up in the status window.  Since  the  recognition 
             algorithm  used just looks for the first word following  the 
             'DE space' sequence and assumes that it has the callsign, be 
             careful  to  check it when operating under  QRM  conditions.  
             You can override the automatic call selection with the Enter 
             Callsign command in the Call Menu.

             The automatic CQ sequence is canceled when an incoming  call 
             is detected (only if the Beacon or Robot/Mailbox Mode is not 
             selected), if you push the disconnect command key, or if you 
             change communications modes.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 26  


             4.7 Activate Type Ahead Buffer/AMTOR Relink (F7)

             This key is not available in the Packet Communications Mode.  
             It  also  functions somewhat differently in  the  AMTOR  and 
             other  communications  modes as described in  the  following 
             sections.

                  4.7.1 Activate Type Ahead Buffer

                  The  use of this key sets LAN-LINK to the "Type  Ahead" 
                  Mode.   This is necessary for the PK-232 only, the  KAM 
                  and the MFJ1278 have the feature built in.  Any charac-
                  ters then typed at the keyboard will be placed into the 
                  TNC  transmit buffer.  The contents of the buffer  will 
                  be  transmitted over the air when the transmit  command 
                  is invoked with Function Key 10 [F10].  

                  This  feature  allows you to 'type-ahead'  as  you  can 
                  enter  text  into  the transmit  buffer  while  viewing 
                  incoming words in the INPUT window in the screen.   Any 
                  characters  typed from the keyboard will be  echoed  in 
                  the OUTGOING window on the screen.

                  4.7.2 AMTOR Relink

                  If  you  return  to the Command  Mode  when  linked  to 
                  another  station in AMTOR, use this key to get back  to 
                  the Converse Mode.  If the link times out, you can  try 
                  to relink with this key if you have entered the  SELCAL 
                  of the other station.

             4.8 Disconnect, Disengage or Receive (F8)

             This  function  key  returns  the  station  to  the  receive 
             communications  (TNC command) mode.  It may also be used  to 
             abort  the automatic CQ sequence.  If you use it to abort  a 
             CQ  sequence while the transmission is in progress, you  may 
             also want to flush the PK-232  transmit buffer by using  the 
             Flush  command  in  the  TNC  Menu  or  the  Alt-F  hot  key 
             combination.

             In  a multiconnect situation the program will prompt you  to 
             tell it which I/O channel to disconnect.

             In  AMTOR  this  command key toggles  LAN-LINK  between  the 
             Chirpcopy  Mode  (listening  to  a  QSO  in  progress)   and 
             monitoring FEC transmissions (CQ calls).

             4.9 Put TNC in CMD Mode (F9)

             This  command puts the TNC into the Command Mode.   At  this 
             time, the program is transparent and acts as a dumb terminal 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 27  


             (except  for  placing  incoming and  outgoing  text  in  the 
             relevant windows).  You use this Mode for overriding any  of 
             the TNC default conditions.  (SEE I TOLD YOU THAT YOU HAD TO 
             READ THE TNC MANUAL).

             4.10 Put TNC in CONVERSE /Transmit Mode /AMTOR FEC (F10)

             This  command places the TNC into the transmit  or  Converse 
             Mode.  The transmitter is turned on and the contents of  the 
             transmit buffer are transmitted.  In the non packet communi-
             cations  modes, the outgoing characters will be echoed  back 
             from the TNC and displayed in the INCOMING window on the CRT 
             as they are transmitted on the air.  

             In the AMTOR modes this key puts the TNC in the FEC Mode and 
             turns the transmitter on.

             4.11 Alternate Function Keys

             These  keys  transmit the files with the  fixed  names  LAN-
             LINK.001 through LAN-LINK.010 (the suffix number corresponds 
             to  the  function  key) which must be located  in  the  same 
             directory  as the LAN-LINK.EXE program.  The transmitter  is 
             left on when the file has been sent.

                  4.11.1  Send/Talk file LAN-LINK.001
                  4.11.2  Send/Talk file LAN-LINK.002
                  4.11.3  Send/Talk file LAN-LINK.003
                  4.11.4  Send/Talk file LAN-LINK.004
                  4.11.5  Send/Talk file LAN-LINK.005
                  4.11.6  Send/Talk file LAN-LINK.006
                  4.11.7  Send/Talk file LAN-LINK.007
                  4.11.8  Send/Talk file LAN-LINK.008
                  4.11.9  Send/Talk file LAN-LINK.009
                  4.11.10 Send/Talk file LAN-LINK.010

             In  the non packet communications modes, the transmitter  is 
             left on when the file has been sent.  In AMTOR, the  change-
             over character pair (+?) is not sent.

             4.12 Shift Function Keys

             These function keys show the contents of the files with  the 
             fixed  names LAN-LINK.001 through LAN-LINK.010  (the  suffix 
             number  corresponds  to  the function  key)  which  must  be 
             located  in the same directory as the LAN-LINK.EXE  program.  

                  4.12.1  Show contents of file LAN-LINK.001
                  4.12.2  Show contents of file LAN-LINK.002
                  4.12.3  Show contents of file LAN-LINK.003
                  4.12.4  Show contents of file LAN-LINK.004
                  4.12.5  Show contents of file LAN-LINK.005


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 28  


                  4.12.6  Show contents of file LAN-LINK.006
                  4.12.7  Show contents of file LAN-LINK.007
                  4.12.8  Show contents of file LAN-LINK.008
                  4.12.9  Show contents of file LAN-LINK.009
                  4.12.10 Show contents of file LAN-LINK.010

             4.13 Control Function Keys

             These  function keys show the first lines of the files  with 
             the  fixed  names  LAN-LINK.001  through  LAN-LINK.010  (the 
             suffix number corresponds to the function key) which must be 
             located in the same directory as the LAN-LINK.EXE program.  

        5.0  Main menu

        When  you  press the Escape Key, the Main Menu  appears  on  your 
        screen  and provides a number of choices which are  described  in 
        the following sections.  
                  A Quick menu
                  B BBS Menu
                  C Call Menu
                  D eDit Menu
                  E Event Menu
                  F Files Menu
                  H Help Menu
                  J Jump to DOS Shell
                  K LAN-LINK Menu
                  L Log Menu
                  M Message Menu
                  N TNC Menu
                  O AMSAT-OSCAR Menu
                  P Parameter Menu
                  Q Q Codes [NC/L]
                  S communicationS Mode Menu
                  T Terminal Mode Menu
                  X eXit LAN-LINK

        Type in the single letter to make your choice.

        NOTE:   Different options will show up in each menu depending  on 
        the  connect  state (in packet) or the type of TNC that  you  are 
        using.   For example, if you are using a TNC that  only  supports 
        packet, the non packet menus will not be seen.  An other  example 
        is  that  the BBS Menu is only active when you are  connected  to 
        another station.

             5.1 The Quick Menu

             The  Quick Menu is designed for new users and  provides  the 
             most  commonly  used functions in a single Menu.  The  Quick 
             Menu Provides the following options.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 29  


             A Auto CQ
             B Send Brag Tape
             C Call Someone
             L Log Menu
             M Change Communications Mode
             Q Call CQ
             S Send/Talk File
             Z QRZ
             1..0 Send/Talk LAN-LINK files 001..010

             Type in the single letter to make your choice.  Each  option 
             is described below.

             5.2 Auto CQ

             This  option  initiates the automatic CQ sequence  in  which 
             LAN-lINK  sends out a CQ call, listens for a reply,  and  if 
             none  is received, sends out another CQ call, and so on,  ad 
             infinitum.  It is the same as using Function Key 6 (F6)  and  
             is described in Section 4.6.

             5.3 Send Brag Tape

             This  option  transmits the Brag Tape is the same  as  using 
             Function  Key  2 (F2) and is described in  Section  4.4  and 
             10.3.

             5.4 Call Someone

             This  option  is used when you want to call  or  connect  to 
             another station. It is described in Section 7.2.

             5.5 Log Menu

             This option invokes the logbook, described in Section 14.

             5.6 Change Communications Mode

             This option invokes the Communications Mode Menu,  described 
             in  Section  20.  You use it to  change  TNC  communications 
             modes.

             5.7 Call CQ

             This  option described in Section 7.6 is used to  initiate  a 
             single CQ call.

             5.8 Send/Talk File

             This  option is used to send a file. When the file has  been 
             sent, the transmitter will stay on. This option performs the 
             same function as does Function Key 4 (F4).


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 30  



             5.9 QRZ

             This  option is the same as using Alternate Q  Function  Key 
             (Alt-Q) and is described in Section TBS.

             5.10 Send/Talk LAN-LINK files 001..010

             This  option  is used to transmit the contents  one  of  the 
             LAN-LINK buffer files. You select the number, LAN-LINK  does 
             the  rest.  The option is the same as that provided  by  the 
             Alternate Function Keys and is described in Section 4.11.

        6.0 The BBS Menu

        This menu gives you smart file transfer capabilities with a  BBS.  
        The menu is only active when you are connected to another  packet 
        station.  The BBS Menu provides the following capability.

        D Download Text Files.

        Type in the single letter to make your choice.

             6.1 Download Text Files

             This option lets you download a text file from the BBS  into 
             a  separate  text  file on your disk.  Enter  the  full  BBS 
             download command at the prompt line.

             To download a file  from a W0RLI BBS such as FILENAME.TYP in 
             the  A  subdirectory  you'd  enter  'DA  FILENAME.TYP'.   To 
             download  the  same file from the PACKET subdirectory  of  a 
             WA7MBL BBS you'd enter the command 'D \PACKET\FILENAME.TYP'.

             If you use the 'D' command to download a text file, it  will 
             end up in a separate file on your disk ONLY IF a file of the 
             same name does not exist on your drive.  If a file with  the 
             selected name already exists on your disk drive you will get 
             an error message.  

        7.0 The Call Menu

        The call menu is used to enter calls, either to call/connect/link 
        a  station  or  to remember a call or path.  Each  time  you  are 
        prompted for a call, LAN-LINK will remember the previous 15 calls 
        and  you may use the Up and Down arrows to move the cursor  to  a 
        remembered call. If you wish to capture a call from the  incoming 
        text  window, push Function Key 10 (F10) to enter the window  and 
        move  the  cursor to the desired callsign.  When  the  cursor  is 
        positioned on any character in the text, push the 'Enter' Key and 
        that  word  will be recognized as the callsign.   Any  characters 
        joined  to the call (such as a '.') will be picked up as part  of 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 31  


        the  call.  If the cursor is positioned on a space or blank,  the 
        connect attempt will be inhibited.

        In  AMTOR, whenever you are asked to enter a  callsign,  LAN-LINK 
        will prompt you with its guess at the SELCAL.  If you agree  with 
        it,  just  press  the 'Enter' Key, if you  disagree,  enter  your 
        choice over the prompt version.

        The Call Menu provides the following choices. 

                  A Alert Call (packet) or ARQ Call Talk (AMTOR)
                  C Connect/Call
                  D Show Directory
                  E Enter Call
                  M reMember Path
                  P Packet Cluster
                  Q Call CQ
                  R Retry
                  T Target Call
                  U aUto CQ
                  X Set DX Flag On/Off
                  Z Zap BBS

        Type in the single letter to make your choice.

             7.1 Alert Call/ARQ Call

             7.1.1 Alert Call

             The Alert call feature is used in the Packet  Communications 
             Mode  when disconnected and the terminal set for  'TRFC'  or 
             'CQ/BEACON'.  LAN-LINK will scan the packet headers received 
             from  the  TNC, and, when it sees a  packet  originated  (or 
             digipeated if the MRPT parameter in the TNC is set to 'ON'), 
             by  the station whose call you have entered as  the  'Alert' 
             call,  it  will sound an alarm at the  console.    The  line 
             containing the packet header will also be displayed in light 
             green.

             This  option toggles the Alert call feature on and off.   If 
             it  is off, you are prompted for the call to  be  monitored, 
             and, if it is on, it is turned off.  The toggle is set  when 
             you  enter  a  callsign, and cleared when  you  depress  the 
             'Enter' Key instead of a callsign.

             The  Alert call will be shown flashing in the status  window 
             when in the disconnected state.

             NOTE: If the terminal is set for 'CQ/BEACON' the Alert  will 
             only  sound if the specified station transmits CQ or  BEACON 
             packets.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 32  


             7.1.2 ARQ Call

             In  AMTOR, this option will attempt to send an ARQ  call  to 
             the  desired  station, transmit the callsign  sequence  when 
             linked and allow you to continue typing text (Note that  the 
             C option sends the '+?' after the callsign sequence).

             7.2 Connect/Call

             This  option  works in almost the same manner  in  both  the 
             packet  and non packet communications modes as described  in 
             the following sections.

                  7.2.1 Non packet Modes

                  You  use  this option to call a station  heard  on  the 
                  band.   In AMTOR the link request will be sent  in  the 
                  ARQ Mode to the SELCAL of the desired station.

                  7.2.2 Packet Mode

                  You  use this option to attempt a connect with  another 
                  packet  station.  In a multiconnect situation the  LAN- 
                  LINK  will automatically select a free I/O  channel  to 
                  try the connect. 

                  7.2.2.1 Names, Handles and Paths

                  If  you  so  desire, you can create  a  directory  file 
                  (default name is LAN-LINK.DIR) and keep a list of names 
                  and  calls.  The computer will look up a name and  call 
                  the station by its callsign.  For example if you put 

                            Joe G3ZCZ

                  as  a line in the file, when you tell the  computer  to 
                  connect  to Joe, it will try to connect to  G3ZCZ.   If 
                  you enter 

                            4X4HF 4X4HF V 4X1AA, 4Z4ZB, 4X4IL  

                  you  only  need to type '4X4HF' to set up  the  correct 
                  connect path.  

                  You  can  also use this feature to automate  a  NET/ROM 
                  and/or a KA Node path connection.  

                  7.2.2.2 NET/ROM and TheLink

                  In  the manual NET/ROM path setting up mode, you  would 
                  first  connect  to your local node, then when  you  are 
                  connected with it, connect to the next node, and so  on 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 33  


                  through  any intermediate nodes within the  whole  path 
                  before  you  finally  connect  with  your   destination 
                  station.   You may also have digipeaters in any of  the 
                  paths.

                  For  example if you wish to connect to K1HTV who is  in 
                  range  of the SSCT node, and you are in Washington  DC, 
                  you  might first have to connect to your local  NET/ROM 
                  node   (ELK)  via  a  digipeater,  then  each  of   the 
                  intermediate nodes, SNJ3, NNJ, WMA before you could try 
                  to connect with K1HTV.

                  Consider  the manual sequence to make  the  connection.  
                  K1HTV  is  the station the contact is  being  attempted 
                  with,  and  he  is located within  range  of  the  SCCT 
                  NET/ROM  node.  The station attempting the  connect  is 
                  located  in  the Washington DC area one  digipeat  away 
                  from the ELK NET/ROM node.

                  The  connection to the local node is  performed  first.  
                  The  operator  has to type 'C ELK v WB4APR-5'  to  make 
                  that link. When the connect with the node is  achieved, 
                  the operator must type 'C SNJ3' to connect to the  next 
                  node.   Each time the connection is made, the  operator 
                  must  type in the command to make the next  one,  until 
                  finally the last node is reached and a connect  request 
                  can  be made to the destination station (either  direct 
                  or  via  a  digipeater).  Sometimes  there  may  be  an 
                  intermediate   non-NET/ROM   connection   between   two 
                  stations somewhere in the path.

                  This  procedure is tedious and time consuming,  because 
                  it  may take several seconds to complete each stage  of 
                  the link.  LAN-LINK automates this sequence by scanning 
                  the  line in the LAN-LINK.DIR file associated with  the 
                  callsign  entered and transmitting each section of  the 
                  line  when it recognizes the 'Connected to' reply  from 
                  each NET/ROM node in the path.  When it finally gets to 
                  the destination it sounds a chime to alert you that the 
                  connect has been achieved.

                  The  LAN-LINK.DIR  file  entry  for  this  path  is  as 
                  follows:

                       K1HTV ELK v WB4APR-5!SNJ3!NNJ!WMA!SCCT!K1HTV

                  where the '!' separates each stage of the link.

                  The key word is K1HTV.  LAN-LINK then scans the line to 
                  see if there is a '!' in it.  If there is it knows that 
                  it  is dealing with a NET/ROM path.  It then tells  the 
                  TNC to attempt a connect with the characters  following 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 34  


                  the  key  word up to the first '!'.  In  this  case  it 
                  tells the TNC to connect to ELK via WB4APR-5. When  the 
                  TNC  sends back the connected message,  LAN-LINK  tells 
                  the TNC to try to connect to the next node in the path, 
                  namely  in this example, SNJ3. The  sequence  continues 
                  each  time  a  connection is made  until  the  link  is 
                  complete.

                  To  set up a directory entry just use the format  shown 
                  above.   Place  a '!' sign after the  uplink  path  and 
                  different  node  segments. Do not place one  after  the 
                  downlink path.

                  Depending  on the configuration, LAN-LINK will issue  a 
                  'disconnect'  command  to  the TNC  in  the  event  the 
                  NET/ROM or KA-Node connect attempt fails.  This feature 
                  is  designed  for  known paths  not  for  general  path 
                  determination.

                  7.2.2.3 KA-Nodes

                  You  can  connect or cross connect via  KA-Nodes  using  
                  the   directory  file.   You  must  still  use  the   ! 
                  separators as well as two new symbols %  and &.  Use  % 
                  for 'C' and  & for 'X' in KA-Node links..

                  For example, given that a path to W9TNN-2 is first to a 
                  local  KA node [JRW] then to a second node on the  same 
                  VHF frequency [W3EAX-7] and lastly via a cross  connect 
                  on  40 Meters to W9TNN-2, the line in the  LAN-LINK.DIR 
                  file would be as follows.

                  w9tnn-2  jrw!%w3eax-7!&w9tnn-2

                  You can mix NET/ROM and KA-Node paths as in:

                  n7dva!g3zcz-9!&WA6IEL-4!n7dva v kl7vz-3

                  The different symbols are used for the KA node to  tell 
                  LAN-LINK  which replies to look for as well as what  to 
                  prefix the call with.

                  Depending  on  the Node Drop Link  Flag  configuration, 
                  LAN-LINK  will issue a 'disconnect' command to the  TNC 
                  in  the  event the NET/ROM or KA-Node  connect  attempt 
                  fails.   This feature is designed for known  paths  not 
                  for general path determination.

                  7.2.2.4 Loop Backs

                  In the Packet Communications Mode, if you want to  loop 
                  back through someone else you would have to type 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 35  



                        C <yourcall> V <hiscall>. 

                  For  example if I (G3ZCZ) wanted to loop  back  through 
                  4X6AA, I would have to type the command

                        C G3ZCZ V 4X6AA

                   to the TNC.

                  In  LAN-LINK you just have to enter the  '/'  character 
                  followed  by the call of the station you want  to  loop 
                  back through.  For example if I (G3ZCZ) wanted to  loop 
                  back through 4X6AA, I just need to enter 

                                         /4X6AA

                  as  the call to connect to at the correct  prompt,  and 
                  LAN-LINK  will tell the TNC to try to connect to  G3ZCZ 
                  via  4X6AA, namely issue the command 'C G3ZCZ V  4X6AA' 
                  to the TNC.

             7.3 Enter Call

             This  option lets you enter the call of any station  calling 
             you into the program. If you type the Enter Key in  response 
             to  the  prompt,  you can later use  Function  Key  (F3)  to 
             transmit the sequence "DE <yourcall>". You may also use  the 
             Retry feature to call that station.

             In  AMTOR,  you use the feature to enter  the  callsign  and 
             SELCAL  of the station you are listening to and may want  to 
             call later.

             7.4 ReMember Path

             You may use this option to put an entry in the  LAN-LINK.DIR 
             file.  

             7.5 Zap Packet Cluster

             This  option  firsts prompts you with the  callsign  of  the 
             PacketCluster. If you enter a callsign, the entered callsign 
             will become the new PacketCluster call. LAN-LINK then issues 
             a connect request to the PacketCluster.  When the connection 
             is achieved, and the PacketCluster sends you a '>' character 
             at the end of a line of text, LAN-LINK will issue a 

                  'SHOW/WWV' command followed by a 'SHOW/DX'

             command to the PacketCluster and return to manual operation.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 36  


             Note:  PacketCluster  is  a  specialized  BBS/conference  by  
             Pavilion Software for DX chasers.

             7.6 Call CQ

             You  use  this  command  key to  call  CQ.   In  the  Packet 
             Communications  Mode, the TNC will transmit a line  of  text 
             along with the CQ packet.  The line of text is set up in the 
             LAN-LINK.SYS file described in Section 22.
              
             In  the  AMTOR  Communications Mode,  your  SELCAL  will  be 
             transmitted along with the CQ call in the FEC Mode.

             7.7 Retry

             This   option   (also activated by the Alt-R  function  key) 
             allows  you to retry a connect that for some reason did  not 
             go through the first time.  It saves wear and tear on   your 
             fingers  particularly if the desired connect path is  via  a 
             number  of  digipeat relays or through a number  of  NET/ROM 
             NODES.

             In the non packet modes, it allows you to retransmit a  call 
             to another station without having to reenter the call.

             If  you  have  previously used the Enter feature  to  put  a 
             callsign in the program when you hear that station, you  can 
             then use the Retry command to call him later when the QSO in 
             progress terminates. 

             7.8 Show Call Directory

             This  option  displays the contents of  the  call  directory 
             file (LAN-LINK.DIR).

             7.9 Target Call

             The Target call feature is used in the Packet Communications 
             Mode when disconnected. LAN-LINK  will monitor the  stations 
             connecting  to  you. When it sees a connect by  the  station 
             which you have entered as the 'Target' call, it will set the 
             flashing Connect Count display to show a 'happy face'. 

             This option toggles the Target call feature on and off.   If 
             it is off, you are prompted for the call to be monitored, if 
             it  is  on, it is turned off.  The toggle is  set  when  you 
             enter a callsign, and cleared when you press the 'Enter' Key 
             instead of a callsign.

             The Target call will be shown flashing in the status  window 
             when in the disconnected state.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 37  


             7.10 Auto CQ

             This option is the same as Function Key 6 (F6).

             7.11 Toggle DX Flag

             LAN-LINK allows you to call either 'CQ' or 'CQ DX'.  If this 
             flag  is  set, all CQ calls will be to "CQ DX".   If  it  is 
             cleared, all CQ calls will be plain CQ's.  

             7.12 Zap BBS

             The BBS Mail Snatch can be initiated in two ways. It can  be 
             initiated when your incoming screen displays a "Mail" beacon 
             (received  from your local BBS) with your call in the  first 
             line  following  the  header,  or  by  LAN-LINK's  Zap   BBS 
             function.  The automatic BBS Zap will not take place if LAN-
             LINK is in the multi-user mode.

             In the event of a BBS Mail-Snatch, if the *.BBS file  exists 
             for  that BBS, the file will be processed and  the  contents 
             sent to the BBS.  Thus if you don't get a chance to send the 
             mail  before  LAN-LINK downloads the mail from the  BBS,  it 
             will send it for you. 

             When the BBS has accepted the commands the name of the  file 
             is  changed  from '*.BBS' to '*.n', where 'n'  is  a  number 
             increasing sequentially each time the function is performed. 
             For  example,  the  file name KE8X.BBS will  be  changed  to 
             KE8X.001  the first time it happens.  In this way, you  will 
             have  a  copy of the outgoing file on your  disk  until  you 
             choose to delete it.

             In the real world however, message formats are  nonstandard, 
             and  can  contain  any set  of  characters.   The  algorithm 
             developed  here  transmits the next line in the  *.BBS  file 
             when  LAN-LINK sees a 'trigger' character-string unless  one 
             of the 'inhibitor' character-strings is also present on  the 
             line of the message text received by LAN-LINK.

             These  'trigger'  character-strings  are '>'  (as  the  last 
             character  of the line of text ), 'Enter', 'Subject',  'Sj:' 
             and 'Msg:'.  The 'inhibitor' character-strings are 'R:', '<' 
             and 'Message'(R: as in routing headers and < and Message  as 
             in Message-Id: <message number> in message headers).

             This should cover most simulated manual BBS message  reading 
             (WA7MBL and W0RLI/VE3GYQ) and avoid false triggering due  to 
             '>'s showing up in message and routing headers.

             NOTE that when LAN-LINK finishes processing the *.BBS  file, 
             it  will  send  a 'B' command to the BBS  to  terminate  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 38  


             session.  This feature is designed to minimize the time  you 
             spend  connected  to  the BBS by allowing you  to  scan  the 
             message list when automatically receiving your mail, prepare 
             your  replies and download requests off-line and then  later 
             read  the  incoming messages or files without tying  up  the 
             BBS.  It thus positively disconnects you from the BBS.

             In the Packet Communications Mode, the Alt-Z key initiates a 
             BBS  Mail Snatch.  You use this key if you connect to a  BBS 
             before you hear its beacon, or if you have disabled the  BBS 
             Mail Snatch feature.  If you are connected to a BBS, the key 
             must be used BEFORE the first '>' is received.  Note: it  is 
             that  first  '>' that triggers the sequence.   If  you  have 
             already  received that first '>', send the BBS any  command, 
             and  the sequence should begin when the BBS signals that  it 
             has  completed  processing  that command.  If  you  are  not 
             connected,  LAN-LINK will first try to connect to  the  BBS, 
             then perform the sequence.

             When  you use this command you will be asked if you want  to 
             upload  or download. If you want to download, just push  the 
             'Enter'  Key.   A Download (Mail from the BBS to  you)  will 
             automatically  be  followed by an Upload if the  *.BBS  file 
             exists.

             The download sequence performed by the BBS Mail Snatch is as 
             follows:

             RM        To read your messages, (Configurable)
             L         To let you know what is new on the BBS,
             LM        To list ALL your messages on the BBS,
             B         To log you off the BBS.

             LAN-LINK will wait for the '>' as the last character of  the 
             line of text being received from the BBS, before issuing the 
             next command in the sequence.  Your messages will be  placed 
             in a message file <yourcall>.OUT as if someone else had left 
             a message for you.

             The 'RM' may be customized in the LAN-LINK.SYS file to  'RN' 
             or 'VM' depending on the software in your local BBS and your 
             preference.

             During  the  time  that the BBS is  responding  to  the  'L' 
             command  with a list of new messages, LAN-LINK  is  scanning 
             the  lines  containing the messages to see if it  finds  one 
             containing a Scan Word.  If it does it will queue a  request 
             to download that message.

             If  you wish to add a 'KM' to the sequence, place it in  the 
             BBS.BBS file. If you use 'KM' as you may delete mail  BEFORE 
             reading it.   


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 39  



             If you use the 'D' command to download a text file, the file 
             will  end up in a separate file on your disk ONLY IF a  file 
             of the same name does not exist on your drive.

             Do  delete 'read' mail from your local BBS.   Don't  clutter 
             the  BBS's  disk with your read mail. The  'LM'  command  is 
             built  into  LAN-LINK  to remind you of what  you  have  out 
             there. 

             The BBS 'S' command (including its variations such as  'SP') 
             is the only multiple line command allowed.  You can thus put 
             all  the single line commands such as D, H, ?, L, and  R  in 
             the BBS.BBS file.

             A  'multiple  command'  is defined in  this  instance  as  a 
             command which allows you to enter multiple lines before  the 
             BBS  will send back a '>' character (i.e. one that  the  BBS 
             tells you to type in text and terminate it with the  Control 
             Z character).

             Each  message must be in the format expected by the BBS  and 
             must  end with the " :EOF: " character string, but there  is 
             no need for any special end of BBS file character.

             A typical message could be as shown below.

             SP G3ZCZ @ N4QQ
             LAN-LINK
             I   think   it is great. However, why don't you  change  the 
             following......  (add  your comments here).

             :EOF:  {last line may also be '/EX'}

        8.0 Edit Menu

        This menu provides the following choices.

                  B Brag Tape
                  D Call Directory File
                  F Any other File
                  K Answer Ctdsk File
                  M Answer Incoming Mail
                  N Note
                  O Pick *.OUT (Message) File to Edit
                  P Pick Ctdsk File to Edit
                  R Capture to Disk File
                  S LAN-LINK.SYS
                  T Two Files
                  1,2 - 0 LAN-LINK.001 - 010

        Type in the single letter to make your choice.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 40  



        LAN-LINK  contains an ASCII text editor suitable for  files  less 
        than  64k in size.  It is built based on Borland's  Turbo  Pascal 
        Editor Toolbox and the commands are compatible with Sidekick  and 
        Wordstar.  A summary of the editor commands is shown below. 

             F10      Switch Windows (if more than one window open)

             Backspace Delete left char
             Del       Delete Char
             Enter     New line
             Ins       Toggle insert mode
             PgUp      Move cursor up one page
             PgDn      Move cursor down one page

             ^A        Move cursor left one word
             ^C        Move cursor down one page
             ^D        Move cursor right one character
             ^E        Move cursor up one line
             ^F        Move cursor right one word
             ^G        Delete one character
             ^H        Delete left one character
             ^I        Tab
             ^L        Find/replace next occurrence
             ^P        Insert a control character into the text
             ^M        New line
             ^N        Insert line
             ^R        Move cursor up one page
             ^S        Move cursor left one character
             ^T        Delete one word after cursor 
             ^V        Toggle insert mode
             ^W        Scroll up
             ^X        Move cursor down one line
             ^Y        Delete line at cursor
             ^Z        Scroll down

             ^K^B      Mark beginning of block
             ^K^C      Copy block to position of cursor
             ^K^D      Save file and exit edit 
             ^K^H      Hide block marker
             ^K^K      Mark end of block
             ^K^Q      Abandon file and exit edit
             ^K^R      Read file into screen
             ^K^T      Mark single word as block
             ^K^V      Move block to position of cursor
             ^K^W      Write block to disk file
             ^K^Y      Delete block
             ^K 1..9   Set marker 1 .. 9

             ^Q^A      Find text and replace
             ^Q^B      Move to beginning of block
             ^Q^C      Move to end of file


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 41  


             ^Q^D      Move to right of line
             ^Q^E      Move to top of window
             ^Q^F      Find text
             ^Q^I      Toggle autoindent mode
             ^Q^K      Move to end of block
             ^Q^R      Move to top of file
             ^Q^S      Move to left of line
             ^Q^X      Move to bottom of window
             ^Q^Y      Delete to end of line
             ^Q 1..9   Jump to marker 1..9

             The  following options can be set in the Find/Find  and  Re-
             place (^Qf and ^Qa) operations.

             # locates #th occurrence
             G global replace
             N replace without Y/N question
             U ignore upper case/lower case
             W match whole words only

        Notes

        1    The ^ key in front of a character identifies that  character 
             as  a  'control' character.  To activate it, hold  down  the 
             Control key AND the character key.  

        2    Some of the commands require two keystrokes.

        WHILE  USING THE EDITOR, LAN-LINK can't receive  characters  from 
        the TNC. All other features ARE INHIBITED OR LOCKED OUT.  THUS IF 
        SOMEONE CONNECTS TO YOU, THE TNC WILL KNOW BUT LAN-LINK WILL NOT.  
        BE WARNED !!!  

        The Edit menu allows you to call up the various files for editing 
        as follows.

             8.1  Edit Brag Tape

             This option allows you to create and edit the Brag Tape File 
             (LAN-LINK.TXT).

             8.2  Edit Call Directory file

             This option allows you to create and edit the Call Directory 
             File (LAN-LINK.DIR).

             8.3  Edit any other file

             This option allows you to create and edit any other file.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 42  


             8.4   Answer Ctdsk File (Split Screen)

             This option allows you to edit the capture-to-disk file  and 
             reply  to incoming  bulletins/messages  in  a split   screen  
             mode.  The contents of the  incoming bulletins and  messages 
             will  be displayed in the top window, and the reply file  in 
             the  lower  window.  The reply file is assumed to  be  named      
             according to the Zap convention (*.BBS file).  You will have 
             to  set up the replies/outgoing messages in the  form  shown 
             below.

             SP Call @ BBS
             Subject of the message

             content lines

             End the message with either 

             ':EOF:'  , '/ex' or '/EX'

             as  the first word on a separate line (without the ').   For 
             example,

             SP G3ZCZ@N4QQ
             Test
             This is a test

             73
             /ex

             Use  Function key 10 (F10) to switch windows.  At this  time 
             you cannot transfer text between windows.

             8.5  Answer Incoming Messages (Split Screen)

             This  option  allows you to answer incoming  messages  in  a 
             split  screen  mode. The contents of the  incoming  messages 
             will  be displayed in the top window, and the reply file  in 
             the  lower  window.  The reply file is assumed to  be  named 
             according  to  the  Zap  convention  (*.BBS  file).    Reply 
             messages are set up as described in Section 8.4.

             Use  Function key 10 (F10) to switch windows.  At this  time 
             you cannot transfer text between windows.

             8.6  Leave Note for Someone

             In  all  modes  you can leave a  brief  note  (message)  for 
             another  station.  When you invoke this option, you will  be 
             prompted for the call of the station that you want to  leave 
             a note for.  The date/time header is written to the  message 
             file, then as you enter the text it is stored on the disk in 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 43  


             the  usual  format.        

             After you have left the note and received the 'QSL'  message      
             from LAN-LINK, if you are in the Packet Communications Mode,      
             press  Function Key 8 (F8) or Alt-D to load the callsign  of      
             the recipient into the beacon.

             When  you  leave a note, leave it for the root call  of  the 
             connectee, for example to leave a note for G3ZCZ/W3 leave it 
             for G3ZCZ, similarly to leave a note for  WB8WKA-1 leave  it 
             for  WB8WKA.  LAN-LINK is smart enough to extract  the  root 
             call from any callsign it links/connects with.  

             8.7  Edit Capture-to-Disk file

             This  option allows you to edit the Capture-to-Disk file  as 
             long as it is smaller than 64k.

             8.8  Edit Two Files (Split Screen)

             This  option  allows you to create and edit any  two  files.  
             Use  Function Key 10 (F10) to switch windows.  At this  time 
             you cannot transfer text between windows.

             8.9  Edit Configuration file

             This option allows you to edit the Configuration File  (LAN-
             LINK.SYS).

             8.10 Edit LAN-LINK.001 through LAN-LINK.010 files

             This option allows you to create and edit the 10 files (LAN-
             LINK.001 to LAN-LINK.010).  Use the suffix number to  access 
             the  respective LAN-LINK.* file, use the number 0 to  access 
             the LAN-LINK.010 file .

             8.11  Pick Capture-to-disk to Edit

             This option presents you with a directory window  containing 
             a  list  of  capture-to-disk files  (YYMMDD.RUN).  Move  the 
             cursor  down to the desired file and touch the 'Enter'  key. 
             If you don't want to edit any of them, then move the  cursor 
             down to a blank line. If you have more files than one screen 
             full,  use the Pgdn (Page Down) key to show the next  screen 
             full.


             8.12  Pick Message file to Edit

             This option presents you with a directory window  containing 
             a list of message files (*.OUT. Move the cursor down to  the 
             desired message file and touch the 'Enter' key. If you don't 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 44  


             want  to  edit any of them, then move the cursor down  to  a 
             blank line. If you have more files than one screen full, use 
             the Pgdn (Page Down) key to show the next screen full.

        9.0 Event/Clock Menu

        LAN-LINK contains some time dependent features which allow you to 
        schedule  events.  These features are controlled from  this  menu 
        and are listed below.

                  A Set Alarm
                  C Connect/Call
                  D Display Event
                  P Periodic Event
                  R Turn Robot ON/OFF
                  S Turn ConteSt ON/OFF
                  T Turn Time Display ON/OFF
                  X Cancel Event
                  Z Zap BBS

        Type in the single letter to make your choice.

        To set a scheduled event, first select the event, then enter  the 
        time.   You  may set the event to occur once a day,  or  once  an 
        hour.  If you wish the event to occur once an hour, enter an hour 
        value  greater than 23 when asked to enter the hour.   Each  time 
        the event occurs, the feature will be cleared.

             9.1  Set Alarm

             This option allows you to set an alarm clock.

             9.2  Connect

             This  option allows you to set LAN-LINK to issue a  call  or 
             connect request at some later time.

             9.3  Display Event

             This option allows you to display the scheduled event.

             9.4  Periodic Event

             This option allows you to set a periodic connect request  or 
             call  event.  You can set the start time, the end  time  and 
             the  time interval between the connect/call  attempts.   The 
             first  connect  that  goes  through  will  clear  the  event 
             scheduler.

             9.5  Turn Robot ON/OFF

             This option allows you to turn the AMTOR/Packet Robot on  or 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 45  


             off at a fixed time.

             9.6  Turn Contest ON/OFF

             This  option allows you to turn the  AMTOR/Packet  Automatic 
             Contester  on or off at a fixed time. You will  be  prompted 
             for the time, a starting QSO number (in case you a  restart-
             ing  the contest) and the Contest Text (in case you wish  to 
             change it).

             9.7  Turn Time Display ON/OFF

             This option allows you to turn the clock display on or off.

             9.8  Cancel Event

             This option allows you to cancel a scheduled event.

             9.9  Zap BBS

             This  option  allows  you  to  schedule  a  BBS  Zap  at   a 
             predetermined  time (like in the middle of the  night).  You 
             may  for example set it to attempt to connect to a BBS at  a 
             fixed  time or hourly at any desired minute after the  hour.  
             Should  the  connect be made, the event  scheduler  will  be 
             cleared and no further connect attempts will be made.

        10.0 Files Menu

        The Files Menu provides the following choices.  

                  B Send Brag Tape
                  D File Directory
                  E Erase File
                  R Rename File
                  S Send File
                  T Send/Talk File
                  U Send Uppercase File
                  V View file

        Type in the single letter to make your choice.

        During  the file transfer, the outgoing text will appear  in  the 
        OUTwindow.  If the text is long enough and fills the TNC  buffer, 
        you will see it stop, and then continue when the TNC is ready  to 
        accept  more text, the message sequence will resume.  NOTE  hard-
        ware flow control NOT ^S/^Q software is used.

        When you transmit a file (B or S) you are returned to the receive 
        mode  after the file is sent except in the Packet  Communications 
        Mode.  In the Packet Communications Mode, when the file has  been 
        loaded into the TNC the computer will add the ^Z character to the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 46  


        outgoing text to signal to the recipient that the file  transmis-
        sion is over.  

        The computer will signal you (using the bell character) when  the 
        file has been loaded into the TNC,  Note that is not the same  as 
        the  time that the TNC has transmitted the file, because the  TNC 
        incorporates a character buffer.

             10.1  Send Brag Tape

             This  command  allows you to transmit a standard  text  file 
             historically  known as a "Brag Tape".  The default  name  of 
             the brag tape file is LAN-LINK.TXT, and it should be created 
             with a word processor in the non-document mode.  

             10.2  File Directory

             This command shows you the directory of the disk drive.

             10.3  Erase File

             This command allows you to erase or delete a file.

             10.4  Rename File

             This  command  allows you to rename a file.  You  could  for 
             example rename a document file to a "<callsign>.OUT" file so 
             that  someone will receive it automatically next  time  they 
             connect.

             10.5  Send File

             This  option  lets  you  transmit  an  ASCII  file.  In  the  
             non  packet  modes, it will turn the transmitter  off  after 
             sending  the  file.  In the packet mode it will  send  a  ^Z 
             character when the file is complete.

             10.6  Send/Talk File

             This  option  lets  you  transmit  an  ASCII  file.  In  the 
             non  packet  modes, it will leave the transmitter  on  after 
             sending the file.

             10.7  Send Uppercase File

             This  option  lets you transmit an ASCII file  and  converts 
             each   line  of  text  in  the  file  to  UPPERCASE   before 
             transmitting  it.  The file itself is not  changed.  In  the 
             non  packet  modes, it will turn the transmitter  off  after 
             sending the file.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 47  


             10.8  View file

             This option lets you view the contents of a file.  Use it if 
             you must on long files.  On files with less than 64k charac-
             ters, use the Edit Menu.  

             10.9 View Ctdsk File

             This  option lets you view the contents of  the  capture-to-
             disk  file (YYMMDD.RUN).  Use it if you must on long  files.  
             On files with less than 64k characters, use the Edit Menu.  

             10.10

             This option lets you view the contents the Incoming  message 
             file (yourcall.OUT).  Use it if you must on long files.   On 
             files with less than 64k characters, use the Edit Menu.  

        11.0 Help Menu

        This option will activate the HELP display. Help displays a brief 
        summary of the function and hot keys.  This window will remain on 
        display until a character is typed at the keyboard.

        12.0 Jump to DOS Shell

        This  option  allows  you to enter a DOS shell.  If  you  do  not 
        restore  the  system  to the directory  which  contains  LAN-LINK 
        before you EXIT from the shell, LAN-LINK will do so for you.

        You may use  the DOS shell while in QSO when you have loaded  the 
        computer/TNC output buffers and output will continue to flow.

        To  exit from the DOS shell back to LAN-LINK, enter  the  command 
        'EXIT'.  LAN-LINK  will automatically return you to  the  correct 
        subdirectory.

        13.0 LAN-LINK Menu

        The LAN-LINK menu provides different options depending on whether 
        you  are  connected  to another station or  not.   The  following 
        options are available when connected.  

                  B :QBU: External Protocols
                  M :QBM: File
                  P :QSP: Message
                  Q :QDB: File
                  S :QSM: File
                  T :QTA: Messages
                  U :QRU: Messages

        The following option is available when not connected.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 48  



                   W Who is "ON-LINE"

        Type  in  the  single letter to make your choice.   

        Each  of  the features (except the :QBU:) may also  be  performed 
        manually by typing the full sequence of Network Control  Language 
        (see Appendix 3) character strings.  

             13.1 The :QBU: Command 

             This is a Sequence for external operations and only shows up 
             in  the LAN-LINK Menu when connected. It requires  that  the 
             batch  file 'QBU-TX.BAT' be present in the  initiating  sta-
             tion, and that the batch file 'QBU-RX.BAT' be present in the 
             receiving  station.  When the QBU sequence is  executed  the 
             following occurs:-

             The transmitting station sends a :QBU:

             The receiving station sends a :QRV: and an amount of  memory 
             left on disk, enters the transparent mode, jumps to dos  and 
             executes the batch file 'QBU-RX.BAT'. 

             Upon  receipt  of the :QRV:, the transmitting  station  then 
             puts  the TNC in the transparent mode and jumps to  Dos  and 
             executes the batch file 'QBU-TX.BAT'. The batch file  should 
             exit and return to LAN-LINK. LAN-LINK then exits the  trans-
             parent mode.

             When  the receiving station batch file finishes and  returns 
             to  LAN-LINK. LAN-LINK then exits the transparent  mode  and 
             transmits  a :QSL: if the DOS Error level was 0 and a  :QNO: 
             error if it wasn't.

             At this time both stations are back in the converse mode.

             You  may  use this technique for  transmitting  pure  binary 
             files  using  external (to LAN-LINK)  protocols).   You  may 
             change  the  default names of the batch files  in  the  LAN-
             LINK.SYS configuration file.

             13.2 :QBM: File

             You use this option to download a file from another LAN-LINK      
             station.    It  is  the  same  as  manually  typing 
             ':QBM: FILENAME'.

             13.3 :QSM: Message  

             You  use this option to request a repeat of a message. It is 
             the same as manually typing ':QSM:'.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 49  



             13.4 :QSP: Message
              
             You  use this option to store a message on another  LAN-LINK 
             station.  It is the same as manually typing 
             ':QSP: <callsign>'.

             LAN-LINK contains store and forward routines for messages in 
             a Local Area Network (LAN) as described in Appendix 2. 

             When connected to another LAN-LINK station, you may use  the 
             NC/L :QSP: command to leave a message at that station.  This 
             QSP  command  automates that feature for you.  It  lets  you 
             just  enter the callsign of the station you wish to leave  a 
             message  for.   It will then send the  text  sequence  :QSP: 
             <callsign>.   The  other LAN-LINK HOST station  will  either 
             reply  :QNO: followed by a number or :QRV: <callsign>.   The 
             'QNO'  message means that the other computer  cannot  accept 
             the message, the :QRV: message means that it is waiting  for 
             you to send it.

             If  you get the :QRV: reply, go ahead and type the  message, 
             or  send the text file containing the message.  If you  type 
             the  message,  use a control Z (^Z) character  and  carriage 
             return  to terminate the message.  (In AMTOR, LAN-LINK  will 
             translate the ^Z to :EOF: +? to terminate the message).  You 
             will  then  receive either a :QSL: from  the  other  station 
             meaning that the message is accepted, or a :QNO: followed by 
             a message that something went wrong and the message was  not 
             stored.  

             13.5 :QDB: File

             You  use  this option to upload a file to  another  LAN-LINK 
             station.  It is the same as manually typing
              ':QDB: FILENAME'.  

             This option saves you typing the file name twice.

             13.6 :QRU: Messages

             The  NC/L  QRU  command allows you to  upload  a  number  of 
             messages  to  the other station.  You use it when  you  have 
             messages  pending on your system and want to pass them to  a 
             third  computer for storage in the LAN, while you take  your 
             computer off-line.

             You  use  this  option  to begin  the  upload   sequence  to 
             transfer  messages for a number of stations to another  LAN-
             LINK station.  It is the same as manually typing :QRU:.  

             You  can only use this option with a station which you  have 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 50  


             previously  designated as a store and forward mail box,  for 
             specific  stations, namely one for which you have set  up  a 
             <callsign>.MBX  file.  This command may be triggered by  you 
             using this choice or by the connecting station sending you a 
             :QRU: command.

             When the sequence is over, the computer sending the messages 
             will transmit the NC/L command word :QJG: to signal that the 
             sequence is complete.  Should you receive it before you  get 
             any messages, then there weren't any pending. 

             If  you  want  to download messages  from  another  LAN-LINK 
             system,  connect to it and type the sequence :QRU:  followed 
             by the 'Enter' character.  That system will then respond  to 
             you as if the operator there had initiated a QRU command.

             Appendix 2 contains more information on the LAN capabilities 
             of LAN-LINK.

             13.7 Who is "ON-LINE"

             You   use this option (when unconnected and  monitoring  the 
             traffic  on a channel) to see who is 'ON-LINE' on  the  LAN.  
             It  is  the same as going manually into the  Converse   Mode  
             and  transmitting  an  unconnected  packet  containing   the 
             character string :QRA:.

             13.8 :QTA: Messages

             If you have a bad path (See Section 24.12) and your messages 
             are  not  automatically deleted by the other  station  after 
             they  have been sent to you, you use this option  to  delete 
             your message. It is the same as manually typing ':QTA:'.

        14.0 Log Menu

        LAN-LINK   performs  automatic logbook entries  for  Packet   and 
        AMTOR   Beacon   mode  Connects,   and   semiautomatic    logbook 
        entries for other modes.  The Log files are in dBASE 3 format and 
        can be  processed  by  the DBASE  Logbook  Package  in PC-HAM for  
        indexed listings,  tracking of DXCC and other AWARDS, etc.   This  
        is  ideal  for special event stations and DX-peditions, for   the 
        whole  QSL  process and further statistical  analyses  of   their 
        operation.   The  structure  of the logbook files  are  as  shown 
        below.

             Field  Field Name  Type      Length    Dec
                 1  DATE        Character      8  
                 2  TIME        Character      4  
                 3  BAND        Character      3  
                 4  CALL        Character     10  
                 5  RX          Character      3  


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 51  


                 6  TX          Character      3  
                 7  MODE        Character      4  
                 8  POWER       Character      4  
                 9  QSLSENT     Character      1  
                10  QSLRX       Character      1  
                11  COMMENTS    Character     20  
             -----------------------------------------------
             ** Total **                      62

        The size of the COMMENTS field is a compromise.  Each field is  a  
        fixed  size  so  that each  log  entry  takes  up  52  characters  
        worth  of  space on the disk  even  if  all  the character  space 
        is  unused. You may change the size  of  the field if  you  wish, 
        but  to do that you will have to use dBASE.  Note also,  that  if 
        you  do  make  the comments field longer,  the  display  will  be 
        screwed up.

        For   the logging feature to work, the logbook file   VHF.DBF  or 
        HF.DBF) must  be present  on the disk.  

        When   an   AMTOR beacon mode or packet   connect   occurs,   the 
        connect   is  automatically logged.  In the  Packet   Mode,   the 
        connect   path   is  placed in the  comments   section   of   the 
        logbook  entry.  In the non packet modes, the log data  entry  is  
        set  up  for  you  with default  599  values  for   the   reports 
        exchanged.  

        When you bring up the Log Menu you will be shown the last  screen 
        or page of log entries.  The last entry will be  highlighted.  At 
        this  time  a  number of function keys can be used,  or  you  may 
        depress  the  'Escape' key to bring up the Main  Log  Menu.   The 
        following are the Function Keys are active in the Log Menu.

        Alt-A      Append Entry 
        Alt-E      Edit Log Entry 
        Alt-F      Find an Entry 
        Alt-S      Scan Log by Call 
        Alt-U      Toggle Delete Mark 
        Alt-Z      Pack Log 
        Ins        Toggle Insert Mode 
        End        Show Last Page 
        Home       Show First Page 
        PgUp       Move Up One Page
        PgDn       Move Down One Page 
        Up Arrow   Move Up One Entry
        Down Arrow Move Down One Entry

        The operation of each function key is described below.

             14.0.1 Alt-A   Append Entry 

             This function key allows you to manually append an entry  to 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 52  


             the log.  You can also use this command to enter the odd SSB  
             contact  into  the  logbook  file.   If  you  do,  use   the 
             characters   'SSB' or 'FM' for those voice modes  to  remain 
             compatible with  the rest of the DBASE logbook package.

             When   appending   or  editing  an  entry,   LAN-LINK   will 
             automatically  enter the date, time, callsign of  the  other 
             station, band, mode and QSL information in upper case.

             The   comments  field  in  the  LAN-LINK  logbook  file   is 
             restricted  to a maximum of 20 characters.  If you  try  and 
             enter more than 20, the surplus will be ignored.
             
             14.0.2 Alt-E   Edit Log Entry 

             This function key allows you to edit the highlighted  entry.  
             Move  the  cursor  with the arrow keys,  and  end  the  edit 
             process by depressing the 'Escape' key.  

             You  may use the 'QSL' entry to tag the fact that  you  have 
             written out or received a QSL card.

             14.0.3 Alt-F   Find an Entry 

             This  function  key  allows  you to find  an  entry  by  the 
             (record)  number  assigned to it by LAN-LINK.  This  is  the 
             number displayed in the first column.

             14.0.4 Alt-S   Scan Log by Call 

             This function key allows you to scan the logbook by callsign 
             prefix. 

             14.0.5 Alt-U   Toggle Delete Mark 

             This function key allows you to mark an entry for  deletion, 
             or un-mark it in case you change your mind.  Entries  marked 
             for deletion will be flagged by an '*' character next to the 
             record number.

             14.0.6 Alt-Z   Pack Log 

             This function key allows you to pack the logbook files.  All 
             entries  marked for deletion will really be deleted at  this 
             time.

             14.0.7 Ins     Toggle Insert Mode 

             This function key allows you to turn the insert mode ON  and 
             OFF for the edit/append functions.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 53  


             14.0.8 End     Show Last Page 

             This function key moves you to the last page of the logbook.

             14.0.9 Home    Show First Page 

             This  function  key  moves  you to the  first  page  of  the 
             logbook.

             14.0.10 PgUp   Move Up One Page 

             This  function  key  moves the display up one  page  of  the 
             logbook.

             14.0.11 PgDn   Move Down One Page 

             This  function  key moves the display down one page  of  the 
             logbook.

             14.0.12 Up Arrow    Move Up One Entry

             This function key moves the highlight up one  entry  in  the 
             logbook.

             14.0.13 Down Arrow  Move Down One Entry

             This function key moves the highlight down one entry  in the 
             logbook.

             When  you  bring  up  the Main Log  Menu,  it  provides  the 
             following choices. 

        A Append Entry
        B Scan Log by Band
        C Change Log
        D find Date
        E Edit Log Entry
        F Find an Entry
        I Import-Convert Log
        H Help Function Keys
        M Scan Log by Mode
        P Print Log
        S Scan Log by Call
        U Update from Old data
        X eXit From Log Menu
        Z fuZzy scan

        Type in the single letter to make your choice.

             14.1 Append an Entry

             This option lets you append an entry.  It is the same as the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 54  


             Alt-A logbook mode function key.

             14.2 Scan Log by Band

             This option lets you scan the logbook file and display  QSOs 
             made on a particular band.  

             14.3 Change Logbook File

             This  option lets you temporarily change the  logbook  file.  
             If you want to change it permanently, change it in the  LAN-
             LINK.SYS  file.  When you enter the new name, LAN-LINK  will 
             assume  that it is a filetype DBF. For example, if you  have 
             different logbooks for different operations on-line, such as 
             4X.DBF or W8.DBF, you only need answer 4X in response to the 
             question  to  change to the 4X.DBF logbook.   In  accordance 
             with the dBASE convention, you cannot use any filetype other 
             than DBF.

             14.4 Find Date

             This  option  lets  you locate and  move  the  highlight  to 
             entries for a particular date.  If no entries are found  for 
             the  desired date, the first entry after that date  will  be 
             highlighted.   Note  you can also scan for parts of  a  date 
             such as "90/01" for the first entry in January 1990.

             14. 5 Edit Log Entry
             
             You  invoke this option to edit the highlighted entry.  This 
             function is the same as that invoked with the Alt-E function 
             key.

             14.6 Find an Entry

             This option lets you find an entry by its number.  It is the 
             same as the Alt-F logbook mode function key.

             14.7 Import-Convert Log

             This  option lets you import logs from earlier  releases  of 
             LAN-LINK (up to and including Version 1.56). It can also  be 
             used  to  import  a  log generated  by  the  PC-HAM  CONTEST 
             program.

             14.8 Help Function Keys

             This option brings up a menu for the function keys.

             14.9 Scan Log by Mode

             This option lets you scan the logbook file and display  QSOs 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 55  


             made using a particular mode.  

             14.10 Print Log

             This  command prints the contents of the logbook file  in  a 
             formatted manner to the printer. 

             14.11 Scan Log by Call

             This command displays the contents of the logbook file in  a 
             formatted manner on the screen. It requests the callsign  of 
             the log entry to be displayed. If you  want  to see  entries  
             for  particular calls or parts of  call,  enter those   call 
             or  parts of calls. Valid entries are G, G3,  G3Z  etc.   If  
             you  want  to  see every entry in the log,  don't  use  this 
             command,  use the Page Up and Page Down keys from  the  Main 
             Log menu.

             14.12 Update from Old data

             This  option is identical to the Append option  except  that 
             the  date  and time are not entered for  you  automatically. 
             You'd  use this option to manually enter old data  into  the 
             logbook.

             14.13 Exit From Log Menu

             This  option lets you exit from the Log Menu.   It  provides 
             the same function as the Alt-X key.

             14.14 Fuzzy Scan

             This  option allows you to scan the callsign or the  comment 
             field (your choice) for a character string.  For example you 
             could scan the comments field for all entries with the  word 
             "Joe".  You could scan the callsigns for all calls with  the 
             suffix of "ZCZ".

        15.0 Message Menu

        The Message Menu provides the following choices. 

                  B BBS Command Files
                  C Current Messages
                  N leave Note
                  O Old Messages
                  T Time tag
                  V View Message

        Type in the single letter to make your choice.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 56  


             15.1 BBS Command Files

             This option shows you a list of the BBS command files on the 
             default directory.  In other words, all files with the  file 
             extension of '.BBS'.  

             15.2 Current Messages

             This  option shows you a list of the outgoing messages  that 
             have not been sent. In other words, all files with the  file 
             extension of '.OUT'.  

             15.3 View Message

             This  feature allows you to view messages in  the  computer.  
             After  depressing the key you will be prompted for INcoming   
             or  OUTgoing (I/O) messages.  If you request 'I'  (Incoming) 
             messages  you  will  see  the  messages  addressed  to  your  
             callsign.   If  you request 'O' (for OUTgoing) you  will  be 
             presented  with  a  directory window containing  a  list  of 
             messages.  Move the cursor down to the desired message,  and 
             touch  the  'Enter' key. If you don't want to  view  any  of 
             them, then move the cursor down to a blank line. If you have 
             more messages than one screen full, use the Pgdn (Page Down) 
             key to show the next screen full.

             15.4 Leave Note

             This feature allows you to leave a note for another  station 
             on the LAN in your system.  It works in the manner described 
             in Section 8.
             
             15.5 Old Messages

             This feature shows you a list of the messages that have been 
             sent.  In other words, all files with the file extension  of 
             '.OLD'.

             15.6 Time Tag

             This option is used to place a date time header on a message 
             file  previously prepared by a word processor.  The name  of 
             the file must be in the format 'CALLSIGN.OUT' (For  example, 
             G3ZCZ.OUT).   It requests the callsign of the message  file.  
             It then opens a new file, writes the header to the new  file 
             and copies the contents of the original '*.OUT' file to  the 
             new one.  When all is done, the original filename is changed 
             to '*.BAK' and the new one becomes '*.OUT'.






        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 57  


        16.0 TNC Menu

        The TNC Menu provides the following choices. 

                  D Set TNC Date/Time
                  F Flush TNC Buffer
                  I Initialize TNC
                  M calls Monitored List
                  S Show Connect Status
                  Q Change CQ Text
                  X Change CTEXT
                  Y Activate TNC Mailbox
                  Z Deactivate TNC Mailbox

        Type in the single letter to make your choice.

             16.1 Set TNC Date/Time

             This  feature puts the TNC into the Command Mode  and  loads 
             the date into it from the computer time of day clock. 

             This command does not work on the TNC1.

             16.2 Flush TNC Buffer

             This  option  is used to flush the program's  outgoing  text 
             buffer and that of the PK-232.  When used with other TNCs it 
             will only flush contents (if any) of the outgoing buffer  in   
             the PC.

             16.3 Initialize TNC

             This feature sets up the defaults for the TNC from the  file 
             LAN-LINK.SYS.   If  you have put batteries in the  TNC,  you 
             should normally only have to run this command when you first 
             power  up  the TNC or change the  batteries.   However,  the 
             batteries must be removed initially since they are there  to 
             retain the default settings of the TNC (particularly the PK- 
             232).  Once the initialization is complete, you can  replace 
             the  batteries but leave the TNC on since the  battery  pro-
             vides power to the RAMs after the TNC power is turned off.

             It  will also set the date and time within the TNC from  the 
             computer  clock, and, when it has loaded  the  configuration 
             file,  may prompt you to set the TNC Terminal mode.  If  you 
             are  using a TNC1 or a TNC2, it will not prompt you  because 
             it assumes that they only operate on VHF packet. If you  are 
             using a KPC-2, you may select 'H' or 'V', and of course,  if 
             you have a PK-232, you may choose any of the options.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 58  


             16.4 Show Calls Monitored List

             This  feature performs the same operation as Function Key  5  
             (F5). 

             16.5 Show Connect Status

             When you are in the Packet Communications Mode, this command 
             lets you see the state of the connection.  It will show  you 
             if  there  are any unacknowledged packets en route  to   the 
             other  station.   If  you  have been  sending  text,  it  is 
             advisable   to  use this command before you disconnect,   to  
             ensure that all the data has been received and  acknowledged 
             by   the other  party.   You may use this command in  either  
             the  TNC Command or the TNC Converse Mode.  

             In a multiconnect situation, it will show you the status  on 
             all the I/O channels. 

             You  may  also use this command to reset the  status  window 
             display  after  a relink or any other event  which  was  not 
             reflected in the status window.

             16.6 Change CTEXT

             This  feature allows you to change the message that will  be 
             received by another packet station when it connects to  you. 
             Refer to the 'CTEXT' command in the TNC manual.

             16.7 Activate TNC Mailbox

             This option allows you to activate the Mailbox in your  TNC.  
             You  use it to read your mail, or before shutting  down,  if 
             you have not set the shut down mode to 5.

             When  reading  your  TNC Mailbox mail,  you  must  type  the 
             commands listed in your TNC manual.

             16.8 Deactivate TNC Mailbox

             This  option  allows you to deactivate the Mailbox  in  your 
             TNC.  You use it after you have read your mail.

        17.0 AMSAT-OSCAR Menu

        This menu allows you to configure the KAM, MFJ1278 or the  PK-232 
        to  copy signals from AMSAT-OSCAR Spacecraft  telemetry  beacons.  
        The following options are available.

                  A UoSAT ASCII Beacon
                  B Phase 3 RTTY Beacon
                  C SAREX Menu   (only   if  you  are   in   the   Packet  


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 59  


                          Communications Mode)

        Type in the single letter to make your choice.

             17.1 UoSAT ASCII Beacon

             This  option is only available on the PK-232. It  configures 
             the  PK-232 for receiving UoSAT 1200 Baud ASCII  signals  in 
             the following manner.

             ASCII
             AB 1200
             VHF ON         (Bell 202 tones)
             RXR OFF
             TXR OFF
             WI ON          (850 Hz shift)

             Signals from UoSAT-OSCAR 11 may be copied in this configura-
             tion.  Note that although UoSAT-OSCAR 11 transmits Bell  202 
             compatible  tones, the data sense is reversed.   A  hardware 
             modification is required in the PK-232 to reverse  the sense 
             of  the  data at the modem output BEFORE it  passes  to  the 
             digital section of the unit.  

             17.2 Phase 3 RTTY Beacon

             This  option configures the KAM, the MFJ1278 and the  PK-232 
             for  receiving  the  AMSAT-OSCAR 10 and  13  RTTY  telemetry 
             beacons in the following manner.

             BAUDOT
             WI OFF         (170 Hz shift)    [ KAM : SH 170]
             TXR OFF
             RXR OFF
             RB 50          (50 baud)
             USOS OFF       (Unshift on space off)

             17.3 SAREX Menu

             This menu is only active in the Packet Communications  Mode.  
             It is designed for use with the Shuttle Amateur Radio Exper-
             iment  (SAREX) and the packet radio Microsats.   Apart  from 
             the  Attack  Mode, it can also be used as a  diagnostic  LAN 
             tool for monitoring LAN traffic.  

                  17.3.1 Attack Mode ON/OFF

                  If the Attack Mode is set, this option will cause  LAN-
                  LINK  to  issue  a connect request to  the  SAREX  Call 
                  whenever  a  packet sent to or from it is  heard.   The   
                  mode is cleared when the connect is made (and does  not 
                  retry out) or when the 'A' option is selected a  second 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 60  


                  time, or when the Alert Call is cleared.  If this  mode 
                  is  enabled, the Alert/SAREX Call prefix shown  in  the 
                  Status Window will indicate accordingly.

                  A  happy face will be displayed next to the '>'  before 
                  the call once the connect has been achieved.

                  Be careful using this feature, as it has the  potential 
                  to  cause a great deal of QRM.  It can also be  cleared 
                  by another station connecting to you and telling you to 
                  ':QRT:'.  In the SAREX configuration you are  listening 
                  on one channel while transmitting on an other. If  this 
                  feature  was  used  on  a  simplex  channel   (everyone 
                  transmits  and listens on the same channel) aimed at  a 
                  DX-pedition,  there  is a potential  lockout  mode,  in 
                  which any one station sending a connect request to  the 
                  desired/SAREX  call  will  trigger the  other  ones  on 
                  frequency  who will in turn trigger the first. If  this 
                  pile  up situation occurs, I hope the  DX-station  will 
                  QSY and leave the automatic stations to do their thing.  
                  IN  any event, if you use this feature and  cause  QRM, 
                  anyone  can connect to you with the callsign of the  DX 
                  station (as a pirate) and shut you down.  You will then 
                  not get the coveted DX QSL.

                  17.3.2 Change SAREX Call

                  This option lets you temporarily change the SAREX call.  

                  17.3.3 SAREX Packets Capture to Disk ON/OFF

                  This option allows you to configure LAN-LINK to capture 
                  to  disk  any packets addressed to or  from  the  SAREX 
                  callsign.  A [S] will be displayed in the status window 
                  when  this option is active.  The capture to disk  file 
                  is opened by a packet header containing the SAREX call, 
                  and closed by another packet header not containing  the 
                  call.   When  the  file is open, the  [S]  will  blink.  
                  Packet  headers are considered to be lines with  a  '>' 
                  character in them.  LAN-LINK thus considers both of the 
                  lines below as packet headers.

                  N4QQ*>G3ZCZ
                  N4QQ BBS>

                  If you use this feature for monitoring BBS traffic, the 
                  BBS   prompt lines ('E.G. N4QQ BBS>') will not be  cap-
                  tured to disk.  Do not get your SYSOP to remove the '>' 
                  from the prompt line, or the ZAP feature will then  not 
                  work.

                  A  happy  face will be displayed in the [S]  after  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 61  


                  SAREX call has been heard.

                  If you want to see an ORBITER menu, temporarily  change 
                  the SAREX call to be the same as your call and bring up 
                  the AMSAT-OSCAR Menu.

             17.4 SAREX Orbiter Features 

             You  need the ROBOT EPROM for this menu to actually do  any-
             thing.  The  EPROM may be available from The  Radio  Amateur 
             Satellite Corporation (AMSAT) for DX-pedition use.

             In  the Orbiter mode, LAN-LINK does not scan  incoming  text 
             for  the  'CONNECTED' and 'DISCONNECTED' messages  when  the 
             SAREX  Robot  is active.  This inhibits the  bells  and  the 
             capture-to-disk.   It also means that the Robot must be  OFF 
             for any :Q: code uploads or downloads to occur.

             17.4.1 Status Window Display

             A flashing '>>' appears in the status window when the  SAREX 
             robot is  active.  The SAREX Configuration boots up assuming  
             that the SAREX Robot is active (Default).

             17.4.2 Alt-O Function key.

             The Alt-O Function Key brings up the Orbiter menu.  This  is 
             a faster route than the  'Esc O' sequence.

             17.4.3 The Meta Beacon

             The  Meta beacon is loaded from the contents of one  of  the 
             META.00n files.  These files may be created by the  LAN-LINK 
             editor.  When  loading, LAN-LINK will insert a pass  charac-
             ter  (^V) into the text before a carriage return, so as  not 
             to  end the packet before at least 240 characters,  and  not 
             more  than 255 characters have been output to the TNC.   The 
             maximum  number  of characters that can be loaded  into  the 
             Meta  beacon  is 1776.  The maximum number of packets  in  a 
             Meta  beacon is 7.  You can also end force a  hard  carriage 
             return  or 'end of packet' in the Meta beacon by  using  the 
             '\' (backslash) character, which will not be transmitted.


             17.4.4 SAREX Orbiter Menu

             The following commands are active in the Orbiter Menu.

                  17.4.4.1 Activates Beacons/SAREX Robot.

                  This  option activates the SAREX Robot and  loads  Meta 
                  Beacon.   This  command is designed for  use  when  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 62  


                  SAREX is returned to the regular frequency.

                  17.4.4.2 Set QRZ/QSL Beacon Interval

                  This  command  allows you to change the  beacon  timer.  
                  The default value is 120.

                  17.4.4.3 Set SAREX Call. 

                  This  command  allows  you to change  the  SAREX  call.  
                  Don't  use  this command on orbit (its for  ground  use 
                  only)

                  17.4.4.4 Turn SAREX ROBOT OFF

                  The  Robot must be turned On and Off this way  to  syn-
                  chronize LAN-LINK to the TNC.  When the Robot is turned 
                  OFF the following commands are sent to the TNC by  LAN-
                  LINK.

                     USERS 1
                     |A
                     RO OFF
                     CMSG OFF
                     NO OFF

                  17.4.4.5  Set SAREX ROBOT Heard Count

                  This command lets you set the Heard Count number.

                  17.4.4.6 Show I/O Status

                  Shows who is on each stream, the SAREX Robot state, the 
                  number of USERS, the beacon timer value, the metabeacon 
                  timer value and the CTEXT.

                  17.4.4.7 ChecK Count

                  Shows both heard and worked counts.

                  17.4.4.8 List Heard Calls

                  Lists calls of the last few stations heard.

                  17.4.4.9 Load Metabeacon

                  This command loads the Metabeacon.  You will be prompt-
                  ed  for  a  text file number in  the  META.00n  series.  
                  Enter a number 1-9 corresponding to  META.001-META.009. 
                  The  0  value is file META.010. Note the  delays  after 
                  loading the file to allow the TNC to stabilize.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 63  


                  17.4.4.10 Show Worked Calls

                  Shows the last 35 or so calls worked.

                  17.4.4.11 Turn SAREX ROBOT ON

                  The SAREX Robot must be turned On and Off via the menu.  
                  When the Robot is turned ON the following commands  are 
                  sent to the TNC by LAN-LINK.

                     USERS 9
                     CONOK ON
                     CMSG ON
                     RO ON
                     NO ON

                  17.4.4.12 Stop Metabeacon

                  This  command stops the Meta beacon.   When  activated, 
                  the  contents of the beacon are dumped to  the  UNPROTO 
                  address  (default  SAREX)  by the TNC,  rather  like  a 
                  regular  BBS  dumping packets when a  user  disconnects 
                  abnormally.
                  
                  17.4.4.13 Set Metabeacon Interval

                  This  command allows you to set the Meta Beacon  timer. 
                  It  will be loaded into the TNC the next time that  the 
                  Meta Beacon is loaded.  Even though loaded into the TNC 
                  immediately, it does not take effect till then.

                  17.4.4.14 Set SAREX ROBOT Worked Count

                  Lets you set the number.

                  17.4.4.15 Set Connect TeXt

                  This is the text (CTEXT) that will be transmitted to an 
                  incoming   station  when the ROBOT mode is  off.   This 
                  option lets you set up a new text string to go with the 
                  QSO number.

                  17.4.4.16 Selects Silent Mode

                  This command turns off the beacons, the SAREX Robot and 
                  also  stops the Meta beacon.  This command is  designed 
                  to be used just before any prearranged packet activity.

                  17.4.4.17 Restart TNC
                  
                  This command RESTARTs the TNC, loads the date from  the 
                  computer's  clock and turns the 'EC OFF'.  It seems  to 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 64  


                  have  no  effect on the SAREX ROBOT and  counters,  but 
                  does kill the Meta beacon.

                  17.4.4.18 Capture QSL/QRZ Calls
                  
                  This  command initiates the log-to-disk  operation.  It 
                  turns the capture-to-disk 'on' and sends the  following 
                  commands  to the TNC :- 'DA', 'SERW',  'SERH','MW',MH'.  
                  When  the calls have stopped  scrolling,  use  Function 
                  key 1 to turn the capture-to-disk off.

        18.0 Parameter Menu

        The Parameter Menu provides the following choices.  

        B Turn Beacon Mode ON/OFF      0 Change Band/Mode
        C Clear Connect Count          1 Change BBS Parameters             
        D Turn Digipeat Detect ON/OFF  2 Change Callsigns                  
        E Turn Command Echo ON/OFF     3 Change Directories                
        F Stay Connected after BBSZapp 4 Enter Common Calls                
        I Turn Beacon ON/OFF           5 Change File Names                 
        K Change Keyboard Beep Count   6 Change LAN-LINK Parameters        
        L Turn Ctdsk ON/OFF            7 Change PC Communications Params   
        M Set Message Count            8 Change Colors                     
        N Turn NODE Drop Link ON/OFF   9 Change SAREX Parameters          
        P Turn Printer ON/OFF          U Update LAN-LINK.SYS
        Q Turn QTC Snatch ON/OFF       V Verify Changes
        R Turn :QSP: Relay Flag ON/OFF W Change Scan Words
        S Turn Sound ON/OFF               
        T Turn Contest Mode ON/OFF    
        X Turn DCD Flag ON/OFF         ! Zapp BBS on Next Beacon
        Y Turn BBS Snatch ON/OFF       + Turn Misc. Flag ON/OFF
        Z Turn Time Id. ON/OFF        

        The colors used for the option letter differentiate between those 
        options that are "remembered" in the SYS file and those that  are 
        only set temporarily for the session.

        Type in the single letter to make your choice.
             
             18.1 Turn Beacon Mode ON/OFF
             
             This command toggles the beacon option for the automatic  CQ 
             caller  in the AMTOR and Packet Communications Modes.   When 
             it  is active a [B] will be displayed in the status  window. 
             In  this mode, the Automatic CQ sequence will  resume  after 
             the  AMTOR link is dropped or a Packet  Communications  Mode 
             disconnect.    

             In  the  Beacon Mode, the last few logbook entries  will  be 
             displayed in the logpage window which overlays the  outgoing 
             text window at the bottom of the screen.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 65  



             In the Packet Mode, the CTEXT message is the only  transmis-
             sion  from you that the other station will receive, so  make       
             it good and don't forget to set 'CMSG ON'.

             In  the AMTOR Mailbox/Beacon Mode, the contents of the  LAN- 
             LINK.TXT file will be transmitted to the station who  called 
             you.   The capture-to-disk will then be turned on to  record 
             one  transmission from that station.  The QSO will  then  be 
             logged  to  the  logbook file.  Don't forget  to  check  the 
             entries  in  the LAN-LINK.LOG and text in  the  LAN-LINK.RUN 
             files in case the computer made a mistake in recognizing the 
             call sign of the other station.

             THE  BEACON MODE IS DESIGNED TO ENCOURAGE PEOPLE TO QSY  OFF 
             THE  CROWDED PACKET HF CHANNELS. DO NOT USE IT ON A  CROWDED 
             HF CHANNEL OR ON AN ACTIVE VHF CHANNEL.  IF YOU DO, YOU WILL 
             SOON FIND THAT OTHER STATIONS HAVE SET THEIR TNCS TO  REJECT 
             YOUR  PACKETS, AND YOU WILL NOT WORK ANYBODY, YOU WILL  JUST 
             BE A SOURCE OF QRM AND WILL BE KNOWN AS SUCH.

             THE  MODE IS ALSO DESIGNED FOR ROBOT BEACONS FOR THE  HIGHER 
             FREQUENCIES.  FOR EXAMPLE IF YOU LEAVE IT RUNNING ON 6 OR 10 
             METERS YOU NEVER KNOW WHEN A SHORT OPENING WILL ALLOW A  QSO 
             TO  SOME  PART OF THE WORLD,  A DX CONTACT  YOU  WOULD  HAVE 
             OTHERWISE  MISSED.    DO NOT LEAVE IT RUNNING ON  20  METERS 
             WHEN THE BAND IS OPEN.  FURTHER APPLICATIONS ARE IN  METEOR-
             SCATTER AND OTHER "EXOTIC" MODES OF COMMUNICATIONS.

             If you are using this Mode in a special event station or DX-
             pedition  you may type characters into the transmit  buffer, 
             while the other station is sending to you.  When he, she  or 
             even  it  turns  it back to you,  you  will  transmit  those 
             characters before the sign-off sequence. 

             In both the Packet and AMTOR communications modes, the robot 
             may  be shut down by stations connecting to you and  telling 
             you to QRT.

             18.2 Clear Connect Count         

             You  use  this option to reset the PACKET and  AMTOR  Beacon 
             Mode  "connect  has taken place indicator"  and  QTC  Snatch 
             count.   These  are  flashing [C] and [Q]  displays  in  the 
             status  window.  Whenever someone else connects or links  up 
             to  you  the [C] display will be  incremented.   The  number 
             shown with the 'C' is the number of connects that have taken 
             place since the Indicator was last reset.  If a 'happy face' 
             is  flashing  along  with the connect  count,  your  "target 
             station"  was  amongst those connecting. The  [Q]  indicator 
             alerts  you  to the fact that LAN-LINK tried to  connect  to 
             another  station  after  recognizing your  call  in  a  mail 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 66  


             beacon.   Both  are  reset  by  this  option.   If  you  are 
             monitoring  Packet traffic on a channel, you may not  notice 
             that a connect has previously taken place.  These indicators 
             alert  you to check the contents of the Incoming  mail  file 
             ('yourcall.OUT') for any incoming messages.  

             If the 'Q' count is much greater than the 'C' count you  may 
             be  copying a beacon from a station that you cannot  connect 
             with directly.

             18.3 Turn Digipeat Detect ON/OFF

             This option toggles the digipeat display command on and off.  
             If  the Digipeat Display is active, any  signals  digipeated 
             through  you will be stored to the LAN-LINK.RUN file  and  a 
             'beep'  will  be sounded for each packet  being  digipeated.  
             The status display window will also contain a [D].

             18.4 Turn Beacon Control ON/OFF

             This  option toggles the LAN-LINK Handshake  features.  When 
             they  are on (default), the Connect handshake message  

                         [ZCZ] *** LAN-LINK 1.58> 

             will  be transmitted on incoming connects. The  beacon  text 
             and time will be controlled by LAN-LINK as a function of the 
             messages you have posted on your system.  When they are off, 
             LAN-LINK  does not do anything to your beacon, nor  does  it 
             transmit the handshake.

             18.5 Turn Command Echo ON/OFF       

             This option toggles the 'Command ECHO ON/OFF' flag.  If  the 
             Command  Echo  flag is set, the commands and  (contents  of) 
             files  that LAN-LINK sends to the TNC will be  displayed  in 
             the  outgoing  window.  Set this flag to  see  how  LAN-LINK 
             commands the TNC in the different modes.

             18.6 Change Keyboard Beep Count  

             LAN-LINK  counts the number of characters entered on a  line 
             at  the  keyboard.  When it gets to a preset value  it  will 
             beep, signaling you to start a new line. This option changes 
             the value that the keyboard beep counter is compared with to 
             sound the audio signal. 

             18.7 Set Message Count           

             As  an  alternative to Function Key 8 (F8) or  Alt-D,  using 
             this  option  will  also load a QTC 'Mail'  list  into  your 
             Packet  Communications  Mode Beacon and  initiate  a  beacon 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 67  


             transmission every 30 minutes (Refer to the BTEXT command in 
             the  TNC manual).  If no messages are present, or  the  only 
             message   is   to  you  (incoming   or   snatched),   beacon 
             transmissions   are  inhibited.   This  conforms   to   good 
             operating practice on crowded Packet channels.

             18.8 Turn NODE Drop Link ON/OFF     

             When connecting via NET/ROM, the normal way of operating  is 
             to  disconnect  if  the  connect  attempt  fails.   You  may 
             configure the NET/ROM connect attempt flag to stay connected 
             at the node where the failure occurred.  Use the normal mode 
             when  trying  to get through on a known path, and  the  stay 
             alive mode when exploring NET/ROM circuits.

             18.9 Turn Printer ON/OFF             

             This  option  toggles  the printer on  and  off.   When  the 
             printer  is turned on, any incoming data will be printed  in 
             real  time.  If you intend to print files received  at  1200 
             baud in the Packet Communications  Mode, use a print spooler 
             or  you may lose data.  The printer is automatically  turned 
             off in the Packet Mode when a disconnect occurs.

             18.10 Turn QTC Snatch ON/OFF         

             This option toggles the QTC Snatch flag on and off.  If  the 
             QTC  Snatch flag is enabled, LAN-LINK scans the contents  of 
             packets  appearing in the Inwindow on the screen  while  the 
             terminal  is  disconnected.  Should it recognize  the  three 
             text  strings 'LAN-LINK',  ':QTC:', and 'your  callsign'  in 
             the  contents  of  a packet, it will then  issue  a  connect 
             request  to  the  callsign  of  the  LAN-LINK  station  that 
             originated the beacon transmission.  If the connect is made, 
             the  other station will send you the  message  automatically 
             which  LAN-LINK  will "capture to disk".  The  connect  will 
             time out and terminate a few minutes later.

             The  normal  connect  request will be  made  DIRECT  to  the 
             station.  If you expect messages from stations you can  only 
             connect  with via a digipeater, place the path in your  LAN-
             LINK.DIR  directory file.  It should be there anyhow if  you 
             connect  to  the  station regularly.  For  example,  if  you 
             expect  messages  from  4Z4ZB  whom you  can  only  work  if 
             digipeated via 4X1AA then place an entry like

                                4Z4ZB   4Z4ZB V 4X1AA

             in the LAN-LINK.DIR  file.

             The  QTC  Snatch  leaves your messages  in  a  message  file 
             <yourcall>.OUT.   It  is  triggered by the first  >  in  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 68  


             initial  connect response of LAN-LINK 1.55R> (note the  '>') 
             and  terminated by the 'over' at the end of the message  ea. 
             G3ZCZ/W8>  (note the '>'). If you train stations  not  using 
             LAN-LINK who want to leave you messages to trigger your QTC-
             Snatch, by transmitting the following unaddressed packet

                              LAN-LINK :QTC: <yourcall> 

             your  system will connect to them.  (For example to leave  a 
             message for me, they would send  

                               LAN-LINK :QTC: G3ZCZ 

             as  an  unaddressed  packet  [in  Converse  Mode  when   not 
             connected, or in their beacon text].)

             If they then send you a '>' on a line by itself, followed by 
             the  message  itself, and terminated by another '>'  as  the 
             last  character  of the line, the message will end up  in  a 
             message  file rather than in the LAN-LINK.RUN file  and  you 
             can  scan it fast using Alt-M (Message Scan  Menu  Options).  
             It  goes without saying that the message itself  should  not 
             contain  the  '>' character.  If it does, by  the  way,  the 
             first part of the message will be in the message file, while 
             the remainder will be in the LAN-LINK.RUN file.

             18.11 Turn :QSP: Relay Flag ON/OFF  

             This  option  toggles the Store and  forward  Message  Relay 
             Capability of your system on and off.  If the Message  Relay 
             Capability is active (toggled on), any one who connects  can 
             store a message in your system using the ':QSP:  <callsign>' 
             NC/L command. If the Message Relay Capability is not  active 
             anyone  who  attempts to ':QSP: a message'  will  receive  a 
             ':QNO:  1' "error" message.  The status display window  will 
             show a [R] when the Message Relay Capability is active.  The 
             default  state  for the Message Relay Capability  is  loaded 
             from the LAN-LINK.SYS file.

             When the Store and forward capability is active, the  suffix 
             'R' will be added to the 

             '[ZCZ] *** LAN-LINK 1.58' ie., '[ZCZ] *** LAN-LINK 1.58R' 

             message  received  by anyone connecting to  your  system  to 
             notify  them that they can store messages.  In  this  manner 
             they  don't  have  to try to leave a message  and  then  get 
             ':QNO:'  error  message  to find out  that  the  feature  is 
             toggled off.

             Remember,  if  you  configure your  computer  to  store  and 
             forward  messages,  you have a moral obligation  to  deliver 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 69  


             them.

             18.12 Turn Sound ON/OFF             

             This  option toggles the sound on and off.  If the sound  is 
             off,  a flashing indicator will be displayed in  the  Status 
             Window.   When the sound is toggled on again, a  chime  will 
             sound to verify the audio.

             18.13 Turn Contest Mode ON/OFF

             This option first toggles the Contest Mode.  If the  Contest 
             Mode  is active, the word 'TEST' and the number of the  next 
             QSO will be displayed in the status window. When the Contest 
             Mode is toggled on, this command then prompts you to set the 
             starting  QSO number and the standard message that  will  be 
             transmitted  as  part of the exchange of messages  during  a 
             contest.   The QSO number will be incremented each time  you 
             log a contact.  

             There are two special character sequences that you can enter 
             in  the  contest text string.  If you enter   a  double  '#' 
             sign, as in '##', it will be replaced by the QSO number when 
             the text is transmitted.  You may also use '#1' to represent 
             the callsign of the station being worked in the contest text 
             string.   For  example, use the following  entries  for  the 
             following contests;

             '##1 UR ##A' ... in the Sweepstakes,
             '5905'  ... in the WAZ,
             '59 MD' ... in the ARRL DX, and
             '59 ##' ... in the WPX.

             As  an example, if I (W3/G3ZCZ) was in the Sweepstakes  con-
             test,  and my Contest text line was,

             '##1 UR ##A W3/G3ZCZ 68 MDC'.  

             If  the next QSO number is 345, and I am working KW3C,  LAN-
             LINK  would  transmit the following line when  I  touch  the 
             'End' key;

             'KW3C UR 345A W3/G3ZCZ 68 MDC'.  

             The contest feature is toggled off the next time you  select 
             this feature.

             Note  that  while  this does  give  you  some  semiautomatic 
             contest  operation  by  using  command  keys,  there  is  no 
             checking of callsigns for duplicates built into the program.  
             You may do that by using the Alt-S hot key.  



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 70  


             In  a contest, you enter the callsigns  and call  the  other 
             station  in  the normal manner, then use the  'End'  Key  to 
             transmit the exchange (QSO number and standard text).   LAN-
             LINK will only transmit the contest text in this manner.  If 
             you  want to add a 'K' or 'KN', you will need to put  it  in 
             the  contest  text string.  It is also advisable  to  use  a 
             different  log file for each contest to cut down the  search 
             time.   The contest QSO number increments each time you  log 
             the QSO (Alt-L).  

             You  may  put  the Contest Mode into automatic  if  you  are 
             operating AMTOR or packet.  To do so, use the Alt-O function 
             key.

             18.14 Turn DCD Flag ON/OFF          

             If you are using a KAM or a PK-232 then this flag should  be 
             set to ON.  If you are using another TNC, if you can  jumper 
             the TNC so that pin 8 on the RS-232 interface changes  state 
             when  connected,  do  so and set this flag to  ON.   If  you 
             can't, then set this flag to OFF.  If this flag is OFF,  the 
             multiple  connect  modes will not work so don't  attempt  to 
             invoke them.  If this flag is OFF, the words '*** CONNECTED' 
             and  '***  DISCONNECTED'  when seen in  the  LAN  may  cause 
             spurious apparent connects and disconnects in LAN-LINK.

             18.15 Turn BBS Snatch ON/OFF        

             If the BBS Mail Snatch is enabled, when a BBS sends a packet 
             announcing 'Mail', if your callsign is in the first line  of 
             that  message, LAN-LINK will issue a connect request  (again 
             via the path in LAN-LINK.DIR) to that BBS.  When  connected, 
             it will act as if you have initiated a ZapBBS command.   The 
             Zap counter will be incremented each time a  BBS Mail Snatch 
             takes place.

             A  typical KAM display which triggers a BBS Mail Snatch  for 
             any of the calls listed below follows.

             N4QQ>MAIL/V [09/03/89  18:49:24]:
             LstMsg# 19428 Mail: N4FG KL7VZ WA6IEL N7DVA W4TNX G3ZCZ 

             Note if the BBS Mail beacon has an extra line in it (between 
             the  header and the list of calls) as follows, the BBS  Mail 
             snatch will not work.

             N4QQ>MAIL/V [09/03/89  18:49:24]:
             BBS Serving Silver Spring Md.
             LstMsg# 19428 Mail: N4FG KL7VZ WA6IEL N7DVA W4TNX G3ZCZ 

             If a message is posted for any call containing the character 
             string  "N4FG" such as N4FGA, N4FG will respond to the  mes-


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 71  


             sage.  This gives rise to a lock out situation, because N4FG 
             will  respond  to the beacon, go through  the  sequence  de-
             scribed  in the Zapbbs section and disconnect.   The  beacon 
             message will not be cleared because it was not read, so  the 
             next  mail beacon from the BBS will contain the call  N4FGA, 
             and N4FG will once again respond to it.

             Should  you be unlucky and happen to be in  this  situation, 
             disable the BBS Snatch flag and set a Periodic Event to Zap 
             your   BBS   sometime   in  the   middle   of   the   night.  
             Alternatively,  when you come into the shack and the BBS  is 
             in use, set the 'Zapp BBS on Next Mail Beacon' parameter  to 
             ON (See Section 18.32).

             18.16 Turn Time Id ON/OFF         

             This option is only active in the PK-232.  It allows you  to 
             determine   if  the  callsign  sequence  transmitted   using 
             Function key 3 (F3) will contain a date/time stamp.  If  the 
             Id is set ON a date/time stamp will be transmitted.

             18.17 Turn Automatic Capture-to-Disk Flag ON/OFF         

             This option allows you to turn the automatic capture-to-disk 
             ON and OFF.

             18.18 Change BBS Parameters      

             This  sub-menu allows you to change the BBS  Parameters,  as 
             described in the following paragraphs.

                  18.18.1 Local BBS Callsign

                  This option lets you change the call of the local  BBS.  
                  This is the call that LAN-LINK will show in the  prompt 
                  for the 'Zap' command.

                  18.18.2 Mail-Snatch Trigger Word

                  You  can  set the Mail-Snatch Trigger in the  BBS  Mail 
                  beacon.   Most  BBS's use word 'Mail' and a  string  of 
                  calls  to indicate the presence of messages.   If  your 
                  BBS uses something else, you may customize LAN-LINK  on 
                  this line to tell it what word your BBS uses.

                  Note that if your BBS uses 'QTC' you may end up calling 
                  yourself if you disconnect while traffic is flowing  on 
                  the LAN.

                  18.18.3 Read Request Command

                  This is the command LAN-LINK issues to the BBS during a 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 72  


                  Zap  sequence to request your mail.  The default  value 
                  is RM for Read Mine. On a WA7MBL BBS you may change  it 
                  to  VM for a Verbose Read of the full  packet  headers.  
                  On a W0RLI BBS you may change it to RN to only  request 
                  new messages.  If you do change it, use the 'V'  option 
                  in the Parameters Menu to make sure it is correct.   If 
                  it isn't correct, the Zap BBS feature will not work.

                  18.18.4 Read Bulletin Request Command

                  This is the command LAN-LINK issues to the BBS during a 
                  Zap  sequence to read bulletins identified by the  scan 
                  words. The default value is R for Read. On a WA7MBL BBS 
                  you  may change it to V for a Verbose Read of the  full 
                  packet  headers.  On a W0RLI BBS you may change  it  to 
                  RH.

             18.19 Change Callsigns           

             This  sub-menu allows you to change the Callsign  and  AMTOR 
             SELCAL, as described in the following paragraphs.

                  18.19.1 Callsign

                  The  default  callsign  is G8BTB.  Please  do  not  use 
                  G8BTB.   Replace  G8BTB   with yours.  You  may  use  / 
                  characters  if  you wish.  This is the call  sign  that 
                  will be used in the non packet modes.  You may thus use 
                  "portable  designators"  such  as  G3ZCZ/A,   G3ZCZ/W3, 
                  W3/G3ZCZ or G3ZCZ/4X, which you cannot do in Packet.  

                  This  is  the call that will be monitored  for  in  the 
                  Digipeat  Monitoring  Mode.   In this  Mode,  which  is 
                  toggled  on  and off by the selection of the  D  Option 
                  included  in  the Parameter Menu  (PK-232  only),    if 
                  someone  uses  you as a digipeater while  you  are  not 
                  connected  to anyone else, the event will be logged  to 
                  disk.   This  Mode will only work if your  callsign  as 
                  stored in this line is a valid (uppercase only)  packet 
                  callsign.  

                  For  example, in the PK-232, if the callsign  is  G3ZCZ 
                  then  the  sequence  >G3ZCZ> will be  recognized  as  a 
                  digipeat and the event logged.  Thus 4X6AA*>G3ZCZ>4Z4ZB 
                  would be logged as a digipeat event.  

                  Store  your callsign using UPPERCASE characters if  you 
                  want  the DIGIPEAT DETECT option to work  (EA.  G3ZCZ).  
                  If  you  use lower case (ea. g3zcz),  recognition  will 
                  never  take place. The TNC automatically converts  case 
                  to upper case in the non packet communications modes.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 73  


                  If  you are using an SSID (e.g. G3ZCZ-8) in the  Packet 
                  Communications  Mode, you should enter the  whole  call 
                  INCLUDING the SSID.

                  18.19.2 The SELCAL

                  This  is your AMTOR SELCAL. LAN-LINK will try to  guess 
                  it  and  prompt you with a SELCAL configured  for  your 
                  callsign.   If you want a different one, overwrite  the 
                  prompted version.

                  If  you are not using a PK-232 or KAM or  the  MFJ1278, 
                  the SELCAL must still be in the Configuration file.

                  18.19.3 The PacketCluster Call

                  This option allows you to change the PacketCluster Call 
                  without connecting to it.
                  
             18.20 Change Directories         

             This  sub-menu allows you to change the Directories used  by 
             LAN-LINK, as described in the following paragraph.

                  18.20.1 QBM Download Directory

                  This is the directory the :QBM: command will search  to 
                  find  a  file to be downloaded.  The default  value  is 
                  \LAN-LINK\FILES\.   Set them up using DOS.  If  you are 
                  using   a  hard  disk,  put  LAN-LINK  in  a   LAN-LINK 
                  subdirectory.  Note: that last '\' MUST be present.

             18.21 Enter Common Calls         

             Each  time you call another station, LAN-LINK  remembers  it 
             (up  to the last 16).  When you update the SYS  file,  these 
             calls that you use most commonly will be saved to disk.  You 
             can use this option to add calls, delete calls or edit calls 
             in the list.  Use the 'Delete' key to delete a call.

             18.22 Change File Names          

             This  sub-menu allows you to change the default  file names 
             used by LAN-LINK, as described in the following paragraphs.

                  18.22.1 VHF Logbook File (VHF.DBF)

                  This  is  the name of the file to be used as  your  VHF 
                  Packet logbook.  





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 74  


                  18.22.2 HF Logbook File (HF.DBF)

                  This  is  the name of the file to be used  as  your  HF 
                  logbook.   It  is  used for  all  modes,  including  HF 
                  packet.

                  18.22.3 Path Directory File (LAN-LINK.DIR)

                  This  is  the  name  of the  file  used  as  your  call 
                  directory.  

                  18.22.4 Brag Tape (LAN-LINK.TXT)

                  This is the name of the file used as your brag tape. 

                  18.22.5 QBU Upload File Name (QBU-TX.BAT)

                  This  is the name of the batch file used to initiate  a 
                  QBU. 

                  18.22.6 QBU Download File Name (QBU-RX.BAT)

                  This  is the name of the batch file used when  a  :QBU: 
                  command is received from a remote station. 

             18.23 Change LAN-LINK Parameters 

             This sub-menu allows you to change the LAN-LINK  Parameters, 
             as described in the following paragraphs.


                  18.23.1 Change CQ Text

                  This  feature allows you to change the contents of  the 
                  CQ text message string. This is the message string that 
                  is  transmitted along with the CQ call.  Think of  this 
                  message as a CQTEXT line.  

                  18.23.2 Set the Default Band

                  The  default  value is 2 for 2 Meters.  Use  the  Meter 
                  value for the band to keep the display correct.  It  is 
                  displayed  in  the  status  window.   If  you  normally 
                  operate  on  another band change the default  value  to 
                  reflect your usual default state.

                  18.23.3 Set the Default Transmitter Power

                  The default value is 10 for 10 watts.  It is  displayed 
                  in  the  status  window.  If your  transmitter  uses  a 
                  different  power  level  change the  default  value  to 
                  reflect your usual default state.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 75  



                  18.23.4 Set CQ delay time Seconds

                  This  option  allows you to change the  time  (seconds) 
                  that the LAN-LINK waits for a response after a CQ  call 
                  until  the following one is transmitted.   The  default 
                  value (in minutes and seconds) is loaded from the  LAN-
                  LINK.SYS file.  

                  18.23.5 Set CQ delay time Minutes

                  This  option  allows you to change the  time  (minutes) 
                  that the LAN-LINK waits for a response after a CQ  call 
                  until  the following one is transmitted.   The  default 
                  value (in minutes and seconds) is loaded from the  LAN-
                  LINK.SYS file.  

                  18.23.6 Set Number of lines in a Non Contest CQ Call

                  This option allows you to change the number of lines in 
                  a CQ call from the default value of 3 to any number you 
                  wish.   Note that in the contest mode, this option  has 
                  no effect.  This parameter is not remembered when  LAN-
                  LINK is terminated, so if you want to use a value other 
                  than  3, you will have to set it each time you  operate 
                  this program.

                  18.23.7 Set Shut Down Mode (QRT Flag)

                  This  option  allows  you to customize  the  shut  down 
                  sequence  of the TNC.  You have the choice of QRT,  QRV 
                  and  QRV + CTEXT Toggle as described in  the  following 
                  sections.

                       18.23.7.1 QRT 

                       Turns  the  TNC into a VHF  Digipeater  and  turns 
                       CONOK  OFF (CFROM NONE for the PK-232).   In  this 
                       condition the TNC will reject connect requests.

                       18.23.7.2 QRV

                       Allows you to stay alive on turnoff. It will  send 
                       MON  OFF  (MON  0 for the PK-232) to  the  TNC  at 
                       shutdown  without touching  CONOK/CFROM  {PK-232}, 
                       and  at turn on. You will then have to  initialize 
                       the terminal and Communications Mode after reading 
                       your mail.  Connects should then be logged at  the 
                       time you read the mail, not at the time they  took 
                       place.  




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 76  


                       18.23.7.3 QRV + CTEXT TOGGLE

                       This  is  the same as the QRV state  but  CMSG  is 
                       toggled  on/off.   When stations  connect  to  you 
                       while  LAN-LINK is active, they will  not  receive                
                       the CTEXT message.  When other stations connect to                
                       you  while  LAN-LINK  is  not  active,  they  will                
                       receive the CTEXT message

                       18.23.7.4 BBS

                       This option lets you activate the PBBS in the  TNC 
                       when you close LAN-LINK. It inhibits the PBBS when 
                       you bring LAN-LINK up the next time.

                       18.23.7.5 SOLO

                       This option puts the TNC in the SOLO mode when you 
                       shut  down,  so as not to fill the buffer  in  the 
                       TNC.

                       18.23.7.6 BBS+SOLO

                       This option combines the two previous ones.

                   Set this value as follows, 

                   0 = QRT,                
                   1 = QRV, 
                   2 = QRV + CMSG toggle,  
                   3 = BBS, 
                   4 = SOLO, and 
                   5 = BBS+SOLO.

                  18.23.8 Set Default Users

                  This  option  allows you to set the maximum  number  of 
                  multiple users that can be connected to your TNC at the 
                  same  time, and to configure the default start up  mode 
                  of  the program.  If this parameter is set to  1,  LAN-
                  LINK will configure itself to the single user mode, and 
                  set the maximum number of users to 9. If this parameter 
                  is set to any number other that 1, LAN-LINK will assume 
                  that  value  to  be  the  maximum  number  of   allowed 
                  connects,  and  configure itself in the  Multiple  user 
                  Mode (equivalent to the TNC Menu Option 0).

             18.24 Change PC Communications Parameters

             This sub-menu allows you to change the Communications Param-
             eters  between the PC and the TNC, as described in the  fol-
             lowing paragraphs.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 77  



                  18.24.1 The Communications Port

                  This  is the default Communications port.  The  default 
                  value  is 1. You may set it at any value between 1  and 
                  4.  If you only have one serial port in your  PC,   set 
                  the parameter to '1' even if your card is configured as 
                  COM2.   LAN-LINK will ALWAYS assume COM1 for  a  single 
                  card.  

                  The Com3 and Com4 port addresses are as follows.

                           Port Address IRQ
                           Com3   3E8    4
                           Com4   2E8    3

                  18.24.2 The Terminal Baud Rate

                  This Parameter tells LAN-LINK what baud rate the TNC is 
                  set  to.  This  is the baud rate  on  the  RS-232  line 
                  between the TNC and the computer.  Valid baud rates for 
                  LAN-LINK  are 300, 1200, 2400, 4800, 9600  and  19,200.  
                  If you specify something else LAN-LINK will default  to 
                  1200.  

                  You  may  experience  problems when  using  baud  rates 
                  greater  than 1200.  It depends on the CPU  clock  rate 
                  and the I/O card in the PC.  LAN-LINK scans the  incom-
                  ing text constantly, something which requires time.  My 
                  PK-232,  when used with my XT Clone at 10MHz, does  not 
                  like  baud  rates faster than 2400, and  sometimes  not 
                  even that. The   PK-232 seems to drop the first charac-
                  ter  of some lines at 4800 baud.   Use 1200  until  you 
                  have tested and are sure that a faster one will work.

                  This  program has been tested on a TNC2 and an  MFJ1278 
                  using  a  terminal baud  rate of 9600 baud  and  worked 
                  correctly.  It  also works correctly with a KAM at 2400 
                  Baud.

                  18.24.3 TNC Data Bits

                  You can set the number of data bits on the RS-232  line 
                  between  the computer and TNC to 7 or 8.  Use 7 with  a 
                  TNC 2 if you have problems with Greek characters. 

                  Set this value to either 7 or 8.

                  18.24.4 TNC Parity

                  Use this parameter to set the Parity bit on the  RS-232 
                  line between the computer and TNC as described below.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 78  



                   0 = None, 1 = Odd, 2 = Even, 3 = Mark, 4 = Space.

                  18.24.5 Number of TNC Stop Bits

                  You can set the number of stop bits on the RS-232  line 
                  between  the computer and the TNC to 1 or 2.  Use 1  at 
                  all terminal (not packet) baud rates except 300.

                  Set this value to 1 or 2.

             18.25 Change Colors

             This  option lets you change the default colors.  A  display 
             of all of the combinations is shown on the left side of  the 
             screen.  You will then be prompted to sequence through  each 
             window/message  color  that can be  customized.   Enter  the 
             number  shown  in  the combination window  followed  by  the 
             'Enter'  key  to set a value.  If you don't wish to  make  a 
             change, just press the 'Enter' Key.

             The following identifications are made to the color choices:
                  18.25.1   OutWindow Color

                  This  is the color of the text (typed at the  keyboard) 
                  in the outgoing window.

                  18.25.2   StatusWindow Color

                  This is the color of the Status Window.

                  18.25.3   PromptWindow Color

                  This is the color of most of the menus.

                  18.25.4   LogWindow Color

                  This is the color of the text in the log window.

                  18.25.5   InWindow Color

                  This is the color of the text in the window showing the 
                  incoming characters.

                  18.25.6   ScrollBackWindow color

                  This  is  the  color of the text  in  the  Scroll  back 
                  window.

                  18.25.7   MHWindow Color

                  This  is  the color of the text in  the  monitor  heard 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 79  


                  calls (MH) window.

                  18.25.8   Alarmwindow Color

                  This  is the color of the text in the Error  and  Alarm 
                  window.

                  18.25.9   BottomWindow Color

                  This is the color of the text in the prompt line at the 
                  bottom of the screen.

                  18.25.10  Emphasis Color

                  This  is the color of the emphasized text in  the  Menu 
                  windows.

                  18.25.11  Prompt Color

                  This  is  the  color of the prompt  text  in  the  Menu 
                  windows.

                  18.25.12  Option Color

                  This  is the color of selected option text in the  Menu 
                  windows.

                  18.25.13  Connected Text Color

                  This  is the color of the text in the  incoming  window 
                  when connected in the packet communications modes.

                  18.25.14  Computer Color

                  This is the color of the computer generated text in the 
                  outgoing  window when the Command Echo Flag  option  is 
                  enabled.

                  18.25.15  VHF Header Color

                  This  is  the  color of the VHF  Header  lines  in  the 
                  Incoming window when not connected.

                  18.25.16  HF Header Color

                  This  is  the  color  of the HF  Header  lines  in  the 
                  Incoming window when not connected.

                  18.25.17  Alert Call Color

                  This is the color of the packet header lines containing 
                  the  Alert  call  in  the  Incoming  window  when   not 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 80  


                  connected.   It is also the color of the  non-permanent 
                  Parameter Menu prompts.

                  18.25.18  Outgoing Text Color

                  This  is the color of the outgoing text echoed  in  the 
                  Incoming window in the AMTOR Communications Mode.

                  18.25.19  Multi I/O Stream Color[1]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 1.

                  18.25.20  Multi I/O Stream Color[2]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 2.

                  18.25.21  Multi I/O Stream Color[3]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 3.

                  18.25.22  Multi I/O Stream Color[4]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 4.

                  18.25.23  Multi I/O Stream Color[5]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 5.

                  18.25.24  Multi I/O Stream Color[6]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 6.

                  18.25.25  Multi I/O Stream Color[7]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 7.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 81  


                  18.25.26  Multi I/O Stream Color[8]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 8.

                  18.25.27  Multi I/O Stream Color[9]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 9.

                  18.25.28  Multi I/O Stream Color[10]

                  This  is  the color of the text lines in  the  Incoming 
                  window  in the Multiconnect Mode when connected to  I/O 
                  stream 10.

             NOTE that LAN-LINK does not overwrite all existing  windows.  
             Thus  if you want to be sure of seeing the  changed  colors, 
             save  the  color changes using the Update option,  and  then 
             exit from and reload LAN-LINK. 

             18.26 Change SAREX Parameters    

             This sub-menu allows you to change the SAREX Ground  Station 
             parameters, as described in the following paragraphs.

                  18.26.1 SAREX CallSign

                  This is the callsign of the SAREX station.

                  18.26.2 Change SAREX Capture to Disk File

                  This  option  lets  you change the name  of  the  SAREX 
                  Capture-to-disk  file.  Don't change file  names  while 
                  capture-to-disk  is  in progress (flashing [S]  in  the 
                  status  window), or the old one will stay open and  may 
                  not close properly when LAN-LINK is terminated, result-
                  ing in data loss.

             18.27 Update Configuration File

             Use  this  option to save the changes (permanently)  in  the 
             configuration file (LAN-LINK.SYS).

             18.28 Verify Changes             

             This feature lets you display how LAN-LINK was configured by 
             the  LAN-LINK.SYS file.  It also displays the state  of  any 
             flags  you have set/reset if they are not already  shown  in 
             the  Status  window or Parameter Menu.  YOU  SHOULD  USE  IT 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 82  


             AFTER  EDITING  THE  LAN-LINK.SYS FILE  TO  MAKE  SURE  THAT 
             EVERYTHING IS CORRECT.

             18.29 Change Scan Words          

             In  the ZAP BBS feature you can ask the program to scan  the 
             lines read from the BBS and if it sees any of the scan words 
             in  the line, it will queue a request for that  bulletin  by 
             number.   You  can only set 16 such Scan  words  (should  be 
             enough) and request up to 63 messages/bulletins at a time.  

             Use the 'Delete' key to delete a word from the list.

             NOTE  that  words that show up in the BBS  prompt  line  are 
             ILLEGAL.  For example if your BBS prompts you with

                                      N4QQ BBS> 

             then 'N4QQ' and 'BBS' should not be used as Scan Words.

             DON'T  LEAVE  A BLANK LINE IN THE SCAN WORD SECTION  OF  THE 
             CONFIGURATION FILE.

             18.30 Turn Misc. Flag ON/OFF

             The Miscellaneous Flag performs several different  functions 
             in the different Communications modes as follows.

                  18.30.1 All Modes:- Debug or state-sequence numbers

                  Shows  debug  or state-sequence numbers  in  left  hand 
                  corner of the status window.  These are used to  figure 
                  out what went wrong in the automatic sequences.

                  18.30.2 BAUDOT Mode:- Navy MARS Protocol Verify

                  When  the flag is set, and the BAUDOT Navy MARS  option 
                  is  enabled,  the  character  string  ':CR:'  will   be 
                  displayed  in the outgoing window each time a  carriage 
                  return  character is received in the  incoming  window.  
                  Similarly,   every  time  a  line  feed  character   is 
                  received,  a ':LF:' will be displayed in  the  incoming 
                  window.  

                  You may use this feature to verify that another station 
                  is  sending files using the correct protocol.   If  you 
                  do,  make  sure that you tell the PK-232 not to  add  a 
                  line feed to incoming carriage returns by setting 'ALFD 
                  OFF'  in the Command Mode.  You will have to set  'ALFD 
                  ON'  again when you change communications modes or  all 
                  incoming lines will overwrite each other.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 83  


             18.31 Change Band/Mode

             This  option is used to set the band and radio mode  without 
             invoking the Log Menu. You use it when changing from  packet 
             vhf to an hf mode.

             18.32 Zapp BBS on Next Mail Beacon

             This  parameter causes LAN-LINK to Zapp your local BBS  next 
             time it beacons with a list of calls for which it has  Mail.  
             You use this when you want to upload a set of messages,  and 
             are  not sure if there are any messages waiting for  you  on 
             the BBS. A typical situation is where there are a lot of NTS 
             messages stacked up in the BBS.BBS file waiting to go.  This 
             parameter will be reset when the connect goes through, so if 
             the Zapp attempt failed, it will try again on the  following 
             Mail beacon.  This will not work in the Multi-user mode.

             18.33 BBS Zapp, Don't Disconnect After Sequence

             This  parameter  stops LAN-LINK from issuing  the  automatic 
             disconnect  when the Zapp sequence is over.  You can set  it 
             during  the Zapp sequence. Use it to stop the disconnect  if 
             the sequence gets out of sync with the messages, or if there 
             is  something interesting you wish to do to the  BBS.   This 
             parameter resets when the Zapp sequence terminates.

        19.0 Q Codes [NC/L]

        This  option  displays  help information about  the  use  of  the 
        Network Communications Language (NC/L) "Q" codes.

        20.0 Communications Modes

        This  menu  allows you to change the communications mode  of  the 
        TNC.   If  your TNC hardware cannot support  those  modes,  don't 
        bother to try them.  This is software not hardware, and in  spite 
        of  what  people  tell you, software can't  do  everything.   The 
        following communications modes are available.

                   V VHF PACKET
                   H HF PACKET
                   A AMTOR (STANDBY RECEIVE)
                   B BAUDOT (RTTY)
                   C MORSE (CW)
                   M AMTOR (ALIST [chirpcopy])
                   S ASCII (RTTY)
                   G SIGNAL
                   N NAVTEX

        Type  in the single letter to make your choice.  Don't forget  to 
        select the correct Radio port on the PK-232.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 84  



             20.1 VHF PACKET

             This  is the 1200 baud VHF Packet Mode. LAN-LINK will  opti-
             mize the TNC link parameters for this mode.

             20.2 HF PACKET

             This is the 300 baud HF Packet Mode. LAN-LINK will  optimize 
             the TNC link parameters for this Mode.

             20.3 ASCII (RTTY)

             This is the ASCII RTTY Mode. LAN-LINK will configure the TNC 
             parameters for this Mode at 110 baud.

             20.4 BAUDOT (RTTY)

             This  is the BAUDOT RTTY Mode. LAN-LINK will  configure  the 
             TNC parameters for this Mode at 45 baud.

             20.5 MORSE (CW)

             This is the CW Mode. LAN-LINK will configure the TNC parame-
             ters for this Mode at 20 wpm (10 wpm for the KAM).

             In this Mode the ALT-D Key will disengage the receive  speed 
             lock  inside the PK-232 to facilitate locking  onto  another 
             signal  and  Function Key 8 (F8) will turn  the  transmitter 
             off.

             20.6 AMTOR (STANDBY RECEIVE)

             When  you select the AMTOR Standby Mode you are placed  into 
             the  'Standby  Receive' Mode.  If you are in  AMTOR  Standby 
             Mode,  you  will  not  be able to  display  signals  of  the 
             Chirpcopy  Mode  (which means that you will not be  able  to 
             display a QSO in progress).

             The  Alt-D  Key or Function Key 8 (F8) toggles  between  the 
             AMTOR ARQ and the ALIST communications modes.

             20.7 AMTOR (ALIST [chirpcopy])

             If  you  want to read the mail on an existing AMTOR  QSO  in 
             progress, select the AMTOR ALIST or Chirpcopy Mode.  

             The  Alt-D  key or Function key 8 (F8) toggles  between  the 
             AMTOR ARQ and the ALIST communications modes.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 85  


             20.8 SIGNAL

             Use  the 'G' option to select the 'SIGNAL' Mode.   Read  the 
             PK-232  documentation carefully to understand how this  mode 
             works.  Once the PK-232 has identified the digital signal it 
             is  tuned  to,  use the Communications Mode  Select  Menu  a 
             second  time  to select the relevant mode and then  set  the 
             baud rates and shift to display the data if necessary.

             20.9 NAVTEX

             Use the 'N' option to select the 'NAVTEX Mode.  Read the PK-
             232   documentation  carefully to understand how  this  Mode 
             works.  

        21.0 Terminal Mode Menu

        This menu allows you to set the Terminal Configuration Mode.  The 
        Terminal  Menu  provides  different choices  depending  on  which 
        communications mode you have selected.

             21.1 Packet Terminal Menu

             The  Packet Terminal Mode of operation will be shown in  the 
             Status window at the top of the screen.  If you are  reading 
             the mail on a station, the callsign of that station will  be 
             shown  next  to the word "MAIL".  If you  are  connected  to 
             someone,  the call (and path) will be shown prefixed by  the 
             "*>" sequence.

             In  the Packet Communications Mode, you are  presented  with 
             the following choices. 

              B Change Packet Baud Rate
              C CQ/Beacons
              E Everything
              M Read the Mail
              S Just My Station (Solo)
              T All Traffic
              0 Multiple User Connects
              1 Single User Connects
              F Conference
              R Conference Bridge On/Off

             Type in the single letter to make your choice.

             21.1.1 Change Packet Baud Rate

             In the PACKET Mode you may change the RF baud rate   between 
             300, 600, 1200 and 2400 baud.  




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 86  


             21.1.2 CQ/Beacons

             In  this  Mode, you will see CQ and BEACON  packets  on  the 
             channel.  (This corresponds to 'MONITOR 1'on the PK-232). 

             This Mode only works on the PK-232 and the KAM.

             21.1.3 Everything

             You can set the TRAFFIC Mode to 'Everything'. It corresponds 
             to 'MONITOR 6' on the PK-232.

             21.1.5 Read the Mail

             You  can  read the mail on a BBS or other  station  and  get 
             bulletins without connecting to that station yourself.   You 
             use  this Mode to do so.  You will be prompted for the  call 
             whose  packets you wish to monitor.  Remember to  enter  the 
             call of the station sending the packets, not the call of the 
             one  receiving them.  (This corresponds to 'MONITOR  0'  and 
             'MBX'  callsign). This Mode only works without  showing  the 
             packet  headers  on  the PK-232.  On  the  other  TNCs  the 
             headers will also be displayed.

             You  can also use this command to monitor both  sides  (read 
             the mail) on a QSO on a busy packet channel.

             You may want to turn the Digipeat Data Display Mode off when 
             reading the mail.

             21.1.6 Just My Station (Solo)

             In  this Mode, you will only see messages addressed to  you.  
             You  will only get messages from people who connect to  you. 
             (This corresponds to 'MONITOR 0' or 'MONITOR OFF').

             21.1.7 All Traffic

             In this Mode you will see all of the data packet traffic  on 
             channel.   You  can use this Mode to check that the  TNC  is 
             working. (This corresponds to 'MONITOR 4' or 'MONITOR ON').  

             21.1.8 Single User Connects

             This is the normal one-on-one Mode of operation ('USERS 1').

             21.1.9 Multiple User Connects

             When you are in a Multiple Connect Mode, an asterisk will be 
             shown in the status window next to the word 'PACKET'.   Each 
             I/O  stream  will  show up in the Inwindow  in  a  different 
             color.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 87  



             LAN-LINK supports two multiple connect modes, Individual and 
             Conference.

             An  extract of an actual 'off the air' CRT display  (showing 
             received  text  only) in a multi-user mode is  shown  below.  
             Note  each line of text as received by the TNC  is  prefixed 
             (by the PK-232) with the I/O channel number and callsign  of 
             the station its connected to.

             1:4X4IL: *** CONNECTED to 4X4IL via 4X4IC, 4X6JP
             0:4X4IC: joe do u read?
             2:4Z4ZB: *** CONNECTED to 4Z4ZB
             1:4X4IL: Look for me on PR via 4X6JP 73s and Shalom.
             2:4Z4ZB: GE JOE I WILL DIS THEN U CAN GO VIA THE REP....>
             1: *** DISCONNECTED: 4X4IL via 4X4IC, 4X6JP
             0:4X4IC: UNPROTO  CQ
             2:4Z4ZB: GO AHEAD BOYS...DE ALON..>
             0:4X4IC: 
             2: *** DISCONNECTED: 4Z4ZB

             This is the normal Multiconnect Mode as described in the TNC 
             manual.   Here you  are connected to up to 10  stations  and 
             will send different traffic to each of them.  Each time  you 
             wish  to  send something to a particular station,  you  must 
             select  the I/O channel the station is connected  on  before 
             typing the text or sending the file.

             The stream change character for all TNCs in the VHF multiple 
             connect modes is '|' ($7C). In the KAM, it is '\' on HF  and 
             '|' on VHF.  They are both on the same key but one is in the 
             shift  case.  Be careful on HF as the '\' shows up  in  file 
             directories  and  confuses the computer.  THESE  VALUES  ARE 
             HARD  CODED  INTO LAN-LINK. IF YOU USE SOMETHING  ELSE,  THE 
             COLOR  AND  OTHER MULTIPLE CONNECT FEATURES  WILL  NOT  WORK 
             CORRECTLY.

             You  select the I/O channel using the Alt-N key  and  moving 
             the  cursor  to  the desired stream, or by  typing  the  '|' 
             character  followed by (in the TNC) the channel  letter/num-
             ber.  For example to do it manually, if you are connected to 
             G8BTB  on I/O channel 0 and to G3ZCZ on I/O channel 1,  then 
             to  talk to G8BTB you would type '|0' before any  text,  and 
             similarly  to send something to G3ZCZ you would type a  '|1' 
             before  the  text you're going to send me.  If you  are  not 
             using a PK-232, read the TNC manual to determine if the  I/O 
             streams  are identified by numbers or by letters.  The  TNC2 
             standard configuration uses letters (|A etc.).

             Use the Alt-N key and move the cursor up and down to  select 
             the I/O channel automatically.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 88  


             21.1.10 Conference

             In  the Conference Mode on the other hand,  everything  that 
             you  type  at the keyboard is automatically  transmitted  to 
             each  station that you are connected with.  Thus if you  are 
             linked  to two stations each line will be packeted twice  by 
             the  TNC.  You don't have to worry about sending  the  wrong 
             thing to the wrong person, as they will all get the stuff. 

             You  enter  this  Mode by selecting the 'F'  option  in  the 
             Terminal Menu.  You terminate this Mode by selecting the '1' 
             option.

             You  connect in the usual manner using Alt-C or the  Connect 
             Option in the Call Menu.  You MUST WAIT FOR A CONNECTION  TO 
             BE  ESTABLISHED OR TIME OUT before attempting to connect  to 
             the  next  station.  If you do not, you will  get  an  error 
             message back from the TNC.

             In  the Conference Mode, as the same text is transmitted  on 
             all I/O channels, the throughput will be reduced.  Slow down 
             your  typing speed or use short packets.  Should  you  check 
             the link status or call monitored list, you may not be  able 
             to  get  back into the Converse Mode if you  have  too  many 
             packets outstanding. If that happens, wait a while and  then 
             try  to  set the Converse Mode with Function Key  10  (F10).  
             You  may have to try it a few times, depending on  how  good 
             your links are.

             DON'T  TRY TO SEND A FILE IN THE CONFERENCE MODE, IT IS  NOT 
             DESIGNED FOR IT. KEEP THE PACKETS SHORT. 

             BE ALSO WARNED THAT IF YOU USE THE CONFERENCE (BRIDGE)  MODE 
             ON  BAD LINKS (SUCH AS CROWDED HF CHANNELS AND  OTHERS  WITH 
             LOTS  OF RETRIES), THE KEYBOARD MAY SEEM TO LOCK  UP,  WHILE 
             LAN-LINK  WAITS  FOR SPACE IN THE TNC BUFFER TO  OUTPUT  THE 
             TEXT.
             
             The Conference Mode will only work in the PK-232 if  DCDCONN 
             is  set to ON.  So if you are using a PK-232, LAN-LINK  will 
             do it for you when you enter the Conference Terminal Mode in 
             case you forgot or/and haven't set the LAN-LINK.SYS file  to 
             include   the  line  'DCD  ON'.   At  the  same   time   set         
             LAN-LINK.SYS  default  states  to show the  calls  of  other 
             stations  on  each incoming line in the  Multiconnect  modes 
             (read the TNC manual on how to do this).

             The Conference Mode will only work in the TNC2 if DCDCONN is 
             jumpered so that Pin 8 of the RS-232 Interface changes state 
             when you connect to someone else.  If you get error messages 
             and see the characters '|J' on your screen, then the  jumper 
             probably isn't set.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 89  



             The Conference Mode does not work on the TNC1.

             In  the  Conference  Mode,  if  any  one  of  the   stations 
             disconnects,  the TNC will return to the Command  Mode,  and 
             you must use Function Key 10 (F10) to return to the Converse 
             Mode before you type another character of text.

             21.1.11 Conference Bridge On/Off

             This option toggles the Conference Bridge on and off. In the 
             Bridge Multiconnect Mode you are acting as a central switch.  
             You  can  link together up to 10 stations  in  one  multiway 
             connection.  In this Mode any packets arriving on any stream 
             are echoed to all other streams that you have 'connects'  on 
             except the one that they came in on.  Anything you type will 
             be sent to all connected streams.

             In  this  manner, all stations will not see their  own  text 
             echoed  back.  Each line of text output by LAN-LINK in  this 
             Mode  will contain the callsign of the  station  originating 
             the  packet. Your packets will contain your call as  entered 
             in  line 1 of the LAN-LINK.SYS file.  Thus for  example,  if 
             your  call was KB8RP/4X and normally shows up in the  packet 
             header as KB8RP here it will show in the data as KB8RP/4X.

             Just remember that the Bridge puts out a lot of packets,  so 
             do  multiway connects on a quiet frequency.  You must be  in 
             the  Conference  Mode  to  turn  the  bridge  on,  and   any 
             disconnect  will take the bridge down.  Should that  happen, 
             toggle  it on again.  A bridge will be shown in  the  status 
             window whenever the Conference Bridge is up.

             21.2 AMTOR Terminal Menu

             In the AMTOR Communications Mode, you are presented with the 
             following choices. 

              C Force Break [ACHG]
              F Start Mode B [FEC]
              L Force LETTERS case
              M Read the Mail [ALISTEN]
              O Override ROBOT/Mailbox
              S Standby Receive [ARQ]
              R Set ROBOT/Mailbox
              W CW Identification

             Type in the single letter to make your choice.

             21.2.1 Force Break [ACHG]

             This  option forces a changeover or 'break in'.  If for  any 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 90  


             reason  you want to interrupt the other station you  send  a 
             'BREAK' signal in software this way.

             21.2.2 Start Mode B [FEC]

             This option places the terminal into the FEC Transmit  Mode. 
             This  puts  you  on  the air,  anything  you  type  will  be 
             transmitted.  Function Key 10 (F10) does the same thing.

             21.2.3 Force LETTERS case

             This  option  lets  you force the  PK-232  receiver  to  the 
             letters  case  if for some reason you appear to  be  in  the 
             numbers case.  It will return you to the Converse Mode.

             21.2.4 Read the Mail [ALISTEN]

             This option lets you read the Mail on a QSO.  Unfortunately,  
             when you tune in a chirping AMTOR QSO in the ARQ or  Standby 
             Mode you won't get any copy on the QSO in progress.  You can 
             however read the mail on one by entering the ALISTEN Mode.  

             21.2.5 Override ROBOT/Mailbox

             This  option lets you temporarily override the ROBOT  BEACON 
             and chat to a station that has linked to the ROBOT.  Use  it 
             after the message in LAN-LINK.TXT has been sent, namely when 
             the other station is sending a message to you.

             21.2.6 Standby Receive [ARQ]

             This option returns you to the ARQ Standby Mode. You must be 
             in this Mode to receive signals from another station who  is 
             calling  you.   When  you  tune for  CQ  calls,  they  sound 
             somewhat like fast RTTY with a ringing sound similar to  the 
             connect  alarm  used by LAN-LINK (but at  a  faster  ringing 
             rate).

             21.2.7 Set ROBOT/Mailbox

             This  option lets you turn on the Mailbox during  a  regular 
             AMTOR  QSO so that the other station can leave a message  or 
             download  a  file remotely. You must only use  it  when  the 
             other station is sending text.

             21.2.8 CW Identification

             This  option is used to send a CW identification.  The  CWID 
             is sent in the FEC Mode.  

             The  identification  consists  of  the  sequence  'DE  <your 
             callsign>' where your call sign is that entered into the PK-


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 91  


             232 as  'MYCALL'.

             You  use  this  feature  if your  license  requires  you  to 
             identify in Morse code as well as in the operating mode.  

             21.2.9 Set ROBOT Infinite Delay

             You  use  this  option  to  prevent  the  Robot  from   ever 
             transmitting  when  not linked. In the  normal  manner,  the 
             Robot counts down the CQ delay parameter, and, when it  gets 
             to  0 puts a CQ call on the air.  If the Infinite  Delay  is 
             set,  the CQ call will be inhibited. This option  thus  puts 
             the  Robot into an indefinite wait mode where it  thinks  it 
             has sent out a CQ call and is waiting for a reply.

             You would use this Mode if you want to set up a MailBox on a 
             known frequency for some group or organization.

             21.3 Baudot Terminal Menu

             In  the Baudot Communications Mode, you are  presented  with 
             the following choices. 

              B Set Baud Rate
              F Select Shift
              N NAVY MARS Message Protocol
              U USOS Off
              S SELCAL On/Off
              W CW Identification

             Type in the single letter to make your choice.

             21.3.1 Set Baud Rate

             This feature allows you to set a desired communications baud 
             rate  directly.  You will be prompted to enter  the  desired 
             rate.  Use this command to avoid having to shift through too 
             many intermediate states, if for example, you want to make a 
             direct change from 45 to 100 baud.

             21.3.2 Select Shift

             This  feature lets you select Wide (850 Hz) or  narrow  (170 
             Hz)  shift  directly.  The PK-232 will copy 170  Hz  signals 
             using its internal 200 Hz circuitry.  If you have a KAM, you 
             may also select the Commercial Shift (425 Hz).

             The  shift is displayed in the status window at the  top  of 
             the screen. It is shown as 'W', 'N' or 'C' for wide,  narrow 
             or commercial respectively. 




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 92  


             21.3.3 NAVY MARS Message Protocol

             The Navy Mars option toggles the Navy MARS Mode on and  off.  
             This  feature is only present on the PK-232.   When  active, 
             the feature provides the following protocol.

             21.3.3.1  Any  Carriage  Return  or  Enter  (CR)  from   the 
                       keyboard  is  sent as CR, CR. (two  sequential  CR 
                       characters.

             21.3.3.2 In  a file transmission lines are terminated  by  a 
                       CR,CR,LF (Line Feed) sequence.

             21.3.3.3  In a file transmission, blank lines are sent as  a 
                       LF (without a CR).

             21.3.3.4  In  a  file transmission, a plus sign '+'  in  the 
                       file  is  replaced by a sequence of  12  "letters" 
                       characters.  There can be more than one + sign  on 
                       a line.

             21.3.3.5  In  a  file transmission, the sequence  'NNNN'  is 
                       transmitted followed by a sequence of 12 "letters" 
                       characters.  There can only be one 'NNNN' sequence 
                       on a line.

             When the NAVY MARS feature is active a [N] will be displayed 
             in the status window.

             21.3.4 USOS On/Off

             This  option toggles the Unshift on space (USOS) feature  on 
             and  off.   When  the USOS is on, the  TNC  reverts  to  the 
             letters shift each time a 'space' character is received.  It 
             helps when displaying noisy copy.

             If USOS is active, 'USOS' will be shown in the status window 
             at the top of the screen.  

             21.3.5 SELCAL On/Off

             This  command  key toggles the SELCAL feature  on  and  off.  
             When the SELCAL is activated, as shown in the status window, 
             the incoming text from the TNC is scanned.  When either  the 
             letters  "ZCZC" or 'your callsign' (as entered in line 1  of 
             the LAN-LINK.SYS file) is received the "capture-to-disk"  is 
             turned  on.  All subsequent text will be stored in the  LAN-
             LINK.RUN  file  until the letters "NNNN" are  received.   At 
             that time the "capture-to-disk" is turned off.

             You  may  use this feature when monitoring  commercial  RTTY 
             broadcasts  to  record news and other information,  or  when 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 93  


             calling CQ to start recording all incoming text and keep the 
             QSO on disk.

             You may use Function Key 1 (F1) to turn the capture to  disk 
             permanently  on  to override the automatic  turnoff  if  you 
             wish.

             21.3.6 CW Identification

             This  option is used to send a CW identification.   You  use 
             this if your license requires you to identify in Morse  Code 
             as well as in the operating mode.  

             The  identification  consists  of  the  sequence  'DE  <your 
             callsign>' where your call sign is that entered into the PK-
             232 as  'MYCALL'.

             21.4 ASCII Terminal Menu

             In the ASCII Communications Mode, you are presented with the 
             following choices. 

              B Set Baud Rate
              F Select Shift
              S SELCAL set/reset
              W CW Identification

             Type in the single letter to make your choice.

             21.4.1 Set Baud Rate

             This feature allows you to set a desired communications baud 
             rate  directly.  You will be prompted to enter  the  desired 
             rate.  Use this command to avoid having to shift through too 
             many intermediate states, if for example, you want to make a 
             direct change from 110 to 1200 baud.

             21.4.2 Select Shift

             This  feature lets you select Wide (850 Hz) or  narrow  (170 
             Hz)  shift  directly.  The PK-232 will copy 170  Hz  signals 
             using its internal 200 Hz circuitry.  If you have a KAM, you 
             may also select the Commercial Shift (425 Hz).

             The  shift is displayed in the status window at the  top  of 
             the screen. It is shown as 'W', 'N' or 'C' for wide,  narrow 
             or commercial respectively. 

             21.4.3 SELCAL On/Off

             This  command  key toggles the SELCAL feature  on  and  off.  
             When the SELCAL is activated, as shown in the status window, 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 94  


             the incoming text from the TNC is scanned.  When either  the 
             letters  "ZCZC" or 'your callsign' (as entered in line 1  of 
             the  LAN-LINK.SYS file) is received the  capture-to-disk  is 
             turned  on.  All subsequent text will be stored in the  LAN-
             LINK.RUN  disk file until the letters "NNNN"  are  received.  
             At that time the capture-to-disk is turned off.

             You may use Function Key 1 (F1) to turn the capture to  disk 
             permanently  on  to override the automatic  turnoff  if  you 
             wish.

             21.4.4 CW Identification

             This  option is used to send a CW identification.   You  use 
             this if your license requires you to identify in Morse  code 
             as well as in the operating mode.  

             The  identification  consists  of  the  sequence  'DE  <your 
             callsign>' where your call sign is that entered into the PK-
             232 as  'MYCALL'.

             21.5 CW Menu

             In  the CW Communications Mode, you are presented  with  the 
             following choices. 

              L Lock to Receive Signal
              S Set Morse Speed
              U Unlock Morse Speed

             Type in the single letter to make your choice.

             21.5.1 Lock to Receive Signal

             This option locks the PK-232 to the speed of the incoming CW 
             signal.

             21.5.2 Set Morse Speed

             This option lets you set the CW speed.

             21.5.3 Unlock Morse Speed

             This option unlocks the PK-232 from the incoming CW  signal.  
             It  performs the same task as the Alt-D option keys.  It  is 
             used  to  speed up capture of a new signal or to  break  the 
             lock when the PK-232 appears to have locked up at the  wrong 
             speed.

        22.0  eXit to DOS

        When  you  exit the program and return to DOS, if the  Shut  down 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 95  


        (QRT) flag is set to 0, the TNC is put into the VHF default  mode 
        in  which it rejects calls from any other stations.  (Read  about 
        the  'CFROM'  command in the TNC manual).  You can thus,  if  you 
        wish,  leave  it  powered, and if you also leave  the  VHF  radio 
        powered  up, you will be active as a digipeater, but at the  same 
        time  anyone trying to connect with you will receive a busy  sig-
        nal.  The MBX command (Reading the Mail) is also cleared at  this 
        time.

        If you want to leave the TNC set up to accept messages when  LAN-
        LINK is not active, customize the shut down state as described in 
        the Section 18.23.

        23.0 Hot Keys

        LAN-LINK  also  contains a number of "Hot" keys to allow  you  to 
        perform  common  operations with a minimum of key  strokes.   The 
        keys  perform  related  but  slightly  different  tasks  in  each 
        communications mode.  A list of those available is shown in Table 
        23.   Should you require any more hot keys, I suggest you use  an 
        external  program  with  a  Keyboard  Macro  capability  such  as 
        Borland's Superkey.

        Consider the action of each key in detail.
             23.1 Alt-A - Alert Call (Packet) and AMTOR ARQ call/talk

             In  the  Packet Communications Mode,  this  key  combination 
             performs the same task as the Alert Call option in the  Call 
             Menu.

             In  the  AMTOR  Communications Mode,  this  key  combination 
             performs the same task as the AMTOR ARQ call/talk option  in 
             the Call menu.

             23.2 Alt-B - Send Break/AMTOR Changeover

             In  the  Packet  Communications Mode,  activating  this  key 
             combination sends a 'BREAK' signal to the TNC.  Use this key 
             combination to get out of the TNC's transparent mode.

             In  the AMTOR Communications Mode, use this key  combination 
             to force a changeover.  You can type text into the  outgoing 
             buffer and then force a changeover without losing that text.

             23.3 Alt-C - Call/Connect to

             This  key  combination performs the same task  as  the  Call 
             option in the Call Menu.  






        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 96  


        Table 23 Summary of Hot Keys
        ____________________________________________________________________
        Hot Key                Communications Mode
             _______________________________________________________________
                Packet         AMTOR        BAUDOT/ASCII        CW
        ____________________________________________________________________
        A    Set ALERT Call ARQ Call/Talk     ------           ------
        ____________________________________________________________________
        B    Send 'Break'   Force Changeover  ------           ------
             to TNC
        ____________________________________________________________________
        C    Connect        ARQ Call          Call             Call
        ____________________________________________________________________
        D    Disconnect     Toggle Receive    Receive         Disengage
                            Modes             Mode            Speed Lock
        ____________________________________________________________________
        E    Enter Call     Enter Call and   Enter Call        Enter Call
                            Selcal         
        ____________________________________________________________________
        F          Flush TNC Buffer (all communications modes)
        ____________________________________________________________________
        H                      Display Help Screen
        ____________________________________________________________________
        J            Jump to DOS (all communications modes)
        ____________________________________________________________________
        K            Jump to DOS quick return (all communications modes)
        ____________________________________________________________________
        L          Edit Log Entry (all communications modes)
        ____________________________________________________________________
        M           Scan Message (all communications modes)
        ____________________________________________________________________
        N  Next I/O Stream
        ____________________________________________________________________
        O    Turn Robot ON  Turn Robot ON     ------           ------
        ____________________________________________________________________
        P         Turn Printer ON/OFF (all communications modes)
        ____________________________________________________________________
        Q    call QRZ       call QRZ in FEC   call QRZ         call QRZ
        ____________________________________________________________________
        R    Retry Connect    Retry last Call (entered).
             (not ZAP)
        ____________________________________________________________________
        S           Scan Logbook (all communications modes)
        ____________________________________________________________________
        X            Exit to DOS (all communications modes)
        ____________________________________________________________________
        Y    Zap PacketCluster 
        ____________________________________________________________________
        Z    Zap BBS        Drop Link after       Receive mode after  
                            sending contents       sending contents 
                            of buffer                 of buffer
        ____________________________________________________________________


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 97  


             23.4 Alt-D - Disconnect or Receive

             This key combination performs the same task as Function  Key 
             8 (F8) EXCEPT in MORSE and AMTOR. 

             In  Morse this key disengages the receive speed lock in  the 
             PK-232 to unlock the PK-232 from the last signal copied.  It 
             lets you lock onto another signal faster.

             In  AMTOR this key toggles the receive mode between ARQ  and 
             FEC signals (Qso's in progress and Cq calls).

             23.5 Alt-E - Enter Call

             This  key  combination performs the same task as  the  Enter 
             Call option in the Call Menu.  

             23.6 Alt-F - Flush TNC Buffer

             This key combination performs the same task as the Flush TNC 
             Outgoing buffer option in the TNC Menu.

             23.7 Alt-J - Jump to DOS

             This  key  combination lets you "Jump to a DOS  Shell".   It 
             performs  the  same function as the 'J' option in  the  Main 
             Menu.

             23.8 Alt-K - Jump to DOS, Quick Return

             This  key  combination lets you "Jump to a DOS  Shell".   it 
             performs  the  same function as the 'J' option in  the  Main 
             Menu.  When the command is executed, control is returned  to 
             LAN-LINK without the 'type exit to quit the shell sequence'.

             23.9 Alt-L - Edit Log

             This  key  combination performs the same task  as  the  Edit 
             option in the Log Menu. 

             23.10 Alt-M - Message Scan

             This  key combination performs the same task as the  Message 
             Scan choice in the Message Menu. 

             23.11 Alt-N - Next Stream

             In  the  Packet Communications Mode, if you  are  using  the 
             multiple  connect capability of LAN-LINK, this key  combina-
             tion  prompts  you to change I/O streams,  and  display  the 
             state  of the I/O streams showing which ones were last  used 
             to  send or receive something.  To change I/O streams,  move 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 98  


             the cursor to the desired stream then push the 'Enter'  Key.  
             The  calls  in the Next Stream window update  when  stations 
             connect   and  disconnect.  In the event of the  window  not       
             being correct, you may manually enter or delete calls  using      
             the  'Insert' Key to enter a call, and the 'Delete'  Key  to      
             remove a call.

             The data about the streams will be shown in the same  colors 
             as the multistream text colors.

             23.12 Alt-O - Turn Robot On

             This  key combination performs the same function as the  Set 
             ROBOT option in the AMTOR Terminal Menu. The hot key  combi-
             nation  however,  is  active in both the  Packet  and  AMTOR 
             communications modes.

             This  function  key also puts the Packet and  AMTOR  Contest 
             operation into automatic.

             23.13 Alt-P - Turn Printer ON/OFF

             This  key  combination  performs the same  function  as  the 
             toggle printer on/off option in the Parameter Menu.  

             23.14 Alt-Q - Call QRZ

             This key combination transmits the sequence 'QRZ QRZ QRZ  DE 
             YOURCALL'  and  turns the transceiver back to  receive.   In 
             AMTOR, it sends the sequence in FEC and adds the SELCAL.

             23.15 Alt-R - Retry Call/Connect

             This  key  combination performs the same task as  the  Retry 
             choice in the Call Menu. 

             23.16 Alt-S - Scan Log

             This key combination performs the same function as the  Scan 
             option in the LOG Menu.

             23.17 Alt-X - Exit to DOS

             This  key combination performs the same task as the Exit  to 
             Dos  choice  in  the Main Menu. It  exits  the  program  and 
             returns you to DOS.  

             23.18 Alt-Y - Zap PacketCluster

             This  key combination performs the same task as the  Packet-
             Cluster  choice  in the Call Menu. It connects  you  to  the 
             PacketCluster  and issues a 'SHOW/DX' instruction when  con-


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 99  


             nected.  

             23.19 Alt-Z - Zap BBS

             This  key combination performs the same task as the Zap  BBS 
             choice in the Call Menu. 

             23.20 Alt-= - Toggle Miscellaneous Flag

             This  key  combination performs the same function as  the  + 
             option in the parameters menu.

             23.21 End -  > +?  [Over]

             In  the Packet Communications Mode this command  sends  your 
             callsign  followed by the > and Line feed  characters.   You 
             may use this to signal 'OVER' in a packet contact.

             In  the  AMTOR Communications Mode this  command  sends  the  
             '+?'  sequence  of characters which is the  software  'OVER' 
             signal. 

             In  the  MORSE and RTTY (Baudot  and  ASCII)  communications 
             modes, this command lets you transmit the 'KN' sequence  and 
             returns  you  to the Receive Mode.  For example if  you  are 
             4X6AA and you are working G3ZCZ then you would use  Function 
             Key  3  (F3) to transmit the sequence 'G3ZCZ de  4X6AA'  and 
             this  key to send 'KN' and revert to receive.  You use  this 
             at the END of a transmission in any mode except Packet.

             If  you  have typed something into the 'type  ahead  buffer' 
             then  press  this key, the contents of the  buffer  will  be 
             transmitted followed by the turnover command.

             23.22 PgUp - Scrollback (Scrolls back incoming text)

             This  key lets you repeat the display of up to 255 lines  of 
             incoming text which has scrolled out of the incoming window.  
             You may print it or capture it to disk during the repeat.  

             A  small menu displays your options when showing the  scroll 
             back information.  You may move the menu window up and  down 
             with  the left and right arrow keys.  Use the 'ESC'  key  to 
             terminate the Scrollback Mode.

             You can save the contents scrollback buffer displayed on the 
             screen by turning the "Capture-to-Disk' on, and then writing 
             text to the window.  Anything written will be captured.   If 
             the  Capture-to-disk is ON before or during scrollback,  you 
             will get two copies of the text in the file.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 100  


             23.23 The Home Key

             The  Home Key will clear the window screen that  the  cursor 
             happens to be in at the time that the key was depressed, and 
             will then position the cursor at the top left hand corner of 
             that window.

             23.24 The Down Arrow Key

             The  Down  Arrow  Key toggles  the  Normal/Reverse  Sideband 
             command  in  all PK-232 communications modes  except  MORSE.  
             The sideband is depicted in the status window by the Up  and 
             Down arrows.  If the Down Arrow is showing, you are set  for 
             Lower Sideband (LSB) which is the one normally used.

             If you have reversed the sidebands a flashing Up Arrow  will 
             be displayed.

             If you set your transceiver to LSB you will be set correctly 
             for all modes.   

             For CW operation you may set your rig to the CW position and 
             ignore the sideband setting.  If you use FSK just set it  so 
             that it works for you.

             23.25 Shift/Baudrate Control Keys
             
             The  following keys are used to control the Shift  (Wide  or 
             narrow) and the Radio link Baudrate in the BAUDOT and  ASCII 
             communications  modes.  In the BAUDOT and  ASCII  communica-
             tions  modes all baud rates supported by the PK-232  may  be 
             selected.


                  23.25.1 RIGHT ARROW speeds up the baud rate.
                  23.25.2 LEFT ARROW slows down the baud rate.
                  23.25.3 UP  ARROW toggles the shift from Wide (850  Hz) 
                          to Narrow (170 Hz) and back.
                  23.25.4 DELETE toggles the USOS command (RTTY only).

                  In  the  CW  communications mode, the  left  and  right 
                  arrows change the CW speed by 1 wpm.

                  The  state of each of the above commands are  displayed 
                  in the status window at the top of the screen.  If USOS 
                  is active, 'USOS' will be shown.  The shift is shown as 
                  'W' or 'N' for wide or narrow respectively. 

             23.26 Control-Z (^Z)

             This  key  combination is used in the  Packet  Communication 
             Mode  to signal the end of a file or message,  when  loading 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 101  


             messages into another LAN-LINK system or into a BBS.  In the 
             AMTOR  Communications Mode, it is  automatically  translated 
             into  the sequence ' :EOF: +? ' which can be used to  termi-
             nate a message being stored in another LAN-LINK AMTOR  mail-
             box. 

        24.0  LAN-LINK Disk Files

        The following disk files are associated with the program.
                  LAN-LINK.COM
                  LAN-LINK.SYS
                    *.RUN
                  LAN-LINK.LOG
                  LAN-LINK.DIR
                  CONFIG.SYS
                    *.MBX
                    *.BBS
                  LAN-LINK.001 .. LAN-LINK.010
                  QBU-RX.BAT
                  QBU-TX.BAT
                  LAN-LINK.QTA

        Consider each of them in turn.

             24.1  LAN-LINK.EXE

             This is the program.  You activate it from DOS by typing the 
             word  LAN-LINK  followed by ENTER in the  normal  manner  of 
             invoking DOS commands.

             24.2  LAN-LINK.SYS

             This  file contains the configuration information  for  both 
             the  program and the TNC.  YOU MUST EDIT IT before  you  run 
             the   program   on  the  air  the  first  time.    Use   the 
             customization  options  in the parameters menu to  make  the 
             changes.

             The contents of first few lines of the default file together 
             with an item number are shown below.

             1.   Callsign
             2.   Selcal 
             3.   CQ Text
             4.   Band
             5.   Power
             6.   CQ Delay (seconds)
             7.   CQ Delay (minutes)
             8.   :QSP: Message Relay Flag
             9.   PC Serial Communications Port Number
             10.  TNC Type
             11.  PC to TNC Baud Rate


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 102  


             12.  VHF Log Book File    
             13.  HF Log Book File    
             14.  Capture-to-Disk File name (spare/not used in 1.58)
             15.  Path Directory File name
             16.  Brag Tape File name
             17.  BBS Snatch Mail Trigger Word
             18.  QTC Snatch Flag
             19.  BBS Snatch Flag               
             20.  Shut Down Mode
             21.  PC to TNC Data Bits
             22.  PC to TNC Parity Bits
             23.  PC to TNC Stop Bits
             24.  DCD Flag
             25.  QBM Download Subdirectory 
             26.  BBS Read Request Command
             27.  Local BBS Callsign
             28.  SAREX Callsign
             29.  SAREX Capture to Disk File name
             30.  PacketCluster Call
             31.  Digipeat Detect Flag
             32.  Node Drop Link Flag
             33.  Sound Flag
             34.  Display Computer Generated Commands Flag
             35.  Digipeat PK-232 Date/timestamp in Call Sequence Flag
             36.  Keyboard Character Beep value.
             37.  :QBU: Receiving Station Batch file (QBU-RX.BAT)
             38.  :QBU: Originating Station Batch file (QBU-TX.BAT)
             39.  Capture-to-disk Flag
             40.  Beacon Control/LAN-LINK handshake Flag
             41.  Spare
             42.  Start of Scan Words (MUST HAVE AT LEAST ONE)
             43.  * end of Scan Words
             44.  Start of Common Calls (MUST HAVE AT LEAST ONE)
             45.  * end of Common Calls
             46.  Default users
             47.  Start of Custom Colors
             48.  Remaining TNC start up Commands.

             The  contents of each line are described in the  section  of 
             the Parameters menu which deals with customizing them.   The 
             remaining  lines contain commands to the TNC.   For  further 
             information  about them refer to the TNC  manual.   LAN-LINK 
             assumes different defaults in some instances to those set in 
             the TNC.  The SYS file contains only those that are  differ-
             ent to the TNC default reset state. 

             NOTE: If you are not using a TNC1 you MUST set the  HEADERLN 
             parameter  to  ON.  The packet headers and the text  of  the 
             packets must show up on your screen on separate lines.   You 
             must  also have the "Echo as Sent" feature set ON ('EAS  ON' 
             for PK-232 and 'XM' ON ' for the KAM).



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 103  


             24.3  *.RUN

             These files contain incoming data from the TNC recorded while 
             the  'capture to disk' function was active.  LAN-LINK  names 
             them  as YYMMDD.RUN automatically (YY = Year, MM  =  Month, 
             DD = Date, i.e 900903.RUN is a file for 3 Sept 1990).

             24.4  *.DBF (HF.DBF and VHF.DBF)

             These  file  contain the log entries.  They are Dbase 3  and 
             4 compatible.  The format of the logbook file is the same as 
             that   used by the LOGBOOK package of the  PC-HAM   software 
             package, with more space for comments.

             24.5  LAN-LINK.DIR

             This  is the directory file as described in  Section  6.1.2. 
             You  use it to store connect, NET/ROM, TheLink,  KA-Node  or 
             digipeat paths as well as name/callsign relationships.  

             Examples are
             Joe  G3ZCZ
             Alon 4Z4ZB V 4X6AA
             Milt 4X6AA
             LR   4X6LR
             hf-il 4x4hf v 4z4zb 4x4il
             hf-rj 4x4hf v 4z4zb 4z4rj
             K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT! K1HTV
             w9tnn-2  jrw !% w3eax-7 !& w9tnn-2

             You  create this file with your word processor in  its  non- 
             document mode.  You must leave AT LEAST one space  character 
             between the first (key) word and the connect path.  When you 
             type in the key word, the program does not care about  upper 
             or lower case.  

             You may also use the 'reMember Path' option in the Call Menu 
             to make entries in this file.

             If  you already have a YAPP.DIR or a PK232COM.DIR file  just 
             rename it to LAN-LINK.DIR and add any NET/ROM and/or KA-Node 
             paths.  

             NOTE:  All path entries in LAN-LINK.DIR must be on a  single 
             80 column line.

             24.6  CONFIG.SYS

             You must have a CONFIG.SYS file on the boot disk if you  are 
             going  to  use the disk logging features.   This  file  must 
             contain the line 



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 104  


                  FILES = 20

             See the DOS manual for more information about the CONFIG.SYS 
             file.

             24.7  *.MBX

             These  are the files associated with the stations  you  have 
             designated  as LAN store and forward mailboxes.  Other  sta-
             tions can only :QRU: with you if you have a  'theircall.MBX' 
             file  on  your disk.  Thus if for example you  want  to  use 
             4Z4ZB  as  a  store and forward mailbox, you  will  have  to 
             create  an ASCII file called 4Z4ZB.MBX using Edit  Menu,  or 
             the non-document mode of your word processor.  In this  file 
             you will put a list of the call signs of the stations  4Z4ZB 
             can  connect to reliably.  If for example you want 4Z4ZB  to 
             be  able to store messages from you to 4X6AA, 4X6LR,  G3ZCZ, 
             ON8IK, F0WN,and G8BTB, you would put those call signs in the 
             file, one call on a line as follows.

             4X6AA
             4X6LR
             G3ZCZ
             ON8IK
             F0WN
             G8BTB

             When  the QRU function is invoked either by you manually  or 
             by  4Z4ZB  connecting  to you and sending  you  the  command 
             :QRU:, any message files present on your system addressed to 
             any of those stations (E.G. G3ZCZ.OUT and ON8IK.OUT) will be 
             transferred  from you to 4Z4ZB just as if you had  tried  to 
             :QSP:  the  messages manually or as if G3ZCZ or  ON8IK   had 
             connected  directly to you.  The file names on  your  system 
             will be changed to *.OLD.

             You  must  create  one file for each  designated  store  and 
             forward station, ie. 4Z4ZB.MBX, G3ZCZ.MBX etc.

             24.8  *.BBS

             These are BBS AUTO-Upload Command files.

             Each file is named for the callsign of the BBS that you wish 
             to access.  It must have exactly the name as the callsign of 
             the  BBS.  Thus if the BBS is W9TNN-1 the name of  the  file 
             must  be W9TNN-1.BBS, or if the BBS is 4Z4ZB then  the  file 
             must  be called 4Z4ZB.BBS.  The file must be an ASCII  file.  
             That  means  the  word processor must be used  in  the  non- 
             document mode to create it.

             This file contains the command sequence that you would  have 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 105  


             typed  at  the  keyboard  if  you  were  accessing  the  BBS 
             manually.  The ONE difference is that the text of a  message 
             you are uploading with the S command must be followed by the 
             character  string :EOF: (on a separate line) as  illustrated 
             by the example below.

             The  contents of A TYPICAL *.BBS file is shown below  as  an 
             example.

             k 1234
             d \net\lan-link.doc
             s g8btb
             Test Message
             This is a test message.
             :EOF:
             sp G3ZCZ @ N4QQ
             Greetings
             The text of this message is greetings from LAN-LINK.
             /ex
             lm
             r 567
             r 593

             24.9 LAN-LINK.001 - LAN-LINK.010

             These  are 10 different ASCII files with fixed  names.  They 
             can be transmitted using the Alternate function keys.  Their 
             contents  can be viewed using the Shift function  keys.   In 
             all  cases  the function key to use for  a  particular  file 
             corresponds  to the number in the file suffix. For  example, 
             use Alt/Shift Function Key 3 (Alt-F3) to transmit/view  file 
             LAN-LINK.003.  You may also use the Edit Menu to edit/create 
             the files.

             In  case you forget what you put in each of the files,  LAN-
             LINK allows you to take a peek into all of them at the  same 
             time.   Use Control Function key 1 (Control-F1) to  look  at 
             the first line of all the LAN-LINK.001 - LAN-LINK.010  files 
             and the Brag Tape.

             24.10 QBU-RX.BAT

             This  is the command or batch file used in the :QBU:  origi-
             nating station.

             24.11 QBU-TX.BAT

             This is the command or batch file used in the :QBU:  receiv-
             ing station.





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 106  


             24.12 LAN-LINK.QTA
             
             You can leave a message on your system for someone else in a 
             file  named  CALLSIGN.OUT.   When  the  station  with   that 
             callsign connects to you, the message will be sent, and  the 
             filename will be changed from CALLSIGN.OUT to  CALLSIGN.OLD.  
             This is fine as long as the path between the stations  good. 
             If  the path is marginal, it is possible that  your  station 
             will  transmit the message and change the filename, but  the 
             link  will  drop out before the message is received  at  the 
             other station.  If the other station does not connect to you 
             and  :QSM:,  the message may get lost.   If  this  situation 
             occurs,  you  can  tell LAN-LINK that there is  a  bad  path 
             between  you  and that station, and not to change  the  file 
             names without an explicit :QTA: instruction from that  other 
             station.  You do this by putting the call of the  station(s) 
             having a bad path in an ASCII file called LAN-LINK.QTA.  Put 
             one call on each line in the form

             N9BE
             G8BTB

             You  must use the root call of the station without an  SSID. 
             That  means, if the station is N9BE-4, just put N9BE in  the 
             file.


        25.0 Mailbox features

        This section describes the mail box and message handling features 
        built into LAN-LINK.

             25.1 Answering Machine

             LAN-LINK  contains an AMTOR (Robot beacon CQ mode only)  and 
             PACKET  Mode   SMART "answering machine" facility.  You  can 
             leave  messages on your disk (in the same directory  as  the 
             LAN-LINK.*  files,  if  you  are using  a  hard  disk),  for 
             different  stations.  When someone connects to you,  if  you 
             left  a message for him, he (or she or even it as  the  case 
             may be) and only that station will receive it automatically.  
             No one else will normally be able to download that message. 

             25.2  Mail Beacon (Annunciator)

             To ensure that people know that you have left a message  for 
             them a 'MAIL for' list is loaded into your Packet Beacon and 
             transmitted every 30 minutes (Refer to the BTEXT command  in 
             the TNC manual) as  ':QTC:' followed by a list of calls.  If 
             no  mail is pending, or the only message in your  system  is 
             one   addressed  to  you,  the  beacon   transmissions   are 
             inhibited.   This  conforms to good  operating  practice  on 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 107  


             crowded channels (at least inhibiting the beacon does).

             The mail beacon in the AMTOR Mode is transmitted as part  of 
             the beacon AUTOCQ message.  It is automatically updated when 
             a message is transmitted.  If you don't set the beacon  (see 
             below)  you  will not transmit a mail beacon  text  in  your 
             AMTOR CQ message.

             The  Mail  beacon text is set up either when  you  tell  the 
             computer  to set it up or when you disconnect a  packet  QSO 
             from another station.  

             In this manner you may update the list while the program  is 
             running,  for  example  by using Sidekick  or  the  included 
             Editor, to write a message, or preferably the NOTE feature. 

             Any   station   using   LAN-LINK  can   be   configured   to 
             automatically  attempt  a connect (QTC-Snatch)  when  seeing 
             their callsign in someone else's LAN-LINK :QTC: beacon  mail 
             message list.

             If  for some reason the message got lost (e.g.  because  the 
             link  was  marginal), :QSM: will get you a  repeat  of  that 
             message.

             25.3  How to leave a message

             You  can use the note feature or type the message as a  non-
             document  file on Wordstar, the included Editor, or  if  you 
             use another word processor, you must leave the message as an 
             ASCII text file.  

             If  you  use the Note feature, the message will be  given  a 
             header  as  if it came in from someone else.  if you  use  a 
             word processor or the included Editor to write the  message, 
             you will have to write in a header or show somehow that  the 
             message  is  not  'live'.  You may then  later  time  tag  a 
             message  header  on  message  files  created  by  the   word 
             processor.   In this way people will realize that it  is  an 
             automatic message by seeing the header.  On the other  hand, 
             you may wish to fool people into thinking that you are home.

             You  just  name  the message file as  the  callsign  of  the 
             station  to whom you wish the message to be sent at  connect 
             time.  You must also give it the filetype of 'OUT'.

             For example a message for G3ZCZ would be stored on the  disk 
             as  a  file named 'G3ZCZ.OUT', and similarly  a  message  to 
             4X6AA would be stored on disk as '4X6AA.OUT'.  

             Once the message has been sent, an entry to that effect will 
             be made in the LAN-LINK.RUN  data capture file. The  message 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 108  


             file  will  then  be renamed and given  the  file  extension 
             '.OLD'.  At that time any previously existing mail file with 
             the  file extension '.OLD' will be deleted.  This stops  the 
             addressee  receiving the message on successive  connects  if 
             you  can't delete it for some reason (you forget)  while  at 
             the same time, the message is still available to you in case 
             you need it.

             You  should use a separate utility program if you  want  the 
             calls  in the mail beacon sorted.  You may for example  wish 
             to  sort them alphanumerically or in the order of  the  date 
             that they were left in your answering machine.

             Incoming  messages triggered by the QTC-Snatch will be  left 
             in a message file '<yourcall>.OUT', which can be scanned  by 
             using  the Alt-M Key combination. If you have  non  LAN-LINK 
             friends, train them to trigger the QTC-Snatch by  simulating 
             a  beacon,  and prefixing and ending their text  with  lines 
             containing the '>' as the only character.  Better yet,  give 
             them a copy of LAN-LINK and tell them to register it.

             25.4 Remote Beacon Shutdown

             I recognize that some stations may abuse the beacon facility 
             of  this  program.  I have thus built  into  the  program  a 
             'remote  shutdown' capability.  If someone running  LAN-LINK 
             has their beacon timer set too often, connect to them in the 
             AMTOR   or  Packet Communications modes, and  tell  them  to 
             :QRT:  which will clear their beacon mode and take them  off 
             the air for a while at least.

             In the Packet Communication Mode, the CQ beacon is shut down 
             but the 30 minute mail beacon is not touched.  In the  AMTOR 
             Communication  Mode, the CQ delay time is set  to  infinity.  
             The  LAN-LINK  Mailbox  will thus still be  active  in  both 
             modes, but will not call CQ on the air.


















        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 109  


        APPENDIX 1. ANOMALIES and BUGS

        A1.1 Command/Converse Mode anomalies

        Since  the Program has no way to check the command/converse  mode 
        status  of the TNC, you may see various Cmd: and  error  messages 
        from  the  TNC  when using the menus or  function  key  commands.  
        Ignore them for now.  If you get an error message, try using  the 
        function key again.

        A1.2 Buffer messages in AMTOR Beacon CQ Mode

        In the AMTOR Beacon CQ Mode, if the other station drops the  link 
        while  you are recording the text, BEFORE the callsign  has  been 
        recognized  as  a valid callsign, LAN-LINK will time  out  before 
        logging the QSO and restarting the CQ sequence.  If someone  else 
        calls  in  before the time-out has occurred, the text  from  both 
        stations  should be captured to disk, but the log entry  may  not 
        show  both  stations, thus the 'LOG' must be  compared  with  the 
        'RUN' file for QSO purposes.

        LAN-LINK in the Beacon/Mailbox Mode, normally logs the contact at 
        the  end  of the line in which it recognized the  callsign  as  a 
        valid callsign.

        A1.3 FEC +? responses in AMTOR Beacon CQ Mode

        In the AMTOR Beacon CQ or Mailbox mode, if another station  sends 
        a  +? in the FEC Mode, the beacon will attempt to send  the  LAN-
        LINK.TXT file.  The PK-232 however is not in the Converse Mode at 
        that  time and will interpret the text of the file  as  commands.  
        If  by some chance, the text corresponds to a valid  command  the 
        PK-232 will execute it and put the PK-232 in an unknown state and 
        you  may  not notice that it did.  As such I recommend  that  the 
        first  character  of  each line in the  file  LAN-LINK.TXT  be  a 
        non  valid command character such as a number or a period (.)  or 
        another punctuation sign.

        A1.4 Using a CGA card with a monochrome monitor

        If  you are using a CGA card with a monochrome monitor, the  text 
        you  type  into the OUTWINDOW will be fainter than  the  incoming 
        text.   This is because of the colors used.  If you are  using  a 
        Hercules  compatible  card you will not  notice  any  difference.  
        Change the colors using the Parameter Menu.

        A1.5 The Packet Conference Mode

        The  Conference  Mode has been tested on a PK-232, KAM,  a  SANYO 
        MBC-675  which  has a clock speed of 4.7MHz and other  PC  clones 
        with faster clock speeds.  If you have problems with intermittent 
        selection of I/O channels try slowing down your CPU clock.  There 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 110  


        is a software delay loop in the program that is used to allow the 
        TNC time to switch I/O streams after receipt of the stream change 
        command.   This  delay  is there because  LAN-LINK  tests  for  a 
        connect  on each channel before outputting any text, so  that  it 
        does not send unaddressed packets on non connected I/O channels.

        A1.6 Packet Conference Mode disconnects

        A  Packet  conference  Mode disconnect returns  the  TNC  to  the 
        Command  Mode, even if you remain connected to one or more  other 
        stations.

        A1.7 Strange Events

        If  the TNC does not use an interrupt driven serial port you  may 
        experience problems when using baud rates greater than 1200.  The 
        PK-232  DOES  NOT LIKE LAN-LINK to use RS-232 baud  rates  faster 
        than 2400, and sometimes not even that.  Use 1200 until YOU  have 
        tested and ARE SURE that a faster one will work.  

        IF YOU HAVE ANY STRANGE PROBLEMs AND ARE USING an RS-232 TERMINAL 
        BAUD RATE to the TNC WHICH IS GREATER THAN 1200, set the Terminal 
        Baud Rate to 1200 and see if the problem goes away.

        Make sure that your configuration is set the way you think it is.  
        Verify  it  using the 'display deFault' (and the  Misc.  Flag  if 
        necessary) option(s) in the Parameter Menu.

        You  must have at least one common call or scan word in your  SYS 
        file, or you will get errors when you update the SYS file.

        A1.8 *** DISCONNECTED

        In  the  Packet Communications Mode, when you  are  connected  to 
        someone and the TNC sends this text string to the computer,  LAN-
        LINK thinks you have been disconnected and resets.  This normally 
        only happens when a true disconnect occurs.  However, if the text 
        shows up in the middle of a line being sent to you, it WILL  HAVE 
        THE SAME EFFECT AND THINK THAT YOU HAVE DISCONNECTED if the  DCD-
        Flag is not set in the SYS file, and the TNC does not use the DCD 
        signal on pin 8 of the RS-232 interface.

        A1.9 *** CONNECTED

        In  the  Packet  Communications Mode,  when  you  are  monitoring 
        traffic  on  the  LAN someone sends this  text  string,  LAN-LINK 
        thinks you have been connected if the DCD-Flag is not set in  the 
        SYS file, and the TNC does not use the DCD signal on pin 8 of the 
        RS-232 interface.  





        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 111  


        A1.10 Greek Characters and other garbage in the Incoming Screen.

        If  you see Greek characters in the Incoming screen you  probably 
        have  the wrong parity set in the TNC. first make sure  that  the 
        RS-232 baud rate is correct.  If it is, take the batteries out of 
        it and reset it.  If that fails, play with the parity.   LAN-LINK 
        sets  the serial port as configured in the TNC.SYS file for  each 
        TNC.   For example, for the PK-232 it is 8 bits, no  parity,  for 
        the  TNC2 it is 7 bits.  If you still can't get it to  work,  set 
        the interface to 7 bits in the configuration file.

        A1.11 Dumb TNC

        If  the  TNC  seems to respond to commands  but  is  not  sending 
        anything back, you may have one of two problems.  You may have  a 
        bad RS-232 cable with on wire disconnected.  If the computer  can 
        operate  the TNC in another communications program, try to  reset 
        the  TNC, take the batteries out, etc.  You may also have a  not-
        so-compatible PC. 

        A1.12 Intermittent Lockup

        Watch out for flow control problems on the cable between the TNC 
        and the PC and between the PC and the Display.  

        Versions  of  LAN.LINK  upto and  including  1.55  used  software 
        handshaking.   Anytime  the program received a   Control-S   (^S) 
        character from the TNC it waited until it subsequently   received 
        a Control-Q (^Q).  These  characters  can  appear  on  the LAN in 
        a  binary  packet, either when  binary  file transfers   are   in 
        progress,  or  in  a Inter NET/ROM   message.    To  avoid   this  
        lockup,  a line containing 'MFILTER 19'  was added in  your  LAN-
        LINK.SYS  file so make the TNC filter the  ^S  character out  and  
        not  pass it to LAN.LINK.  LAN-LINK 1.56 and onward use  hardware 
        handshaking  so  this problem should not appear. However  if  the 
        FLOW  and XFLOW parameters are not set to OFF in your  TNC,  LAN-
        LINK can appear to lockup.  Make sure that they are both set  OFF 
        in your TNC.

        APPENDIX 2. Local Area Network Capability

        VHF  Packet  radio systems can be considered as part of  a  Local 
        Area  Network (LAN) in which messages can be left by one  station 
        in the computer belonging to a second station.  At HF the same is 
        true,  but the area becomes greater.  The basic problem  here  is 
        that  people  can only send and receive messages to or  from  you 
        when you are on-line.  To compensate for this, BBS stations  were 
        developed which allowed both messages and bulletins to be  stored 
        by anyone for later retrieval.

        LAN-LINK  allows you to store messages in your computer so as  to 
        use  it  as  an  automatic answering  machine.   By  storing  the 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 112  


        messages in a file called by the name of callsign, with the  file 
        extension  '.OUT',  anyone connecting to the  computer  will  get 
        their  message  without  having to request  it.    LAN-LINK  also 
        extends  that concept to cover the eventuality of you wanting  to 
        take  your computer off-line for some reason.  You may  now  load 
        the  message  into any other computer you can  connect  to  using 
        elements  of  the  Q  code adapted  to  the  High  Level  Network 
        Communications  Language (NC/L) proposed in my book Software  for 
        Amateur  Radio, (Book number 1560) published by TAB  Books,  Blue 
        Ridge Summit, Pa. 17214 U.S.A.

        A2.1 LAN Protocol (G3ZCZ Version)

        The  protocol  is as follows. When connected to someone  who  has 
        their  LAN-LINK  configured  as a host, if you want  to  store  a 
        message  you send the following instruction to the other  station 
        :QSP:  <callsign>  where  <callsign> is the call of  the  station 
        that the message is for, not the callsign of the host station  in 
        whose  computer you are storing the message. [Note use  only  one 
        space  character  after  the :QSP:].  LAN-LINK  sends  the  :QSP: 
        message automatically using QSP option in the Message Menu.

        For  example if you want to store a message for 4Z4ZB in  4X6AA's 
        computer  which is configured as a Store and Forward system,  you 
        would first connect to 4X6AA and then send the command as

                                  :QSP: 4Z4ZB .

        Better  still use :QSP: option in the Lan-Link Menu  to  automate 
        the sequence.

        The computer at 4X6AA will respond either with a statement saying 
        that  it is ready for you to go ahead, or send a  message  saying 
        that  it can't comply.  If it is ready you get a  positive  reply 
        which will take the form :QRV:  <callsign> which if you know  the 
        Q code, means " I am ready to accept a message for  <callsign>".

        At this time you may go ahead and send the message.  If you  type 
        the message at the keyboard, you may use either a control Z  (^Z) 
        character or the character sequence :EOF: followed by a  carriage 
        return  (the  ENTER key) to terminate the message.  If  you  have 
        first  written the message into a text file you may then send  it 
        using  the  'Send  File'  option  of  the  Files  Menu  and   the 
        termination sequence is automatic.

        Once  you have completed the message, the other  (host)  computer 
        will  either reply that the message has been successfully  stored 
        or give you an error message.

        If  the  message  is stored and ready to be sent  next  time  the 
        addressee  connects  to that computer, you will see  the  message 
        :QSL: on your screen.  If something went wrong, you will get back 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 113  


        a  negative message taking the form :QNO: followed by  a  number.  
        The number tells you why the operation failed.

        A2.2 Message Format

        The  message is stored just as if you had left it in your  system 
        (except that a header is added identifying the time of  reception 
        and  the call of the sending station).  It will contain a  header 
        showing  the  date and time it was received  and  your  callsign.  
        Should a message for that station already be in the system, yours 
        will be appended to it.  In the event the your upload is aborted, 
        the  amount  of text received before the abort occurred  will  be 
        stored as the message.

        When  you  disconnect from the other LAN-LINK host  station,  its 
        mail beacon will be updated.

        Once the message is loaded in the host, it can only be deleted by 
        the operator of the host station.  When the addressee connects to 
        the host and receives the message, the file type will change from 
        '.OUT' to '.OLD'.

        A2.3 File Uploading/Downloading

        There  comes a time when you want to leave a file on your  system 
        for someone to download later.  You can do this by using NC/L  to 
        control the transfer.  You must leave the file in a  subdirectory 
        defined  in  the LAN-LINK.SYS FILE called  \LAN-LINK\FILES.   You 
        must first create it if it does not exist.  The station who wants 
        the message just asks for it using :QBM: <filename>, note they do 
        not  need to use the full subdirectory path.  They  must  however 
        leave  a single space character between :QBM: and  the  filename.  
        In AMTOR the Mailbox must be turned on for remote functions.

        For  example, you have the latest ARRL DX bulletin, and you  want 
        to  pass it on.  You could pass it to selected people by  copying 
        the  file to individual messages with the filetype  '.OUT',  e.g. 
        4X6AA.OUT, 4Z4ZB.OUT or even G3ZCZ.OUT if you want me to get  it, 
        which wastes a lot of disk space.

        On  the  other  hand  you could tell people  that  the  file  was 
        available  for downloading, either in the CTEXT  connect  message 
        line  which everyone gets when connecting to you  by  configuring 
        LAN-LINK accordingly, or in individual ('.OUT') messages.

        If you include the following in your CTEXT message 

                           "ARRLDX.015 now available"

        people will know that to download it, they just have to type  the 
        line  ':QBM: ARRLDX.015' (one space character between  :QBM:  and 
        the  file name) to get the file.  LAN-LINK is not designed  as  a 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 114  


        BBS,  however,  if you copy the contents of  the  \LAN-LINK\FILES 
        subdirectory  into  a  file called DIR (USE DIR >  DIR  in  DOS), 
        anyone  can  get a list of the files you have stored  in  it  for 
        downloading by typing :QBM: DIR.  Since they do not get the  real 
        directory, just what was in it at the time you copied it into the 
        file  'DIR',  you may keep "hidden" files in  this  subdirectory.  
        You may thus leave a file for someone to download, tell them that 
        its  there  by  leaving  them a  message  (which  they  will  get 
        automatically when they connect) and no one else connecting  will 
        know that it is there.

        :QDB: allows you to upload text or ASCII files.

        If  you  use the 'lan-linK' option of the Packet  Terminal  Menu, 
        LAN-LINK will automate the QDB and QBM features for you.

        A2.4 Path Determination to a Dx station

        If  you want to establish a digipeat path to a  station  somewhat 
        out of your direct range, you need to know which of the  stations 
        that you can connect to can hear that desired DX station.  If you 
        could  get a call monitored (MH list) from the stations that  you 
        connect  to,  you  would be able to see if the  station  you  are 
        connected to has heard your desired DX station.   

        LAN-LINK  uses  the :QMH: command to request such a  list.   When   
        LAN-LINK   receives  a :QMH: command, it drops back  to  the  TNC 
        Command  Mode and issues a 'MH' command to the TNC (except  to  a 
        TNC1 which does not support it).  It stores the list received  in 
        a  temporary  buffer, and then returns to the Converse  Mode  and 
        transmits the list back to the station it is linked to.

        By  judicious  use  of :QMH: you can  determine  paths  to  other 
        stations.   Note however, that just because one station can  hear 
        another  station,  it  does not mean that it can  work  it.   For 
        example,  the station you are connected to may be using  a  power 
        level  of 1 watt or so, while the station 200 miles away that  it 
        heard was using 100 watts.  Test the path yourself, or/and  leave 
        a message asking how reliable the connect path between those  two 
        stations is.

        If  you and a small group use a non standard packet  channel  for 
        inter-group  communications, you may also use the :QMH:  function 
        to  find  out who the station you are connected with,  has  heard 
        recently, when you first sign on the LAN channel.

        APPENDIX 3     BASIC NC/L DICTIONARY

        Messages can be transferred into any other LAN-LINK computer  you 
        can connect with using elements of the Q code adapted to the High 
        Level Network Communications Language (NC/L) proposed in my  book 
        Software  for Amateur Radio, (Book number 1560) published by  TAB 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 115  


        Books, Blue Ridge Summit, Pa. 17214 U.S.A.

        NC/L  command words are summarized in the  following  paragraphs.  
        There  is  no command word to request your message.   To  receive 
        your message, you do nothing, you will receive your mail automat-
        ically  when  connecting/linking with a  LAN-LINK  station.   You 
        cannot normally read messages addressed to another person.

        A3.1 :QBM: 

        To download a file, send

                   :QBM: filename.type

        The filename.type is the file you want. For example 

                  :QBM: dir
                  :QBM: help
                  :QBM: LAN-LINK.doc

        A3.2 :QDB: 

        To upload files to another LAN-LINK system send 

                  :QDB: filename.type

        Files  will be uploaded into the same sub-directory as  LAN-LINK, 
        and will have a message header inserted at the top of the file to 
        allow  the  operator  to  know who uploaded  the  file.   If  the 
        operator  then wants to make the file available for  downloading, 
        he or she can move it to the \LAN-LINK\FILES sub-directory.   The 
        '.TYP' following the filename is optional.  

        If  you attempt to upload a file which has the same name  as  one 
        that  already  exists on the remote system, you will  receive  an 
        'error' message.

        This command is the reverse of :QBM:.

        A3.3 :QMH: 

        To request a call monitored list ('MH') from the LAN-LINK station 
        that you are connected with, send

                  :QMH:

        A3.4  :QSM: 

        To  request a repeat of a message from a station using  LAN-LINK, 
        send

                  :QSM:


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 116  



        This  command will be valid as long as the host station  has  not 
        deleted  the <yourcall>.OLD file on his disk.  If the  file  does 
        not exist, you will receive a :QNO: 2 'error' response.

        A3.5  :QSP: 

        To leave a message, send

                  :QSP: callsign

        The  callsign is that of the station you wish to leave a  message 
        for.

        A3.6 :QRA:

        When  disconnected, to see what stations (using  LAN-LINK  1.53+) 
        are on the LAN, or which LAN-LINK stations have messages pending, 
        send
             :QRA:

        All LAN-LINK stations will reply with a mail beacon within a  few 
        seconds.

        A3.7 :QRT: 

        To shut down an AMTOR/Packet mode Mailbox/beacon station which is 
        causing QRM, link or connect to the station and send

             :QRT:

        A3.8 :QRU: 

        To  upload messages from one LAN-LINK/PK232COM (1.38+) system  to 
        your computer, send 

             :QRU:

        You  may  only use the QRU function with stations  designated  as 
        Store and Forward mailboxes.  Put a list of stations that you can 
        connect  to reliably in your <callsign>.MBX file and send  it  to 
        other  stations in your LAN also using LAN-LINK.  They will  then 
        be  able to dump their mail messages on you and you on  them.  If 
        they  do the same and send you their file, then you will be  able 
        to send messages via them for stations that they can work.

        While  QRU  gives you the capability to bulk upload  messages  to 
        another  station in your local area, when you take  your  machine 
        off  line, it may also be used to transfer messages  between  two 
        LANs via well sighted gateway digipeaters.




        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 117  



        A3.9  :QNO: 

        ':QNO:' and error message text is a response to a request.  


        A3.10 :QJG: is a response to :QRU:

        It confirms that the QRU sequence is complete.  There are no more 
        messages pending.

        A3.11 :QRV: callsign is a response to :QSP: callsign.

        The computer is ready to send the message. End the message with a 
        control Z (^Z) character, or the sequence :EOF: 

        A3.12 :QSL: is a response to a command

        It  confirms receipt of message to that callsign or that  a  file 
        has  been successfully uploaded and stored to disk.  It  is  also 
        used to acknowledge receipt of a ':QRT:' command.

        A3.14 :QTA: message 

        If   LAN-LINK  receives  :QTA:  and  a  message  exists  for  the 
        connecting station, LAN-LINK will change the filetype from  'OUT' 
        to 'OLD' and respond with a 'QSL'.  If a message does not  exist, 
        it will respond with a 'QNO'.

        A3.14 :QTC: message list

        If  LAN-LINK receives :QTC: it will respond with the beacon  text 
        showing the mail queue.  

        :QTC:  precedes a list of callsigns for whom messages are  stored 
        up  on a computer.  It is used in Packet Beacon transmissions  or 
        AMTOR Beacon mode CQ calls.  

        A3.15 :QBU: External Protocols

        This  feature is supplied to allow experimentation with  external 
        protocols.


        PROPOSED EXTENSIONS

        A3.16 :QYU:     YAPP format file upload.
        A3.17 :QYD:     YAPP format file download.






        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 118  


        APPENDIX 4. USING OTHER TNCs

        The PACKET Mode capabilities can be used on all TNCs.  There are 
        minor  differences  in  the command  dialogue  between  different 
        TNCs.  The dialogue differences affecting the operation of  LAN-
        LINK are built into the program and set when the TNC type is read 
        from  the  LAN-LINK.SYS file at the program load time.   The  non 
        packet modes will obviously result in error messages if attempted 
        on a packet mode only TNC.

        The   following  notes  apply  to  different  TNCs  or   digital 
        communications controllers.

        A4.1 TNC2 (MFJ 1270) Version 1.1.2

             A4.1.1 Default Commands

             Rename  the  LAN-LINK.SYS  file as  PK232.SYS.   Rename  the 
             TNC2.SYS  file as LAN-LINK.SYS and edit it using  your  word 
             processor  in its non document mode to customize it to  your 
             station.

             A4.1.2    Program differences

             The following functions DO NOT WORK because the TNC does not 
             support them.

             All NON PACKET modes.
             Software controlled HF/VHF switching.
             Software controlled baudrate switching.
             CQ/BEACON Packet terminal mode.
             TNC Transmit Buffer flush.

        A4.2 TNC1 (HD-4040)

        The Packet Communications Mode header colors are not supported in 
        LAN-LINK for this TNC.

             A4.2.1     Default Commands

             Rename  the  LAN-LINK.SYS  file as  PK232.SYS.   Rename  the 
             TNC1.SYS  file as LAN-LINK.SYS and edit it using  your  word 
             processor  in its nondocument mode to customize it  to  your 
             station.

                  Ignore error messages at start up.

             A4.2.2     Program differences

             The following functions DO NOT WORK because the TNC does not 
             support them.



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 119  


             All NON PACKET modes.
             Day/Time functions. 
             'MH' and remote :QMH: functions. 
             MAIL Packet Terminal Mode. 
             CQ/BEACON Packet Terminal Mode.
             TNC Transmit Buffer flush.
             Conference and multiconnect modes.

        A4.3 Kaypro KPC-2

        The Packet Communications Mode header colors are not supported in 
        LAN-LINK for this TNC.

             A4.3.1     Default Commands

             Rename  the  LAN-LINK.SYS  file as  PK232.SYS.   Rename  the 
             KPC.SYS  file  as LAN-LINK.SYS and edit it using  your  word 
             processor  in its nondocument mode to customize it  to  your 
             station.

             A4.3.2     Program differences

             The following functions DO NOT WORK because the TNC does not 
             support them.

             All NON PACKET modes.
             MAIL Packet Terminal Mode. 
             CQ/BEACON Packet Terminal Mode.
             TNC Transmit Buffer flush.

        A4.4 KAM  

        LAN-LINK switches colors when it sees the /V or /H following  the 
        callsign  in the packet header, or in the calls monitored  ('MH') 
        list.  If you are monitoring both HF and VHF simultaneously,  the 
        colors  will show you which radio you heard which signal on.   If 
        the  Mail-Snatch or the QTC-Snatch are triggered,  LAN-LINK  will 
        change  modes  and attempt the connect on the correct  radio  but 
        will  not  change the band/power information or  the  logbook  to 
        reflect  that change in the logbook or in the status window  dis-
        play.

             A4.4.1     Default Commands

             Rename  the  LAN-LINK.SYS  file as  PK232.SYS.   Rename  the 
             KAM.SYS  file  as LAN-LINK.SYS and edit it using  your  word 
             processor  in its nondocument mode to customize it  to  your 
             station.

             A4.4.2     Program differences

             The following functions DO NOT WORK because the TNC does not 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 120  


             support them.

             TNC Transmit Buffer flush. 
             The SIGNAL Communications Mode.
             The NAVTEX Communications Mode.
             The Alt-D key in the MORSE Communications Mode.
             The AMSAT-OSCAR Menu does not allow UoSAT option, as the KAM 
             does not have 1200 baud ASCII capability.
             The BAUDOT NAVY MARS Protocol is also not available.

        A4.5 PK-232 EPROM Version 30 DEC 1988 and subsequent ones.

        Turn   the  'BBS  OFF'  if  you  want  the  Alert  Call,   packet 
        communications mode header colors and Digipeat Detect features to 
        work otherwise turn it on.

        A4.6 MFJ 1278 

        LAN-LINK  assumes  that  the Radio 1 port  is  connected  to  the 
        VHF/UHF packet transceiver, and the Radio 2 port is connected  to 
        the HF transceiver with the multi mode communications capability.

        To transmit CW turn the VOX on.

        The MFJ1278 suffers from one major deficiency as far as  LAN-LINK 
        is concerned.  The Echo-As-Sent only works in the AMTOR  Communi-
        cations Mode.  That means that you will not see the contents of a 
        file  echo in the incoming window as the file is being  transmit-
        ted.

             A4.6.1     Default Commands
             
             Rename  the  LAN-LINK.SYS  file as  PK232.SYS.   Rename  the 
             MFJ1278.SYS file as LAN-LINK.SYS and edit it using your word 
             processor  in its nondocument mode to customize it  to  your 
             station.

             A4.6.2     Program differences

             The  following functions DO NOT WORK because either the  TNC 
             does  not  support them or does not do so  in  a  consistent 
             manner.

             TNC Transmit Buffer flush. 
             The SIGNAL Communications Mode.
             The AMSAT-OSCAR Menu does not allow UoSAT option. 
             The BAUDOT NAVY MARS Protocol is not available.
             CW Identification.

             The  NAVTEX communications mode.  (MFJ1278 allows,  but  not 
             set in LAN-LINK).



        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 121  


        A4.7 Heath HK-21

        K3WGF  noticed that his Heath HK-21 TNC didn't seem to  have  the 
        proper  circuitry  to  support true DCD on pin  8  of  the  RS232 
        connector.  Even though the pin was labeled DCD it didn't  signal 
        properly.   Set the DCD function in LAN-LINK to OFF to  make  the 
        Capture-to-Disk close out normally rather than continue to remain 
        engaged.   

        APPENDIX 5 UPDATES/REVISION HISTORY

        1.55 Changed  to Turbo Pascal 5.5. Initialize calls,  :QDB:  long 
             file transfer and Sound display bugs fixed. F3 and F8  turns 
             Robot  off.  Expanded  contest operation.  KAM  AMTOR  Robot 
             drop-link  added. KN fixed in CW. RTTY and Navy MARS  Baudot 
             File Transfer Bug.

        1.56 RTTY and Navy Mars File transfer bug fixed. Command Echo bug 
             fixed.  Disconnect  Capture-to-Disk bug  fixed.   Alt-K  and 
             Alt-Y added. :QBU: added. J option in parameter menu  delet-
             ed, I and L options added. BBS Bulletin read command custom-
             izable.  Automatic packet/AMTOR contest mode  added.   Call-
             signs  converted  to upper case. CW speed  shown  in  status 
             window,  left/right  arrows change CW speed by 1 wpm.  Sound 
             flag kills ^G bell on incoming text. /EX or  /ex as well  as 
             :EOF: can now be used in *.bbs file column 1. 'RY's  deleted 
             from  RTTY  CQ call. PC to TNC now uses  hardware  handshake 
             (^S/^Q  deleted).   SAREX  Orbiter  menu/functions  changed. 
             SAREX Orbiter Metabeacon interface changed. Logs split to HF 
             and VHF.  PacketCluster added. Update changed.

        1.57 dBASE compatible logbook files. AutoCQ bug, 1.56 Non KAM vhf 
             PACLEN  bug, Packet 'End' key bug and Editor F10 bug  fixed, 
             changes  in order of colors in SYS file. K option  added  to 
             Edit  menu. ! F and 0 options added in Parameters Menu.  PK-
             232 Mailbox commands changed at start-up and shut-down.  QSM 
             added to LAN-LINK Menu. Com 3/4 addresses/IRQs changed  from 
             PS-2  to XT. Capture-to-disk files automatically named  each 
             day as YYMMDD.RUN. Quick Menu added. Kam/KPC Shut-down state 
             4/5 turns PBMON and NDMON off.  

        1.58 Default  users  added. Editor stack/ 1.57  lockout  bug  and 
             other  anomalies fixed, X and Y options added to  TNC  Menu.  
             O,  P,  Y and Z options added to Files  Menu.   Pick  option 
             added to message Menu. Com port set up changed.   Multi-user 
             operations changed. :QTA: Added.








        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 122  


        APPENDIX 6 LAN-LINK 1.58 REGISTRATION FORM

        To: Joe Kasser G3ZCZ, P O BOX 3419, SILVER SPRING, MD 20918.

        CALL ________________   TODAY'S DATE _____________
        NAME ______________________________________________
        ADDRESS ___________________________________________
                ___________________________________________
        CITY    ___________________________________________
        STATE   _________  POSTCODE  ____________ TELEPHONE ____________
        TNC TYPE _________ FIRMWARE REV __________  HOME BBS ___________
        DISK SIZE 5.25 _____ 3.5 ____ Other ? _____________

        I  enclose  a check for $35.00. Please register me as a  user  of 
        LAN-LINK.  I am currently  using Version ______  which I obtained 
        from  _________________________________________.

        Please send me the latest version of LAN-LINK or if a more recent 
        one  does not exist at this time, QSL my registration and add  my 
        name  to  the  list  to receive a free  update  when  it  becomes 
        available.

        Signature 

        My favorite operating modes are ______________________________.

        Additional  Features I'd like to see in future releases  of  LAN-
        LINK.
        Keep Conference Bridge Up  __ YAPP Binary File compatibility   __
        Expanded Contest Operation __ More AMTOR (explain below)       __ 
        NTS capability             __ Picture Transfer capability      __
        Telephone Modem capability __ PacketCluster Menu (Like BBS)    __
        Kenwood Radio Control Menu __ Printed Manual ($15.00)          __
        Inhibit Sign On Message   (Registered Users only)              __
        Dumb Terminal (CP-1, ST-5 etc.) Baudot/ASCII RTTY operation    __
        Others 




        NOTE:  some  additions  come into LAN-LINK as a  result  of  user 
        suggestions, so here's your chance to get some input in.

        Comments, likes, dislikes, wish list, etc.










        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 123  


        APPENDIX 7 LAN-LINK PROBLEM REPORT

        Name ______________________________________  CALL _______________
        Street __________________________________________________________
        City _______________________________  State _____  ZIP __________
        Tel. ____________________  LAN-LINK version ____

        1.  Describe your computer system.

        Manufacturer ____________________ Model ___________TNC __________
                                                           Firmware _____
        DOS Version  ________________  Clock Frequency _________ MHz.

        List peripheral equipment and cards installed in your computer.

        Video Herc/EGA/CGA_____  _______________________
        _______________________  _______________________
        _______________________  _______________________

        What  memory  resident programs were installed when  the  problem 
        occurred?
        _______________________  _______________________
        _______________________  _______________________

        2.   Describe  the problem in detail. What were  the  Misc.  flag 
        state-sequence numbers when the problem was happening?


        3.  Describe the sequence of events or keystrokes that led to the 
        problem.

        4.  Any other information that may help in locating the problem.



        Use  additional sheets of paper if necessary.  ATTACH a  copy  of 
        your  LAN-LINK.SYS  file.  

        Mail to:  Joe Kasser, P O Box 3419, Silver Spring, MD. 20918.















        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 124  


        APPENDIX 8 Other PC Software by Joe Kasser G3ZCZ

        8.1 PC-HAM 3.52 BY G3ZCZ

             LOGBOOK

             Full  blown logging package.  With automatic check  of  logs 
             for awards such as DXCC.  Allows you to recall any entry  by 
             call sign within seconds. Indexed displays, QSL'ing, Contest 
             mode QSL'ing (prints the lot) and lots more. Although  writ-
             ten  in  dBASE3  the package  contains  a  compiled  version 
             (LOGBOOK.EXE),  so  you  don't need dBASE to  run  it.   The 
             source   code  is ONLY given to registered users.   It   can  
             convert  your exported LAN-LINK.LOG file to LAN-LINK.DBF  to 
             put  this package  to  work.  Ideal for DX-peditions or  for  
             DX robot users to handle QSLing and log statistics.

             CONTEST

             Keeps  Dupes in memory, logs QSO's to disk in  format  which 
             can  be processed by the LOGBOOK package.  Now  compiled  in 
             Turbo BASIC, source code is supplied so that you can  modify 
             the program to meet your requirements.

             CQSS

             Sweepstakes  game compiled in Turbo BASIC.  Work the    ARRL 
             Sweepstakes contest on your computer.  You are located  just 
             outside  Washington DC.  A propagation model is built in  to 
             the program.   This program is REQUIRED  training  for   all 
             sweepstakes  operators.  Earlier version of the  program  is 
             described  in detail in 'Software for Amateur Radio' by  Joe 
             Kasser   G3ZCZ, published by TAB Books, Blue  Ridge  Summit,      
             PA. 17214.

             WHATSON

             Predict  HF  Propagation for given days. Contest  mode  with 
             printout to whole world at hourly intervals. Needs BASIC.

        This  software  AND MORE comprises PC-HAM which is  available  as 
        Shareware  from G3ZCZ.  Send a blank formatted disk, SASE, and  a 
        QSL card for a copy or save time and money and register as a user 
        for  $36.50 (half of $73).  Request PC-HAM and specify disk  size 
        (3.5 or 5.25 inches).


        8.2 STARTREK The Computer Program

        An  ideal  task  for the beginner to learn a  language  on  is  a 
        simulation  game  which is written around the computer  that  the 
        beginner  has  available.  For in that case,  there  is  complete 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 125  


        control  of all inputs and outputs,   This kind of game in  which 
        the player makes decisions based on the information available  to 
        him  or  her  available at the time), can  be  made  sufficiently 
        sophisticated  and complex so as to make writing it  an  adequate 
        challenge for anybody.

        The  techniques  used in writing a good game are  the  same  that 
        programmers use in professional activities.  Writing a good  game 
        poses  a  challenge that allows you to develop  good  habits  and 
        techniques  for  programming  and  also allows  you  to  learn  a 
        language in an interesting manner.  By taking an orderly approach 
        to the game design, complex operations may be clearly  understood 
        and  converted  to  computer  code with the  aid  of  a  language 
        reference manual, irrespective of the language being used.

        This product teaches the techniques for writing such a game using 
        the  STARTREK game as an example, and the BASIC language  as  the 
        programming language in which to write the code.

        Registration fees.

        Single   Copy   $15.00
        10 - 50  Copies $12.00 per registered copy.
        50 - 100 Copies $10.00 per registered copy.
        100 +    Copies  $8.00 per registered copy.

        This  is  available  as  Shareware  from  G3ZCZ.   Send  a  blank 
        formatted disk and an SASE for a copy or save time and money  and 
        register  as a user by sending a check for the  registration  fee 
        according  the  schedule posted above.  Request  Startrek  -  The 
        Computer Program and specify disk size (3.5 or 5.25 inches).

        8.3 WHATS-UP 0.55

        This version of WHATS-UP is a concept demonstration version of an 
        ASCII  Telemetry Decoding and display Program for the  Fuji-OSCAR 
        20 and the AMSAT Microsat Spacecraft (OSCARs 16, 17, 18 and  19).  
        It  is   table   driven via the configuration  files   to   allow  
        maximum flexibility.

        This  version  does not do binary telemetry  decoding.   It  only 
        decodes the ASCII format. It also contains a few cosmetic display 
        bugs. I expect (but don't promise) to put out Revision 1.00  with 
        more  features,  (such  as automatic  spacecraft  parameter  file 
        switching   to   match   spacecraft,   scheduled   events,    TNC 
        configuration  files, etc.) and proper documentation once  binary 
        telemetry formats have been standardized and stabilized.

        WHATS-UP contains the following features:

        * Supports DOVE and Fuji-OSCAR 20 ASCII format packet telemetry.
        * Real time and Playback modes.


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 126  


        * Dumb Terminal mode.
        * Automatic Capture-to-disk of raw telemetry.
        * Extracts telemetry channel data to a  database or   spreadsheet 
          readable file for further analysis.
        * Link quality measurement.
        * Capability to print the raw telemetry as it is received.
        * Up  to  16 user configurable display pages (screens).  You  set  
          the position on the page (width of engineering unit field,  and 
          number of decimal places) that a parameter is displayed  at.
        * Wild card page (parameter shows up on all pages).
        * Selectable  display of Engineering units or raw byte  for  each  
          display page.
        * Display of raw packets (i.e. STATUS)
        * Color changes if a parameter value changed between   successive 
          frames.
        * Audio  and  visual alarms if a telemetry value  exceeds,  falls  
          below or falls outside a preset limit value(s).
        * Dumb split screen terminal mode (a la LAN-LINK).
        * Customizable colors, PC to TNC baud rate, data parity and  stop 
          bits.
        * Default spacecraft configuration files.
        * Time of day clock display (in HH:MM:SS format)

        If  you  would  like a copy of WHATS-UP  and  have  captured  any 
        telemetry  to  disk,  especially daytime  or  southern hemisphere 
        passes, please put them  on  the disk.  Don't let the data  files 
        become too long. I  suggest  that you  rename  them  every day in 
        the  format  YYMMDD.SC,  such  as 900824.D17, 900824.F20, etc.

        Suggestions for improvements and additions are always welcome.
























        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 127  


        APPENDIX 9 HOW SHAREWARE WORKS:

        The  Association of Shareware Professionals (ASP) has established  
        standards for its members and for any organization which has "ASP 
        Approved"  status. The ASP wants to make sure that the  shareware 
        principle  works for you. If you are unable to resolve a  problem 
        with  an  ASP  member  or  organization  (other   than  technical 
        support),  the ASP may be able to help. Please write to  

        The  ASP Ombudsman, P.O. Box 5786, Bellevue, WA  98006, USA.

        You  are encouraged to copy the floppy disk and share  it  freely 
        with  others.  You have the luxury of trying out the  product  at 
        your own pace and in the comfort of your own home or workplace.  

        After  you  have used the material for  a  reasonable  evaluation 
        period  (90  days),  you should either  discontinue  use  of  the 
        material  or register your copy.  Your support is  important  and 
        greatly  appreciated.  With it, Shareware authors are  encouraged 
        to  design and distribute new products. Without it, a great  deal 
        of high quality, low cost software will cease to be available.

        Why pay at all?

           *  You receive support from the author.
           *  You receive a CURRENT copy of the program.
           *  Your input and ideas help shape future products.
           *  A sense of pride and ownership in having honestly
              participated in the Shareware revolution.
           *  You help to keep software prices down by supporting a
              distribution method which doesn't depend on expensive
              advertising campaigns.

        Be  aware of the following restrictions, designed to protect  the 
        community  of Shareware users and to prevent greedy  people  from 
        taking unfair advantage of the trust, hard work and good will  of 
        Shareware authors. 

        1.   No  price or consideration may be charged for the  material. 
             However, a distribution cost may be charged for the cost  of 
             the diskettes, shipping and handling, not to exceed $6.

        2.   The  files and programs on the disks may not be modified  or 
             deleted.

        3.   The  material  cannot  be sold as part of  some  other  more 
             inclusive package.

        4.   The material cannot be "rented" or "leased" to others.

        5.   The end user must be told clearly in writing on the  outside 
             of  the package and in all advertising that the  diskette(s) 


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 128  


             are "Shareware."

        6.   The package must contain a written explanation that the disk 
             is   for  evaluation  purposes,  and  that   an   additional 
             "registration  fee"  is  expected  by  the  author,  if  the 
             material is used beyond an initial evaluation period.

        7.   In the case of distribution via any telecommunications link, 
             the following must be done:

             An error checking protocol must be used.

             The individual files must be combined into, and  transferred 
             in a library or archive format.  

        8.   Shareware  distribution  is  permitted only  in  the  United 
             States, Canada, England, and Australia.





































        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 129  


                                      INDEX
        Accordance, 54
        ACHG, 7, 89
        Acitivate, 5
        Alarm, 3, 25, 31, 44, 79, 90
        Alarmwindow, 6, 79
        ALFD, 82
        ALIST, 7, 83, 84
        Alt-A, 4, 8, 51, 54, 95
        Alt-B, 8, 95
        Alt-C, 8, 16, 22, 88, 95
        Alt-D, 8, 18, 43, 66, 84, 94, 97, 120
        Alt-E, 4, 8, 22, 51, 52, 54, 97
        Alt-F, 4, 8, 26, 51, 52, 54, 97, 105
        Alt-J, 8, 97
        Alt-K, 8, 97, 121
        Alt-L, 8, 70, 97
        Alt-M, 8, 68, 97, 108
        Alt-N, 8, 87, 97
        Alt-O, 8, 18, 19, 61, 70, 98
        Alt-P, 8, 98
        Alt-Q, 8, 18, 30, 98
        Alt-R, 8, 36, 98
        Alt-S, 4, 8, 51, 52, 69, 98
        Alt-U, 4, 51, 52
        Alt-X, 8, 16, 17, 55, 98
        Alt-Y, 8, 98, 121
        Alt-Z, 4, 8, 38, 51, 52, 99
        AMSAT-OSCAR, 5, 13, 28, 58, 59, 61, 120
        AMTOR, 2, 7, 8, 9, 11, 12, 13, 14, 15, 18, 20, 21, 22, 25, 26, 27, 
          31, 32, 35, 36, 44, 45, 49, 50, 51, 64, 65, 70, 72, 73, 80, 83, 
          84, 89, 90, 95, 96, 97, 98, 99, 101, 106, 107, 108, 109, 113, 116, 
          117, 120, 121, 122
        AMTOR-FEC, 20
        APPENDIX, 9, 10, 16, 19, 48, 49, 50, 109, 111, 114, 118, 121, 122, 
          123, 124, 127
        ARQ, 3, 7, 8, 25, 31, 32, 84, 89, 90, 95, 96, 97
        Arrow, 4, 8, 20, 51, 52, 53, 99, 100
        Arrows, 30, 100, 121
        ASCII, 2, 5, 7, 8, 11, 12, 13, 14, 19, 20, 40, 46, 58, 59, 83, 84, 
          93, 96, 99, 100, 104, 105, 106, 107, 114, 120, 122, 125
        Attack, 5, 59
        AUTO-Upload, 104
        AutoCQ, 21, 107, 121
        Automatic, 2, 5, 12, 13, 14, 18, 19, 20, 22, 25, 26, 29, 37, 45, 
          50, 60, 64, 70, 71, 82, 83, 93, 94, 98, 107, 111, 112, 121, 124, 
          125, 126
        Automatically, 12, 13, 15, 23, 32, 38, 46, 47, 50, 51, 52, 55, 67, 
          72, 87, 88, 101, 103, 106, 107, 112, 114, 115, 121

        Batteries, 16, 57, 111
        Battery, 15, 57


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 130  


        Baud, 6, 7, 8, 15, 16, 19, 59, 67, 77, 78, 84, 85, 91, 93, 100, 101, 
          110, 111, 120, 126
        BAUDOT, 2, 7, 8, 11, 12, 14, 20, 21, 59, 82, 83, 84, 91, 96, 99, 
          100, 120, 121, 122
        Baudrate, 8, 20, 100, 118
        BBS, 1, 3, 4, 5, 6, 7, 8, 9, 13, 16, 20, 28, 30, 31, 36, 37, 38, 
          39, 42, 44, 45, 55, 56, 60, 63, 64, 70, 71, 72, 76, 82, 83, 86, 
          96, 99, 101, 102, 104, 105, 111, 114, 120, 121, 122
        BBSZapp, 64
        Beacon, 5, 7, 9, 12, 13, 14, 21, 25, 31, 37, 38, 43, 50, 51, 58, 
          59, 61, 62, 63, 64, 65, 66, 67, 68, 70, 71, 83, 86, 90, 102, 106, 
          107, 108, 109, 113, 116, 117, 118, 119
        Beep, 5, 64, 66, 102
        Bell, 46, 59, 121
        BIT, 19, 77
        Bits, 6, 77, 78, 102, 111, 126
        Blink, 25, 60
        BottomWindow, 6, 79
        Bridge, 7, 13, 22, 85, 88, 89, 122
        BTEXT, 67, 106
        Buffer, 2, 5, 8, 9, 12, 19, 26, 27, 30, 45, 46, 57, 65, 76, 88, 95, 
          96, 97, 99, 109, 114, 118, 119, 120
        Bug, 20, 121
        Bugs, 9, 109, 121, 125
        Bulletin, 20, 72, 82, 113, 121
        Bulletins, 13, 42, 72, 82, 86, 111

        Call, 2, 3, 4, 5, 6, 8, 13, 14, 16, 18, 21, 22, 24, 25, 28, 29, 30, 
          31, 32, 34, 35, 36, 37, 39, 41, 42, 43, 44, 50, 51, 52, 53, 55, 
          59, 60, 61, 62, 65, 70, 71, 72, 73, 74, 75, 79, 85, 86, 88, 89, 
          90, 91, 93, 94, 95, 96, 97, 98, 99, 102, 103, 104, 106, 108, 110, 
          112, 113, 114, 115, 120, 121, 122, 123, 124
        Calls, 5, 22, 24, 25, 26, 30, 32, 37, 55, 57, 58, 62, 63, 64, 70, 
          71, 73, 79, 83, 88, 90, 95, 97, 98, 102, 106, 108, 109, 117, 119, 
          121
        Callsign, 2, 5, 7, 13, 15, 18, 20, 22, 24, 25, 30, 31, 32, 33, 35, 
          36, 43, 46, 49, 50, 52, 55, 56, 60, 67, 68, 69, 70, 71, 72, 73, 
          81, 85, 86, 87, 89, 90, 92, 93, 94, 99, 101, 102, 103, 104, 106, 
          107, 109, 112, 113, 116, 117, 119
        Callsigns, 5, 55, 64, 69, 70, 72, 117
        Capture-to-Disk, 3, 5, 18, 20, 23, 42, 43, 47, 61, 64, 65, 71, 81, 
          92, 94, 99, 102, 121, 126
        CFROM, 75, 95
        CGA, 9, 109, 123
        Character, 12, 16, 24, 25, 27, 30, 35, 37, 38, 39, 40, 41, 45, 46, 
          47, 48, 49, 50, 51, 52, 55, 60, 61, 68, 69, 70, 82, 87, 89, 92, 
          102, 103, 105, 108, 109, 111, 112, 113, 117
        Chime, 33, 69
        CHIRPCOPY, 7, 14, 26, 83, 84
        CMD, 2, 24, 26, 109
        CMSG, 18, 62, 63, 65, 76
        Color, 6, 7, 14, 22, 78, 79, 80, 81, 86, 87, 126


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 131  


        Colors, 6, 13, 15, 17, 64, 78, 81, 98, 102, 109, 118, 119, 120, 121, 
          126
        Column, 52, 103, 121
        Command, 4, 5, 9, 11, 13, 14, 16, 17, 18, 23, 24, 25, 26, 27, 30, 
          33, 34, 35, 36, 37, 38, 39, 46, 47, 48, 49, 50, 52, 55, 56, 57, 
          58, 61, 62, 63, 64, 66, 67, 68, 69, 70, 71, 72, 73, 74, 79, 82, 
          86, 89, 91, 92, 93, 95, 97, 99, 100, 102, 104, 105, 106, 109, 110, 
          112, 114, 115, 116, 117, 118, 121
        Commands, 10, 11, 15, 19, 37, 39, 40, 41, 58, 61, 62, 63, 64, 66, 
          100, 101, 102, 109, 111, 118, 119, 120, 121
        Comments, 1, 39, 51, 52, 55, 103, 122
        Common, 5, 23, 64, 73, 95, 102, 110
        Conference, 7, 9, 13, 22, 36, 85, 87, 88, 89, 109, 110, 119, 122
        CONFIG, 9, 101, 103, 104
        Configuration, 2, 11, 12, 17, 18, 19, 34, 43, 48, 57, 60, 61, 73, 
          81, 82, 85, 87, 101, 110, 111, 125, 126
        Connect, 2, 3, 5, 8, 12, 13, 14, 16, 20, 22, 24, 25, 28, 29, 30, 
          31, 32, 33, 34, 35, 36, 38, 44, 45, 46, 50, 51, 57, 58, 59, 60, 
          63, 64, 65, 66, 67, 68, 70, 75, 76, 83, 86, 87, 88, 90, 95, 96, 
          97, 98, 103, 104, 106, 107, 108, 110, 112, 113, 114, 116, 119
        Connected, 6, 9, 12, 13, 21, 22, 28, 30, 32, 33, 34, 38, 47, 48, 
          49, 61, 64, 67, 68, 70, 72, 76, 79, 80, 81, 85, 87, 88, 89, 104, 
          110, 112, 114, 115, 120
        CONOK, 63, 75
        Contest, 2, 3, 5, 6, 12, 14, 18, 19, 20, 21, 44, 45, 54, 64, 69, 
          70, 75, 98, 121, 122, 124
        Control-F, 105
        Control-Q, 111
        Control-S, 111
        Control-Z, 8, 100
        CONVERSE, 2, 9, 11, 26, 27, 48, 50, 58, 68, 88, 89, 90, 109, 114
        Copy, 1, 15, 25, 37, 40, 58, 90, 91, 92, 93, 108, 114, 123, 124, 
          125, 126, 127
        CP, 122
        CQ, 2, 3, 6, 7, 9, 14, 18, 21, 22, 25, 26, 29, 31, 36, 37, 57, 64, 
          74, 75, 85, 86, 87, 90, 91, 93, 97, 101, 106, 107, 108, 109, 117, 
          118, 119, 121
        CQTEXT, 74
        Ctdsk, 3, 39, 42, 47, 64
        CTEXT, 5, 6, 18, 57, 58, 62, 63, 65, 75, 76, 113
        Ctrl-Z, 8
        Customize, 17, 71, 75, 95, 118, 119, 120
        CW, 7, 8, 83, 84, 89, 90, 91, 93, 94, 96, 100, 120, 121
        CWID, 90

        DBF, 5, 6, 8, 23, 51, 54, 73, 74, 103, 124
        DCD, 5, 64, 70, 88, 102, 110, 121
        DCD-Flag, 110
        Deactivate, 5, 57, 58
        Defaults, 13, 15, 19, 57, 102
        Digipeat, 5, 13, 21, 33, 36, 64, 66, 72, 86, 102, 103, 114, 120
        Digipeated, 31, 66, 67


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 132  


        Digipeater, 33, 67, 72, 75, 95
        Digipeaters, 33, 116
        DIR, 6, 9, 14, 17, 32, 33, 34, 35, 36, 41, 67, 70, 74, 101, 103, 
          114, 115
        Directories, 5, 64, 73, 87
        Directory, 3, 5, 6, 14, 27, 28, 31, 32, 34, 36, 39, 41, 43, 45, 46, 
          47, 56, 67, 73, 74, 102, 103, 106, 114
        DISCONNECTED, 9, 31, 36, 61, 67, 70, 87, 110, 111, 116
        Display, 3, 13, 22, 24, 25, 36, 44, 45, 47, 51, 53, 54, 58, 61, 65, 
          66, 68, 70, 74, 78, 81, 84, 85, 86, 87, 96, 97, 99, 102, 110, 111, 
          119, 121, 125, 126
        Displayed, 16, 20, 21, 22, 27, 31, 42, 52, 55, 60, 64, 66, 69, 74, 
          82, 86, 91, 92, 93, 99, 100, 126
        Displaying, 22, 92
        Displays, 17, 19, 20, 22, 36, 37, 47, 55, 65, 81, 83, 99, 124
        DOVE, 125
        Downlink, 34
        Download, 3, 5, 6, 9, 13, 30, 38, 39, 48, 50, 73, 74, 90, 102, 106, 
          113, 114, 115, 117
        Drop-link, 121
        DUPLEX, 11, 12

        EAS, 102
        EAX, 34, 103
        Echo, 5, 23, 25, 64, 66, 79, 102, 120, 121
        Echo-As-Sent, 120
        Edit, 3, 4, 8, 13, 17, 19, 23, 28, 39, 40, 41, 42, 43, 44, 47, 51, 
          52, 53, 54, 73, 96, 97, 101, 104, 105, 118, 119, 120, 121
        Editor, 13, 19, 23, 40, 41, 61, 107, 121
        EGA, 123
        End, 4, 8, 12, 13, 18, 24, 30, 35, 39, 40, 41, 42, 44, 51, 52, 53, 
          61, 68, 69, 70, 71, 99, 100, 102, 109, 117, 121, 127
        Enter, 3, 5, 8, 12, 17, 24, 25, 26, 30, 31, 32, 35, 36, 37, 38, 39, 
          40, 42, 43, 44, 47, 49, 50, 52, 54, 55, 56, 62, 64, 69, 70, 73, 
          78, 86, 88, 91, 92, 93, 96, 97, 98, 101, 112
        EOF, 39, 42, 49, 101, 105, 112, 117, 121
        Erase, 3, 45, 46
        Error, 11, 16, 19, 30, 48, 68, 79, 88, 109, 112, 115, 116, 117, 118, 
          128
        Errors, 110
        Escape, 16, 28, 51, 52
        Events, 9, 44, 110, 123, 125
        Explicit, 106

        Features, 5, 9, 11, 14, 17, 41, 44, 48, 61, 66, 87, 103, 106, 114, 
          120, 122, 125
        FEC, 2, 7, 9, 14, 25, 26, 27, 36, 89, 90, 96, 97, 98, 109
        Files, 2, 3, 4, 8, 13, 15, 17, 18, 19, 21, 23, 27, 28, 29, 30, 38, 
          39, 40, 41, 43, 44, 45, 47, 48, 50, 52, 55, 56, 61, 65, 66, 67, 
          73, 82, 101, 103, 104, 105, 106, 107, 112, 113, 114, 115, 121, 
          125, 126, 127, 128
        Filetype, 17, 54, 107, 113, 117


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 133  


        Fine, 106
        Firmware, 17, 122, 123
        Flashing, 20, 21, 22, 31, 36, 61, 65, 69, 81, 100
        FSK, 100
        Function, 2, 4, 11, 12, 13, 14, 16, 19, 23, 26, 27, 28, 29, 30, 35, 
          36, 37, 42, 43, 47, 51, 52, 53, 54, 55, 58, 61, 64, 66, 70, 71, 
          84, 88, 89, 90, 93, 94, 97, 98, 99, 103, 104, 105, 109, 114, 116, 
          121

        Gateway, 116
        Greek, 9, 16, 77, 111

        Handshake, 16, 66, 102, 121
        Header, 6, 13, 31, 37, 42, 56, 60, 70, 79, 89, 107, 113, 115, 118, 
          119, 120
        HEADERLN, 102
        Headers, 17, 22, 31, 37, 60, 72, 86, 102
        Hercules, 109
        HF, 2, 6, 7, 8, 11, 17, 18, 23, 32, 51, 65, 74, 79, 83, 84, 87, 88, 
          102, 103, 111, 118, 119, 120, 121, 124
        Highlight, 53, 54
        Highlighted, 51, 52, 54

        Indicator, 13, 21, 25, 65, 69
        Inhibit, 122
        Inhibitor, 37
        Intermittent, 9, 109, 111
        InWindow, 6, 67, 78, 86
        IRQ, 77
        IRQs, 121

        KA-Node, 34, 103
        KA-Nodes, 34
        KAM, 1, 10, 11, 17, 18, 26, 58, 59, 70, 73, 77, 84, 86, 87, 91, 93, 
          102, 109, 119, 120, 121
        Kaypro, 10, 119
        Kenwood, 122
        KM, 38
        KN, 70, 99, 121
        KPC, 1, 10, 57, 119, 121

        Labeled, 121
        LAN, 9, 13, 14, 17, 20, 23, 24, 27, 32, 43, 48, 49, 50, 54, 56, 59, 
          62, 65, 67, 69, 70, 71, 75, 92, 94, 104, 105, 110, 111, 112, 114, 
          116
        LAN-LINK, 1, 2, 3, 4, 6, 7, 8, 9, 10, 11, 13, 14, 15, 16, 17, 18, 
          19, 20, 21, 22, 23, 24, 25, 26, 27, 28, 29, 30, 31, 32, 33, 34, 
          35, 36, 37, 38, 39, 40, 41, 43, 44, 46, 47, 48, 49, 50, 52, 54, 
          57, 59, 60, 61, 62, 63, 64, 65, 66, 67, 68, 70, 71, 72, 73, 74, 
          75, 76, 77, 81, 82, 83, 84, 87, 88, 89, 90, 92, 94, 95, 97, 101, 
          102, 103, 105, 106, 107, 108, 109, 110, 111, 112, 113, 114, 115, 
          116, 117, 118, 119, 120, 121, 122, 123, 124, 126


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 134  


        Left, 20, 27, 38, 40, 41, 43, 48, 78, 82, 99, 100, 106, 108, 111, 
          113, 121
        Link, 5, 12, 17, 18, 20, 22, 24, 26, 27, 30, 32, 33, 34, 43, 48, 
          49, 54, 62, 64, 65, 67, 69, 70, 75, 84, 88, 89, 92, 94, 96, 100, 
          102, 105, 106, 107, 109, 111, 116, 126, 128
        LM, 38, 39, 105
        Lockout, 60, 121
        Lockup, 9, 111
        Log-to-disk, 64
        Logbook, 5, 6, 12, 23, 29, 50, 51, 52, 53, 54, 55, 64, 65, 73, 74, 
          96, 103, 119, 121, 124
        LogWindow, 6, 78

        Mail, 1, 7, 9, 13, 20, 22, 37, 38, 39, 50, 58, 65, 66, 70, 71, 72, 
          75, 83, 84, 85, 86, 89, 90, 95, 101, 102, 106, 107, 108, 113, 115, 
          116, 117, 119, 123
        Mail-Snatch, 5, 37, 71, 119
        Mailbox, 5, 7, 9, 12, 13, 14, 25, 57, 58, 65, 89, 90, 91, 104, 106, 
          108, 109, 113, 116, 121
        MARS, 7, 8, 15, 21, 82, 91, 92, 120, 121
        MBX, 9, 50, 86, 95, 101, 104, 116
        Menu, 2, 3, 4, 5, 7, 8, 11, 12, 13, 15, 16, 18, 19, 25, 26, 28, 29, 
          30, 31, 39, 41, 44, 45, 47, 48, 50, 51, 53, 54, 55, 57, 58, 59, 
          61, 63, 64, 68, 72, 76, 79, 80, 81, 83, 85, 88, 89, 91, 93, 94, 
          95, 97, 98, 99, 101, 102, 103, 104, 105, 109, 110, 112, 114, 120, 
          121, 122
        Menus, 11, 23, 28, 78, 109
        Message, 3, 4, 5, 8, 9, 12, 13, 14, 16, 18, 19, 20, 28, 30, 34, 37, 
          38, 39, 42, 43, 45, 47, 48, 49, 50, 55, 56, 58, 64, 65, 66, 67, 
          68, 69, 70, 71, 74, 76, 78, 88, 90, 91, 92, 96, 97, 100, 101, 104, 
          105, 106, 107, 108, 109, 111, 112, 113, 114, 115, 116, 117, 121, 
          122
        Meta, 61, 62, 63, 64
        Metabeacon, 62, 63, 121
        MFILTER, 111
        MFJ, 1, 10, 11, 17, 26, 58, 59, 73, 77, 118, 120
        MH, 24, 64, 79, 114, 115, 119
        MHWindow, 6, 78
        Mode, 2, 3, 4, 5, 6, 7, 9, 11, 12, 13, 14, 16, 18, 19, 20, 21, 22, 
          24, 25, 26, 27, 28, 29, 31, 32, 34, 36, 37, 38, 40, 41, 42, 43, 
          45, 46, 48, 50, 51, 52, 53, 54, 55, 57, 58, 59, 60, 61, 63, 64, 
          65, 66, 67, 68, 69, 70, 72, 73, 75, 76, 80, 81, 82, 83, 84, 85, 
          86, 87, 88, 89, 90, 91, 92, 93, 94, 95, 96, 97, 99, 100, 101, 102, 
          103, 104, 106, 107, 108, 109, 110, 114, 116, 117, 118, 119, 120, 
          121, 124, 126
        Morse, 2, 7, 8, 11, 12, 14, 20, 25, 83, 84, 91, 93, 94, 97, 99, 100, 
          120
        MRPT, 31
        Multi-user, 37, 83, 87, 121
        MYCALL, 91, 93, 94

        NAVTEX, 7, 20, 83, 85, 120


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 135  


        NDMON, 121
        NET, 14, 32, 33, 34, 36, 67, 103, 105, 111
        NNNN, 92, 94
        NODE, 5, 11, 14, 16, 32, 33, 34, 64, 67, 102
        NTS, 83, 122

        OutWindow, 6, 45, 78, 109

        Packet, 1, 2, 3, 7, 8, 9, 11, 12, 13, 14, 18, 20, 21, 22, 23, 24, 
          25, 26, 27, 28, 30, 31, 32, 34, 35, 36, 38, 43, 44, 45, 46, 50, 
          51, 57, 58, 59, 60, 61, 63, 64, 65, 66, 67, 68, 70, 72, 73, 74, 
          78, 79, 83, 84, 85, 86, 89, 95, 96, 97, 98, 99, 100, 102, 106, 
          107, 108, 109, 110, 111, 114, 116, 117, 118, 119, 120, 121, 125
        PacketCluster, 5, 35, 36, 73, 96, 98, 102, 121, 122
        PacketClusterZap, 21
        PACLEN, 121
        PBBS, 76
        PBMON, 121
        PC-HAM, 12, 50, 54, 103, 124
        PgDn, 4, 40, 43, 44, 51, 53, 56
        PgUp, 4, 8, 40, 51, 53, 99
        Pick, 3, 39, 43, 121
        PK, 1, 10, 11, 15, 17, 18, 22, 26, 57, 58, 59, 70, 71, 72, 73, 75, 
          77, 82, 83, 84, 85, 86, 87, 88, 90, 91, 92, 93, 94, 97, 100, 102, 
          103, 109, 110, 111, 116, 118, 119, 120, 121
        Possible, 106
        Presents, 43
        Prompt, 6, 26, 30, 31, 35, 57, 60, 62, 71, 73, 79, 82
        PromptWindow, 6, 78
        Putting, 106

        QBM, 4, 5, 9, 47, 48, 73, 102, 113, 114, 115
        QBU, 4, 6, 47, 48, 74, 102, 105, 117, 121
        QBU-RX, 6, 9, 48, 74, 101, 102, 105
        QBU-TX, 6, 9, 48, 74, 101, 102, 105
        QDB, 4, 9, 47, 49, 114, 115, 121
        QJG, 9, 50, 117
        QJL, 10
        QMH, 9, 13, 114, 115, 119
        QNO, 9, 48, 49, 68, 113, 116, 117
        QRA, 4, 9, 14, 50, 116
        QRM, 11, 19, 25, 60, 65, 116
        QRT, 6, 9, 21, 60, 65, 75, 76, 95, 108, 116, 117
        QRU, 4, 9, 47, 49, 50, 104, 116, 117
        QRV, 6, 9, 48, 49, 75, 76, 112, 117
        QRZ, 2, 8, 29, 30, 62, 64, 96, 98
        QSL, 9, 43, 48, 49, 50, 52, 60, 62, 64, 112, 117, 122, 124
        QSM, 4, 9, 47, 48, 106, 107, 115, 121
        QSO, 12, 21, 22, 23, 26, 36, 45, 47, 63, 65, 69, 70, 84, 86, 90, 
          93, 107, 109
        QSP, 4, 5, 9, 21, 47, 49, 64, 68, 101, 104, 112, 116, 117
        QSY, 60, 65


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 136  


        QTA, 4, 9, 47, 50, 101, 106, 117, 121
        QTC, 5, 9, 13, 21, 64, 65, 66, 67, 68, 71, 102, 106, 107, 117
        QTC-Snatch, 107, 108, 119
        QYD, 9, 117
        QYU, 9, 117

        Radio, 1, 2, 11, 12, 13, 59, 61, 83, 95, 100, 111, 112, 114, 119, 
          120, 122, 124
        Recognize, 11, 16, 18, 25, 67, 108
        REJECT, 65, 75
        ReMember, 3, 12, 30, 31, 35, 68, 86, 89, 103
        Repeat, 9, 25, 48, 99, 107, 115
        Restart, 18, 45, 63
        RETRIES, 88
        RH, 72
        RM, 38, 72
        RN, 38, 72
        Robot, 2, 3, 7, 8, 18, 19, 21, 22, 25, 44, 61, 62, 63, 64, 65, 89, 
          90, 91, 96, 98, 106, 121, 124
        Route, 58, 61
        RTTY, 5, 7, 14, 15, 21, 25, 58, 59, 83, 84, 90, 92, 99, 100, 121, 
          122
        Runfile, 3
        RXR, 59
        RY's, 121

        SAREX, 5, 7, 14, 21, 58, 59, 60, 61, 62, 63, 64, 81, 102, 121
        Scheduler, 13, 44, 45
        Screen, 3, 9, 14, 15, 19, 26, 28, 37, 40, 42, 43, 44, 51, 55, 56, 
          64, 67, 78, 79, 85, 88, 91, 92, 93, 96, 99, 100, 102, 111, 112, 
          126
        Screwed, 51
        Scroll, 23, 40, 78, 99
        Scrollback, 8, 99
        ScrollBackWindow, 6, 78
        SELCAL, 5, 8, 14, 15, 21, 22, 26, 31, 32, 35, 36, 72, 73, 91, 92, 
          93, 96, 98, 101
        Semiautomatic, 12, 50, 69
        Shift, 2, 8, 20, 27, 59, 85, 87, 91, 92, 93, 100, 105
        Shut-down, 121
        Shutting, 58
        Sideband, 100
        SIGNAL, 7, 8, 13, 14, 16, 20, 25, 46, 50, 66, 83, 84, 85, 90, 94, 
          95, 97, 99, 100, 110, 119, 120, 121
        SOLO, 6, 7, 22, 76, 85, 86
        ST, 122
        Stack, 121
        STANDBY, 7, 83, 84, 89, 90
        Status, 2, 5, 15, 19, 20, 25, 31, 36, 57, 58, 60, 61, 62, 64, 65, 
          66, 68, 69, 74, 78, 81, 82, 85, 86, 88, 89, 91, 92, 93, 100, 109, 
          119, 121, 126, 127
        StatusWindow, 6, 78


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 137  


        Stream, 6, 7, 8, 62, 80, 81, 86, 87, 89, 96, 97, 98, 110
        Streams, 17, 22, 87, 89, 97, 98, 110
        Sub-directory, 115
        Sub-menu, 71, 72, 73, 74, 76, 81
        Sub-modes, 21
        Subject, 37, 42
        Suffix, 27, 28, 43, 55, 68, 105
        SYS, 3, 7, 8, 9, 15, 16, 17, 18, 25, 36, 38, 39, 43, 48, 54, 57, 
          64, 68, 73, 75, 81, 82, 88, 89, 92, 94, 101, 102, 103, 104, 110, 
          111, 113, 118, 119, 120, 121, 123

        TheLink, 32, 103
        Time-out, 109
        Timer, 25, 62, 63, 108
        Timestamp, 102
        TNC, 1, 2, 5, 6, 8, 9, 10, 11, 12, 13, 15, 16, 17, 18, 19, 24, 25, 
          26, 27, 28, 29, 31, 33, 34, 35, 36, 41, 45, 46, 47, 48, 57, 58, 
          61, 62, 63, 64, 66, 67, 70, 72, 75, 76, 77, 78, 83, 84, 86, 87, 
          88, 89, 92, 94, 95, 96, 97, 101, 102, 103, 106, 109, 110, 111, 
          114, 118, 119, 120, 121, 122, 123, 125, 126
        Traffic, 7, 22, 50, 59, 60, 66, 71, 85, 86, 87, 110
        Trigger, 5, 14, 37, 60, 68, 71, 102, 108
        TXR, 59
        TXT, 6, 18, 24, 41, 46, 65, 74, 90, 109
        Type-ahead, 26

        Un-mark, 52
        UNPROTO, 63, 87
        Unshift, 59, 92
        Unshift-on-space, 20
        Upload, 6, 9, 38, 49, 74, 83, 113, 114, 115, 116, 117
        Uppercase, 3, 45, 46, 72
        USOS, 8, 20, 59, 91, 92, 100

        Verbose, 72

        Watch, 111
        Window, 2, 15, 19, 20, 23, 24, 25, 26, 27, 30, 31, 36, 40, 41, 42, 
          43, 47, 56, 58, 60, 61, 64, 65, 66, 68, 69, 74, 78, 79, 80, 81, 
          82, 85, 86, 89, 91, 92, 93, 98, 99, 100, 119, 120, 121
        Windows, 27, 40, 42, 43, 79, 81
        Wpm, 84, 100, 121

        XFLOW, 19, 111

        YAPP, 2, 9, 17, 103, 117, 122
        Yellow, 20, 21, 22
        Yourcall, 35, 38, 47, 66, 67, 68, 98, 108, 116
        YYMMDD, 8, 23, 43, 47, 103, 121, 126

        Zap, 3, 7, 8, 31, 35, 37, 42, 44, 45, 60, 70, 71, 72, 82, 96, 98, 
          99


        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990

        LAN-LINK VERSION 1.58 PAGE 138  


        ZapBBS, 20, 21, 70, 71
        Zapp, 64, 71, 83
        ZCZC, 92, 94



















































        LAN-LINK.DOC (c) G3ZCZ 1988, 1989, 1990