Program STSORBIT

                  Space Shuttle and Satellite Orbit Simulation















                                  Version  9027
                                  July 01, 1990




                             by David H. Ransom, Jr.
                             Rancho Palos Verdes, CA

                               BBS: (213) 541-7299


   Program STSORBIT Space Shuttle Orbit Simulation                    Page i




                                TABLE OF CONTENTS
                                -----------------

   INTRODUCTION ......................................................1
   PROGRAM DESCRIPTION ...............................................4
   THE STSORBIT GROUND TRACK DISPLAY .................................6
   STSORBIT'S ORBITAL MODELS .........................................8
   STSORBIT FILES ....................................................10
   STARTING PROGRAM STSORBIT .........................................11
   STSORBIT MAIN MENU ................................................14
     F1  Program STSORBIT Demonstration (STS-29) .....................14
     F2  Read NASA/NORAD 2-Line Elements .............................15
     F3  Read Prior Mission Information from *.INI File ..............16
     F4  Enter New Orbital Information ...............................16
     F5  Adjust Orbital Parametrers ..................................17
     F9  DOS Shell ...................................................18
     F10 Set STSORBIT Program Options ................................18
     ENTER  Resume Prior Mission .....................................18
     ESC    Quit STSORBIT (Save Current Mission) .....................19
   PROGRAM OPTIONS MENU ..............................................20
     F1  Program STSORBIT Information ................................20
     F2  Set New Local Coordinates ...................................20
     F3  Enable/Disable Additional Map Grid Lines ....................22
     F4  Display NASA Tracking Stations ..............................22
     F5  Show Ascending & Descending Node Data .......................23
     F6  Set Map Center (USA/Europe) .................................23
     F7  Set for SLOW COMPUTER or NO COPROCESSOR .....................23
     F8  Set/Reset Satellite Symbol Blinking .........................24
     F9  Set UTC Time Offset and Daylight Flag .......................24
     F10 Enable/Disable Printer Logging ..............................25
   USING DISPLAY OPTIONS .............................................27
   ADJUSTING ORBITAL PARAMETERS ......................................29
   STSORBIT REVISION HISTORY .........................................31


   Program STSORBIT Space Shuttle Orbit Simulation                    Page 1


   INTRODUCTION
   ------------

        Program STSORBIT is an orbital tracking and display program for use 
   during Space Shuttle missions, for simulating a Space Shuttle mission, or 
   for general satellite tracking using NASA/NORAD 2-Line Elements. STSORBIT 
   is free for non-commercial use. Use it if you like it, discard it if you 
   don't. There are no warranties of any kind. If you wish to use STSORBIT 
   commercially, write for license information. The only request I make of 
   users is that they take the time to complete and return the confidential 
   questionnaire in file README. The questionnaire gives users a chance to 
   offer comments and suggestions, and lets me know that people use and 
   appreciate program STSORBIT.
        Program STSORBIT is intended to display the approximate orbital 
   position and ground track of the Space Shuttle on a global map during a 
   typical NASA mission. When used with NASA/NORAD 2-Line Elements, other 
   satellite ground tracks may also be displayed. An IBM-compatible computer 
   is required. When used with an EGA or VGA video adapter, the display is in 
   color; CGA and HGC systems can only present graphics in monochrome. In the 
   past, NASA has not published or made available very precise information as 
   to the orbital parameters either before or during a "normal" mission; 
   recently, however, more accurate data has been published in magazines such 
   as Aviation Week and in various NASA publications. NASA now also releases 
   the "2-Line Elements", classical orbital elements which enable much more 
   precise calculation of orbital positions. Military missions, of course, are 
   almost completely blacked out. It is something of a challenge, therefore, 
   to devise a program which will at least come close and which, as more or 
   different information becomes available, will permit the program's data to 
   be updated "on the fly". The primary objective is to present an interesting 
   and attractive real time graphics display of a Space Shuttle mission or 
   satellite ground track, rather than to generate mathematically precise 
   positional information.
        The initial premise of STSORBIT was to attempt to duplicate the wall 
   map in NASA's Mission Control Center in Houston, Texas. Before I started 
   this project, I had seen  several other programs which attempted to do that 
   same task, but each fell short of my objectives for one reason or another; 
   since then other programs have appeared which produce similar information, 
   most notably Paul Traufler's excellent TRAKSAT. It may be, of course, that 
   others will judge this effort lacking as well. One problem is that of size 
   and resolution: the wall map at Mission Control Center is some twenty feet 
   wide with an impressive pixel resolution, very different from the typical 
   personal computer and the size and resolution of its monitor. The NASA wall 
   map shows essentially the entire globe in a cylindrical projection; 
   STSORBIT uses a cylindrical projection but restricts the vertical display 
   to latitudes from +80 degrees to -80 degrees in order to achieve reasonable 
   proportions and vertical resolution while at the same time showing 
   recognizable land features.
        As a consequence of the basic inaccuracies relative to the orbital 
   parameters of a Space Shuttle mission while it is in progress, I did not 
   originally try to be especially precise with respect to the orbital 
   mathematics. Additionally, mathematical complexity must be held to a 
   reasonable minimum if older computers not equipped with a math coprocessor 
   are to be able to maintain the presentation in real time. The higher 
   resolution and color graphics available with more advanced displays such as 
   the EGA and VGA greatly enhance the program, but my Zenith laptop computer 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 2


   emulates the older CGA graphics display in (blue) monochrome. Therefore, in 
   order to use my own program on all of my computers, STSORBIT maintains 
   compatibility with all three display standards. Recently, compatibility 
   with HGC (Hercules Graphics Card) has been improved.
        My somewhat casual attitude toward mathematical precision changed with 
   the launch of the Hubble Space Telescope (HST) and the regular availability 
   of NASA/NORAD 2-Line Elements via modem. Until HST, I had been content to 
   update the orbital data occasionally during the course of a typical five 
   day mission and live with the errors inherent in my original orbital model. 
   The accuracy of that model degrades rapidly after ten or twenty orbits and, 
   although it may be the only method available at the start of a mission, 
   more accurate data is now readily available within a day or so of launch. 
   Beginning with Version 9022, therefore, STSORBIT was modified to also read 
   orbital data from these 2-line elements and maintain significantly improved 
   accuracy over longer periods of time. As an incidental benefit, the ground 
   tracks of other satellites (such as the Russian space station MIR) may now 
   also be displayed. At present, the orbital model (SGP4) used with 2-line 
   elements is accurate only for low Earth orbits; deep space orbits, defined 
   as orbits having an orbital period greater than or equal to 225 minutes, 
   require a more complex orbital model (SDP4). STSORBIT calculates data and 
   displays a ground track for deep space objects but the accuracy of these 
   data has not been tested. The SDP4 orbital model may be added to STSORBIT 
   at a later time.
        A brief biographical note: I am a retired physicist and engineer who 
   has spent all of his professional life in the world of electronics, data 
   communications and, more recently, computers. As a young man I was actively 
   involved in the early American space program, including projects such as 
   Ranger, Mariner, Mercury, and Apollo; my interest in space has continued to 
   this day. The desire to "keep in touch" with our Space Shuttle missions was 
   one of the principal incentives in the development of this software. If 
   STSORBIT also serves to help spark the interest of young people in science 
   and technology or can be a learning tool at any level, I will have more 
   than achieved my goal.
        In addition to individual users all over the world, STSORBIT is also 
   being used in an educational setting in several instances. At a middle 
   school in Kansas, the program is projected in the school auditorium from 
   time to time during a mission to show the children graphically what is 
   happening and to give them a sense of "real time" participation in our 
   space program. At an Air Force training facility, STSORBIT is one of many 
   tools used to prepare Air Force officers for their duties in the Air Force 
   Space Command.
        As with most of the programs which I have written recently that are 
   intended for public distribution, STSORBIT was first written using 
   Microsoft's QuickBASIC, Version 4.50. (The current versions use Microsoft 
   BASIC Compiler Version 7.00 for improved performance.) While not 
   necessarily the most efficient language that might have been used, BASIC is 
   by far the best known computer language, the single language available to 
   almost any programmer regardless of experience or computer environment, and 
   is relatively inexpensive. Many of the SUB and FUNCTION procedures in 
   STSORBIT have been lifted more or less intact from my program ASTROCLK. 
   While not included as part of the public program distribution, the complete 
   program, including source code, is available by mail (see below).
        For others who are interested in our space program and who have access 
   to a modem, I recommend NASA's SpaceLink Bulletin Board System in 
   Huntsville, Alabama, (205) 895-0028, available twenty four hours per day. 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 3


   NASA SpaceLink, supervised by Bill Anderson of the NASA Marshall Space 
   Flight Center, provides a wealth of information on NASA and its projects. 
   In addition to educational materials, general information on NASA programs 
   and plans, news releases, and graphics images from prior spacecraft 
   missions such as Voyager, SpaceLink also devotes a complete section to 
   current news and information on the Space Shuttle. I particularly 
   appreciate the STS Mission Press Kit, available about two weeks before each 
   mission, which provides a great deal of information on the upcoming 
   mission, payload and crew as well as broadcast schedules on NASA Select 
   Television, Satellite F2-R, Transponder 13. Mission status reports are 
   generated daily during the course of a mission. I regularly call SpaceLink 
   and post files of interest on my own bulletin board system (BBS).
        Special thanks to Paul Traufler whose programs STS95 and TRAKSAT not 
   only demonstrate excellent accuracy but his documentation also spells out 
   the factors which generate the major perturbations to low Earth orbits. 
   While the accuracy of STSORBIT still does not quite equal Paul's method, it 
   has been substantially improved. My thanks as well for Paul's help in 
   upgrading STSORBIT to use the NASA/NORAD 2-Line Elements.
        My thanks also to Brian K. Jones and his program SUNMAP (available on 
   my BBS), an interesting program in its own right, for the initial map 
   coordinate data file used in that program. SUNMAP served as a demonstration 
   that a reasonable world map display WAS possible, particularly on EGA and 
   VGA monitors, and encouraged me to start this STSORBIT project.
        Finally, thanks as well to all those individuals who have taken the 
   time to call me or leave a message on my BBS with comments and suggestions. 
   While I haven't been able to implement every suggestion, many are now 
   included.
        For current orbital information (if a mission is in progress), current 
   NASA/NORAD 2-line element sets, and the most recent version of the program, 
   call my bulletin board system (BBS) at (213) 541-7299. If the BBS has not 
   answered by the third ring, hang up, wait TWO MINUTES, then call back; the 
   system has a power controller and if the system is off it takes that long 
   for the computer to boot and do its housekeeping chores. If you do not have 
   access to a modem or if you wish the full source code for STSORBIT, you may 
   send US$10.00 to cover materials, postage and handling for a copy of the 
   latest version; please specify 5-1/4" 360K or 3-1/2" 720K disks.


                                           David H. Ransom, Jr.
                                           7130 Avenida Altisima
                                           Rancho Palos Verdes, CA 90274

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 4


   PROGRAM DESCRIPTION
   -------------------

        A typical Space Shuttle orbit is nearly, but almost never exactly, 
   circular with an altitude of approximately one hundred and sixty nautical 
   miles plus or minus thirty nautical miles and an inclination of from about 
   28 degrees through about 57 degrees. Occasional missions, especially 
   military missions, fly at higher altitudes and/or inclinations and often 
   use more elliptical orbits. Little of this information is known to very 
   good accuracy by the casual listener.
        Initially, therefore, the interested would-be mission observer may 
   have only the time and date of launch to initialize a tracking program. 
   Given the geographical coordinates of the Kennedy Space Center, assuming a 
   circular orbit, and using the typical altitude and inclination of a Space 
   Shuttle orbit, the data should be sufficient to give at least a rough idea 
   of the Shuttle's position for the first several orbits. After that, 
   additional information is required if the position is going to be very 
   close.
        Fortunately, Mission Control Center does occasionally announce the 
   orbital altitude, which is usually in the neighborhood of about one hundred 
   and sixty nautical miles; the reader is cautioned that the popular press 
   and television often (but not always) convert the orbital altitude to 
   statute miles with the inevitable confusion resulting. If a television 
   viewer has access to NASA Select Television on Satcom F2R, Transponder 13, 
   he will periodically see Mission Control Center's huge wall map on which 
   the current position of the Space Shuttle is always displayed. Using this 
   display, the careful viewer can make a visual estimate of the longitude of 
   the ascending or descending node, the point at which the orbit crosses the 
   Earth's equator in the Northbound or Southbound direction respectively. Not 
   exactly high-tech data acquisition, but better than nothing at all!
        Given all of these uncertainties, I did not feel it necessary or 
   worthwhile to try to hone the mathematics of my "simple" orbital model in 
   program STSORBIT beyond that required to give an approximate position in 
   real time. Coincident with the Hubble Space Telescope mission I added the 
   J2 perturbation factor for improved accuracy.
        As an example, STSORBIT was used to track STS-31, Discovery and the 
   Hubble Space Telescope, and gave an accurate position over more than 25 
   orbits. Whenever practical, I generate the information required by STSORBIT 
   as an initialization file, for example HST.INI for the Hubble Space 
   Telescope, which may be read directly by the program and which uses the 
   most current data. These .INI files are normally posted on my BBS during a 
   mission. When orbital parameters change during a mission, as was the case 
   with STS-31, new .INI files are posted as soon as the new data are 
   determined. 
        Within a day or two of launch, the NASA/NORAD 2-line elements are 
   usually available and will yield a more accurate position over longer time 
   periods provided no orbital maneuvers are made. Using NASA/NORAD 2-line 
   elements is quite simple. No adjustment of orbital parameters is necessary 
   when using the 2-line elements. All that is required is to obtain the 
   current 2-line elements file (from my BBS or elsewhere), enter the name of 
   the file (for example, NASA710.TXT) and the name of the desired satellite 
   (HST for Hubble Space Telescope). STSORBIT takes care of all the rest. The 
   2-line element set available at the time of this release of STSORBIT is 
   included in the program files. The data for each satellite included in the 
   2-line element set is referenced to a specific date and time, the "Epoch" 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 5


   of the data. As a general rule, orbital calculations will be relatively 
   accurate for 10 to 20 days after the Epoch date; the lower the orbit, the 
   greater the effect of factors such as atmospheric drag and the less 
   accurate the calculations will be as time passes. Users who prepare their 
   own 2-line element files are cautioned to make certain no extraneous lines 
   are included, that the satellite name is on a single line, and that the two 
   data lines exactly conform to the 69-character/line format.
        Particularly with the relatively low resolution (640x200) of a CGA 
   monitor, the display errors alone are significant; using an EGA or VGA 
   monitor improves the vertical resolution by about a factor of two (640x350 
   or 640x480, respectively), but does nothing to improve the horizontal 
   resolution. The HGC (Hercules Graphics Card) has also been included; HGC 
   users will note that of the 720 horizontal pixels available, only the left 
   640 pixels are used in the present code. Higher resolution monitors are 
   available (at a price!) but are not in general use and so are not suitable 
   for a program such as STSORBIT which is intended for public distribution. 
        STSORBIT displays a portion of the Earth using a cylindrical 
   projection of the surface area almost from one pole to the other; a small 
   area near each pole (approximately ten degrees) is omitted to maintain 
   optimum map proportions. The map shows most of the Earth's land boundaries, 
   and continental areas and major oceans are easily recognizable. At any 
   time, the display shows the Space Shuttle or satellite as a small symbol, 
   the projected orbit for approximately the next three orbits (or four and a 
   half hours), and the orbit track for the past orbit (or one and a half 
   hours).
         The program may be operated in real time or in "fast time", which is 
   ten or sixty times normal time. For "simple" orbits, the orbital parameters 
   may be manually entered or adjusted for the desired mission, or a pre-
   programmed demonstration may be run to permit the user to become familiar 
   with the program and its display. The lower section of the screen displays 
   current data about the mission in progress.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 6


   THE STSORBIT GROUND TRACK DISPLAY
   ---------------------------------

        The STSORBIT ground track display consists primarily of a map of the 
   world extending from approximately +80 degrees to -80 degrees using a 
   linear cylindrical projection. Omitting the two 10 degree bands at the 
   poles permits better detail in the mid latitudes where all space shuttle 
   orbits and many other satellite orbits are concentrated. Ground track 
   details very near the poles are therefore sacrificed for a better display 
   in the main portion of typical orbits. The vertical resolution of the 
   display is automatically adjusted for the type of display system in use 
   from 200 lines (CGA) to 480 lines (VGA).
        Centered around the user's geographic location is a magenta "circle" 
   of the approximate line of sight visibility for the mission in progress. 
   The circle appears on the display as an ellipse because of the scaling 
   factors used by the map projection. The radius of this circle of visibility 
   is calculated for each satellite based upon its current altitude and the 
   user's elevation above mean sea level. Actual visibility, of course, 
   depends upon more than simply whether or not the satellite is above the 
   viewer's horizon. Most important is the sun/earth/satellite/viewer 
   geometry; the satellite must be in sunlight and the viewer in darkness for 
   reasonable visibility. Almost as important is the size and geometry of the 
   satellite itself; a large, bright-metal satellite with huge solar arrays 
   reflects far more sunlight than a small dark satellite. In addition to the 
   satellites themselves, many booster rockets and other "spare parts" are 
   orbiting the Earth. Since they are not attitude stabilized, booster rockets 
   usually are tumbling and may therefore appear to flash on and off as they 
   pass over.
        For the Space Shuttle as well as most other satellites with near 
   circular orbits, the circle of visibility calculations are reasonably 
   accurate; however, the position of the sun and the effect of atmospheric 
   refraction are not taken into account, only whether or not the satellite is 
   in line of sight view of the observing location. For highly eliptical 
   orbits, however, the accuracy is substantially degraded since the radius of 
   the circle of visibility changes dramatically depending upon whether the 
   satellite is nearer apogee or perigee at the time the calculation is made 
   and the period of the orbit. In the course of a single pass overhead, such 
   a satellite's altitude may change by thousands of miles. Satellite "DE 1", 
   usually included in the NASAnnn.TXT 2-line elements file, is in a highly 
   elliptical orbit with long period and illustrates the problem.
        The world map consists of a series of some 7500 coordinate pairs. When 
   used with an EGA or VGA color monitor, the coastal outlines are in cyan, 
   the equator and longitude grid are in blue, the Space Shuttle or satellite 
   is in white, the projected orbit is in green, and the past orbit track is 
   in red. On HGC, EGA and VGA monitors, the two TDRS satellites (Tracking and 
   Data Relay Satellites), used for most communications to and from the Space 
   Shuttle, are shown as a dot inside a small circle in yellow on the equator, 
   and the various NASA ground tracking stations (and their approximate 
   antenna range) may be displayed. CGA and monochrome monitors, of course, 
   display everything in a single color.
        Orbital calculations are performed every second in real time and every 
   ten or sixty seconds in "fast time", and the position of the Space Shuttle 
   or satellite symbol is updated every ten (real time or X10) or every sixty 
   (X60) seconds. The predicted orbit and past orbit track markers are updated 
   every sixty seconds, primarily to avoid "cluttering" the display with too 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 7


   many dots scattered around. Each dot therefore represents one minute of 
   time along the orbit. When the program is first started, three hours of 
   predicted orbits are traced and the program "catches up" to real time. As 
   the mission continues, the orbit track will be left behind until 
   approximately six hours of ground track are visible, one and a half hours 
   of past ground track and four and a half hours of predicted ground track. 
   Thereafter, the past and predicted ground track will "move" as time passes, 
   with one dot of past ground track removed from the display each minute as a 
   new dot of predicted ground track is added to the display.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 8


   STSORBIT'S ORBITAL MODELS
   -------------------------

        The initial version of STSORBIT was prepared without reference 
   materials of any kind and the simplest possible orbital model was therefore 
   selected. The primary objective was to duplicate the NASA wall map at 
   the Mission Control Center in Houston, Texas. This "simple" model assumed 
   that the orbit was perfectly circular at a specified altitude and 
   inclination which never degraded due to other factors such as drag or 
   perturbation. Some simplifying assumptions were incorporated to handle the 
   initial ascent portion of a mission and the launch site was hard coded to 
   Cape Canaveral, Florida. With only minor modifications, the program was 
   essentially unchanged for the next year.
        The launch of STS-31 and the Hubble Space Telescope highlighted the 
   need for improved accuracy because of public interest and the length of the 
   mission. The orbital calculations were modified (STSORBIT Version 9015) to 
   include the J2 factor, the perturbation of low Earth orbits due to 
   variations in the gravitational field related to the non-spherical shape of 
   the Earth (among other factors); omission of the J2 factor caused errors in 
   longitude of approximately -5 to -7 degrees per day. That is, the orbital 
   track drifted Westward from its true position by that amount. More accurate 
   models of low orbits also include the J3 and J4 perturbation factors, 
   atmospheric drag, and a host of other less significant items.
        Although by now reasonably accurate for the first day or so of a space 
   shuttle mission, the "simple" model is by no means ideal. In calculating 
   the current orbital longitude, for example, the "simple" model assumes a 
   circular orbit with an orbital inclination of zero degrees. For orbits with 
   low inclinations, as is typical for launches from Kennedy Space Center, 
   these errors are not particularly significant and are probably overshadowed 
   by the fundamental uncertainties in orbital parameters and by the 
   limitations imposed by display resolution. Orbits with higher inclinations, 
   as would be the case if near-polar launches from Vandenburg AFB in 
   California are ever initiated, would have much larger periodic errors which 
   would be both noticeable and objectionable. More important for longer 
   missions and for general satellite tracking is the fact that due to the 
   method used, errors in the orbital calculations tend to be cumulative. 
   Although it may be the only method available at launch, after about a week 
   the errors can become unacceptably large.
        The real problem with the simple method, of course, is that the Earth 
   is not a perfect sphere and actual satellite orbits are never perfectly 
   circular. Satellite orbits are significantly perturbed by the non-spherical
   gravitational field of the Earth, by the Sun and Moon, and other factors. 
   Accurate satellite tracking over longer periods of time therefore demands 
   more accurate data and a more rigorous treatment of satellite orbits. The 
   only practical alternative is to use the NASA/NORAD 2-line element sets. 
   Not only are the data readily available publicly, but they are relatively 
   accurate and are updated regularly. 2-line element sets for non-military 
   space shuttle missions are typically available by the second or third day 
   of the mission.
        Six quantities are required by classical gravitational theory to 
   completely characterize the orbit of one body about another in time and 
   space, the "Two Body Problem". These six quantities, often referred to as 
   Keplerian orbital elements, are included in the NASA/NORAD 2-line element 
   sets along with other numerical and statistical data. NORAD, the North 
   American Air Defense Command headquartered in Cheyenne Mountain, Colorado, 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 9


   developed the 2-line element format many years ago as part of their 
   satellite tracking efforts and NASA subsequently adopted the same format -- 
   more or less. My own analyses of 2-line element sets obtained independently 
   from other NASA centers suggest that NASA and NORAD do not always use the 
   same definition for revolution (orbit) numbers; NASA frequently gives a 
   number one greater than NORAD, calling the first partial orbit number one. 
   Except for short duration missions, such as the Space Shuttle, revolution 
   numbers are of no practical importance.
        Having timely and accurate orbital data is of little help without a 
   computer model or program which can use those data. NORAD has rather 
   arbitrarily divided satellite orbits into two categories: near Earth orbits 
   and deep space orbits. Near Earth orbits are defined as those with orbital 
   periods of 225 minutes or less and deep space orbits are all others. 
   Computer models are described in the literature for each category. STSORBIT 
   employs the SGP4 Near Earth Model only, using a composite of code of my own 
   combined with translated Fortran and Basic source supplied by Paul Traufler 
   and C source by Paul Hirose. Not only are the near Earth orbits generally 
   of more interest to observers, but the errors associated with deep space 
   orbits processed with the SGP4 model rather than the correct SDP4 model are 
   not particularly significant for the purposes of a program such as 
   STSORBIT. Watching a geostationary satellite orbit on the screen is not 
   unlike watching grass grow and is about as exciting.
        For the past several years, T S Kelso has been making the NASA/NORAD 
   data available as a public service on his Celestial BBS at (513) 427-0674. 
   The 2-line element sets are downloaded by Kelso directly from NASA Goddard 
   Space Flight Center by special arrangement. I regularly post a slightly 
   edited version (certain introductory text material is removed so that the 
   file may be used directly by programs such as STSORBIT) of the current 
   element sets on my own RPV ASTRONOMY BBS as file NASAnnn.TXT, where "nnn" 
   is the NASA bulletin number. Kelso provides data for several categories of 
   satellites:  Amateur Radio, Earth Resources, Manned Spacecraft, Navigation, 
   Weather, and NASA's 30 Day Specials (which contain objects launched within 
   the last 30 days and are often easy to spot visually). More specifically, 
   these include the following satellites or satellite series: OSCAR, Radio 
   Sputnik, UOSAT, Cosmos, LandSat, SeaSat 1, SPOT, Mir, Salyut 7, Soyuz, 
   Space Shuttle, NAVSTAR (GPS), GOES, Meteor, and NOAA.                                                 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 10


   STSORBIT FILES
   --------------

        STSORBIT is normally distributed in archived format using either the 
   PAK or ZIP format. The following files are usually included:

             STSORBIT.EXE        Main program        (required)
             STSORBIT.DOC        Documentation       (not required)
             STSORBIT.MAP        World map data      (required)
             STSORBIT.CTY        City coordinates    (optional)
             STSORBIT.INI        Initialization data (optional)

             MSHERC.COM          Hercules driver     (required for HGC)

             NASAnnn.TXT         2-Line Elements     (optional)
             STS35.INI           HST Sample File     (optional)
             STS35.TXT           HST 2-Line Elements (optional)

             STS386.PIF          Windows 3.0         (386 enhanced mode)
             STS286.PIF          Windows 3.0         (normal mode)

             README              STSORBIT Confidential Questionnaire

   Files noted as "(required)" must be in the current default directory for 
   program operation. Files noted as "(optional)" do not need to be in the 
   default directory when STSORBIT is operated but provide additional features 
   or information if present. If file STSORBIT.INI is not present it will be 
   created.

        Program MSHERC must be executed before running STSORBIT for systems 
   equipped with Hercules Graphics Cards or Hercules Graphics Plus Cards. 
   STSORBIT will otherwise report an error and remind the user to run MSHERC.

        File NASAnnn.TXT (where "nnn" will be a number such as "713") is a set 
   of NASA/NORAD 2-line elements as of the program release date. Note that the 
   2-line elements should only be used for ten to twenty days after the epoch 
   date for each satellite if reasonable accuracy is to be maintained. File 
   HST.TXT is the 2-line element data for the Hubble Space Telescope extracted 
   from the NASAnnn.TXT file. File HST.INI contains simple orbital model data 
   for the Hubble Space Telescope; the launch time and date must be corrected 
   to reflect the date actually launched.

        The two PIF files have been tested with Microsoft Windows Version 3.0. 
   File STS386.PIF uses the 386 enhanced mode and file STS286.PIF uses the 
   normal mode. Since a PIF file includes specific filename and directory 
   information, each file will have to be edited to reflect the drive, 
   directory, and filenames actually in use. (The samples included use drive 
   I: and subdirectory STSORBIT.)

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 11


   STARTING PROGRAM STSORBIT
   -------------------------

        To start program STSORBIT, enter one of the following commands:

             STSORBIT            (any monitor, CGA/HGC/EGA/VGA)

             STSORBIT /EGA       (force EGA or lower monitor)

             STSORBIT /CGA       (force CGA monitor)

             STSORBIT /M         (force monochrome operation, EGA/VGA)

             STSORBIT /EUR       (center map on Prime Meridian)

             STSORBIT /R         (resume last mission automatically)

             STSORBIT /S         (force shuttle icon for speed)

        Only one display option (/EGA or /CGA or /M) may be used. Options may 
   be combined and entered in any order. For example, using the following 
   command will resume the prior mission, force the shuttle icon, and force 
   EGA mode:

             STSORBIT /R/S/EGA


                                    * * * * *

                       Hercules Graphics Card USERS NOTE:
                       ----------------------------------
                              
        Run the program MSHERC prior to running STSORBIT. This Microsoft 
   program works with QuickBASIC 4.5 to enable use of the Hercules Graphics 
   Card. One user reported that setting the HGC to FULL and selecting Page 
   Zero (using software supplied with the HGC) was sufficient for proper 
   operation with program STSORBIT. At least one HGC "clone" user reported 
   improper operation.

                                    * * * * *


        If you have already run STSORBIT (or if you have file STSORBIT.INI) 
   and simply wish to resume viewing that same mission, use the /R command 
   line option. STSORBIT will sense the monitor type, enable color for EGA and 
   VGA systems, read the map data as usual, then proceed directly to plotting 
   the mission. The data from the last run, as saved in file STSORBIT.INI, is 
   used to initialize the program. Once started in this manner, pressing the 
   ENTER (or RETURN) key after plotting has started will return to the Main 
   Menu.
        European users, or those users accustomed to viewing a map of the 
   world centered on the Prime Meridian at zero degrees longitude (Europe), 
   may include the /EUR by itself or in addition to other options.
        The program automatically checks for the presence of a VGA or EGA and 
   will execute in color if one is found UNLESS the /M command line option is 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 12


   used to force monochrome operation. However, if you wish to operate 
   STSORBIT in the EGA mode when you have a VGA monitor, use the /EGA option. 
   In cases where a monochrome monitor is connected to an adapter which 
   simulates color with gray scale, the /M command line option may be omitted 
   but the various portions of the display may or may not be visible. STSORBIT 
   depends upon Microsoft QuickBASIC to determine whether or not a particular 
   monitor type is available. Some video adapter boards which claim to be VGA 
   are not recognized as such by QuickBASIC and therefore cannot be used in 
   the higher resolution VGA display mode. Similarly, "clone" Hercules 
   Graphics Cards do not always perform correctly.
        The /M option is not required for HGC and CGA graphics operation, 
   since those adapters always render their high resolution graphics in 
   monochrome. Naturally, the operation of the program is enhanced by the use 
   of a color monitor. The vertical resolution is also adjusted depending upon 
   the type of adapter which has been detected. The program checks for the 
   presence of a math coprocessor and will use it if found. Once STSORBIT has 
   started, the display type may not be changed without halting the program at 
   the Main Menu with the ESC key, then restarting the program with the new 
   option selection(s). 
        STSORBIT normally selects the icon or symbol used to graphically 
   represent the satellite based upon the mission name. Names which start with 
   the letters "STS" will use the space shuttle icon and all other missions 
   will use an icon resembling the Hubble Space Telescope. However, the "other 
   satellite" symbol has approximately three times as many pixels (dots) as 
   does the space shuttle symbol and therefore takes longer to draw and erase. 
   If you are using a slower computer or one not equipped with a math 
   coprocessor, using the "/S" option may improve performance by forcing the 
   use of the space shuttle symbol. The /S option may be used by itself or in 
   combination with other options.
        STSORBIT first reads in the map coordinates from file STSORBIT.MAP, 
   which must be in the current drive and directory. These coordinates are 
   converted to screen coordinates for the type of monitor detected and stored 
   internally so that they need only be read once. For slower processors, 
   systems equipped only with floppy disks, or systems without a math 
   coprocessor, this may take several minutes; there are over 7,500 sets of 
   coordinates to process for the world map. By processing the map data as it 
   is loaded, the time to subsequently display the map is much reduced. As the 
   map coordinates are being read, the initial title screen is shown on the 
   display. The "Percent processed" shows how much of the map data has been 
   processed so far. To cancel program STSORBIT at this point and return to 
   DOS, press ESC.

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9027

                               by David H. Ransom, Jr.

                                Current time: 17:11:42
                               Current date: 06/23/1990

                             Last Mission = HST [NASA710]

                               Loading STSORBIT Map Data 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 13



                                   Please wait ...

                               Percent processed = 70.4%


        When all of the map coordinates have been read from disk and 
   processed, the program presents its Main Menu which allows the user to 
   select the desired program function. Press the Function Key corresponding 
   to the function desired. 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 14


   STSORBIT MAIN MENU
   ------------------

        Once the map coordinates have been stored internally, STSORBIT 
   presents its Main Menu:


                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9027

                                Current time: 17:12:28
                               Current date: 06/23/1990

            F1     Program STSORBIT Demonstration (STS-29)
            F2     Read NASA/NORAD 2-Line Elements from *.TXT File
            F3     Read Prior Mission Information from *.INI File
            F4     Enter New Orbital Information (Simple Orbital Model)
            F5     Adjust Orbital Parameters (Simple Orbital Model)
            F9     DOS Shell (CAUTION: DOS Version 3.x ONLY!)
            F10    Set STSORBIT Program Options
            ENTER  Resume Prior Mission (HST [NASA710])

            ESC    Quit STSORBIT (Save Current Mission)

            Select desired function:  _


   F1     Program STSORBIT Demonstration (STS-29)
   ----------------------------------------------

        The F1 command may be used to demonstrate the operation of STSORBIT 
   and to verify that the program will operate correctly. No other information 
   is required. The demonstration automatically sets up the data to simulate a 
   mission and clears the screen. A slight delay may follow while the program 
   calculates the initial parameters of the orbit. Then the world map is 
   drawn, the ground track for the first three orbits (approximately) is drawn 
   as a series of dots (green for color monitors), and mission data is 
   displayed at the bottom. Mission Elapsed Time (MET) is set to shortly 
   before launch time and counts down to zero.
        When MET reaches zero, the computer's "bell" sounds and the shuttle 
   symbol appears over Cape Canaveral. For CGA and HGC systems, the shuttle 
   will blink; for EGA and VGA systems, the shuttle will be steady. At first 
   the shuttle will move along the ground track very slowly, simulating the 
   ascent phase of the mission. After several minutes the shuttle reaches 
   orbital altitude and proceeds along the ground track normally, passing a 
   dot every minute. Press F (for Fast time) once or twice to speed up the 
   progress of the simulation. Press ENTER to return to the Main Menu.
        Data are displayed by STSORBIT in standard formats:

            4/05/1990       Date in month/day/year
             14:33:00       Time in hours:minutes:seconds
           3/09:23:15       MET in days/hours:minutes:seconds
               -69.34       Longitude and Latitude in degrees

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 15


                            WEST longitude and SOUTH latitude are negative
               320.50 nm    Altitude in nautical miles

   F2     Read NASA/NORAD 2-Line Elements from *.TXT File
   ------------------------------------------------------

        In order to read the NASA/NORAD 2-line elements, you must have a file 
   with that data. Typical files from my BBS system have names such as 
   "NASA710.TXT" where the "710" corresponds to the particular NASA data set 
   and may change several times per week. A sample file is included with the 
   normal distribution of STSORBIT.
        Entering the F2 command will display the following prompts:

             Read NASA/NORAD 2-Line Element File

             Press ENTER to enter the current default
             name as shown in square brackets [...].


             Enter 2-Line Filename  [NASA710.TXT]:

             Enter desired Satellite Name   [HST]:

        In each case, pressing ENTER will select the default choice shown 
   inside the square brackets. For the example shown, the defaults are the 
   file NASA710.TXT and the satellite HST. If you wish to change the 
   information (or if no default is shown), enter the required information 
   followed by ENTER. For the filename, if no filetype is included, STSORBIT 
   will automatically add ".TXT". For the satellite, only sufficient letters 
   to unambiguously identify the desired satellite, upper or lower case, are 
   required. For example, "Alou" would select "Alouette 1". Once this 
   information has been entered, STSORBIT will attempt to locate the specified 
   file and the data for the requested satellite. Once a satellite matching 
   the requested name is found, the data is displayed:

             Satellite Name:              HST
             Elements File:               NASA710.TXT
             Satellite Rec #:             91

             Elements Epoch:              90144.02899116
             Rev at Epoch:                438
             Satellite Number:            20580
             Launch Year:                 1990
             Launch Number:               37
             Launch Piece:                B
             Element Number:              68
             Inclination:                 28.4702
             RA of Ascend Node:           43.2557
             Eccentricity:                .0006169
             Arg of Perigee:              241.1778
             Mean Anomaly:                118.8166
             Mean Motion:                 14.84320861

             Press ENTER to ACCEPT this satellite, OR
             Press any other key to REJECT and continue searching: _

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 16



        If this is the satellite you wish, press ENTER and the data will be 
   entered into STSORBIT. If, on the other hand, a different satellite is 
   desired, press any other key (such as the SPACE BAR) and STSORBIT will 
   search for another name matching the requested satellite. For example, 
   there are a number of NAVSTAR Global Positioning Satellites usually 
   included in the file with official names such as "GPS-0001", "GPS-0002", 
   "GPS BII-01" and so forth; requesting "GPS" will allow you to cycle through 
   all the available choices. The file NASA710.TXT is an ASCII file; it may be 
   helpful to print the file to show the available satellite names. 
        Once the satellite has been selected, STSORBIT will require a brief 
   time to calculate certain required orbital parameters, then will proceed 
   directly to the display of the ground track.


   F3     Read Prior Mission Information from *.INI File
   -----------------------------------------------------

        The F3 command displays all files in the current directory with a 
   filetype of .INI and then prompts the user to enter the name of the desired 
   data file. File STSORBIT.INI is the file which has the data from the last 
   time the program was run; to use file STSORBIT.INI, press ENTER. STSORBIT 
   will automatically supply the filetype .INI if you do not include a 
   filetype. If the requested file is not present, an error will be reported. 
   To create new .INI files, enter the desired data then exit STSORBIT and use 
   the DOS COPY command to copy STSORBIT.INI into a file with a the desired 
   name.
        Two additional .INI files are included (more may be added later), 
   STS28.INI and STS30.INI; these were launched in August 1989 and May 1989 
   respectively. Since Space Shuttle missions normally last only five to ten 
   days, using these files at later dates will generate "unusual" mission 
   elapsed times and orbit numbers! Note that the launch time in these files 
   has been converted to Universal Time (UT); prior releases (Version 9019 and 
   earlier) of these files included the launch time in PACIFIC standard or 
   daylight time.
        STSORBIT also expects your computer clock to be set to the correct 
   local time and date; use the DOS TIME and DATE commands. See the Z command 
   below for information on setting the UTC Zone Offset. Of course, you may 
   "fool" STSORBIT by setting your computer time and date using the DOS TIME 
   and DATE commands, but be aware that for most computers using MS-DOS/PC-DOS 
   3.3 or greater the hardware clock is also set with these commands.


   F4     Enter New Orbital Information (Simple Orbital Model)
   -----------------------------------------------------------

        The F4 command uses the "simple" orbital model and allows the user to 
   enter the orbital altitude, inclination, and launch date/time to determine 
   the orbital parameters. To manually enter orbital data, you will be 
   prompted for the required information. 

        Enter mission title:

   Enter the title of the mission, such as "STS-30 ATLANTIS" without the 
   quotation marks. If you press ENTER, the title "STS Mission Simulation" 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 17


   will be used.

        Enter orbit altitude (nm):

   Enter the orbit altitude (or average orbit altitude for non-circular 
   orbits), in nautical miles. 

        Enter orbit inclination:

   Enter the inclination of the orbit in degrees; a decimal fraction is 
   allowed. For example, STS-30 was flown at an inclination of 28.85 degrees 
   and STS-28 is expected to have an inclination of 57 degrees. Press ENTER
   to use the default value of 28.00 degrees.

        Enter Launch Date (MM/DD/YYYY):

   Enter the date in the format shown. The full four digit year is required 
   and be sure to use the SLASH "/" rather than the MINUS "-" as the 
   separator; STSORBIT's internal date algorithms will interpret the minus 
   sign as just that and some rather strange dates can result! You may also 
   use relative dates: -1 will use the prior day, +2 will use two days hence, 
   and so forth. Press ENTER to use today's date.

        Enter Launch Time (HH:MM:SS):

   Enter the time in the format shown using 24-hour notation and local time. 
   One or two digit numbers may be used as required. [The comma is also 
   acceptable as a separator in place of the colon.] You may omit seconds [or 
   minutes and seconds] if desired. For example, an entry of "16" will be 
   entered as 16:00:00 or 4:00 PM. Press ENTER for "launch" ASAP, as soon as 
   possible; depending upon the system, this will be in from 30 to 60 seconds 
   from the current time.

        Normal or fast time (N,f):

   If the "launch" has not yet occurred, this prompt will allow you to select 
   normal time (x1), x10, or x60 fast time for the display. Press ENTER to 
   select normal time. If you change your mind during the display, use the F 
   command to toggle the time (see below).


   F5     Adjust Orbital Parameters (Simple Orbital Model)
   -------------------------------------------------------

        The F5 command uses the "simple" orbital model and is NOT available 
   when using 2-line elements. When the orbital parameters change in mid-
   mission for the "simple" orbital model, use this command to adjust the 
   orbital period/altitude, orbital longitude, and time along orbital track. 
   This technique allows the "launch time" to remain correct, which in turn 
   assures that Mission Elapsed Time is correct, while adjusting the orbital 
   parameters so that the position is displayed correctly in later orbits. The 
   following items may be adjusted; in each case, the required units or input 
   format is shown in parentheses (...) and the current value of the item is 
   shown within square brackets [...]. Press ENTER to leave an item unchanged.


   Program STSORBIT Space Shuttle Orbit Simulation                    Page 18


             Enter LAUNCH DATE (MM/DD/YYYY)  [05/15/1990]:
             Enter LAUNCH TIME (HH:MM:SS)      [21:45:00]:
             Enter ORBITAL ALTITUDE (nm)        [ 187.23]:
             Enter LONGITUDE adjust (deg)      [   0.000]:
             Enter TIME adjust (min)            [  0.000]:

        In order to make these adjustments, the current orbital altitude is 
   required, along with the longitude and time of one or more equator 
   crossings (obtained from the NASA Television wall map). NASA is not too 
   good about making sure that the map is on the screen when the Shuttle makes 
   an equator crossing (Northbound is Ascending Node, Southbound is Descending 
   Node); they have a distressing tendency to cut away just before the 
   crossing. With sufficient patience, however, the data can be interpolated 
   from the television screen. In the case of STS-30, the orbital time at 
   Orbit 34 changed to 90.85 minutes and the longitude of the descending node 
   was approximately -36 degrees, crossing at 2/2:18:00 MET. See the section 
   ADJUSTING ORBITAL PARAMETERS below for more information.


   F9     DOS Shell (CAUTION: DOS Version 3.x ONLY!)
   -------------------------------------------------

        If a system function is desired at the Main Menu, press F9 to execute 
   QuickBASIC's DOS SHELL function. This will return you to a DOS prompt and 
   most DOS commands may be executed immediately. One of the most frequent 
   reasons to return to DOS is to adjust the system time or date using the DOS 
   commands TIME and DATE. Users of DOS Versions 3.3 and higher should be 
   aware that the TIME and DATE commands for these DOS versions now set not 
   only the SOFTWARE clock in DOS but also the HARDWARE clock.
        When the Shell is executed, STSORBIT remains in memory and the map 
   data will not be re-read when you return. Enter "EXIT" (without the 
   quotation marks and followed by ENTER) at the DOS prompt when you wish to 
   return to STSORBIT. CAUTION: The QuickBASIC SHELL function is only reliable 
   for versions of DOS of 3.0 or higher! Systems with less than 640K memory 
   may fail to execute the shell and applications requiring large amounts of 
   memory may also fail.


   F10    Set STSORBIT Program Options
   -----------------------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. These selections are further described in the section 
   "Program Options Menu" below.

   ENTER  Resume Prior Mission
   ---------------------------

        Pressing ENTER resumes the current mission shown in parentheses at the 
   right. In the example shown, the 2-line elements file used for the data is 
   shown in the square brackets. Any manually entered data is retained. 
   "ENTER" means the key marked ENTER, RETURN, or with a left pointing arrow -
   - but not the backspace or cursor position keys which may also be marked 
   with arrows! (I am afflicted with too long a memory; once upon a time this 
   function was known as Carriage Return and was often shortened to RETURN or 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 19


   even CR. With the advent of electronic typewriters, video terminals, dot 
   matrix printers and all the rest, "Carriages" have long since disappeared 
   but old habits die hard! Most PC keyboards are now marked with "ENTER".)
        Use ENTER to resume plotting a mission in progress after returning to 
   the Main Menu to perform some change (such as enabling the node display, 
   enabling the NASA tracking stations, or adjusting your computer's time).


   ESC    Quit STSORBIT (Save Current Mission)
   -------------------------------------------

        Press ESC (the key marked "ESC" or "Esc", not the letters E+S+C) to 
   quit program STSORBIT. If you press ESC to quit the program and have 
   manually entered orbital data, STSORBIT will save all required mission data 
   in file STSORBIT.INI prior to terminating. This will be the data available 
   with the ENTER key the next time you execute the program. The demonstration 
   data will not be saved, preserving any previously saved mission data.
        When you have finished with STSORBIT, press ESC at the Main Menu to 
   return to DOS. The data (and any adjustments you have made) for the current 
   mission are saved in file STSORBIT.INI, but the map data is lost and will 
   be re-read when you next use program STSORBIT. NOTE: If you have neither 
   entered data (with the E command) nor read a previously saved .INI file 
   (with the F command), no data will be saved when you exit STSORBIT.



   Program STSORBIT Space Shuttle Orbit Simulation                    Page 20


   PROGRAM OPTIONS MENU
   --------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. When used with CGA displays, the features shown below 
   as selected by function keys F3 and F4 are not available because of the low 
   resolution of the CGA display. The following Options Menu is displayed when 
   the F10 command is entered from the Main Menu:

                                   Program STSORBIT

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9027
                                Current time: 17:12:58
                               Current date: 06/23/1990

            F1             Program STSORBIT Information
            F2             Set New Local Coordinates (Rancho Palos Verdes, CA)
            F3     OFF     Enable/Disable Additional Map Grid Lines
            F4     ON      Display NASA Tracking Stations
            F5     OFF     Show Ascending & Descending Node Data
            F6     USA     Set Map Center (USA/Europe)
            F7     OFF     Set for SLOW COMPUTER or NO COPROCESSOR
            F8     ON      Set/Reset Satellite Symbol Blinking
            F9     -7.00   Set UTC Time Offset and Daylight Flag
            F10    OFF     Enable/Disable Printer Logging

            ENTER          Return to MAIN MENU

            Select desired function:


   F1     Program STSORBIT Information
   -----------------------------------

        Function Key F1 displays information about program STSORBIT including 
   the version number, my name and address, and the telephone number of my RPV 
   ASTRONOMY BBS (Bulletin Board System). The current version of STSORBIT is 
   always posted on the BBS. The BBS has a power controller; if it hasn't 
   answered by the THIRD RING, hang up and call back in two minutes.


   F2     Set New Local Coordinates
   --------------------------------

        In order to perform the calculations related to satellite visibility 
   and altitude/azimuth, STSORBIT must know the geographic coordinates for the 
   user's location. The default coordinates are set to Rancho Palos Verdes, 
   California, near Los Angeles. The current location is indicated by the name 
   in parentheses on the Options Menu. The program provides two methods for 
   setting your own coordinates: reading a file of city names and coordinates 
   (STSORBIT.CTY); or manually entering the information.
        Pressing F2 will display the following reminder:

        STSORBIT will search for the CITYNAME you enter anywhere in the city 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 21


        names in the file. For example, 'SAN' appears in 'SAN FRANCISCO', 'SAN 
        DIEGO', 'SANTA ANA', 'THOUSAND OAKS', etc. Press ENTER to cancel the 
        search or enter '*' to enter a new city name and coordinates.

        In other words, when you enter a name or partial name, STSORBIT will 
   attempt to match that group of characters anywhere in the names which 
   appear in the city file. 'SAN' matches 'SAN diego' as well as 'thouSANd 
   oaks'. To get 'SAN FRANCISCO' on the first try, enter 'SAN F' with a space 
   between the N and F. Case is not significant; upper and lower case letters 
   are treated identically. If you change your mind and wish to cancel the 
   operation, simply press ENTER by itself. Use BACKSPACE to make corrections.
        To begin the search, enter the desired name after the prompt. In the 
   example which follows, the name 'ran' was entered for the search.

        Enter CITYNAME to search for:  ran

        Processing record  1
          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city, OR
        Press SPACE to search for next city:  _

        If the city displayed is the one desired, press ENTER and the data 
   will be entered into STSORBIT and subsequently saved in file STSORBIT.INI. 
   If you wish to search further in the file, press the SPACE BAR.

        NOTE: The elevations contained in file STSORBIT.CTY are all zero 
        except for Rancho Palos Verdes, CA and Calaveras County, CA, locations 
        for which I have accurate elevations above mean sea level. If you know 
        the correct elevation, edit the file using any ASCII text editor and 
        change the last number on the line. STSORBIT.CTY contains 
        approximately 720 cities and uses a different format than the .CTY 
        files for program ASTROCLK. If users send me their correct elevations 
        (or additional cities they wish added), I will incorporate that data 
        into subsequent versions of file STSORBIT.CTY.

        To enter location data manually, press "*" (without the quotation 
   marks) followed by ENTER. You will be prompted for the city name, latitude, 
   longitude, and elevation. Latitude and longitude may be entered using three 
   different formats for convenience (note the use of comma and decimal 
   point):

             DDD.DDDDD           Degrees and decimal fraction
             DD,MM.MMM           Degrees, minutes and decimal fraction
             DD,MM,SS.SS         Degrees, minutes, seconds and fraction

   Note that SOUTH latitude and WEST longitude must be entered as NEGATIVE 
   numbers as measured south of the equator or west of Greenwich, 
   respectively. The default unit for elevations is meters above mean sea 
   level; add "F" (upper or lower case without the quotation marks) if you 
   wish to use feet.
        After the elevation has been entered, the data will be displayed for 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 22


   approval. All data are converted to degrees or meters as appropriate, 
   regardless of the units used on input.

          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city, OR
        Press SPACE to cancel this data:  _

   Press ENTER to accept the data as shown or SPACE to cancel the data and 
   return to the Options Menu. If the data is accepted, STSORBIT will ask if 
   you wish to append (add) this city/location to the existing file 
   STSORBIT.CTY so that it will be automatically available thereafter.

        Do you with to append this data to file STSORBIT.CTY (Y/n):  _

   Press "Y" or ENTER to append the data or press "N" to not modify the file.


   F3     Enable/Disable Additional Map Grid Lines
   -----------------------------------------------

        This command is not available for CGA systems. The world map normally 
   includes the equator and the meridians at 0 degrees, 90 degrees, and -90 
   degrees shown in blue on color monitors; the equator and the prime meridian 
   are shown in bright blue. Turning on the map grid adds lines of longitude 
   every 30 degrees and lines of latitude every 10 degrees. Displaying the 
   additional grid lines on monochrome monitors usually makes the screen too 
   "busy" and is not recommended.


   F4     Display NASA Tracking Stations
   -------------------------------------

        The F4 command enables/disables the display of NASA's 14 ground 
   tracking stations; this command is not available for CGA monitors. Each 
   ground tracking station is shown as a small symbol surrounded by a "circle" 
   which gives the approximate area of antenna coverage and shows how small a 
   proportion of each orbit can be monitored without the TDRS system. When for 
   some reason the TDRS system is down (as has occurred during infrequent 
   computer failures at White Sands, New Mexico, the TDRS Ground Station), 
   these ground tracking stations become the only means of communication with 
   the Space Shuttle.
        The antenna range circle is displayed on the screen as an ellipse 
   because of the scaling factors used by the map projection. Some of these 
   ground tracking stations are scheduled to be shut down in the near future 
   due to budgetary constraints. For all systems except CGA, the locations of 
   the two TDRS (Tracking and Data Relay Satellite) are shown as small circles 
   on the equator at -41 degrees and at -171 degrees; on CGA displays the TDRS 
   coverage is NOT shown in order to avoid confusing the display. The 
   following table lists the ground tracking stations which are shown along 
   with their abbreviations and approximate map coordinates (longitude, 
   latitude):

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 23



             MIL     -81,28       Merritt Island, FL
             BDA     -64,32       Bermuda
             DKR     -17,14       Dakar
             ACN     -14,-8       Ascension Island
             MAX     -5,41        Central Spain
             IOS      56,-5       Indian Ocean
             HAW     -156,20      Hawaii
             GWM      145,14      Gwam
             VAN     -122,35      Vandenberg, CA
             YAR      115,-29     Yargidy, Australia
             CAN      149,-36     Canberra, Australia
             GDX     -116,34      Goldstone, CA
             CTS     -105,38      Colorado Springs, CO
             AGO     -71,-34      Santiago, Chile


   F5     Show Ascending & Descending Node Data
   --------------------------------------------

        The nodes of an Earth orbit are the points on the ground track where 
   the path crosses the equator. The ascending node crosses from South to 
   North and the descending node crosses from North to South. Orbit numbers 
   normally increment at the ascending node. This command adds two additional 
   lines of data at the lower left of the screen giving the MET and longitude 
   of the most recent ascending and descending nodes. This information is 
   useful when comparing STSORBIT's data against other sources such as the 
   wall map in Mission Control.


   F6     Set Map Center (USA/Europe)
   ----------------------------------

        The F6 command changes the center of the displayed world map. By 
   default, the map is centered on the United States at 90 degrees West 
   longitude. Most Americans are accustomed to viewing the map in that 
   orientation, but it is sometimes convenient to shift the map center when 
   the Space Shuttle is near the edge of the map. If you prefer to have the 
   map centered at the prime meridian or zero degrees (Greenwich, England), 
   use the F6 command or use the /EUR command line option when starting 
   STSORBIT. Each time you use the F6 command the map center is changed to the 
   alternate meridian and the map data is re-read from disk.


   F7     Set for SLOW COMPUTER or NO COPROCESSOR
   ----------------------------------------------

        Particularly since the addition of the calculations related to 2-line 
   element sets, it has become increasingly difficult for very slow computers 
   or computers not equipped with a math coprocessor to keep up with real time 
   orbital calculations. For example, my vanilla Zenith Z-148, operating at 
   4.77 MHz and no math coprocessor, takes approximately 4.5 seconds to make a 
   full set of orbital position calculations; when switched to 8.0 MHz, the 
   same calculations require only 2.5 seconds. In either case, the program 
   gets hopelessly behind itself and can never catch up.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 24


        While perhaps not the "ideal solution" as compared to having a math 
   coprocessor, setting STSORBIT for Slow Mode can help in all but the most 
   severe cases. Instead of attempting to update its position calculations 
   every second, the update is slowed to every five seconds in this mode. This 
   allows the computer to more or less keep up at a cost of not having data 
   quite in real time on a second-by-second basis. Except for the frequency of 
   updates, all program features are unchanged. When STSORBIT is operating in 
   the Slow Mode, the phrase "SLO" appears at the lower right of the tracking 
   display (above "RNG:").


   F8     Set/Reset Satellite Symbol Blinking
   ------------------------------------------

        The symbol representing the space shuttle or satellite is normally 
   blinking for CGA and HGC systems in order that it may more readily be 
   identified on the monochrome display. On EGA and VGA systems the symbol is 
   bright white which normally is easily located. However, some users may find 
   the blinking symbol distracting and it also requires additional computing 
   time to draw and erase the symbol. STSORBIT may automatically defeat 
   blinking in slower computers. NOTE: Use the "B" command to toggle the 
   blinking on or off while the ground track is displayed.


   F9     Set UTC Time Offset and Daylight Flag
   --------------------------------------------

        STSORBIT uses UT (Universal Time, formerly known as GMT or Greenwich 
   Mean Time) and which is approximately the same as UTC (Coordinated 
   Universal Time), for certain functions such as launch time. This permits 
   data to be used across many time zones without conversion. However, it also 
   means that STSORBIT must know what number of hours to add to UT in order to 
   obtain your local time, and whether or not you are currently using daylight 
   savings time (summer time in the UK).
        When prompted, enter the time offset in hours from your local time to 
   Universal Time. Examples are shown for most time zones in North America. 
   STSORBIT then asks if you are using daylight savings time; enter "0" if 
   not, and "1" if so. The sum of these two values is shown on the Main Menu; 
   for example, if the computer is set to Pacific Daylight Time (UT offset is 
   -8.00 hours and Daylight Flag = 1), the value shown will be -7.00. For most 
   time zones in North America, the correct zone abbreviation will be shown on 
   the ground track display for Local date and time. The values are saved in 
   file STSORBIT.INI. When you change your computer from/to daylight savings 
   time, use this command to update STSORBIT. The following shows the display 
   when using the Z command:


   Set UTC TIME ZONE OFFSET and DAYLIGHT FLAG

             STSORBIT must know the difference between your local time zone 
        and Universal Coordinated Time (UTC), also sometimes known as 
        Greenwich Mean Time (GMT). With this information, STSORBIT can 
        automatically adjust launch or Epoch times and dates for your local 
        time zone. In addition, STSORBIT must know if your computer is now set 
        to STANDARD or DAYLIGHT time.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 25


             First, enter the difference between your STANDARD time zone and 
        UTC in hours. Do NOT include the hour for daylight time if you are now 
        on DAYLIGHT time; it will be entered separately. For most time zones 
        in the United States and Canada, the entries required are:

             Eastern Standard Time     EST    -5.0
             Central Standard Time     CST    -6.0
             Mountain Standard Time    MST    -7.0
             Pacific Standard Time     PST    -8.0

             Enter UTC Offset (hours):          -8
             Enter DAYLIGHT Flag (0=OFF, 1=ON): 1


        Once this information has been entered, it will be saved in file 
   STSORBIT.INI and will not be requested again. If you change from Standard 
   to Daylight Time or vice versa, use the F10 command to update the Daylight 
   Flag. INI files obtained from other users may be from a prior version of 
   STSORBIT and the time information may have to be corrected.


   F10    Enable/Disable Printer Logging
   -------------------------------------
        I have found it interesting to log the orbital data and the ascending 
   and descending node information on my printer when analyzing the mission 
   data over long periods of time. The F10 command toggles the printer logging 
   function on and off. The first page of the log includes the current orbital 
   data and subsequent pages contain only node information. In addition to the 
   information presented on the display, the printer log also calculates the 
   current orbital time, the time from one ascending (descending) node to the 
   next. When printer logging is enabled and the ground track is displayed, 
   the word "LOG" will appear in yellow at the right of the text area. A 
   typical log is shown below. BE SURE THE PRINTER IS TURNED ON PRIOR TO 
   ENTERING THE F10 COMMAND. 


   STSORBIT: Space Shuttle Tracking Program, Version 9027          Page 1

   ORBITAL DATA for STS-31 Discovery/HST

             Launch Date:             04/24/1990
             Launch Time:             05:33:52
             Orbit Inclination:       28.4695
             Orbit Altitude:         329.50 nm

             Adjust Longitude:         9.80
             Adjust Orbit Time:        8.40 min

                                                                  ORBITAL
   LOCAL DATE      TIME              ORBIT    LONG           MET     TIME
   04/28/1990  20:32:52  Ascend Node:   70  -69.95    4/14:58:07  1:36:55
   04/28/1990  21:20:52  Dscend Node:   70   97.64    4/15:46:35  1:36:55
   04/28/1990  22:09:52  Ascend Node:   71  -94.77    4/16:35:02  1:36:55



   Program STSORBIT Space Shuttle Orbit Simulation                    Page 26


        When a printer log is prepared for 2-line orbits, the Adjust Longitude 
   and Adjust Orbit Time entries will not be shown in the header data. The 
   Launch Date and Launch Time entries are replaced by Epoch Date and Epoch 
   Time. Note also that the orbit altitude shown is the altitude at the start 
   of the log and will not be correct for subsequent entries if the satellite 
   has an elliptical orbit (high eccentricity).
        A printer log may be prepared in advance by enabling printer logging 
   from the Main Menu with the F10 command, then starting the ground track 
   display with ENTER, pressing the F key twice to set STSORBIT in the X60 
   fast time mode, and allowing the simulation to run for the desired length 
   of time. When a sufficient number of orbits has been logged, press ENTER 
   twice to return to the Main Menu and to then resume the simulation in real 
   time. While the ground track is active the "L" command performs the same 
   function as the F10+F10 command to enable or disable printer logging.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 27


   USING DISPLAY OPTIONS
   ---------------------

        Once the orbital display is in progress, a number of keys are active:

           ENTER  Return to Main Menu (cancel this simulation)

               B  Toggle the BLINK mode of the space shuttle symbol between 
                  blinking and steady.

               F  Toggle FAST mode from x1 to x10 to x60 to x1, etc.

               R  Resynchronize MET or T+Epoch with Local Time. Resets plot to 
                  real time.

                  NOTE: The Resynchronization was feature was originally 
                  intended only for testing and should only be performed when 
                  the simulated time and local times are reasonably close to 
                  each other. The plot may otherwise have some extraneous 
                  pixels left around! This feature has not been extensively 
                  tested. To restore the ground track completely, press ENTER 
                  to stop the display and return to the Main Menu, then press 
                  ENTER again to resume the mission.

               P  Enable/Disable PAUSE mode; only the local date and time are 
                  updated. The plot is frozen at the current position and the 
                  "+" and "-" commands are enabled.

               +  During PAUSE mode only, moves the satellite to the NEXT 
                  calculated position based upon the FAST mode then in effect: 
                  simulated time is advanced 1, 10, or 60 seconds.

               -  During PAUSE mode only, moves the satellite to the PREVIOUS 
                  calculated position based upon the FAST mode then in effect: 
                  simulated time is backed up 1, 10, or 60 seconds.

                  NOTE: Since this "-" or reverse feature was implemented 
                  primarily for testing and demonstration, the ground track 
                  logic does not recognize these reverse movements and will 
                  become slightly convused. To restore the ground track 
                  completely, press ENTER to stop the display and return to 
                  the Main Menu, then press ENTER again to resume the mission.

               L  Enable or disable printer logging. If logging is enabled, 
                  the word LOG appears in the lower right of the screen. Be 
                  sure the printer is turned on BEFORE using the L command.

        The Pause command is active in the normal as well as the "catch up" 
   modes. The Fast and Resynchronize commands are only active during the 
   normal plotting mode. The simulated time, taking into account any fast time 
   that may have been in effect up to that point, is shown at the lower left 
   of the screen. For reference, the launch or epoch time and the actual local 
   time (as determined by the computer's internal DOS clock) are also 
   displayed. The MET (Mission Elapsed Time) or T+Epoch display at the lower 
   right of the screen shows the current elapsed time in the mission and will 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 28


   include an additional message, "(x10)" or "(x60)", when fast time is in 
   effect.
        When using 2-line elements or when the launch has already occurred 
   (you have entered a date and time that is in the past), the program goes 
   back approximately two hours then "catches up" and plots the position of 
   the Space Shuttle as it does so. The program plots a point for each minute 
   during that time, so it can take a few minutes to get up to real time. 
   Computers with 8088 processors and/or without a math co-processor may 
   require a considerable time for this process. Once the plot reaches the 
   current time, it will slow to real time and resume normal plotting. Using 
   this technique, you may re-plot the orbit after receiving improved orbital 
   information or resume a plot after an interruption.

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 29


   ADJUSTING ORBITAL PARAMETERS
   ----------------------------

        The original "simple" orbital model used in STSORBIT is imperfect, to 
   say the least. The data generally available from NASA prior to launch often 
   does not describe upcoming shuttle orbits at all precisely. In particular, 
   STSORBIT's initial orbital calculations, those related to the time from 
   liftoff to orbital insertion, are more or less guesswork. Once a mission is 
   established in orbit, it may be therefore desirable to adjust the orbital 
   parameters to make STSORBIT's displayed ground track correspond more 
   closely to that displayed on the wall map in Mission Control Center. To 
   make the adjustment, use the following procedure:

   1.   Start program STSORBIT. After the map data has been read in, select 
        the program options command, F10, then press F5 to enable display of 
        the data for the ascending and descending nodes. Enter the original 
        launch time and orbital data using the F4 command or restore prior 
        data using the ENTER key or F3 command if no adjustments have been 
        entered. The plot will appear on the screen.

   2.   Observe the crossing time and longitude of the node of interest and 
        calculate the difference from the desired crossing time. Note that 
        NASA performs all orbital calculations referenced to the Ascending 
        Node, the point at which the ground track crosses the Equator in a 
        North-bound direction. In order to view a given node crossing 
        repeatedly, you may find it convenient to reset the DOS clock to a 
        minute or two prior to the expected time.

        HINT: Use the F9 command to go back to DOS, then use DOS's TIME 
        command to set the clock. BE SURE TO RESET YOUR COMPUTER CLOCK WHEN 
        YOU HAVE COMPLETED ALL ORBITAL ADJUSTMENTS!

   3.   When adjusting orbital parameters, it is preferable to adjust the TIME 
        before adjusting the LONGITUDE. This is because the longitude of the 
        node is affected by the rotation of the Earth (by 15 degrees per hour) 
        when the time is changed. Calculate the difference between the time of 
        the observed node crossing and the time of crossing plotted by 
        STSORBIT. If the observed time is earlier than the plotted time, the 
        time adjustment must be positive, otherwise it must be negative. The 
        time must be calculated in minutes and decimal fractions of a minute.

   4.   Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the new orbital altitude in nautical miles (or 
        altitude in kilometers by adding "km"); usually, the orbital altitude 
        has not changed and you should press ENTER to leave this item 
        unchanged.

   5.   Press ENTER to leave the longitude adjustment set at zero.

   6.   Enter the calculated time difference for the node crossing as the time 
        adjustment (in minutes).

   7.   Press ENTER to leave the launch time unchanged.

   8.   Inspect the data displayed to be sure it is correct. If it is not, 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 30


        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSORBIT will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSORBIT, and press ENTER to 
        resume current mission.

   9.   Again observe the plotted time of crossing and repeat from Step 4 if 
        the time is not correct. If the time is correct, note the longitude of 
        the node and calculate the difference from the observed longitude. If 
        the plotted longitude is less than the observed longitude, the 
        adjustment must be positive, otherwise it must be negative. The 
        longitude adjustment must be entered in degrees and decimal fractions 
        of a degree.

   10.  Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the calculated longitude adjustment, then press 
        ENTER twice to leave the time adjustment and launch time unchanged.

   11.  Inspect the data displayed to be sure it is correct. If it is not, 
        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSORBIT will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSORBIT, and press ENTER to 
        resume current mission.

   12.  This procedure should enable you to set the orbital parameters with 
        considerable accuracy. However, even minor changes of the orbit in 
        flight can cause a significant cumulative error in the ground track 
        displayed by STSORBIT. If all this seems like too much effort, just 
        enjoy the program "as it comes from the box"!

   13.  During the course of a non-military mission, I normally watch NASA 
        Select TV (if I'm around!) and post updated .INI files from time to 
        time on my BBS. You may call the BBS and download the updated .INI 
        files; these files typically have names such as STS31A.INI, STS31B.INI 
        and so forth. Use the F3 command to read the updated .INI file into 
        program STSORBIT. Also, within a day or two of a Space Shuttle launch, 
        the 2-line elements for the mission will usually be available on my 
        BBS.


   Program STSORBIT Space Shuttle Orbit Simulation                    Page 31


   STSORBIT REVISION HISTORY
   -------------------------

        Program STSORBIT underwent multiple revisions during the first days of 
   the STS-30 Atlantis/Magellan mission (May 1989) and the process was 
   repeated during the STS-28 Columbia mission (August 1989). At one point, I 
   was releasing new versions every couple of hours! Lacking any equations or 
   data for the first minutes of a typical mission, the first tries were 
   largely guesswork and needed to be refined considerably. After all of that, 
   comparison of STSORBIT's plot with the NASA wall map data (as seen on NASA 
   Select Television) and interpolation of that data shows good agreement 
   through about the first ten orbits. However, after orbital maneuvers, such 
   as occur with the deployment of a satellite or spacecraft, the initial data 
   is much less accurate. Unfortunately, the NASA wall map is not always on 
   the screen and orbital information may otherwise be difficult to obtain 
   during the first day or two of a mission.
        The launch of the Hubble Space Telescope (May 1990) and the 
   availability of the NASA/NORAD 2-Line Element Sets has prompted a major 
   revision of the program at Version 9022 to permit accurate tracking over 
   longer periods of time using these data. This has required a major rewrite 
   of the program which required many days of effort. As with any major 
   software change, not all problems and bugs are detected in the first 
   releases. User feedback and patience will be appreciated.
         Each released version of STSORBIT uses a four digit revision code 
   such as 8916. The first two digits indicate the year and the second two 
   digits indicate the week of the year. In some cases, an additional letter 
   suffix is added to distinguish changes occurring within the same week. A 
   partial week at the beginning or end of the year is counted as a full week. 
   Using this method, a year will typically have 53 weeks although it is 
   possible to have 54 weeks in a leap year (1972 is an example). The current 
   year-week revision code is shown on the Julian Date display, Display Mode 
   7, in my program ASTROCLK.
        This file records the revision history of program STSORBIT through all 
   of the minor twists and turns that usually accompany the evolution of such 
   a program.  It illustrates the tortuous process of maintaining and refining 
   a program as ideas and problems are reported from every quarter. The early 
   versions were rushed to meet the launch schedules, probably too much so. 
   These notes may also be helpful to users who are upgrading from one version 
   to another to find out what has changed.

                                                 David H. Ransom, Jr.
   9027      7/01/90
   -----------------
   -Rewrote main menu to use Function Keys and added new secondary menu for 
   program options. Special keys used during map display are unchanged.
   -Documentation extensively revised to reflect menu changes and additional 
   features.
   -Added Slow Mode for very slow computers or systems without a math 
   coprocessor. Position calculations performed every five seconds rather than 
   every second when in this mode.
   -Added circle of visibility to map showing the approximate area about the 
   observing location through which the current satellite may be seen.
   -Added Range, Altitude and Azimuth to current position calculations.
   -Added local observing coordinates and ability to read STSORBIT.CTY with 
   approx. 720 city locations. NOTE: The city file includes the local 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 32


   elevation but all elevations are set to zero since I don't have that 
   information. Location data may also be input manually.
   -Added graphics clipping to restrict graphics to map area for orbits with 
   high inclinations. (Example: Alouette)
   -Adjusted top edge of map to top of screen.
   -Revised CGA HST icon for faster drawing and better proportions.
   -"/R" is now sufficient for RESUME command line option.
   -Added "/S" command line option to force space shuttle icon. Requires less 
   time to draw than HST icon for slower computers. 
   -Adjusted blink timing for more reliable blinking. If computational delays 
   are too great (especially 2-line orbits which require more than twice the 
   calculation time compared to simple orbits), blinking is defeated.
   -Two sample PIF files are included for use with Windows 3.0, one for 386 
   enhanced mode and one for normal mode. Files must be edited to set correct 
   drive/directory names.

   9023      6/03/90
   -----------------
   -Added an icon resembling the Hubble Space Telescope to be used when the
   mission title does NOT begin with the letters "STS". Space Shuttle icon is 
   unchanged.

   9022B     5/31/90
   -----------------
   -Corrected two errors with the E command: QuickBASIC Error 11 (again!) and
   typographical error causing altitudes entered in km to be zero.
   -Eliminated the R Command since that function is now obtained by pressing 
   the ENTER key to resume the current mission, or by using the 2 or F 
   commands to load files.
   -Meridian longitude numbers (0, -90, etc.) at top of map removed to yield 
   approximatly 5% more range in latitude.
   -Orbit number calculations changed so that both orbital models agree with 
   NORAD; first ascending node after launch starts orbit 1. NASA often counts 
   the first partial orbit as orbit 1; STSORBIT now always counts this as 
   orbit 0. Preliminary, pre-launch 2-line elements from NASA also often have 
   the orbit count 1 higher than subsequent elements with the first ascending 
   node set at orbit 2.
   -Changed from QuickBASIC V4.5 to BASIC Compiler V7.0 for optimized code and 
   more flexible error handling.
   -Improved error processing for 2-line files.

   9022A     5/30/90
   -----------------
   -Fixed the R command so that with NASA 2-line elements the program would 
   not abort with QuickBASIC error 11 upon initial entry.
   -Fixed the D command so that it would not abort with QuickBASIC Error 11.
   -Fixed a minor bug for "old style" (not NASA 2-line) simulations that 
   caused the simulation date and time to be incorrect if the current time was 
   prior to the launch time.
   -Reduced search time in NASA 2-line elements files.
   -Corrected a number of typographical and spelling errors in this doc.

   9022      5/28/90
   -----------------
   -This is a MAJOR UPGRADE in performance and features. STSORBIT may now be 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 33


   used with NASA/NORAD 2-Line Elements which yield far more accurate orbital 
   information over long periods. Much of the original code has been rewritten 
   and an almost equal amount has been added. Many thanks to Paul Traufler for 
   his assistance.
   -IMPORTANT NOTE: Version 9022 is a BETA RELEASE. While considerable testing 
   has been performed and no major problems are known at this time, minor bugs 
   may remain. In particular, error checking associated with the new 2-line 
   elements features is minimal in this version. To avoid errors, be sure the 
   2-line elements file name and the satellite name are correct. Comments and 
   problem reports will be appreciated!
   -Because some of the software adapted for this version of STSORBIT was 
   originally written by others and is private, the source code is not 
   available for this version.
   -Upon first time entry, STSORBIT now requests UT (Greenwich Mean Time) 
   offset in hours and whether or not daylight savings time is in effect. Both 
   parameters are now saved in the .INI file.
   -Local time and date now updated while loading map data.
   -Map coordinates file converted from ASCII to binary, duplicate data points 
   removed, and renamed to STSORBIT.MAP. File size and map loading time are 
   more than cut in half. Users of prior versions may delete file STSORBIT.DAT 
   since it is no longer used.
   -Internal timekeeping switched from local time to UT in order to allow .INI 
   files to be exchanged across time zones without conversion. Users 
   exchanging .INI files should use the "F" command to read in foreign .INI 
   files (rather than copying them to file STSORBIT.INI) to avoid accidentally 
   changing the UT Time Zone on their system. NOTE: Old .INI files (Version 
   9019 or earlier) will be automatically converted to UT; STSORBIT assumes 
   they were created in the time zone and daylight status now in use and 
   therefore the data should be verified!
   -Launch time and simulation time displays now show UT rather than local 
   time. Local time display now includes the appropriate time zone 
   abbreviation for US time zones (PST/PDT, etc.) and GMT/BST (Greenwich Mean 
   Time/British Summer Time) for UK.
   -When STSORBIT is first entered, pressing RETURN at the Main Menu resumes 
   the last mission (if present) rather than generating an error.
   -Missing cursor on Main Menu repaired.
   -Various minor cosmetic changes.

   9019      5/06/90
   -----------------
   -This is primarily a DOCUMENTATION UPDATE. The Main Menu text has been 
   completely rewritten. Various other minor changes and clarifications.
   -Added information on NASA SpaceLink.
   -README questionnaire added to package.
   -Added input and display of orbit altitude in kilometers.
   -Cleared screen prior to exit if no .INI update required.
   -Several minor cosmetic changes.

   9017A     4/27/90
   -----------------
   -Added L command to enable printer logging to record orbital information 
   and ascending and descending node information.
   -Added B command to toggle shuttle symbol blinking for all display types.

   9017      4/24/90 

   Program STSORBIT Space Shuttle Orbit Simulation                    Page 34


   -----------------
   -Added code to cause shuttle icon to flash once per second. Applies ONLY to 
   CGA and HGC displays.
   -Fixed position of longitude labels at top of screen for Hercules Graphics 
   Card.
   -Added reminder to execute MSHERC before running STSORBIT if using Hercules 
   Graphics Card.
   -STSORBIT is now one year old!

   9015      4/12/90 
   -----------------
   -Added code for calculation of the J2 factor, the perturbation of low 
   orbits due to the non-spherical shape of the Earth and consequent 
   gravitational field variation. I confess that the J2 factor contributed a 
   far greater error that I had supposed, amounting to as much as 5-7 degrees 
   per day. The accuracy of the longitude of the nodes is improved by 
   approximately an order of magnitude.

   [Intermediate revision notes removed to save space. Available on request.]

   8916      4/24/89 
   -----------------
   -Initial BETA VERSION Release.