ETM Version 1.2 for the USC family of devices
               =============================================

                                  Copyright 1990,1991 Zilog Inc.
  
                                       210 Hacienda Ave.
                                       Campbell, CA 95008
                                       Tel (408) 370-8113
                                       Fax (408) 370-8056
                                       BBS (408) 370-8024


Files on this disk
------------------
- README: you are reading it.
- *.EXE and *.LST: the ETM executable programs, and 
                   field and register list files:

         - ETMUSC.EXE    /.LST for the USC  (Z16C30)
         - ETMMUSC.EXE   /.LST for the MUSC (Z16C33)
         - ETMIUSC.EXE   /.LST for the IUSC (Z16C31)


Version 1.2 release notes
-------------------------
1. The Help menu displays three more options than are described in the 
  user's guide:
  - Editors: explains the three editors of the ETM.
  - Field Types: the ETM considers four types of register fields, listed and
    compared here.
  - Code Generation: provides explanations on the C files generated by the
    ETM.

2. Memory requirements
  The ETM dynamically allocates memory when you build an initialization
  sequence and open windows.  To avoid a shortage of memory, it is advised
  to work with 640k RAM with a maximum of that memory available to
  executable programs.  You should remove all TSR programs (Terminate-
  Stay-Resident).  

3. Cross-references to technical documentation
  The ETM provides cross-references to the technical documentation of the 
  supported device.  These references are displayed on the bottom-right 
  corner of the screen with the following formats:
  
    (TM:page number) for reference to a Technical Manual
    (PS:page number) for reference to a Product Specification

  ETMUSC.EXE and ETMMUSC.EXE
    reference the Z16C30/Z16C33 technical manual
    
  ETMIUSC.EXE
    reference the Z16C30/Z16C33 technical manual
    and the Z16C31 product specification  


BBS information
---------------
Zilog's Bulletin Board can be accessed at the following number

        (408) 370-8024
	(2400 bds, 8 bits/no parity, 1 stop bit)

For a full access to the Bulletin Board services, you must register by
returning the enclosed registration card.  Your priviledges will be updated
to allow you to download next releases of the ETM.


USC Initialization window
-------------------------
From the set of USC initialization variables, seven primary variables 
should particularly catch your attention: 

    Configuration, Protocol, BaudRate,
    TxMethod, RxMethod, TSA, Enables

If you choose to implement any of these variables, the ETM will ask you
to set the secondary variables (Interfaces, Processor, ExtClockRate, 
etc...) as required.

This is the complete set of initialization variables of the ETM Version 1.2.

    Configuration
        Interface8            type of 8-bit interface
        Interface16           type of 16-bit interface
        Processor             type of processor
        IntAckPin             configuration of INTACK pin
    Protocol
        ModemControl          modem control signals
    BaudRate
        ExtClockRate          external clock rate value
        ExtClockPin           pin for external clock
        ThisBaudRateFor       baud rate for reception or transmission
        UseDPLL               sets baud rate using DPLL or not
        DPLL_X                DPLL multiplier
        Async_X               Asynchronous protocol special multiplier
        CTR_X                 5-bit counter multiplier
        BRG_X                 baud rate generator multiplier
    TxMethod
        StatusIntEnable       enable for status interrupts
    RxMethod
    TSA
    Enables

The BaudRate and ExtClockRate are numerical variables.  You can select
one of the proposed values or enter your own.  You can use decimal values
in the following formats:

    - 9600    
    - 64k or 64K     for 64,000
    - 1m  or 1M      for 1,000,000

These programs are released as an engineering aid to electronic design
engineers using the Zilog family of data communication products.  They may 
not be altered in any way.


                   This is the first release of Zilog's
  
                      ELECTRONIC TECHNICAL MANUAL

                     for the USC family of devices
           To help us improve this product and its successors
        please let us know your impressions, suggestions, comments.

Brady Williams - ZiLOG District Sales Manager 404-448-9370.

                                --oOo--