Program JPLCLOCK

            NASA/JPL Multimission Computer Control Center Clock






               (C) Copyright David H. Ransom, Jr., 1991
                           All rights reserved.







                               Version  9130
                               July 22, 1991





                          by David H. Ransom, Jr.
                          Rancho Palos Verdes, CA




                             RPV ASTRONOMY BBS
                              (213) 541-7299
                      (310) 541-7299 [November, 1991]

Program JPLCLOCK Multimission Control Center Clock                 Page i



                             TABLE OF CONTENTS
                             -----------------


INTRODUCTION ......................................................1
     JPLCLOCK FEATURES ............................................1
PROGRAM DESCRIPTION ...............................................5
JPLCLOCK HARDWARE AND SOFTWARE REQUIREMENTS .......................7
JPLCLOCK FILES ....................................................8
STARTING PROGRAM JPLCLOCK .........................................9
     JPLCLOCK Command Line Options ................................9
     Setting UTC Zone and Daylight Flag ...........................9
JPLCLOCK MAIN CLOCK DISPLAY .......................................12
JPLCLOCK MAIN MENU ................................................16
     F1   Program Information .....................................17
     F2   Set LOCATION CLOCKS .....................................18
     F3   Set EVENT/MISSION TIMERS ................................20
          Set MISSION/EVENT TIMERS ................................21
          Set SELECTED EVENTS .....................................27
     F4   Set DAYLIGHT and Defaults ...............................28
     F5   Read or Save INI and MTD Files...........................30
          READ and SAVE INI Files .................................31
          READ and SAVE MTD Files .................................31
          INI Files from Other Locations ..........................33
     F6   Self-Calibration using TIMESET ..........................34
     F7   Switch TEXT Mode ........................................36
     F8   Switch PAGE Mode ........................................36
     F9   DOS SHELL (DOS 3.3+ ONLY) ...............................36
     F10  TIME SYNCHRONIZATION ....................................37
          Configuring Program TIMESET .............................37
          Time Synchronization Menu ...............................39
          VIEW or SET Time Sync Data ..............................39
          TIMESET Time Synchronization ............................40
          MANUAL Synchronization ..................................40
DOS CLOCK CALIBRATION .............................................42
     Setting DOS Time .............................................43
     Maintaining DOS Time .........................................44
     Calibrating DOS Time .........................................46
          Manual Hardware Clock Calibration .......................47
          Manual Software Clock Calibration .......................49
USING TEXT MODE ...................................................51
     Preparing TEXT Files .........................................52
COMMENTS AND KNOWN PROBLEMS .......................................53
     Computer BIOS Problems .......................................53
     Monitor Type and Video Adapter Cards .........................53
     Computer Processor and Math Coprocessor ......................53
     DOS Version and the Shell Feature ............................53
     Unstable Hardware or Software Clocks .........................54
     Typical Calibration Results ..................................54
     Color Variations .............................................55
FUTURE IMPROVEMENTS AND FEATURES ..................................56
UTC AND TIME ZONES ................................................57
JPLCLOCK REVISION HISTORY .........................................59

Program JPLCLOCK Multimission Control Center Clock                 Page ii



                    JPLCLOCK (NORMAL MAIN CLOCK SCREEN)



º JPLCLOCK by David H. Ransom, Jr.  Version 9130 º  JD2448422.63779  5 JUL 1991
                                                                     þþþþþþþþþþ
É[ NASA Jet Propulsion Laboratory ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»  Ú[ Magellan ]ÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
º                                                º  ³        604   12:18:25   ³
º   ÕÍÍÍ» ÉÍÍÍ»    Õ»   ÉÍÍÍ»   ÕÍÍÍ» ÉÍÍÍ¸      º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
º       º º   º þ   º   º   º þ     º º          º
º   ÉÍÍÍ¼ º   º     º   ÌÍÍÍ¹   ÉÍÍÍ¼ ÈÍÍÍ»  PDT º  Ú[ Ulysses ]ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
º   º     º   º þ   º   º   º þ º         º      º  ³        251   15:31:10   ³
º   ÈÍÍÍ¾ ÈÍÍÍ¼   ÔÍÊÍ¾ ÈÍÍÍ¼   ÈÍÍÍ¾ ÔÍÍÍ¼      º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
º                                                º
º   ÉÍÍÍ» ÕÍÍÍ»    Õ»   ÉÍÍÍ»   ÕÍÍÍ» ÉÍÍÍ¸      º  Ú[ Galileo ]ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
º   º   º     º þ   º   º   º þ     º º          º  ³        616   14:18:25   ³
º   º   º  ÆÍÍ¹     º   ÌÍÍÍ¹   ÉÍÍÍ¼ ÈÍÍÍ»  UTC º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
º   º   º     º þ   º   º   º þ º         º      º
º   ÈÍÍÍ¼ ÔÍÍÍ¼   ÔÍÊÍ¾ ÈÍÍÍ¼   ÈÍÍÍ¾ ÔÍÍÍ¼      º  Ú[Hubble Space Telescope]Ä¿
º                                                º  ³        403   14:44:33   ³
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Ú[ GDX  Goldstone ]ÄÄÄÄ¿  Ú[ CAN  Canberra ]ÄÄÄÄÄ¿  Ú[ Gamma Ray Observatory]Ä¿
³  165  20:18:25  PDT  ³  ³    166  14:18:25     ³  ³         70   11:55:40   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Ú[ JSC  Houston ]ÄÄÄÄÄÄ¿  Ú[ MAX  Madrid ]ÄÄÄÄÄÄÄ¿  Ú[ ROSAT Observatory ]ÄÄÄÄ¿
³  165  22:18:25  CDT  ³  ³  166  04:18:25  CES  ³  ³        378   05:30:26   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



NOTE: Pages ii and iii use the IBM "line drawing" characters as they appear 
on the display screen. If your printer cannot print these characters, these 
pages may appear garbled. These line drawing characters are not used 
elsewhere in this documentation; instead, I substitute similar characters 
from the normal character set.

Program JPLCLOCK Multimission Control Center Clock                Page iii



                    JPLCLOCK (SMALL MAIN CLOCK SCREEN)



º JPLCLOCK by David H. Ransom, Jr.  Version 9130 º  JD2448436.59025  5 JUL 1991
                                                                     þþþþþþþþþþ
É[ NASA Jet Propulsion Laboratory ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»  Ú[ Galileo ]ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
º                                                º  ³        522   15:09:58   ³
º    179  19:09:58 PDT      180  02:09:58 UTC    º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
º                                                º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼  Ú[ Magellan ]ÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                                                    ³        780   18:09:58   ³
ÚÄÄ SELECTED EVENTS ÄÄÄ¿  ÚÄÄ PRIORITY EVENTS ÄÄÄ¿  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
³                      ³  ³                      ³
Ú[Hubble Space Telesc]Ä¿  Ú[ Test 6 ]ÄÄÄÄÄÄÄÄÄÄÄÄ¿  Ú[ Ulysses ]ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³    417  13:36:06     ³  ³      0  00:24:08     ³  ³        265   08:23:58   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
³                      ³  ³                      ³
Ú[Gamma Ray Observato]Ä¿  Ú[ Test 5 ]ÄÄÄÄÄÄÄÄÄÄÄÄ¿
³     84  10:47:13     ³  ³      0  00:24:18     ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Ú[ GDX  Goldstone ]ÄÄÄÄ¿  Ú[ CAN  Canberra ]ÄÄÄÄÄ¿  Ú[ Gamma Ray Observatory]Ä¿
³  179  19:09:58  MST  ³  ³    180  13:09:58     ³  ³         84   10:47:13   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

Ú[ JSC  Houston ]ÄÄÄÄÄÄ¿  Ú[ MAX  Madrid ]ÄÄÄÄÄÄÄ¿  Ú[ ROSAT Observatory ]ÄÄÄÄ¿
³  179  21:09:58  EST  ³  ³  180  03:09:58  CES  ³  ³        392   04:21:59   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



NOTE: Pages ii and iii use the IBM "line drawing" characters as they appear 
on the display screen. If your printer cannot print these characters, these 
pages may appear garbled. These line drawing characters are not used 
elsewhere in this documentation; instead, I substitute similar characters 
from the normal character set.

Program JPLCLOCK Multimission Control Center Clock                 Page 1


INTRODUCTION
------------

     JPLCLOCK is a clock and event timer program written especially for use 
in the NASA Jet Propulsion Laboratory's Multimission Computer Control 
Center (MCCC) in Pasadena, California. JPLCLOCK provides mission 
controllers in the MCCC with current JPL time (Pacific Standard or Daylight 
Time), UTC (Coordinated Universal Time), and DSN (Deep Space Tracking 
Network) times as well as up to 60 selected mission or event timers. A text 
presentation mode allows the display of supplementary text and other 
messages when the program is used for more general applications.
     JPLCLOCK is copyrighted software; you are hereby granted a non-
exclusive license for non-commercial or educational use only. Agencies of 
the U. S. Government are hereby also granted a non-exclusive license for 
the use of this program. Use it if you like it, discard it if you don't. 
There are no warranties of any kind. If you wish to use JPLCLOCK 
commercially, write for license information.


JPLCLOCK FEATURES
-----------------

-    JPLCLOCK can turn an "ordinary" IBM-compatible personal computer into 
     a precision clock, synchronized to the National Institute of Standards 
     and Technology in Boulder, Colorado or to the U.S. Naval Observatory 
     in Washington, DC.

-    When used with the NIST or USNO Telephone Time Service, JPLCLOCK can 
     maintain its displayed time to an accuracy of 0.2 seconds or better 
     over extended periods of time.

-    JPLCLOCK automatically and continuously compensates for the drift of 
     the DOS software clock.

-    JPLCLOCK can display your local time and Universal Coordinated Time in 
     large, easy to read characters in its Main Window.

-    JPLCLOCK can display the local time at four additional locations 
     around the world.

-    JPLCLOCK tracks as many as 60 different missions or events, displaying 
     the Mission Elapsed Time or a countdown to Time Zero for each event. 
     Mission/event times may range from -27 years to +274 years!

-    JPLCLOCK can display up to four special PRIORITY EVENT timers that 
     automatically select events whose Time Zero is closest to the current 
     time.

-    All features and events are set by the user so that JPLCLOCK may be 
     easily configured for each installation.

-    JPLCLOCK can present supplementary text information on as many as 10 
     successive display screens for news and public information.



Program JPLCLOCK Multimission Control Center Clock                 Page 2


     JPLCLOCK Version 9126 was the first limited public release of the 
program, after a number of beta versions tested by Charles White at the 
NASA Jet Propulsion Laboratory. Thanks to Charles, a number of interesting 
features have been added to the early versions, bugs have been squashed, 
and the program has been tested in the MCCC and elsewhere. Other interested 
individuals at JPL have also evaluated the program, offered criticism and 
suggestions, and researched some of the older mission times. Mike Gardner 
in Sunnyvale has reviewed an early version of my documentation and offered 
his usual constructive criticism. To all of these people, my thanks!
     Although my initial discussions at JPL envisioned a "simple" program, 
JPLCLOCK is definitely NOT simple. The original idea was to adapt my 
program ASTROCLK to the task required in the MCCC. I have indeed borrowed 
freely from ASTROCLK (as well as from another of my programs, STSORBIT) and 
this helped get the first versions up and running relatively quickly. As 
usually happens, the project quickly grew in scope and complexity. Everyone 
involved, myself included, had new ideas or suggestions. Equally 
significant, the personal computer is hardly the ideal precision clock, yet 
JPLCLOCK is intended for the JPL MCCC where accuracy is critical. Making 
sure that JPLCLOCK will maintain the required accuracy has consumed 
considerable time and thought. It wasn't long before the source included 
thousands of lines of code and the documentation grew to over 40 pages. All 
this in the space of a couple of weeks of my "spare time"! 
     Given the clock drift and accuracy problems inherent in the design of 
the typical IBM-compatible personal computer, JPLCLOCK would not have been 
practical without the various time services provided by the National 
Institute of Standards and Technology (NIST) and the U.S. Naval Observatory 
(USNO). The NIST radio stations WWV and WWVH provide an inexpensive and 
convenient means for "ordinary folks" to synchronize clocks and other 
equipment. The NIST and USNO Telephone Time Services offer a high precision 
standard time calibration source when such accuracy is required.
     Every effort has been made to assure that program JPLCLOCK performs 
its task accurately and reliably. However, while no known errors of any 
consequence remain, JPLCLOCK is still a young program and it is almost 
certain that some bugs are yet to be discovered. In addition, there is 
still much that can be done to further enhance JPLCLOCK, so new versions 
can be expected from time to time. User comments, suggestions, and bug or 
problem reports will be appreciated!
     Programs such as JPLCLOCK take many hours to develop and maintain. 
While it is not required, I would appreciate your registration of the 
program; the cost is very nominal and it will encourage me to continue 
supporting the program. The only other request I make of users is that they 
take the time to complete and return the confidential questionnaire in file 
README. The questionnaire gives users a chance to offer comments and 
suggestions, and lets me know that people use and appreciate JPLCLOCK.
     For those who are interested in our space program and who have access 
to a modem, I recommend NASA's SpaceLink Bulletin Board System in 
Huntsville, Alabama, (205) 895-0028, available twenty four hours per day. 
NASA SpaceLink, supervised by Bill Anderson of the NASA Marshall Space 
Flight Center, provides a wealth of information on NASA and its projects. 
Orbital elements for a Space Shuttle mission are usually available while a 
mission is in progress. In addition to educational materials, general 
information on NASA programs and plans, news releases, and graphics images 
from current and prior spacecraft missions such as Voyager and Magellan, 
SpaceLink also provides current news and information on missions in 
progress. Mission status reports for all active missions are generated 

Program JPLCLOCK Multimission Control Center Clock                 Page 3


periodically. I regularly call SpaceLink and post files of interest on my 
own bulletin board system (BBS).
     Special thanks to Charles White of the NASA Jet Propulsion Laboratory 
for his comments and suggestions during the development and testing of this 
program, as well as a fascinating visit to the JPL Multimission Computer 
Control Center. Like many others, I consider the Jet Propulsion Laboratory 
to be a unique national resource, unequaled anywhere else in the world. 
JPLCLOCK is entirely "a labor of love", to repeat a well-worn phrase; to 
see my software operating in the MCCC where amazing projects such as 
Voyager and Magellan are controlled is sufficient reward.
     A brief biographical note: I am a retired physicist and engineer who 
spent all of his professional life in the world of electronics, data 
communications and, more recently, computers. As a young man I was actively 
involved in the early American space program as a contractor for the Jet 
Propulsion Laboratory, working on projects such as Ranger and Mariner. 
Perhaps as a consequence of these and the many other remarkable NASA 
projects directed by JPL, my respect and admiration for The Lab and its 
people practically knows no bounds. I was also involved with the Mercury, 
Gemini, and Apollo projects and my interest in space has continued to this 
day. My experience includes both hardware and software, and I designed and 
implemented software professionally for many years with considerable 
success.
     I have been writing software for IBM-compatible personal computers, 
usually oriented toward space and astronomy, for a number of years. Since 
1987 I have also maintained the RPV ASTRONOMY BBS, a free access bulletin 
board system with an emphasis on space and astronomy. So successful has
my latest "hobby" become that it is threatening to overwhelm my bulletin 
board system and consume all of my available time just answering the mail! 
All of my programs are free although I do encourage users to register them 
for a modest fee. If my software also serves to help spark the interest of 
young people in science and technology or can be a learning tool at any 
level, I will have more than achieved my purposes.
     Two of my programs, ASTROCLK and STSORBIT, have become widely known 
throughout United States, Canada, and Europe. ASTROCLK is an attempt to 
consolidate a multiplicity of astronomy and time related programs into a 
single useful computer tool. My desire to "keep in touch" with our Space 
Shuttle missions led to the development of STSORBIT, a simulation of the 
large wall map in Mission Control at the Johnson Space Center in Houston, 
Texas. STSORBIT eventually found its way (several times) to JPL where it is 
now often projected in the MCCC during Space Shuttle missions and for other 
Earth orbiting missions, and was the catalyst for JPLCLOCK. The initial 
versions of JPLCLOCK were written over a period of several weeks in June of 
1991 with close coordination with JPL. Even before the program was 
"finished" (if such programs are EVER really finished!), JPLCLOCK was being 
used during a planned power outage as the primary time standard in the 
Mission Control Center. JPL is also considering use of the program outside 
the Mission Control Center to help inform Lab personnel and visitors. How 
useful it may be to others remains to be seen.
     For current space and astronomy programs and data, as well as the most 
recent version of this program, call my bulletin board system (BBS). If the 
BBS has not answered after the fourth ring, hang up, wait TWO MINUTES, then 
call back; the system has a power controller and if the system is off it 
takes that long for the computer to start up and do its housekeeping 
chores. The system now has almost 1000 users and is often busy, so be 
patient.

Program JPLCLOCK Multimission Control Center Clock                 Page 4




                             RPV ASTRONOMY BBS

                              (213) 541-7299


                              IMPORTANT NOTE
                              --------------

          The area code for my BBS telephone number is scheduled 
          to change in November, 1991 as the Los Angeles 213 area 
          code is once again split to accommodate Southern 
          California's continuing growth. The new number will be 
          (310) 541-7299.


     If you do not have access to a modem, you may send US$10.00 to cover 
materials, postage and handling for a copy of the latest version on disk; 
please specify 5-1/4" 360K or 3-1/2" 720K disks.
     JPLCLOCK can be a complex program when all of its features are used, 
perhaps more complex than was originally anticipated. This documentation 
attempts to completely describe the program and its operation. There may be 
errors in this documentation, but please read it BEFORE you drop me a nasty 
note or give up!

                                   David H. Ransom, Jr.
                                   7130 Avenida Altisima
                                   Rancho Palos Verdes, CA 90274

Program JPLCLOCK Multimission Control Center Clock                 Page 5


PROGRAM DESCRIPTION
-------------------

     The NASA/JPL Multimission Computer Control Center (MCCC), located at 
the Jet Propulsion Laboratory in Pasadena, California, is the "nerve 
center" where all NASA planetary missions and some Earth orbiting missions 
are controlled. Other NASA and ESA (European Space Agency) missions may 
also be supported by MCCC from time to time. The Control Center resembles 
other similar installations with consoles for each of the controllers and 
other responsible individuals directing the progress of a mission and 
coordinating the operation of the NASA Deep Space Network and other 
critical resources. Operations continue around the clock with a number of 
missions typically active. Missions active at this time include Voyager 1 
and 2, Magellan, Ulysses, and Galileo.
     Above the main floor of the Control Center and in plain view of all 
controllers and individuals in the visitors gallery are seven projection 
screens, five large and two slightly smaller. These screens display 
television or computer generated images related to missions in progress. 
For example, NASA Select Television is frequently displayed when it is 
broadcasting. JPLCLOCK is normally displayed on one of the screens as 
selected by Control Center personnel.
     JPLCLOCK displays various time information for the convenience of 
Control Center personnel. The current local time (Pacific Standard/Daylight 
Time) and Coordinated Universal Time (UTC, or GMT as it was formerly 
designated) are displayed in large characters in the program's main window. 
Below that window are four smaller windows displaying local time at the DSN 
locations or other selected installations. On the right side of the screen 
are six smaller windows which display the Mission Elapsed Time for selected 
missions in progress (green background) or Countdown Time for missions or 
events due to occur (red background). The background color switches from 
red to green when the countdown reaches zero or the event occurs. As many 
as 60 different missions or events may be monitored with these timers.

                              IMPORTANT NOTE
                              --------------

          Before using program JPLCLOCK in applications requiring 
          high accuracy, read the section DOS TIME CALIBRATION in 
          this documentation!

     JPLCLOCK may be operated in two modes: NORMAL and PAGE. The NORMAL 
mode displays the main window, four location time windows, and from one to 
six timer windows continuously. The PAGE mode displays the same main window 
and four location windows but sequences through up to 60 different timer 
windows using ten different timer "pages". The timer page is normally 
switched every thirty seconds; however, when any timer on a particular page 
is within one hour of of "Time Zero", the display will "freeze" on that 
timer page. As long as events which occur within several hours of one 
another are arranged on the same screen page, JPLCLOCK will automatically 
ensure that the timer for each event is displayed from one hour before to 
one hour after Time Zero.
     In addition, up to ten screen pages of supplementary text information 
or messages may be displayed in conjunction with the PAGE mode. When the 
TEXT mode is active, the program cycles through all of the active timers 
then switches and presents the text pages in sequence. This real time to 

Program JPLCLOCK Multimission Control Center Clock                 Page 6


text to real time sequence repeats indefinitely unless an active timer 
reaches the plus or minus one hour period around its Time Zero, in which 
case that timer page freezes as described above.
     The default JPLCLOCK configuration is arranged for the convenience of 
the Jet Propulsion Laboratory MCCC. One or more initialization files, files 
with a file type ".INI" and containing alternate or supplementary time and 
location data, may also be included from time to time. Manual configuration 
features are included for setup at other locations. Window titles, mission 
or event names, and window times are easily configured for the desired 
location or event. Inactive location or timer windows may be removed from 
the screen. The current configuration is saved each time JPLCLOCK is run so 
that the program may be resumed at any time. While the program is running, 
all keyboard operations are timed so that inattention on the part of the 
user for more than ten to thirty seconds (depending upon the operation 
being performed) will result in automatic restarting of the program.
     JPLCLOCK is intended for a dedicated IBM-compatible computer running 
MS-DOS version 3.3 or higher. Best performance will be achieved using a 286 
or better processor equipped with a math coprocessor chip. However, the 
program should execute correctly (but perhaps with perceptible delays) 
using any IBM-compatible computer with or without a math coprocessor chip. 
For normal use, the program should started from the computer's AUTOEXEC.BAT 
file so that it is restarted in the event of a power failure.
     As of June 1991, JPLCLOCK is still a relatively new program. Although 
all known problems have been corrected, there are doubtless a few minor 
bugs yet to be discovered. User comments and suggestions are welcome. 
Future versions are anticipated at periodic intervals as new features are 
added and/or problems are corrected. Planned features include optional 
automatic synchronization with compatible external time signals. 

Program JPLCLOCK Multimission Control Center Clock                 Page 7


JPLCLOCK HARDWARE AND SOFTWARE REQUIREMENTS
-------------------------------------------

     JPLCLOCK is written for use on IBM-compatible computers and has only 
been tested on computers equipped with an 80286 or higher processor. Most 
of the features should operate correctly on older computers but those 
features which use the clock/calendar chip, introduced with the AT-class 
computer and subsequently retrofitted to older computers as an add-on chip 
or circuit card, may not operate correctly. Several different clock chips 
have been used on PC and XT machines which are NOT compatible with the AT 
chip and may not be compatible with program TIMESET.
     JPLCLOCK requires a modest amount of the computer's memory. The 
program has not been tested on a machine with less than 640K of main RAM. 
Although most JPLCLOCK operations are entirely memory resident, program 
startup, use of program TIMESET, and the DOS shell all require disk 
accesses. Because of the excessive time delays associated with floppy disk 
drives, a hard disk is strongly recommended. Even with a hard disk, delays 
and system software vary considerably and performance may differ from drive 
to drive.
     JPLCLOCK assumes DOS Version 3.3 or higher; MS-DOS and PC-DOS are 
considered equivalent although testing has been performed only on systems 
using MS-DOS. Limited testing has been performed using a beta version of 
DOS 5.0 with no problems encountered. The DOS shell feature of DOS, 
required for use of program TIMESET, is considered unreliable for versions 
of DOS prior to DOS 3.1. If you have not upgraded to at least DOS 3.3, 
consider doing so!
     As discussed in more detail elsewhere, the DOS software clock varies 
considerably from computer to computer and from one version of DOS to 
another. Avoid using your favorite TSR (Terminate and Stay Resident) 
programs when running JPLCLOCK. Several hours of operation with JPLCLOCK 
will establish whether or not your computer and DOS software clock are 
suitable for use with the program. If the DOS software clock varies too 
much with time or temperature it cannot be used with JPLCLOCK and there is 
no remedy in most cases except to use a different computer.
     Because JPLCLOCK is a new program (as of Version 9128), user feedback 
on both problems and successes will be appreciated! The variety and range 
of quality of hardware and software "out there" is almost unbelievable and 
it is helpful if I know which brands of hardware and software work or fail.

Program JPLCLOCK Multimission Control Center Clock                 Page 8


JPLCLOCK FILES
--------------

     JPLCLOCK is normally distributed in archived format using either the 
PAK or ZIP format. The following files are usually included:

          JPLCLOCK.EXE        Main program          (required)
          JPLCLOCK.DOC        Documentation         (not required)
          JPLCLOCK.INI        Initialization data   (optional)
          JPLCLOCK.MTD        Mission Timer Data    (optional)
          JPLCLOCK.MSG        Sample TEXT file      (optional)
          JPLFONT.COM         Experimental EGA font (optional)
          README              Program Registration  (not required)

Files noted as "(required)" must be in the current default directory for 
program operation. Files noted as "(optional)" do not need to be in the 
default directory when JPLCLOCK is operated but may provide additional 
features or information if present. File JPLCLOCK.MTD contains data for 
selected missions. If file JPLCLOCK.INI is not present, it will 
automatically be created the first time the program is executed.
     Additional MTD files (files with filetype ".MTD", standing for 
"Mission Timer Data") may be included from time to time with interesting or 
upcoming events pre-programmed. Other MTD files may be posted periodically 
on my bulletin board system for upcoming events.
     Registration of program JPLCLOCK is not required but certainly will be 
appreciated! See the file README for registration information. JPLCLOCK has 
required considerable effort to develop and test and your response will 
encourage me to continue enhancing and supporting the program. As an 
additional "bonus" for registration, I will send the latest version of 
JPLCLOCK to you on disk; please specify the disk size desired: 5-1/4" 360K 
or 3-1/2" 720K (supplied if no disk size specified).

Program JPLCLOCK Multimission Control Center Clock                 Page 9


STARTING PROGRAM JPLCLOCK
-------------------------

     Before starting program JPLCLOCK for the first time, make sure that 
all required files are in the current drive and directory (see below). 
Delete the file JPLCLOCK.INI if it has been created by a previous version 
of JPLCLOCK or you are using the program at a different location from the 
one which prepared the file. The format of the INI file may change with 
new versions and, although the program may read prior versions of .INI 
files, it is safer to "start from scratch". The INI file also includes 
specific information related to the local time zone.
     To start program JPLCLOCK for operation in the NORMAL mode, enter the 
following command at the DOS prompt:

          JPLCLOCK

As described in the summary of command line options below, you may add the 
"/M" command line option to the examples above to force monochrome 
operation on CGA, EGA, and VGA systems. 


JPLCLOCK Command Line Options
-----------------------------

     All JPLCLOCK program features (except monochrome operation) may be 
enabled or disabled from within the program. However, to facilitate use 
with batch files, certain features may be enabled using "command line 
options", specific words preceded by the slash ("/"), used when the program 
is started from the DOS prompt. A command line consists of the program name 
followed by the desired command line option(s): "JPLCLOCK [option] ... 
[option]". The following command line options are available:

     ?         (Special option) Displays brief help information to remind 
               users of the principal command line options and then returns 
               to DOS.

     /M        Force monochrome operation. On color monitors, this usually 
               forces white or light white on black background.

     /SMALL    Enables the SMALL main clock window and the additional four 
               SELECTED/PRIORITY timer windows.

     /PAGE     Enables PAGE mode operation with up to 60 Mission/Event 
               Timers displayed in "pages" of six timers each. Default is 
               the non-page mode with only 6 Mission/Event Timers.

     /TEXT     Enables TEXT (and PAGE) mode operation if file JPLCLOCK.MSG 
               is found. Up to ten screen pages of prepared text may be 
               sequentially displayed.


Setting UTC Zone and Daylight Flag
----------------------------------

     JPLCLOCK must know the correct time and time zone in order to operate 

Program JPLCLOCK Multimission Control Center Clock                 Page 10


accurately. The first time JPLCLOCK is executed (or any time the program 
cannot find the file JPLCLOCK.INI), the program prompts you for your UTC 
Offset and asks if you are now on Daylight or Summer time:

     Set UTC TIME ZONE OFFSET and DAYLIGHT FLAG

     JPLCLOCK must know the difference between your local time zone and 
     Universal Coordinated Time (UTC), also sometimes known as Greenwich 
     Mean Time (GMT). With this information, JPLCLOCK can automatically 
     adjust launch times and dates for your local time zone. In addition, 
     JPLCLOCK must know if you are now on STANDARD or DAYLIGHT (SUMMER) 
     time.

     First, enter the difference between your STANDARD time zone and UTC in 
     hours. Do NOT include the hour for daylight time if you are now on 
     DAYLIGHT time; it will be entered separately. For most time zones in 
     the United States and Canada, the entries required are:

          Eastern Standard Time     EST    -5.00
          Central Standard Time     CST    -6.00
          Mountain Standard Time    MST    -7.00
          Pacific Standard Time     PST    -8.00

     Enter UTC Offset (hours)  [not set]:    -8
     Enter Daylight Flag (0=OFF, 1=ON)  [0]: 1

The example entries shown above illustrate the required information for 
Pacific Daylight Time: "-8" for the standard time zone offset from UTC and 
"1" to signify that Daylight Time is in effect. Enter the information that 
is appropriate for your time zone. Once the UTC Offset and Daylight Flag 
information have been entered, these data are saved in file JPLCLOCK.INI 
and will not be requested again.
     Not surprisingly, JPLCLOCK relies upon the internal clock in your 
computer to maintain accurate time. However, not all computer clocks are 
created equal; some are much more accurate than others and it is difficult 
to predict that performance in advance. The computer clock was simply not 
designed as a high precision timekeeping instrument. Further, recent 
versions of DOS (3.3 and higher) can reset an otherwise relatively accurate 
hardware clock if the software clock loses time. 
     Just as your quartz watch will keep time most consistently (as opposed 
to accurately) when you leave it always on your wrist, so too your computer 
clock will keep time best if it is left on continuously. Time and 
temperature changes are a quartz oscillator's worst enemy, along with a 
long term crystal aging effect. Taken together, these effects can cause 
your clock to lose or gain up to several seconds per day. For reasonably 
accurate operation, your computer clock should be synchronized against a 
time standard from time to time. See the sections DOS CLOCK CALIBRATION and 
TIME SYNCHRONIZATION for additional discussion, especially for 
installations where high precision is desired or required.
     Other factors may also affect the accuracy of the computer's clock. 
One of the most common and severe offenders is Local Area Network (LAN) 
software; while this can vary depending upon the LAN BIOS and network 
hardware being used, the networking software in many systems may completely 
or partially ignore the clock's "time ticks" during network operations. 
Another frequent offender is high speed communication (usually about 50Kb 

Program JPLCLOCK Multimission Control Center Clock                 Page 11


per second or higher) via the serial communications ports, COM1 through 
COM4; in this case too, time ticks may be lost and the clock will fall 
behind. Clock problems related to networking or other software can result 
in time losses up to tens of seconds or even minutes per day! There is no 
remedy for this situation except to avoid using the software which causes 
the problem.
     Once the UTC Offset and Daylight Flag are set, JPLCLOCK continues with 
its normal startup and displays the title screen (see below). Verify that 
the current local and UTC time and date (including your local time zone 
abbreviation if you are located in the United States) are correct before 
proceeding. JPLCLOCK will start automatically in 10 seconds and the message 
on the screen will count down during the wait time. No operator action is 
required if you wish JPLCLOCK to start; you may also press ENTER twice to 
immediately start the program, bypassing the 10 second delay.
     JPLCLOCK's full name and the current version are shown on the title 
screen, followed by the current time and date. At this point the program is 
awaiting user input; if no keyboard input is detected within 10 seconds, 
the program will automatically begin operation. Press ENTER to display the 
Main Menu or ESC to quit the program and return to DOS. All other keys are 
ignored except that a timed message is displayed at the upper right of the 
screen reminding the user to press ENTER for the Main Menu.

Program JPLCLOCK Multimission Control Center Clock                 Page 12




                                Program JPLCLOCK

              NASA/JPL Multimission Computer Control Center Clock
                                  Version 9129


                   Current time:  20:18:02 PDT   03:18:02 UTC
                   Current date:    06/30/1991     07/01/1991


                JPLCLOCK will start automatically in 10 seconds

                                       OR

                        Press ENTER for MENU, ESC to QUIT



                    (C) Copyright David H. Ransom, Jr., 1991
                              All rights reserved.


     Note both the local time and date (Pacific Daylight Time in the 
example) and UTC time and date (Coordinated Universal Time). Be sure that 
ALL time and date items are correct. If not, press ENTER to go to 
JPLCLOCK's Main Menu and then press F4 to correct the information.


                              IMPORTANT NOTE
                              --------------

          If you are using a JPLCLOCK.INI file (or any other INI 
          file) prepared at some other location, your local time 
          and date may not be correct. If all else fails, quit 
          program JPLCLOCK, delete file JPLCLOCK.INI, and restart 
          the program. JPLCLOCK will assist you in setting up the 
          program for your time zone and will create a new 
          JPLCLOCK.INI file for subsequent use.


JPLCLOCK MAIN CLOCK DISPLAY
---------------------------

     The Main Clock display for JPLCLOCK is illustrated on Pages ii and iii 
above. Two screen layouts are available, selectable either by a command 
line option or by a Function Key, NORMAL or SMALL. The NORMAL screen 
provides a large window with special large characters for Local and UTC 
Times and is recommended when the program will be used on a normal monitor 
which may have to be viewed from some distance. The SMALL screen provides a 
smaller window for Local and UTC Times along with up to four additional 
timers and may be preferred when JPLCLOCK is projected on a large screen.
     The remaining windows are the same for both screen layouts. The four
Location Clocks are below the main window, and the six Mission/Event Timers 

Program JPLCLOCK Multimission Control Center Clock                 Page 13


are on the right side of the screen. The Location Clocks and the 
Mission/Event Timers are separately described in following sections. In 
addition to these data, the main clock display also includes the program 
name and version, as well as the current Julian Date (a standard method of 
day numbering used by scientists and astronomers) and local date (day-
month-year) at the upper right corner of the display.
     The following keys are active while JPLCLOCK is running and the clocks 
and timers are displayed on the screen:

          ENTER     Stop the main clock display and go to JPLCLOCK's Title 
                    Screen. Press ENTER again to go to the Main Menu. See 
                    the section below for a description of the available 
                    commands at the Main Menu.

            ESC     Quit JPLCLOCK and return to DOS. You will be asked to 
                    press ESC again to confirm that you wish to quit the 
                    program. If not, press ENTER to resume operation.

         ALT-F1     Freeze the display. Updating the screen stops EXCEPT 
                    that Local and UTC Time will be updated above the Main 
                    Window and the word "FREEZE" will flash in yellow above 
                    the Mission Timer Windows while the freeze is in 
                    effect. The freeze will be automatically released in 
                    five minutes, or press ENTER to release the freeze 
                    immediately. (Actually, pressing any key except keys 
                    which do not generate a character, such as SHIFT, ALT, 
                    or CTRL, will release the freeze.)

         ALT-F5     Change SELECTED/PRIORITY EVENTS display. This key is 
                    active ONLY when the SMALL Main Window is active. The 
                    choices are: four SELECTED Mission Timers; two SELECTED 
                    Mission Timers and two PRIORITY Mission Timers; or, 
                    four PRIORITY Mission Timers. Press again for the next 
                    arrangement.

         ALT-F6     Switch between the LARGE Main Window and the SMALL Main 
                    Window. Enabling the SMALL Main Window also displays 
                    the four SELECTED/PRIORITY Event Timers (as currently 
                    selected).

         ALT-F7     Enable or disable the TEXT mode if the file 
                    JPLCLOCK.MSG is present; otherwise, this command has no 
                    effect. See the section USING TEXT MODE for further 
                    information on this mode of program operation. This 
                    command is the same as the F7 command on the Main Menu.

         ALT-F8     Enable or disable the PAGE mode. If the TEXT mode is 
                    enabled when the PAGE mode is disabled, the TEXT mode 
                    will also be disabled. This command is the same as the 
                    F8 command on the Main Menu.

         ALT-F9     EXPERIMENTAL COMMAND to enable a special screen font, 
                    similar to "Helvetica", for EGA and VGA monitors ONLY. 
                    Press ALT-F9 to enable the special screen font and 
                    large numbers in the time displays; press ALT-F9 again 

Program JPLCLOCK Multimission Control Center Clock                 Page 14


                    to use "normal" size characters in the time displays.

                    The special font is designed primarily for EGA systems 
                    and may not operate correctly on some VGA systems. (On 
                    one VGA system, for example, the last few lines of the 
                    screen show a variety of text and graphics symbols when 
                    program TIMESET is executed, and these symbols remain 
                    on the screen when JPLCLOCK resumes operation.)

        ALT-F10     Immediately perform TIME SYNCHRONIZATION using the 
                    external program TIMESET to call either the National 
                    Institute of Standards and Technology (NIST) or the 
                    U.S. Naval Observatory (USNO). See the section TIME 
                    SYNCHRONIZATION for further information on this command 
                    and program TIMESET. This command is the same as the 
                    F10+F1 commands on the Main Menu.

     Four additional timer windows appear on the screen below the Main 
Clock window when the SMALL Main Window is selected. These are divided into 
two classes: SELECTED EVENTS and PRIORITY EVENTS. SELECTED EVENTS are just 
like regular Mission/Event Timers except that they are always displayed; 
they may be selected from the current Mission/Event Timers by pressing 
F3+F2 from the Main Menu. PRIORITY EVENTS are those events which have a 
Time Zero which is within 24 hours of the current time.
     Three different arrangements of SELECTED EVENTS and PRIORITY EVENTS 
may be selected by pressing ALT-F5 when the SMALL Main Clock is displayed. 
These two classes of events are always selected from the available 60
Mission/Event Timers; note that the titles have been truncated because the 
window width is shorter than the normal Mission/Event Window. The default 
arrangement displays four SELECTED EVENTS:

          +--------------- SELECTED EVENTS ----------------+
          |                                                |
          +[Hubble Space Telesc]-+  +[ Voyager 1 ]---------+
      #1  |    424  01:38:02     |  |  5,051  01:13:54     |  #3
          +-----------------------  +----------------------+
          |                                                |
      #2  +[Gamma Ray Observato]D+  +[ Voyager 2 ]---------+
          |     90  22:49:09     3  3  5,066  23:47:54     |  #4
          +----------------------+  +----------------------+
          +------------------------------------------------+

     Pressing ALT-F5 once will change the arrangement to two SELECTED 
EVENTS and two PRIORITY EVENTS:

          +-- SELECTED EVENTS ---+  +-- PRIORITY EVENTS ---+
          |                      |  |                      |
      #1  +[Hubble Space Telesc]D+  |                      |  #1
          |    424  01:37:27     |  |                      |
          +----------------------+  |                      |
          |                      |  |                      |
      #2  +[Gamma Ray Observato]-+  |                      |  #2
          |     90  22:48:34     |  |                      |
          +----------------------+  |                      |
          +----------------------+  +----------------------+

Program JPLCLOCK Multimission Control Center Clock                 Page 15



Note that only the first two SELECTED EVENTS are now displayed. In this 
example, there are no active PRIORITY EVENTS and therefore that window area 
is blank. JPLCLOCK continuously scans all 60 Mission/Event Timers to 
determine if any are less than 24 hours (plus or minus) from the current 
time. Events which have not yet occurred are shown with a RED background, 
and events yet to occur are shown with a GREEN background. If any events 
are found within the 24 hour range, they are sorted in such a way that #1 
is that event now closest to Time Zero and #2 is the next closest to Time 
Zero. The ordering of PRIORITY EVENTS is set dynamically and will change as 
the time difference between the Time Zero set in the Mission/Event Timers 
changes with respect to current time.
     Pressing ALT-F5 again will change the arrangement to four PRIORITY 
EVENTS:

          +--------------- PRIORITY EVENTS ----------------+
          |                                                |
          +[ Test Event ]--------+                         |
      #1  |      0  01:38:02     |                         |  #3
          +-----------------------                         |
          |                                                |
      #2  |                                                |
          |                                                |  #4
          |                                                |
          +------------------------------------------------+

As described above, the PRIORITY EVENTS are continuously scanned and 
sorted. With this display arrangement, from zero to four PRIORITY EVENTS 
may be displayed. In the example shown, the Mission/Event Timer called 
"Test Event" has been detected as within 24 hours of Time Zero (1 hour and 
38 minutes past Time Zero in this case) and is therefore displayed.

Program JPLCLOCK Multimission Control Center Clock                 Page 16


JPLCLOCK MAIN MENU
------------------


                                Program JPLCLOCK

              NASA/JPL Multimission Computer Control Center Clock
                                  Version 9129


                   Current time:  20:18:50 PDT   03:18:50 UTC
                   Current date:    06/30/1991     07/01/1991


                JPLCLOCK will start automatically in 10 seconds



       F1   Program Information            F6   CLOCK Calibration [OFF]
       F2   Set LOCATION CLOCKS            F7   Switch TEXT Mode  [OFF]
       F3   Set EVENT/MISSION TIMERS       F8   Switch PAGE Mode   [ON]
       F4   Set DAYLIGHT and Defaults      F9   DOS Shell (3.3+ ONLY!)
       F5   Read/Save INI & MTD Files     F10   Time Synchronization

    ENTER   Resume Program JPLCLOCK       ESC   Quit Program JPLCLOCK

            Enter selection:

     As with the title screen, JPLCLOCK is awaiting user input; if no 
keyboard input is detected within 10 seconds, the program will 
automatically resume operation. Note that the Main Menu displays the 
current status of CLOCK Calibration, TEXT Mode, and PAGE Mode. Press ENTER 
to immediately resume program operation. Press ESC to quit and return to 
DOS; the program will request that you press ESC a second time to confirm 
that you wish to return to DOS. (To resume JPLCLOCK when this message 
appears, press ENTER.) To go to one of the sub-menus, press the indicated 
Function Key. The purpose and operation of each menu item is described on 
the following pages.

Program JPLCLOCK Multimission Control Center Clock                 Page 17


F1   Program Information
------------------------


     Function Key F1 displays a brief description of the program and 
gives the telephone number of my bulletin board system (BBS), RPV ASTRONOMY 
BBS, in Rancho Palos Verdes, California near Los Angeles. This is a free 
access BBS which I maintain as a public service. There are nearly 1,000 
more or less regular callers, and the system is frequently busy, so please 
be patient! The BBS computer has a power controller; if the BBS has not 
answered by the fourth ring, hang up and call back in approximately two 
minutes.

                             RPV ASTRONOMY BBS

                              (213) 541-7299
                      (310) 541-7299 [November, 1991]


                              IMPORTANT NOTE
                              --------------

          The BBS area code number will change in November, 1991 
          as the telephone company again splits the Los Angeles 
          213 area code into two areas. The new number will be 
          (310) 541-7299.

     Program JPLCLOCK was written especially for the NASA/JPL Multimission
     Computer Control Center. It provides a main window with local and UTC
     time, four location clocks usually displaying local time at the NASA
     Deep Space Network sites in Goldstone, Canberra, and Madrid, and six
     event timers used to display mission elapsed time or the time for an
     upcoming event of interest. The current version of JPLCLOCK is always
     available on my BBS.

                                                 David H. Ransom, Jr.

Program JPLCLOCK Multimission Control Center Clock                 Page 18


F2   Set LOCATION CLOCKS
------------------------

     JPLCLOCK displays from one to four LOCATION CLOCKS. When the program 
is used in the JPL Mission Control Center, three of the clocks normally 
display the time for the DSN (Deep Space Network) antenna locations; the 
fourth location clock may be used for another location of interest or may 
be left blanked out. The location clocks are numbered #1 through #4 and are 
located in the lower left portion of the display screen below the main 
window in the following relative positions:

          |      Main Window       |  |
          +------------------------+  +---

          +----------+  +----------+  +---
          |    #1    |  |    #3    |  |
          +----------+  +----------+  +---

          +----------+  +----------+  +---
          |    #2    |  |    #4    |  |
          +----------+  +----------+  +---

     Each Location Clock displays the local time at the location using the 
following format (all times in 24-hour notation, HH:MM:SS):

          147   13:24:16 PDT
          --+   -+ -+ -+ --+
            |    |  |  |   |
            |    |  |  |   +---  Time Zone Abbreviation (if present)
            |    |  |  |
            |    |  |  +-------  Local Seconds
            |    |  +----------  Local Minutes
            |    +-------------  Local Hours
            |
            +------------------  Local Day of the Year

     Function Key F2 allows the user to change the name and time zone 
information for the four location clocks displayed below the main window.
If a location name is PRESENT for a given location clock, that clock will 
be displayed on the screen; if the location name is ERASED (the "Location 
Name" column for the clock is blank in the display), the clock will NOT be 
displayed on the screen. The default location clocks are shown below:

                                                         Uses
                    #  Location Name          UTC Offset  DST
                    -----------------------------------------
                    1  GDX  Goldstone              -8.00  YES
                    2  JSC  Houston                -6.00  YES
                    3  CAN  Canberra               11.00   NO
                    4  MAX  Madrid                  1.00   NO

                    Enter LOCATION # to change:

JPLCLOCK will automatically resume operation if no keyboard input is 
detected within 30 seconds. Each keystroke resets the 30 second timer. 

Program JPLCLOCK Multimission Control Center Clock                 Page 19


Press ENTER to cancel this function and return to the Main Menu making no 
changes. To continue, enter the number of the location clock to change and 
press ENTER. Then enter the new location name for that clock:

                    Enter new LOCATION NAME:

Press the TAB key to leave the name unchanged for this clock and skip to 
the time information. Press ENTER to erase the name and remove the clock 
from the display screen. To enter a new or corrected location name, type 
the new name and then press ENTER. JPLCLOCK will automatically capitalize 
the first letter of each word if it is lower case.
     In order to show the local time correctly for each location, JPLCLOCK 
must know the UTC Offset for the location; this is the number of hours 
which must be ADDED to UTC (Universal Coordinated Time) in order to obtain 
the local STANDARD time for the location. Do NOT include the additional 
hour if the location is on U.S. Daylight Savings Time; DO include the 
additional hour if the location is on daylight or summer time but the time 
changes do not correspond to those used in the United States. See the 
additional discussion below. 

                    Enter New UTC Offset (hours):

Press the TAB key to leave the current UTC Offset value unchanged. Press 
the ESC key to cancel all changes to this location clock. Otherwise, type 
the new UTC Offset in hours (and decimal parts of an hour if necessary) and 
then press ENTER.
     JPLCLOCK will independently adjust each location clock time for U.S. 
Daylight Savings Time if the special flag in the column "Uses DST" is 
marked "YES". As a general rule, therefore, respond "YES" if the location 
is within the United States (including Alaska and Hawaii); respond "NO" if 
the location is outside the United States.

                    Uses US Daylight (N=NO, Y=YES): 

     IMPORTANT NOTE: When the main Daylight Flag is changed (using F4+F3 
from the Main Menu), the appropriate correction will be automatically made 
for all locations which indicate "YES" in the "Uses DST" column. Locations 
outside the United States which use daylight or summer time but which 
change at different times from the United States should indicate "NO" in 
the "Uses DST" column and must be manually adjusted for each time change.
     
     When all of these questions have been answered, the information will 
be updated on the screen and the user may either continue to another 
location clock or return to the Main Menu.

Program JPLCLOCK Multimission Control Center Clock                 Page 20


F3   Set EVENT/MISSION TIMERS
-----------------------------

     One of the most important functions of JPLCLOCK is to be able to 
display Mission Elapsed Time (MET) or Countdown/Countup Time for a variety 
of missions and events. MIssion Elapsed Time usually measures the time 
since the mission was launched and is the primary time measure used for the 
Mission Timeline, the schedule of planned events and operations; this 
applies equally to short duration missions such as the Space Shuttle as 
well as to long duration missions such as Voyager and Hubble Space 
Telescope. Countdown/Countup Times may be critical events in the progress 
of a mission, such as scheduled Launch Time or Venus Orbit Insertion for 
Magellan, and controllers need to be able to judge the time remaining until 
(or time passed since) specific tasks or operations are to be (or were 
supposed to have been) performed.
     JPLCLOCK is able to independently time up to 60 different events or 
missions using six MISSION TIMER WINDOWS on the display screen and 
switching from one mission timer "page" to another to display up to ten 
pages. The mission timer windows are numbered #1 through #6 and are located 
on the right of the display screen beside the main window in the following 
relative positions:

          ---+  +----------------+
             |  |    TIMER #1    |
           M |  +----------------+
           a |
           i |  +----------------+
           n |  |    TIMER #2    |
             |  +----------------+
           W |
           i |  +----------------+
           n |  |    TIMER #3    |
           d |  +----------------+
           o |
           w |  +----------------+
             |  |    TIMER #4    |
          ---+  +----------------+

          ---+  +----------------+
             |  |    TIMER #5    |
          ---+  +----------------+

          ---+  +----------------+
             |  |    TIMER #6    |
          ---+  +----------------+

     Each Mission/Event Timer displays the current time value for that 
mission or event using one of the following formats (all times are shown as 
HH:MM:SS, hours:minutes:seconds):

          143  13:01:47       The event occurred 143 days plus time ago. 
                              When applied to a mission, this format is 
                              measured from the time of launch and is known 
                              as Mission Elapsed Time (MET) and is used for 
                              all mission event planning.

Program JPLCLOCK Multimission Control Center Clock                 Page 21



          -16  01:33:19       The event will occur in 16 days plus time.

           -0  07:44:51 *     The event will occur in the time shown and a 
                              flashing asterisk denotes less than 24 hours.

           -0  00:58:29 **    The event will occur in the time shown and 
                              two flashing asterisks denote less than 1 
                              hour remains.

           -0  00:08:14 ***   The event will occur in the time shown and 
                              three flashing asterisks denote less than 10 
                              minutes remain.


     Pressing F3 from the Main Menu displays the menu for setting the 
MISSION/EVENT TIMERS and the SELECTED EVENTS:

                        F1   Set MISSION/EVENT TIMERS
                        F2   Set SELECTED EVENTS

                     ENTER   Return to Main Menu

Press the Function Key for the desired selection or press ENTER to return 
to the Main Menu.

Set MISSION/EVENT TIMERS
------------------------

     Using F1, each Mission/Event Timer may be set to any desired time and 
date in the past or future over a range of from approximately minus 27 
years (-9,999 days before the event) to approximately plus 274 years 
(99,999 days after the event) referenced to the current time. Given the 
time scale of interplanetary missions such as Voyager 1 and 2 or Pioneer 
11, these time ranges are reasonable and necessary even though it may seem 
like "overkill" for a 5-day Space Shuttle mission. The Mission Timer Window 
background color (for color monitors) is RED if the event has not yet 
occurred and GREEN if the event has occurred. The color switch occurs when 
the Mission Timer reaches 0 days and 00:00:00 (hours:minutes:seconds).
     As a special feature to call attention to events about to occur, a 
single asterisk ("*") appears to the right of the countdown time when the 
event is less than 24 hours from occurrence; this changes to two asterisks 
at T minus one hour and to three asterisks at T minus ten minutes. The 
asterisks are removed once the scheduled event time occurs.
     When JPLCLOCK is operated in the NORMAL mode, Mission Timers #1 
through #6 are displayed continuously; the remaining 54 timers are neither 
checked nor displayed. However, when JPLCLOCK is operated in the PAGE mode, 
all 60 Mission Timers are checked and are displayed if a valid time and 
date has been entered. The Mission Timers are divided into ten pages of six 
timers each. The pages are numbered 0 through 9; Mission Timers #1 through 
#6 appear on Page 0, Mission Timers #7 through #12 appear on Page 1, and so 
forth. If any one of the timers in a given page is valid, that page will be 
displayed; if no timers in a given page are valid, that page will be 
skipped. Each page is displayed for 30 seconds and then the program cycles 
to the next valid page. With active Mission Timers in each of the ten 

Program JPLCLOCK Multimission Control Center Clock                 Page 22


pages, it can require up to 5 minutes to complete a full cycle through the 
timers.
     When the PAGE mode is active and JPLCLOCK is cycling through all 
active Mission Timers, a special "bar meter" is displayed at the top right 
of the Mission Timers. This is a row of ten special square symbols, one for 
each of the ten Mission Timer pages, which indicates the status of the 
page. If there are no active Mission Timers on the page, the symbol is 
GRAY. If one or more Mission Timers on the page is in the countdown mode 
(the event has not yet occurred), the symbol is RED. If all active Mission 
Timers on the page are in the countup or Mission Elapsed Time mode, the 
symbol is GREEN. The current active page is flashing.
     With up to 60 Mission Timers active in the PAGE mode, it might be easy 
to overlook an event which is scheduled to occur in the near future. The 
flashing asterisks described above may help to avoid this situation but 
JPLCLOCK solves the problem by holding the display on a page if any Mission 
Timer on that page will reach Time Zero within the next hour. When the 
current page is being held in this manner, the word "HOLD" appears above 
the Mission/Event Timers and the flashing symbol corresponding to the held 
page changes to YELLOW. The HOLD remains in effect until all timers on that 
page are either more than one hour before Time Zero or have passed Time 
Zero by more than one hour OR until another page includes events closer to 
their Time Zero. When the hold is removed, normal cycling is resumed and 
the program checks for other potential HOLD opportunities on each page 
before selecting the next page to display. See also the discussion below 
(in the section Set DAYLIGHT and Defaults) regarding setting the PAGE Delay 
for additional suggestions.
     Not all Mission Timers on a particular page must be programmed. If the 
Event/Mission Name is blank, that Mission Timer will not be displayed and 
its position on the display screen will be blank. The user may therefore 
arrange both which page(s) will be displayed as well as what position(s) 
is(are) used to display the active timers on a given page. As noted above, 
if ALL Mission Timers on a particular page are blank, that page will be 
skipped.
     Function Key F3 provides the capabilities to enter, erase, or correct 
the Mission Timers. The first time F3 is used, Page 0 and the first six 
Mission Timers will be displayed; subsequent uses of F3 may start on a 
different page. The Page Number is shown along with the data for the 
individual Mission Timers on that page.


         #  Event/Mission Name      Time(UT)  Date (MDY)  Julian Date
PAGE     ---------------------------------------------------------------
         1  Galileo                 11:00:00  01/22/1990  2447913.958333
+---+    2  Magellan                08:00:00  05/09/1989  2447655.833333
|   |    3  Ulysses                 17:46:00  10/06/1990  2448171.240278
|   |    4  Hubble Space Telescope  12:33:52  05/07/1990  2448019.023519
|   |    5  Gamma Ray Observatory   15:22:45  04/05/1991  2448352.140799
+---+    6  ROSAT Observatory       21:47:59  06/01/1990  2448044.408322
         (Home, PgUp, PgDn, ENTER to return to Main Menu)
         Enter EVENT # to change (1-60):

     The reminder enclosed in parentheses indicates the special keys that 
are active at this prompt:


Program JPLCLOCK Multimission Control Center Clock                 Page 23


          Home      Display PAGE 0
          PgUp      Go to NEXT PAGE
          PgDn      Go to PRIOR PAGE
          ENTER     Return to Main Menu

Use PgUp or PgDn to review each of the ten Mission Timer pages or type the 
number of the desired Mission Timer followed by ENTER to edit that Mission 
Timer. When a Mission Timer has been selected, a flashing diamond will 
appear to the left of the Mission Timer number in the display and you will 
be asked to enter a new MISSION NAME. For the following example, Mission 
Timer #7 was desired and "7" was typed:

         #  Event/Mission Name      Time(UT)  Date (MDY)  Julian Date   
PAGE     ---------------------------------------------------------------
       * 7  Voyager 1               12:58:00  09/05/1977  2443392.040278
 -+      8  Voyager 2               14:24:00  08/20/1977  2443376.100000
  |      9                                                              
  |      10                                                             
  |      11                                                             
--+--    12                                                             
         (TAB to SKIP, #nn to COPY, ESC to CANCEL, ENTER to ERASE #7 data)
         Enter #7 EVENT/MISSION NAME:                                   

     The asterisk shown above will actually be displayed as a flashing 
diamond to indicate the selected Mission Timer. The reminder enclosed in 
parentheses indicates the special keys that are active at this prompt:

          TAB       SKIP the name, leaving it unchanged, and continue.
          ESC       CANCEL making changes to this Mission Timer
          ENTER     ERASE all data for this Mission Timer

     In some cases, you may wish to copy an event from one Mission Timer to 
another. If the event is simply being moved, you would then go back and 
erase the original entry; otherwise, the event will appear in multiple 
Mission Timers (which might be desired for certain important events). The 
"#nn" format may be used for this purpose by substituting the SOURCE 
MISSION TIMER NUMBER for "nn". Thus, after selecting the DESTINATION 
MISSION TIMER NUMBER in the previous step, you would enter "C13" to copy 
all data from Mission Timer #13 to the selected Mission Timer.
     In other cases, you may wish to prepare a group of related Mission 
Timers relative to a single time. A sequence of operations following launch 
or satellite deploy are examples of this situation. To do this, first 
select the "base time" event and enter its information into a selected 
Mission Timer. Next, select each successive Mission Timer whose time is 
relative to the "base time" and use one of the following formats:

          #nn+ddd/hh:mm:ss
          #nn+hh:mm:ss
          #nn-ddd/hh:mm:ss
          #nn-hh:mm:ss

where:

          #    Specifies the COPY syntax
          nn   SOURCE MISSION TIMER NUMBER, 1 to 60

Program JPLCLOCK Multimission Control Center Clock                 Page 24


          +    Specifies ADD to "base time"
          -    Specifies SUBTRACT from "base time"
          ddd  The number of DAYS to add/subtract to "base time"
          /    Separates DAYS from TIME
          hh   The number of HOURS to add/subtract to "base time"
          mm   The number of MINUTES to add/subtract to "base time"
          ss   The number of SECONDS to add/subtract to "base time"
          :    Separates hours:minutes and minutes:seconds

Note that the days portion of the command, "ddd/", may be omitted if the 
value is zero; omitting the days is equivalent to a days portion of "000/". 
The number of digits shown for each portion of the command may not be 
exceeded, but leading zeroes may be omitted. Times may differ by as little 
as one second. (In fact, they may be identical if you wish.)
     As an example of relative Mission Timer programming, suppose that the 
"base time" for a sequence of events is on 7/11/1991 at 13:44:00 UTC and 
that a series of subsequent events will occur at this "base time" plus 37 
seconds, 1 minute and 30 seconds, and 3 hours and 7 minutes. The following 
commands will set up this sequence of Mission Timers:

          25             Event Timer Number
          Base Event     Event Name
          7/11/91        Event Date
          13:44          Event Time

          26             First Subsequent Timer Number
          #25+00:00:37   Relative time to Mission Timer 25

          27             Second Subsequent Timer Number
          #25+00:01:30   Relative time to Mission Timer 25

          28             Third Subsequent Timer Number
          #25+03:00:07   Relative time to Mission Timer 25

After these commands have been entered, Mission Timers 25 through 28 will 
contain the base event and the three subsequent events. Since the "copy" 
format has been used for the subsequent events, the names will be identical 
in all four Mission Timers. You may then edit Mission Timers 26 through 28 
by selecting them in turn, entering a new event name, then pressing TAB in 
place of a date entry to leave that information unchanged.
     Future events are sometimes rescheduled. To accommodate this 
situation, the "#nn" command may be used to copy an event to the same 
Mission Timer with a positive or negative time adjustment. Select the 
Mission Timer number you wish to adjust, enter the "#nn" command as 
described above (including the relative time adjustment) and the change 
will be made. For example, to advance the time for Mission Timer 44 by one 
hour and thirty minutes, enter the following commands:

          44             Timer Number to adjust
          #44+1:30       Advance the time by 1:30

This example illustrates a "shortcut": if the seconds are zero, they may be 
omitted. Similarly, if both minutes and seconds are zero, both may be 
omitted. The hours could also have been entered with a decimal fraction and 
the minutes omitted: "#44+1.5" to achieve the same result. The optional 

Program JPLCLOCK Multimission Control Center Clock                 Page 25


days ("#44+3/1:30" to advance the time by 3 days, 1 hour, 30 minutes) could 
have been used if required.
     If you wish to enter new data for the selected mission timer, type the 
new name for this Mission Timer followed by ENTER. You will then be asked 
to enter the new DATE for this timer:

          (ESC to CANCEL)                
          Enter new DATE (MM/DD/YYYY or JD/MJD):

Press ESC to CANCEL making changes to this Mission Timer or type the new 
DATE followed by ENTER. Dates are normally entered using "MM/DD/YYYY" 
format where "MM" is the MONTH (month number), "DD" is the DAY, and "YYYY" 
is the YEAR. JPLCLOCK will also accept a two-digit year and add 1900 to the 
value entered; "1991" and "91" will both be accepted as "1991". JPLCLOCK 
will also accept several "JD" (Julian Date) formats by prefixing the date 
entry with one of the following:

       Prefix        Julian Date   Format Name               Starting Date
       -------------------------------------------------------------------
           JD     2448424.375000   Standard Julian Date   (-4713 JAN  1.5)
          MJD       48423.875000   Modified Julian Date    (1858 NOV 17.0)
          DJD       33404.375000   Dublin Julian Date      (1900 JAN  0.5)
          TJD        8423.875000   Truncated Julian Date   (1968 MAY 23.0)

All of the Julian Date formats in the example are equal to June 16, 1991, 
at 14:00 PDT. "JD" is the standard format used by astronomers and most 
scientists. The other formats have been developed to reduce the number of 
digits required to uniquely identify a specific date but have more 
restricted range if negative numbers or large numbers are to be avoided. 
NASA, for example, frequently uses the "TJD" format.

NOTE: When one of the Julian Date formats is used, the time is implicit and 
the "New TIME" prompt will be skipped. Thus, an entry of "JD2448424.375" or 
"TJD8423.875" would yield the same time and date as "6/16/91" (for DATE) 
and "14:00P" (for TIME).

     After the new date has been entered (and provided you did not use one 
of the Julian Data formats), you will be prompted for the new TIME:

          (ESC to CANCEL)
          Enter new TIME (UTC or Zone):

Type the desired new time using the "HH:MM:SS" format followed by ENTER. 
JPLCLOCK is very flexible as to the time format. JPLCLOCK requires the 24-
hour format. Decimal fractions for the last value entered are accepted, 
leading zeroes are NOT required, the separator may be either the colon 
(":") or the comma (","), and the entry may omit values which are zero. 
Each of the following examples will be accepted as 14:15 (2:15 PM):

          14:15:00
          14,15
          14.25

JPLCLOCK assumes that the time entered is Coordinated Universal Time (UTC) 
unless a suffix is added to indicate otherwise. The following time zone 

Program JPLCLOCK Multimission Control Center Clock                 Page 26


suffixes are supported by JPLCLOCK:

          U    UTC       Universal Coordinated Time
          A    AST/ADT   Atlantic Time Zone
          E    EST/EDT   Eastern Time Zone
          C    CST/CDT   Central Time Zone
          M    MST/MDT   Mountain Time Zone
          P    PST/PDT   Pacific Time Zone
          Y    YST/YDT   Yukon Time Zone (sometimes "Alaska")
          H    HST/HDT   Hawaiian Time Zone

     Except for UTC, JPLCLOCK will automatically adjust the entered time 
for the appropriate time zone AND for daylight savings time (if in effect). 
Thus, an entry of "14:00P" will be interpreted as Pacific Standard Time 
(PST) if the Daylight Flag is OFF, and as Pacific Daylight Time (PDT) if 
the Daylight Flag is ON. If no suffix is included or if the "U" suffix is 
added, no adjustment for the Daylight Flag will be made and the time entry 
will be accepted as UTC. By using the appropriate time zone suffix, times 
may thus be entered directly in local time for each time zone in the United 
States, Alaska, and Hawaii without making any conversions (or mistakes!). 
JPLCLOCK makes the required conversions to the time (and date, if 
necessary) and displays the resulting Mission Timer values in UTC.

Program JPLCLOCK Multimission Control Center Clock                 Page 27


Set SELECTED EVENTS
-------------------

     Press F2 to set the SELECTED EVENTS. The program will display the 
currently selected SELECTED EVENTS, if any, and remind you that the 
SELECTED EVENTS are displayed ONLY when the SMALL Main Clock window is 
active. To make the SMALL Main Clock window active, press ALT-F6 when the 
Main Clock window is on the screen.

            SELECTED EVENTS are active with SMALL Main Window ONLY!

                    #    MT#    Mission/Event Name
                    ----------------------------------------
                    1    11     Hubble Space Telescope
                    2    17     Gamma Ray Observatory
                    3    23     Voyager 1
                    4    24     Voyager 2

              (ENTER to CLEAR, TAB to SKIP, ESC to CANCEL)
              Enter MISSION/EVENT TIMER # for Selected Event #1:

In the sample display above, the column marked "#" lists the four SELECTED 
EVENT timers in order; the column marked "MT#" lists the Mission/Event 
Timer which is associated with the corresponding SELECTED EVENT; and, the 
column marked "Mission/Event Name" lists the name of the selected 
Mission/Event Timer.
     The information for each SELECTED EVENT is requested in turn. The 
first prompt asks for Selected Event #1. As noted, press ENTER to clear 
that event, press TAB to skip to the next event, or press ESC to cancel and 
return to the Main Menu.
     The only information that can be entered here is the Mission/Event 
Timer number which you wish to be associated with each SELECTED EVENT. The 
actual data, the event name, date, and time, must already have been entered 
into the Mission/Event Timer (F3+F1 from the Main Menu). Note also that the 
while the full Mission/Event Name is displayed on the menu as shown above, 
the actual window on the screen will truncate the name to a maximum of 19 
characters; this is because the SELECTED EVENT windows are somewhat 
narrower than the main Mission/Event Timer windows. If you wish to edit the 
name so that it will fit correctly in the SELECTED EVENT windows, you must 
edit the Mission/Event Timer entry using F3+F1 from the Main Menu (or just 
F1 from the event menu).

Program JPLCLOCK Multimission Control Center Clock                 Page 28


F4   Set DAYLIGHT and Defaults
------------------------------

     Function Key F4 allows you to switch the system from local STANDARD 
time to local DAYLIGHT time and set a number of program defaults. Pressing 
F4 from the Main Menu displays the following menu:


         Enter selection:
                           F1   Switch STANDARD/DAYLIGHT Time
                           F2   Set LOCAL NAME and TIME ZONE
                           F3   Restore Program DEFAULT DATA
                           F4   Set PAGE and TEXT Mode Delays [15,30]
                          ESC   Return to Main Menu
                        ENTER   Resume Program JPLCLOCK

                                Enter selection:

     Pressing ESC will return you to the Main Menu.
     Pressing ENTER will resume operation of program JPLCLOCK.
     Pressing F1 will switch the Daylight Flag between Standard time and 
Daylight time. NOTE: This function does NOT change your computer's clock; 
you must set the correct local time BEFORE using this function!
     Pressing F2 will allow you to enter a new name for your location and 
to set its standard UTC Offset (in hours) and Daylight Flag.
     Pressing F3 will restore the "hard-coded" program default data for the 
Local Name, Location Clocks and Mission Timers.
     Pressing F4 will prompt you to enter new values for the PAGE delay and 
the TEXT delay. The current values are shown at the right. The following 
information will be displayed and you will be asked for the PAGE Delay:

          PAGE Delay sets the time to display each page of Mission
          Timers. TEXT delay set the time to display each text page.

          PAGE Delay must be between 5 and 900 seconds.
          TEXT Delay must be between 5 and 900 seconds AND an even
          multiple of PAGE Delay. The times are adjusted if necessary.

          Enter PAGE Delay [15] (seconds):

The current PAGE Delay is shown in square brackets. Enter the desired new 
value for the PAGE Delay in seconds or press ENTER to leave the present 
value unchanged. You will then be asked for the TEXT Delay:

          Enter TEXT Delay [30] (seconds):

The current TEXT Delay is shown in square brackets. Enter the desired new 
value for the TEXT Delay in seconds or press ENTER to leave the present 
value unchanged.
     Note the minimum and maximum values allowed for these delays, 5 and 
900 seconds respectively. Note also that the TEXT Delay must be an even 
multiple of the PAGE Delay (for internal programming reasons). If this is 
not the case, TEXT Delay will be automatically adjusted accordingly. The 
values shown in the examples above are recommended as the minimum values 
for JPLCLOCK. Smaller values may allow insufficient time for reading.

Program JPLCLOCK Multimission Control Center Clock                 Page 29


     JPLCLOCK was originally designed for use with multiple events which 
are well spaced in time such as NASA planetary missions. Typical events in 
this environment are usually spaced minutes, hours, or even days apart. 
When the Mission/Event Timers are used for fast paced events such as the 
launch of a space shuttle (where events are separated by as little as a 
second or two), set the PAGE Delay to 5 seconds and disable the TEXT mode. 
Using that technique, JPLCLOCK will check all timers every five seconds and 
select the page with events closest to Time Zero. 
     However, even with the PAGE Delay set to 5 seconds JPLCLOCK may miss 
certain events which are spaced only a few seconds apart and which are on 
different Mission/Event Timer pages. This is dependent upon the actual 
times programmed compared to the PAGE Delay time; if an event occurs just 
after the PAGE Delay, that page will be held for the full delay time and 
other pages will not be checked until after the expiration of the delay 
time. With the PAGE Delay set to 5 seconds, this means that page switching 
may not occur until as many as four seconds have passed since Time Zero for 
an event on a given page. Where practical, events should be programmed such 
that there is more than twice the PAGE Delay separating events on different 
pages.

Program JPLCLOCK Multimission Control Center Clock                 Page 30


F5   Read or Save INI and MTD Files
-----------------------------------

     Two types of files are used to save and restore information by 
JPLCLOCK, distinguished by the filetypes ".INI" and ".MTD". INI files 
include all program initialization, Location Clock, and Mission/Event Timer 
data. MTD files include data for from 1 to 60 Mission/Event Timers only.
     Pressing Function Key F5 from the Main Menu will display the following 
menu:

          F1   Read external INI File      F3   Read external MTD File
          F2   Save external INI File      F4   Save external MTD File
         ESC   Return to Main Menu
       ENTER   Resume Program JPLCLOCK

               Enter selection:

     JPLCLOCK reads the file JPLCLOCK.INI each time it is started, and 
writes a new JPLCLOCK.INI file each time the program is halted. This INI 
file contains all the information about the local installation, the 
Location Clocks, and the Mission Timers. For installations where only the 
first six Mission Timers are used, this information will change only 
infrequently and additional INI files will probably not be required.
     Users may find it convenient to re-read the normal INI file, 
JPLCLOCK.INI, if they have incorrectly changed information and wish to 
restore the original information. (NOTE: Exiting program JPLCLOCK in this 
situation will cause the incorrect information to be written to file 
JPLCLOCK.INI and the original data in that file will be permanently lost!) 
As a protection against this sort of problem, it is recommended that all 
users create a standard INI file, named STANDARD.INI for example, that 
represents the normal program configuration. This is most easily done by 
verifying the configuration of JPLCLOCK (by running the program) and then 
quiting the program and copying file JPLCLOCK.INI to file STANDARD.INI. 
Function Key F1 may then be used from this menu to reload the standard
configuration at any time.
     However, installations using JPLCLOCK in the PAGE mode may find that 
advance preparation of INI and MTD files (using another computer running 
JPLCLOCK) is very helpful in preparing for upcoming events on multiple 
missions. In order to facilitate this process, JPLCLOCK can both read and 
write INI files. This takes advantage of JPLCLOCK's internal editing 
capabilities (using Function Key F3 from the Main Menu) and may avoid 
errors due to manual editing and time/date conversions, especially when 
various different time zones are involved. In most cases, only the 
Mission/Event Timers change and therefore the MTD file format is 
recommended. When a completely new setup is configured, the INI file format 
is recommended.
     A new set of Mission/Event Timers can be prepared on an "offline 
computer", tested, and written to an MTD file for use on an "online 
computer". Files may be exchanged via disk, local area networks, or 
telecommunications software. Since the dates and times in an MTD file are 
saved in the Julian Date format, these date are independent of time zone 
and location. Once the new MTD or INI file has been loaded onto the "online 
computer", JPLCLOCK may be paused, the new file read, and program operation 
resumed. Performed in this manner, the entire updating process will take 
the "online computer" offline for a few seconds. Any number of INI and MTD 

Program JPLCLOCK Multimission Control Center Clock                 Page 31


files may be prepared in this fashion, the only requirement being that they 
have unique names and the correct filetype.


READ and SAVE INI Files
-----------------------

     INI files MUST have the file type ".INI". The filename may be any 
legal file name EXCEPT "JPLCLOCK.INI". Manual editing of INI files is NOT 
recommended; however, if this is done be certain to use a simple ASCII 
editor or an editor which has a "non-document" mode. Although the format of 
the INI file uses a simple comma-delimited format, an error in the file 
structure may cause the program to operate incorrectly or to crash (halt 
with an error message). If all else fails, delete the file JPLCLOCK.INI and 
restart the program; JPLCLOCK will then use its internal default data and 
construct a new INI file.
     Press F1 to read an INI file or F2 to write an INI file. All files are 
assumed to be in the current drive and directory. For file read operations, 
the file must exist. For file write operations, if the file does not exist 
it will be created and if the file does exist it will be overwritten. If 
either F1 or F2 is pressed, the following prompt will be displayed:

     INI files contain the setup and mission/clock data for JPLCLOCK.
     Enter the name of the INI file which you wish to READ or SAVE.
     Do NOT include a filetype; the program automatically adds '.INI'.
     (ENTER = 'JPLCLOCK', ESC to CANCEL)
     Enter filename to READ (without .INI):

If you have pressed F2 to SAVE, the word "READ" will be replaced by the 
word "SAVE" in the sample above. Press ESC to CANCEL the file read or 
write. Press ENTER to use the default file name JPLCLOCK.INI. Otherwise, 
type the filename WITHOUT the ".INI" filetype followed by ENTER. JPLCLOCK 
will automatically append ".INI" to the filename and then read or write the 
file and return to this menu.


READ and SAVE MTD Files
-----------------------

     MTD files are processed in a manner almost identical to INI files. The 
default filename used if ENTER is pressed is JPLCLOCK.MTD. The principal 
difference is that since only the Mission/Event Timer data is included, 
JPLCLOCK must know which timers to SAVE or the first timer to which data 
should be READ.
     Pressing F3 to READ an MTD file will display the following prompts in 
turn:

     Enter FIRST TIMER NUMBER [1]:
     Enter TIME OFFSET [0]:

In each case, the number enclosed in square brackets "[...]" is the default 
response if ENTER is pressed. When reading an MTD file, only the first 
Mission/Event Timer number is required. JPLCLOCK will read the file until 
all data have been read or until timer 60 has been read, whichever comes 
first. You may also add a TIME OFFSET to the Mission/Event Timer data as it 

Program JPLCLOCK Multimission Control Center Clock                 Page 32


is read; this may be helpful if the schedule for the events in the MTD file 
has changed. The TIME OFFSET is entered in one of the following formats:

          +ddd/hh:mm:ss
          +hh:mm:ss
          -ddd/hh:mm:ss
          -hh:mm:ss

where:

          +    ADD the TIME OFFSET to event time
          -    SUBTRACT the TIME OFFSET from event time

          ddd  The number of DAYS to add/subtract to event time
          /    Separates DAYS from TIME
          hh   The number of HOURS to add/subtract to event time
          mm   The number of MINUTES to add/subtract to event time
          ss   The number of SECONDS to add/subtract to event time
          :    Separates hours:minutes and minutes:seconds

Note that the days portion of the command, "ddd/", may be omitted if the 
value is zero; omitting the days is equivalent to a days portion of "000/". 
The number of digits shown for each portion of the command may not be 
exceeded, but leading zeroes may be omitted. 
     Pressing F4 to SAVE an MTD file will display the following prompts in 
turn:

     Enter FIRST TIMER NUMBER [1]:
     Enter LAST TIMER NUMBER [60]:

In each case, the number enclosed in square brackets "[...]" is the default 
response if ENTER is pressed. The only constraints are that the LAST TIMER 
NUMBER must be greater than or equal to the FIRST TIMER NUMBER, and no 
timer number may exceed 60. After these special prompts are answered, the 
next prompt requests the MTD filename:

     MTD files contain only selected MISSION TIMER data for JPLCLOCK.
     Enter the name of the MTD file which you wish to READ or SAVE.
     Do NOT include a filetype; the program automatically adds '.MTD'.
     (ENTER = 'JPLCLOCK', ESC to CANCEL)
     Enter filename to READ (without .MTD):

If you have pressed F4 to SAVE, the word "READ" will be replaced by the 
word "SAVE" in the sample above. Press ESC to CANCEL the file read or 
write. Press ENTER to use the default file name JPLCLOCK.MTD. Otherwise, 
type the filename WITHOUT the ".MTD" filetype followed by ENTER. JPLCLOCK 
will automatically append ".MTD" to the filename and then read or write the 
file and return to this menu.
     The MTD file format is ideal for preparing Mission/Event Timer data 
for multiple systems whose configuration and/or time zone may not be the 
same. Since the time and data information is saved in the Julian Date 
format, it is independent of the local time zone for any particular 
installation of JPLCLOCK. Further, since the Mission/Event Timer number is 
specified by the ultimate user, different users may select different timer 
numbers to suit their own installations.

Program JPLCLOCK Multimission Control Center Clock                 Page 33


     Included with the JPLCLOCK files is STS43.MTD; this file has 13 events 
associated with Space Shuttle Mission STS-43, scheduled for July 23, 1991. 
The events include the important milestones of the ascent phase, the deploy 
events for TDRS-E, and the deorbit burn and landing. Although the flight of 
STS-43 is a one-time event, the MTD file may serve as an example of how to 
prepare and use MTD files; for example, read the file into the system 
starting at timer #43.
     As with file STS43.MTD, events of interest may be prepared in advance 
and distributed to users without regard for their location or time zone. By 
maintaining a backup copy of their "standard" INI file, users may freely 
read in MTD files, use them for as long as desired, then restore their 
original configuration by reading in their "standard" INI file.
     The same techniques may be used to move events from one set of timers 
to another. First write the MTD file for the desired events, then clear the 
timers involved (either one by one using F3+F1, or by reading in your 
"standard" INI file), then read the MTD file just created using the new 
timer numbers. After some experimentation, I discovered that it would be 
handy to be able to add a time offset (plus or minus) to events as they are 
being read from the MTD file so that schedule changes or delays might be 
easily accommodated; the next version of JPLCLOCK will include an 
additional prompt to permit you to add such an offset which will be applied 
equally to all timer events being read.
     Another use for the MTD file is to easily set up all active 
Mission/Event Timer pages with the same set of events for the first several 
timers. The sample INI file distributed with JPLCLOCK illustrates this 
technique; the first three timers are always the same and only the bottom 
three change from page to page. In this case, save an MTD file with the 
desired "constant" events, then read that MTD file back on each active 
timer page at the appropriate timer number. The "constant" events could as 
easily be the last timers on each page by selecting the appropriate timer 
numbers.


INI Files from Other Locations
------------------------------

     Except when JPLCLOCK is first started, the information specific to 
your location (Location Name, UTC Offset, Daylight Flag, etc.) is NOT 
processed when you read an INI file using F1. Therefore, if you receive an 
INI file from elsewhere, you should rename it to a convenient name (which 
might remind you of the source of the data, for example) and then read it 
into JPLCLOCK using F3. Since all of the remaining information in the INI 
file is recorded using UTC, JPLCLOCK will be able to make the necessary 
time conversions for display in your time zone.
     If you wish to use missions or events from a received INI file, you 
may read it in using F5, then save the desired information in selected 
Mission Timer Pages to an MTD file. Having saved the information, you may 
then re-read your own JPLCLOCK.INI file (press ENTER when asked for the INI 
filename) and read the mission or event data you saved to the MTD file 
using F5 as usual. Note that the times and dates shown on each Mission 
Timer page are always Coordinated Universal Time (UTC), not your local 
time, so the times will automatically be adjusted for your location and 
time zone.

Program JPLCLOCK Multimission Control Center Clock                 Page 34


F6   Self-Calibration using TIMESET
-----------------------------------

     Function Key F6 enables a special self-calibration procedure which 
causes JPLCLOCK to use program TIMESET to perform a series of calibration 
measurements over a period of 7 hours. Note that TIMESET must have been 
correctly configured and tested prior to automatic use. See the procedure 
for configuring TIMESET in the section F10 TIME SYNCHRONIZATION below and 
read the TIMESET documentation.
     When the Self-Calibration procedure is initiated, JPLCLOCK immediately 
makes a call using TIMESET and resets the drift and offset parameters. The 
program then makes subsequent calls at 1, 2, and 4 hour intervals (for a 
total of four calls) to enable calculation of new parameters. When the last 
call has been completed, a reasonable calibration of the DOS clock should 
have been calculated.
     The computer must be allowed to run JPLCLOCK continuously during the 
procedure. However, the usual commands are available for use between calls 
PROVIDED you do not exit to DOS and the clocks are displayed when the time 
comes to make each call. Of particular interest after the second call (in 
other words, after more than one hour has elapsed since the procedure was 
started) is the calculated DOS Clock Drift. With the main clock display on 
the screen, press ENTER twice to obtain the Main Menu, then press F10+F1 to 
view the current data:

                       DOS time:  06:45:26.17      07-05-1991
                      CMOS time:  06:45:27         07-05-1991
                  JPLCLOCK time:  06:45:27 PDT   13:45:27 UTC
                  JPLCLOCK date:    07/05/1991     07/05/1991

                JPLCLOCK will start automatically in 88 seconds

                 Current Julian Date:   2448443.073229
                 Last Synchronized:     2448442.500926
                 Time since Last Sync:        0.572303 days
                 Current Clock Offset:        0.00     seconds
                 Current DOS Drift Rate:     -1.512899 seconds/day
                 Current Total Adjust:       -0.87     seconds

                 Press ESC for Sync Menu, ENTER to ADJUST data:

In the example above, about half a day has elapsed since the last 
synchronization was performed. As a result of that measurement, JPLCLOCK 
has calculated that the drift rate of the DOS clock is -1.512889 seconds 
per day and that the current time must be adjusted by SUBTRACTING -0.87 
seconds from the DOS clock. Above these data are four time displays showing 
the present DOS clock (the one being calibrated), the CMOS clock (the 
computer's hardware clock), and the JPLCLOCK time and date both for the 
local time zone and for UTC. The JPLCLOCK time is the time displayed in the 
Main Clock window and reflects the current calculated adjustment from the 
DOS time.
     When using self-calibration, ALWAYS press ESC after viewing these data 
to return to normal operation. If you press ENTER by mistake, press the TAB 
key to leave all items unchanged.
     JPLCLOCK generates a "temporary" automatic synchronization schedule 
during self-calibration, saving the prior schedule (if any). Thus, the 

Program JPLCLOCK Multimission Control Center Clock                 Page 35


program will perform the procedure over 7 hours and then revert to the 
original automatic schedule (if automatic synchronization is ENABLED) or 
turn off automatic synchronization (if automatic synchronization is 
DISABLED). You may verify the current status of the automatic 
synchronization from the Main Menu by pressing F10+F3; this will show the 
schedule now in effect; note that the times shown in the schedule are UTC.

                   F1   Execute TIMESET (Manual)
                   F3   Set Automatic Synchronization: ENABLED
                          NEXT TIME = 00:55:00 UTC
                          START     = 08:55:00 UTC
                          INTERVAL  = 04:00:00
                  ESC   Return to Sync Menu
                ENTER   Resume Program JPLCLOCK

                        Enter selection:

In the example shown, the automatic synchronization schedule has been set 
to start at 00:55:00 UTC and repeat every four hours. Comparing this 
schedule against the current time, JPLCLOCK will next perform the 
synchronization at 08:55:00 UTC.

Program JPLCLOCK Multimission Control Center Clock                 Page 36


F7   Switch TEXT Mode
---------------------

     Function Key F7 permits you to enable or disable the TEXT mode 
provided the text file JPLCLOCK.MSG is present on the current drive and 
directory when the program is started. This command is equivalent to the 
"/TEXT" command line option. If the file JPLCLOCK.MSG has been added while 
using the DOS SHELL (F9), the text will NOT be available since the file is 
read ONLY when JPLCLOCK is started from DOS. Quit program JPLCLOCK and 
restart the program if you wish to add or edit JPLCLOCK.MSG.


F8   Switch PAGE Mode
---------------------

     Function Key F8 permits you to enable or disable the PAGE mode. This 
command is equivalent to the "/PAGE" command line option. Disabling the 
PAGE mode will also disable the TEXT mode if it is currently enabled.


F9   DOS Shell (DOS 3.3+ ONLY)
------------------------------

     Function Key F9 invokes the DOS SHELL, loading a second copy of 
COMMAND.COM and displaying the usual DOS prompt. Most DOS commands and 
programs are now available. To return to JPLCLOCK, type the following at 
the DOS prompt (followed by ENTER):

          EXIT

     Note that using the SHELL with versions of DOS prior to Version 3.3 
may yield unpredictable results. Because program JPLCLOCK remains in memory 
and a second copy of COMMAND.COM is also loaded into memory, the memory 
available to execute programs under the SHELL is considerably reduced. Some 
programs may fail to execute due to insufficient memory or you may receive 
an "Out of Memory" message. If this happens, check to see that all TSR 
(Terminate and Stay Resident) programs that are not required have been 
disabled. If this does not solve the problem, the program in question 
cannot be executed with the shell.
     Except for the potential memory problem, the SHELL operates exactly 
the same as normal DOS. Although JPLCLOCK is resident in memory, it is not 
active. The timer which causes execution of the program to automatically 
resume after some seconds is therefore also NOT active and the computer 
will remain in the SHELL until you type "EXIT" followed by ENTER.

Program JPLCLOCK Multimission Control Center Clock                 Page 37


TIME SYNCHRONIZATION
--------------------

     As discussed at length elsewhere, the hardware and software clocks on 
the typical personal computer do not keep accurate time. In order to use 
JPLCLOCK in a critical installation such as the JPL Multimission Computer 
Control Center, additional steps must be taken to ensure the accuracy of 
the JPLCLOCK display.

     NOTE: Before proceeding with this section, please read the section DOS 
CLOCK CALIBRATION below. An understanding of that section and its 
procedures is essential before time synchronization is attempted.

     Time synchronization may be accomplished either manually (using the 
DOS TIME command outside program JPLCLOCK) or by using the program TIMESET. 
TIMESET, in turn, may be invoked either on demand or its use may be 
scheduled to occur at any desired interval. The balance of this section is 
concerned with the use of program TIMESET. TIMESET is copyrighted software 
distributed separately, and it must be registered before regular use. See 
the TIMESET documentation for details. (Additional information on TIMESET 
is also given in the section DOS CLOCK CALIBRATION, below.)


Configuring Program TIMESET
---------------------------

     JPLCLOCK has been tested ONLY with Professional TIMESET Version 6.0 
and may not operate correctly with other versions of the program. Before 
program TIMESET may be used with JPLCLOCK it must be configured for your 
computer system. In addition to the "regular" configuration described in 
the TIMESET documentation, an additional process is required here. In order 
for TIMESET to operate successfully with JPLCLOCK, two special versions of 
the program must be prepared: one for your local STANDARD time and one for 
your local DAYLIGHT time. If you have not already done so, configure 
TIMESET by entering the following command at the DOS prompt:

          TIMESET /C

     The following configuration screen will be displayed for your 
approval. The information shown here is that used on one of my test 
computers.

             Outside phone: NULL
         Naval Observatory: 12026530351
      Inst. Stds. Technol.: 13034944774

===>             Time zone: PACIFIC
===>           Time season: STANDARD

               Serial port: COM1
            Dialing method: TONE
         Dialing baud rate: 2400
          Lock modem speed: NO



Program JPLCLOCK Multimission Control Center Clock                 Page 38


           User's commands: L2X4S7=45&C1&D2

            Computer clock: DOS CLOCK-CALENDAR

===>   Immediate/countdown: IMMEDIATE
===>      Manual/automatic: AUTO NIST
                Video type: COLOR

You will not need to change some of the information shown here. Verify that 
the modem information is correct. You WILL need to set your TIME ZONE to 
the correct zone and to set the TIME SEASON to STANDARD. Make sure the 
IMMEDIATE/COUNTDOWN is set to IMMEDIATE and that MANUAL/AUTOMATIC is set to 
AUTO NIST or AUTO USNO (depending upon the time service you wish to use. 
The four critical items are each marked with an arrow ("===>") in the 
sample above. Once all data are correct, press F10 to save the configured 
version, then ESC to exit the program.
     You will now have a program file, TIMESET.COM which represents your 
basic TIMESET configuration for STANDARD time in your time zone. It may be 
used at any time by simply entering the following command at the DOS 
prompt:

          TIMESET

Use the DOS COPY command to save a separate STANDARD TIME version of this 
program for JPLCLOCK's use:

          COPY/B TIMESET.COM TIMESTD.COM

Now, repeat the configuration process by entering the command "TIMESET /C" 
and leave everything the same EXCEPT change the TIME SEASON to DAYLIGHT. 
Press F10 when you have made the change to save a DAYLIGHT version of 
TIMESET. Then use the DOS COPY command to save a separate DAYLIGHT TIME 
version of this program for JPLCLOCK's use:

          COPY/B TIMESET.COM TIMEDAY.COM

Use the DOS DIR command to be certain that you now have two specially named 
versions of TIMESET on disk:

          TIMESTD.COM
          TIMEDAY.COM

Copy these two files to your JPLCLOCK disk and/or directory.


                              IMPORTANT NOTE
                              --------------

          Unfortunately, TIMESET cannot be instructed to select
          STANDARD TIME or DAYLIGHT TIME from the command line, 
          only by changing the its configuration. JPLCLOCK 
          already knows which time season is in effect and uses 
          these two special versions of TIMESET as appropriate. 
          If these two files are not present, JPLCLOCK's auto-
          matic time synchronization functions will NOT execute 

Program JPLCLOCK Multimission Control Center Clock                 Page 39


          correctly!

          CHECK AGAIN TO BE SURE THESE TWO FILES ARE IN YOUR 
          JPLCLOCK DRIVE AND DIRECTORY:

               TIMESTD.COM
               TIMEDAY.COM

          TEST BOTH PROGRAMS CAREFULLY TO BE CERTAIN THAT EACH 
          VERSION CALLS THE SELECTED TELEPHONE TIME SERVICE AND 
          SETS YOUR COMPUTER CLOCK CORRECTLY AND FOR THE SELECTED 
          TIME SEASON. JPLCLOCK HAS NO WAY OF DETECTING IF YOUR 
          COMPUTER CLOCKS ARE SET INCORRECTLY!

     This completes configuration of program TIMESET for use with JPLCLOCK. 
It might be wise to make backup copies of the two special versions of the 
program so that they will be readily available if needed.


Time Synchronization Menu
-------------------------

                      F1   VIEW or SET Time Sync Data
                      F3   TIMESET Time Synchronization
                      F5   MANUAL Synchronization
                     ESC   Return to Main Menu
                   ENTER   Resume Program JPLCLOCK

                           Enter selection:

Select F1 to view the current time synchronization data or to manually 
execute program TIMESET. Select F3 to enable or disable automatic time 
synchronization using program TIMESET. Select F5 to manually synchronize 
the DOS clock against an external source such as radio station WWV using 
audio tones.


VIEW or SET Time Sync Data
--------------------------

                 Current Julian Date:   2448430.351713
                 Last Synchronized:     2448428.036412
                 Time since Last Sync:        2.315301 days
                 Current Clock Offset:        0.00     seconds
                 Current DOS Drift Rate:     -3.034839 seconds/day
                 Current Total Adjust:       -7.03     seconds

                 Press ESC for Sync Menu, ENTER to ADJUST data:

Press ESC to return to the Time Synchronization Menu, or press ENTER to 
adjust the Last Synchronized, Clock Offset, and/or DOS Drift Rate 
parameters. See the section DOS CLOCK CALIBRATION for additional 
information on measuring these parameters. During CALIBRATION or after the 
DOS software clock has been correctly set, do NOT manually adjust these 
data!

Program JPLCLOCK Multimission Control Center Clock                 Page 40




TIMESET Time Synchronization
----------------------------

                   F1   Execute TIMESET (Manual)
                   F3   Set Automatic Synchronization: ENABLED
                          NEXT TIME = 16:55:00 UTC
                          START     = 00:55:00 UTC
                          INTERVAL  = 08:00:00
                  ESC   Return to Sync Menu
                ENTER   Resume Program JPLCLOCK

                        Enter selection:

     Press F1 to immediately execute program TIMESET. JPLCLOCK will select 
either program TIMESTD or TIMEDAY depending on whether it is set for 
STANDARD or DAYLIGHT time.
     Press F3 to enable, disable, or change the automatic time 
synchronization function. The sample shown above indicates that the 
automatic function is ENABLED, that it will next occur at 16:55:00 UTC, and 
that JPLCLOCK will automatically schedule time setting starting at 00:55:00 
UTC each day and at eight hour intervals thereafter. Press ENTER to DISABLE 
the automatic time synchronization feature, or enter the START time and the 
TIME INTERVAL when requested.
     As a general rule and to minimize use of the NIST and USNO telephone 
time services, the longer the synchronizing interval, the more accurate the 
time measurements. This is because the DOS clock ticks occur at 55 
millisecond intervals and in order to maintain the desired accuracy of plus 
or minus 250 milliseconds per day or better, this "granularity" should be 
small compared to the total time used to make the measurements. Where 
practical, I recommend a normal interval of at least 8 hours and preferably 
12 or more hours (after initial calibration).


MANUAL Synchronization
----------------------

                 Current Julian Date:   2448453.693785
                 Last Synchronized:     2448448.302674
                 Time since Last Sync:        5.391111 days
                 Current Clock Offset:       -0.50     seconds
                 Current DOS Drift Rate:     -1.512899 seconds/day
                 Current Total Adjust:       -8.66     seconds

                       (Press ESC to return to Sync Menu)

                 Press: +/= to INCREMENT    - to DECREMENT
                        Z to RESET Offset   S to SET Sync Time

     Manual Synchronization causes JPLCLOCK to present the display shown 
above and to generate a brief tone each second. This may be compared to the 
one second "ticks" generated by radio station WWV and JPLCLOCK's tone 
adjusted in 50 millisecond increments until the two tones occur 
simultaneously. It is my experience that synchronization to within about 

Program JPLCLOCK Multimission Control Center Clock                 Page 41


100 or 150 milliseconds may be obtained using this technique.
     Press the "+" or "=" (an unshifted "+" for convenience) key to 
increment the Current Clock Offset, or press the "-" key to decrement the 
Current Clock Offset. When you are satisfied that JPLCLOCK is synchronized 
as accurately as is possible, press the "S" key (upper or lower case) to 
set the synchronization time for use in drift calculations. Press the "Z" 
key (upper or lower case) to reset the Current Clock Offset.
     While not as accurate as using the NIST or USNO Telephone Time 
Services, this method can be used over extended times to calibrate JPLCLOCK 
to reasonable accuracy. The only additional equipment required is a 
shortware receiver capable of receiving WWV, WWVH or a similarly accurate 
time source. WWV and WWVH may be received on the following frequencies:

          2.5 MHz
          5.0 MHz
         10.0 MHz
         15.0 MHz
         20.0 MHz   (WWV only)

The quality of reception will vary with time of day, atmospheric conditions 
and distance from the transmitter (Fort Collins, CO or Hilo, HI). 
Propagation delay may be estimated at approximately 5 microseconds per 
statute mile or 5 milliseconds per 1,000 miles, probably not significant 
when performing manual synchronization.

Program JPLCLOCK Multimission Control Center Clock                 Page 42


DOS CLOCK CALIBRATION
---------------------

     The primary purpose of JPLCLOCK is to display the current time and 
other related information in the JPL Multimission Computer Control Center. 
Accuracy and precision in that environment are essential. There is a 
tendency these days to accept whatever a computer says as the absolute 
truth without regard for whether or not the information is even 
"reasonable". For something as basic as time, even an experienced computer 
user often assumes that it is correct. JPLCLOCK attempts to match reality 
with that expectation.
     Given that a computer clock has been set with reasonable accuracy, the 
computer's time will indeed be sufficient for many applications; if you are 
using a word processing or spreadsheet program, knowing the time to within 
a minute or two is probably adequate. For JPLCLOCK, however, this level of 
accuracy simply will not suffice; when used in the Multimission Mission 
Control Center, the information displayed must be correct to within less 
than a second. Unless other steps are taken to set the clock and to 
maintain its accuracy, this will not be the case. No matter how accurately 
the clock on a typical personal computer is set, it will only be a matter 
of hours before the time will have drifted by some seconds. Measured over a 
number of days, the accumulated errors can easily amount to a minute or 
more.
     The timekeeping operations of an IBM-compatible computer are actually 
performed by two separate and independent functions: a clock-calendar 
integrated circuit and lithium battery combination which maintains the 
current time and date in hardware; and a section of the MS-DOS or PC-DOS 
operating system software which maintains the current time and date in 
software. When computer power is off, the hardware chip continues to 
operate using its battery; when the computer is started ("booted"), the 
operating system software reads the hardware clock and sets its internal 
software clock. Absent special software, the DOS time thereafter relies 
entirely on the software clock until the next time the computer is 
restarted. Unfortunately, neither of these clocks was designed for 
accuracy; early versions of the PC did not even include the 
hardware/battery arrangement. Even the typical electric clock, which uses 
the power line frequency for its timekeeping reference, is far more 
accurate.
     The accuracy of the DOS time at any instant is the result of the 
accumulated errors in both clocks. The hardware clock will drift as a 
function of time, temperature, and crystal aging; the software clock will 
gain or lose time depending upon the skill with which its software was 
written and how well that software "cooperates" with the balance of the 
computer's hardware and software. Some software, especially network and 
high speed communications software, can prevent the DOS clock software from 
incrementing when it should, usually resulting in the DOS clock losing 
time. The problem was compounded with the release of DOS Version 3.3; 
beginning with that version, the DOS TIME and DATE commands adjust BOTH the 
hardware and software clocks and thereby potentially eliminate the hardware 
clock as even a modestly reliable reference. If today's personal computers 
used the power line frequency as their primary reference, and only used the 
battery powered crystal oscillator if the power line was not present, clock 
accuracy could at one stroke be improved by at least several orders of 
magnitude.


Program JPLCLOCK Multimission Control Center Clock                 Page 43



Setting DOS Time
----------------

     Bearing these considerations in mind, there are a number of approaches 
to the DOS time question. The most obvious approach, used by the vast 
majority of computer users, is to either ignore the computer clock entirely 
or to say "It's close enough". Regardless of the application, I strongly 
recommend that the DOS clock be set to the approximate time if only to 
assure that files are more or less correctly date stamped. If the accuracy 
of DOS time is important, the computer clock may be set or synchronized 
in a number of ways, some of which are described below. In this context, 
"ACCURACY" means the accuracy of the time setting operation and NOT the 
longer term accuracy of the DOS time.

     1.   TELEPHONE: Many local telephone companies offer a telephone time 
          service, usually with a message such as "When you hear the signal 
          the time will be ... (beep)". I am not aware of any commercial 
          equipment which uses this signal for time setting purposes.

          ACCURACY: Generally plus or minus 5 seconds. With the advent of 
          digital voice response equipment, the accuracy has improved in 
          recent years to perhaps plus or minus 1 second.

     2.   COMMERCIAL RADIO: Use commercial radio hourly time signals to 
          manually set the time. (My experience suggests that the CBS time 
          signal is normally quite reliable.)

          ACCURACY: Usually within plus or minus 2 seconds, depending upon 
          the source.

     3.   SHORTWAVE RADIO: Time signals are broadcast on shortwave radio
          stations WWV and WWVH by the National Institute of Standards and 
          Technology. These time signals may be used to manually set the 
          time. WWV and WWVH broadcast on several frequencies: 2.5MHz, 
          5MHz, 10MHz, 15MHz, and 20 MHz (WWV only). Reception will vary 
          according to your distance from the transmitter, time of day, and 
          atmospheric conditions. These time signals are very precise; the 
          only major variable is the propagation delay, the time it takes 
          the radio signal to travel from the transmitter to your receiver. 
          The typical propagation delay is approximately 5 microseconds per 
          mile. Outside North America, other national radio services such 
          as the British Broadcasting Company's BBC World Service offer 
          accurate hourly shortwave time signals.

          ACCURACY: Time setting using WWV or WWVH can usually be performed 
          to within about plus or minus 250 milliseconds, of which up to 25 
          milliseconds is transmission time and the balance is user 
          response time. With practice, plus or minus about 100 
          milliseconds is practical.

     4.   NIST/USNO TELEPHONE TIME SERVICE: When real precision and 
          accuracy are required, the computer clock may be set remotely 
          using the telephone time service of either the National Institute 
          of Standards and Technology (NIST, formerly the National Bureau 

Program JPLCLOCK Multimission Control Center Clock                 Page 44


          of Standards or NBS) in Boulder, Colorado or Hilo, Hawaii, or the 
          U.S. Naval Observatory (USNO) in Washington, D.C. This method 
          requires a modem connected to a telephone line and is available 
          for systems using DOS version 3.3 or higher AND equipped with 
          80286 processor or higher; some 8088-equipped systems may also 
          use this method depending upon the type of clock hardware 
          installed and the version of DOS being used. The recommended 
          method uses the program TIMESET (see below) although other 
          similar commercial and shareware programs are available.

          ACCURACY: This is the most accurate method available for setting 
          the DOS clocks. Depending upon which service is used, NIST or 
          USNO, and whether or not line delay compensation ("lag") is 
          employed, the DOS time can be set to within plus or minus 2 
          milliseconds. However, since the "time ticks" of the DOS software 
          clock occur every 55 milliseconds, or 18.2 times per second, this 
          "granularity" effectively limits the accuracy of reading the DOS 
          clocks. See the documentation for program TIMESET for additional 
          discussion.

     5.   HEATH GC-1000 MOST ACCURATE CLOCK: The GC-1000 is a combination 
          digital clock and scanning shortwave radio receiver which may be 
          equipped with an RS-232 communications port for use with 
          computers and other electronic equipment. This is the only method 
          which provides more or less continuous accurate time information. 
          RECOMMENDED!

          ACCURACY: When properly configured for your location, equipped 
          with an external antenna, used with appropriate computer 
          software, and when the receiver is locked to one of the WWV (or 
          WWVH) time signals, the GC-1000 can provide time information and 
          a standard calibration frequency to an accuracy of plus or minus 
          10 milliseconds. When signal lock is lost, the receiver scans the 
          5MHz, 10MHZ, and 15MHz broadcasts to reacquire signal and lock. 
          Even after signal lock is lost, the receiver maintains an 
          accuracy of plus or minus 100 milliseconds for some hours.

     Choose one of the methods suggested or a suitable alternative based 
upon your precision and accuracy requirements. Other methods of maintaining 
an accurate time standard, such an atomic clocks and NIST time code 
equipment, are available -- for a price. Those methods are beyond the scope 
of program JPLCLOCK and this documentation.


Maintaining DOS Time
--------------------

     Just in case you missed the point earlier, accurately setting DOS time 
is only half the battle. Even if the DOS time is set very precisely as 
discussed above, all that assures is that the time is correct to the 
required accuracy at that instant. The problem then becomes one of knowing 
how the DOS clocks change or drift with time and how to compensate for 
those changes or, alternatively, checking the DOS time frequently enough 
that any drift on the part of the DOS clocks is acceptable for the intended 
application.

Program JPLCLOCK Multimission Control Center Clock                 Page 45


     Of the two clocks in a typical personal computer, the hardware clock 
is considerably more consistent and reliable. I have checked perhaps a 
dozen PC hardware clocks in recent years, and almost all kept reasonably 
good time over a period of several days; as expected, none kept "perfect" 
time. Typical drift rates ranged from about 3 seconds per day to near zero 
seconds per day, with the magnitude and direction of the drift more or less 
constant over the period of measurement. Once a hardware clock has been 
calibrated, therefore, the drift can be calculated with reasonable accuracy 
over periods of some weeks or more; for these results, the computer must 
always be left on and the ambient temperature held constant. Crystal aging 
rates suggest that calibration should be performed at least annually.
     The hardware clock is normally interrogated only when the computer is 
first started or rebooted. The correct time can therefore only be predicted 
at that moment for a calibrated hardware clock and given the last time that 
clock was synchronized with an appropriate time standard. Microsoft 
provides no standard software tools for interrogating the hardware clock at 
other times. Quite the contrary; beginning with DOS Version 3.3, using the 
DOS TIME and DATE commands to set the DOS software clock will also set the 
hardware clock and effectively destroy its usefulness as a calibrated time 
reference. I am at a complete loss to understand the reasoning behind this 
change in DOS; I presume that users were being "confused" by differences 
between the hardware and software clocks; instead of either explaining or 
fixing the problem, Microsoft elected to "legislate" the problem away -- a 
process any politician would recognize instantly. The only mitigating 
consideration is that any really effective solution would probably require 
hardware as well as software changes. Blame IBM, I guess.
     The software clock provides the only time information accessible to 
DOS using standard software. Since this clock is maintained entirely in 
software, with no reference to the hardware clock except at bootup, it is 
at the mercy of other software which may execute from time to time. The 
software clock increments its time using "interrupts", a technique which 
stops a software process in progress just long enough to do the required 
tasks and then resumes the interrupted process. These interrupts occur 
every 55 milliseconds. So long as none is missed, the software clock should 
keep accurate time -- if the software is written correctly and if the 
computer's crystal controlled oscillator is in turn accurate. It may be 
that neither of these conditions is true; certainly the crystal controlled 
oscillator (quite similar to the one which runs the hardware clock) was not 
designed for accuracy or stability. It's original purpose was solely to 
generate the necessary timing signals for the correct operation of the 
computer. Cost, not keeping accurate time, was the primary consideration in 
its design.
     Other software designers have contributed to the problem by writing 
software which, deliberately or inadvertently, prevents the software clock 
from being updated. Off-brand BIOS firmware can present occasional 
problems. Local Area Network (LAN) and high speed communications software 
are typical culprits in this respect. For example, a casual check of the 
clock while using Brooklyn Bridge (a computer-to-computer transfer program) 
indicated that the clock was effectively suspended when data transfers were 
in progress. In one relatively brief period, the DOS clock lost about 30 
seconds.
     As a result of all of these factors, the accuracy of the DOS software 
clock can vary wildly from one computer to the next and from one 
manufacturer to another. One inexpensive "clone" computer that I'd rather 
forget couldn't manage to keep time to better than about 30 seconds per 

Program JPLCLOCK Multimission Control Center Clock                 Page 46


HOUR! Before planning to use a particular computer as a time reference with 
programs like JPLCLOCK, check the computer hardware and software you intend 
to use very carefully.


Calibrating DOS Time
--------------------

     Regardless of the method used, the DOS time must be set from time to 
time in order to maintain even reasonable accuracy. More demanding 
applications will require calibration of the hardware or software clock or 
both. The method and frequency of calibration will depend upon your 
accuracy requirements and cost. For my "normal" work, involving program 
development and word processing, I use NIST station WWV and a digital 
PLL shortwave receiver to manually set my computer clocks on a regular 
basis. From time to time I require higher accuracy; given my location in 
California, I usually use a program like TIMESET to call the NIST Telephone 
Time Service in Boulder, Colorado when precise time setting is required.
     When using a program such as JPLCLOCK where consistent accuracy is 
essential over extended periods of time, calibration of the hardware and 
software clocks may be required. I recommend program TIMESET for this 
purpose. TIMESET is a copyrighted program by Peter Petrakis which is      
distributed using the "shareware" concept. If not available on a      
convenient bulletin board system, TIMESET may be obtained by writing:

          Life Sciences Software
          8925 271st N.W., Suite 112
          P.O. Box 1560
          Stanwood, WA  98292

          (206) 387-9788

          US$35.00/copy (as of April, 1991)

     TIMESET is an elegant and very precise method for setting the hardware 
and software clocks in your computer. Note that TIMESET sets your computer 
based upon Coordinated Universal Time (UTC) rather than UT1; the offset 
between UTC and UT1 is displayed by TIMESET but is not used. TIMESET is 
superior to any of the several other similar programs I have evaluated. You 
must have a modem and a telephone line connected to your system to use 
TIMESET. Note that the process involves making a telephone call to either 
Boulder, CO or Washington, DC and toll or long distance charges may apply! 
For additional information on configuring TIMESET for use with JPLCLOCK, 
see the section TIME SYNCHRONIZATION.
     The current version of TIMESET, Version 6.0, is not without its 
shortcomings. First, if the modem does not make connection to a telephone 
line correctly, TIMESET may hang indefinitely waiting for a response from 
the modem which will never arrive. This is the case with one of my internal 
modems that is convinced that the first call after initialization is at 
2400 baud; since the call to NIST is being made at 1200 baud, the modem is 
definitely "confused". This problem has not been observed when using a 
standard Hayes 2400 modem. Second, TIMESET does not record the statistical 
results of its operations to a disk file. This means that calibration must 
be performed manually; normal time setting, however, operates automatically 
with no problems. Third, TIMESET does not return an "error code" to 

Program JPLCLOCK Multimission Control Center Clock                 Page 47


indicate whether or not synchronization was successfully performed. I hope 
to convince Mr. Petrakis of the need to address these relatively minor 
problems in an otherwise excellent program.
     The method being used for time synchronization and adjustment will 
determine whether or not calibration of your hardware clock is required. If 
you use the Heath GC-1000 Most Accurate Clock, calibration is probably not 
required. Similarly, if you place a program like TIMESET in your 
AUTOEXEC.BAT file and synchronize your DOS clocks every time you start your 
computer, hardware calibration is not required. If, on the other hand, you 
wish to call NIST as infrequently as possible so as to minimize the 
telephone charges, hardware clock calibration is definitely recommended. 
Unless you use the Heath GC-1000 (or some other time standard) and poll it 
regularly, calibration of the software clock is always required.
     The following suggested calibration procedures assume the use of 
program TIMESET and that TIMESET has already been configured for your 
computer and for your time zone. See the TIMESET documentation for 
instructions. If you use some other program, it must provide similar 
information and you must make appropriate changes to these procedures as 
required by the software actually used.


Manual Hardware Clock Calibration
---------------------------------

     Hardware clock calibration requires a minimum of 48 hours to 
accomplish. The computer should be located in the environment in which it 
is expected to operate and should be turned on and off at the "usual" 
times. The idea is to duplicate the actual operating conditions to the 
maximum extent possible, especially temperature. The following procedure is 
suggested:

     1.   Operate the computer in its normal environment and according to 
          its usual schedule for at least 24 hours prior to the test.

     2.   Set the hardware clock using TIMESET according to instructions. 
          Use a screen capture program or manually record the ACTION 
          SUMMARY prepared by TIMESET. The most significant information is 
          shown as:

          Local computer time was:  06:59:41.95
                           Set to:  06:59:44.01 Pacific Daylight
          Local computer date was:  06-19-1991
                           Set to:  06-19-1991, Wednesday

     3.   Operate the computer normally for the next 24 hours. Do NOT use 
          the DOS DATE and TIME commands!

     4.   After approximately 24 hours, reboot the computer and repeat the 
          time setting with TIMESET and record the same information as in 
          Step 2.

     5.   Using the data obtained in Steps 2 and 4, calculate the hardware 
          clock drift in seconds per day.

     6.   Operate the computer normally for the next 24 hours. Do NOT use 

Program JPLCLOCK Multimission Control Center Clock                 Page 48


          the DOS DATE and TIME commands!

     7.   After approximately 48 hours, reboot the computer and repeat the 
          time setting with TIMESET and record the same information as in 
          Step 2.

     8.   Using the data obtained in Steps 4 and 7, again calculate the 
          hardware clock drift in seconds per day. Repeat as required until 
          consistent results are obtained. If consistent results cannot be 
          obtained, the selected computer may not be suitable for your 
          intended use.

NOTE: The current version of JPLCLOCK does not directly use the hardware 
clock drift in its time adjustment calculations. This capability will be 
added in a future version. Instead, JPLCLOCK accepts a "Clock Offset" value 
which represents the total hardware clock drift in seconds between the last 
time synchronization was performed and the most recent time the computer 
was booted. If the computer is always synchronized immediately prior to 
running JPLCLOCK, the hardware calibration is not required and the Clock 
Offset should be set to zero.

Program JPLCLOCK Multimission Control Center Clock                 Page 49


Manual Software Clock Calibration
---------------------------------

     Manual software clock calibration is quite similar to hardware clock 
calibration and is recommended for all installations using JPLCLOCK which 
do not plan to use the automatic synchronization and calibration features 
of the program. The recommended procedure requires 28 hours to accomplish. 
The computer should be located in the environment in which it is expected 
to operate and should be turned on and off at the "usual" times. The idea 
is to duplicate the actual operating conditions to the maximum extent 
possible, especially temperature. The following procedure is suggested:

     1.   Operate the computer in its normal environment and according to 
          its usual schedule for at least 24 hours prior to the test.

     2.   Set the hardware and software clocks using TIMESET according to 
          instructions. Use a screen capture program or manually record the 
          ACTION SUMMARY prepared by TIMESET. The most significant 
          information is shown as:

          Local computer time was:  06:59:41.95
                           Set to:  06:59:44.01 Pacific Daylight
          Local computer date was:  06-19-1991
                           Set to:  06-19-1991, Wednesday

     3.   Operate the computer normally for the next 4 hours. "Normal 
          operation" means using the particular software, JPLCLOCK in this 
          case, that is planned for the computer. Do NOT use the DOS DATE 
          and TIME commands!

     4.   After 4 hours, repeat the time setting with TIMESET and record 
          the same information as in Step 2.

     5.   Using the data obtained in Steps 2 and 4, calculate the software 
          clock drift in seconds per day.

     6.   Operate the computer normally for the next 12 hours. "Normal 
          operation" means using the particular software, JPLCLOCK in this 
          case, that is planned for the computer. Do NOT use the DOS DATE 
          and TIME commands!

     7.   After 12 hours, repeat the time setting with TIMESET and record 
          the same information as in Step 2.

     8.   Using the data obtained in Step 7, again calculate the software 
          clock drift in seconds per day. Repeat as required until 
          consistent results are obtained. If consistent results cannot be 
          obtained, the selected computer may not be suitable for your 
          intended use.

     9.   Now enter the latest synchronization date and time (from Step 7) 
          and calculated drift (from Step 8 or Step 5) in seconds per day 
          into program JPLCLOCK. From the Main Menu, press F10+F1 and enter 
          the data as prompted. Enter zero for Clock Offset.


Program JPLCLOCK Multimission Control Center Clock                 Page 50


     Other time sources may be similarly used to calibrate the DOS clock. 
The final result of this calibration should be a software clock drift in 
seconds per day that should remain reasonably stable for relatively long 
periods of time. The calculated clock drift is POSITIVE if your DOS clock 
GAINS time with respect to the time source and NEGATIVE if your DOS clock 
LOSES time with respect to the time source. These data may then be entered 
into JPLCLOCK so that the program will automatically adjust the displayed 
time for the predicted drift.
     Note that the predicted drift calculations assume that JPLCLOCK is 
operating continuously. If you exit JPLCLOCK and perform operations that 
affect the DOS clock (such as disk accesses or high speed communications), 
the drift calculations will still be accurate but you will have to add a 
clock offset to compensate for the DOS clock changes. If you turn off your 
computer, you must reset your clock (to the desired accuracy) and then 
adjust the last synchronization time to correspond to the time you reset 
your computer clocks. For maximum accuracy, perform a manual time 
synchronization (F10+F3+F1 from the Main Menu) each time you reboot your 
computer; JPLCLOCK will automatically update the last synchronization time.
     Program JPLCLOCK is a "well behaved" program written and compiled 
using Microsoft's QuickBASIC Compiler, Version 4.5. No "clever tricks" are 
used to fool the system into doing something that might interfere with 
accurate timekeeping by the DOS software clock. The software clock drift 
obtained by this suggested procedure should be relatively consistent from 
day to day.

Program JPLCLOCK Multimission Control Center Clock                 Page 51


USING TEXT MODE
---------------

     In addition to its use in the Multimission Computer Control Center, 
JPL is also considering the use of JPLCLOCK as a means of displaying 
the current mission and event times in other locations at the Laboratory, 
and for display to visitors and guests. In order to explain the data, to 
provide additional commentary on missions in progress, and to provide 
other supplementary information, JPL suggested the addition of a TEXT mode 
to further enhance JPLCLOCK.
     Each time JPLCLOCK is started, it searches for a special message file 
named "JPLCLOCK.MSG" in the current drive and directory. If the file is 
found, it reads the file into memory and thereafter permits the TEXT MODE 
to be enabled. This occurs ONLY when the program is started from the DOS 
prompt; if you use the DOS SHELL (Function Key F9 from the Main Menu) to 
copy or create the special message file, JPLCLOCK will NOT recognize the 
file until the program is restarted.
     The TEXT mode has a capacity of up to 10 screen pages of text with 20 
lines per screen page. The normal distribution of the program includes a 
demonstration message file with the name JPLCLOCK.MSG. To enable TEXT mode, 
you must first enable PAGE mode. This may be done when the program is 
started from the DOS prompt:

          JPLCLOCK /TEXT

or by using Function Key F7 to enable TEXT mode from the Main Menu. 
Disabling PAGE mode automatically disables the TEXT mode. TEXT mode cannot 
be enabled if the special message file JPLCLOCK.MSG was not found when the 
program was started OR if the file contains no text.
     When the TEXT mode is enabled, JPLCLOCK first cycles through all 
active Mission Timers (as in the usual PAGE mode), then cycles through all 
available text pages in order. The process then repeats. The sample special 
message file contains five text pages.
     When the TEXT mode is active and JPLCLOCK is cycling through all 
active Mission Timers and text pages, a special "bar meter" is displayed 
at the top left of the Mission Timer Windows. This is a row of ten special 
square symbols, one for each of the ten text pages, which indicates the 
status of the page. Each available text page is denoted by a BLUE symbol; 
the active text page symbol is flashing. Inactive text pages (pages without 
any text) are shown with a GRAY symbol.
     In addition to the prepared text in file JPLCLOCK.MSG, the display 
includes a title line with the program version number, the current Julian 
Date, and the local date in conventional notation. The second line displays 
the current UTC Time, Local Time, and the two "bar meters". The left bar 
meter gives the status of title pages, and the right meter the status of 
the Mission Timer pages. The following is the first screen page in the 
supplied sample file JPLCLOCK.MSG. Special "line drawing" characters 
actually used in the display have been replaced in this text by similar
printing characters.

Program JPLCLOCK Multimission Control Center Clock                 Page 52


| JPLCLOCK by David H. Ransom, Jr.  Version 9129 |  JD2448430.26897 22 JUN 1991
  18:27:19 UTC                      11:27:19 PDT    **********       **********
---------- NASA Jet Propulsion Laboratory -------------------------------------

                              Welcome to JPLCLOCK!
                              --------------------

                                   Written by
                              David H. Ransom, Jr.
                            Rancho Palos Verdes, CA


     JPLCLOCK is a real time clock and mission/event timer program written
especially for the NASA Jet Propulsion Laboratory in Pasadena, California for
use in the Multimission Computer Control Center (MCCC) and elsewhere in the
Laboratory. The MCCC is the "nerve center" where all the NASA planetary
missions such as Magellan, Ulysses, and Galileo are controlled. Other NASA and
European Space Agency missions are also supported by the JPL MCCC either
directly or through NASA's Deep Space Network, three large antenna systems
located in Goldstone, California, near Madrid, Spain and near Canberra,
Australia. The MCCC is in turn supported by the scientists and engineers at JPL
and at the California Institute of Technology, which operates JPL for NASA.


Preparing TEXT Files
--------------------

     The demonstration message file JPLCLOCK.MSG may be used as a template 
to create customized text files. When preparing text files for use with 
JPLCLOCK, use an ASCII editor, or use a word processor program in the "non-
document" or "ASCII" mode. Before editing, make a backup copy of file 
JPLCLOCK.MSG. I recommend that all text files for JPLCLOCK be created with 
the filetype ".MSG". Future versions of JPLCLOCK may include a feature to 
read additional text files and the required filetype will be ".MSG".
     The sample file contains 5 screen pages of text. Each screen page 
consists of exactly 20 lines of text, and a maximum of 10 screen pages (or 
200 text lines) is allowed. After creating a new text file (and having made 
a backup copy of the original JPLCLOCK.MSG file!), copy the new file to 
JPLCLOCK.MSG and start program JPLCLOCK in the TEXT mode to view the 
results. My testing indicates that it takes several attempts before the 
appearance of the screen pages suits my taste.
     The TEXT mode displays text lines exactly as it finds them in file 
JPLCLOCK.MSG. As illustrated in the sample file, the "line drawing" 
characters and other special characters are displayed. (Some editors are 
unable to place these special characters in a text file. I recommend the 
shareware editor QEDIT for editing text files for JPLCLOCK.)

Program JPLCLOCK Multimission Control Center Clock                 Page 53


COMMENTS AND KNOWN PROBLEMS
---------------------------

1.   Computer BIOS Problems

     Not all PC's are created equal. A program like JPLCLOCK may execute 
correctly on one machine and not on another. The most likely culprit in 
these cases is the computer's BIOS (Basic Input Output System) which is 
built into each machine (in ROM, Read Only Memory) by the manufacturer. 
Even computers with the same model number may have a different BIOS, 
depending upon when they were manufactured; different model numbers by the 
same manufacturer may perform differently. Brands which have demonstrated 
problems in this area include Tandy, Leading Edge, and Ergo.

2.   Monitor Type and Video Adapter Cards

     Not all video adapter cards are created equal either. While most CGA 
adapters perform about the same, EGA and VGA adapters can vary 
considerably. The same card, operated in different video modes, can be a 
star or a lemon. There are too many different types of adapters to even 
attempt any generalizations. One practical note: Some VGA monochrome 
monitors "confuse" the VGA BIOS and/or the VGA adapter and require the 
command "MODE CO80" (from the DOS prompt) for proper gray-scale operation 
with JPLCLOCK.

3.   Computer Processor and Math Coprocessor

     JPLCLOCK has been tested primarily on computers equipped with the 
80286 or higher processor and including a math coprocessor chip. There are 
no known problems if the computer does NOT have a math coprocessor chip but 
there may be perceptible delays visible on the screen; obviously, there's 
no solution except a faster computer or the addition of a math coprocessor 
chip. No testing has been performed on 8088-class machines (the original PC 
and XT computers and their clones). Operations involving the CMOS 
clock/calendar chip will usually fail on these machines since their design 
did not include that feature; the various add-on clock chips and circuit 
cards are usually incompatible with the current clock chips. If you have 
such a computer and wish to use program TIMESET, read the TIMESET 
documentation carefully and test the program thoroughly before use with 
JPLCLOCK.

4.   DOS Version and the Shell Feature

          The "Shell to DOS" feature, used by Function Key F9 from the Main 
Menu and when program TIMESET is executed from within JPLCLOCK, is 
generally NOT reliable for versions of DOS prior to 3.1 and the results of 
attempting to use this command with DOS Version 2.x and lower are 
unpredictable. I recommend MS-DOS/PC-DOS Version 3.3 as the best, most 
stable DOS available. The Shell feature may also fail on certain computers 
for no apparent reason, probably related to the BIOS. I have also performed 
limited testing on DOS Version 5.0 without any problems to date. (I'm still 
using a Beta Version of DOS 5.0 and will resume testing as soon as I get 
the Real Thing installed.)


Program JPLCLOCK Multimission Control Center Clock                 Page 54


5.   Unstable Hardware or Software Clocks

     Some clock circuits have been implemented in such a manner that they 
are essentially a simple tuned resistance-capacitance design which 
effectively ignores the presence of a crystal. Such circuits may drift 
wildly as a function of time, temperature and/or voltage, and make the host 
computer unsuitable for an application such as JPLCLOCK. Any decent crystal 
controlled oscillator should be able to hold to within a second per day, 
but not many PC computer clocks are that good. I've been told that tests on 
a typical PC hardware clock several years ago showed a 5% difference in 
clock frequency when operated on AC power versus the lithium battery. I 
would not have believed that big a difference was even possible with a 
crystal oscillator!
     However, what appears to be an unstable DOS clock may, in fact, be the 
fault of certain software. Network and communications software are 
notorious for turning off the interrupt system and doing other bad things 
which prevent the DOS clock from keeping accurate time. This problem 
usually shows up as a significant time loss AFTER network access or high 
speed communications. Avoid the use of these programs when running JPLCLOCK 
and eliminate any TSR (Terminate and Stay Resident) programs which may 
interfere with the clock.
     The fact that there are two clocks in the PC can cause confusion and 
apparent errors. While JPLCLOCK is running, only the DOS clock is 
interrogated and it is this clock that requires the most careful 
calibration for extended operations. However, each time a computer with a 
battery supported clock/calendar is booted, the hardware clock is used to 
initially set the DOS clock. These two clocks have independent drift 
direction and rate; thus, the time may appear to drift in one direction if 
the computer is booted frequently, and in the opposite direction if it is 
left on. Microsoft compounded the problem by "fixing" the DOS TIME command 
in Version 3.3 and up so that it sets both the hardware and software 
clocks, thereby eliminating the hardware clock as any sort of a reliable or 
stable reference!

6.   Typical Calibration Results

     During the testing of JPLCLOCK I have used both 286 and 386 computers 
and have calibrated each of their software clocks using the NIST telephone 
time service. While the drift rates varied from computer to computer, each 
computer was able to maintain the correct time using JPLCLOCK to within 150 
milliseconds after: a) running for a minimum of 4 hours prior to attempting 
calibration; and b) using a calibration time of at least 4 hours. Since the 
DOS clock ticks occur at 55 millisecond intervals, calibration runs of less 
than four hours will yield an uncertainty which is of the same order of 
magnitude as the desired calibration accuracy.
     For applications requiring maximum accuracy, these tests indicate that 
the computer should be set using NIST each time the computer is booted and 
then resynchronized at 4 to 24 hour intervals. The stability of the DOS 
clock will determine the optimum interval. JPLCLOCK records the measured 
drift rate each time it makes a synchronization call; use F3+F3+F1 from the 
Main Menu to view the data and adjust the synchronization interval to the 
longest time which yields consistent results. Another consideration is to 
minimize the number of calls to NIST or USNO; these telephone time services 
are a precious resource and should be used as infrequently as possible 
consistent with the needs of your application (as well as your willingness 

Program JPLCLOCK Multimission Control Center Clock                 Page 55


to pay the toll charges).

7.   Color Variations

     Especially with EGA and VGA adapter cards, displayed colors may vary 
considerably from those described. The most common variation is "dim 
yellow" (used for the version number on JPLCLOCK's title screen) which 
often appears as either brown or a dim red which is all but 
indistinguishable from the "real" dim red. Other colors may also vary from 
system to system and from monitor to monitor.

Program JPLCLOCK Multimission Control Center Clock                 Page 56


FUTURE IMPROVEMENTS AND FEATURES
--------------------------------

     JPLCLOCK is still a very young program and, in addition to repairing 
the inevitable bugs and problems that are bound to be found, I have a 
number of additional features that I hope to add in future releases of the 
program. Here are a few that are being considered:

1.   Add better manual calibration procedures to include a brief tone so 
     that users who don't choose to pay the telephone charges to NIST or 
     USNO can still calibrate their systems reasonably accurately by using 
     radio stations WWV or WWVH. Casual experimentation on my part has 
     indicated that I can hear differences as small as about 100 
     milliseconds without much difficulty. Propagation delay from Fort 
     Collins, Colorado to the Los Angeles area is only about 20 milli-
     seconds so it should be simple to calibrate the clocks to plus or 
     minus 250 milliseconds in a day or so.

2.   Add automatic calibration of the hardware (CMOS) clock comparable to 
     that now provided for the software (DOS) clock. This is a little more 
     complicated since the hardware clock can only be read to the nearest 
     second.

3.   Add automatic synchronization using the Heath GC-1000 Most Accurate 
     Clock. When equipped with an RS-232 interface and external antenna, 
     the GC-1000 can maintain an accuracy of plus or minus about 10 
     milliseconds with WWV or WWVH. With software overhead, this probably 
     translates into about plus or minus 50 milliseconds for the PC, the 
     resolution of the DOS clock ticks.

4.   Give the user the choice of displaying UTC or UT1 (required for 
     navigation, for example) if synchronization is done using the NIST 
     telephone time service or the Heath GC-1000 Clock (which are the only 
     available services which supply the correction from UTC to UT1). The 
     current correction is +0.2 seconds as of July 1, 1991.

5.   For systems equipped with a CMOS clock/calendar chip (286 and higher), 
     add the optional capability to use the hardware clock to adjust the 
     DOS time when leaving JPLCLOCK to do disk operations, etc.

6.   Add automatic correction to/from Daylight Savings Time. This will
     require automatically adjusting the DOS clock by one hour at the 
     appropriate times each April and October. This is a real "must do"!

7.   Improve readability of the times (especially when using the SMALL Main 
     Window) by using an alternate font for EGA and VGA monitors. I'm at 
     the mercy of QuickBASIC and the computer's BIOS for this feature; some 
     systems accept alternate fonts from within a QuickBASIC program and 
     others do not.

Not all of these features may ever be added and others may find their way 
to the top of the list first. Comments and suggestions will be appreciated.

Program JPLCLOCK Multimission Control Center Clock                 Page 57


UTC AND TIME ZONES
------------------

     Coordinated Universal Time (UTC) is the world wide civil standard time 
as broadcast by national radio time services such as stations WWV and WWVH 
of the National Institute of Standards and Technology (formerly the 
National Bureau of Standards) and the BBC World Service. It is roughly the 
same as UT1, the time standard used by astronomers and scientists for 
celestial and solar system measurements. However, because the orbital time 
and rotation rate of the Earth is not constant, periodic adjustments of one 
second are required. These adjustments, called Leap Seconds, are usually 
made at the end of June and/or the end of December in order to maintain the 
difference between UTC and UT1 to within 0.9 seconds. As I discovered while 
writing my program ASTROCLK, there are many other defined time standards. 
Because of the ready availability of UTC for synchronization, JPLCLOCK 
assumes that the computer's internal clock is set to local time and that 
time has a fixed relationship to UTC.
     The original plan for time zones required each zone boundary to be 
located at the 15 degree meridians around the globe. Since that arrangement 
seldom coincided with national or political boundaries, many adjustments 
have been made over the past one hundred years for political reasons or for 
local convenience. Some time zones are approximately "nominal" while others 
are quite large; all of China, for example, uses a single national time 
zone -- at least officially.
     All civil time zones are related to UTC, usually by an integral number 
of hours (although there are several "half hour zones" and at least one 
"quarter hour zone"). Many countries, including the United States and most 
of Europe, also adjust their civil time by one hour during summer months. 
In the United States, Daylight time begins on the first Sunday in April and 
ends on the last Sunday in October. Other countries use different dates and 
those dates may change from time to time. JPLCLOCK can adjust for Daylight 
time for all time zones in the United States (including Alaska and Hawaii) 
with a single function key; other time zones must be individually set for 
standard or summer time.
     The following time zone abbreviations are used by JPLCLOCK for the 
main window and the four location clocks at the lower right of the display 
screen:

    ABBR  OFFSET    ZONE NAME
    ----------------------------------------------------
     UTC       0    Coordinated Universal Time
                    (formerly GMT = Greenwich Mean Time)

     AST      -4    Atlantic Standard Time
     ADT      -3    Atlantic Daylight Time
     EST      -5    Eastern Standard Time
     EDT      -4    Eastern Daylight Time
     CST      -6    Central Standard Time
     CDT      -5    Central Daylight Time
     MST      -7    Mountain Standard Time
     MDT      -6    Mountain Daylight Time
     PST      -8    Pacific Standard Time
     PDT      -7    Pacific Daylight Time
     YST      -9    Yukon Standard Time
     YDT      -8    Yukon Daylight Time

Program JPLCLOCK Multimission Control Center Clock                 Page 58


     HST     -10    Hawaiian Standard Time
     HDT      -9    Hawaiian Daylight Time

     GMT       0    Greenwich Standard Time (UK)
     BST      +1    British Summer Time (UK)
     CET *    +1    Central European Time
     CES *    +2    Central European Summer Time

    AEST *   +10    Australian Eastern Standard Time
    AEST *   +11    Australian Eastern Summer Time
    ACST *    +9.5  Australian Central Standard Time
    ACST *   +10.5  Australian Central Summer Time
    AWST *    +8    Australian Western Standard Time

     * denotes non-standard abbreviation

     Users with specific information on time zone names, abbreviations, and 
and relationship to UTC as well as official times for changing to and from 
daylight/summer time are encouraged to send me that information so that I 
may update or correct the program if necessary. The information will be 
added to subsequent versions of JPLCLOCK.

Program JPLCLOCK Multimission Control Center Clock                 Page 59


JPLCLOCK REVISION HISTORY
-------------------------

      Each released version of JPLCLOCK uses a four digit revision code 
such as 9126. The first two digits indicate the year and the second two 
digits indicate the week of the year. In some cases, an additional letter 
suffix is added to distinguish changes occurring within the same week. A 
partial week at the beginning or end of the year is counted as a full week. 
Using this method, a year will typically have 53 weeks although it is 
possible to have 54 weeks in a leap year (1972 is an example). The current 
year-week revision code is shown on the Julian Date display, Display Mode 
7, in my program ASTROCLK.
     This file records the revision history of program JPLCLOCK through all 
of the minor twists and turns that usually accompany the evolution of such 
a program.  It illustrates the tortuous process of maintaining and refining 
a program as ideas and problems are reported from every quarter. These 
notes may also be helpful to users who are upgrading from one version to 
another to find out what has changed.

                                              David H. Ransom, Jr.


9130      7/22/91
-----------------
-Changed the PAGE HOLD and PAGE SELECTION logic to accommodate fast paced 
events such as a space shuttle launch. When used in the PAGE mode (use the 
"/PAGE" command line option or F8 from the Main Menu), JPLCLOCK now checks 
each time a page change is scheduled for Mission/Event Timer events due to 
occur within 1 hour, selects the page with events closest to Time Zero, 
jumps to that page, and enters the PAGE HOLD mode. HINT: Set the PAGE DELAY 
(F4+F4 on the Main Menu) to 5 seconds for fastest page scanning.
-By popular request from amateur radio and BBS operators who keep their 
computers set to UTC, added DOS CLOCK FLAG to select LOCAL or UTC time for 
the DOS CLOCK. With the flag set to LOCAL, JPLCLOCK assumes the computer is 
set to the correct local time (including Daylight Savings Time); with the 
flag set to UTC, JPLCLOCK assumes the computer is set to the correct UTC 
time. The program then performs all necessary time conversions so that the 
correct times are displayed. Set by F4+F2 from the Main Menu.
-Corrected a minor bug which sometimes displayed Time Zero (0  00:00:00) 
with a RED background instead of a GREEN background. This was caused by a 
rounding problem with the double precision Julian Date.
-Corrected a minor bug around midnight that might cause the incorrect date 
to be displayed for a few seconds as a function of the calculated Clock 
Offset and Total Drift adjustments.

9129      7/15/91
-----------------
-Added Manual Synchronization using audio tones (F10+F5) to permit 
synchronization using WWV or WWVH. Accuracy of 100 to 150 milliseconds can 
be obtained with practice.
-Added abbreviations for Australian time zones (with an added "A" prefix 
letter). The abbreviations are the same for STANDARD and for SUMMER time; 
SUMMER time is denoted by an asterisk after the abbreviation. See text for 
details.
-Corrected bug in HOLD logic (if an event is within 60 minutes ot T-0) that 

Program JPLCLOCK Multimission Control Center Clock                 Page 60


caused HOLD to not take effect under certain circumstances.
-Modified Mission/Event Timer windows to not "blink" if all event data is 
the same from one page to another (that is, when the same event is 
programmed for multiple timers).
-Modified ALT-F9 so that it both enables the experimental EGA screen font 
and toggles between "large" and "normal" size numbers in the time displays.
-Added description for MTD files.
-Various cosmetic changes to the program. Corrections, changes, and 
numerous typographical errors corrected in this text.

9128      7/05/91
-----------------
-Repaired bug that caused CALIBRATION (F6) to fail to execute subsequent 
TIMESET calls at the correct time interval after the first two. Also 
corrected a sign error in the drift calculation during self-calibration.
-Corrected screen text for CALIBRATION (F6) to show correct calibration 
intervals of 1, 2, and 4 hours. The total time required is 7 hours.

9127      7/01/91
-----------------
-Added "/SMALL" command line option to display smaller Main Window with 
Local Time and UTC Time. See text for details.
-Added ALT-F6 during clock display to switch between LARGE and SMALL Main 
Window.
-Added four additional SELECTED and PRIORITY EVENT windows below the SMALL 
Main Window. User may select: four SELECTED EVENTS (default); two SELECTED 
EVENTS and two PRIORITY EVENTS; or, four PRIORITY EVENTS. Change using ALT-
F5 when SMALL Main Window is active. These additional four windows are 
displayed ONLY when the SMALL Main Window is selected ("/SMALL" command 
line option or ALT-F6 when clock display is active). 
-Added "/SYNC" command line option to force immediate time synchronization 
(using program TIMESET) when JPLCLOCK is started. The time synchronization 
performed as a result of the "/SYNC" command line option is independent of 
the automatic time synchronization (F10+F3+F3).
-Changed "/TEXT" command line option so "/PAGE" is no longer also required. 
"/TEXT" now forces PAGE mode.
-The word "HOLD" now appears above the Mission Timer windows if the current 
page of Mission Timers is being held on the screen because one or more of 
the timers is within 1 hour of its Time Zero.
-Changed SCREEN FREEZE (ALT-F1) to time out in 5 minutes if no key is 
pressed. Current UTC and Local time are now displayed and updated on line 2 
during the screen freeze. JPLCLOCK will no longer freeze indefinitely!
-Changed Location Clock prompts for "Uses US Daylight Time" (F2) to "Y" for 
YES and "N" for NO.
-Corrected bug in Mission Timers: countdown time at zero days displayed "0" 
days rather than "-0" days.
-Corrected a bug introduced at Version 9126: INI files were interpreted 
incorrectly and reset the Daylight Flag on the Location Clocks which use US 
Daylight Savings Time.
-In most instances, pressing BACKSPACE will reset the timer in the message 
"JPLCLOCK will start automatically in NN seconds". When typing characters, 
the BACKSPACE will delete the previous character.
-Modified large clock logic in the Main Window to write only digits that 
have changed. This improves performance with slower computers and/or slow 
video adapter cards.

Program JPLCLOCK Multimission Control Center Clock                 Page 61


-Improved prompts for Read/Write INI & MTD files (F5) and corrected a minor 
bug when ESC was pressed to CANCEL. Added warning that disk operations may 
affect JPLCLOCK's time accuracy.
-Added warning when exiting to DOS (F9) that disk operations may affect 
JPLCLOCK's time accuracy.
-Fixed "?" command line help so correct time is shown and added "/TEXT" 
command line reminder.
-Corrected references to the DOS timer rate. The timer ticks occur 18.2 
times per second or every 54.945 milliseconds. Previous text had the 
frequency given where period was indicated.
-Various cosmetic changes.

9126      6/22/91
-----------------
NOTE: Program JPLCLOCK and this documentation were prepared largely from 
memory some hundreds of miles away from my usual references and other 
resources. Technical revisions and corrections can be expected in future 
releases! Comments and suggestions are welcome.
-INITIAL PUBLIC RELEASE OF JPLCLOCK.
-Added F10 to Main Menu for manual and automatic time synchronization and 
calibration functions. See the section TIME SYNCHRONIZATION for details.
-Added automatic offset and drift compensation to JPLCLOCK displayed time 
based upon measured time offset and drift rate. Once the average drift rate 
of the computer's clock is known, JPLCLOCK will compensate for that drift 
and display the corrected time.
-Added TEXT mode for the display of up to 10 screen pages of supplementary 
information or messages. A sample text file, JPLCLOCK.MSG, has been added 
to the standard distribution files. See text for details.
-Added "bar meter" above the Main Window to provide countdown to automatic 
time synchronization. Meter appears 100 seconds before JPLCLOCK suspends 
and counts down in increments of 10 seconds.
-Added two "bar meters" above the Mission Timer windows to display active 
Mission Timer pages and active TEXT pages. The right meter is for Mission 
Timer pages and the left for TEXT pages. Active page markers are in color 
and inactive page markers are gray.
-Added "#nn" copy format to Mission Timer input (F3).
-Added TAB to skip an entry and leave it unchanged in several menus.
-Added F7 to switch TEXT mode from Main Menu.
-Added F8 to switch PAGE mode from Main Menu.
-Added ALT-F1 to FREEZE clock display. Press any key to resume operation.
-Added ALT-F7 to switch TEXT mode from clock display. NOTE: PAGE mode must 
first be enabled before TEXT mode can be enabled.
-Added ALT-F8 to switch PAGE mode from clock display. NOTE: TEXT mode will 
be disabled (if enabled) when PAGE mode is disabled.
-Added F4 on the DEFAULTS menu (F4+F4 from Main Menu) to allow the user to 
set the PAGE Delay and the TEXT Delay. See text for details.
-Swapped Location Windows #2 and #3 to make numbering scheme conform to the 
other windows, top to bottom in a given column.
-INI file format has changed but JPLCLOCK will correctly read Version 9125B 
INI files and subsequently write the new format. Use F5 from the Main Menu 
to convert prior files; first read the old file then write a new file using 
the same or a new filename.
-The menu message "JPLCLOCK will start automatically in NN seconds" now 
counts down as the allowed time for keyboard input decreases.
-Various cosmetic changes and minor bug repairs.

Program JPLCLOCK Multimission Control Center Clock                 Page 62


-Documentation updated. 

9125B     6/16/91
-----------------
-Added /PAGE command line option for page mode operation.
-Number of timers now set to 60 in 10 pages.
-Mission Timer capacity changed to allow from -9,999 days to +99,999 days 
to accommodate long duration interplanetary missions such as Voyager 1 and 
2 and Pioneer 11 as they leave the solar system.
-Corrected Daylight Savings Time adjustment and default values for the four 
location clocks.
-Added Voyager 1 and 2 to default data but times and dates are only 
approximate.
-Function keys on several menus changed or swapped.
-Many minor and cosmetic changes.
-Documentation updated.

9125A     6/14/91
-----------------
-Interim test release.
-Documentation not updated.

9125      6/12/91
-----------------
-First fully functional release.
-All configuration features now available.
-Preliminary documentation released.
-Mission Elapsed Time for Magellan, Galileo, and Ulysses are NOT correct. 
Dummy values have been used for testing.

9124      6/10/91 
-----------------
-Initial BETA VERSION Release. This version was an operational 
demonstration of the program and did not include any configuration 
features.