OPERATION AND INSTALLATION OF
                                       LCPANEL
                     A CONTROL PROGRAM FOR THE LOGICAL CONNECTION
                              PERIPHERAL SHARING SYSTEM

                (Logical Connection is a registered trademark of Fifth
                                 Generation Systems)


             LCPANEL is offered as is, with no warranty as to fitness or
                   purpose.  Any user assumes all risk for its use.


             ********************** LICENSE ****************************

             LCPANEL is copyright (C) 1988,1989,1991 by A. J. McPhate Jr.

          All persons or organizations, other than employees of Fifth
          Generation Systems or Fifth Generation Systems itself, are
          granted a license to use LCPANEL in any manner they wish, so
          long as they understand that this software is offered
          without any warranty whatsoever, that no consideration or
          fee may be charged for this software, and this software may
          not be distributed in conjunction with any product for which
          a fee is charged.

          Employees of Fifth Generation Systems and computers owned by
          Fifth Generations Systems may not use this product at all.
          They may provide it at no charge to customers who request
          it, but it cannot be distributed with the Logical Connection
          product.

          Operators of electronic bulletin board systems are encouraged to
          post LCPANEL for downloading by their users, subject to the above
          conditions.

          *****************************************************************

          DESCRIPTION
          =================================================================
          Now that that's out of the way, we can get down to business.  If
          you have used the Logical Connection peripheral sharing system,
          you know that it is generally a good system.  However, one of its
          weak links is its control software.  LCPANEL is a replacement for
          POPLC, the program that comes with the Logical Connection.
          (POPLC is also a registered trademark of Fifth Generation
          Systems).

          If you want a quick rundown of the shortcomings of POPLC and what
          LCPANEL does to solve them, here it is:

          POPLC is FAT: it occupies 20192 bytes of precious ram when
          loaded.  LCPANEL only takes up 5648 bytes;

          POPLC is RUDE: if you forget where you are and pop-up POPLC while
          in graphics mode, you will have your RAM scrambled.  LCPANEL will
          not pop-up in graphics mode;

          POPLC has a limited vocabulary: you can only store four control
          sequences of 44 characters in POPLC.  LCPANEL lets you store up
          to ten control sequences of up to 60 characters each.  You can
          even give each user his or her own special control sequences;

          POPLC requires more keystrokes: it forces you to send one control
          string per pop-up session.  LCPANEL lets you send multiple
          control strings in a single pop-up session;

          POPLC is dirty: its screen contains a bunch of garbage you don't
          need to see, like eight peripherals when you only have two.
          LCPANEL will limit the number of devices to whatever you say.  If
          you only have two, then two is what you will see;

          POPLC has limited hot-keys: LCPANEL will let you assign any
          keycode and scan mask as the hot-key;

          POPLC won't let you use all your ports: if you want to send data
          out your parallel port thru a parallel/serial converter to a
          serial port on the Logical Connection, POPLC assumes you goofed
          up and won't let you.  LCPANEL lets you use any port to talk to
          any port.  After all, we know we only get two COM ports, but we
          get three LPT ports.  How many of you have three parallel devices
          on your PC?


          INSTALLATION
          ===============================================================
          LCPANEL is installed similar to the way POPLC is installed.  The
          CONFIG.LC file must reside in the same subdirectory as LCPANEL,
          as does the new user command file, COMMANDS.LC.  The command line
          parameters are not case sensitive and may be entered in any
          order.  The quick summary of usage is:

          lcpanel pc=aaad lc=a [kc=ddd sm=dd od=d]

          The parameters are described in detail below.  The first two
          parameters are REQUIRED!  The remaining parameters are optional,
          but I recommend you specify od, as it sure makes things look
          cleaner.

          In detail, the parameters are:

          pc=aaad

          which represents the port on the PC used to communicate with the
          Logical Connection.  The 'aaa' is 'lpt' or 'com' and 'd' is '1',
          '2', or '3', as the case may be.  There is no default.

          lc=d

          where 'd' is the port number on the Logical Connection that the
          PC is plugged into, 0 thru 7.  There is no default.

          kc=ddd

          representing the hot-key that pop-ups LCPANEL. The 'ddd' is a key
          scancode in decimal.  ALL THREE DIGITS MUST BE USED! (so 99 is 099)
          The default is 038, for L.  The scan codes are:

          001    esc  011   0    021   y    031   s    041   `
          002    1    012   -    022   u    032   d    042   lshft
          003    2    013   =    023   i    033   f    043   \
          004    3    014   bs   024   o    034   g    044   z
          005    4    015   tab  025   p    035   h    045   x
          006    5    016   q    026   [    036   j    046   c
          007    6    017   w    027   ]    037   k    047   v
          008    7    018   e    028   cr   038   l    048   b
          009    8    019   r    029   ctl  037   ;    049   n
          010    9    020   t    030   a    040   '    050   m

          051   ,     061   f3   071  home  081  pgdn  091
          052   .     062   f4   072  up    082  ins   092
          053   /     063   f5   073  pgup  083  del   093
          054 rshft   064   f6   074  g-    084        094
          055  g*     065   f7   075  left  085        095
          056  alt    066   f8   076  g5    086        096
          057  spc    067   f9   077  right 087        097
          058  caps   068   f10  078  g+    088        098
          059  f1     069  numlk 079  end   089        099
          060  f2     070  scrlk 080  down  090        100

          sm=dd

          representing the shift key status of the hot-key.  The 'dd' is a
          shift mask representing the status of modifier keys such as alt,
          ctrl, or both.

          The shift mask is equal to the sum of each keys value:

          right shift    1
          left shift     2
          ctrl           4
          alt            8

          so for a hot key of ctrl-alt-L, you would set kc=038 and sm=12
          (24 = 4 + 8).  The default hot-key is Alt L.

          od=d

          which represents the number of output devices you have on the
          system.  If you want to switch between the first three devices,
          set od=3.  Default is 8.

          USER COMMANDS
          ===============================================================
          LCPANEL does not use the control sequences imbedded in the
          CONFIG.LC file.  This lets the user configure different commands
          or add commands without reconfiguring the Logical Connection.
          Control sequences for user commands are stored in a file called
          COMMANDS.LC located in the same directory as LCPANEL.COM and
          CONFIG.LC.  It contains up to ten lines of up to 80 characters
          each.  The first twenty characters of each line are that
          command's name and the remaining 60 characters are the command
          string itself.  Escape sequences and other unprintable characters
          are represented by \ddd where the ddd is the decimal value of the
          character.  Escape is \027.  An example file is included for your
          use and study.  You must use a straight text processor that does
          not expand or compress tabs when building this file.

          USING LCPANEL
          =================================================================
          LCPANEL is very intuitive and easy to use.  You can probably
          figure out LCPANEL just by looking at it and playing with it, but
          for those of you who want to know what to expect:

          Del     immediately clears the buffer.
          ?       puts the configuration data in the message window.
          Space   scrolls the output device window.
          Esc     exits without doing anything.
          Enter   exits and executes whatever you have indicated you want
                  done.
          F1-F10  toggle a user command.

          You may have more than one command toggled when you exit.  They
          will be sent in sequence.  They will be sent *after* the device is
          switched, if you have indicated a new device, so you can switch
          devices and configure them all at one session.  Commands toggle off
          as well as on.  The window at the bottom of the pop-up reports any
          errors that might occur with the communications.

          VERSION HISTORY
          =================================================================
          1.00- Original shareware release.
          1.01- Increased intra-message time delay for better performance
                with plotters.
          2.00- Fixed a bug in the time delay technique and removed redundant
                bidirectional switch string that was causing problems with
                plotters. Corrected a bug with the command file parser that
                made it incompatible with some editors.  Removed port
                configuration data from the screen and allowed it to be
                accessed via the "?" key. Corrected errors in documentation.
          2.10- Fixed a bug with the CGA compatibility.  Now works on CGA
                systems.  Changed default hot key to same as POPLC, Alt L.
                Fixed documentation errors about shift masks.
          2.20- Restored the redundant bidirectional switch string to maintain
                compatibility with old version of POPLC.
          2.40- Removed the section of code that tests for port 0 of the
                configuration file, allowing users to set the lc=0 value.
                Removed the requirement for licensing and license fee.
                The final version of LCPANEL.