TIDRV   -  The Timer-System for realtime-applications
                   on PC/XT/AT's

                   Version 1.1


        (c) Dec 27 1991, K.Kuhn
                         Bahnhofstrasse 17
                         CH-8752 Schwanden

                         CompuServe: #100016,1112




        This is shareware. If you want use this software in
        a professional way, you can get a registered version.
        See last page for more information about this.



        HISTORY:

            Version 1.0, Startrelease Dec 27th, 91

            Version 1.1, Jan 5th, 92

                    - added "unload"-feature to remove
                      TIDRV from memory
                    - BUG FIX: TIDRV-ISR was not interruptable
                               by other HW-IRQ's. Corrected.



        1. INTRODUCTION


           TIDRV.EXE is a TSR program, that gives you timing capability
           to your program, if it supports accessing software interrupts.
           The use of TIDRV is demonstrated by TITEST, a little program
           in TP 6.0, which uses some of the available TIDRV-functions to do
           some testing.

           You can program interval-timers (will be fired, when the programmed
           period is run down) or clock-timers (will be fired at the
           programmed time hh:mm). Timers can be programmed as SINGLE SHOOT
           or to reload the timer value automaticly after a timer event
           occured (AUTO RELOAD). Each timer can be disabled at any time.
           Finally, you can program your timer, to do a cold-boot, if the
           specified time has run out (Watch-Dog).

           This description is a very small one, but I think, you don't
           need more information; TIDRV is really simple to use and the
           sample-program TITEST is well documented.

           HAVE FUN!




       2.  BASICS

           The timer system must be accessed througt the Software-Interrupt
           61H. It's the same method as you can use DOS or BIOS functions.
           TITEST.PAS may give you an idea, how to communicate with the
           timer-system. Run TIDRV.EXE to install the timer system and run
           TITEST to see how it works. To uninstall TIDRV run TIDRV again;
           it will remove itself from memory.

           Because more then one user or task may use the timer system at
           a time, each user must fist login. The shareware version supports
           up to 8 Users (=Tasks), which can handle 256 Timers totally. Each
           task does not care about another, so it's not a problem to
           use same timer-numbers on the different tasks.


           BRIEFING

           No of Timers:        256
           No of Users:         8
           Timer-Types:         Tic-interval (55 ms), Sec-interval (1s),
                                Time (hh:mm)
           Timer-Modes:         single shoot, auto reload, watch-dog (new
                                system boot is performed)
           RAM:                 Uses about 13KB of main-memory
           CPU-Time:            Uses less then 5% CPU-Time on a 12 MHz AT
           Requirements:        PC/XT/AT/386/486 industry-standard-computer,
                                tested with DOS 5.0



       3.  INTERFACE TIDRV <-> APPLICATION

           There are 6 functions, which must be invoked by the software-
           interrupt 61h. Parameter are passed by register values, in
           both directions.


           INIT

           out:         ah: 0  {INIT, initializing the whole timer system; }
           return:      none   {      is done anyway at installation-time  }


           LOGIN

           out:         ah: 1 {LOGIN, the timer system will give you a     }
                              {       identification-number, with you must }
                              {       use for further communications with  }
                              {       the timer system.                    }
                        al: Number of desired Timers
           return:      al: UserID (Identification)
                        cl: set to zero, if no error occured


           LOGOUT

           out:         ah: 2 {LOGOUT, releasing all your timers, but only }
                              {        yours. Timers used by another task  }
                              {        which is related to another UserID  }
                              {        are not affected.                   }
                        al: UserID
           retrun:      none



           SETTIMER

           out:         ah: 3 {SETTIMER, programming a timer of your choice, }
                              {          you have to give a timer-number in  }
                              {          Reg. DX                             }
                        al: UserID (you got it when you logged in)
                        bh: timertyp
                             0 : interval-timer, 1 Tic = 1 s
                             1 : interval-timer, 1 Tic = 55 ms
                             2 : clock-timer
                        bl: timermode
                             0 : single-shoot
                             1 : auto-reload
                             2 : watch-dog (does a cold boot, if running out)
                             0ffh: disable the timer
                        cx:  # of Tics, if timertyp 0 or 1
                             ch = hh,   if timertyp set to 2
                             cl = mm,   if timertyp set to 2
                        dx:  timernumber (0..65535)
           return:      cl:  set to 0, if operation successful



           ASKTIMER

           out:         ah: 4 {ASKTIMER, polling this functions informs    }
                              {          you immediately, if a timer-event }
                              {          is waiting                        }
                        al: UserID (you got it when you logged in)
           return:      al: 0 -> no timerevents waiting
                            1 -> timerevent, timernumber in DX
                            2 -> timerevent overrun, timernumber in DX
                        bh: timertyp (what you programmed before)
                        bl: timermode (what you programmed before)
                        cx:  Timervalue (what you programmed before)
                        dx:  Timernumber (you programmed it before)
           return:      none



           CLRALL

           out:         ah: 5 {CLRALL, all your timers will be cleared,   }
                              {        but not given away to other users. }
                              {        To release timers completely you   }
                              {        must use the LOGOUT function.      }
                        al: UserID (you got it when you logged in)
           return:      none





       4.  REGISTRATION


           For registration and automatic update, send sFr 30.- /$20 to me.
           Registration is valid for all further Versions of TIDRV. The
           registered Version allows you to change some parameters (No of
           Users, No of Timers, ...etc) to customize TIDRV.


                K.Kuhn
                Bahnhofstrasse 17
                CH-8762 Schwanden

           (Sorry, no cards)