Program MAK2LINE

               Make 2-Line Elements using Keplerian Elements







                  (C) Copyright 1992, All Rights Reserved

                          by David H. Ransom, Jr.
                          Rancho Palos Verdes, CA





                               Version  9208
                             February 16, 1992





                            BBS: (310) 541-7299

MAK2LINE Program Documentation                                    Page 1



INTRODUCTION
------------

     This program provides a means to individuals without modems to receive 
the so-called "Keplerian Orbital Elements" and reliably prepare "2-Line 
Orbital Elements" as required by satellite tracking programs such as my own 
STSORBIT and STSORBIT PLUS as well as Paul Traufler's excellent TRAKSAT and 
other similar programs. However, more information is included in the 2-line 
orbital element set than is usually included in the Keplerian orbital 
elements; this means that the "missing" information must either be obtained 
from other sources or be set to a specified value or zero. These 
instructions and the example and sample form which follows will help the 
unskilled user to do these tasks.
     The current version of MAK2LINE is always available on my RPV 
ASTRONOMY BBS at (310) 541-7299 in Rancho Palos Verdes, CA near Los 
Angeles. It is a very busy system, so please be patient (especially during 
Space Shuttle missions).
     Program MAK2LINE is copyrighted software. Use it if you like it, 
discard it if you don't. There are no warranties of any kind. Program 
registration is not required; however, if you use and enjoy Program 
MAK2LINE, a donation of US$10.00 will be much appreciated and will encourage 
me to continue supporting the amateur radio and satellite tracking 
communities with software big and small. A donation of US$10.00 will also 
bring you the latest version of the program on disk. Please specify disk 
size, 5-1/4" 360K or 3-1/2" 720K.


                                        David H. Ransom, Jr.
                                        7130 Avenida Altisima
                                        Rancho Palos Verdes, CA  90274

MAK2LINE Program Documentation                                    Page 2



PROGRAM NOTES
-------------

     Program MAK2LINE has but a single purpose: to prepare 2-line orbital 
elements from Keplerian orbital elements by means of user keyboard input. 
Since the program is designed only to transcribe valid data from one format 
to another, no error checking is performed and the program makes no tests 
of the "reasonableness" of the various data and parameters. The user is 
therefore cautioned to check his data before using this program, or to use 
the resulting data with caution until it has been verified.
     The information shown below is usually included in the Keplerian 
orbital elements as received via modem or via voice (amateur radio or 
telephone). This sample is an actual file from Space Shuttle Flight STS-42 
in January of 1992 and received via modem direct from the NASA Johnson 
Space Center:

     Satellite: STS-42
     Catalog number: 21846
     Epoch time:      92024.87908918        (24 JAN 92   21:05:53.31 UTC)
     Element set:     JSC-005
     Inclination:       56.9720 deg
     RA of node:       233.8707 deg          Space Shuttle Flight STS-42
     Eccentricity:     .0009197                SGP4 Keplerian Elements
     Arg of perigee:   264.4174 deg         from NASA flight Day 3 vector
     Mean anomaly:      95.5875 deg
     Mean motion:   15.91353638 rev/day               G. L. Carman
     Decay rate:    2.10000e-03 rev/day^2      NASA Johnson Space Center
     Epoch rev:              37

     If you compare the information requested by Program MAK2LINE (as shown 
on the example on the following page) with that above, several items are 
missing or may be in a slightly different format. Here are some 
suggestions. 

1.   A sample form is included in this documentation which will assist you 
     when receiving Keplerian orbital information by voice line or when it 
     is transmitted by amateur radio link. Note that the form includes 
     lines for "IAU Designation" and "BSTAR Drag"; these items are 
     frequently omitted from voice transmissions.

2.   The NORAD Number is assigned by the U. S. Space Command at Cheyenne 
     Mountain after a satellite has been successfully launched. Initial or 
     pre-launch Keplerian elements may use the mission number or some other 
     convenient number for this item. Most tracking programs will accept 
     any number here.

3.   The IAU (International Astronomical Union) Designation is often not 
     assigned until well after a flight is in progress; press ENTER to use 
     all spaces for this item.

4.   For the 2-line orbital element set, the element set number (shown as 
     "JSC-005" in the example above) MUST be numeric. For this example, 
     enter "5" or "005". Most tracking programs will accept any number for 
     this item, up to a maximum of FOUR DIGITS.

MAK2LINE Program Documentation                                    Page 3



5.   The "Epoch Rev/Orbit" is the orbit number at the epoch (the instant 
     when the data is taken). Up to FOUR DIGITS may be entered here but 
     except for the orbit number on displays, this number has no effect on 
     the propagated orbit.

6.   When MAK2LINE asks for "NDOT2 Drag/Decay", the information being 
     requested is the "Decay rate" in the Keplerian elements. It may be 
     entered in the form shown in the example or as a decimal fraction such 
     as ".0021" (which is identical to the "2.10000e-03" in scientific 
     notation as used in the example).

7.   When MAK2LINE asks for "NDDOT6 Drag", press ENTER to insert a value of 
     zero. This should be satisfactory for most tracking programs.

8.   When MAK2LINE asks for "BSTAR", you may press ENTER to insert a value 
     of zero. This will be satisfactory for times very close to the Epoch 
     Time for the elements. However, as time progresses the satellite may 
     lag behind the propagated (projected) ground track if no value is 
     avaialble for BSTAR. It may be satisfactory to use a value from a 
     similar satellite or a prior set of 2-line elements in order to 
     achieve more accurate long term results.

9.   After the last data item has been entered, MAK2LINE will request the 
     filename to which the 2-line orbital data is to be written. Enter the 
     full file name such as "TESTSAT.TXT". The file will be written to the 
     current drive and directory by default. A drive and/or path may 
     optionally be included in the filename entered. Any prior file by the 
     same name will be overwritten.

10.  If you make a mistake during the data entry process, you may use the 
     BACKSPACE key until ENTER has been pressed. If you wish to cancel the 
     program without writing the data to a file, press CTRL-C.

     Finally, a word about the NDOT2 and BSTAR parameters. Both the U. S. 
Space Command (formerly NORAD) and Johnson Space Center have been known to 
"tweak" these values for a variety of reasons. Usually it is because the 
orbit is in a state of change due, perhaps, to maneuvers or excessive drag. 
A positive value for BSTAR, which indicates positive acceleration and is 
somewhat unusual (and often also an indication of "tweaking"), is NOT 
handled correctly by MAK2LINE at this point and must be manually edited. If 
this proves troublesome, it will be corrected in a future release of the 
program.

MAK2LINE Program Documentation                                    Page 4



PROGRAM MAK2LINE EXAMPLE
------------------------

Enter 2-LINE ELEMENTS

Enter the required data as prompted. Most essential data is
so-called Keplerian Orbital Data available to amateur radio
enthusiasts. Other data may be inserted if available or may
be omitted if not. Accuracy may be affected, see documentation.

Enter Satellite Name (15 chars max):      sts-42
Enter NORAD Number (NNNNN):               21846
Enter IAU Designation (8 chars max):      92  2  A
Enter Epoch Time (YYDDD.TTTTTTTT):        92024.87908918
Enter Element Set Number (NNN):           5
Enter Inclination (DDD.DDDD):             56.972
Enter RA of Ascend Node (DDD.DDDD):       233.8707
Enter Eccentricity (.NNNNNNN):            .0009197
Enter Arg of Perigee (DDD.DDDD):          264.4174
Enter Mean Anomaly (DDD.DDDD):            95.5875
Enter Mean Motion (NN.NNNNNNNN):          15.91353638
Enter Epoch Rev/Orbit (NNN):              37
Enter NDOT2 Drag/Decay (.NNNNNNNN):       .0021
Enter NDDOT6 Drag (NNNNN-N):
Enter BSTAR (NNNNN-N):                    61700-3

Satellite Name (15 chars max):            Sts-42
NORAD Number (NNNNN):                     21846
IAU Designation (8 chars max):            92  2  A
Epoch Time (YYDDD.TTTTTTTT):              92024.87908918
Element Set Number (NNN):                  5
Inclination (DDD.DDDD):                    56.9720
RA of Ascend Node (DDD.DDDD):             233.8707
Eccentricity (.NNNNNNN):                  .0009197
Arg of Perigee (DDD.DDDD):                264.4174
Mean Anomaly (DDD.DDDD):                   95.5875
Mean Motion (NN.NNNNNNNN):                 15.91353638
Epoch Rev/Orbit (NNN):                     37
NDOT2 Drag/Decay (.NNNNNNNN):             .00210000
NDDOT6 Drag (NNNNN-N):                    00000-0
BSTAR (NNNNN-N):                          61700-3

Sts-42
1 21846U 92  2  A 92024.87908918  .00210000  00000-0  61700-3 0    59
2 21846  56.9720 233.8707 0009197 264.4174  95.5875 15.91353638   379

MAK2LINE Program Documentation                                    Page 5



RECEIVED KEPLERIAN ORBITAL DATA
-------------------------------

     This form is provided as a convenience to users receiving Keplerian 
orbital data via voice link (amateur radio or telephone). Each set of 
underline characters indicates an expected character; the decimal point is 
shown where expected (if appropriate for the item). Make multiple copies of 
this form prior to a mission.


Satellite:          __ __ __ __ __ __ __ __ __ __ __ __ __ __ __


Catalog Number:     __ __ __ __ __


IAU Designation:    __ __ __ __ __ __ __ __
     

Epoch Time:         __ __ __ __ __ . __ __ __ __ __ __ __ __


Element Set:        __ __ __ __


Inclination:        __ __ __ . __ __ __ __


RA of Node:         __ __ __ . __ __ __ __


Eccentricity:       . __ __ __ __ __ __ __


Arg of Perigee:     __ __ __ . __ __ __ __


Mean Anomaly:       __ __ __ . __ __ __ __


Mean Motion:        __ __ . __ __ __ __ __ __ __ __


Decay Rate:         . __ __ __ __ __ __ __ __


BSTAR Drag:         __ __ __ __ __ - __


Epoch Rev:          __ __ __ __

MAK2LINE Program Documentation                                    Page 6



MAK2LINE REVISION HISTORY
-------------------------

     Each released version of MAK2LINE uses a four digit revision code such 
as 9208. The first two digits indicate the year and the second two digits 
indicate the week of the year. In some cases, an additional letter suffix 
is added to distinguish changes occuring within the same week. A partial 
week at the beginning or end of the year is counted as a full week. Using      
this method, a year will typically have 53 weeks although it is possible to 
have 54 weeks in a leap year (1972 is an example). The current year-week 
revision code is shown on the Julian Date display, Display Mode 7, using my 
program ASTROCLK.
     This section records the revision history of program MAK2LINE through 
all of the minor twists and turns that usually accompany the evolution of 
such a program. It illustrates the tortuous process of maintaining and 
refining a program as ideas and problems are reported from every quarter. 
It may also be helpful to users who are upgrading from one version to 
another to find out what has changed. This section may also describe recent 
changes not included in the main documentation.


Version 9208  02/16/92
----------------------
-Initial public release of the program.
-User comments and suggestions are welcome.