***OPTHEAT.DOC***
                       Jerry P. Davis - 1/88

Input Data Description:
  --Boiler outlet temp: at boiler stop valve inlet.
  --Boiler outlet press:         "
  --Boiler steam flow:           "
  --Blowdown flow: as decimal fraction of boiler steam flow.
  --Blr/turb delta P: pressure drop from boiler stop to turbine throttle.
  --Turb eff: ratio of actual enthalpy drop to isentropic enthalpy drop.
  --Alt/gearbox eff: ratio of gross terminal power to gearbox input power.
  --Condenser pressure: condenser pressure in inches mercury absolute.
  --Net makeup flow: as decimal fraction of boiler steam flow.
  --Dea/fwh pressures and gland steam exhaust flows: exhaust flows as
    decimal fractions of boiler steam flow.

Assumptions:
  --Thermal heat losses assumed equal to pump enthalpy inputs from condenser
    out to boiler in. No heat losses assumed from boiler out to turbine out.
  --Slight temp drops from isenthalpic throttling/line losses are ignored.
  --Turbine extraction pressures assumed 7.5% higher than dea/fwh pressures.
    Approach delta T is from saturated steam temp to feedwater outlet
    temp for each fwh. Superheat, if present, allows outlet pinch point to
    be slightly higher than approach delta T. At inlet, pinch point is
    assumed equal to approach delta T. Drain coolers are assumed for all
    feedwater heaters (not dea). #1 drain cooler cascaded to #2 if present.
    All approach delta T's assumed to be 10 F.
  --Gland steam exhausts may be directed to any fwh/dea in any specified
    amount. Enthalpies all taken as equal to turbine inlet steam value.
  --Boiler blowdown flashed. Steam to dea, liq to fwh #4 if present.
  --Turbine expansion based on overall turbine efficiency and constant for
    entire expansion i.e. interstage reheat included in efficiency value.

Note:
  --Steam/water properties derived from equations shown in program code and
    will result in errors of 1-2 percent. Accuracy deteriorates significantly
    above about 1200 psia and 1000 F.
  --Several variables in program are redundant to permit future development
    of more complex cycles.

If reheat is desired, it is assumed that the full steam flow just after #2
fwh extraction is resuperheated to the original turbine inlet temperature.
Steam is returned to the turbine at a pressure 10% lower than the pressure"
it was exhausted at (which is about 2.5% lower than #2 fwh pressure).

Optimization of feedwater heater pressures is accomplished by "brute force"
variation of fwh pressures in 10% increments until heat rate has been
minimized.  Since boiler outlet steam flow is being held constant, it is
entirely possible that power output will be lower at optimuum than some
other fwh pressures.  It is the HEAT RATE which is being minimized by the
optimization.  After optimization is completed, answer (n)o when queried if
you wish to optimize. (If your machine is not equipped with a math
coprocessor - be prepared for a long wait during optimization).

DATA screens are simple ASCII files.  The important character is the
colon (:).  The program reads in the numeric value immediately following
a colon into a numeric array.  You may therefore edit the included "HB.SCR"
file to change the default values, or make new files with different defaults
for each one.  However, the fundamental definitions and sequence of the
variables must stay the same to be consistent with the program itself.

If you desperately need help or guidance with this program, contact
Jerry Davis at 617-622-1020.