USER'S MANUAL
         
         
                    ******************************************
         
                    PARTFULL 1.1 - Gravity Flow in Round Pipes
                                        
                    ******************************************
         
                   Solves capacity of sloped drains and sewers
                   that are part full. Computes flow, actual
                   depth, and actual velocity. Also calculates
                   critical velocity and critical depth for hy-
                   draulic jump analysis. User can select either
                   of two types of hydraulic elements; Manning
                   based or those based on observed data. Also,
                   User can choose either of two types of flow
                   formulas; the Manning or Kutter Formulas. Size
                   can be changed from 40 to 5 lines to increase
                   speed. Toggles between English and Metric
                   system with all input and output data convert-
                   ed.
         
                   The functions are extremely complex and no
                   simple solution for a PC has been published
                   before. Accuracy and speed is obtained using
                   interpolation in lookup tables.
         
                   For all kinds of engineers that use round
                   pipes, hydraulic specialists, utility workers,
                   road and site designers, and contractors. The
                   program is written in a familiar spreadsheet
                   format to decrease learning time. Many spread-
                   sheet type commands are incorporated.
         
                   Will run on any IBM compatible with 512 K and
                   either one high density floppy; two low densi-
                   ty floppies; or a hard disk. Includes a con-
                   figuration program for most types of monitors
                   and printers. Display colors can be changed as
                   preferred.
         
                         *******************************
         
                      Copyright, 1991. All rights reserved.
         
             WHEELER GRAPHICS, 75 Stelfox Street, Demarest, NJ 07627
         
                   Voice Mail 201-767-3689 -- FAX 201-767-5620


                                                                         2
         CONTENTS
         
                   SUBJECT                             PAGE
                   
                   Running The Program..................2
                   Introduction.........................2
                   Economic Impact......................3
                   Two Hydraulic Element Methods........4
                   Hydraulic Jump.......................4
                   Comparisons with Other Equations.....5
                   Research Needs.......................5
                   Notes................................5
                   General Description..................6
                   Operating the Program................6
                   Documentation........................9
                   Verifying the Program...............10
                   Registration........................10
                   What Shareware is...................10
                   Disclaimer-Agreement................11
                   Registration........................12
                   Registration Form...................13
                   Technical Support...................14
         
         RUNNING THE PROGRAM
         
         All of the files should be copied on to a hard disk or a floppy. To
         start type:
              
                   RUN   (or)
         
                   RUN PARTFULL
         
         The program operates like a spreadsheet. To change pipe size,
         slope, n-value, starting flow, or flow increment, simply overwrite
         the highlighted value and press enter. For more details, see
         OPERATING THE PROGRAM.
         
         INTRODUCTION
         
         One of the main reasons for writing this program is the complexity
         of the equations and methods. It is almost too tedious to compute
         depth, velocities and the tendency for hydraulic jump in part full
         pipes with gravity flow. This difficulty causes too many engineers
         to skip past these calculations when designing sewers or checking
         existing.
         
         The common practice is to design drains and sewers based on the
         capacity and velocities when flowing full. With this approach the
         investigator doesn't have to be concerned with part full depths and
         velocities, or hydraulic jump. Hydraulic jump cannot occur in a
         full pipe. The reasoning has always been that if the pipe and slope
         is adequate when flowing full, it will be adequate when part full.
         Therefore why bother with hours of complex calculations?


         
                                                                         3
         Actually, a gravity flow pipe almost never flows full. In most
         cases, the pipe must carry whatever flow rate that is put into it
         and this rate is constantly changing. This causes hydraulic levels
         in the pipe to oscillate up and down.
         
         There are many good reasons why it is necessary to know what
         depths, velocities and the tendency for hydraulic jump might be.
         
         For example, it might be desirable to eliminate the possibility of
         hydraulic jump. Hydraulic jump causes turbulence, which in turn,
         causes the release of sewer gases. In 1991 Kienow reported that
         these gases when released can accelerate sewer corrosion. Also,
         odors can be released in residential neighborhoods. Jones describes
         a pumping station design to avoid wet well turbulence and the res-
         ulting odors.
         
         Another reason, is that hydraulic jump can cause unaccounted for
         hydraulic losses. The capacity of an existing sewer cannot be
         accurately determined under these circumstances.
         
         The advantages of knowing levels and velocities should be obvious.
         If the design of a wet well is going to take advantage of unused
         sewer volumes to reduce wet well size then there must be confidence
         in the calculations. Sediment deposition has always been a design
         criteria and minimum sewer velocities should always be calculated
         accurately.
         
         ECONOMIC IMPACT
         
         As a rule of thumb, about two-thirds of the cost of a sewerage
         system is in the design and construction of sewers. As huge amounts
         of money are spent on these systems world-wide, the design should
         be as perfect as modern computation methods allow. Computations
         methods should not be short cut methods but should be as faultless
         as economical methods allow.
         
         Also, a round pipe is probably the most common structure used in
         environmental engineering construction. Still, the methods of
         computing capacity in some areas may be too difficult for practical
         use.
         
         The difference in results can be very large depending on the
         computation methods used. For example, consider a case where a
         sewer is designed to avoid hydraulic jump at all flow conditions.
         If Manning based hydraulic elements are used, then the capacity
         will be some 30 percent less than if observation based elements are
         employed. A 30 percent difference in capacity would be too much for
         many engineers to ignore.
         
         Most are not aware of these and other large differences because of
         the difficulty of making comparisons both ways and for all
         conditions. Sewer design should be based on full knowledge of all
         conditions. A designer should not be required to make assumptions 


         
                                                                         4
         simply because computation methods have not kept pace with
         technology.
         
         TWO HYDRAULIC ELEMENT METHODS
         
         The American Society of Civil Engineers in Manual of Practice No.
         60 describes two methods of computing the hydraulic elements of a
         round pipe. The hydraulic elements are the relation of part full
         depth and velocity in relation to full. These two methods use
         either a constant or a variable n. The terminology may obscure what
         is meant. A variable n means that part full depth and velocity are
         based on observations. Also, a fixed n means that the hydraulic
         elements are based on values derived from the Manning formula. The
         ASCE says that the decision as to what hydraulic elements to be
         used "must be left to the engineer." Saatci recently questioned the
         use of observed values. On the other hand Escritt espouses that the
         use of the "theoretical" values "has been proved a fallacy."
         
         A review of all this information, including Camp's original paper,
         suggests that the actual observations cannot be ignored. The use of
         the Manning based hydraulic elements may have strong roots in
         tradition, but this should not be a basis for sewer design. A
         conservative design approach, might be to run calculations both
         ways and use the most severe results. Still, economy of con-
         struction cannot be disregarded. 
         
         The program allows computation both ways but notes that Manning
         based hydraulic elements might not be accurate.
         
         HYDRAULIC JUMP
         
         The term hydraulic jump usually means that under conditions of free
         flow, the water surface suddenly changes from a low stage to a high
         stage. Turbulence results and is the cause of head loss. Hydraulic
         jump can occur when the velocity exceeds the critical velocity or
         when the depth is less than the critical depth.
         
         There is abundant information available on the occurrence of
         hydraulic jump in rectangular channels, but the literature is less
         than abundant on circular channels. The program computes the
         critical velocity at the actual depth of flow; and the critical
         depth at the actual velocity. These are compared by ratios. The
         term critical flow, means that flow which produces critical depth
         and velocity. If the actual velocity is the same as the critical
         velocity then the flow is critical.
         
         The actual depth of flow and velocity is computed by the hydraulic
         elements which in turn is computed from the flow formula. Thus the
         tendency for hydraulic jump can be influenced by all data input,
         including the flow formula, the n value, the slope and the type
         hydraulic elements. 
         
         


         
                                                                         5
         As both velocity and depth are critical simultaneously, either is
         a measure of the tendency for hydraulic jump. The exact point at
         which hydraulic jump will start cannot always be determined. If
         hydraulic jump is to be avoided then many feel that the critical
         velocity and depth must not be within 10 to 20 percent of the
         actual.
         
         COMPARISONS WITH OTHER EQUATIONS
         
         There is at least one approximate formula and at least one
         nomograph that computes depth directly from the flow and diameter
         and does not take into consideration the other variables. These
         approximate methods check reasonably well for typical values.
         Still, it was found for the same flow and diameter the tendency for
         hydraulic jump changes with slope, type of hydraulic elements, head
         loss formula, and n value. It is not difficult to get results that
         vary 15 percent or more from the true values.
         
         As you run PARTFULL you will see that as input changes, other than
         flow and diameter, the tendency for hydraulic jump also changes.
         Therefore any Equation or graphic solution that does allow input of
         all of the variables will probably not be the most accurate
         solution.
         
         RESEARCH NEEDS
         
         Many will contend that more research is needed in the area of
         hydraulic elements and hydraulic jump for round pipe. It is
         particularly difficult to accept that the hydraulic elements do not
         change from a 4-inch to 12-foot diameter pipe. Still, this is what
         our current data tells us. This research is especially important as
         so much of civilization's infrastructure uses gravity flow round
         pipes.
         
         Yet, the best analytical methods available should be used until our
         data is updated. It is believed that this program uses the most
         current information published. It is also believed that the use of
         this program would be faster and more accurate than other methods
         proposed.
         
         NOTES
         
         This program produces results of far greater accuracy than is
         justified by the hydraulic formulas used. The intent is not to
         introduce computational errors by approximations. It should not be
         inferred that such accuracy is possible.
         
         Part of this program was developed for a discussion on Saatci's
         paper that is expected to be published in the Journal of the ASCE,
         Hydraulics Division in 1992.
         
         William Wheeler, P.E. has a bachelor's and master's degree in Civil
         Engineering, is a Diplomate in the AAEE and a Fellow in the ASCE.


         
                                                                         6
         GENERAL DESCRIPTION
         
         RUN.EXE, RUN.OVL, RUN.SET CONFIG.EXE, and PARTFULL.JWK - These are
         files in object code for compiled, complete standalone program with
         a configuration program. The compiled program does not require the
         use of another program and provides filing, display and printing
         options. Formulas are hidden and no revisions can be made.
         
         OPERATING THE PROGRAM
         
         RUNNING THE PROGRAM - The program is installed for an EGA monitor.
         It will run on CGA, VGA and some monochrome monitors as they are.
         If the program does not run, or does not run well, please run the
         configuration program. This can be done only after unpacking the
         files. To configure type:
         
                   C: (A: or B:)>CONFIG <Enter>
         
         The configuration program will give step by step instructions with
         menus for selecting the printer, the monitor and will let you
         select display colors as you choose. 
         
         To run the program type at a DOS prompt:
         
                   C: (A: or B:)>RUN <Enter>
         
         The program will prompt the User to select the program displayed.
         (Other programs may use the same engines. Also, you may wish to
         save customized versions of the program under a different name.
         Then, you could call up the version needed for a specific applica-
         tion).
         
         OPERATING - As you will see when the program has been loaded, the
         program is in spreadsheet format and produces a table of flows,
         depths and velocities for a given size and slope of pipe. The
         spreadsheet format is probably the most familiar mode among
         technical users and should allow intuitive operation for most.
         
         A five line table is the initial display but the table size can be
         increased to 40 lines, if desired. Operation is extremely simple
         and no menus are needed. Just enter the values you want, overwrit-
         ing the (highlighted) values on the screen, and the program will
         recalculate the entire table. This can be done using only the
         cursor keys and the enter key. Almost no typing is needed.
         
         The program as received will have values already entered. These
         values can be overwritten and the program will recalculate after
         pressing Enter.
         
         The program calculates depths, velocities and critical velocities
         for; both Manning's and Kutter's formula; for both Manning based
         and observation based hydraulic elements; and for both the English
         and Metric systems of units. The table is prepared from flow input,
         

                                                                         7
         and the starting flow on the first line of the table. The next
         value of flow, and subsequent values are spaced by the increment
         selected. Any diameter, n value, and pipe length can be input.
         Length is not necessary except to compute fall. Note that there is
         a "Round-Plcs" number that can be entered or changed. This allows
         any degree of rounding desired but does not always change the
         number of digits displayed. Also note that there is a "Marginal
         Point" that can be changed. This changes the point at which the
         condition changes from "OK-subcr" to "Marginal." When either ratio
         is greater than the marginal point entered, then the work
         "Marginal" will be displayed.
         
         If either the Flow or Flow Increment values are zero, the program
         will use default values to calculate a table. For a 5-line display
         the flows will be spaced 20 percent apart. For the 40-line display,
         they will be 2.5 percent apart. The defaults are automatically
         overridden by entering a value in the blank space. This permits the
         User to customize the flows to any degree desired.
         
         The function key tasks are as follows:
         
              F1 - Changes the table from the Observed values of hydraulic
         elements to the Manning based values. Pressing F1 again toggles the
         display back to Observed values. Generally, the observed values are
         preferred and should be used is design but there are some instances
         where the Manning based values would be used.
         
              F3 - A toggles that changes the table from Manning Formula
         values to Kutter Formula and back again. The Manning Formula has
         gained widespread use because of its simplicity. Many believe that
         the Kutter Formula might be more accurate.
         
              F5 - Changes the table size from five lines to 40 and back to
         five lines again. The five line display will recompute must faster.
         
              F6 - Prints the entire page of the table.
         
              F7 - Leaves the program to a DOS prompt.
         
              F10 - Converts values and units from the English System with
         flows in mgd, then cfs, and then to the Metric System. If the F10
         key is pressed again, units will return to units at the start. All
         of the inputs and the outputs are converted.  This key lets the
         user switch back and forth from the Metric to the English System
         and back to the Metric System. Mixed units can be entered while in
         the second system. For example, if you are working in the Metric
         System but want to enter a 14-inch pipe. First, switch to the
         English System, then enter only 14 inches keeping the other data.
         Now switch back to the Metric and the conversion will be made.
         
              F2 - Allows the editing of a cell if there is text. Where the
         cell value is a computed number, the F2 key will display all of the
         digits the rounding digits entered will allow. Changing the "Round-


         
                                                                         8
         Plcs" number will display more or less digits.
         
              F9 - Recalculates the display. This is only useful if the
         recalculation method is changed by the "/-command" menu.
         
         Note that by pressing the "/" key a menu is displayed. This is a
         "generic spreadsheet" menu than will enable the User to perform
         some filing, formatting and other functions in the same mode as a
         spreadsheet. For example, if you want the program to wake up in the
         Metric system, with Manning based Values, and with certain discrete
         values installed, save the spreadsheet this way using the menu
         commands and overwrite the existing file or write a new one.
         Previously stored files can be recovered by using this menu. No
         changes made this way would affect the packed file. Thus, the
         original file can always be recovered.
         
         The "/-command" menu can be useful for changing the width of
         columns to either display more digits or have more blank space
         between columns. The printing options, such as margins or printing
         codes can also be changed. The program wakes up set for 10-pitch
         printing but this might not suit your needs.
         
         Suppose, as an example, you are studying a particular section of
         sewer and you are publishing this information in a report. It is
         necessary to save the display so that it can be recalled without
         reentering data or changing the formatting. This can be done by
         saving this version of the program using the "/", "F" and "S" keys,
         in order. You will then be asked to insert the new file name, and
         the file will be saved with the data entered. 
         
         The command menu works similar to spreadsheet programs and has many
         other uses. Please see a typical User's Manual on spreadsheets for
         operating details.
         
         If you have several versions of this program stored under different
         names, then typing "RUN" alone will allow you to choose the program
         desired. The "/-F-R"  command can be used instead.
         
         The compiled program has an advantage in that formulas cannot be
         either viewed or changed. This, of course, can be a disadvantage if
         you want to change a formula. There are some unprotected cells on
         the top of the table that can be overwritten if a project or an
         author's name is to be inserted before printing or saving.
         
         By pressing the TAB key several times, the lookup tables will be
         displayed. Lookup table values can be overwritten but this is not
         advised. Also displayed will be the unit names and conversions
         values. These can be changed if desired, but the order of rotation
         is fixed. For example, you might prefer "Feet" to "Ft". Changing
         the conversion constants is also possible except for the primary
         flow value.
         
         The program wakes up with the Global Protection on. This means that
         

                                                                         9
         cells that only the highlighted can be changed. By disabling the
         Global Protection all areas, except those with formulas can be
         overwritten. This could be a useful feature if the program is
         operated by non-English speaking Users or there are special
         terminology requirements.
         
         DOCUMENTATION
         
         METHODOLOGY - Both programs perform interpolations from lookup
         tables for computing depth of flow in the pipe, the velocity and
         the critical velocity. Unit conversion and lookup interpolations
         are made by revising the values in a table by transferring them
         from other tables. The formulas are not changed. 
         
         Logic is written in equations that prevents any flow greater
         than full flow from being used. The hydraulic elements show
         that flow can sometimes be greater than full flow at between
         80 percent and 100 percent of depth. This is considered as an
         unstable condition and has been eliminated for that reason.
         This upper limit that changes pipe depth to full can be
         revised, if desired.
         
         Hydraulic elements are from the American Society of Civil Engineers
         Manual of Practice No. 60, "Gravity Sanitary Sewer Design and
         Construction, 1982, Figure 5-21. From this Figure, Manning based
         hydraulic elements are for n and f constant. Observed hydraulic
         elements are from n and f variable with depth. Equations for this
         data are best solved with lookup tables. Points in the tables are
         spaced 1 percent apart so that straight line interpolation can be
         very accurate. (Accuracy is much greater than is justified by the
         data).
         
         The tendency for hydraulic jump is assumed to be a function of the
         critical velocity and depth. As the actual velocity and depth
         approach the critical velocity and depth, the possible occurrence
         of hydraulic jump increases. Critical velocity and depth is
         calculated using long accepted critical velocity equations, again
         using lookup.
         
         HARDWARE AND SOFTWARE PROBLEMS - The size of the program has been
         optimized for IBM compatible 16-bit computers running at 12 to 16
         Hz and with a coprocessor. Some older computers may run the program
         slowly. It should take about 4 to 8 seconds to recompute the entire
         40-line table with a 16-bit machine and a coprocessor. The
         five-line table should be recalculated in a blink. If your machine
         is much slower, or you don't have a coprocessor, you may want to
         operate only in the five-line mode. This would probably give you
         adequate information. 
         
         The program should run on any IBM compatible computer with 512K
         memory. A coprocessor is not necessary but is recommended. The 
         program will run on machines with only two 360 K floppies and no
         hard disk. You may need another computer to rearrange the files so 


         
                                                                        10
         they will fit in the right order on each floppy. The files RUN.OVL
         and CONFIG.EXE should be installed on the second floppy and all
         others on the first. It would also be helpful if the path was set:
         A:>PATH A:,B: <Enter>.
         
         VERIFYING THE PROGRAM
         
         The methods for solving both hydraulic elements and hydraulic jump
         criteria, are extremely complex. Many equations, graphs and a
         definition sketch are necessary for full understanding. Unfortu-
         nately, the limitations of an ASCII file does not allow this
         information to be presented here. Also, much of this information
         had to be specially developed for this program and is not available
         from other references.
         
         As a result, the computational results of the program will be
         difficult to verify. To assist in this verification and to permit
         full understanding of the program, the following information is
         available: 
         
              - Equations used 
         
              - The references for these equations, or how they were derived
         
              - Other approximate methods used for independent cross
              checking
         
              - Specially developed tables of hydraulic elements, critical
              depth and velocity
         
         It is strongly recommended that before the program is used on real
         world problems, the equations and computational results be
         verified. This is not only needed to ensure that the results are
         accurate but also to confirm that the User knows what is meant by
         the terminology and expressions used.
         
         Detailed information will be sent to assist in verification when
         the program is registered.
         
         REGISTRATION
         
         PARTFULL is shareware. No sales commissions or fees are paid. No
         demo disks are sent because the full program is available on a
         trial basis.
         
         For information on customized versions or site licenses please
         call or FAX.
         
         WHAT SHAREWARE IS
         
         Shareware distribution gives users a chance to try software
         before buying it. If you try a Shareware program and continue
         using it, you are expected to register. 


         
                                                                        11
         Shareware is a distribution method, not a type of software. The
         Shareware system makes fitting your needs easier, because you can
         try before you buy. And because the overhead is low, prices are
         low also. Shareware has the ultimate money-back guarantee -- if
         you don't use the product, you don't pay for it.
         
         DISCLAIMER - AGREEMENT
         
         Users of PARTFULL must accept this disclaimer of warranty:
         "PARTFULL is supplied as is.  The author disclaims all warran-
         ties, expressed or implied, including, without limitation, the
         warranties of merchantability and of fitness for any purpose. The
         author assumes no liability for damages, direct or consequential,
         which may result from the use of PARTFULL."
         
         PARTFULL is a "shareware program" and is provided at no charge
         to the user for evaluation.  Feel free to share it with your
         friends, but please do not give it away altered or as part of
         another system.  The essence of "user-supported" software is to
         provide personal computer users with quality software without
         high prices, and yet to provide incentive for programmers to
         continue to develop new products.  If you find this program
         useful and find that you are using PARTFULL and continue to use
         PARTFULL after a 30 DAY trial period, you must make a registra-
         tion payment of $15. to Wheeler Graphics.  The $15. registration
         fee will license one copy for use on any one computer at any one
         time.  You must treat this software just like a book.  An example
         is that this software may be used by any number of people and may
         be freely moved from one computer location to another, so long as
         there is no possibility of it being used at one location while
         it's being used at another. Just as a book cannot be read by two
         different persons at the same time.
         
         Users of PARTFULL must register and pay for their copies of
         PARTFULL within 30 days of first use or their license is with-
         drawn. Anyone distributing PARTFULL for any kind of remuneration
         must first contact Wheeler Graphics for authorization.
         
         Teachers may distribute PARTFULL but they must not charge for the
         program. The verification data given when the program is regis-
         tered cannot be copied and can only be distributed by Wheeler
         Graphics.
         
         This authorization will be automatically granted to distributors
         recognized by the (ASP) as adhering to its guidelines for
         shareware distributors, and such distributors may begin offering
         PARTFULL immediately (However Wheeler Graphics must still be
         advised so that the distributor can be kept up-to-date with the
         latest version of PARTFULL).
         
         You are encouraged to pass a copy of PARTFULL along to your
         friends for evaluation.  A User's Manual is on disk that can also
         be distributed. Please encourage them to register their copy if 


         
                                                                        12
         they find that they can use it.
         
         REGISTRATION
         
         All registered users will receive the following:
         
                   - A printed description of how the program operates and
                   the methods used for making the calculations.
         
                   - Equations used in the program for hydraulic elements
                   and hydraulic jump. Also the source of these equations
                   or how they were derived. 
         
                   - Graphs and figures essential for the verification and
                   understanding of the program.
         
                   - Selected references
         
                   - Tables for the quick solution of hydraulic elements,
                   critical velocity and depth for those instances where a
                   rapid verification of conditions is necessary, or a
                   computer is not available. Instructions for use of the
                   tables with an example is included.
         
         The registration fee does not include a floppy disk with the
         latest version of the program. If the most recent version is
         desired there is an additional copying and mailing charge of $15.
         If both an additional program disk and a registration is desired,
         the fee is $30. New Jersey residents please add sales tax. Please
         send to:
         
                                 Wheeler Graphics
                      75 Stelfox Street, Demarest, NJ 07627
                        Voice Mail . . . . . 201-767-3689
                        FAX  . . . . . . . . 201-767-5620
         
         Development of new software related to PARTFULL and in the
         environmental field will continue. Your financial support will be
         greatly appreciated. It will put more resources to work and will
         make available more new software sooner.
         
         REGISTRATION FORM
         
         For your convenience a Registration Form/Invoice that can be
         printed or copied, is on the next page:


                                                                        13
         *****************************************************************
         
                          REGISTRATION FORM AND INVOICE
         
         *****************************************************************
         
         
                                       Date:___________________
         
         Mail to:  Wheeler Graphics
                   75 Stelfox Street
                   Demarest, NJ 07627
         
                                       PO # (If Needed)___________________
         
         
         From:____________________________________________________________
         
              ____________________________________________________________
         
              ____________________________________________________________
         
              ____________________________________________________________
         
         
         _____Enclosed is a check for $15. Please register the program and
         send me all of the verification information including equations,
         sources, derivations, graphs, figure, tables, instructions and
         references.
         
         _____Enclosed is a check for $30. Please register the program and
         send me all of the verification information as described above.
         Also send me a copy of the latest version of the program. Please
         send copy on a ________5-inch, or a________3.5-inch size disk.
         
         New Jersey residents please include sales tax. Only checks drawn
         on a US bank in US funds can be honored. Cost of transfer of
         other funds is prohibitively expensive.
         
         Comments are welcome. Are there any changes or additions you
         would like to see incorporated?
         
         ________________________________________________________________
         
         ________________________________________________________________
         
         ________________________________________________________________
         
         ________________________________________________________________
         
         


                                                                        14
         
         TECHNICAL SUPPORT
         
         Free technical support is offered at the above address and
         telephone numbers. Support is offered to all Users whether
         registered or unregistered. 
         
         PRINTING THIS MANUAL - This manual has been written an ASCII
         format and should be read by almost any word processor. Using a
         word processor would give the User control over printing and
         allows formatting. This file also can be printed (without control
         and formatting) by using the DOS commands:
         
                   A:>PRINT USER-MAN.DOC <Enter>