DEFINITIONS OF TERMS USED IN THE PV COMPARE PROGRAM

Useable Watt: a watt which charges the battery or is used by a load
	      connected to the battery or Maximum Power Tracker.
	      Useable watts must be calculated based on the parameters
	      of each particular system, and cannot be determined 
              from the module type alone.

Maximum Power Tracker:
	Aka Maximum Power Point Tracker, MPPT, MPT.  Forces the PV module
	to operate at the knee of the I-V curve, thereby producing maximum
	wattage.

I-V Curve:    Current (I) vs. Voltage (V) curve for a particular PV module,
  	      recorded at a specific temperature and irradiance.  When a
	      PV module is short circuited, it produces maximum current at
	      almost zero voltage.  When a PV module is in an open circuit,
	      it produces maximum voltage and zero current.  The I-V curve
	      describes the voltage and current outputs that occur when
	      loading conditions are between open circuit and short circuit.
	      Note that output current decreases as output voltage rises -
              thus increased voltage drop between the PV module and battery
	      decreases the PV module output current.  

Array:  a group of PV modules in series and/or parallel combination.

Module: a group of PV cells in series and/or parallel combination, usually
	in a sealed, pre-wired unit.

Cell:   an individual photovoltaic cell
	      	  
Irradiance:   Solar radiation (sunlight) received.  Usually specified in
	      watts per meter squared.  1000 watts per meter squared is
	      essentially equivalent to unobscured sunlight at noon.

Voltage drop: 
	Voltage that can be measured across the component in question,
	such as the wire connecting the PV array and battery.  Wiring 
	voltage drop multiplied by the current flowing = power
	dissipated ("wasted") as heat.  However, in a battery
	charging application, these watts would not have been produced
	if the wiring resistance did not exist.  Therefore, voltage drop 
	is not a direct measure of watts gained or lost by using a particular
	wire gauge.  Note that the PV array voltage operating point is 
	forced higher by any voltage drops between the array and battery.
	I-V curve data must be used to determine which wire gauge will
	be most cost effective for a particular system.
	      
Cmf:    Circular mil foot: in this program, a conductor one thousandth 
	of an inch in diameter, one foot long.

AWG:    American Wire Gauge