WeatherFAX  V3.0
		   Weather Facsimile for IBM and
		   Compatible Personal Computers



			   USER'S GUIDE







					Third edition
					February 1991

					Copyright 1990 Jerry Dahl

					6404 Lakerest Court
					Raleigh, NC 27612














	 TABLE OF CONTENTS
	 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


GENERAL INFORMATION ............................ 3

    Changes in Version 3.0

    Introduction

    Purpose and Goals

    License information

    The Software

    The Author


SUPPORTED CONFIGURATIONS ....................... 5

    Hardware

    Software


INSTALLATION INSTRUCTIONS ...................... 6

    Installing the WeatherFAX card

    CONFIG.SYS Modifications

    AUTOEXEC.BAT Modifications

    Copying the diskette

    Starting the Program


GETTING STARTED ................................ 8

    Getting help information

    Testing the card

    Selecting your printer type and display mode

    Connecting your computer to your fax receiver






USING WeatherFAX ............................... 11

    Adjusting the page alignment

    Getting the image

    Viewing the image

    Printing the image

    Saving the image to disk


ADDITIONAL INFORMATION ......................... 20

    Calibrating the card

    Using Expanded Memory (LIM 4.0)

    Using Super VGA (800 X 600 Pixel) mode

    Sources for weather facsimile pictures

    WeatherFAX program specifications


IF YOU HAVE DIFFICULTY ......................... 25


ADAPTER/SOFTWARE AVAILABILITY .................. 27


TRADEMARKS USED IN THIS GUIDE .................. 27





GENERAL INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  CHANGES IN VERSION 3.0

	 This version (V 3.0) of FAX.EXE contains many improvements
	 over the original (V 2.0) and is a direct result of user
	 feedback. My goal is to make this the best weather-facsimile
	 package for professional users -- regardless of cost.
	 I believe that this goal has been accomplished largely with
	 this version.

	 The new features in Version 3 are:

	 VERY HIGH RESOLUTION GRAPHICS. New graphics drivers are
	 added for 1024 x 768 x 256 color resolution and lower.
	 This resolution is essential for viewing large Polar and
	 GOESTAP images.

	 Graphics cards that use Tseng ET3000/4000 and ATI chip
	 sets are supported. These cards include Orchid ProDesigner,
	 Genoa Super VGA, Boca Research SVGA, Sigma VGA/H, STB
	 VGA Extra, Everex Viewpoint VRAM and the ATI VGAWonder+.
	 The Everex Viewpoint VRAM card has been fully tested at
	 1280 x 1024 x 16 color resolution.

	 Here is a list of the new graphics drivers and the chip
	 sets supported:

	 1024  x  768 x 256 colors   (Tseng 4000)
	  800  x  600 x 256 colors   (Tseng 3000/4000, ATI)
	  640  x  480 x 256 colors   (Tseng 3000/4000, ATI)
	 1280  x 1024 x 16 colors    (Tseng 4000)
	 1024  x  768 x 16 colors    (Tseng 3000/4000, ATI)

	 Drivers for Paradise and Video 7 chip sets are also included
	 on an experimental basis. They have not been tested by
	 the author.

	 MORE ENHANCEMENT OPTIONS:

	 All 20 NOAA/NESDIS image-enhancement curves are included
	 as an aid in analyzing infrared images. Also included
	 are Log-Black and Log-White curves for analyzing
	 visible-light images. You can shift and scale the curves
	 to better fit the curve to the image.

	 PALETTE SPAN--Interpolation allows you to set a few
	 color palette levels and have the software fill in the
	 in-between values.




	 SKIP LINES--This option reduces the size of HF Fax and
	 GOESTAP images. Skipped lines are not lost, but are
	 averaged with saved lines.

	 AUTOMATIC FILE SAVE--Images are continually saved to
	 disk using a time stamp as the file name.

	 SCHEDULE-TIMER FOR UNATTENDED OPERATION--Specify the
	 starting time and duration to automatically capture
	 images. This is needed for capture polar-orbiting
	 satellites that do not transmit start and stop tones.
	 You can specify the times from either a pull-down menu
	 or as a command-line option.

	 GOESTAP MODE--Allows you to capture GOESTAP images.

	 USER-SPECIFIED SPM--Specify any scan-per-minute value
	 and capture images using nonstandard SPM rates. You can
	 now capture the Meteor-satellite images at 20 SPM and
	 wire photos on C-band that use nonstandard rates.

	 MIRROR IMAGE--Reverse right-to-left wire photos that are
	 sent as mirrored images.

	 BETTER PRINTER/FILE SUPPORT--You can now print and save
	 images when they are reduced using the 50-percent Zoom
	 feature. This allows you to print more of the image area
	 and reduce the image file size.

	 OTHER MISCELLANEOUS CHANGES:

	 -  The 256-color modes have finer scrolling steps that allow
	    you to more-accurately align the image on the display.
	    This is useful for saving the images and using other
	    software to "loop" the saved images.

	 -  RTTY support is removed.

	 -  The command line /Hxx parameter that specifies the
	    800 x 600 x 16 color mode is no longer needed and
	    should not be used if your card uses either the Tseng
	    or ATI chip set.

	 -  24-hour time is used in lieu of 12-hour AM/PM time.

	 -  The screen is cleared as each new image is acquired.





  INTRODUCTION

	 These instructions explain how to install and use the
	 WeatherFAX weather scan converter and software. You may
	 print this guide with your printer by typing the
	 following command from the DOS command line:

	 COPY FAXGUID3.DOC LPT1

	 This scan converter and software is used with your IBM or
	 compatible personal computer. With the proper receiving
	 equipment and antenna, your computer will be able to
	 capture, enhance, save and print--not just black and white--
	 but gray-scale weather-facsimile images received on the HF,
	 VHF and UHF bands. Users of this Automatic Picture
	 Transmission (APT) imagery include military and commercial
	 meteorologists, ships at sea, scientific observers,
	 educators, and amateurs.

	 This package was described in a two-part feature article in
	 QST magazine. See "A Weather-Facsimile Package for the
	 IBM PC," April and May 1990.

	 The WeatherFAX software reads and writes GIF and TIFF
	 format image files and displays them in CGA, EGA, MCGA,
	 VGA and SVGA graphics modes. Resolutions up to
	 1024 x 768 x 256 colors and 1280 x 1024 x 16 colors are
	 supported. You can enhance the imagery and adjust the
	 color palettes. You can also print up to 16 gray shades
	 on 9- and 24-pin dot matrix and laser printers. When
	 used with the WeatherFAX scan converter, the program
	 allows capture of all APT modes: HF fax, GOESTAP, polar
	 and GOES satellites. The image size is limited only by
	 the available memory in your computer: Up to 32 Mb of
	 EMS memory is supported. Additional enhancements are
	 being developed that will offer even higher-resolution
	 graphics, more operating modes and enhancement options.






	 The system features include:

	  o Direct weather-satellite imagery, including: geo-
	    stationary earth-orbiting satellites (GOES APT/WEFAX,
	    METEOSAT), polar-orbiting satellites (NOAA 9/10 APT
	    IR/Vis, Soviet Meteor), HF-FM NAFAX, and similar APT
	    formats.

	  o Expanded memory support. You can capture images with
	    a wide variety of resolutions. The size of the
	    captured image is limited only by the amount of RAM
	    in your computer. To view images larger than your
	    monitor can display at one time, you can scroll up,
	    down, left, and right.

	  o Incoming pictures can be saved directly to disk.
	    Either the Tag Image File Format (TIFF) or Graphical
	    Interchange Format (GIF) can be selected to allow the
	    images to be used with other graphics-based software.

	  o Print images with 16-level gray scale on a wide
	    variety of printers including 9- and 24-pin dot-
	    matrix printers and laser printers.

	  o Very high resolution. All standard graphics cards are
	    supported including CGA, MCGA, EGA, VGA, and
	    Super VGA(800 x 600) mode. Also for Tseng and ATI
	    chip sets resolutions up to 1280 x 1024 are
	    supported.

	  o Histograms, enhancement, zoom, scroll, gray scale,
	    256,000+ colors, interpolation, reverse, real-time
	    acquisition/display. NOAA/NESDIS and logarithmic curves.

	  o Automatic gain-lock circuitry. The optimum gain
	    value for WEFAX-signal reception is statistically
	    calculated. This provides better and more consistent
	    pictures than either automatic gain control (AGC) or
	    fixed-gain circuits.

	  o No need for external test equipment to verify, test and
	    calibrate the card. The software and special
	    circuitry on the board allow the computer to automate
	    the testing and calibration.

	  o Unattended operation. Image capture can be fully or
	    partially automatic, including APT start tone detect,
	    sync, image save to disk, APT stop-tone detect and
	    cycle repeat.





  LICENSE INFORMATION

	 Your right to use WeatherFAX

	 This software is copyrighted in order to control its
	 orderly development. However, you have the right to
	 use the program for private, noncommercial purposes
	 without further permission. That is, you can copy it,
	 use it, and share it so long as you do not charge any
	 money for it other than the cost of the disk or other
	 transfer medium, not to exceed $2.

  THE SOFTWARE

	 The development of the program began in early 1986, and has
	 gone through several revisions. New versions will be
	 released as features are added and corrections are made
	 to previously released versions. Ideas for future
	 enhancement include:
	    - Higher resolution graphics drivers
	    - Direct AVHRR temperature calibration for polar and
	      GOESTAP images.
	    - Looping of images for animation
	    - Gridding for polar satellite images
	 I am also considering modifying the software to support
	 a very high resolution VAS (Visable and Infrared Spin Scan
	 Radiometer/Atmospheric Sounder) digital scan converter
	 for Modes AAA and GVAR format images from GOES satellites.
	 This system would feature a very high resolution visible channel
	 and 20 IR channels from the Atmospheric Sounder instrument on board
	 the spacecraft.

	 Please let me know what new features are needed for this
	 program to suit your needs.






  THE AUTHOR

	 The author can be contacted by mail at the following
	 address:

		     Jerry Dahl
		     6404 Lakerest Court
		     Raleigh, NC 27612

	 For a mail reply, please enclose a self-addressed,
	 self-stamped envelope.

	 Credit must also be given to the many users who have
	 made suggestions for improving the program. Most of
	 their suggestions have been incorporated into this
	 version of WeatherFAX software.





SUPPORTED CONFIGURATIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  MACHINE REQUIREMENTS

	 WeatherFAX supports most IBM compatible computer systems
	 from the least to the most powerful.

	 The ideal system for a professional user would have a
	 minimum of a 80386 processor and 4 MB of RAM.	The graphics
	 card would contain at least 1MB of RAM using the Tseng 4000
	 chipset.  A math co-processor is not required.

	 A typical system would have a 80286 or better processor,
	 640 KB of conventional memory and a SVGA graphics card.

	 A low end system would have an 8088 processor, 512 KB
	 of conventional memory and CGA or better graphics.

	 o WeatherFAX Card

	 o IBM PC or compatible computer that uses the standard
	   PC-bus architecture.

	 o RAM (Random Access Memory):

	   - 512 kbytes or more of memory:

	     In most configurations, approximately 190 kbytes of
	     memory is required for DOS, drivers loaded by
	     CONFIG.SYS and the WeatherFAX program. All of the
	     remaining memory is available for image storage.

	   - Expanded Memory (optional)

	     LIM 4.0 expanded memory allows up to 32 Mbytes for
	     image storage. Requires both expanded memory and a
	     LIM 4.0 software driver.

	 o A graphics monitor and video adapter card including

	   - Color/Graphics Adapter (CGA)

	   - Enhanced Graphics Adapter (EGA)

	   - Multi-Color Graphics Array (MCGA).

	   - Video Graphics Array (VGA)

	   - Super VGA (up to 1280 x 1024-pixel resolution)

	 o One diskette drive (one of the following):

	   - 5.25-inch drive (360 kbytes)

	   - 3.5-inch drive (720 kbytes).

	 o Fixed disk (optional)

	 o Printer: (optional)

	   Printer types and print resolution - dots per inch
	   (dpi)
	   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	   - All standard 9-pin dot-matrix printers  (120 dpi)

	   - All standard 24-pin dot-matrix printers (180 dpi)

	   - IBM Pageprinter 3812	      (240 dpi)

	   - PCL command compatible (laser) printers (300 dpi)




	 o Receiving equipment and antenna for the frequencies
	   you want to cover.


  PROGRAM REQUIREMENTS

	 To run the WeatherFAX software, you need:

	 o IBM Personal Computer Disk Operating System (DOS)
	     Version 3.0 or later


INSTALLATION INSTRUCTIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  INSTALLING THE WEATHERFAX ADAPTER

	 Refer to the Guide to Operations for your computer for
	 instructions for installing cards. You will need to
	 turn the computer off and remove the cover from the
	 computer to insert the fax card into an unused card
	 socket.

  CONFIG.SYS MODIFICATIONS

	 No changes to CONFIG.SYS are normally needed. However,
	 if you ever get the error message "DRIVE NOT READY" when
	 retrieving very large files (1 Mbyte or larger), the
	 reason may be the assignment of an insufficient number
	 of DOS buffers. Try increasing the number of buffers by
	 adding the statement BUFFERS=64 to the CONFIG.SYS file.

  AUTOEXEC.BAT MODIFICATIONS

	 NOTE FOR USERS HAVING THE ORIGINAL IBM CGA DISPLAY
	 ADAPTER AND SOME VERY EARLY CLONE EGA CARDS (does not
	 apply for most VGA or EGA displays).

	 In those cards, the graphics adapter ROM does not
	 include the entire graphics character set. You will need
	 to load the DOS graphics-character-set driver
	 GRAPHICS.COM into memory. The driver is available on the
	 DOS diskette. Add the statement GRAPHICS.COM to your
	 DOS AUTOEXEC.BAT file to load the driver every time you
	 start your computer. If GRAPHICS.COM is in a
	 subdirectory, supply the necessary path information on
	 the driver statement. For example: C:\DOS\GRAPHICS.COM.

	 When using this program, make sure your AUTOEXEC.BAT
	 file is "clean."  Some terminate-stay-resident (TSR)
	 programs--especially those that control screen functions
	 (such as screen blanking) may interfere with the proper
	 operation of the software. If you experience difficulty
	 when running the fax software, check your AUTOEXEC.BAT
	 file first.




  COPYING THE DISKETTE

	 Copy the WeatherFAX diskette and save the original
	 diskette in a safe place. You can copy the diskette
	 to either a hard disk or to another diskette. Refer
	 to your DOS manual for instructions for copying
	 diskettes. The WeatherFAX program is not copy
	 protected.

  STARTING THE PROGRAM

	 Start the WeatherFAX program by typing FAX.EXE from
	 the DOS command line.

	 Optional Command Line Parameters:
	 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	 ³ Syntax: FAX [options]   where options are:	       ³
	 ³						       ³
	 ³ /C	  Use conventional memory.		       ³
	 ³						       ³
	 ³ /E	  Use Expanded (EMS) memory if installed       ³
	 ³	   (Requires LIM 4.0 driver)		       ³
	 ³						       ³
	 ³ /FG	  Default to GIF file format		       ³
	 ³ /FT	  Default to TIFF file format		       ³
	 ³						       ³
	 ³ /Hxx   BIOS display mode for 800 x 600 x 16 mode    ³
	 ³	 (do not use for ATI or Tseng chip sets)       ³
	 ³						       ³
	 ³ /Thh:mm,dd  Automatic acquire for polar satellites. ³
	 ³	 Go into acquire mode, wait until	       ³
	 ³	 hh:mm (24-hour time), acquire image for       ³
	 ³	 dd minutes, save file then exit to DOS.       ³
	 ³						       ³
	 ³ /Whh:mm,dd  Automatic acquire for GOES satellites.  ³
	 ³	 Go into acquire mode, wait until	       ³
	 ³	 hh:mm, then wait for Start tone,	       ³
	 ³	 acquire until either Stop tone or dd	       ³
	 ³	 minutes after hh:mm, save file, then	       ³
	 ³	 exit to DOS				       ³
	 ³						       ³
	 ³ The /T and /W parameters allow you to write DOS     ³
	 ³ batch files to automatically capture many images    ³
	 ³ at various times during the day.		       ³
	 ³   hh:mm = starting time in 24 hour time	       ³
	 ³   dd    = capture duration in minutes	       ³
	 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	 NOTE: The program will automatically use EMS memory if
	 the available EMS memory size is greater than the
	 conventional memory size.

	 Examples:

	    C:>FAX /H52

	     Enables 800 x 600-pel resolution mode for Oak
	     SVGA graphics card. See the section:
	     Using Super VGA (800 X 600 Pixel) mode.





GETTING STARTED
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  GETTING HELP INFORMATION

	 Help information is available anytime you see F1=Help
	 displayed on the screen. You can access Help by pressing
	 the F1 key. Press the Esc key to quit viewing Help.

  TESTING THE ADAPTER

	 Test the fax adapter by using the Test option on the
	 Main Menu. The various tests will indicate whether
	 the adapter is operating within its correct operating
	 region. If any of the tests indicate that the adapter
	 needs calibration, refer to the section: Calibrating
	 the adapter.

	 Static Test

	   This test is used to check for normal operation and
	   calibration. The nominal parametric values on the
	   adapter are displayed. All of the marks should be in
	   the OK region.

	 Dynamic Test

	   A test signal is applied to the input of each function
	   and the output is checked for correct operation. The
	   Start and Stop Detectors are tested for both ON and
	   OFF states. The FM and AM Detectors are tested to
	   verify linear operation.

	 AM Graph Test

	   A test signal is applied to the AM Detector at various
	   amplitudes and the output linearity is displayed. The
	   graph line should be straight and sloping upward.

	 FM Graph Test

	   A test signal is applied to the FM detector at various
	   frequencies and the output linearity is displayed. The
	   graph line should be straight, sloping upward, and
	   centered between 0 and 256.





  SELECTING YOUR PRINTER TYPE AND DISPLAY MODE

	 Go to the fax menu to specify the Display Mode and
	 Printer type.

	 You can select a compatible printer type from the list
	 of supported printers. Check your printer documentation
	 to determine which of the supported types that it
	 emulates.


			    Printers supported
			   and print resolution
			     (dots per inch)

	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	     ³ Epson compatible 8-pin printers (120 dpi)    ³
	     ³	 - Epson FX, MX, RX, LX series		    ³
	     ³	 - IBM Graphics or Proprinter		    ³
	     ³	 - Okidata 192I+, 193I+, 292, 293	    ³
	     ³	 - Okidata in IBM-compatible mode	    ³
	     ³	 - Panasonic KX-P1080i, P1091i, P1093	    ³
	     ³	 - Cannon PW-1156A			    ³
	     ³	 - Citizen MPS-25			    ³
	     ³	 - Star Micronics: Gemini 10X		    ³
	     ³						    ³
	     ³ Okidata compatible 8-pin printers (120 dpi)  ³
	     ³	 - Okidata 192, 193			    ³
	     ³						    ³
	     ³ Apple ImageWriter II (160 dpi)		    ³
	     ³						    ³
	     ³ Epson  24-pin compatible printers (180 dpi)  ³
	     ³	 - Epson LQ series			    ³
	     ³	 - IBM Proprinter X24 and XL24		    ³
	     ³						    ³
	     ³ Toshiba 24-pin compatible printers (180 dpi) ³
	     ³	 - Toshiba P321, P341, P351		    ³
	     ³						    ³
	     ³ IBM Pageprinter 3812		  (240 dpi) ³
	     ³						    ³
	     ³ PCL command compatible printers	  (300 dpi) ³
	     ³	 - HP LaserJet series II		    ³
	     ³	 - HP DeskJet				    ³
	     ³	 - Apple LaserWriter II 		    ³
	     ³	 - IBM LaserPrinter			    ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ




	 NOTE:

	 If you are using a printer attached to the serial port
	 (COM1), you need to set up the serial port using the
	 DOS MODE command before starting the WeatherFAX program.
	 These commands could be placed in your AUTOEXEC.BAT
	 file.

	   1) Set the baud rate and other parameters with the DOS
	   MODE command. (e.g., MODE COM1:96,N,8,1,P)

	   2) Redirect LPT1 to COM1 with the DOS MODE command
	   (e.g., MODE LPT1=COM1)

	   3) Start WeatherFAX program and set the Printer
	   Destination in the SETUP MENU to LPT1

	 Serial port printers are usually configured for either
	 7-bit or 8-bit graphics mode. Be sure that the printer
	 is configured for 8-bit mode. Otherwise, the printed
	 sample will have a blank row (space) every 8 lines.


  CONNECTING YOUR COMPUTER TO YOUR FAX RECEIVER

	 Use a two-wire cable to attach the fax adapter to
	 your fax receiver. The cable should have a standard
	 3.5-mm phone plug on the end that plugs into the
	 adapter. Plug the cable into either the receiver
	 earphone jack or fax output jack.




USING WEATHERFAX
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


  ADJUSTING THE PAGE ALIGNMENT

	 You will need to set the page alignment the first time
	 you use the adapter. The page alignment synchronizes
	 the timing of the computer with the fax image. The
	 image will appear slanted across the display screen when
	 the page alignment needs to be changed. Once set, the
	 page alignment will not normally need to be changed
	 again.

	 The alignment is set while an image is being received.
	 The procedure is listed below.

	 1) Begin receiving an image into computer memory. Set
	    fax parameters and select the Acquire fax action. The
	    program will automatically capture the next image
	    into the computer storage. After the adapter has
	    started to display an image, go to step 2.

	 2) Use the cursor down (down-arrow) key until the page
	    alignment function is selected. If the image slants
	    to the right, use the cursor left (left-arrow) key to
	    decrease the alignment value. Otherwise, use the
	    cursor right (right-arrow) key to increase the
	    alignment value. Continue adjusting until the image
	    appears perfectly vertical. The alignment value is
	    automatically stored in the program file on disk so
	    that the image is perfectly aligned each time you use
	    the program.





  GETTING THE IMAGE

	 1) SET THE FACSIMILE TYPE.

	 o ADAPTER MODE. The fax card can capture four types
	   of weather facsimile images:

	   - Marine Weather Facsimile. These images are received
	     on HF radio on shortwave radio frequencies (e.g.,
	     8080 kHz). The adapter is set to FM mode.
	     The fax adapter allows the FM Marine fax signal to
	     be within a wide amplitude range. However, if the
	     signal output from your receiver is very strong or
	     very weak, you can compensate by adjusting
	     attenuation pads on the adapter. You can adjust the
	     level while in this pull-down menu by pressing the F4
	     key. Usually, you will keep the attenuation set at
	     NORMAL. This setting allows operation for input-signal
	     amplitudes that vary between -20 dBm to +10 dBm.

	   - WEFAX image. This is the format for geostationary
	     weather satellites. The receiver is usually tuned
	     to S-Band 1691 MHz. The adapter is set to AM mode
	     and Automatic Gain Lock (AGL) is used to automatically
	     set the correct level for any type of image.

	     AGL determines the optimum gain setting at the
	     beginning of every image and fixes the gain level
	     for the duration of the image. This technique
	     provides a distortion free high dynamic range image
	     each time, whether the image capture is started
	     automatically or manually.

	   - Polar image. These are images transmitted from
	     polar-orbiting satellites at VHF (137.xxx MHz). The
	     adapter is set to AM mode and a fixed gain level is
	     used.

	     While this pull-down menu is displayed, you can
	     press the F4 key allows you to set the gain of the
	     fax adapter so that the signal level is just right.
	     Use the cursor keys to increase or decrease the
	     signal level while an image is active so that the
	     level covers a wide dynamic range without exceeding
	     the MAX (clipping) value.

	   - GOESTAP image. This is the format transmitted over
	     phone lines and distributed by a private service on
	     C-Band satellite.



	   2) SETTING THE FAX PARAMETERS

	     You can set the configuration parameters for the selected
	     adapter mode by pressing the F4 key on the Acquire Fax
	     menu. You can set parameters separately for each adapter
	     mode. This allows you to preconfigure the parameters for
	     each mode and quickly switch between modes.

	     TABLE OF PELS-PER-LINE FOR VARIOUS IMAGE TYPES
	     ÚÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÄ¿
	     ³Image Type ³ PELS PER LINE ³ SPM ³ IOC  ³
	     ³		 ³  SKIP LINES	 ³     ³      ³
	     ³		 ³  NO	 ³ YES	 ³     ³      ³
	     ÃÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ´
	     ³ HF Fax	 ³ 1800  ³  900  ³ 120 ³ 576  ³
	     ³ WEFAX	 ³  840  ³  420  ³ 240 ³ 268  ³
	     ³ GOESTAP	 ³ 2048  ³ 1024  ³ 120 ³      ³
	     ³ Polar	 ³ 1800  ³  900  ³ 120 ³ 288  ³
	     ³ Wire Photo³ 2048  ³ 1024  ³  *  ³      ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÄÙ

	     If your computer has a limited amount of RAM, select SKIP
	     LINES = YES and PELS PER BYTE = 2.

	     o SCANS PER MINUTE  (SPM)

	       Selects the number of image lines sampled every minute.
	       Use the same value as that of the signal that you
	       receive. Typically GOES WEFAX satellites are 240 and
	       others are 120. Many wire photos on C-Band use
	       nonstandard rates. This menu also allows you to set a
	       user-defined value that allows you to capture images
	       that use nonstandard rates.

	     o PELS PER SCAN LINE

	       Selects the number of samples (pixels) stored for each
	       image line. You would typically set this value to be at
	       least as large as the resolution of your graphics
	       display mode (e.g., 640 for EGA or VGA). This sets the
	       resolution of the image and affects the amount of
	       computer storage needed to hold the image.

	       The fax program uses all of the available memory in
	       your computer to capture images. The image size in
	       bytes can be calculated by the formula:

	       IMAGE_SIZE = PELS_PER_LINE * NUM_LINES / PELS_PER_BYTE

	       Where:

		PELS_PER_LINE = pixels stored for each image line

		NUM_LINES     = lines in the image

		PELS_PER_BYTE = pels stored per byte, either 1 or 2

	       NOTE: The greater the number of Pels Per Line the
	       greater the image resolution. However, the maximum
	       value may be limited by the speed of your computer. For
	       earlier PCs having a 4.77-MHz clock speed use a maximum
	       value of 700 when using 240 Scans Per Minute.





	       The "squareness" of the displayed image depends upon
	       the Index of Cooperation (IOC) of the received image,
	       the Pels Per Line setting, and the aspect ratio of your
	       display adapter. The relationship for these parameters
	       is:

		PELS_PER_LINE = ã * IOC * ASPECT / SKIP

		Where:

		  ã = Pi = 3.14

		  IOC = Index of Cooperation of received signal

		  GOES (WEFAX) = 268

		  Polar satellites = 288

		  HF fax (Marine) = 576

		ASPECT = horizontal/vertical pixel density set by
		adapter display mode, not the physical size of the
		display. Super VGA, VGA = 1.00 SKIP = 1 if Skip Line
		option is OFF 2 if Skip Line option is ON.

	     o PELS PER BYTE controls the number of gray shades stored
	       for the image. If your computer has limited memory
	       (less then 640 kbytes), consider selecting 2 pels per
	       byte and use the Skip Line option. 2 Pels per byte
	       saves memory by packing two pixels into each memory
	       storage byte, which allows you to capture images twice
	       as large. The image is stored with 16 gray shades and
	       once captured, you cannot enhance the brightness and
	       contrast.

	       If you have expanded memory (LIM 4.0), you should
	       select 1 pel per byte. The image is stored with 256
	       shades of gray, and you can enhance the brightness and
	       contrast of the image at any time.

	     o SKIP LINES

	       This option reduces the size of images by storing every
	       other line. The skipped line is not lost but averaged
	       the previous saved line. This option is very useful for
	       reducing the size of HF FAX and GOESTAP images. A
	       normal GOESTAP image is over 3.2 MB with 2048 pels per
	       line. With the Skip line option you can capture the
	       same GOESTAP image using only 1024 pels per line and
	       use 1/4 the amount of memory.







	   3) SELECT ACQUIRE FAX or SCHEDULE/TIMER ACTION.

	       To acquire images you must have a fax card installed in
	       your computer and your receiver must be attached to the
	       card with a cable. If you use the Schedule/Timer
	       specify 24-hour time for the starting times. The
	       program will automatically capture each image at the
	       specified time. If Automatic File Save is enabled the
	       images will automatically be saved to disk.

	       The program will automatically capture each image from
	       the fax receiver into the computer's memory. If the
	       first image appears slanted, the page alignment needs
	       to be adjusted.

	       The bottom line of the display is the action line. It
	       displays the current receive status and allows you to
	       select various actions while receiving the image.
	       Different actions are displayed using the cursor keys.

	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	     ³ ACTION LINE SELECTIONS				   ³
	     ³							   ³
	     ³ Manual start	    Press <ÄÙ for manual start	   ³
	     ³ Move/scroll image    <- -> keys scroll left/right   ³
	     ³ Darker - 	    <- -> to adjust brightness	   ³
	     ³ Adj contrast	    <- -> to adjust contrast	   ³
	     ³ Printer: on/off	    <ÄÙ   to turn printer on/off   ³
	     ³ Disk   : on/off	    <ÄÙ   to save to disk on/off   ³
	     ³ Page alignment	    <- -> adjust timing.	   ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	       Page alignment allows you to adjust the adapter timing
	       if the image is slanted. Once adjusted, the timing
	       should not need to be changed again. Use cursor keys to
	       increase and decrease the timing value. Increase if the
	       image slants to the left. Decrease if the image slants
	       to the right.



	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	     ³ RECEIVE STATUS			       ³
	     ³					       ³
	     ³ Wait	  : Waiting for start signal   ³
	     ³ Start	  : Start signal detected      ³
	     ³ Sampling   : Putting image into buffer  ³
	     ³ End of mem : Image size exceeds buffer  ³
	     ³ Stop	  : Stop signal detected       ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	   4) EXIT ACQUIRE MODE

	       After image is captured, press the Esc key exit to the
	       Fax Acquire Menu. Press Esc again to exit to the Fax
	       Action Menu. From the Fax Action Menu you can view or
	       print the image.

  VIEWING THE IMAGE

	       You can view an image once it is stored in memory. The
	       image may be either retrieved from disk, or acquired
	       from the fax card. You can then view the image with
	       different display modes, scroll, zoom, and enhance the
	       image details in several ways.

	       When viewing the image, you can either:
	       1) scroll using the cursor keys, or
	       2) enhance the image using the pull-down menus.

	       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	       ³ The active keys used for scrolling are:		³
	       ³							³
	       ³ cursor keys:	 Scrolls the image window up, down,	³
	       ³		 right and left.  A beep is sounded	³
	       ³		 when you reach the edge.		³
	       ³							³
	       ³ Shift Cursor:	 Hold the Shift key and press a cursor	³
	       ³		 key for fast scrolling.		³
	       ³							³
	       ³ Home		 Go to top of image.			³
	       ³							³
	       ³ End		 Go to bottom of image. 		³
	       ³							³
	       ³ F1		 Help (this screen).			³
	       ³							³
	       ³ Esc		 Used for several purposes		³
	       ³		 - return from help screen		³
	       ³		 - abort when writing screen		³
	       ³		 - return to previous screen		³
	       ³							³
	       ³ Alt/F1..F4	Hold the Alt key and press either	³
	       ³		F1, F2, F3 or F4 to select one of the	³
	       ³		user-defined color palette tables.	³
	       ³							³
	       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ



	       If you press the space bar while viewing the image, an
	       action line appears. Use the cursor keys to chose an option,
	       then press the Enter key. The different image enhancement
	       selections are described below. Press the Esc key to return
	       to scroll mode.

	     PALETTE

	       You can change the colors and gray scales of the image
	       by changing the look-up tables (LUT) that define the
	       way the image is displayed. This allows you to emphasize
	       selected areas of the image.  Four tables can be defined.
	       For each table, you can adjust the red, green, and blue
	       colors separately.

	       The histogram displays a bar chart of the distribution
	       of intensity levels in the displayed part of the image.
	       It is used as a visual aid to to help set the palette
	       table.  The horizontal axis is the intensity level from
	       0 to 255.

	       The active keys are:

		 Up/Down cursor    :  selects 1 of the 5 functions
		 Right/Left cursor :  change value
		 Esc		   :  return to previous menu
		 F1		   :  Help (this screen)
		 F9		   :  interpolate colors between the last
				      two colors that have been modified.
		 F10		   :  reset colors to gray levels.

	       Functions:
		 1) Color number  - Indicates the image intensity level.
				    All areas in the image with the same
				    intensity level will momentary flash
				    to help locate areas of interest.
				    Use cursor Right/Left to change.
		 2) Red value	  - Indicates the color's Red component.
				    Use cursor Right/Left keys to change.
		 3) Green value   - Indicates the Green component
		 4) Blue value	  - Indicates the Blue component.
		 5) Table number  - Use Right/Left keys to change palette
				    tables

	     HISTOGRAM

	       The histogram displays a bar chart of the distribution
	       of intensity levels in the displayed part of the image.
	       It is used as a visual aid to to help adjust the brightness
	       and contrast.  The horizontal axis displays the brightness
	       level from 0 to 255. The vertical axis displays the number of
	       pixels for each brightness level.
	       This option is available only if the image was captured with
	       pels per byte = 1.

	       For Brightness, the right cursor key makes the image
	       darker. For Contrast, the right cursor key increases
	       the contrast.  For the 16-color modes (e.g., VGA) the
	       display is redrawn with the new Brightness and Contrast
	       values when you exit the menu using the Esc key.
	       This changes the display Look Up Table (LUT). The actual
	       image data is not changed.

	       The adjustment scale "[   ³   ]" indicates both the
	       contrast range and brightness level. The center mark
	       "³" indicates the brightness level. You can make the
	       image darker by moving the "³" to the right using the
	       right arrow key. The "[ ]" marks indicate the contrast
	       range. The contrast is increased by moving the "[ ]"
	       marks closer together.





	       OVERALL PICTURE ADJUSTMENT

	       1) Use the histogram to locate the right and left edges
		  of the curve where the number of pixels decreases.

	       2) Adjust the brightness so that the "³" mark is
		  centered between the edges on the histogram.

	       3) Adjust the contrast range so that the "[  ]" marks
		  are directly under the right and left edges of the
		  curve respectively.


	     ENHANCEMENT

	       Select one of the image enhancement curves.
	       Both logarithmic and NOAA/NESDIS curves are available.

	       Logarithmic curves include both LOG-White and LOG-Black and
	       are used for enhancement of visible light imagery.  Both
	       curves are defined in the "Weather Satellite Handbook",
	       4th Edition, published by the ARRL.

	       The 20 NOAA/NESDIS curves are primarly used by professional
	       meteorologists and are defined by the NOAA/NESDIS IR Imagery
	       Enhancement Program as described in the 1983
	       GOES User's Guide.  Includes BD, CC, CE, DD, EC, FC, HC,
	       HD, IB, IC, JF, JG, LA, MB, NA, PC, SA, TA, ZA and ZB.

	     ZOOM, NEGATIVE and ROTATE

	       ZOOM:  You can select a Zoom of 50, 100, 200 or 400 percent.
	       The 50 percent zoom is useful for shrinking the image
	       to half size to display more of it at one time. The 200
	       and 400 percent zooms can be used to enlarge the image
	       to better display small details of interest.

	       NEGATIVE:  This displays the negative view of the image
	       similar to a photographic negative.  The negative view is
	       useful when displaying GOESTAP, IR images and wirephotos.

	       ROTATE:	Select either Mirror or 180 Degree Rotate.
	       Mirror is useful for wire photos that are often
	       sent as mirror images.  Rotate is useful for viewing images
	       from ascending-node (South-to-North track) polar-
	       orbiting satellites that send images upside down.





  PRINTING THE IMAGE

	       Before printing for the first time, use the Setup Menu
	       to select your printer. You can print the image either
	       to a printer connected to your computer's printer port
	       or to DOS device name. The device name could be a file
	       name or the name of a printer attached to a Local Area
	       Network.

	       You can print the entire image or just the part
	       displayed on the screen.

	       NOTE: Printing does NOT scale the image to fit the page.
		     The image will always be printed starting at the
		     TOP AND LEFT SIDE DISPLAYED ON THE SCREEN.  This
		     allows you to trim the top and align the left-hand
		     side before printing. Printing will continue across
		     the line until the page width is reached.

	       You can print the image in black and white, or with a
	       choice of various gray-scale dithering patterns.
	       Dithering is a printing method of using a series of
	       dots in an area to simulate gray information in the
	       same way that a newspaper would via the halftone
	       technique. The dither patterns allow your image to be
	       printed with up to 16 gray shades.

	       Because of the lower resolution of 9-pin dot-matrix
	       printers, you will get good results using either black
	       and white, or 2- and 4-gray-shade dithering patterns.




	     For 24-pin dot-matrix and laser printers, you will get
	     excellent results with all of the dithering patterns
	     including the 16 gray-shade dithers. The 16 gray-shade
	     dithers available are:

	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	     ³ BAYER	       ³ Brings out detail at the expense   ³
	     ³		       ³ of tonal reproduction (contrast).  ³
	     ³		       ³ Used for very detailed images.     ³
	     ³ FATTING	       ³ Good compromise between detail     ³
	     ³		       ³ and good tonal reproduction.	    ³
	     ³ VERTICAL LINE   ³ Emphasizes horizontal lines.	    ³
	     ³ HORIZONTAL LINE ³ Emphasizes vertical lines.	    ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	     Choosing the best dithering pattern for an image is a
	     matter of both experimentation and experience. The
	     Fatting dither offers a good compromise between detail
	     and contrast and is commonly used.

	     The print head on some printers may overheat when
	     printing large images. If this happens the printer will
	     go into a pause mode to cool down. If the wait is longer
	     than approximately 20 seconds, the program will time out
	     and quit waiting for the printer to resume.

	     If the print head overheats:

	     - wait for a few minutes for the printer to cool before
	       printing another image.

	     - configure the printer for Unidirectional printing
	       instead of Bidirectional printing. This will slow the
	       printer and allow more time for cooling.

	     - Use the DOS MODE command to prevent the printer time-
	       out condition and to allow the printer to resume
	       printing the image after the print head has cooled down
	       (e.g.,MODE LPT1:,,P). This DOS command could be placed
	       in the AUTOEXEC.BAT file so that it is executed every
	       time the computer is started.

	     NOTE:

	     If you're using the graphics driver shipped with DOS 4.0
	     (or later), the 'Shift/Print Screen' keys on the computer
	     keyboard can be used to print a very crude representation
	     of the image. The DOS GRAPHICS.COM driver must first be
	     loaded into memory. The graphics driver shipped with DOS
	     4.0 supports VGA graphics mode.




  SAVING THE IMAGE TO DISK

	     You can save either the entire image or just the part
	     displayed on the screen.

	     If you select the entire image then the image is saved
	     starting at the TOP AND LEFT SIDE DISPLAYED ON THE
	     SCREEN. This allows you to trim the top and align the
	     left hand side before saving to disk. You can save the
	     image using either the standard TIFF (Tag Image File
	     Format) or GIF (Graphics Interchange Format). TIFF has
	     fast file operations and stores an image as an
	     uncompressed raster-scan gray-scale image. GIF is the
	     standard format used for storing images by CompuServe and
	     most computer bulletin boards systems (BBS). GIF is
	     slower than TIFF, but uses an efficient compression
	     algorithm that minimizes file size and saves disk space.

	     These standard image file formats allow images to be
	     imported as graphics files into various painting and
	     Desktop Publishing applications that support either of
	     the formats.

	     TIFF files are supported by Aldus PageMaker, IBM Image
	     Edit, Logitech PaintShow, and WordPerfect 5.0. Image Edit
	     is excellent for modifying large TIFF image files. GIF
	     format files are used by many computer bulletin board
	     systems (BBS) and are supported by Compuserve CSHOW and
	     several painting programs.




ADDITIONAL INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  CALIBRATING THE ADAPTER

	     WeatherFAX card physical layout

	     ÚÄÄÄÄÝÛÄÄÄÄÄÄÝÛÄÄÄÄÄÄÄÄÄÄÄÄÝÛÄÄÄÄÄÄÄÄÄÝÛÄÄÄÄÄÄ¿
	     ³	ÚÄÛÛÄ¿	ÚÄÛÛÄ¿	      ÚÄÛÛÄ¿	 ÚÄÛÛÄ¿    ³ÚÄÄÄ
	     ³	³POT2³	³POT4³	      ³POT3³	 ³POT1³    ³³
	     ³	ÀÄÄÄÄÙ	ÀÄÄÄÄÙ	      ÀÄÄÄÄÙ	 ÀÄÄÄÄÙ    ³³
	     ³	 Stop	 Start		AM	  FM	   ³³
	     ³ Detector  Detector   Demodulator  Demod.    ÛÛÛÛÛ <Ä¿
	     ³	450 Hz	 300 Hz        2400 Hz	  1800 Hz  ÛÛÛÛÛ  phono
	     ³						   ³³	  jack
	     ³						   ³³
	     ³						   ³³
	     ³						   ³³
	     ³						   ³³
	     ³						   ³³
	     ³						   ³³
	     ÀÄÄÄÄÄÄÄÄÄ¿			       ÚÄÄÄÙ³
		       ÀÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÝÙ    ³


	     Calibration is needed if any of the Self-Tests indicate
	     that the card is operating out of the indicated
	     operating range. The self tests will indicate which
	     parameter is out of range and needs adjustment.
	     Instructions are provided below for making the
	     adjustment. The procedure is simple and can be performed
	     without special tools or knowledge. Because adjustments
	     are made while the computer is powered on it is
	     recommended the adjustment be done by a qualified
	     service technician.

	     A nonmetallic screwdriver should be used for the
	     adjustment. This will prevent damage to the computer
	     if the screwdriver should accidentally be dropped into
	     the computer.

	     1) Turn power to the computer off.

	     2) Remove the cover of the computer. Refer to the User's
		Guide for your computer for instructions for
		removing the cover.

	     3) Locate the fax card.

	     4) Turn computer power on and start the WeatherFAX
		program.

	     5) Select Test Adapter, and then Static Test. Adjust the
		potentiometers for the parameter out of range. When
		you are finished all parameters should be in the OK
		region.

	     6) The final adjustment for the FM demodulator should be
		done while viewing the FM Graph Test. The line should
		be linear, sloping upward with time, and centered
		between 0 and 256. If not centered adjust the FM
		potentiometer while viewing the Graph.




  USING EXPANDED MEMORY (LIM 4.0)

	     Expanded memory eliminates the problem of acquiring
	     images that are too large for the computer's 640 kbytes
	     of conventional memory. The LIM (Lotus Intel Microsoft)
	     standard allows up to 32 Mbytes for image storage. It
	     requires both expanded memory and a LIM 4.0 software
	     driver. The WeatherFAX program will automatically use
	     either conventional or expanded memory based upon the
	     larger available amount of RAM.

	     If you have an 80386 type computer then EXTended memory
	     can emulate LIM 4.0 EXPanded memory by using an expanded
	     memory manager driver. The QEMM 386 driver by Quarterdeck
	     Office Systems is fast and recommended. The HIMEM.SYS and
	     EMM386.SYS drivers shipped with Microsoft Windows 3.0 are
	     slower and may cause interrupts to be lost when capturing
	     very high resolution images.

	     Some of the newer 80286-type computers use the NEAT(r)
	     chip sets that allow the EXTended memory to emulate
	     Expanded memory. However EXTended memory on other 80286-
	     type computers without the special chip sets cannot
	     emulate EXPanded memory. You must use an actual LIM 4.0
	     capable memory card (e.g. Intel AboveBoard).

  USING SUPER VGA FOR CARDS USING TSENG AND ATI CHIP SETS.

	     These cards include Orchid ProDesigner, Genoa Super VGA,
	     Boca Research SVGA and Everex Viewpoint VRAM.
	     The ATI VGAWonder+ uses the ATI chip set.

	     If you have a Super VGA card, consult your User's Manual
	     to identify the chip set type and the enhanced graphics
	     modes. If the chip set is listed in the table below, you
	     can select all of the resolutions listed. To identify the
	     chip set type, you can either:

	       1) refer to the User's Manual

	       2) visually inspect the SVGA card

	       3) try to match the video BIOS modes in the manual with
		  those in the following table.




	      TABLE OF VIDEO BIOS MODES FOR SUPPORTED RESOLUTIONS
	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
	     ³		       ³	    VIDEO BIOS MODES	     ³
	     ³		       ³640x480³ 800x600 ³ 1024x768³1280x1024³
	     ³ CHIP SET        ³  256  ³ 16 ³ 256³ 16 ³ 256³  16     ³
	     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÅÄÄÄÄÅÄÄÄÄÅÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
	     ³ Tseng ET3000    ³  2E   ³ 29 ³ 30 ³ 37 ³ NA ³  NA     ³
	     ³ Tseng ET4000    ³  2E   ³ 29 ³ 30 ³ 37 ³ 38 ³  NA     ³
	     ³ ATI	       ³  62   ³ 54 ³ 63 ³ NA ³ NA ³  NA     ³
	     ³ Paradise        ³  5F   ³ 58 ³ NA ³ 5D ³ NA ³  NA     ³
	     ³ Video Seven     ³  67   ³ 62 ³ 69 ³ 65 ³ NA ³  NA     ³
	     ³ Everex Viewpoint³  30   ³ 02 ³ 31 ³ 20 ³ 32 ³  21     ³
	     ³		       ³       ³    ³	 ³    ³    ³	     ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ

	      NOTES:

	      1) NA indicates that the mode is not supported.

	      2) A multifrequency (multisync) display is required for
		 resolutions greater than 800 x 600.

	      3) 512 kbytes of video RAM is required on the graphics
		 card for the 800 x 600 x 256 and 1024 x 768 x 16
		 color modes. 1 MB is required for the 1024 x 768 x
		 256 and 1280 x 1024 x 16 color modes.

	      4) Everex Viewpoint, Genoa Super VGA, Orchid
		 ProDesigner, Boca Research SVGA, Sigma VGA/H and STB
		 VGA Extra use the Tseng chip set. ATI VGAWonder+ use
		 the ATI chip set. AST VGA Plus, Compaq VGA, Paradise
		 VGA Plus/Prof and Dell VGA use the Paradise chip set.
		 Video7 VRAM/Fastwrite use the Video Seven chip set.

	      5) The ATI VGAWonder is not supported at 1024x768-16
		 colors because the card does not support the BIOS
		 commands used by the WeatherFAX program for the pull-
		 down menus.

	     If your SVGA chip set is not listed above, then VGA and
	     the 800 x 600 x 16 enhanced graphics mode can be still be
	     used by specifying the BIOS mode as a command-line
	     parameter. See section below for instructions.





  USING SUPER VGA (800 X 600 PIXEL) MODE
  (chip sets other than Tseng/ATI)

	     If you have a multifrequency (multisync) monitor and a
	     graphics card that supports the super 800 X 600 x 16
	     color graphics mode, you can display images in this mode.
	     Because different cards use different 800 by 600 BIOS
	     mode numbers, you must specify the mode as command line
	     parameter when starting FAX.EXE. To specify the graphics
	     mode:

	       FAX.EXE /Hxx	 where: 'xx' is the hex mode.

	     Example:
	     For Oak the hex mode is 52 	  ->   FAX.EXE /H52

	     Be sure to check that you have the correct monitor and
	     graphics card. The software does not verify the monitor
	     or graphics card. Selected cards and their respective 800
	     X 600 graphics mode (hex) are listed below. If your
	     graphics card is not listed, you will have to consult
	     your card's user's guide to determine the correct mode.

	      TABLE LISTING 800 x 600x 16-COLOR BIOS MODES
	      FOR VARIOUS GRAPHICS CARDS

	     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄ¿
	     ³ CARD		      ³ CHIP SET ³ MODE ³
	     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄ´
	     ³ Chips & Technology     ³ C&T	 ³ /H70 ³
	     ³ Everex		      ³ Everex	 ³ /H02 ³
	     ³ Great Wall of China    ³ Trident  ³ /H5B ³
	     ³ Oak Technology	      ³ Oak Tech ³ /H52 ³
	     ³ Tecmar VGA-AD	      ³ 	 ³ /H18 ³
	     ³ AST VGA Plus	      ³ 	 ³ /H58 ³
	     ³ Compaq VGA	      ³ 	 ³ /H58 ³
	     ³ Dell VGA 	      ³ 	 ³ /H58 ³
	     ³ Genoa Super VGA/VGA    ³ 	 ³ /H29 ³
	     ³ Paradise VGA	      ³ 	 ³ /H58 ³
	     ³ Video7 VRAM/Fastwrite  ³ 	 ³ /H62 ³
	     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÙ

	     If your card isn't listed above, you should determine the
	     correct 800 x 600 x 16-color mode from the User's Manual
	     that came with your card.




  SOURCES OF WEATHER-FACSIMILE SIGNALS

	     There are three direct sources for weather-fax signals:
	     geostationary satellites; polar-orbiting satellites; and
	     Marine weather-radio transmitters. The fax card along
	     with the WeatherFAX software can capture all the above
	     types of facsimile. Tone detectors on the card will
	     automatically detect the beginning and ending of each
	     image.

	     Geostationary Satellites.

	       Geostationary satellites include US GOES, European
	       Space Agency METEOSAT, and Japanese GMS. These
	       satellites broadcast on S-Band frequencies; GOES at
	       1691 MHz and Meteosat at 1694.5 MHz. These satellites
	       are located approximately 22,000 miles above the Earth
	       and provide WEFAX (Weather Facsimile) transmissions
	       using the standard Automatic Picture Transmission (APT)
	       format.

	       Reception of WEFAX images requires an antenna,
	       downconverter, and receiver. The antenna can be either
	       a small parabolic dish or a loop Yagi. The
	       downconverter  converts the S-Band signal to 137.5 MHz.
	       An inexpensive  scanner radio can be used for the
	       receiver. A two-wire cable from the receiver plugs into
	       the WeatherFAX card.  Configure the software for AM
	       mode and 240 scans per minute.

	     Polar-Orbiting Satellites.

	       These satellites transmit on VHF frequencies between
	       137 and 139  MHz. The NOAA (TIROS-N) series transmit at
	       137.50 MHz and 137.62 MHz. The Russian Meteor series
	       satellites transmit at 137.15, 137.30 and 137.850 MHz.
	       A general-purpose scanner receiver capable of receiving
	       the frequencies between 136-138 MHz is required. Many
	       of the newer Regency, Uniden, and Radio Shack scanners
	       cover this frequency range and give excellent results.
	       This receiver can also be used in conjunction with the
	       geostationary satellite antenna and downconverter.
	       Configure the software for AM mode and 120 scans per
	       minute.

	     Marine weather radio facsimile.

	       These broadcasts can be received direct from government
	       radio transmissions. There are over 65 transmitter
	       sites worldwide which utilize over 200 different radio
	       frequencies. The information transmitted includes
	       weather-analysis charts, satellite pictures, and radar
	       charts. These radio signals are received on short wave
	       radio frequencies (e.g., 8080 kHz) on Upper Sideband. A
	       stable general coverage single sideband (SSB) receiver
	       is required.  The published frequency is normally the
	       center frequency of the upper sideband. Tune your SSB
	       receiver approximately 1600-1700 Hz below the published
	       frequency. For example, the US Navy Fleet Weather
	       Station at Norfolk (NAM), transmits at 8080 kHz. Tune
	       your receiver to 8078.3 kHz (USB) to receive its
	       transmissions. Configure the software for FM mode and
	       120 scans per minute.





  WEATHERFAX SPECIFICATIONS

	     o Recording Rate : 60, 90, 120, 240 SPM (Scans Per
	       Minute)

	     o Index of cooperation IOC

	       576 - Marine fax
	       288 - TIROS
	       267 - WEFAX (GOES)

	     o FSK input: 1500 Hz "black", 2300 Hz "white"

	     o FSK input level:  Range selectable by pads.

	       -10 dBm to +20 dBm   Strong Signal
	       -20 dBm to +10 dBm   Normal Signal
	       -30 dBm to   0 dBm   Weak Signal

	     o AM input:  2400-Hz AM modulation
	       lower voltage  = "black"
	       higher voltage = "white"

	     o AM input level : -20 dBm to +10 dBm.

	     o Input impedance:  10 kilohms

	     o Control signals	 Automatic start, frame, and stop
	       with manual start and frame.

	       - START : Signal modulated between "black" and
		 "white" at 300 Hz rate for 5 seconds.

	       - STOP : Signal modulated between "black" and "white"
		 at a 450 Hz rate for 5 seconds.

	       - FRAME : "black" signal interrupted by a short burst
		 at a "white" signal each scan line for 5 seconds
		 immediately following start signal.

	     o Hardware interrupt:  8 (BIOS timer interrupt)

	     o I/O Addresses:  386H and 387H

	     o Voltage and current requirements:


	       ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
	       ³ Voltage ³ Current ³
	       ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
	       ³  + 5V	 ³ 120 mA  ³
	       ³  +12V	 ³  25 mA  ³
	       ³  -12V	 ³  15 mA  ³
	       ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ





IF YOU HAVE DIFFICULTY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	     SYMPTOM	 SOLUTION
	     ÄÄÄÄÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
	     ALIGNMENT	    1) Reduce the value of Pels per Line.
	     WAVY -
	     CANNOT BE	    2) If you have a 80386-type computer,
	     SET	       remove the Expanded Memory driver and
			       restart the computer. IF THE PROBLEM
			       GOES AWAY THEN THE DRIVER IS TOO SLOW.
			       If so then use the EMM-386 driver from
			       Quarterdeck Office Systems.

	     NO PICTURE      1) Run fax card tests to assure that the
				card is operating within the correct
				range.

			     2) Verify that Adapter Mode is set
				correctly for the facsimile signal.

			     3) For Marine fax mode verify that the
				receiver signal level is within the
				range of the fax card attenuation
				pads. If the signal level is very weak
				then decrease the attenuation pads
				using the F4 key on the adapter mode
				menu.

			     4) Is the fax receiver powered on and the
				cable connected to the fax adapter?







	     DISTORTED	     1) Verify that the Adapter Mode is set
	     PICTURE		correctly for the received signal.
				(e.g., if the image is WEFAX then the
				Adapter Mode must be set to AM.

			     2) Verify that Scans per minute is set
				correctly for the received signal.

			     3) If the image is slanted then the Page
				Alignment needs to be adjusted while
				an image is received.

			     4) For FM Marine fax verify that the
				receiver is tuned correctly. Marine
				fax images are usually transmitted
				using Upper Side Band (USB). The
				receiver must be tuned approximately
				1700 Hz lower then the center
				frequency.

				Example: For a 8080 kHz HF fax signal,
				the receiver should be tuned to 8078.3
				kHz. (8080 kHz - 1.7 kHz = 8078.3
				kHz). Vary the receiver frequency
				slightly to get the best picture.

			     5) Check to see if any TSR (terminate and
				stay resident) programs are in memory.
				If they are, remove them. Some TSR
				programs may cause problems when
				running WeatherFAX.

	     EXPANDED		Be sure that the Expanded memory
	     MEMORY NOT 	device driver (LIM 4.0) is loaded
	     RECOGNIZED:	into memory. If you have an 80386 type
				computer, then the EXTended memory can
				emulate LIM 4.0 EXPanded memory using
				a device driver shipped with DOS 4.0.
				For most 80286 computers, EXTended
				memory cannot emulate EXPanded
				memory.

	     800 x 600	     1) Verify your graphics card supports
	     DISPLAY		this mode.
	     DOESN'T WORK
			     2) Verify that you have a multifrequency
				monitor that supports 800 x 600
				resolution.

			     3) Verify you have set the correct BIOS
				display mode.

			     4) Verify that the correct mode is listed
				as a command line parameter.




ADAPTER/SOFTWARE AVAILABILITY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	     The WeatherFAX adapter and software are available from:

	       OFS Software
	       6404 Lakerest Ct.
	       Raleigh, NC 27612

	     o Assembled and tested scan-converter board, software and
	       instructions ..................................$360.

	     o Kit including PC board, all parts, software and
	       assembly instructions .........................$230.

	     o Software only (Version 3.0) ....................$30.

	     Terms:

	     - Specify either 5.25" or 3.5" diskette format for the
	       software.

	     - North Carolina residents add 5% sales tax.

	     - Please add $6.50 for shipping and handling (or add
	       $12.00 for overseas orders.)

	     - Check drawn on a US bank in US funds. International
	       bank or postal money order in US funds. All foreign
	       orders must be prepaid.

	     - Please allow 4-6 weeks for US delivery.





TRADEMARKS USED IN THIS GUIDE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

	     o GIF and Graphics Interchange Format are trademarks of
	     Compuserve Incorporated

	     o Turbo C is a trademark of Borland International

	     o IBM and PS/2 are trademarks of International Business
	     Machines Corporation

	     o PageMaker and Aldus are registered trademarks of Aldus
	     Corporation.

	     o Apple, ImageWriter are registered trademarks of Apple
	     Computer Inc.

	     o LaserJet is a trademark of Hewlett-Packard Company.

	     o Intel is a trademark of Intel Corporation.

	     o Microsoft, and MS-DOS are registered trademarks of
	     Microsoft Corporation.

	     o WordPerfect is a trademark of WordPerfect Corporation.