This page covers notes for PrintCAD 1.16 that  are not included in the
         v1.14 manual.

           Low resolution (180 dpi) Canon BJ and BJC drivers have been dropped.

           /F0 drives HP-GL/2 raster devices. The nominal output resolution may
           be appended to the /F option, for example /F0 300. The actual device
           resolution may also be appended, for example /F0 300,303,299

           /FG drives the Pacific Data Products ProTracer.

           The nominal output resolution of PostScript or HP-GL may be appended
           to the /F option,  for example /FS 600.  HP-GL with dashed lines, at
           other than 1016 dpi, requires HP 7550 enhanced IW mode.

           The PostScript XP macro selects a paper tray. To use it set a prefix
           code such as /J48 32 88 80 for tray 1 or /J49 32 88 80 for tray 2.

           The  + and  - suboptions of /X let you increase or shrink PrintCAD's
           memory space.

           Line width N turns a pen off.

           /F7+  is  a  two pass BJ-330  driver,  which gives  dark  print  and
           eliminates indexing gaps.

           /FB+ is a BJC driver with sparse line to line overlap.

           /F8 adds support for the HP 7220.

           Esc breaks out of PrintCAD, leaving  the printer ready for new data.
           Ctrl-Break  (as before)  stops PrintCAD  immediately and  a  printer
           reset is usually needed in this case.

           The E suboption of /Y sets HP 7550 enhanced IW command mode.

           The N suboption of /L suppresses the form feed.