VGASAVE


        Author:   Ken Singer

        Purpose:  Blanks VGA screen after a specified interval of no keyboard
                  or BIOS video activity; a keystroke or BIOS video write
                  restores the screen.  Optionally, the silmultaneous
                  depression of the CTRL and ALT keys can also be used to
                  manually blank the screen.

        Format:   VGASAVE [nn][-]

        Remarks:  The square brackets [] indicate optional parameters.

                  nn is the delay time, in minutes, after which VGASAVE will
                  blank the screen if no keyboard or BIOS video activity
                  occurs.  This time can range from 01 to 60 minutes.  A value
                  of 00 will disable the automatic screen blanking.  If the
                  time is not specified on the command line, it defaults to 03
                  (minutes).

                  - (minus) enables the ability to manually blank the screen by
                  pressing the CTRL and ALT keys at the same time.  (The screen
                  is restored when any key is pressed or a BIOS video write is
                  executed.)  Executing VGASAVE without the minus disables this
                  feature.

                  Following are some examples:

                       VGASAVE
                       (3 minutes automatic blanking, manual blanking disabled)

                       VGASAVE -
                       (3 minutes automatic blanking, manual blanking enabled)

                       VGASAVE 05
                       (5 minutes automatic blanking, manual blanking disabled)

                       VGASAVE 05-
                       (5 minutes automatic blanking, manual blanking enabled)

                       VGASAVE 00
                       (no automatic blanking, manual blanking disabled)

                       VGASAVE 00-
                       (no automatic blanking, manual blanking enabled)



                VGASAVE


                  The first time VGASAVE is executed, it becomes resident.
                  Subsequent executions only change appropriate parameters in
                  the resident copy.  Thus, it can be run as many times as
                  desired to change the blanking time, disable or enable the
                  manual blanking capability, etc.

                  VGASAVE uses several VGA registers to blank and restore the
                  screen; therefore, it requires a VGA card compatible with the
                  IBM VGA at the register level.  The program has been tested
                  satisfactorily with the COMPAQ VGA and the IBM Personal
                  System/2 (VGA) Display Adapter, but the program does not work
                  with an early version of the VEGA VGA card.

                  This program takes over the Keyboard (09h), Video (10h), and
                  Timer (08h) interrupts, but passes through all parameters to
                  the interrupt routines it "stole" the vectors from.  The
                  Video and Timer interrupt vectors are released when the 00
                  blanking time is specified.  While VGASAVE has been
                  sucessfully tested with a variety of resident programs, there
                  is always the possiblilty it will conflict with one.  For
                  that reason, it should be carefully tested in your
                  environment before using it in a production mode.

                  VGASAVE may be freely copied and used in any environment, as
                  long as: (1) No charge is made for its use; and (2) It is not
                  modified.

                  Comments can be directed to:

                       Ken Singer
                       HAL-PC Telecom I Bulletin Board
                       (713) 847-3200

                  Versions of this program are also available for Hercules
                  (HERCSAVE) and EGA (EGASAVE) cards.