CPCHND.SYS Documentation

		CPCHND.SYS is a DOS device driver that allows the Complete 
	PC Scanner to be used with PC Paintbrush with INTERRUPTS.
	Dither and Brightness are set on the scanner itself. 
	Resolution is dependent on the scanner type:

			Scanner			Resolution(s) in DPI
		Complete Hand Scanner/400		400,300,200
		Complete Half Page Scanner		200
		Complete Half Page Scanner/400 	400, 300, 200

		It is unnecessary to run the bundled software that comes with 
	the Complete PC Scanner. Insert CPCHND.SYS into the CONFIG.SYS file
	using the appropriate options. At boot the driver will respond with
	a message based on the options. When Paintbrush is run, the scanner
	will light up briefly before the tools are drawn on the screen. 
	If this	happens you are ready to scan. If not, you must turn off your 		system, re-address the dip switches, and try again.
		
		Options are:

		Default	Complete Hand Scanner/400
		/1	Complete Hand Scanner/400
		/2	Complete Half Page Scanner
		/3	Complete Half Page Scanner/400 
		/Cx	Channel for DMA, where x is 1 or 3 (default is channel 			3)
		/Hxxx	Hex port value, where xxx is the hex value. The 						default is 3E0H (no 'H' 			needed)
		/Ix	IRQ number, where x is 2-5 (INTERRUPT number is required)
				
	Examples:
	device=cpchnd.sys /2 /H2E0 /I2 /C3
		Complete Half Page Scanner, port = 220H, IRQ=2, DMA=3
		
	Available Port Settings:
		220H	260H	2A0H	2E0H	320H	360H	3A0H 	3E0H		
		
   			Scanner interface card DIP Switches
	Port	#1	#2	#3	#4	#5	#6	#7	#8
	  				|N.A.	|IRQ2	|IRQ3	|IRQ4	|IRQ5

	220H	on 	on 	on 	off	off	off	off	off
	260H	off	off	on 	off	off	off	off	off
	2A0H	off	on 	on 	off	off	off	off	off
	2E0H	on 	off	off	off	off	off	off	off
	320H	off	on	on	off	off	off	off	off
	360H	off	on 	off	off	off	off	off	off
	3A0H	off	off	on 	off	off	off	off	off
	3E0H	off	off	off	off	off	off	off	off
	
	Note: DIP switch  UP = ON 

	Make sure that only one interrupt is set on.