Genius Documentation
	ZSoft Corporation's GENIUS.SYS is designed to work with the 
	Genius hand scanner. This scanner device driver presently has
	only one option: DMA channel.
	
	DMA channel:	/C1		DMA channel 1
			/C3		DMA channel 3
	
	Example CONFIG.SYS entry:
			DEVICE=GENIUS.SYS /C3

	The driver is set up for the Genius 4500 and DMA channel 3.

	The scanner supports 100, 200, 300, and 400 dpi.

	This device driver does not support interrupts. Therefore, 
	to obtain the best performance, GENIUS.SYS requires EMS.

	Paintbrush may save buffers to the hard disk while scanning. 
	When the disk is accessed, scan lines are lost, resulting in gaps 
	in the image. To prevent this, the entire scan may be scanned into 
	Expanded Memory and then read back as required, greatly reducing the 
	chance of losing scan data.