The Kyocera A-800 Scanner requires 2 device drivers in CONFIG.SYS.
The first one:

device=SCNDRV.SYS DMA=3 IRQ=5 ADR=300

These settings coincide with the factory settings on the scanner board
and are optional.  They need to be changed only if you change the switches
on the interface board.

The second one:

device=KYSCANER.SYS /R=xxx,xxx,xxx,xxx,xxx,xxx

The optional /R switch allows the users to specify their own resolution pairs.

For example:

device=KYSCANER.SYS /R=200,175,150,125,100,75

The driver will implement these new settings if they are specified correctly:
i.e., descending sequence and within the scanner's resolution range.