LOGITECH.SYS Documentation

	LOGITECH.SYS is a DOS device driver that allows the Logitech 
ScanMan to be used with PC Paintbrush IV Plus. The resolutions are 400, 300,
200 and 100 dpi. Dither and Brightness are set on the scanner itself.

	Options are:
	/Cx	channel for DMA, where x is 1 or 3 (default is channel 1)
	/D	double buffering switch (for some EMS boards)
	/Hhhh	hex port value, where hhh is the hex value. Default is 
		280H (no 'H' needed at end)
	/N	new Logitech scanner interface card (with the switches on
		the back of the scanner)

	Examples:
	device=logitech.sys		set up for DMA channel 1 and Port
				        280H
	device=logitech.sys /c1		set up for DMA channel 1
	device=logitech.sys /c3 /h3e0	set up for DMA channel 3 and Port 3E0H