This document describes the device driver WILLOWGS.SYS version 1.0.

  WILLOWGS.SYS allows Paintbrush to capture gray scale images
  from the Willow frame grabber.

     File Setup:  Copy WILLOWGS.SYS to wherever you keep your system device
		  drivers.

		  Add the following line to your CONFIG.SYS file:
		  Device=WILLOWGS.SYS /x (where x is 1 or 2. See below.)

		  Copy W320x200.CNF and W640x400.CNF to your
		  main Paintbrush directory.

  There are two types of switches that may be specified on the WILLOWGS.SYS
  command line in CONFIG.SYS:

       Resolution:   /1  ( 320 x 200 )
		     /2  ( 640 x 400 )

		    If no resolution switch is specified, /2 is assumed.
		    See below for more about the available resolution
		    switches.

	     Port:   /A - /H.  If the data capture port must be reassigned
			       with a jumper on the board, the port in use
			       must be specified to this driver.

				     /A = 300H	  /E = 340H
				     /B = 310H	  /F = 350H
				     /C = 320H	  /G = 360H
				     /D = 330H	  /H = 370H

			      If this switch is omitted, /D (330H) is assumed.

	  Default:  	      Device=WILLOWGS.SYS [/2/D]


  There are two capture resolutions you can add to the CONFIG.SYS line:

       /1  ( 320 x 200 )   This mode extracts the image from one of the
			   four buffers on the Willow board. It's fast,
			   (1 second per full page scan) due to the fact
			   that scan lines may be extracted linearly,
			   just like a scanner.

       /2  ( 640 x 400 )   This mode combines the contents of the four
			   Willow buffers to produce a high quality gray
			   scale image.

   General note...  The Willow frame capture logic is actually designed
		    for fast, continuous video display, and the four banks
		    lend themselves to that requirement.  Each bank is
		    sent to a video segment in one step and merged by the
		    video hardware.

		    A stand-alone executable program might have the luxury
		    of allocating memory for merging the banks into a
		    linear map, but this device driver does not. Nor will it
		    use the disk as virtual memory or scratch file storage.

		    Instead, whenever Paintbrush requests a number of scan-
		    lines, each bank is repositioned to its last position,
		    and the image data is stored dynamically in Paintbrush's 
		    buffer.

		    Since bank switching resets the input latch to the top
		    of the frame, each bank is processed completely before
		    moving to the next bank.

		    This technique requires more processing time, but has
		    the advantage of zero memory requirements on the part
		    of the driver.

		    Full page scans may take about 9 seconds. Half
		    of this time is spent by Paintbrush writing the gray 
		    scale data to virtual memory on disk. Machines with
		    sufficient extended memory will obviously benefit.


  This device driver takes 5K of user memory.


  Setting up Paintbrush:  The scanner interface of PC Paintbrush is designed
			  for 8.5" by 11" images.

			  Willow images are setup as 100 dpi.  This is a
			  relative term, simply used for conversion into
			  inches. 
			  Thus a 320 x 200 image is 3.2 inches wide,
			  2.0 inches tall.
			  640 x 400 is 6.4 inches wide, 4.0 inches tall.

  Configuration:  	  If you scanned a Willow frame into the 8.5 x 11
			  preview area, it shows up relative to the larger
			  frame. The framing box is also in effect, which
			  means the upper left corner will be clipped.

			  Ideally, the preview frame should match the size
			  of the image, and the framing box should be pulled
			  all the way out to the edges of the frame.


		8.5 x 11.0	      3.2 x 2.0 	      6.4 x 4.0
	      --------------	    --------------	 --------------------
	      |*******	   |	    |************|	 |******************|
	      |*******---- |	    |************|	 |******************|
	      |*******	 | |	    |************|	 |******************|
	      |*******	 | |	    |************|	 |******************|
	      | |	 | |	    --------------	 |******************|
	      | |	 | |				 |******************|
	      | ---------- |				 |******************|
	      | 	   |				 --------------------
	      --------------




			  The configuration options of Paintbrush are quite
			  extensive, and all of the above may be accomplished.

			  The configuration may also be saved to disk so you
			  only have to do this once for each mode and load it
			  once when you start Paintbrush.

			  In fact, you can copy two configuration files
			  provided on this disk into Paintbrush's directory.
			  These files are:   W320x200.CNF and W640x400.CNF.


  More about setting up:  Resolution is fixed at 100 dpi. 

			  Enhancements: The only enhancement option is
			  REVERSE. You can use this option to reverse black
			  and white.

			  Gray scale 256 shades is the ONLY valid setting.
			  Paintbrush defaults to B/W mode, and the Paintbrush
			  message "Scanner Initialization Failed"
			  will occur if you scan in black and white.  Simply
			  select Gray Scale under Image Type to resolve.

			  Gray scale mode is automatically selected in both
			  configuration files on this disk.

			  Brightness and Contrast are both nicely adjustable.

			  Always load the grays palette (GRAYS.PAL) when you
			  start Paintbrush. You could also create a small .PCX
			  file with the GRAYS palette, and load it when you
			  start up. This technique gets you to the scanning
			  logic quicker.

  Sequence for Scanning:  Decide on your resolution.  640x400 (default) is
			  recommended. (/2 or nothing...)  Be sure to reboot
			  to activate your new CONFIG.SYS environment.

			  Start Paintbrush in 320x200 x 256 colors for mode
			  /1, or 640x480 x 256 colors for mode /2. Any 256
			  color mode will work.  The 640x480 mode gives a 
	      		  better spatial effect to 640x400 video, while
		          640x400 mode gives you a full screen image. If your
			  system can handle 800x600 x 256 or 1024x768 x 256
			  colors, it should look great.

			  If you use a 16 color mode, Paintbrush converts each
			  image to 16 shades.  You can scan in 640X480 X 256
			  colors, save the image and reload it into, for
		 	  example, 800x600 x 16 colors to approximate to 16
			  shades only once.


		 Next...  Select cancel for Load File and Create Work Space.
			  Select Load Palette under Options. Select GRAYS.PAL.

			  Start scan mode by choosing File/Scan
			  or by pressing Ctrl G.

			  Load your configuration file. This may be done under
			  File/Open or by pressing Alt F, O and selecting the
			  filename. (W320x200.CNF or W640x400.CNF)

			  Remember to select the configuration applicable to
			  the resolution you specified for this driver
			  (/1 or /2).

			  To scan a full page, press Ctrl R, Y(es) or Space.
			  To enter the preview area, press Ctrl S.

			  To return to Paintbrush's main drawing area, press
			  Ctrl G.