Keyboard Codes Recognized by GET
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³      Function Key Scan Codes(1)    ³    Alphabetic & Other ASCII Keys     ³
³Key  Normal   Shift Control    Alt  ³ Key/  Normal   Shift  Control  Alt(1)³
³F1      59      84      94     104  ³ Shift  ASCII   ASCII   ASCII     Scan³
³F2      60      85      95     105  ³  Tab       9      15     148(s)   165³
³F3      61      86      96     106  ³   a       97      65       1       30³
³F4      62      87      97     107  ³   b       98      66       2       48³
³F5      63      88      98     108  ³   c       99      67       3       46³
³F6      64      89      99     109  ³   d      100      68       4       32³
³F7      65      90     100     110  ³   e      101      69       5       18³
³F8      66      91     101     111  ³   f      102      70       6       33³
³F9      67      92     102     112  ³   g      103      71       7       34³
³F10     68      93     103     113  ³   h      104      72       8       35³
³F11    133     135     137     139  ³   i      105      73       9       23³
³F12    134     136     138     140  ³   j      106      74      10       36³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´   k      107      75      11       37³
³      Number & Top Row Keys         ³   l      108      76      12       38³
³Key/  Normal   Shift  Control Alt(1)³   m      109      77      13       50³
³Shift  ASCII   ASCII   ASCII   Scan ³   n      110      78      14       49³
³ `/~    96     126      -       41  ³   o      111      79      15       24³
³ 1/!    49      33      -      120  ³   p      112      80      16       25³
³ 2/@    50      64      3(s)   121  ³   q      113      81      17       16³
³ 3/#    51      35      -      122  ³   r      114      82      18       19³
³ 4/$    52      36      -      123  ³   s      115      83      19       31³
³ 5/%    53      37      -      124  ³   t      116      84      20       20³
³ 6/^    54      94      30     125  ³   u      117      85      21       22³
³ 7/&    55      38      -      126  ³   v      118      86      22       47³
³ 8/*    56      42      -      127  ³   w      119      87      23       17³
³ 9/(    57      40      -      128  ³   x      120      88      24       45³
³ 0/)    48      41      -      129  ³   y      121      89      25       21³
³ -/_    45      95      31     130  ³   z      122      90      26       44³
³ =/+    61      43      -      131  ³  [/{     123      91      27       26³
³ \/|    92     124      28      43  ³  ]/}     125      93      29       27³
³BkSp     8       8     127      14  ³  ;/:      59      58       -       39³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´  '/"      39      34       -       40³
³    Cursor Pad & Grey Key Codes     ³  ,/<      44      60       -       51³
³Key   Normal   Shift  Control Alt(1)³  ./>      46      62       -       52³
³PrtSc      -      -      114      - ³  //?      47      63       -       53³
³Insert     -      -       -     162 ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³Home       -      -       -     151 ³    Number Pad (NumLock On(2)) Codes  ³
³PageUp     -      -       -     153 ³ Key Normal(2) Shift(2) Control Alt(3)³
³Delete     -      -       -     163 ³ 0/Ins     48      82      146  AltNum³
³End        -      -       -     159 ³ 1/End     49      79      117  AltNum³
³PageDown   -      -       -     161 ³ 2/Down    50      80      145  AltNum³
³UpArrow    -      -       -     152 ³ 3/PgDn    51      81      118  AltNum³
³LeftArrow  -      -       -     155 ³ 4/Left    52      75      115  AltNum³
³DownArrow  -      -       -     160 ³ 5         53      76      143  AltNum³
³RightArrow -      -       -     157 ³ 6/Right   54      77      116  AltNum³
³ /        47(a)  47(a)  149     164 ³ 7/Home    55      71      119  AltNum³
³ *        42(a)  42(a)  150      55 ³ 8/Up      56      72      141  AltNum³
³ -        45(a)  45(a)  142      74 ³ 9/PgUp    57      73      132  AltNum³
³ +        43(a)  43(a)  144      78 ³ ./Del     46      83      147  AltNum³
³NumEnter 125(4) 125(4)  10(a)   166 ³--------------------------------------³
³Esc      126(4) 126(4) 126(4)     1 ³(2)With NumLock Off swap Normal/Shift.³
³Enter    125(4) 125(4)  10(a)    28 ³(3)AltNum keys enter ASCII characters.³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
(s) indicates scan code, (a) indicates ASCII code where not readily apparent.
(1)To use extended/enhanced keys with GET C and GET T, add 100 to the scan code.
Scan codes of 28 through 150 are reported as surrogates 128 through 250.
To use extended and enhanced keys with GET U, add 255 to the scan code. Many of
the scan codes 28 through 150 are recognized as surrogates 283 through 405.
(4)Surrogate values for use with GET C and GET T.  Also, space will return 255. 

                                   
                              ASCII Table
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Dec   Char   Code ³  Dec  Char ³ Dec  Char ³  Dec  Char ³  Dec  Char ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄ´
³   0   NUL         ³   32 Space ³  64    @  ³   96    `  ³  128    €  ³
³   1   Ctrl-a      ³   33    !  ³  65    A  ³   97    a  ³  129    �  ³
³   2   Ctrl-b      ³   34    "  ³  66    B  ³   98    b  ³  130    ‚  ³
³   3   Ctrl-c      ³   35    #  ³  67    C  ³   99    c  ³  131    ƒ  ³
³   4   Ctrl-d      ³   36    $  ³  68    D  ³  100    d  ³  132    „  ³
³   5   Ctrl-e      ³   37    %  ³  69    E  ³  101    e  ³  133    …  ³
³   6   Ctrl-f      ³   38    &  ³  70    F  ³  102    f  ³  134    †  ³
³   7   Ctrl-g Bell ³   39    '  ³  71    G  ³  103    g  ³  135    ‡  ³
³   8   Ctrl-h BkSp ³   40    (  ³  72    H  ³  104    h  ³  136    ˆ  ³
³   9   Ctrl-i Tab  ³   41    )  ³  73    I  ³  105    i  ³  137    ‰  ³
³  10   Ctrl-j LF   ³   42    *  ³  74    J  ³  106    j  ³  138    Š  ³
³  11   Ctrl-k      ³   43    +  ³  75    K  ³  107    k  ³  139    ‹  ³
³  12   Ctrl-l FF   ³   44    ,  ³  76    L  ³  108    l  ³  140    Œ  ³
³  13   Ctrl-m CR   ³   45    -  ³  77    M  ³  109    m  ³  141    �  ³
³  14   Ctrl-n      ³   46    .  ³  78    N  ³  110    n  ³  142    Ž  ³
³  15   Ctrl-o      ³   47    /  ³  79    O  ³  111    o  ³  143    �  ³
³  16   Ctrl-p      ³   48    0  ³  80    P  ³  112    p  ³  144    �  ³
³  17   Ctrl-q      ³   49    1  ³  81    Q  ³  113    q  ³  145    ‘  ³
³  18   Ctrl-r      ³   50    2  ³  82    R  ³  114    r  ³  146    ’  ³
³  19   Ctrl-s      ³   51    3  ³  83    S  ³  115    s  ³  147    “  ³
³  20   Ctrl-t      ³   52    4  ³  84    T  ³  116    t  ³  148    ”  ³
³  21   Ctrl-u      ³   53    5  ³  85    U  ³  117    u  ³  149    •  ³
³  22   Ctrl-v      ³   54    6  ³  86    V  ³  118    v  ³  150    –  ³
³  23   Ctrl-w      ³   55    7  ³  87    W  ³  119    w  ³  151    —  ³
³  24   Ctrl-x      ³   56    8  ³  88    X  ³  120    x  ³  152    ˜  ³
³  25   Ctrl-y      ³   57    9  ³  89    Y  ³  121    y  ³  153    ™  ³
³  26   Ctrl-z      ³   58    :  ³  90    Z  ³  122    z  ³  154    š  ³
³  27   Ctrl-[ Esc  ³   59    ;  ³  91    [  ³  123    {  ³  155    ›  ³
³  28   Ctrl-\      ³   60    <  ³  92    \  ³  124    |  ³  156    œ  ³
³  29   Ctrl-]      ³   61    =  ³  93    ]  ³  125    }  ³  157    �  ³
³  30   Ctrl-^      ³   62    >  ³  94    ^  ³  126    ~  ³  158    ž  ³
³  31   Ctrl-_      ³   63    ?  ³  95    _  ³  127   DEL ³  159    Ÿ  ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÙ

ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄ¿
³ Dec Char ³ Dec  Char ³ Dec  Char ³ Dec  Char ³ Dec  Char ³ Dec  Char ³
ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄ´
³ 160      ³ 176    °  ³ 192    À  ³ 208    Ð  ³ 224    à  ³ 240    ð  ³
³ 161   ¡  ³ 177    ±  ³ 193    Á  ³ 209    Ñ  ³ 225    á  ³ 241    ñ  ³
³ 162   ¢  ³ 178    ²  ³ 194    Â  ³ 210    Ò  ³ 226    â  ³ 242    ò  ³
³ 163   £  ³ 179    ³  ³ 195    Ã  ³ 211    Ó  ³ 227    ã  ³ 243    ó  ³
³ 164   ¤  ³ 180    ´  ³ 196    Ä  ³ 212    Ô  ³ 228    ä  ³ 244    ô  ³
³ 165   ¥  ³ 181    µ  ³ 197    Å  ³ 213    Õ  ³ 229    å  ³ 245    õ  ³
³ 166   ¦  ³ 182    ¶  ³ 198    Æ  ³ 214    Ö  ³ 230    æ  ³ 246    ö  ³
³ 167   §  ³ 183    ·  ³ 199    Ç  ³ 215    ×  ³ 231    ç  ³ 247    ÷  ³
³ 168   ¨  ³ 184    ¸  ³ 200    È  ³ 216    Ø  ³ 232    è  ³ 248    ø  ³
³ 169   ©  ³ 185    ¹  ³ 201    É  ³ 217    Ù  ³ 233    é  ³ 249    ù  ³
³ 170   ª  ³ 186    º  ³ 202    Ê  ³ 218    Ú  ³ 234    ê  ³ 250    ú  ³
³ 171   «  ³ 187    »  ³ 203    Ë  ³ 219    Û  ³ 235    ë  ³ 251    û  ³
³ 172   ¬  ³ 188    ¼  ³ 204    Ì  ³ 220    Ü  ³ 236    ì  ³ 252    ü  ³
³ 173   ­  ³ 189    ½  ³ 205    Í  ³ 221    Ý  ³ 237    í  ³ 253    ý  ³
³ 174   ®  ³ 190    ¾  ³ 206    Î  ³ 222    Þ  ³ 238    î  ³ 254    þ  ³
³ 175   ¯  ³ 191    ¿  ³ 207    Ï  ³ 223    ß  ³ 239    ï  ³ 255 Blank ³
ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÙ
NOTE: Upper ASCII characters (above 127) can be formed by holding the Alt 
key down while spelling out the decimal value on the number pad.  When 
the Alt key is released, the ASCII character will be displayed.  See the 
documentation for your text editor for the method it uses to enter control 
and upper ASCII values.


                             Scan Code Table(1)
 
Extended and enhanced keys are recognized by their scan codes.  This 
scan code table lists all known scan codes for the 101 enhanced 
keyboard.  GET C and GET T use the upper ASCII characters as 
surrogates for some of the extended and enhanced keys.  GET forms 
these surrogates for many of the scan codes in the range of 28 through 
150 by adding 100 to the scan code and using the corresponding upper 
ASCII character.  For example, the scan code for F1 is 59.  This would 
be confused with the ASCII character <;>, so GET adds 100 to it and 
uses code 159 which is represented by the upper ASCII character <Ÿ>.

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Code  Key      ³ Code  Key       ³ Code  Key      ³ Code   Key         ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
³  1    Esc      ³ 43    Alt-\/|   ³  85   Shift-F2 ³ 127    Alt-8       ³
³  2    1/!      ³ 44    Alt-z     ³  86   Shift-F3 ³ 128    Alt-9       ³
³  3    2/@      ³ 45    Alt-x     ³  87   Shift-F4 ³ 129    Alt-0       ³
³  4    3/#      ³ 46    Alt-c     ³  88   Shift-F5 ³ 130    Alt--       ³
³  5    4/$      ³ 47    Alt-v     ³  89   Shift-F6 ³ 131    Alt-=       ³
³  6    5/%      ³ 48    Alt-b     ³  90   Shift-F7 ³ 132    CtrlPgUp    ³
³  7    6/^      ³ 49    Alt-n     ³  91   Shift-F8 ³ 133    F11         ³
³  8    7/&      ³ 50    Alt-m     ³  92   Shift-F9 ³ 134    F12         ³
³  9    8/*      ³ 51    Alt-,/<   ³  93   Shift-F10³ 135    Shift-F11   ³
³ 10    9/(      ³ 52    Alt-./>   ³  94   Ctrl-F1  ³ 136    Shift-F12   ³
³ 11    0/)      ³ 53    Alt-//?   ³  95   Ctrl-F2  ³ 137    Ctrl-F11    ³
³ 12    -/_      ³ 54    RightShift³  96   Ctrl-F3  ³ 138    Ctrl-F12    ³
³ 13    =/+      ³ 55    Grey*     ³  97   Ctrl-F4  ³ 139    Alt-F11     ³
³ 14    BkSp     ³ 56    LeftAlt   ³  98   Ctrl-F5  ³ 140    Alt-F12     ³
³ 15    Tab      ³ 57    Space     ³  99   Ctrl-F6  ³ 141    CtrlUp      ³
³ 16    Alt-q    ³ 58    CapsLock  ³ 100   Ctrl-F7  ³ 142    CtrlGrey-   ³
³ 17    Alt-w    ³ 59    F1        ³ 101   Ctrl-F8  ³ 143    Ctrl-Num5   ³
³ 18    Alt-e    ³ 60    F2        ³ 102   Ctrl-F9  ³ 144    CtrlGrey+   ³
³ 19    Alt-r    ³ 61    F3        ³ 103   Ctrl-F10 ³ 145    CtrlDown    ³
³ 20    Alt-t    ³ 62    F4        ³ 104   Alt-F1   ³ 146    CtrlIns     ³
³ 21    Alt-y    ³ 63    F5        ³ 105   Alt-F2   ³ 147    CtrlDel     ³
³ 22    Alt-u    ³ 64    F6        ³ 106   Alt-F3   ³ 148    CtrlTab     ³
³ 23    Alt-i    ³ 65    F7        ³ 107   Alt-F4   ³ 149    CtrlGrey/   ³
³ 24    Alt-o    ³ 66    F8        ³ 108   Alt-F5   ³ 150    CtrlGrey*   ³
³ 25    Alt-p    ³ 67    F9        ³ 109   Alt-F6   ³ 151    AltGreyHome ³
³ 26    [/{      ³ 68    F10       ³ 110   Alt-F7   ³ 152    AltGreyUp   ³
³ 27    ]/}      ³ 69    NumLock   ³ 111   Alt-F8   ³ 153    AltGreyPgUp ³
³ 28    Alt-Enter³ 70    ScrollLock³ 112   Alt-F9   ³ 154                ³
³ 29    LeftCtrl ³ 71    Home      ³ 113   Alt-F10  ³ 155    AltGreyLeft ³
³ 30    Alt-a    ³ 72    Up        ³ 114   CtrlPrtSc³ 156                ³
³ 31    Alt-s    ³ 73    PgUp      ³ 115   CtrlLeft ³ 157    AltGreyRight³
³ 32    Alt-d    ³ 74    Grey-     ³ 116   CtrlRight³ 158                ³
³ 33    Alt-f    ³ 75    Left      ³ 117   CtrlEnd  ³ 159    AltGreyEnd  ³
³ 34    Alt-g    ³ 76    Num5      ³ 118   CtrlPgDn ³ 160    AltGreyDown ³
³ 35    Alt-h    ³ 77    Right     ³ 119   CtrlHome ³ 161    AltGreyPgDn ³
³ 36    Alt-j    ³ 78    Grey+     ³ 120   Alt-1    ³ 162    AltGreyIns  ³
³ 37    Alt-k    ³ 79    End       ³ 121   Alt-2    ³ 163    AltGreyDel  ³
³ 38    Alt-l    ³ 80    Down      ³ 122   Alt-3    ³ 164    AltGrey-/   ³
³ 39    Alt-;/:  ³ 81    PgDn      ³ 123   Alt-4    ³ 165    AltTab      ³
³ 40    Alt-'/"  ³ 82    Ins       ³ 124   Alt-5    ³ 166    AltGreyEnter³
³ 41    Alt-`/~  ³ 83    Del       ³ 125   Alt-6    ³                    ³
³ 42    LeftShift³ 84    Shift-F1  ³ 126   Alt-7    ³                    ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
(1)To use extended and enhanced keys with GET C and GET T, add 100 to 
the scan code. Many of scan codes 28 through 150 are recognized as 
surrogates 128 through 250. To use extended and enhanced keys with GET 
U, add 255 to the scan code. Many of scan codes 28 through 150 are 
recognized as surrogates 283 through 405.