April 10, 1991

1.0  INTRODUCTION

1.1  PURPOSE

     The purpose of this document is to aid professional programmers who
     wish to write software to use the high resolution modes supported by
     the VGAWONDER video board. Working knowledge of EGA/VGA graphics and
     assembly language programming is required and assumed. The document
     describes several features unique to the VGAWONDER and how each high
     resolution mode is similar or is different compared to standard VGA
     modes. It does not contain any programming information about standard
     EGA/VGA modes. Refer to the Reference list in the appendix for
     recommended EGA/VGA programmer's references.

1.2  CONVENTIONS

     The code segments contained in this document follow the conventions of
     the MicroSoft MASM assembler. Numbers given in hexadecimal end with a
     lower case h.

2.0  FEATURES OF THE VGA BOARD

2.1  STANDARD VIDEO MODES

     AH = 0  ;set video mode

     AL =    MODE/             RESOLUTION      DIM/          START
             TYPE                              COLOR         ADDRESS
     ---------------------------------------------------------------
     0h      color/alpha       640x200         40x25/ BW     b800:0h
     1h      color/alpha       640x200         40x25/ 16     b800:0h
     2h      color/alpha       640x200         80x25/ BW     b800:0h
     3h      color/alpha       640x200         80x25/ 16     b800:0h
     0*      color/alpha       640x350         40x25/ BW     b800:0h
     1*      color/alpha       640x350         40x25/ 16     b800:0h
     2*      color/alpha       640x350         80x25/ BW     b800:0h
     3*      color/alpha       640x350         80x25/ 16     b800:0h
     0+      color/alpha       720x400         40x25/ BW     b800:0h
     1+      color/alpha       720x400         40x25/ 16     b800:0h
     2+      color/alpha       720x400         80x25/ BW     b800:0h
     3+      color/alpha       720x400         80x25/ 16     b800:0h
     4h      color/graphics    320x200         40x25/  4     b800:0h
     5h      color/graphics    320x200         40x25/ BW     b800:0h
     6h      color/graphics    320x200         80x25/ BW     b800:0h
     7h      mono/alpha        720x350         80x25/ BW     b000:0h
     0dh     color/graphics    320x200         40x25/ 16     a000:0h
     0eh     color/graphics    640x200         80x25/ 16     a000:0h
     0fh     mono/graphics     640x350         80x25/ BW     a000:0h
     10h     color/graphics    640x350         80x25/ 16     a000:0h
     11h     color/graphics    640x480         80x30/ BW     a000:0h
     12h     color/graphics    640x480         80x30/ 16     a000:0h
     13h     color/graphics    320x200         80x25/256     a000:0h
2.2  ENHANCED VIDEO MODES

     23h     color/alpha       1056x350        132x25/16     b800:0h
     27h     mono/alpha        1056x350        132x25/BW     b000:0h
     33h     color/alpha       1056x352        132x44/16     b800:0h
     37h     mono/alpha        1056x352        132x44/BW     b000:0h
     53h     color/graphics    800x560         16            a000:0h
     54h     color/graphics    800x600         16            a000:0h
     55h     color/graphics    1024X768        16            a000:0h
     61h     color/graphics    640x400         256           a000:0h
     62h     color/graphics    640x480         256           a000:0h
     63h     color/graphics    800x600         256           a000:0h
     64h     color/graphics    1024x768        256           a000:0h
     65h     color/graphics    1024x768        16            a000:0h
     67h     color/graphics    1024x768        4             a000:0h

2.3  REQUIRED CONFIGURATIONS

     The enhanced modes have differing memory requirements. Some enhanced 
     modes are supported only on certain monitor types or hardware revisions. 
     The following chart describes the requirements for each enhanced mode.

     Mode#   Resolution      Colors/         Memory          Monitors
     (hex)                   Palette         Required        Supported
     -----------------------------------------------------------------
     23      132x25          16/64           512K            1,2,5
     27      132x25          B&W             512K            1,2,5
     33      132x44          16/64           512K            1,2,5
     37      132x44          B&W             512K            1,2,5
     54      800x600         16/256K         256K            5
     55*     1024X768        256/256K        256K            4,5 
     61      640x400         256/256K        512K            3,4,5
     62      640x480         256/256K        512K            3,4,5
     63      800x600         256/256K        512K            5
     64#     1024x768        256/256K        1M              4,5
     65      1024x768        16/256K         512K            4,5
     67      1024x768        4/16            256K            4,5

     Monitors: (1) TTL mono (2) EGA (3) VGA (4) IBM 8514 (5) Multisync

     * not supported on VGAWONDER V3
     # only supported on VGAWONDER+ 1Mb

3.0  DETERMINING THE STATUS OF THE CARD

     The VGA BIOS features some special functions which will allow the
     programmer to determine if a compatible VGA board is installed and how
     the card is configured within his program.

3.1  IDENTIFYING THE VIDEO CARD

     All EGA and VGA display adapters manufactured by ATI Technologies will
     contain the character string: "761295520" starting at address: C000:31.
     VGA boards which are based on the ATI VGA chip set are identified by the         
   character string "31" at address C000:40. The card is further identified 
     by 2 bytes. The definition of the byte at address C000:42 is:

               bit 0   = 0 16-bit VGA board
               bit 0   = 1  8-bit VGA board
               bit 1   = 1 mouse port present on display adapter
               bit 2   = 1 supports non-interlaced 1024x768
               bit 3   = 1 microchannel product
               bit 4   = 1 contains programmable video clock chip
               bit 5-7 = not currently defined

     The character at address C000:43 contains the revision of the VGA gate
     array. Currently, the following models exist and other revisions 
     may follow in the future.

              '1' = 18800
              '2' = 18800-1
              '3' = 28800-2
              '4' = 28800-4
              '5' = 28800-5

3.2  DETERMINING THE MONITOR TYPE

     The following assembler code segment can be used to determine for
     which monitor the VGA board is currently configured.

                         cli
                         mov     dx,EXTENDED_REG
                         mov     al,DATA_I
                         out     dx,al
                         inc     dx
                         in      al,dx
                         sti
                         and     al,0fh

     returns  al =       0       EGA monitor
                         1       PS/2 monochrome monitor
                         2       TTL monochrome monitor
                         3       PS/2 color monitor
                         4       RGB color monitor
                         5       Multisync monitor
                         7       PS/2 8514 monitor
                         8       Seiko 1430          
                         9       NEC MultiSync 2A
                         a       Crystalscan 860/Tatung 1439
                         b       NEC MultiSync 3D
                         c       TVM 3M         
                         d       NEC MultiSync XL
                         e       TVM 2A
                         f       TVM 3A

     where
                         EXTENDED_REG = see section 4.41 in this document
                               DATA_I = 0bbh

     Note : We reserve the right to add more monitor types at any time. We
     recommend that if an undefined value is returned that the program
     assumed that a multisync is installed.

3.3  DETERMINING MEMORY SIZE

     In terms of memory determination, ATI VGA chipsets fall into 3 groups. The first
group is identified as types 1 and 2 (see section 3.31). The second group is identified as
type 3 and the third group as type 4 or 5. All types can be equipped with 256K or 512K
of RAM. Only types 4 or 5 may be equipped with 1M of RAM.

The following code segment will determine the type of chipset and use the appropriate
method to determine memory size.

.MODEL small,C
.CODE

PUBLIC RAMSIZE
; --------------------------------------------------------------------------
; CALL VALUES: none
; RETURNS VALUES: AX = 256 (100h) for 256K bytes
;                      512 (200h) for 512K bytes
;                      1024 (400h) for 1024K bytes

RAMSIZE PROC NEAR
        push bx                      ; Save used register values
        push dx
        push ds
        mov  ax, 0c000h
        mov  ds, ax
        xor  ax, ax
        mov  dx, word ptr ds:[0010h] ; Get value of ATI extended register
        mov  bl, byte ptr ds:[0043h] ; Get value of ATI chip version
        pop  ds
        mov  bh, 1                   ; Assume 256K ramsize (100h)
        cmp  bl, '3'
        jae  ramsize_V6_up           ; Use different method to determine
        mov  al, 0bbh                ;  memory size of chip version is 3 or
        cli                          ;  higher
        out  dx, al
        inc  dx
        in   al, dx                  ; Get ramsize byte for chip versions
        sti                          ;  1 & 2
        test al, 20h
        jz   eo_ramsize
        mov  bh, 2                   ; Set ramsize return value to 512K (200h)
        jmp  short eo_ramsize        ;  and exit

ramsize_V6_up:                       ; Method used for newer ATI chip versions
        mov  al, 0b0h
        cli
        out  dx, al
        inc  dx
        in   al, dx                  ; Get ramsize byte for versions 3-5
        sti
        test al, 10h                 ; Check if ramsize byte indicates 256K
        jz   ramsize_V7_up           ;  or 512K bytes
        mov  bh, 2                   ; Set ramsize return value to 512K (200h)

ramsize_V7_up:                       ; Check for ramsize for ATI chip
        cmp  bl, '4'                 ;  versions 4 & 5
        jb   eo_ramsize
        test al, 8                   ; Check if version 5 ATI chip has 1024K
        jz   eo_ramsize
        mov  bh, 4                   ; Set ramsize return value to 1024K (400h)

eo_ramsize:
        xor  bl,bl                   ; Zero lower byte of BX
        mov  ax, bx                  ; Return actual ramsize value in AX

        pop  dx                      ; Restore BX and DX registers
        pop  bx
        ret
RAMSIZE ENDP
; --------------------------------------------------------------------------

        END

3.4  DETERMINING WHETHER A MODE IS SUPPORTED

     Your VGA board implements an extended video BIOS call which can be
     used to determine if a particular mode is actually available in the
     user's current configuration. The following assembler routine
     demonstrates this technique:

               push      bp
               mov       bp,sp
               push      es
               mov       al,ARG
               mov       ah,12h
               mov       bx,5506h
               mov       bp,0ffffh
               int       10h
               mov       ax,bp
               pop       es
               pop       bp
               ret

               where ARG = mode desired in hexadecimal

     If this routine returns ax = 0ffffh, that mode is not supported in the
     current configuration. If the mode is supported, ax will contain the
     offset start address of the CRTC parameter table for that mode.

     Note : We recommend this technique as the only reliable means of
     determining if a particular mode is supported on our EGA or VGA boards.

4.0  PROGRAMMING THE HIGH RESOLUTION MODES

4.1  SETTING THE VIDEO MODE

     The VGA card can be set into a video mode through the BIOS by using
     the standard IBM method: AH is set to 0, AL is set to the video mode
     number, and a call to software interrupt 10h is executed. See sections
     2.1 and 2.2 of this manual for a list of available modes. The
     following example will perform this function:

              mov ah,0            ;set mode function
              mov al,MODE         ;select video mode
              int 10h             ;make BIOS call by using the video
                                  ;interrupt

     We recommend that programmers select the video mode through BIOS
     whenever possible rather than programming the mode via the registers.
     For any particular video mode, the configuration of the internal
     registers may differ depending on the type of monitor installed.
     Also, we reserve the right to change the product in a way which would
     be transparent to BIOS but which would have an impact on software
     which writes to the registers.

4.2  VIDEO MEMORY ADDRESSING

4.21 ADDRESS RANGE OF VGA BOARD

     The VGA board uses the RESERVED area designated by IBM for video
     RAM and the video BIOS (A000 to C7FF). The organization is as follows:

     Mono text video RAM:  B000-B7FF
     Color text video RAM: B800-BFFF
     Graphics video RAM:   A000-AFFF (upto eight 64k banked pages with 512K
                                      RAM)
     Video BIOS:           C000-C7FF
     I/O Ports:            1CE-ICF, 3B0-3DF    

4.22 PAGES and PLANES:

     There are two memory mapping systems used with VGA graphics modes:
     Packed pixel and Planar organization.

     The Packed pixel mapping scheme is associated with pages and uses
     contiguous memory to describe each pel. IBM VGA mode 13h uses this
     system. Extended modes 61, 62, 63, and 65h also use the Bit-packed
     scheme but they use a unique method to select which page is
     available for reading and writing.

     The Planar organized memory mapping scheme is associated with
     planes and uses a bit from each plane to describe a pel. IBM VGA
     mode 12h uses this system as does Extended modes 54h, 55h and 67h.

4.23 SELECTING MEMORY PAGES:

     The memory organization of extended modes 61h, 62h, 63h, 64h and 65h are
     arranged into 64k page segments. The data in each page is displayed on
     a specific region of the screen image. For example, mode 63h has eight
     pages. The first page is displayed on the top eighth of the screen
     image, the second page is displayed on the second eighth of the screen
     image, and so on. Data can be read or written to one page at a time.
     The default active page is Page 0. A special code segment is required
     to be executed before data can be read or written to a specific page.
     A page selecting code segment is provided below. VGA cards with 256K
     of RAM have four, those with 512K have eight and those with 1M have 16 
     pages available. Modes 61h, 62h, 63h and 64h require 1 byte per pel and 
     mode 65h requires 1/2 byte per pel.

     The following code segment can be used to select the required page:

              cli
              mov     dx,EXTENDED_REG
              mov     al,PAGE_SELECT
              out     dx,al
              inc     dl
              in      al,dx
              mov     ah,al
              and     ah,PAGE_MASK
              shl     ch,1
              or      ah,ch
              mov     al,PAGE_SELECT
              dec     dl
              out     dx,ax
              sti

     where    ch = required page value (0 to 7 for mode 63h for example)
              PAGE_SELECT  = 0B2h
              PAGE_MASK    = 0E1h
              EXTENDED_REG = value of extended register stored at memory
                             address C000:0010h. See section 4.31


     The following is a table that describes the visible range for
     each extended mode which uses the bit-packed memory organization:

     Mode 61h (640 x 400 - 256 colors):

     Page            Visible range  (column,row)              Memory range
     0               (0,0)      -->  (255,102)                A0000 - AFFFF
     1               (256,102)  -->  (511,204)                A0000 - AFFFF
     2               (512,204)  -->  (127,307)                A0000 - AFFFF
     3               (128,307)  -->  (639,399)                A0000 - AE7FF

     Mode 62h (640 x 480 - 256 colors):

     Page            Visible range  (column,row)              Memory range
     0               (0,0)      -->  (255,102)                A0000 - AFFFF
     1               (256,102)  -->  (511,204)                A0000 - AFFFF
     2               (512,204)  -->  (127,307)                A0000 - AFFFF
     3               (128,307)  -->  (383,409)                A0000 - AFFFF
     4               (384,409)  -->  (639,479)                A0000 - AAFFF

     Mode 63h (800 x 600 - 256 colors):

     Page            Visible range  (column,row)              Memory range
     0               (0,0)      -->  (735,81)                 A0000 - AFFFF
     1               (736,81)   -->  (671,163)                A0000 - AFFFF
     2               (672,163)  -->  (607,245)                A0000 - AFFFF
     3               (608,245)  -->  (543,327)                A0000 - AFFFF
     4               (544,327)  -->  (479,409)                A0000 - AFFFF
     5               (480,409)  -->  (415,491)                A0000 - AFFFF
     6               (416,491)  -->  (351,573)                A0000 - AFFFF
     7               (352,573)  -->  (799,599)                A0000 - A561F

     Mode 64h (1024 x 768 - 256 colors):
     Page            Visible range  (column,row)              Memory range
     0               (0,0)      -->  (1023,63)                 A0000 - AFFFF
     1               (0,64)     -->  (1023,127)                A0000 - AFFFF
     2               (0,128)    -->  (1023,190)                A0000 - AFFFF
     3               (0,191)    -->  (1023,255)                A0000 - AFFFF
     4               (0,256)    -->  (1023,319)                A0000 - AFFFF
     5               (0,320)    -->  (1023,383)                A0000 - AFFFF
     6               (0,384)    -->  (1023,447)                A0000 - AFFFF
     7               (0,448)    -->  (1023,511)                A0000 - AFFFF
     8               (0,512)    -->  (1023,575)                A0000 - AFFFF
     9               (0,576)    -->  (1023,639)                A0000 - AFFFF
     10              (0,640)    -->  (1023,703)                A0000 - AFFFF
     11              (0,704)    -->  (1023,767)                A0000 - AFFFF
     12                       spare
     13                       spare
     14                       spare
     15                       spare
     
     Mode 65h (1024 x 768 - 16 colors):

     Page            Visible range  (column,row)              Memory range
     0               (0,0)      -->  (1023,127)               A0000 - AFFFF
     1               (0,128)    -->  (1023,255)               A0000 - AFFFF
     2               (0,256)    -->  (1023,383)               A0000 - AFFFF
     3               (0,384)    -->  (1023,511)               A0000 - AFFFF
     4               (0,512)    -->  (1023,639)               A0000 - AFFFF
     5               (0,640)    -->  (1023,767)               A0000 - AFFFF
     6                        spare
     7                        spare

4.3  DETAILS OF EACH EXTENDED VIDEO MODE

4.31 132X25 - Color text (Mode 23h)
     132x25 - B&W text (Mode 27h)
     132X44 - Color text (Mode 33h)
     132X44 - B&W text (Mode 37h)

     Video Memory Organization:

     The memory organization of very similar to standard text modes. Only 
     one page of 6,660 bytes (132X25 modes) or 11,616 bytes (132X44 modes) 
     is availible. 

     Video Data Organization:

     The video data organization is identical to standard text modes.

     BIOS support

     All BIOS calls supported on standard text modes are supported. 

     NOTE! It is a good idea to avoid DOS calls when using the 132X44 text 
     modes. Most versions of ANSI.SYS are not compatible with text modes 
     which have more than 25 lines. This is particularly a problem when 
     scrolling the screen.

4.32 800x600 - 16 COLORS (Mode 54h)

     Video Memory Organization:

     The memory organization is identical to 16 color IBM EGA/VGA modes
     and consists of 256K organized into 4 maps of 64K each. One bit from
     each of the 4 maps is used to compose each pel. The IBM EGA/VGA Map
     Mask Register is used to select any or all the maps to be updated.
      A0000:0 -> ----------
                |          |----------
                |          |          |----------
                |----------|          |          |---------- <===\=======\
                | Reserved |----------|          |          |  60,000    |
                 ----------| Reserved |----------|          |    |       |
                   Plane 0  ----------| Reserved |----------|<===/      64K
                              Plane 1  ----------| Reserved |            |
                                          Plane 2   --------- <===========/
                                                     Plane 3

     Video Data Format:

     The video data format is identical to the 16 color IBM EGA/VGA modes. 

     Color Mapping:

     Color selection and palette changing is identical to the 16 color IBM 
     EGA/VGA mode

4.33 1024x768 - 16 COLORS PLANAR (Mode 55h)

     Video Memory Organization:

     The memory organization is similar to 16 color IBM EGA/VGA modes
     and consists of 2 pages of 256K each organized into 4 maps of 64K. One 
     bit from each of the 4 maps is used to compose each pel. The IBM 
     EGA/VGA Map Mask Register is used to select any or all the maps to be 
     updated.



     Address                                 Page #

     A000:0 ==> +-----+-----+-----+-----+
                |     |     |     |     |
                |     |     |     |     |
                |     |     |     |     |      0 
                |     |     |     |     |
                |     |     |     |     |
     A000:0 ==> +-----+-----+-----+-----+
                |     |     |     |     |
                |     |     |     |     |
                |     |     |     |     |      1
                |     |     |     |     |
                |     |     |     |     |
                +-----+-----+-----+-----+
     Map #         0     1     2     3


     Selecting Memory Page:


     The following code segment demonstates how to switch between pages 
     when in this mode. 

     To change the write plane
              cli
              mov     dx,ATI_REG
              mov     al,PLANE_SELECT
              out     dx,al
              inc     dl
              in      al,dx
              mov     ah,al
              and     ah,WPLANE_MASK
              shl     ch,1
              or      ah,ch
              mov     al,PLANE_SELECT
              dec     dl
              out     dx,ax
              sti

     To change the read plane
              cli
              mov     dx,ATI_REG
              mov     al,PLANE_SELECT
              out     dx,al
              inc     dl
              in      al,dx
              mov     ah,al
              and     ah,RPLANE_MASK
              shl     ch,1
              shl     ch,1
              shl     ch,1
              shl     ch,1
              rol     ch,1
              or      ah,ch
              mov     al,PLANE_SELECT
              dec     dl
              out     dx,ax
              sti

              Where ch = page number required
                    ATI_REG = store in location c000:10h
                    PLANE_MASK = 0e1h
                    WPLANE_MASK = 0e1h
                    RPLANE_MASK = 01eh
                    PLANE_SELECT = 0b2h
                    DIFF_RW_PLANE = 008h
                    MISC2_REG = 0beh
                    DATA_I = 0bbh
    
     The read and write planes can be changed simultaneously.

    4.36 800x600 - 256 COLORS (Mode 63h)

     Video Memory Configuration:

     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. The VGA board must be equipped with 512K of RAM
     to support this mode. Mode 63h uses eight 64K pages. For information
     on selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.


      A0000:0 -> ----------<==============================================\
                |          |----------                                     |
                |          |          |----------                          |
                |          |          |          | \                       |
                |          |          |          |  \                      |
                 ----------|          |          |   \                     |
                    Page 0  ----------|          |    \                    |
                               Page 1  ----------       ---------- <=\  480,000
                                          Page 3  \    |          |  |     |
                                                   \   |          | 64K    |
                                                    \  |          |  |     |
                                                     \ |          |  |     |
                                                        ---------- <=/=====/
                                                           Page 7


     Video Data Format:

     The video data format is identical to IBM VGA mode 13h (320x200-256
     color). Each pel is represented by 1 byte.

     Color Mapping:

     Color selection and palette changing is identical to VGA mode 13h.
 Video Data Format:

     The video data format is identical to the 16 color IBM EGA/VGA modes. 

     Color Mapping:

     Color selection and palette changing is identical to the 16 color IBM 
     EGA/VGA mode

4.34 640x400 - 256 COLORS (Mode 61h)

     Video Memory Configuration:
     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. A VGA board equipped with 256K or 512K of RAM
     will support this mode. Mode 61h uses four 64K pages.  For information
     on selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.

       A0000:0->-----------<===========================================\
                |          |----------                                |
                |          |          |----------                     |
                |          |          |          |---------- <==\=====|
                |          |          |          |          |   |     |
                 ----------|          |          |          |  64K    |
                  Page 0    ----------|          |          |   |   256,000
                               Page 1  ----------|          |   |     |
                                          Page 2  ---------- <==/=====/
                                                     Page 3


     Video Data Format:

     The video data format is identical to IBM VGA mode 13h (320x200-256
     color). Each pel is represented by 1 byte.

     Color Mapping:

     Color selection and palette changing is identical to VGA mode 13h.

4.35 640x480 - 256 COLORS (Mode 62h)

     Video Memory Configuration:

     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. The VGA board must be equipped with 512K of RAM
     to support this mode. Mode 62h uses five 64K pages. For information on
     selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.


      A0000:0 -> ---------- <=============================================\
                |          |---------                                      |
                |          |         |---------                            |
                |          |         |         |---------                  |
                |          |         |         |         |--------- <=\    |
                 ----------|         |         |         |         |  |    |
                   Page 0   ---------|         |         |         | 64K   |
                              Page 1  ---------|         |         |  | 307,200
                                        Page 2  ---------|         |  |    |
                                                  Page 3  --------- <=/====/
                                                            Page 4


     Video Data Format:
     The video data format is identical to IBM VGA mode 13h (320x200-256
     color). Each pel is represented by 1 byte.

     Color Mapping:

     Color selection and palette changing is identical to VGA mode 13h.

4.36 800x600 - 256 COLORS (Mode 63h)

     Video Memory Configuration:

     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. The VGA board must be equipped with 512K of RAM
     to support this mode. Mode 63h uses eight 64K pages. For information
     on selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.


      A0000:0 -> ----------<==============================================\
                |          |----------                                     |
                |          |          |----------                          |
                |          |          |          | \                       |
                |          |          |          |  \                      |
                 ----------|          |          |   \                     |
                    Page 0  ----------|          |    \                    |
                               Page 1  ----------       ---------- <=\  480,000
                                          Page 3  \    |          |  |     |
                                                   \   |          | 64K    |
                                                    \  |          |  |     |
                                                     \ |          |  |     |
                                                        ---------- <=/=====/
                                                           Page 7


     Video Data Format:

     The video data format is identical to IBM VGA mode 13h (320x200-256
     color). Each pel is represented by 1 byte.

     Color Mapping:

     Color selection and palette changing is identical to VGA mode 13h.

4.37 800x600 - 256 COLORS (Mode 64h)

     Video Memory Configuration:

     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. The VGA board must be equipped with 512K of RAM
     to support this mode. Mode 64h uses sixteen 64K pages. For information
     on selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.

      A0000:0 -> ----------<==============================================\
                |          |----------                                     |
                |          |          |----------                          |
                |          |          |          | \                       |
                |          |          |          |  \                      |
                 ----------|          |          |   \                     |
                    Page 0  ----------|          |    \                    |
                               Page 1  ----------       ---------- <=\  786,432
                                          Page 3  \    |          |  |     |
                                                   \   |          | 64K    |
                                                    \  |          |  |     |
                                                     \ |          |  |     |
                                                        ---------- <=/=====/
                                                           Page 15


     Video Data Format:

     The video data format is identical to IBM VGA mode 13h (320x200-256
     color). Each pel is represented by 1 byte.

     Color Mapping:

     Color selection and palette changing is identical to VGA mode 13h.

4.38 1024x768 - 16 COLORS (Mode 65h)

     Video Memory Organization:

     This enhanced resolution mode uses a page memory system unique to this
     VGA board. The memory is organized into contiguous 64K blocks located
     at A0000H to AFFFFH. The VGA board must be equipped with 512K of RAM
     to support this mode. Mode 65h uses eight 64K pages. For information
     on selecting the active page, refer to section 4.23 "SELECTING MEMORY
     PAGES" of this document.

     A0000:0 -> ---------- <=============================================\

               |          |----------                                    |
               |          |          |----------                         |
               |          |          |          | \                      |
               |          |          |          |  \                     |
                ----------|          |          |   \                    |
                  Page 0   ----------|          |    \                   |
                              Page 1  ----------       ---------- <==\ 402,432
                                        Page 2   \    |          |   |   |
                                                  \   |          |   |   |
                                                   \  |          |  64K  |
                                                    \ |          |   |   |
                                                       ---------- <==/===/
                                                          Page 7

     Video Data Format:
     The video data format is unique to this mode. Each pel requires 4 bits
     or half a byte.

       ____________________________________________ High Order
      |    |    |    |    |                              Pixel
      |____|____|____|____|____ ____ ____ ____
      |  H |  H |  H |  H |  L |  L |  L |  L |
      |____|____|____|____|____|____|____|____|
                          |    |    |    |    |
                          |____|____|____|____|________ Low Order
                                                            Pixel

     Color Mapping:

     This mode has a different memory organization than standard EGA mode
     10h. If users want to use colors other than the standard 16 colors,
     users are required to re-program the external palettes (3C8h/3C9h). Re-
     programming the internal palettes (3C0h) will not work the same as it
     would in EGA mode 10h because the color mapping in mode 65h is
     different. It is not recommended to change the internal palettes at
     all for mode 65h. The following table shows the mapping of colors and
     external palettes.

     Palette registers available for re-programming are:

      Palette register   Palette register       default color   color
      (low order pels)   (high order pels)      assignment      value
      ----------------   -----------------      -------------   -----
           00h                 00h                Black           0h
           01h                 10h                Blue            1h
           02h                 20h                Green           2h
           03h                 30h                Cyan            3h
           04h                 40h                Red             4h
           05h                 50h                Magenta         5h
           06h                 60h                Brown           6h
           07h                 70h                White           7h
           08h                 80h                Dark Gray       8h
           09h                 90h                Light Blue      9h
           0Ah                 A0h                Light Green     Ah
           0Bh                 B0h                Light Cyan      Bh
           0Ch                 C0h                Light Red       Ch
           0Dh                 D0h                Light Magenta   Dh
           0Eh                 E0h                Yellow          Eh
           0Fh                 F0h                Bright White    Fh

     For example, to change the default color assignment for palette
     register 4 from Red to Bright White, palette register 4 and 40h would
     need to be re-programmed with the values:

            Red Intensity = 3Fh
            Green Intensity = 3Fh
            Blue Intensity = 3Fh

     so that both the low order AND high order pels are affected. The only
     exception is palette register 0 (Black); re-programming this register
     will affect both the low order and high order pels.

     An Example:

     The following example uses a standard IBM EGA/VGA BIOS call. If more
     information is required, consult the IBM EGA/VGA programmers reference
     list included in this document.

     Example segment to re-program a palette register:

       mov    ah,10h                ;EGA/VGA Set Palette Register BIOS call
       mov    al,10h
       mov    bx,PALETTE_REG_LOW    ;Palette register to be re-programmed
                                    ; for low order pels.
       mov    ch,GREEN_INTENSITY    ;Load new values
       mov    cl,BLUE_INTENSITY
       mov    dh,RED_INTENSITY
       int    10h

       mov    ah,10h                ;EGA/VGA Set Palette Register BIOS call
       mov    al,10h
       mov    bx,PALETTE_REG_HIGH   ;Palette register to be re-programmed
                                    ; for high order pels.
       mov    ch,GREEN_INTENSITY
       mov    cl,BLUE_INTENSITY
       mov    dh,RED_INTENSITY
       int    10h

     where:
       PALETTE_REG_LOW  = low  pel palette register (00,01,02,..,0F)
       PALETTE_REG_HIGH = high pel palette register (00,10,20,..,F0)

       GREEN_INTENSITY
       BLUE_INTENSITY  = 6 bit intensity values for defining the default color
       RED_INTENSITY


4.39 1024x768 - 4 COLORS (Mode 67h)

     Video Memory Organization:

     The memory organization is identical to the IBM 16 color EGA and VGA
     modes. 256K of RAM is divided into 4 maps of 64k. The IBM EGA/VGA Map
     Mask Register is used to select the maps to be updated.

     A0000:0->/------\
              |      | /------\
              |  C0  | |      | /------\
              \------/ |  C1  | |      | /------\ <---+
              Plane 0  \------/ |  C0  | |      |     49152 bytes/plane
              ^        Plane 1  \------/ |  C1  |     |
              |              ^  Plane 2  \------/ <---+
              |              |  ^         Plane 3
              \---odd pels---/  |               ^
                                |               |
                                \---even pels---/


     Video Data Format:

     This mode uses a unique data format where 2 bits are required per pel.
     Plane 0 and 1 contain the data for odd numbered pels and Planes 2 and
     3 contain the data for the even numbered pels.

     Color Mapping:

     This mode supports four palette selections. The palette or color set
     is selected by setting bits 0 & 1 of the IBM EGA/VGA Color Select
     Register.

                                   Color Values (C0, C1)
     Color set #        C0=0,C1=0  C0=1,C1=0  C0=0,C1=1  C0=1,C1=1

         0              black        white      grey     bright white
         1              black        cyan       red      white
         2              black        green      red      yellow
         3              black        cyan       magenta  white

     Examples:

     The following examples use standard IBM EGA/VGA registers. If more
     information is required, consult the EGA/VGA programmers reference
     list included in this document.


     Segment example for selecting the active palette or color set:

       mov   dx,03dah      ;Load Input Status Register One
                           ;
     wait:
       in    al,dx         ;Wait for vertical retrace bit to be set
       test  al,8          ; (bit 3 = 1)
       jnz   wait          ;It is good practise to wait for the vertical
                           ; retrace bit before directly modifying the
                           ; palette registers

       mov   ah,ARG        ;Arg = color set # (0 to 3)
       mov   cl,4          ;Multiply arg by 8 so that bits 4 & 5 of the
       shl   ah,cl         ; palette registers can be modified
       mov   dx,03c0h      ;Load Palette Control Register
       mov   cx,16         ;16 Palette registers to be modified
       xor   bl,bl         ;Start from 0
                           ;
     repeat:               ;Modify bits 4 & 5 of all 16 palette registers with
       mov   al,bl         ; Arg value (color set #)
       out   dx,al         ;Select palette register
       or    al,ah
       out   dx,al         ;Write modified data to selected palette register
       loop  repeat

       mov   al,20h        ;Restore internal registers access to palette data 
       out   dx,al         ; bit 5 must be zero during palette data writing 
                           ; and one after data writing is complete


     Segment example for selecting Bit Planes to be modified during a
     memory write:

       mov   dx,03c4h      ;Load Sequencer Address Register
       mov   al,2          ;Load index of Map Mask Register
       out   dx,al         ;Select Map Mask Register
       inc   dl
       mov   al,ARG        ;Value to select which bit planes are to be
                           ; modified during a memory write
       out   dx,al         ;Select EGA/VGA planes to be modified


     IBM EGA/VGA Map Mask Register (3C5h, index 2) organization:

       Bits:   0     Controls access to Bit Plane 0
               1     Controls access to Bit Plane 1
               2     Controls access to Bit Plane 2
               3     Controls access to Bit Plane 3
               4-7   Not used

       A bit value of 0 disables access to the corresponding Bit Plane and a
       bit value of 1 enables it.

4.4  SPECIAL NOTES

4.41 NOTE ON EXTENDED REGISTER ADDRESS

     Hard-coding this value is not recommended since it is programmable
     and may be changed in subsequent BIOS releases. The value of
     EXTENDED_REG should be retrieved from the BIOS at location C000:0010h.
     The 'mov dx, EXTENDED_REG statement in the page selecting segment can
     be replaced with code to load the value of EXTENDED_REG from its stored
     location. The registers that need to be saved will depend greatly on
     the particular application:

              push es         ;save registers es and bx
              push bx
              mov  ax,0c000h  ;define storage location of EXTENDED_REG
              mov  es,ax
              mov  bx,10h
              mov  dx,es:[bx] ;get the value of EXTENDED_REG from contents
                              ;of the storage location C000:0010h
              pop  bx         ;restore registers es and bx
              pop  es

4.42 NOTE ON DAC REGISTER PROGRAMMING
     In IBM VGA mode 13h (320x200 - 256 color), each color is controlled by
     a corresponding DAC register. There are a total of 256 18-bit DAC
     registers. Therefore, each DAC register can be assigned a color value
     from 0 (BLACK) to 262,143 (BRIGHT WHITE). The first 16 DAC registers
     have assigned color values that correspond to the 16 colors used in
     mode 12h (640x480 - 16 color).  DAC register zero, which has an
     assigned color value of 0 (BLACK), also controls the color of the
     overscan border. This function is also supported in ATI modes 61, 62,
     63, and 65h. On some analog monitors, a non-BLACK overscan border may
     cause line wrapping at either the top or bottom of the screen image
     due to the video bandwidth required. For this reason, it is not
     recommended to change the color value of this DAC register.

4.43 BIOS FUNCTION SUPPORT

     Many versions of the VGAWONDER do not support certain video BIOS
     function calls in some extended video modes due to EPROM space 
     limitations. Programmers should assume that the following functions
     are not supported in the indicted modes:

              MODE #              BIOS FUNCTION

              61h, 62h, 63h,      ah = 06h - Scroll active page up
              65h, 67h            ah = 07h - Scroll active page down
                                  ah = 09h - Read Character at Cursor
                                  ah = 0ch - Write Dot
                                  ah = 0dh - Read Dot
                                  ah = 0eh - Write TTX

     All extended modes have only one active page regardless of the amount
     of memory installed.

5.0  APPENDIX

5.1  LIST OF SUGGESTED REFERENCES

     TITLE:       Programmer's Guide to the EGA/VGA *
     AUTHOR:      George Sutty and Steve Blair
     PUBLISHER:   Brady Books / Simon and Schuster, Inc.
     DATE:        1988

     TITLE:       Advanced Programmer's Guide to SuperVGAs *
     AUTHOR:      George Sutty and Steve Blair
     PUBLISHER:   Brady Books / Simon and Schuter, Inc.
     DATE:        1990                                 

     TITLE:       Programmer's Guide to IBM PC and PS/2 Video Systems
     AUTHOR:      Richard Wilton
     PUBLISHER:   MicroSoft Press
     DATE:        1987

     TITLE:       Programmer's Guide to the EGA and VGA Cards
     AUTHOR:      Richard F. Ferraro
     PUBLISHER:   Addison - Wesley Publishing Co.
     DATE:        July, 1988

     TITLE:       EGA/VGA A Programmer's Reference Guide
     AUTHOR:      Bradley Dyck Kliewer
     PUBLISHER:   McGraw Hill
     DATE:        1988

     TITLE:       Personal System/2 Model 50 and 60 Technical Reference
     AUTHOR:      unknown
     PUBLISHER:   IBM
     DATE:        April, 1987

     TITLE:       Personal System/2 and Personal Computer BIOS Interface
                  Technical Reference
     AUTHOR:      unknown
     PUBLISHER:   IBM
     DATE:        April, 1987

     TITLE:       Programmer's Reference Manual for the VGAWONDER  *
     AUTHOR:      various                
     PUBLISHER:   ATI Technologies (order from Tech Support $40)
     DATE:        1990
              * recommended


     TO OBTAIN A PRINT COPY OF THIS DOCUMENT ON YOUR SYSTEM
     PRINTER, ENTER THE FOLLOWING COMMAND AT THE DOS PROMPT:

              TYPE PROGINFO.DOC>PRN <rtn>