**** DEMO Copy *** DEMO Copy *** DEMO Copy *** DEMO Copy ****
         *                                                           *
         *        COMET - the Background Communications Library      *
         *                                                           *
         *       by CompuSolve  88 Erie Ave  Rockaway, NJ 07866      *
         *                       (201)983-9429                       *
         *************************************************************

          This manual and associated software for COMET is provided as
         a demonstration/evaluation copy.  It's only limitation is
         that file transfers are limited to 2k (2048 bytes) in size.
         Any file transfer commands encountering a file size that
         exceeds this 2k demo limit will automatically cancel.

         Once you're impressed with COMET's abilities you can order
         COMET directly from CompuSolve by phone (VISA-MC-AMEX) or
         send a check for $99 to receive the latest copy of the
         product and a manual.  Of course we'll remove the 2k limit
         for those of you that order!  COMET is sold ROYALTY FREE so
         the necessary COMET.BIN or linked COMET.OBJ can be included
         with all your applications at no additional cost.


         COMING ATTRACTIONS:

         1) A new product, COMET-MP, will support simultaneous usage of
            upto 5 COM ports.  It will retail for $169.00 ( 20$ upgrade
            charge for COMET owners).
         2) A terminal emulate command with user defineable window coordinates.
         3) Your wishes here ...
























         Table Of Contents

         Introduction ...................................  1
         Installation ...................................  2
         Getting Started ................................  3
         Programming ....................................  4
         Commands .......................................  5,6
           ARECV ........................................  7
           ASEND ........................................  8
           CLOSE ........................................  9
           DTR .......................................... 10
           FCHK ......................................... 11
           FIND ......................................... 12
           FLUSH ........................................ 13
           INPUT ........................................ 14
           MSTAT ........................................ 15
           ONDCD ........................................ 16
           ONDONE ....................................... 17
           ONTIME ....................................... 18
           OPEN ......................................... 19
           OUTPUT ....................................... 20
           RTS .......................................... 21
           RXCNT ........................................ 22
           VERS ......................................... 23
           XRECV ........................................ 24
           XSEND ........................................ 25
           YRECV ........................................ 26
           YSEND ........................................ 27
         Appendix A (Auxilary-Byte Table) ............... A-1
         Appendix B (Clipper Event Trapping Notes) ...... B-1





























         Introduction

         Comet is an add on communications library that is compatible
         with dBASE, Fox, Clipper, dBXL and QuickSilver running on an
         IBM PC or compatible.  COMET adds a powerful set of serial
         COM port functions to these languages.  In addition to
         commands for low level serial input and output , there are
         commands for handling file transfers using either ASCII,
         XMODEM or YMODEM.  One of COMET's most unique and powerful
         features is its ability to perform these file transfers
         entirely in the background.  This allows the main database
         application to run at the same time as files are being
         received or sent.  There are several event trapping commands
         that enable the background process (COMET) to signal the main
         program of important events, such as when a file transfer has
         completed or an incoming modem call gets detected.


         This manual assumes the reader is somewhat familiar with
         serial communications and its terminology (ie. baud rate,
         parity, COM port etc.).  Those not familiar with such terms
         should refer to appropriate books on the subject.  In
         addition, those intending to use modems should refer to
         appropriate documentation regarding the particular modem's
         command language.























         Clipper is the registered trademark of Nantucket, Inc.  dBASE
         is the trademark of Ashton-Tate Corp.  dBXL and QuickSilver
         are trademarks of WordTech Systems, Inc.




                                       1



         Installation:

         There are two versions of COMET included on the diskette.
         One version is for Clipper while the other one is for dBASE,
         Fox, dBXL or QuickSilver. Follow the instructions below for
         your particular database language.


         dBaseIII+, FoxBase+, FoxPro, dBXL or QuickSilver:

          Copy the COMET.BIN file from the supplied diskette to the
          directory containing your particular database's .EXE files.
          This file gets LOADed by the  application program generally
          as part of it's startup section (see your database's
          description of the LOAD command).



         CLIPPER:

          Copy the file named COMET.OBJ to your object module
          directory.  To use COMET with any programs compiled in
          Clipper, the link procedure must specify COMET.OBJ as an
          additional object module.


          An example of a PLINK86 .LNK  file:

            OUTPUT MYPROG.EXE
            FI MYPROG.OBJ
            FI COMET.OBJ
            LIB CLIPPER EXTEND


         FILES INCLUDED ON DISKETTE:

         COMET.BIN     - Library for dBASE, Fox, dBXL & QckSlvr
         COMET.OBJ     - Libary for Clipper
         TRM_D3FX.PRG  - Sample program for dBASE, Fox ...
         TRM_CLIP.PRG  - Sample program for Clipper
         READ.ME       - If present, contains release notes














                                       2



         Getting Started

         While COMET is primarily intended for use within a database
         program, it will also work from the dot prompt of any of the
         database languages (except for Clipper which has no dot
         prompt mode).  In fact, experimenting from the dot prompt is
         one of the fastest and easiest ways to get familiar with
         COMET before attempting to write program code.  The following
         few lines demonstrate how to OPEN a COM port (COM1) with a
         Hayes compatible modem attached, then have the modem dial a
         number:

         . LOAD COMET
         . OpenCmd = 'OPEN COM1:2400,N,8,1,N'
         . CALL COMET WITH OpenCmd
         . Dial = 'OUTPUT ATDT123-4567' + CHR(13)
         . CALL COMET WITH Dial

         Now we'll CLOSE COM1 and force modem to disconnect:

         . Close = 'CLOSE'
         . CALL COMET WITH Close
         . QUIT

























         NOTE:
         It is extemely important that a OPENed COM port be CLOSED
         prior to exiting the database language.  Failure to do so
         will most likely result in a system lockup or crash. See OPEN
         and CLOSE commands for additional information.


                                       3



         Programming

         After experimenting with COMET from the dot prompt, the next
         step is to actually write some program code using the COMET
         library commands.  In addition to the command reference
         section of this manual which contains example code, a sample
         program can be found on the COMET diskette.  This program is
         a simple terminal emulation program that supports sending or
         receiving of files using any of the COMET supported
         protocols.  Examining a printout of the sample program is
         well worth the time spent since most COMET commands are used
         in this example. There are two versions of the sample program
         on the diskette:

         TRM_FXD3.PRG - for dBASE, Fox, dBXL or QuickSilver

         TRM_CLIP.PRG - for Clipper






































                                       4



         Commands

         The following section of this manual describes COMET's
         command set.  All of the commands are invoked by using the
         CALL ... WITH command syntax supported by each database
         language.

         The basic format of the CALL statement is:

         CALL COMET WITH <expC>

         <expC> is a character expression consisting of two parts. The
         first part of <expC> is always the name of the COMET command
         to be performed (ie. OPEN, INPUT etc.).  The second part of
         <expC> is used to pass parameters to COMET.  If parameters
         are specified, a space character must separate the two parts.
         Additionally, if a command is supposed to return anything,
         COMET will modify the second part of <expC> as a means of
         returning values or data to the database program.  Note that
         COMET will never change the length of <expC>, only the
         contents.  If <expC> is too short to contain a result, COMET
         will truncate the result.   The <expC> should always be a
         variable rather than a constant since the latter cannot be
         examined for results returned by COMET.  If COMET is passed
         an invalid command name or parameter, then the first
         character of <expC> will be modified to a question mark
         character, overwriting the first character of the command
         name.  Similarly, if a command name is valid but can't be
          performed at that time, a minus sign will replace the first
         character of <expC>.  A typical program might have a single
         UDF or procedure to handle all CALLs to COMET.  In that case
         the routine should always check the first character of <expC>
         after CALLing COMET to check for any errors.






















                                       5



         COMMAND REFERENCE FORMAT:

         The following describes notation conventions used throughout
         the command reference section of this manual.

         ENTRY: - Specifies the required format of the character
         expression to be passed for a particular command.


         <expC> - The character expression that must be passed
         following the WITH clause of the CALL statement.  This
         character expression is usually a variable rather than a
         constant so that data or error messages from COMET can be
         retrieved.


         [ ]    - Indicates an optional item.  Brackets should not be
         entered as part of <expC>.


         RETURN: - Specifies the content of the character expression
         after the command returns to the database program.

            _    - The underscore character indicates that a space
         character is to occupy that position in <expC>.  The
         underscore itself is not to be included in <expC>.





























                                       6



         COMMAND: ARECV

         ENTRY:
         <expC> = "ARECV_filespec[,timeout]"

         filespec = complete DOS path\filename
         timeout  = # seconds before auto-close (0 - 3600)

         RETURN:
         <expC> = unchanged

         PURPOSE:
         Used to begin capturing of incoming COM port data into
         specified file.  The optional timeout parameter specifies the
         duration of receiver inactivity that will force the file to
         automatically close.  The default timeout is 60 seconds.
         Specify a value of 0 to disable auto-close feature.  Other
         than a timeout, there are two other ways the file can be
         closed; if a DOS End-Of-File (EOF = 1Ah = 26d) character is
         received or COMET's FLUSH command gets executed.  When
         capturing is in progress the COM port data can also be read
         from the receive buffer using the INPUT command.  Since ARECV
         operates in the background,  its status can be determined by
         doing a FCHK command.


         EXAMPLE:
         RecvCmd = 'ARECV \MYDIR\MYFILE.RCV'
         CALL COMET WITH RecvCmd
         ? 'File is being received now'

























                                       7



         COMMAND: ASEND

         ENTRY:
         <expC> = "ASEND_filespec"

           filespec = complete DOS path\filename

         RETURN:
         <expC> = unchanged

         PURPOSE:
         Used to begin transmission of a file through the COM port.
         Although this command is normally used to send ASCII rather
         than binary files, all characters will be sent including
         control characters.  It is the size of the file that
         determines when ASEND completes.  Since this command works in
         the background, use FCHK to determine the status of the
         transmission.  To cancel ASEND at any time, issue a FLUSH
         command.


         EXAMPLE:
         SendCmd = 'SEND \MYDIR\MYFILE'
         CALL COMET WITH SendCmd
         ? 'File is being sent now'






























                                       8



         COMMAND: CLOSE

         ENTRY:
         <expC> = "CLOSE"

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To shut down the currently OPENed COM port. After issuing
         this command no further COM port data can be sent or
         received.  In addition to disabling serial interrupts, the
         TSR features of COMET are disabled by removing the "hook" to
         the system timer interrupt that was enabled by the OPEN
         command. This command must be performed prior to exiting the
         database language, otherwise a system crash is likely to
         occur.


         EXAMPLE:
         Flsh = 'FLUSH'
         CALL COMET WITH Flsh
         Clos = 'CLOSE'
         CALL COMET WITH Clos


         NOTE: This command will not be executed if any file transfer
         is in progress.  Therefore it is recommended that a FLUSH
         command always precede a CLOSE.


























                                       9



         COMMAND: DTR

         ENTRY:
         <expC> = "DTR_n"

          n = 0  or  1

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To set the state of the COM port's Data Terminal Ready (DTR)
         output signal. Specify 1 to set the signal active, 0 to
         disable.  By default, the signal will be at an active (1)
         state after the COM port is OPENed.  Data Terminal Ready is
         output from the PC's serial COM port to whatever device is
         attached to the port.  If a modem is attached,  this signal
         is normally required to be at an active (1) state before the
         modem will respond to any commands it receives.  Furthermore
         most modems will automatically disconnect from the telephone
         line if Data Terminal Ready should change from a 1 to a 0
         state during a call.  With modems then, the DTR command is a
         simple way to disconnect or hangup.


         EXAMPLE:
         DTROn = 'DTR 1'
         DTROff = 'DTR 0'
         CALL COMET WITH DTROn   && Set DTR active
         CALL COMET WITH DTROff  && Now, turn DTR off


         NOTE:  Some modems have a dip switch or configuration setting
         that can override the Data Terminal Ready disconnect feature.
         Consult your modem's manual for details.




















                                       10



         COMMAND: FCHK

         ENTRY:
         <expC> = "FCHK________________"

         RETURN:
         <expC> = "FCHK_prot_dir_stat_size_file[_fail]"

                                               (start, len)
           prot = ASCII_, XMODEM or YMODEM        ( 6, 6)
           dir  = RECEIVE_ or TRANSMIT            (13, 8)
           stat = ACTIVE__, COMPLETE or FAILED__  (22, 8)
           size = ####### (bytes rec'd or sent)   (31, 7)
           file = path\name of file               (39, ?)
           fail = CANCELED, DATA ERRORS, FILE: OPEN READ,
                  FILE: WRITE, or TIMEOUT

         PURPOSE:
         To determine the status of the last file transfer command
         issued.  One use for FCHK would be when you want to
         periodically update the screen with information on a file
         transfer that is currently executing.  Used in conjunction
         with the ONTIME command, it is possible to automatically do a
         procedure that displays current FCHK values every so often.
         If the stat is FAILED, the failure type will be returned in
         fail (the brackets are returned too).

         EXAMPLE:
         StatCmd = 'FCHK' + SPACE(80) && Spaces get overwritten
         CALL COMET WITH StatCmd
         Stus = SUBSTR(StatCmd,22,8)   && Extract status
         Cnt =  SUBSTR(Statcmd,31,7)   && Extract byte count
         Last2 = SUBSTR(StatCmd,39)    && File name + fail msg
         SpcAt = AT(' ',Last2)
         FName = SUBSTR(Last2,SpcAt-1) && Now we have file name
         @ 24,0 SAY 'File:' + FName
         @ 24,15 SAY 'Status: ' + Stus
         @ 24,30 SAY '# Bytes: ' + Cnt












         NOTE: FCHK will return <expC> = 'IDLE' if either no file
         transfer is pending or the previous status returned was
     COMPLETE or FAILED .


                                    11



         COMMAND: FIND

         ENTRY:
         <expC> = "FIND_string"

           string = character(s) to find

         RETURN:
         <expC> = "FIND?string"

           ? = plus sign(+) if string found; space if string not found

         PURPOSE:
         To search COMET's receive buffer for a character string.  If
         string is found, a plus sign character will be returned in
         place of the space following FIND in <expC> and the buffer
         pointer will advance to the first character of string so that
         the next time the INPUT command executes, it will return
         string.  If string can't be found, <expC> will remain
         unaltered so that the FIND command can be CALLed repetitively
         until string is found.


         EXAMPLE:

         FindCmd = 'FIND User ID:'
         DO WHILE .NOT. '+' $ FindCmd   && Loop till found
          CALL COMET WITH FindCmd
         ENDDO
         ? 'The text "User ID:" has been found'






















     NOTE:  This command is case sensitive.


                                    12



         COMMAND: FLUSH

         ENTRY:
         <expC> = "FLUSH"

         RETURN:
         <expC> = unchanged

         PURPOSE:
         This command performs several actions.  First, it always
         empties out the COM port receive buffer and clears any paused
         condition due to flow control.  Secondly, if any type of file
         transfer is in progress, it gets canceled.  FCHK will report
         the status as CANCELED in this instance.  As a precaution, a
         FLUSH command should always precede a CLOSE.


         EXAMPLE:

         Flsh = 'FLUSH'
         CALL COMET WITH Flsh


































                                       13



         COMMAND: INPUT

         ENTRY:
         <expC> = "INPUT_t________________"

           t = input termination character

         RETURN:
         <expC> = "INPUT_tnnnndd .. d"

           nnnn   = # data bytes being returned
           dd ..d = COM port data bytes

         PURPOSE:
         To read any previously unread COM port data from the receive
         buffer.  The amount of data returned is dependent on the
         input termination character and the length of <expC>.  This
         command essentially copies data from the receive buffer to
         the <expC> variable until either:

          1) The end of <expC> is encountered
          2) The input termination character is copied
          3) There is no more data in receive buffer

         The maximum number of data chars returned is calculated as:
         LEN(expC) - 11   since 11 chars are used for command name
         and parameters.


         EXAMPLE:

         RdInp = 'INPUT ' + CHR(13) + SPACE(81)  && Term = CR
         CALL COMET WITH RdInp
         Cnt = VAL(SUBSTR(RdInp,8,4)  && Get # bytes returned
         IF Cnt > 0
          ? SUBSTR(RdInp,12,Cnt)  && Print buffer data
         ENDIF














         NOTE: Null characters (0) are stored in <expC> as CHR(255)
     since they are reserved by most database languages to mark
         the end of a character variable or constant.

                                    14



         COMMAND: MSTAT

         ENTRY:
         <expC> = "MSTAT______________________"

         RETURN:
         <expC> = "MSTAT ?DCD ?RI ?DSR ?CTS"

           ? =  plus sign (+) if active, minus sign (-) if inactive

         PURPOSE:
         To determine the state of the four modem status input signals
         at the OPENed COM port.  The command always returns the four
         signal abbreviations with each one preceded by either a plus
         or minus sign to indicate active or not.  This command can be
         called repetitively to poll the port's status for a desired
         state, such as to detect when a modem has connected with
         another modem by waiting for "+DCD" to occur.

         SIGNALS:
          DCD - Data Carrier Detect
          RI  - Ring Indicator
          DSR - Data Set Ready
          CTS - Clear To Send

         EXAMPLE:

         MdemStat = 'MSTAT' + SPACE(21)
         DO WHILE .NOT. '+DCD' $ MdemStat  && Wait for carrier
           CALL COMET WITH MdemStat
         ENDDO
         ? 'Data Carrier Detect is active now'


















         NOTE:  <expC> must be at least 26 characters in length
         otherwise COMET will return a minus sign as first character
     in <expC> indicating an error.


                                    15



         COMMAND: ONDCD

         ENTRY:
         <expC> = "ONDCD_a,x"

           a = key's Ascii code.
               Specify 0 if key has no ASCII value (ie. F1)
           x = key's auXilary-byte value (see appendix A-1).
               Specify 0 if key has an ASCII value.

         RETURN:
         <expC> = unchanged

         PURPOSE:
         This command instructs COMET's background process to signal
         the database program whenever a change in the Data Carrier
         Detect (DCD) input signal occurs.  COMET does this by writing
         the ASCII and auxilary bytes values specified directly into
         DOS's keyboard buffer.  To force the database program to
         execute a specific procedure in response to the DCD event,
         the program should have previously set up an appropriate key
         trap command (ie. ON ESCAPE, ON KEY n, or SET KEY n).

         EXAMPLE:
         ********* Clipper example code ********************
         * Tell Clipper to DO DCDProc if F10 key entered
         SET KEY -9 TO DCDProc
         * Have COMET simulate F10 if DCD changes
         DCDCmd = 'ONDCD 0,68'  && ASCII & Aux-Byte for F10
         CALL COMET WITH DCDCmd

         ******** dBASE, Fox, dBXL or QuickSilver ***********
         ON ESCAPE DO DCDProc
         SET ESCAPE ON
         * Have COMET simulate ESC key if DCD changes
         DCDCmd = 'ONDCD 27,1'
         CALL COMET WITH DCDCmd

         * main application code goes here
         PROCEDURE DCDProc
         COMStat = 'MSTAT' + SPACE(21)
         CALL COMET WITH COMStat  && Chk if DCD + or -
         IF '+DCD' $ COMStat
          DO HaveDCD  && A proc that might do file transfers
         ELSE
          DO LostDCD  && A Proc that deals with disconnects
         ENDIF
         RETURN

         NOTE: To disable DCD event trapping don't specify any
         parameters (ie. <expC> = "ONDCD") .

     CLIPPER USERS: See notes in appendix B


                                    16



         COMMAND: ONDONE

         ENTRY:
         <expC> = "ONDONE_a,x"

           a = key's Ascii code.
               Specify 0 if key has no ASCII value (ie. F1)

           x = key's auXilary-byte value (see appendix A-1).
               Specify 0 if key has an ASCII value.

         RETURN:
         <expC> = unchanged

         PURPOSE:
         This command instructs COMET's background process to signal
         the database program whenever a file transfer command is
         done. COMET does this by writing the ASCII and auxilary bytes
         values specified directly into DOS's keyboard buffer.  To
         force the database program to execute a specific procedure
         when a file transfer command is done, the program should have
         previously set up an appropriate key trap command (ie. ON
         ESCAPE, ON KEY n, or SET KEY n).

         EXAMPLE:

         ********* Clipper example code ********************
         * Tell Clipper to DO DoneProc if S/F10 entered
         SET KEY -19 TO DoneProc
         * Have COMET simulate S/F10 upon file completion
         DoneCmd = 'ONDONE 0,93'  && ASCII & Aux-Byte for S/F10
         CALL COMET WITH DoneCmd

         ******** dBASE, Fox, dBXL or QuickSilver ***********
         ON ESCAPE DO DoneProc
         SET ESCAPE ON
         * Have COMET simulate ESC key upon file completion
         DoneCmd = 'ONDONE 27,1'
         CALL COMET WITH DoneCmd
         *
         * main application code goes here
         *
         PROCEDURE DoneProc
         * Let's disconnect after file transfer is done
         HangUp = 'DTR 0'
         CALL COMET WITH HangUp  && Modem disconnect
         RETURN


         NOTE: To disable DONE event trapping, don't specify any
         parameters (ie. <expC> = "ONDONE").  Any status other than
         ACTIVE is considered done.
      CLIPPER USERS:  See notes in appendix B


                                   17



         COMMAND: ONTIME

         ENTRY:
         <expC> = "ONTIME_t.a,x"

           t = time interval in seconds between events

           a = key's Ascii code.
               Specify 0 if key has no ASCII value (ie. F1)

           x = key's auXilary-byte value (see appendix A-1).
               Specify 0 if key has an ASCII value.

         RETURN:
         <expC> = unchanged

         PURPOSE:
         This command instructs COMET's background process to signal
         the database program every t seconds.  COMET does this by
         writing the ASCII and auxilary bytes values specified
         directly into DOS's keyboard buffer.  To force the database
         program to execute a specific procedure every t seconds, the
         program should have previously set up an appropriate key trap
         command (ie.  ON ESCAPE, ON KEY n, or SET KEY n).

         EXAMPLE:
         ********* Clipper example code ********************
         * Tell Clipper to DO TimeProc if S/F10 entered
         SET KEY -19 TO TimeProc
         * Have COMET simulate S/F10 every 5 seconds
         TimeCmd = 'ONTIME 5,0,93'  && ASCII & Aux-Byte for S/F10
         CALL COMET WITH TimeCmd

         ******** dBASE, Fox, dBXL or QuickSilver ***********
         ON ESCAPE DO TimeProc
         SET ESCAPE ON
         * Have COMET simulate ESC key upon file completion
         TimeCmd = 'ONTIME 5,27,1'
         CALL COMET WITH TimeCmd
         *
         * main application code goes here
         *
         PROCEDURE TimeProc
         *
         * This procedure will execute every 5 seconds
         *
         RETURN


         NOTE: To disable TIME event trapping, don't specify any
         parameters (ie. <expC> = "ONTIME").

     CLIPPER USERS: See notes in appendix B


                                    18



         COMMAND: OPEN

         ENTRY:
         <expC> = "OPEN_COMn:b,p,d,s[,f]"

           n = com port # to open ( 1 - 4)
           b = baud rate (300 - 38400)
           p = parity None, Even or Odd (N, E or O)
           d = # data bits (7 or 8)
           s = # stop bits (1 or 2)
           f = flow control; Xon/Xoff, Rts/cts, or None (X, R or N)

         PURPOSE:
         To activate the desired COM port.  This command must be
         performed prior to any other COMET command since a COM port
         needs to be initialized before using.  OPENing a COM port
         enables that port's serial interrupts.  Also, this command
         makes COMET behave like a Terminate but Stay Resident (TSR)
         program by setting an interrupt "hook" into the system timer
         thereby allowing COMET to work in the background.  Prior to
         exiting, FLUSH and CLOSE commands should be performed.
         Exiting or QUITing the database language while a COM port is
         still OPEN will most likely result in a system crash.

         INTERRUPTS:
         COMET uses the following interrupt structure:

           COM1         - IRQ4 (Interrupt 0Ch)
           COM2,3 or 4  - IRQ3 (Interrupt 0Bh)

         Set any interrupt switches on your serial COM port card to
         the appropriate value.


         EXAMPLE:

         * Let's OPEN COM1 at 2400 baud, no parity, 8 data
         * bits, 1 stop bit and no flow control.
         OpenCmd = 'OPEN COM1:2400,N,8,1,N'
         CALL COMET WITH OpenCmd
         * COM1 now ready for use







         NOTE:  Only 1 COM port can be OPENed at any given time.
         Attempting to OPEN a COM port other than the currently opened
         port, will result in a command rejection error indicated by COMET
         overwriting the first character of <expC>, "O", with a minus sign.



                                    19



         COMMAND: OUTPUT

         ENTRY:
         <expC> = "OUTPUT_string"

           string = character(s) to output

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To output character(s) to the serial COM port.  This command
         does not return until all characters in string have been
         output.  If XON/XOFF or RTS/CTS flow control was specified
         and output has been paused, this command will wait for a XON
         character or CTS to go true.


         EXAMPLE:

         * Let's output a dial command to Hayes type modem
         OUTCmd = 'OUTPUT ATDT(111)222-3333' + CHR(13)
         CALL COMET WITH OUTCmd



























         NOTE: A null (binary 0) character can't be part of <expC>
         since its reserved to indicate or mark the end of character
         strings in the database environment.  To have COMET output a
         null, code it into <expC> as a CHR(255) which will get
         translated to a null at output time.
                                       20




         COMMAND: RTS

         ENTRY:
         <expC> = "RTS_n"

           n = 0 or 1

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To set the state of the COM port's Request To Send (RTS)
         output siganl.  This signal is set active (1) by default as
         soon as the COM port gets OPENed.  RTS can also change states
         if RTS/CTS handshaking was specified in the OPEN command and
         the receive buffer approaches 80% full (RTS goes to 0).
         Likewise, if RTS has gone to a 0 state, as the buffer reaches
         20% capacity the RTS signal will go active (1).  The buffers
         capacity is 3072 characters.



         EXAMPLE:

         RTSOn = 'RTS 1'
         RTSOff = 'RTS 0'
         CALL COMET WITH RTSOn  && Set RTS active/on
         CALL COMET WITH RTSOff && Turn RTS off



























                                       21


         COMMAND: RXCNT

         ENTRY:
         <expC> = "RXCNT______"

         RETURN:
         <expC> = "RXCNT_n"

           n = # bytes in receive buffer (0 - 3072)

         PURPOSE:
         To determine how many characters are pending in the receive
         buffer.  The capacity of this buffer is 3072 characters (3k).
         No leading zeroes or spaces are returned for n.


         EXAMPLE:

         GetCnt = "RXCNT" + SPACE(5)
         CALL COMET WITH GetCnt
         TheCnt = VAL(SUBSTR(GetCnt,7))


































                                       22



         COMMAND: VERS

         ENTRY:
         <expC> = "VERS_____"

         RETURN:
         <expC> = "VERS_#.##"

         PURPOSE:
         To get the version and revision level of the COMET library in
         use.


         EXAMPLE:
         Ver = 'VERS      '
         CALL COMET WITH Ver
         ? 'COMET version in use is ' + Ver






































                                       23



         COMMAND: XRECV

         ENTRY:
         <expC> = "XRECV_filespec"

           filespec = complete DOS path\filename

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To start receiving a file using the XMODEM protocol.  XMODEM,
         using CRC error detection, is always requested from the
         sender.  Should the sender not support CRC, this command will
         fall back to the less reliable checksum method of error
         detection.  Since XRECV operates in the background, use FCHK
         to determine the status of the file transfer at any time.


         EXAMPLE:
         XmdmRecv = 'XRECV C:\MYDIR\MYFILE.EXT'
         CALL COMET WITH XmdmRecv    && Begin receiving file
         *
         * Any code here executes at the same time as file is being
         received
         *





























                                       24



         COMMAND: XSEND

         ENTRY:
         <expC> = "XSEND_filespec"

           filespec = complete DOS path\filename

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To begin sending of a file using the XMODEM protocol.   This
         command supports both CRC and checksum methods of error
         detection.  The method used will depend on what the receiver
         requests at the start of the file transfer.  Since this
         command operates in the background, use FCHK to obtain the
         file transfer status at any time.


         EXAMPLE:

         XmdmSnd = 'XSEND \MYDIR\MYFILE.EXT'
         CALL COMET WITH XmdmSnd
         *
         * Any code here executes while file is sent
         *





























                                       25



         COMMAND: YRECV

         ENTRY:
         <expC> = "YRECV"

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To begin receiving of a file or group of files using the
         YMODEM batch protocol.  No filename is required as the YMODEM
         batch protocol includes a filename along with data for each
         file received.  Any files received will be written to the
         current directory.  Using YMODEM batch is superior to XMODEM
         for several reasons.  First, the block size is 1024 bytes in
         YMODEM versus 128 in XMODEM.  This larger block size yields a
         greater transfer rate than XMODEM.  Secondly, YMODEM batch
         allows the use of DOS wildcard characters in the filespec
         parameter.  This means a group of files can be received with
         one YRECV command, provided that the sender requested
         multiple files.  Since this command operates in the
         background, use FCHK to determine the file transfer status at
         any time.


         EXAMPLE:

         YmdmRecv = 'YRECV'
         CALL COMET WITH YmdmRecv  && Begin receiving file(s)
         *
         * Any code here executes while file(s) are received
         *



















         NOTE: If the sender is using some type of a communications
         package such as XTALK or ProCom, make sure it is configured
         for and supports the YMODEM batch protocol.  Some packages
         claim YMODEM capability, yet don't support the batch version.
                                       26



         COMMAND: YSEND

         ENTRY:
         <expC> = "YSEND_filespec"

           filespec = DOS path\filespec

         RETURN:
         <expC> = unchanged

         PURPOSE:
         To begin sending a file or group of files using the YMODEM
         batch protocol.  The filespec parameter can include wildcard
         characters so that more than one file can be sent within a
         single command.  Since this command operates in the
         background, use FCHK to obtain the file transfer status at
         any time.

         EXAMPLE:

         YmdmSnd = 'YSEND \MYDIR\*.DBF'
         CALL COMET WITH YmdmSnd   && Send all files with DBF
         extension
         *
         * Any code here executes during file send(s)
         *





























                                       27



                              Auxilary-Byte Table
                             ---------------------

         Value  Key            Value  Key            Value  Key
         -----  -------        -----  -------        -----  ---------
         59     F1             110    Alt-F7         44     Alt-Z
         60     F2             111    Alt-F8         45     Alt-X
         61     F3             112    Alt-F9         46     Alt-C
         62     F4             113    Alt-F10        47     Alt-V
         63     F5                                   48     Alt-B
         64     F6             120    Alt-1          49     Alt-N
         65     F7             121    Alt-2          50     Alt-M
         66     F8             122    Alt-3
         67     F9             123    Alt-4          15     Shift-Tab
         68     F10            124    Alt-5
                               125    Alt-6          71     Home
         84     Shift-F1       126    Alt-7          72     Up Arr
         85     Shift-F2       127    Alt-8          73     PgUp
         86     Shift-F3       128    Alt-9
         87     Shift-F4       129    Alt-0          75     Left Arr
         88     Shift-F5       130    Alt-Hyphen
         89     Shift-F6       131    Alt-=          77     Right Arr
         90     Shift-F7
         91     Shift-F8       16     Alt-Q          79     End
         92     Shift-F9       17     Alt-W          80     Down Arr
         93     Shift-F10      18     Alt-E          81     PgDn
                               19     Alt-R          82     Insert
         94     Ctrl-F1        20     Alt-T          83     Delete
         95     Ctrl-F2        21     Alt-Y
         96     Ctrl-F3        22     Alt-U          114    Ctrl-PrtSc
         97     Ctrl-F4        23     Alt-I          115    Ctrl-Lft
         98     Ctrl-F5        24     Alt-O          116    Ctrl-Rgt
         99     Ctrl-F6        25     Alt-P          117    Ctrl-End
         100    Ctrl-F7                              118    Ctrl-PgDn
         101    Ctrl-F8        30     Alt-A          119    Ctrl-Home
         102    Ctrl-F9        31     Alt-S
         103    Ctrl-F10       32     Alt-D          132    Ctrl-PgUp
                               33     Alt-F
         104    Alt-F1         34     Alt-G
         105    Alt-F2         35     Alt-H
         106    Alt-F3         36     Alt-J
         107    Alt-F4         37     Alt-K
         108    Alt-F5         38     Alt-L
         109    Alt-F6











                                      A-1



         CLIPPER EVENT TRAPPING

         Using Clipper's SET KEY n TO procedure command in conjunction
         with any of COMET's event trapping commands may produce some
         undesirable side effects.  The problem becomes evident when
         an ONDCD, ONDONE or ONTIME event occurs during a full screen
         READ operation.  Clipper detects the keyboard character
         produced by the ONxxxx event and branches to the SET KEY
         procedure without a problem.  However, upon RETURNing to the
         READ's active GET field, the cursor position always gets
         forced to the field's leftmost (home) position. The cursor
         would appear to suddenly jump every time an event occurred.
         It is recommended that the following code be put inside the
         SET KEY procedure to alleviate this problem. It takes
         advantage of the READVAR() parameter that is automatically
         passed to any SET KEY procedure.

         PROCEDURE WhatEver
         PARAMETERS Proc, Line, Var     && Automatically passed
         *
         * Place desired event code here
         *

         * Cursor fix code
         IF LEN(Var) > 0               && Is a GET/READ in effect ?
            PosnInGet = LEN(&Var)      && Determine position
            * Stuff right arr's to restore this position
            KEYBOARD REPLICATE(CHR(4), PosInGet)
         ENDIF

         RETURN                        && Exit SET KEY procedure
























                                      B-1