BOOTID

Purpose: Identify a diskette's boot sector type ("hashcode")

Usage:  BOOTID [drive]

Options: (none)

Parameters: drive - the diskette drive to test (default is A:)

What It Does:
Use BOOTID to check the boot sector of DOS diskettes, to produce a 12-byte
hashed identifier string based on the contents of the diskette's first sector.
This boot code can be used to look up a table of known boot sectors (look at
the "CHECKOUT" program if you want a program with an automatic lookup facility
and other nice features).  The aim is to produce an identifying code for each
virus (or good) boot sector. However, the code produced is reasonably useful in
itself (read: not a foolproof test) for spotting boot sector infectors and some
non-DOS (or incompatible DOS) diskettes.

Interpretting the Hash Code:
The general format is always a "#" followed by 7 alphanumeric characters, then
a "." then three more alphanumeric characters.  Notice this makes a valid DOS
filename. The character positions have special significance...

      # a b b b b c d . e f g
where:
      a - indicates the size of the first jump instruction, which should be
          "3" or "4" normally ("2" might be okay, "0" is probably a virus).
          This is the top nibble of the second byte. It comes straight after
          the "#" simply to aid in sorting hashcodes in lists; it tends to
          increase slightly with version of operating system. Very early DOS
          versions may have anything here - even DG10 MSDOS 2.1 has a zero,
          but nowadays anything below "2" is worring (the stoned virus always
          has "0", but so do stoned-immunised diskettes). High numbers also
          are rare (suspicious).
      b - Four bytes that vary seemingly randomly from diskette to diskette;
          they should be the same for identical diskettes (but vary with date
          of release of operating systems, or variants of virus). You can't
          tell anything simply by looking at these bytes (except, perhaps, in
          the case of one version of the Stoned virus), there is not meant to
          be any "trend" where larger values mean anything - its just a hash
          code (as used in data access algorithms).
      c - Another seemingly-random byte. What's the difference? See later!
      d - A check digit. The bottom 3 bits are based on the contents of other
          characters in the code, multiplied by their place in the code. That
          should be enough to spot 88% of the typos.  The top bits represent
          the major version of the program (presently 2, and unlikely to change
          too often).  By the way, when I talk about bits, I mean the unencoded
          byte "behind" the character you see - 0 -> "0", 9->"0", 10->"A", and
          so on up to "Z" (a lot like hexadecimal, isn't it!)
      e - The "Good Flags" - you want as many bits on as possible, so "0" means
          a non-DOS disk, possibly a virus, possibly even an early DOS version,
          but definately strange (no Bios Parameter Block, no AA55 signature,
          and so on. See the source).
      f - The "miscellaneous" byte. The bottom bit indicates an int 13h, the
          next bit indicates the first few bytes are the characteristic Stoned
          virus signature - used both by real viruses and diskettes pretending
          to have already (so they don't get infected). The rest of the bits
          indicate how many non-program bytes were found (small numbers may
          mean complex virus programs, or self-modifying code, etc.)
      g - The "Bad Flags" - normally "0", but in a few cases good diskettes may
          have some flags set here.

Hash Coding Method:
See the source program for the grubby details. The idea is to come up with a
number that is hard to duplicate, both accidentally and in case a virus writer
tries to change bytes in a bad disk to give it the same hash code as some good
disk. The generating function is non-analyitic, and if someone tries every
combination of several bytes, it will take a long time (of the order of 1000
double-precision calculations per iteration), and even then, the "c" byte makes
it harder, since almost-randomly any byte in the boot sector may be used in the
calculation (so anone going through months of combinations may find he'd been
trying a combination of bytes that could never give the desired result). Still,
I don't expect people to try this much, since the code is aimed at identifying
viruses once they've been spotted - and at least one program, ScanBoot, carries
out MUCH greater tests before passing a diskette. A Brief explanation of the
hashing method is:

(1)  working from low to high byte, multiply your CheckTerm by itself xor'ed with
     the new byte, adding the result to the total.
(2)  Use this (temporary) result to calculate which bytes in the sector will
     be used to produce the "c" byte.
(3)  Now repeat (1) but work from high to low memory. This makes extra work for
     virus writers, but not too much for us. Using both directions means virus
     writers can't simply calculate a partial result to save time in each loop.
     (Don't worry if some of the details make little sense; they are relatively
     insignificant to the whole picture, and migt even drop of one day with a
     resounding tinkle :-).

Example:

BootID A:

Read This:
You are free to use BOOTID, distribute it unmodified and non-commercially, use
the source code in your non-commercial programs... I would like to hear of any
modifications, and successes, and please don't distribute modifications under
the same name!  Anyone wanting to use the program commercially are almost as
free to do so - all I ask is that you tell me that you're using it and put in
a reasonable acknowledgement. Remember, this is a relatively early version.
Expect the odd bug or loophole. Do coordinate suggested changes with me via
either e-mail or snail-mail to me, or Software & Support (who'll send you the
latest copy for just the cost of the post & packing). Please don't ask me to
send diskettes.

 Author: Mark Aitchison (E-mail: M.Aitchison@csc.canterbury.ac.nz)
                        (Post:   61 Longfellow Street, Christchurch 2, N.Z.
                         or:     Physics Dept, University of Canterbury, N.Z.
 You can also obtain copies of the latest version from:
     anonymous ftp access to 132.181.30.3 (canterbury.ac.nz)
     or send $20-or-whatever-you-think-will-cover-the-postage to:
          Software & Support,
          P.O. Box 12-292, Christchurch,
          New Zealand

More Notes:
* The program only works with diskettes.
* Options and parameters may be capitals or lower case or a mixture.
* Options may begin with a "/" or a " -", followed by the option name (which
  can be abbreviated to its initial letter) and normally come after the
  keyword (BOOTCODE) but before any parameters, e.g.
   BOOTCODE /V /D /L $3CRQCEN.6V0
* However, the system is flexible enough to handle something like:
   BootCode/V/d $3cRQcen.6v0 -Lpt
* If you specify the /M option and an entry already exists for this type of
  diskette, that entry will be displayed, otherwise one will be created (so
  long as the /BOOTDB directory exists), and you will need to supply a brief
  description of the type of diskette.
* This program does NOT CLAIM to be able to spot all boot sector viruses; it
  certainly spots the stupid old ones like the stoned virus, but is really
  aimed at identifying a diskette - perhaps after another program (such as
  SCANBOOT) has shown it as having a virus.
* The system of file naming is compatible with the BOOTINFO program, that can
  perform a much more thorough test of your diskette.
* If you have Digital Research's DOS 5.0 it is a good idea to password-protect
  the bootdb directory and it's files from writing or deletion. You will then
  need to supply a password when using the /M option (e.g. BOOTCODE/M/P=sfish).
* The format of BootCodes are as follows...

              #3CRQCEN.6V0
Always "#"___/ |       | \\___If the last sector is nonzero, it might be a virus!
Initial jump___|        \ \___Normally about 9; may be "#" if all bytes same (CPM)
                         \____Bit flags for "good" features, shouldn't be 0

The rest of the bytes can be thought of as essentially an encryption of the
contents (other than the Bios Parameter Block), which is generally a unique
number for each boot sector program.

(shesk! 150 lines! This documentation's almost as big as the program!)