FBN Software proudly presents Network. Network is an analysis tool used to 
perform  an AC spectral analysis of an electrical network. The program does 
this by using Kirchoff's laws to solve for the network node voltages and 
currents.

What can I use Network for? Its primary application is to obtain the frequency 
response of an electrical network. It can be used to analyze active and 
passive filter implementations. It is a mini SPICE program without all of the 
bells and whistles. With NETWORK you can prototype a circuit on your computer 
and obtain insight on the actual operation of the real electrical network. You 
can vary parameter values and determine their effect on the network's 
performance.

Network presently allows a maximum of 30 NODES. All node voltages are 
referenced to NODE 0 (electrical ground). The following components can be used 
in the circuit : Resistors (60 max.), Capcacitors (60 max.), Inductors (60 
max.), Amplifiers (10 max.), FET's (30 max.), and Transistors (30 max.).

Included on the disk is a sample network that has been saved to disk : 
TEMP.DTA. This is a 4 node bandpass active filter made up of the following 
components :                               
                                        C1 - 0.1

                            ---------------| |-----------------
                           |                       R2 - 10k   |
                           |                                  |
                           |              --------/\/\/\/\-----
                           |              |                   |
                           |    C2 - 10   |    | .            |
                           |              |    |   .          |
    Input (1)--/\/\/\/\---(2)-----| |----(3)---| -   .  +     |
               R1 - 1K     .                   |     . -------  (4)
                           >       ------------| + .
                  R3 - 100 <       |           | .
                           >       |           |     A1
                           |--------
                         ----- (0)
                          ---
                           -
 The opening screen of network gives you the option of entering your network 
components manually or from a saved file. If you type "D" (or "d") to this 
response and provide the sample file name it will load. You then have the 
option of editing component values and/or adding new components to the network. 
The manual component entry asks you for the input and output node and then 
asks for component values and node connections. After the last component has 
been entered (component type), the program enters into the edit mode so you can 
review and correct any entry errors you might have made. 

The program then enters into the response calculation mode. This mode will 
calculate the output You will be asked for a start frequency, a stop or end 
frequency, and the frequency step size. The sweep can be linear (equal step 
size) or logarithmic (equal steps on a log scale). If you want output to the 
CRT or to a line printer. The program will then output the network response in 
dB and phase angle in degrees for each frequency step. You also have the 
option of saving the sweep output data to disk for input to a plotting 
routine.

 The frequency response (1 Hz - 10KHz) of the network in logarithmic frequency 
steps has been saved in file TEMP.PLT. If you are using a CGA card for video 
output, you can plot this response on your CRT using the program PLOTFL.EXE 
that I have included on the disk. The program PLOTFL.EXE automatically adjusts 
for linear or logarithmic frequency scale. The PLOTFL.EXE graph can also be 
output to a graphics printer via the Shift-PrtSc key if you have loaded 
GRAPHICS.COM (DOS Utility) before running the program.

After the frequency response has been output you will view a menu with the 
option to run a new sweep, Edit/modify component values, or save the network to 
disk. This feature lets you change circuit values to determine their effect on 
the network's response or lets you expand a portion of the frequency sweep in 
order to obtain higher output resolution.

The best way to learn how to use the program is to run it. View the file 
TEMP.PLT in order to obtain a feel for what the network response is. Then run 
NETWORK and load TEMP.DTA. Answer "N" (or "n") to all the edit questions and 
try out the various sweep modes. Then try modifying some component values 
(R3 is a good candidate) and see what effect the change has on the network 
response. You can save the sweep outputs to disk if you want to or just 
observe the changes on the screen and make a mental note of what happens. 
If you save the sweeps to disk, use a different file name for each sweep. I 
personally prefer to view the numbers rather than the graphics because it 
gives me a better feel for what the actual values and response changes are. 
The graphics plot is good for reports and for presentations.

Hints : For convenience capacitor values are input in micro farads. Diodes or 
switches are not valid circuit components since the program is used for linear 
network analysis. Diodes are assumed to be "Ideal" switches which are turned 
on and have 0 resistance and can therefore be replaced by a short. If you want 
to use a diode, approximate the diode with a small resistor which is equal to 
the forward resistance of the diode (10 ohms or so).  The amplifiers are 
provided with differential inputs and outputs. Be sure that you use the proper 
output in feedback circuits (negative feedback is a network between +output 
and -input). The amplifiers (as provided) have infinite bandwidth. You can set 
their open circuit voltage gain and output short circuit impedance. If you 
want to add a gain-bandwidth limitation to an amplifier place a capacitor to 
node 0 from its output. The amplifier response will then be band limited by 
the RC time constant of the capacitor and the amplifier's output resistance  
(Gain-Bandwidth = A/(2*pi*RC), where A is the Open circuit voltage gain of the 
amplifier). Capacitors can also be added in parallel with FET source resistors 
and Transistor collector resistors to limit the frequency response of these 
components.

Suggestions : Since the program uses matrix arithmetic to solve for the 
response, much faster response is obtained for small networks than for larger 
ones. If you have a large network try analyzing the network response by 
breaking it into parts and determine how each part works before attempting the 
final solution. NETWORK.EXE has been compiled using QB 4.0. QB 4.0 emulates 
the 8087 chip, if one is not installed in your machine, which can slow down 
your output.

Problems & Freeware Pitch : I offer this program to the general public as 
"Freeware". By this I mean you can make copies of the ARC file and give them 
to your friends. Just be sure to include all files (Including NETWORK.DOC) in 
NETWORK.ARC. If you have problems and want support, I'll provide it to you for 
a negotiable fee (depending on the difficulty of the problem). If you want to 
modify NETWORK on your own (or you're just curious) I'll provide you with the 
source code for NETWORK (and to PLOTFL) on a 360k 51/4 inch disk for a $10.00 
fee. 

Who am I and where do you send your money : 

Send checks (no plastic) to :

        William L. Gill
        12713 Brunswick Lane
        Bowie,Md. 20715

My qualifications : I am an Electrical Engineer with 27 years of experience. 
My specialty is Signal Processing. I am a former applications engineer for 
Westinghouse Integrated Circuits. I have approximately 15 years of part time 
teaching experience (Application of Digital Integrated Circuits, and the 
Application of Linear Integrated Circuits). So I have a strong background in 
circuit analysis and performance.

Why am I doing this ? I don't really expect to make money from this program. 
It is an engineering program and should therefore have a limited appeal. I 
think it provides a tool that some of you will want to try. The fees that I am 
imposing are to prevent "nuisance calls".