Cport


                 C Language Serial Communications Library

                 Version 1.30

                 30 Oct 91

                 Copyright (c) 1991  Bri Productions








































                                        1




         Table of Contents


         Introduction

                 Acknowledgments.........................5

                 General Description.....................5

                 Disclaimer..............................5

                 Registration............................5

                 Contacting the Author...................6

                 A typedef...............................6

                 Terminology.............................6


         Control Functions

                 Description.............................7

                 ComOpen.................................8

                 ComOpenS...............................12

                 ComActive..............................15

                 ComClose...............................17

                 ComCloseAll............................18

                 ComParam...............................18

                 ComBaud................................19

                 ComMode................................21

                 ComHandshake...........................22

                 ComTx..................................24


         Input Functions

                 Description............................25

                 ComGetc................................26

                 ComGets................................27

                 ComIn..................................28

                 ComFlushRx.............................29



                                        2




                 ComLenRx...............................30

                 ComPeek................................31


         Output Functions

                 Description............................33

                 ComPutc................................34

                 ComPuts................................35

                 ComOut.................................36

                 ComFlushTx.............................37

                 ComLenTx...............................38


         Status Functions

                 Description............................39

                 ComError...............................40

                 ComStatus..............................41

                 ComRts.................................42

                 ComDtr.................................43

                 ComOut1................................44


         Data Integrity

                 Description............................46

                 ComChecksum............................47

                 ComCrc16...............................48


         Miscellaneous Functions

                 Description............................50

                 ComSetBreak............................51

                 ComClrBreak............................51

                 ComPutScrtch...........................52

                 ComGetScrtch...........................53




                                        3




         Appendix A - Things to Look Out For............55

         Appendix B - Handshaking Schemes...............56

         Appendix C - The UART Chip.....................58

         Appendix D - The RS-232 Standard ?!!...........59

         Appendix E - Registration Form.................60


















































                                        4




        Acknowledgments.

         I would like to thank Earl Jensen and Steve Hill for technical
         review, Diana Hill for proofreading the documentation, Chip
         Curry and Luxtron Corp for beta testing, John Kerwin for
         technical advice, and Ton Kneist and No*l Gaskell for
         facilitating development.


         General Description.

         Cport is a C language interrupt-driven serial communication
         library for IBM and compatible computers. Cport is compatible
         with most if not all DOS based C compilers.


         Some of Cport's features are:

         ù Supports COM 1 to COM 4 and special configurations.
         ù Limited simultaneous communications.
         ù Baud rates from 50 to 115200 baud.
         ù Built in hardware and software handshaking.
         ù Both transmitter and receiver are interrupt-driven.
         ù Adjustable transmit and receive queues.
         ù Queues as large as 65534 bytes each.
         ù Transmit and receive queues are handled internally.
         ù Supports the NS16550 UART automatically.
         ù Written in assembly language for optimum speed and efficiency.


         DISCLAIMER.

         Cport is provided AS IS. Bri Productions specifically disclaims
         any and all warranties, expressed or implied, including fitness
         for a particular purpose. Use this product at your own risk.


         Registration.

         Cport is a user supported software product. Distribution of
         this product, unaltered and without charge, is encouraged. If
         you find this product useful, you are encouraged to register
         your copy. This allows Bri Productions to continue to provide
         and support low cost, high quality shareware.

         The registration fee is $35.00 US dollars and includes libraries
         for small, medium, compact and large memory models and complete
         source code. A registration form is provided in Appendix E.











                                        5




       Contacting the author.

         Bri Productions may be contacted by any of the following means:

         CompuServe      -       76635,2246
         U.S. mail       -       Bri Productions
                                 P.O.Box 7121
                                 Fremont, CA 94537-7121

         CompuServe is a trademark of CompuServe Inc.

         A typedef.

         You will see the data type 'byte' throughout the Cport library.
         This is a typedef defined in cport.h. Byte is an unsigned
         character used for byte size values.



         Terminology

         This section defines some of the terminology used in this
         and other Cport documentations.

         'Remote device' refers to the device that the computer is
         communicating with. The actual device may be a modem, serial
         printer or other communications device.

         If a serial port is 'open' it is currently performing or ready to
         perform serial communications. All 'open' ports are either 'active'
         or on the 'active stack'.

         If a serial port is 'active' it is currently recognized by
         Cport functions. For example, calling ComBaud will set the
         baud rate of the 'active' serial port and calling ComGetc
         will fetch a character/byte from the 'active' serial port's
         receive queue.

         If a serial port is on the 'active stack', it continues to
         transmit and receive but is not recognized by the Cport
         functions.


















                                        6





         Control Functions

         Control functions manage the parameters and the modes in
         which the serial port will operate. There are two sets of
         two functions, at least one from each set is mandatory:
         ComOpen or ComOpenS, and ComClose or ComCloseAll.

         ComOpen and/or ComOpenS open a serial port and sets the
         parameters and modes. ComOpen takes discrete parameters while
         ComOpenS takes a pointer to a structure of parameters.

         ComClose and ComCloseAll close the active and all opened
         serial port(s) respectively. ComCloseAll is generally used
         in simultaneous communications for conveniently ensuring
         all serial ports are closed. For single serial port
         communications ComClose is sufficient. Failing to close
         all opened serial ports prior to a program's termination
         will cause the program to crash.

         If more that one serial port is open, ComActive can be used
         to make any of the opened serial ports the active serial port.

         ComBaud and ComMode modify one or more of the parameters/modes
         of the serial port. ComParam reports on the current parameters
         and handshaking under which the currently active serial port
         is operating.

         ComHandshake determines if and what type of handshaking
         scheme will be enabled and sets the receiver threshold. ComTx
         turns the transmitter on and off, allowing you to implement
         your own handshaking scheme. See Appendix B for a description
         of handshaking.


























                                        7




         ----------------------------------------------------------------
         ComOpen
         ----------------------------------------------------------------

         Function

                 Opens serial port and makes it active.


         Syntax

                 #include "cport.h"
                 int ComOpen(unsigned com, int baud, byte mode,
                             unsigned rxQ, unsigned txQ);


         Parameters

                 com   - Constant that defines the serial port to be
                         opened. The upper 4 bits define the interrupt
                         vector while the lower 12 bits define the
                         port address.Possibilities are:

                               * COM1  (PORT0 | IRQ4)
                               * COM2  (PORT1 | IRQ3)
                               * COM3  (PORT2 | IRQ4)
                               * COM4  (PORT3 | IRQ3)

                                 PORT0 0x03F8
                                 PORT1 0x02F8
                                 PORT2 0x03E8
                                 PORT3 0x02E8

                                 IRQ2  0xA000
                                 IRQ3  0xB000
                                 IRQ4  0xC000
                                 IRQ5  0xD000
                                 IRQ6  0xE000
                                 IRQ7  0xF000

                                 BIOS0 (*(int far *)0x400000l)
                                 BIOS1 (*(int far *)0x400002l)
                                 BIOS2 (*(int far *)0x400004l)
                                 BIOS3 (*(int far *)0x400006l)

                         * The COMx constants are usually sufficient


                 baud  - Constant defining the baud rate to which the
                         serial port will be initialized. Possibilities
                         are:

                                 B115200    (1)
                                 B57600     (2)
                                 B38400     (3)
                                 B19200     (6)
                                 B9600     (12)


                                        8




                                 B7200     (16)
                                 B4800     (24)
                                 B3600     (32)
                                 B2400     (48)
                                 B2000     (58)
                                 B1800     (64)
                                 B1200     (96)
                                 B600     (192)
                                 B300     (384)
                                 B150     (768)
                                 B110    (1047)
                                 B75     (1536)
                                 B50     (2304)


                 mode  - Bit ORed constant defining the word
                         length, number of stop bits and the
                         parity that the serial port will use.
                         Possibilities are:

                                 W8  (0x03)  -  8 bit words
                                 W7  (0x02)  -  7 bit words
                                 W6  (0x01)  -  6 bit words
                                 W5  (0x00)  -  5 bit words

                                 S1  (0x00)  -  1 stop bit
                                 S2  (0x04)  -  2 stop bits

                                 NONE   (0x00) -  No parity
                                 ODD    (0x08) -  Odd parity
                                 EVEN   (0x18) -  Even parity
                                 MARK   (0x28) -  Mark parity
                                 SPACE  (0x38) -  Space parity


               * rxQ   - Size, in bytes, of the receive queue.

               * txQ   - Size in bytes, of the transmit queue.

                       * Limited to 32K in small and medium
                         memory models.


         Remarks

                 ComOpen opens the serial port 'com' and makes it the
                 active serial port. If a serial port has been previously
                 opened, it will be pushed into the active stack.

                 The 4 most significant bits in 'com' represent the
                 interrupt vector, while the lower 12 bits represent
                 the port address. Constants are provided in cport.h
                 to facilitate the formulation of the 'com' parameter.
                 The COMx values will work in most cases, however, the
                 IRQx values can be ORed with the PORTx or BIOSx
                 values to produce other combinations. The PORTx
                 values are actual port addresses where the serial


                                        9




                 ports are normally located. The BIOSx values are
                 actually macros that fetch the port address from the
                 BIOS data area. Usually the BIOSx and PORTx values
                 will be the same but it is not guaranteed. Quite
                 often the values at BIOS2 and BIOS3 (com 3 and com 4)
                 will be set to 0 regardless if com3 or com4 exist.
                 The BIOSx macros can also be used to set the values
                 in the BIOS data area as well, for example:

                         if(!BIOS2)
                            BIOS2 = PORT2;


                 The parameter 'baud' is the baud rate divisor which
                 determines the baud rate. Constants are provided in
                 cport.h for the most common baud rates. The 'baud'
                 rate divisor is defined as f / (16 * baud rate) where
                 f is 1.8432e+6.

                 Achieving baud rates above 19200 is largely dependent
                 on many variables such as machine speed, cable length,
                 handshaking activity, degree bidirectional transfers,
                 number of open serial ports, the type UART(s) used
                 (see Appendix C) and activity of other hardware interrupts.

                 The parameter 'mode' determines the word length,
                 number of stop bits and parity of the exchanged data.
                 Bits 0 & 1 determine the word length, bit 2
                 determines the number of stop bits, bit 3 enables
                 parity and bits 4 & 5 determine the type of parity
                 check. Constants which can be ORed together are
                 provided in cport.h.

                 'RxQ' and 'txQ' set the size of the receive and transmit
                 queues respectively. 'RxQ' should be at least 4 times
                 larger than the largest string or block of data the
                 programmer intends to fetch from the queue at once. '
                 TxQ' can be set as small as 1, but is not recommended.
                 In the small and medium memory models, where all data
                 is limited to 64K, the size queues are limited. In
                 the compact and large memory models, each queue can
                 be as large as 64K -1 (65534 bytes).


         Return value

                 If successful, ComOpen returns 0. In the event of an
                 error, it returns one of the following error codes:

                         OPENED    (1) -  Port already opened
                         BAD_COM   (2) -  Bad 'com' parameter.
                         NO_UART   (3) -  No UART chip detected.
                         RCV_ALC   (4) -  Receive queue allocation error.
                         TX_ALC    (5) -  Transmit queue allocation error.





                                        10




         See also

                 ComOpenS ComClose ComCloseAll ComBaud ComMode ComActive


         Example

                 Open COM1 at 9600 baud with 8 bit words, 1 stop bit,
                 no parity, a 1024 byte receiver and a 512 byte
                 transmitter.

                 {
                 int rv;

                    rv = ComOpen(COM1, B9600, W8|S1|NONE, 1024, 512);

                    if(rv)
                    {

                       ...error handler

                    }

                    ...more code
                 }




         ----------------------------------------------------------------
         ComOpenS
         ----------------------------------------------------------------

         Function

                 Opens serial port and makes it active.


         Syntax

                 #include "cport.h"
                 int ComOpenS(const C_param *param);


         Parameters

                 param   - Pointer to the structure of type 'C_param'.

                         The structure 'C_param' is defined as follows:

                         struct C_param{
                            unsigned com;
                            int      baud;
                            byte     mode;
                            unsigned rxQ;
                            unsigned txQ;
                            byte     htype;


                                        11




                            unsigned thresh;
                            };


                 com   - Constant that defines the serial port to be
                         opened. The upper 4 bits define the interrupt
                         vector while the lower 12 bits define the
                         port address.Possibilities are:

                               * COM1  (PORT0 | IRQ4)
                               * COM2  (PORT1 | IRQ3)
                               * COM3  (PORT2 | IRQ4)
                               * COM4  (PORT3 | IRQ3)

                                 PORT0 0x03F8
                                 PORT1 0x02F8
                                 PORT2 0x03E8
                                 PORT3 0x02E8

                                 IRQ2  0xA000
                                 IRQ3  0xB000
                                 IRQ4  0xC000
                                 IRQ5  0xD000
                                 IRQ6  0xE000
                                 IRQ7  0xF000

                                 BIOS0 (*(int far *)0x400000l)
                                 BIOS1 (*(int far *)0x400002l)
                                 BIOS2 (*(int far *)0x400004l)
                                 BIOS3 (*(int far *)0x400006l)

                         * The COMx constants are usually sufficient


                 baud  - Constant defining the baud rate to which
                         the serial port will be initialized.
                         Possibilities are:

                                 B115200    (1)
                                 B57600     (2)
                                 B38400     (3)
                                 B19200     (6)
                                 B9600     (12)
                                 B7200     (16)
                                 B4800     (24)
                                 B3600     (32)
                                 B2400     (48)
                                 B2000     (58)
                                 B1800     (64)
                                 B1200     (96)
                                 B600     (192)
                                 B300     (384)
                                 B150     (768)
                                 B110    (1047)
                                 B75     (1536)
                                 B50     (2304)



                                        12





                 mode  - Bit ORed constant defining the word
                         length, number of stop bits and the
                         parity that the serial port will use.
                         Possibilities are:

                                 W8  (0x03)  -  8 bit words
                                 W7  (0x02)  -  7 bit words
                                 W6  (0x01)  -  6 bit words
                                 W5  (0x00)  -  5 bit words

                                 S1  (0x00)  -  1 stop bit
                                 S2  (0x04)  -  2 stop bits

                                 NONE   (0x00) -  No parity)
                                 ODD    (0x08) -  Odd parity)
                                 EVEN   (0x18) -  Even parity)
                                 MARK   (0x28) -  Mark parity)
                                 SPACE  (0x38) -  Space parity)


               * rxQ  - Size, in bytes, of the receive queue.

               * txQ   - Size in bytes, of the transmit queue.

                       * Limited to 32K in small and medium
                         memory models.


                 htype - Type of handshaking to be used. Possibilities are:


                        OFF   (0)    - No handshaking
                        DTR   (0x01) - The receiver uses DTR
                        RTS   (0x02) - The receiver uses RTS
                        S_RX  (0x04) - The receiver uses XON and XOFF
                                       characters
                        S_TX  (0x08) - XON and XOFF characters are
                                       honored by the transmitter
                        CTS   (0x10) - CTS is checked by the transmitter
                        DSR   (0x20) - DSR is checked by the transmitter
                        DCD   (0x80) - DCD is checked by the transmitter

                        SOFT  (0x0C) - Same as (S_RX | S_TX)
                      * HARD  (0x12) - Same as (RTS | CTS)
                        HARD1 (0x21) - Same as (DTR | DSR)
                      * HARD2 (0x12) - Same as (RTS | CTS)

                 * The constants HARD and HARD2 have the same value. HARD
                   is retained to maintain compatibility with older versions
                   of Cport.

                 NOTE: See Appendix B for a more detailed discussion on
                       handshaking schemes.


                 thresh - Receive queue threshold.


                                        13






         Remarks

                 ComOpenS is an alternative to ComOpen for opening
                 a serial port. It takes a pointer to a structure of
                 parameters instead of taking discrete parameters.
                 It also can set the handshaking without making a
                 separate call to ComHandshake.If a serial port has
                 been previously opened, it will be pushed into the
                 active stack.

                 The 4 most significant bits in 'com' represent the
                 interrupt vector, while the lower 12 bits represent
                 the port address. Constants are provided in cport.h
                 to facilitate the formulation of the 'com' parameter.
                 The COMx values will work in most cases, however, the
                 IRQx values can be ORed with the PORTx or BIOSx
                 values to produce other combinations. The PORTx
                 values are actual port addresses where the serial
                 ports are normally located. The BIOSx values are
                 actually macros that fetch the port address from the
                 BIOS data area. Usually the BIOSx and PORTx values
                 will be the same but it is not guaranteed. Quite
                 often the values at BIOS2 and BIOS3 (com 3 and com 4)
                 will be set to 0 regardless if com3 or com4 exist.

                 The parameter 'baud' is the baud rate divisor which
                 determines the baud rate. Constants are provided in
                 cport.h for the most common baud rates. The 'baud'
                 rate divisor is defined as f / (16 * baud rate) where
                 f is 1.8432e+6.

                 Achieving baud rates above 19200 is largely dependent
                 on many variables such as machine speed, cable length,
                 handshaking activity, degree bidirectional transfers,
                 number of open serial ports, the type UART used
                 (see Appendix C) and activity of other hardware interrupts.

                 The parameter 'mode' determines the word length,
                 number of stop bits and parity of the exchanged data.
                 Bits 0 & 1 determine the word length, bit 2
                 determines the number of stop bits, bit 3 enables
                 parity and bits 4 & 5 determine the type of parity
                 check. Constants which can be ORed together are
                 provided in cport.h.

                 'RxQ' and 'txQ' set the size of the receive and transmit
                 queues respectively. 'RxQ' should be at least 4 times
                 larger than the largest string or block of data the
                 programmer intends to fetch from the queue at once.
                 'TxQ' can be set as small as 1, but is not recommended.
                 In the small and medium memory models, where all data
                 is limited to 64K, the size queues are limited. In
                 the compact and large memory models, each queue can
                 be as large as 64K -1 (65534).



                                        14




                 The parameter 'htype' defines the type of flow
                 control (handshaking) to be used by the transmitter
                 and receiver. 'Threshold' determines when the
                 receiver will assert of disassert the selected
                 handshaking.


         Return value

                 If successful, ComOpenS returns 0. In the event of an
                 error, it returns one of the following error codes:

                         OPENED    (1) -  Port already opened
                         BAD_COM   (2) -  Bad 'com' parameter.
                         NO_UART   (3) -  No UART chip detected.
                         RCV_ALC   (4) -  Receive queue allocation error.
                         TX_ALC    (5) -  Transmit queue allocation error.


         See also

                 ComOpen ComParam ComHandshake ComClose ComCloseAll


         Example

                 Open COM2 with the same parameters as COM1.

                 {
                 struct C_param param;

                    ComActive(COM1);
                    ComParam(&param);
                    param.com = COM2;

                    ComOpenS(&param);
                 }






         ----------------------------------------------------------------
         ComActive
         ----------------------------------------------------------------

         Function

                 Activates a currently opened serial port.


         Syntax

                 #include "cport.h"
                 int ComActive(unsigned com);



                                        15





         Parameters

                 com - Opened serial port which is to be made active.


         Remarks

                 ComActive activates the opened serial port specified
                 by 'com'. The value of 'com' is the same the 'com'
                 parameter which was passed to ComOpen or ComOpenS
                 when the serial port was opened.

                 The specified serial port is taken off the active
                 stack and the previously active serial port is pushed
                 onto the active stack. For example:


                         before:

                         active stack + 1 = COM1
                         active stack + 0 = COM2
                                   active = COM3


                         after: ComActive(COM1);

                         active stack + 1 = COM2
                         active stack + 0 = COM3
                                   active = COM1


         Return value

                 If successful, ComActive returns 0. Otherwise it
                 will return an error code. Possibilities are:

                         BAD_COM  (2) - bad 'com' parameter
                         NOT_OPEN (8) - 'com' is not open


         See Also

                 ComOpen ComOpenS ComClose


         Example

                 If there is data available on COM1, get it and send it
                 out on COM2.

                 {
                 byte buf[128];
                 unsigned len;

                    ComActive(COM1);
                    if(ComLenRx())


                                        16




                    {
                       len = ComIn(buf, 128);

                       ComActive(COM2);
                       ComOut(buf, len);
                    }

                 }





         ----------------------------------------------------------------
         ComClose
         ----------------------------------------------------------------

         Function

                 Closes the currently active serial port.


         Syntax

                 #include "cport.h"
                 void ComClose(void);


         Remarks

                 ComClose closes the currently active serial port. The
                 serial port on the top of the active stack (most recently
                 active) subsequently becomes the active serial port.

                 Failing to close all serial ports before a program
                 is terminated will cause the program to crash.


         See also

                 ComCloseAll ComOpen ComOpenS


         Example

                 Close the only opened serial port prior to terminating.

                 {

                   ...closing code

                   ComClose();     /* only one serial port open */
                   exit(0)

                 }




                                        17




         ----------------------------------------------------------------
         ComCloseAll
         ----------------------------------------------------------------

         Function

                 Closes all the currently opened serial ports.


         Syntax

                 #include "cport.h"
                 void ComCloseAll(void);


         Remarks

                 ComCloseAll closes all the currently opened serial ports.
                 This includes the active serial port and any serial
                 ports on the active stack.

                 Failing to close all serial ports before a program
                 is terminated will cause the program to crash.


         See also

                 ComClose ComOpen ComOpenS


         Example

                 Make sure all serial ports are closed prior to
                 terminating.

                 {

                   ...closing code

                   ComCloseAll();
                   exit(0)

                 }



         ----------------------------------------------------------------
         ComParam
         ----------------------------------------------------------------

         Function

                 Retrieves the parameters of the currently active serial
                 port.





                                        18




         Syntax

                 #include "cport.h"
                 void ComParam(const struct C_param *param);

         Remarks

                 ComParam retrieves the parameters and handshaking
                 status of the currently active serial port and stores
                 them in a structure of type 'C_param'. The structure
                 'C_param' is defined as follows:

                         struct C_param{
                            unsigned com;
                            int      baud;
                            byte     mode;
                            unsigned rxQ;
                            unsigned txQ;
                            byte     htype;
                            unsigned thresh;
                            };

                 See ComOpenS for a discussion of the individual
                 elements.

         See also

                 ComOpen ComOpenS ComMode ComBaud


         Example

                 Open COM2 with the same parameters as COM1.

                 {
                 struct C_param param;

                    ComActive(COM1);
                    ComParam(&param);
                    param.com = COM2;

                    ComOpenS(&param);
                 }




         ----------------------------------------------------------------
         ComBaud
         ----------------------------------------------------------------

         Function

                Changes the baud rate of the currently active serial
                port.




                                        19




         Syntax

                 #include "cport.h"
                 void ComBaud(int baud);


         Parameters

                 baud  - Constant defining the baud rate to which
                         the serial port will be initialized.
                         Possibilities are:

                                 B115200    (1)
                                 B57600     (2)
                                 B38400     (3)
                                 B19200     (6)
                                 B9600     (12)
                                 B7200     (16)
                                 B4800     (24)
                                 B3600     (32)
                                 B2400     (48)
                                 B2000     (58)
                                 B1800     (64)
                                 B1200     (96)
                                 B600     (192)
                                 B300     (384)
                                 B150     (768)
                                 B110    (1047)
                                 B75     (1536)
                                 B50     (2304)


         Remarks

                 The parameter 'baud' is the baud rate divisor which
                 determines the baud rate. Constants are provided in
                 cport.h for the most common baud rates. The 'baud'
                 rate divisor is defined as f / (16 * baud rate) where
                 f is 1.8432e+6.

                 Achieving baud rates above 19200 are largely dependent
                 on many variables such as machine speed, cable length,
                 handshaking activity, degree bidirectional transfers,
                 the type of UART used, number of opened serial ports and
                 activity of other hardware interrupts.


         See also

                 ComOpen ComOpenS ComParam ComMode



         Example

                 Set the currently active serial port to the next baud
                 rate in the table 'baud'.


                                        20





                 {
                 static int indx = 0;
                 int baud[4] = { B9600,
                                 B2400,
                                 B1200,
                                 B300
                                 };

                    indx++;
                    indx %= 4;

                    ComBaud(baud[indx]);
                 }





         ----------------------------------------------------------------
         ComMode
         ----------------------------------------------------------------

         Function

                Changes the word length, number of stop bits and parity
                of the active serial port.


         Syntax

                 #include "cport.h"
                 void ComMode(int mode);


         Parameters

                 mode  - Bit ORed constant defining the word length,
                         number of stop bits and the parity that the
                         serial port will use. Possibilities are:

                                 W8  (0x03)  -  8 bit words
                                 W7  (0x02)  -  7 bit words
                                 W6  (0x01)  -  6 bit words
                                 W5  (0x00)  -  5 bit words

                                 S1  (0x00)  -  1 stop bit
                                 S2  (0x04)  -  2 stop bits

                                 NONE   (0x00) -  No parity)
                                 ODD    (0x08) -  Odd parity)
                                 EVEN   (0x18) -  Even parity)

                                 MARK   (0x28) -  Mark parity)
                                 SPACE  (0x38) -  Space parity)




                                        21




         Remarks

                 The parameter 'mode' determines the word length,
                 number of stop bits and parity of the exchanged data.
                 Bits 0 & 1 determine the word length, bit 2
                 determines the number of stop bits, bit 3 enables
                 parity and bits 4 & 5 determine the type of parity
                 check. Constants that can be ORed together are
                 provided in cport.h.


         See also

                 ComOpen ComOpenS ComParam ComBaud


         Example

                 Toggle the currently active serial port to the next mode
                 in the table 'mode'.

                 {
                 static int indx = 0;
                 int mode[2] = { W8|S1|NONE,
                                 W7|S1|EVEN,
                                 };

                    indx ^= 1;
                    ComMode(mode[indx]);
                 }


         ----------------------------------------------------------------
         ComHandshake
         ----------------------------------------------------------------

         Function

                 Enables or disables flow control (handshaking).


         Syntax

                 #include "cport.h"
                 void ComHandshake(byte htype, unsigned thresh);


         Parameters

                 htype - Type of handshaking to be used. Possibilities are:


                        OFF   (0)    - No handshaking
                        DTR   (0x01) - The receiver uses DTR
                        RTS   (0x02) - The receiver uses RTS
                        S_RX  (0x04) - The receiver uses XON and XOFF
                                       characters


                                        22




                        CTS   (0x10) - CTS is checked by the transmitter
                        DSR   (0x20) - DSR is checked by the transmitter
                        DCD   (0x80) - DCD is checked by the transmitter
                        S_TX  (0x08) - XON and XOFF characters are
                                       honored by the transmitter
                        SOFT  (0x0C) - Same as (S_RX | S_TX)
                      * HARD  (0x12) - Same as (RTS | CTS)
                        HARD1 (0x21) - Same as (DTR | DSR)
                      * HARD2 (0x12) - Same as (RTS | CTS)

                 * The constants HARD and HARD2 have the same value. HARD
                   is retained to maintain compatibility with older versions
                   of Cport.

                 NOTE: See Appendix B for a more detailed discussion on
                       handshaking schemes.

                 thresh - Receive queue threshold.


         Remarks

                 ComHandshake enables or disables software and/or
                 hardware handshaking. In software handshaking, XON
                 and XOFF characters are transmitted and received to
                 suspend and resume communications. In hardware
                 handshaking uses any or all of DTR, DSR, RTS, CTS
                 and DCD lines to suspend and resume communications.
                 'Thresh' determines when the receiver will assert and
                 disassert.


         See also

                 ComParam ComOpenS ComTx


         Example

                 If COM1 is successfully opened, turn on some hardware
                 handshaking and set the receiver threshold to 3/4 of the
                 receiver's full size. The transmitter will not transmit
                 unless both DSR and DCD are true. The receiver will
                 disassert DTR if the receive queue length exceeds the
                 threshold.

                 {
                 int rv;

                    rv = ComOpen(COM1, B9600, W8|S1|NONE, 1024, 512);
                    if(rv)
                    {
                       ...error handler
                    }

                    ComHandshake(DSR|DTR|DCD, RCVQ_SIZE * 3 / 4);



                                        23




                    ...more code
                 }



         ----------------------------------------------------------------
         ComTx
         ----------------------------------------------------------------

         Function

                 Turns the transmitter on or off


         Syntax

                 #include "cport.h"
                 void ComTx(byte on_off);


         Parameters

                 on_off - Determines whether the transmitter is to be
                          turned on or off. Constants are provided in
                          cport.h. Possibilities are:

                                  ON  (1) - Turns the transmitter on
                                  OFF (0) - Turns the transmitter off


         Remarks

                 ComTx allows you to turn the transmitter on and off
                 to suspend and resume transmissions. This function
                 can be very useful when implementing your own
                 handshaking scheme.


         See also

                 ComHandshake ComOpenS ComParam


         Example

                 If the transmitter is off ('off') and needs to be
                 turned on ('turn_on'), turn it on. If the transmitter
                 is on and needs to be turned off, turn it off.

                 {
                    if(off && turn_on)
                       ComTx(ON);

                    else if(!off && turn_off)
                       ComTx(OFF);

                 }


                                        24




       Input Functions

         Input fuctions interface with the active serial port's receiver
         and the internal receive queue.

         There are four functions for fetching from the receive
         queue. ComGetc and ComGets can be used to fetch control codes
         as well as normal ascii characters, while ComIn is intended
         for fetching binary data. ComPeek returns a copy of the head
         character/byte without removing it from the queue.

         ComFlushRx flushes the receiver while ComLenRx finds
         the number of characters/bytes in the queue.














































                                        25




         ----------------------------------------------------------------
         ComGetc
         ----------------------------------------------------------------

         Function

                 Fetches a character from the active serial port's
                 receive queue.


         Syntax

                 #include "cport.h"
                 char ComGetc(void);


         Remarks

                 ComGetc fetches the head character from the active
                 serial port's receive queue. If there are no characters
                 in the receive queue, ComGetc returns a null character
                 ('\0').


         Return value

                 On Success, ComGetc returns the character from the
                 receive queue. If it fails it returns a '\0'.


         See also

                 ComPutc ComGets ComIn ComPeek


         Example

                 Get a character from the serial port and test if it
                 is a start of header control character.

                 #define SOH 1

                 {
                 char c;

                    c = ComGetc();

                    if(c == SOH)
                    {

                       ...SOH code

                    }
                    else
                       return c;
                 }



                                        26





         ----------------------------------------------------------------
         ComGets
         ----------------------------------------------------------------

         Function

                 Fetches a string of characters from the active serial
                 port's  receive queue.


         Syntax

                 #include "cport.h"
                 char *ComGets(char *str, int max_c, char term_c);


         Parameters

                 *str  - Pointer to the buffer where the string of
                         characters will be stored.

                 max_c - Maximum number of characters to fetch.

                 term_c - Termination character. ComGets will return
                         if this character is encountered.


         Remarks

                 ComGets fetches a string of characters from the
                 active serial port's receive queue. The string will
                 be stored in 'str'. 'str' must be at least 'max_c' + 1
                 long to allow for the null terminator.

                 ComGets will return on the first occurrence of one of
                 three conditions: 1) the character 'term_c' is
                 encountered; 2) 'max_c' characters are reached; or 3)
                 No more characters are available in the receive queue.


         Return value

                 ComGets returns a pointer to the null terminated
                 string.


         See also

                 ComPuts ComGetc ComIn ComLenRx


         Example

                 Get a line of max 80 characters from the receive queue
                 and store it in 'str'. The string will be echoed to the
                 display.


                                        27





                 {
                 char str[81];

                    if(ComLenRx() > 80)
                       puts(ComGets(str, 80, '\n'));
                 }


         ----------------------------------------------------------------
         ComIn
         ----------------------------------------------------------------

         Function

                 Fetches a block of bytes from the active serial port's
                 receive queue.


         Syntax

                 #include "cport.h"
                 unsigned ComIn(void *abyte, unsigned num_byte);


         Parameters

                 *abyte - Pointer to the buffer where the block of bytes
                         will be stored.

                 num_byte - Number of bytes to get from the receive queue.


         Remarks

                 ComIn fetches a block of bytes from active serial port's
                 the receive queue and stores it in 'abyte'. ComIn will
                 always fetch 'num_byte' bytes unless not enough bytes are
                 available. ComIn is well suited for receiving binary data.


         Return value

                 ComIn returns the number of bytes fetched.


         See also

                 ComOut ComGetc ComGets ComLenRx


         Example

                 Get a block of 1024 bytes from the serial port.

                 #define BLK_SZ 1024
                 {


                                        28




                 byte block[BLK_SZ];
                 unsigned rs;

                    if(ComLenRx() > BLK_SZ)
                    {
                       rs = ComIn(block, BLK_SZ);
                       if(rs < BLK_SZ)
                       {
                          ...error handler
                       }
                    }
                 }



         ----------------------------------------------------------------
         ComFlushRx
         ----------------------------------------------------------------

         Function

                 Flushes the active serial port's receiver and receive
                 queue.

         Syntax

                 #include "cport.h"
                 void ComFlushRx(void);


         Remarks

                 ComFlushRx flushes the active serial port's receive
                 queue and the UART of any existing characters/bytes.


         See also

                 ComLenRx ComFlushTx


         Example

                 If a receive flush command is in order, flush the
                 receiver.

                 #define ...
                 #define RCV_FLSH 2
                 #define ...
                 {
                 int command;


                    ...fetch command

                    switch(command)
                    {


                                        29




                         case ...:
                            ...case code
                            break;

                         case RCV_FLSH:
                            ComFlushRx();
                            break;

                         case ...:
                            ...case code
                            break;
                    }
                  }



         ----------------------------------------------------------------
         ComLenRx
         ----------------------------------------------------------------

         Function

                 Calculates the number of characters in the active serial
                 port's receive queue.


         Syntax

                 #include "cport.h"
                 unsigned ComLenRx(void);


         Remarks

                 ComLenRx calculates the number of characters in the
                 active serial port's receive queue. Valid numbers are 0
                 to 65534.


         Return value

                 ComLenRx returns the number of characters presently
                 residing in the receive queue.


         See also

                 ComFlushRx ComLenTx


         Example

                 If there are more than 80 characters available, get a
                 line.

                 {
                 char str[81];


                                        30





                    if(ComLenRx() > 80)
                       puts(ComGets(str, 80, '\n'));

                 }



         ----------------------------------------------------------------
         ComPeek
         ----------------------------------------------------------------

         Function

                 Fetches a copy of the head character in the active
                 serial port's receive queue.


         Syntax

                 #include "cport.h"
                 char ComPeek(void);


         Remarks

                 ComPeek fetches a copy of the head character in the
                 active serial port's receive queue. ComPeek will not
                 remove the character from the queue.


         Return value

                 ComPeek returns the copy of the head character.


         See also

                 ComGetc


         Example

                 Determine if the head character is a control character.

                 #define CTRL_A 1
                 #define CTRL_Z 26
                 {
                 char peek_c;
                 char str[81];

                    peek_c = ComPeek();

                    if(peek_c >= CTRL_A && peek_c <= CTRL_Z)
                    {
                       switch(ComGetc())
                       {


                                        31





                         ...command processor

                       }
                    }

                    else
                       puts(ComGets(str, 80, '\n');

                 }

















































                                        32




         Output Functions

         Output functions interface with the active serial port's
         transmitter and it's internal transmit queue.

         There are three functions for putting characters/bytes into
         the transmit queue, all of which return the actual number of
         characters/bytes successfully put. ComPutc and ComPuts can be
         used to put control characters as well as normal ascii characters
         into the transmit queue. ComOut is intended for putting binary
         data into the transmit queue.

         ComFlushTx flushes the transmitter while ComLenTx finds the
         number of characters in the queue.













































                                        33




         ----------------------------------------------------------------
         ComPutc
         ----------------------------------------------------------------

         Function

                 Puts a character into the active serial port's transmit
                 queue.

         Syntax
                 #include "cport.h"
                 int ComPutc(char c);


         Parameters

                 c - Character to be put into the transmit queue.


         Remarks

                 ComPutc puts a character into the active serial port's
                 transmit queue to be transmitted. If the transmit queue
                 is full, the character is not put and ComPutc returns a 0.


         Return value

                 On success, ComPutc returns a 1. If it fails, it
                 returns 0.


         See also

                 ComGetc ComPuts ComOut


         Example

                 Send an BS to the transmitter.

                 #define BS 8

                 {

                    if(!ComPutc(BS))
                    {

                       ...error handler

                    }








                                        34




         ----------------------------------------------------------------
         ComPuts
         ----------------------------------------------------------------

         Function

                 Puts a string of characters into the active serial
                 port's transmit queue.


         Syntax

                 #include "cport.h"
                 int ComPuts(const char *str);


         Parameters

                 *str  - Pointer to the string to be put into the
                         transmit queue.


         Remarks

                 ComPuts puts the string 'str' into the active serial
                 port's transmit queue to be transmitted. If the transmit
                 queue becomes full, ComPuts will not attempt to put any
                 more characters in the queue.


         Return value

                 ComPuts returns the actual number of characters put
                 into the transmit queue.


         See also

                 ComGets ComPutc ComOut


         Example

                 Send the string "hello world" to the transmitter.

                 {
                 char *str = "hello world";


                    if(ComPuts(str) < strlen(str))
                    {

                       ...error handler

                    }
                 }



                                        35




         ----------------------------------------------------------------
         ComOut
         ----------------------------------------------------------------

         Function

                 Puts a block of bytes into the active serial port's
                 transmit queue.


         Syntax
                 #include "cport.h"
                 unsigned ComOut(const void *abyte, unsigned num_byte);


         Parameters

                 *abyte - Pointer to the buffer of the block to be put
                          into the transmit queue.

                 num_byte - Number of bytes to be put into the transmit
                            queue.


         Remarks

                 ComOut puts the block of bytes pointed to by 'abyte'
                 into the active serial port's transmit queue to be
                 transmitted.


         Return value

                 ComOutQ returns the number of bytes actually put into
                 the transmit queue.


         See also

                 ComIn ComPutc ComPuts

         Example

                 Send a block of 128 bytes to the transmitter.

                 #define BLK_SZ 128
                 {
                 byte block[BLK_SZ];

                       if(ComOut(block, BLK_SZ) < BLK_SZ)
                       {

                          ...error handler

                       }
                    }
                 }


                                        36




         ----------------------------------------------------------------
         ComFlushTx
         ----------------------------------------------------------------

         Function

                 Flushes the active serial port's transmit queue.


         Syntax

                 #include "cport.h"
                 void ComFlushTx(void);


         Remarks

                 ComFlushTx flushes any existing characters in the
                 active serial port's transmit queue.


         See also

                 ComFlushRx ComLenTx


         Example

                 If a transmit flush command is in order, flush the
                 transmitter.

                 #define
                 #define TX_FLSH 3
                 #define

                 {
                 int command;

                    ...fetch command

                    switch(command)
                    {

                         case ...:
                            ...case code
                            break;

                         case TX_FLSH:
                            ComFlushTx();
                            break;

                         case ...:
                            ...case code
                            break;

                    }
                  }


                                        37




         ----------------------------------------------------------------
         ComLenTx
         ----------------------------------------------------------------


         Function

                 Calculates the number of characters in the active
                 serial port's transmit queue.


         Syntax

                 #include "cport.h"
                 unsigned ComLenTx(void);


         Remarks

                 ComLenTx calculates the number of characters in the
                 active serial port's receive queue. Valid numbers are
                 0 to 65534.


         Return value

                 ComLenTx returns the number of characters presently
                 in the transmit queue.


         See also

                 ComLenRx ComFlushTx



         Example

                 Check if the transmitter has reached 3/4 of its
                 capacity.

                 {

                    if(ComLenTx() > (TX_SIZE * 3 / 4))
                    {

                       ...pause

                    }
                 }









                                        38




         Status Functions

         Status functions are for obtaining or setting various status of
         the active serial port.

         There are two functions for obtaining status: ComError detects
         line errors in the serial port; and ComStatus returns the status
         of the input hardware lines.

         ComDtr, ComRts and ComOut1 manipulate the output hardware
         lines
















































                                        39




         ----------------------------------------------------------------
         ComError
         ----------------------------------------------------------------

         Function

                 Determines if any errors have occurred on the active
                 serial port's since the last call to ComError.


         Syntax

                 #include "cport.h"
                 unsigned ComError(void);


         Remarks

                 ComError determines if any errors are pending on
                 the active serial port. After a call to ComError, the
                 errors are cleared. ComError returns an error
                 word in which the bits are defined as follows:

                         OVERUN  (0x002)  -  overrun error
                         PARITY  (0x004)  -  parity error
                         FRAMING (0x008)  -  framing error
                         BREAK   (0x010)  -  break detect
                         TIMOUT  (0x080)  -  timeout
                         TXFULL  (0x100)  -  transmit queue overflow
                         RXFULL  (0x200)  -  receive queue overflow


         Return value

                 If an error has occurred, ComError returns an error
                 word. If no errors have occurred it returns a 0.


         See also

                 ComStatus


         Example

                 Determine the source of the error if one has occurred.

                 {
                 unsigned com_err;

                    com_err = ComError();

                    if(com_err)
                    {
                         switch(com_err)
                         {



                                        40




                            case OVERUN:
                               ...over run handler
                               break;


                            case PARITY:
                               ...parity error handler
                               break;

                            case ...

                         }
                    }



         ----------------------------------------------------------------
         ComStatus
         ----------------------------------------------------------------

         Function

                 Retrieves the status of the active serial port's
                 hardware lines.


         Syntax

                 #include "cport.h"
                 byte ComStatus(void);


         Remarks

                 ComStatus retrieves the status of the active serial
                 port's hardware lines. ComStatus returns a status byte
                 in which the bits are defined as follows:

                         DCTS (0x01) - change in clear to send.
                         DDSR (0x02) - change in data set ready.
                         TERI (0x04) - trailing edge ring indicator.
                         DDCD (0x08) - change in data carrier detect.
                         CTS  (0x10) - clear to send.
                         DSR  (0x20) - data set ready.
                         RI   (0x40) - ring indicator.
                         DCD  (0x80) - data carrier detect.


         Return value

                 ComStatus returns the status byte.


         See also

                 ComError ComRts ComDtr



                                        41





         Example

                 Test if the modem is powered up and ready.

                 {

                    ComDtr(ON);
                    delay(40);


                    if(!(ComStatus() & DSR))
                    {
                       puts("modem not responding");

                       ...what to do code

                    }
                 }



         ----------------------------------------------------------------
         ComRts
         ----------------------------------------------------------------

         Function

                 Sets or clears the active serial port's Request to Send
                 line.

         Syntax

                 #include "cport.h"
                 void ComRts(byte on_off);

         Parameters

                 on_off - Determines whether RTS is to be set or
                          cleared. Constants are provided in cport.h.
                          Possibilities are:

                          ON  (1) - Sets RTS.
                          OFF (0) - Clears RTS.

         Remarks

                 ComRts sets or clears the active serial port's RTS line
                 depending on the value of 'on_off'. In many cases, this
                 signal will be looked at by the remote device to determine
                 if it is safe to transmit. This gives the programmer the
                 ability to turn off the remote device's transmitter.

                 NOTE: ComRts should never be called when RTS hardware
                 handshaking is enabled.




                                        42




         See also

                 ComDtr ComOut1 ComStatus


         Example

                 If the receiver is off ('rx_off') but ready to
                 receive, assert RTS. If it is on but not ready, turn
                 off RTS.

                 {

                    if(rx_off && rx_rdy)
                       ComRts(ON);

                    else if(!rx_off && !rx_rdy)
                       ComRts(OFF);
                 }


         ----------------------------------------------------------------
         ComDtr
         ----------------------------------------------------------------

         Function

                 Sets or clears the active serial port's  Data Terminal
                 Ready line.


         Syntax

                 #include "cport.h"
                 void ComDtr(byte on_off);


         Parameters

                 on_off - Determines whether DTR is to be set or
                          cleared. Constants are provided in cport.h.
                          Possibilities are:

                          ON  (1) - Sets DTR.
                          OFF (0) - Clears DTR.


         Remarks

                 ComDtr set or clears the active serial port's DTR
                 line depending on the value of 'on_off'. Setting DTR
                 informs the remote equipment that the computer is ready
                 to establish communications.

                 NOTE: ComRts should never be called when DTR hardware
                 handshaking is enabled.



                                        43





         See also

                 ComRts ComOut1 ComStatus


         Example

                 If an break is detected, turn off DTR.

                 {
                 unsigned com_err;
                 int brk_flg = 0;

                    com_err = ComError();

                    if(com_err)
                    {
                         switch(com_err)
                         {
                            case ...

                            case BREAK:
                               ComDtr(OFF);
                               brk_flg = 1;
                               break;

                            case ...
                         }

                    }
                }


         ----------------------------------------------------------------
         ComOut1
         ----------------------------------------------------------------

         Function

                 Sets or clears the active serial port's Out 1 line.


         Syntax

                 #include "cport.h"
                 void ComOut1(byte on_off);


         Parameters

                 on_off - Determines whether OUT1 is to be set or
                          cleared. Constants are provided in cport.h.
                          Possibilities are:

                          ON  (1) - Sets OUT1.
                          OFF (0) - Clears OUT1.


                                        44






         Remarks

                 ComOut1 sets or clears the active serial port's
                 general purpose OUT1 line depending on the value of
                 'on_off'. OUT1 is a general purpose output sometimes
                 utilized by device for a special feature or reset.


         See also

                 ComRts ComDtr ComStatus


         Example

                 Reset a smart modem.

                 #define ComSMSet() ComOut1(ON)
                 #define ComSMClr() ComOut1(OFF)
                 {
                    ComSMRes();
                    delay(50);
                    ComSMClr();
                 }

































                                        45




         Data Integrity

         Two functions are currently provided for checking the integrity
         of data. They are: ComChecksum and ComCrc16. ComChecksum and
         ComCrc16 perform a checksum calculation and a 16 bit cyclic
         redundancy check respectively, on a block of bytes. Notice also
         that these functions take the same arguments as the functions
         ComOut and ComIn.



















































                                        46




         ----------------------------------------------------------------
         ComChecksum
         ----------------------------------------------------------------

         Function

                 Performs a checksum calculation on a block of bytes.


         Syntax

                 #include "cport.h"
                 byte ComChecksum(const void *abyte, unsigned n_byte);


         Parameters

                 *abyte - Pointer to the block on which the checksum
                          is to be performed

                 num_byte - Number of bytes in the block.


         Remarks

                 ComChecksum performs a one byte checksum on the block
                 of bytes pointed to by 'abyte'. The checksum is
                 calculated by summing all the bytes in the block and
                 ignoring the carry outs.


         Return value

                 ComChecksum returns the one byte checksum.


         See also

                 ComCrc16 ComIn ComOut


         Example

                 Verify the actual checksum matches the received
                 checksum.

                 {
                 struct Xmodem{
                    byte num;
                    byte _num;
                    byte data[128];
                    byte checksum;
                    }block;


                    ComIn(&block, sizeof(struct Xmodem));



                                        47




                    if(ComChecksum(block.data, 128) != block.checksum)
                    {

                         ...bad block handler

                    }

                    else...

                 }





         ----------------------------------------------------------------
         ComCrc16
         ----------------------------------------------------------------

         Function

                 Performs a 16 bit cyclic redundancy check on a block of
                 bytes.


         Syntax

                 #include "cport.h"
                 unsigned ComCrc16(const void *abyte, unsigned n_byte);


         Parameters

                 *abyte - Pointer to the block on which the 16 bit
                          cyclic redundancy check is to be performed.

                 num_byte - Number of bytes in the block.


         Remarks

                 ComCrc16 performs a 16 bit cyclic redundancy check on
                 the block of bytes pointed to by 'abyte'. The 16 bit
                 CRC is calculated using a table of precalculated
                 values.


         Return value

                 ComCrc16 returns the two byte CRC value.


         See also

                 ComChecksum ComIn ComOut




                                        48




         Example

                 Verify the actual CRC matches the received CRC.

                 {
                 struct Xmodem{
                    byte num;
                    byte _num;
                    byte data[128];
                    unsigned crc16;
                    }block;


                    ComIn(&block, sizeof(struct Xmodem));

                    if(ComCrc16(block.data, 128) != block.crc16)
                    {

                         ...bad block handler

                    }

                    else...

                 }


































                                        49




        Misc Functions

         There are two pair of misc functions: ComSetBreak and
         ComClrBreak set and clear a break condition; ComPutScrtch
         and ComGetScrtch write to and read from the scratch register.






















































                                        50




         ----------------------------------------------------------------
         ComSetBreak
         ----------------------------------------------------------------

         Function

                 Set a break condition on the active serial port.

         Syntax

                 #include "cport.h"
                 void ComSetBreak(void);

         Remarks

                 ComSetBreak sets a break condition on the active serial
                 port. The break condition will stay in effect until a
                 subsequent call to ComClrBreak is made.


         See also

                 ComClrBreak


         Example

                 If the an abort condition has been declared, set a
                 break condition. When it clears, release the break
                 condition.

                 {
                 int abrt_flg;
                 int brk_flg;

                    if(abrt_flg && !brk_flg)
                       ComSetBreak();

                    else if(!abrt_flg && brk_flg)
                       ComClrBreak();
                 }






         ----------------------------------------------------------------
         ComClrBreak
         ----------------------------------------------------------------

         Function

                 Clears a previously set break condition on the active
                 serial port.




                                        51




         Syntax

                 #include "cport.h"
                 void ClrBreak(void);


         Remarks

                 ComClrBreak clears a previously set break condition
                 on the active serial port.


         See also

                 ComSetBreak


         Example

                 If the an abort condition has been declared, set a
                 break condition. When it clears, release the break
                 condition.

                 {
                 int abrt_flg;
                 int brk_flg;

                    if(abrt_flg && !brk_flg)
                       ComSetBreak();

                    else if(!abrt_flg && brk_flg)
                       ComClrBreak();

                 }



         ----------------------------------------------------------------
         ComPutScrtch
         ----------------------------------------------------------------

         Function

                 Writes a byte to the active serial port's scratch
                 register.

         Syntax

                 #include "cport.h"
                 void ComPutScrtch(byte abyte);


         Parameters

                 abyte - The byte to be written to the scratch register.




                                        52




         Remarks

                 ComPutScrtch writes the byte value 'abyte' to the
                 active serial port's UART scratch register. Not all
                 UARTs have a scratch register.


         See also

                 ComGetScrtch


         Example

                 Use the scratch register to store a status byte.

                 #define ComSavStatus() ComPutScrtch(ComStatus())
                 #define ComOldStatus() ComGetScrtch()
                 {
                 unsigned old_stat;

                    ComSavStatus();

                    ...later on

                    old_stat = ComOldStatus();
                 }


         ----------------------------------------------------------------
         ComGetScrtch
         ----------------------------------------------------------------

         Function

                 Fetches the byte stored in the active serial port's
                 scratch register.

         Syntax

                 #include "cport.h"
                 byte ComGetScrtch(void);


         Remarks

                 ComGetScratch reads the byte in the active serial
                 port's UART scratch register. Not all UARTs have a
                 scratch register.


         Return value

                 ComGetScrtch returns the byte read from the UART
                 scratch register.




                                        53




         See also

                 ComPutScrtch


         Example

                 Use the scratch register to store a status byte.

                 #define ComSavStatus() ComPutScrtch(ComStatus())
                 #define ComOldStatus() ComGetScrtch()
                 {
                 unsigned old_stat;

                    ComSavStatus();

                    ...later on

                    old_stat = ComOldStatus();
                 }







































                                        54




         Appendix A


         Things to look out for:


         1) Since Cport is driven by hardware interrupts, input and
         output functions will work unpredictably inside a debugger.
         If a break point is set and the program is run, everything
         fuctions until the break point is reached. At that point the
         interrupts will probably cease and the transmitter and
         receiver will freeze. Needless to say, single-stepping is out
         of the question.


         2) Baud rates above 19200 require special attention because they
         are sensitive to many factors. Some of these factors are:

         ù Cable length
         ù Machine speed
         ù Type of UART used
         ù Activity of handshaking
         ù Number of open serial ports
         ù Degree of bidirectional transfer (transmitting and receiving
           simultaneously)
         ù Other interrupt activity

         The last factor, interrupt activity, includes keyboard
         activity which can be a major impedance. During critical high
         speed transfers, some interrupts can be temporarily masked
         out (disabled) at the PIC to preclude them from impeding the
         communications interrupt handler.


         3) In the small and medium memory models, the near heap where
         the queue buffers are allocated is limited. The data segment
         (globals etc.) + the stack + allocated memory (queue buffers)
         must not exceed 64K bytes. If extremely large queue(s) are
         required, the compact or large model where each queue can be
         as large as 65534 bytes must be used.

         4) The functions ComOpen, ComOpenS, ComClose and ComCloseAll
         make calls to the C functions malloc() and free().
















                                        55





         Appendix B



         Handshaking schemes


         There are number of built-in options available for implementing
         handshaking. The options can be divided into two categories.
         One is hardware handshaking and the other is software handshaking.
         In hardware handshaking, one or more of the hardware lines are
         used. In software handshaking, XON and XOFF characters are used.


         Hardware handshaking

         In hardware handshaking, any combination of the hardware signals
         RTS, DTR, DSR, CTS, and DCD can be used to achieve handshaking.
         RTS and/or DTR are used by the receiver to signal the remote device
         to suspend or resume transmitting. Similarly, DSR, CTS, and/or
         DCD can be used by the remote device's receiver to signal
         the transmitter to suspend or resume transmitting.


         Software handshaking

         In software handshaking, the control characters XON (ctrl Q)
         and XOFF (ctrl S) are used to achieve handshaking. When
         receiver software handshaking (S_RX) is enabled, XON and XOFF
         characters are transmitted to signal the remote device to
         suspend or resume it's transmission. Notice that even though
         the XON and XOFF characters are sent by the transmitter, it
         is the receiver which exercises the handshaking in order
         to preclude a receive queue overflow. In transmit software
         handshaking (S_TX), the remote device sends XON and XOFF
         characters to suspend and resume the computer's transmission.
         Notice that even though the XON and XOFF characters are received,
         it is the transmitter which is affected. Both receive and
         transmit handshaking can be enabled simultaneously.


         The receiver

         When receive software and/or hardware handshaking (DTR and/or
         RTS) are enabled the receiver monitors the length of the receive
         queue. If the length exceeds the threshold set by the function
         ComHandshake or ComOpenS, the receiver will take the appropriate
         action to signal the remote device to suspend transmitting. When
         the length of the receive queue subsequently falls below half of
         the threshold, the appropriate action is taken to signal the
         remote device to resume transmitting.


         The transmitter

         When transmit software and/or hardware handshaking (DSR, CTS,


                                        56




         and/or DCD) are enabled and the computer is signaled to suspend
         transmitting with the corresponding handshaking  enabled, the
         transmitter will stop transmitting. Subsequently, when the
         computer is signaled to resume transmitting, the transmitter will
         pick up where it left off.


         User handshaking

         Another option for implementing handshaking is for the programmer
         implement their own handshaking scheme. To accomplish this,
         Cport provides the function ComTx. ComTx enables the programmer
         to turn the transmitter on and off. When the transmitter is
         turned off, transmitting halts immediately. If any characters
         still reside in the transmit queue, they will remain there until
         the transmitter is turned back on or the transmit queue is
         flushed. More characters may be put into the transmit queue
         while the transmitter is turned off.


         Cooperation

         In any handshaking scheme it is imperative that the computer and
         the remote device recognize the handshaking scheme. For instance,
         if the remote device recognizes hardware handshaking and the
         computer does not, the computer will ignore any requests by the
         remote device to suspend transmitting. If the remote device
         recognized software handshaking and the computer did not, bogus
         XON and XOFF characters might be found to be corrupting the
         received data.





























                                        57




        Appendix C


         The UART (Universal Asynchronous Receiver/ Transmitter) chip


         The UART, a single integrated circuit chip, is the backbone
         of serial communications in computers today. Serial
         communications in IBM and compatible computers is based on the
         National Semiconductor family of UARTs. These chips include:

                 INS8250
                 INS8250-B
                 INS8250A
                 INS82C50A
                 NS16450
                 NS16C450
                 NS16550A


         The latest and greatest is the NS16550A which features transmitter
         and receiver FIFO's. If a NS16550 UART is detected when a serial
         port is opened, Cport will automatically take advantage of it's
         advanced features. This feature greatly improves performance.



































                                        58




        Appendix D


         The RS-232 Standard ?!!


         Voltages, logic levels and pin assignments of the RS-232
         standard are more or less adhered to. However, the way the
         RS-232 standard prescribes data transfers to be controlled,
         more commonly know as handshaking, does not work for computers.
         This can lead to much confusion and frustration when trying
         to connect two serial communications devices from different
         manufacturers.

         The book "The RS-232 Solution" by Joe Campbell addresses
         this problem and includes a number of case studies. It is
         recommended reading for both the novice and expert programmer.










































                                        59




    Appendix E


         Cport v1.30 Registration Form

         Name: ______________________________________________________

         Company: ___________________________________________________

         Address: ___________________________________________________

         City: ____________________________  State: _________________

         Zip Code: _________________  Phone # : _____________________

         CompuServe # : _____________________________________________

         How did you acquire Cport ? ________________________________

         What functions do you find most useful ?____________________

         ____________________________________________________________

         What functions do you find least useful ?___________________

         ____________________________________________________________

         What functions, not in Cport, would you like to see ?_______

         ____________________________________________________________

         What other types of libraries would you find useful ? _____

         __Game Port  __Expanded Memory  __IEEE/GPIB  __Sound effects

         Others______________________________________________________

         Other comments ?____________________________________________


         Registration                                      $ 35.00

         California residents add sales tax ( 8.25% )      $________

         Shipping inside continental U.S.   ( $ 2.00 )
         Shipping outside continental U.S.  ( $ 5.00 )     $________


                                                  Total:   $________
         All Payments Must be in U.S. Dollars

         Make check or money order payable to:    Bri Productions
                                                  P.O. Box 7121
                                                  Fremont, CA 94537-7121





                                        60