mxms.doc       copyright 1991 by Thomas Kellar





/* reset the mouse and turn on the mouse cursor (in polled mode)
 * checks if there is an address at the mouse interrupt before
 * doing the reset. This must be called prior to any use of
 * the mouse
 *
 *  call by     return_int = mreset();
 *
 *  returns with 1 if successful
 *  returns with 0 if not successful
 */

int mreset(void);



/* turn the mouse cursor on
 *
 *    call by         mcursor_on();
 *
 * called by mreset() and msave() and mrestore()
 *
 * returns no value
 *
 */

void mcursor_on(void);


/* turn the mouse cursor off
 *
 *   call by        mcursor_off();
 *
 * called by mrestore and msave()
 *
 * returns no value
 */

void mcursor_off(void);





/* initialize mouse interrupt data capture
 *
 *  input the offset and segment address of the buffer to put the
 *   data into and the size in bytes of the buffer that is available
 *   to the interrupt routine.  The interrupt data capture which is
 *   initialized by this call will not fill the buffer beyond size bytes
 *   but will stop putting data in if it fills up.  Each interrupt
 *   requires 8 bytes of storage (4 words).
 *
 * call by    mintial(mouse_buffer_offset,mouse_buffer_segment,size);
 *
 * offset is an unsigned integer value that is the address of the buffer
 *
 * segment is the segment address (unsigned integer)
 *
 * size is an unsigned integer number of bytes in the buffer
 *
 *   Note that the buffer was should be constructed from a far memory
 *   buffer from which you can obtain its far address
 *
 *
 * returns nothing
 *
 */

void minitial(unsigned offset,unsigned segment,unsigned size);



/* extract the interrupt stored data from the buffer of data whos
 * address was passed to minitial(,);
 *
 * call by    while (!mgetint(&d1,&d1,&d3,&d4))     ;   wait
 *
 * returns d1,d2,d3,d4 == condition mask (what type data),
 *                        button state,
 *                        horizontal cursor position, &
 *                        vertical cursor position     respectively
 *
 *  for d1:   if ( (d1 & 0x01) == 0x01) position change
 *            if ( (d1 & 0x02) == 0x02) left hand button press
 *            if ( (d1 & 0x04) == 0x04) left hand button release
 *            if ( (d1 & 0x08) == 0x08) right hand button press
 *            if ( (d1 & 0x10) == 0x10) right hand button release
 *
 * returns 1 if data is valid
 *         0 if no valid data is present (no interrupts)
 *
 */

int mgetint(int *ps,int *status,int *x,int *y);






/* get mouse driver version number
 *
 *   call by   return_int = mgetver();
 *
 *   returns with the 16 bit BCD version number
 *  e.g.   %04X => 0704 == 7.04 release (8.0 is latest as to now)
 *
 */

int mgetver(void);



/* get mouse type and IRQ
 *
 *  call by  type = mgettype();
 *
 *   returns     xxyy   a 16 bit integer of BCD digits with
 *
 *    xx == 1 for bus mouse; 2 for serial mouse; 3 for Inport mouse;
 *          4 for PS/2 mouse; and 5 for HP mouse;
 *
 *    yy == 0 for PS/2; otherwise the IRQ number
 *
 */

int mgettype(void);



/* set interrupt rate (for the so-called InPort mouse only)
 *
 *  call by     msetintr(interrupts_per_second);
 *
 * returns nothing
 *
 */

void msetintr(int rate);






/* set the display page input page number for the mouse
 *
 * input the page number
 *
 * call by      msetpage(2);              2 is the crt page number
 *
 * returns nothing
 */

void msetpage(int page);



/* get the display page number
 *
 *  call by    video_page_integer = mgetpage();
 *
 *  returns the hardware video page
 *
 */

int mgetpage(void);



/* get mouse button press information-with out the coordinates
 *
 * input the passed button number
 * return the number of button presses (0 or more)
 *
 * call by  if (mgetbp(0) > 0) printf("Pressed left");
 *
 */

int mgetbp(int button);






/* get button press information
 * input the passed to it button number (0 == left, 1 == right)
 *
 *    input by value the button number
 *    input by address e.g.    with int    x,y;
 *
 *    call by   Nbuttonpresses = mgetpress(0,&x,&y);   left button
 *
 *  returns the number of button presses for the requested button
 *  and the coordinates of the mouse at the time of the last push
 */

int mgetpress(int button,int *x,int *y);




/* get button release information
 * passed the number of the button  0 == left  1 == right
 * return the number of releases
 *
 * call  by  left_released = mgetrelease(0,&x,&y);
 *
 *  returns in left_released the number of releases of the button in
 *  question since the last call  (range 0..65535)
 *
 * returns the number of button releases and the coodinates of the
 * mouse at the last one
 */

int mgetrelease(int button,int *x, int *y);






/* get status and current mouse position
 *
 * call by   status = mgetstatus(&x,&y);
 *
 *  returns the current screen position in x-y coordinates and
 *
 *  the button status which is a binary number with
 *   status == 00000001 for the left-hand button pressed
 *             00000010 for the right-hand button pressed
 *             00000011 for both buttons pressed
 *
 */

int mgetstatus(int *x,int *y);




/* position the mouse to the center of the current screen factoring
 * in the current constraints set upon the mouse cursor movement
 *
 * (see mconstrain)
 *
 * call by    mcenter();
 *
 * returns nothing
 *
 *  only works with mouse driver 7.05 or later!!!
 *
 */

void mcenter(void);






/* constrain the mouse to screen coordinates passed
 * x1,x2,y1,y2     no checking of validity is done
 * but if if the x1 > x2 then they are exchanged and
 * the same for y1 and y2
 *
 *  call by   mconstrain(xlow,xhigh, ylow,yhigh);
 *    where xlow is the left-right-horizontal coordinates (eg 0..639)
 *    and ylow is the up-down-vertical coordinate (eg 0..479)
 *    pass by values
 *
 * returns nothing
 */

void mconstrain(int xl,int xh,int yl,int yh);




/* set mouse cursor position on the screen
 *
 *  call by    msetpos(x,y);    or msetpos(123,(x2-x1)/2);
 *
 * returns nothing
 *
 */

void msetpos(int x,int y);






/* save the current mouse state
 *
 * call by    if (msave()) printf("Mouse state saved!");
 *
 * multiple saves can be done in a row but the same number of
 * restores must be done to offset the saves (up to 100 max):
 *    msave();
 *    msave();       allows up to 100 msave() in a row
 *    ...
 *    mrestore();
 *    mrestore();
 *
 * returns false (0) of failure true (1) if success
 *
 * uses runtime allocated far memory
 * calls mcursor_on and mcursor_off
 *
 */

int msave(void);




/* restore the mouse state that was saved by the call msave();
 *
 * call by      mrestore();
 *
 * deallocates the far memory
 * calls mcursor_on and mcursor_off
 */

void mrestore(void);




/* cmouse calls the int33 interrupt with and returns with values
 * appropriate to each call
 *
 * call by   cmouse(&type,&v1,&v2,&v3);
 *
 * returns various items depending on the type of call
 *
 */

void cmouse(int *type,int *v1,int *v2,int *v3);