-------------------------------------------------------------------------------
 TDVIDEO.DLL
-------------------------------------------------------------------------------

   In order for the text-based Windows debugger (TDW) and profiler
   (TPROFW) to switch from Window's graphics mode to text mode, some
   information about the graphics mode must be known.  Right now, TDW
   will support all of the standard CGA/EGA/VGA modes up to and
   including mode 12h (640x480x16).  Since there are all sorts of video
   cards out there capable of supporting higher resolution modes
   (640x480x256 on up to 1024x768x256 usually refered to as 'SuperVGA'
   modes), TDW will have to be aware of them to do its switch.  The
   methods used to access these SuperVGA modes all vary from card to
   card (actually the chipset that the card uses), and in order to
   provide support for these modes, we have designed the windows
   debugger and profiler to make use of an external DLL which will
   handle the card-spacific interface.  Therefore to support a new card,
   you simply write a new DLL.  The DLL's that come with version 3.0 of
   the Borland C++ package will support ATI's VGA Wonder+ cards and any
   card that uses the TSENG (ET-3000/ET-4000) chipset (of which there
   are many).  For more information on how to use either of these two
   DLL's that are provided, refer to the README file in the root
   BORLANDC directory.

   The theory behind the TDVIDEO DLLs is, starting with version 3.0, TDW
   (or 2.0 and above for TPROFW) will look for a file called TDVIDEO.DLL
   in the same directory as TDW.EXE (usually the BIN directory).  If it
   is found, TDW attempts to do a LoadLibrary on it.  It then makes Proc
   Instances for each of the nine functions and if any of them are not
   found, TDW tells you the missing function in a MessageBox, and exits
   out.  If the DLL succeeds in loading, a call is made to VideoInit().
   This is where you should do all card/mode checking and dynamic memory
   allocation (if needed). TDW then calls the appropriate functions
   depending on what the user is doing.  As soon as you tell TDW to
   exit, VideoDone() is called which should free all allocated memory.