This is information taken from literature sent by Brown-Wagh Publishing,
distributers of the Sound Blaster Pro.

Sound Blaster Pro card- "The Multimedia sound standard"
Creative Labs, Inc.
2050 Duane Ave.
Santa Clara, CA 95054
Tel: (408) 986-1461  Fax: (408) 986-1777
Distributed by:
Brown-Wagh Publishing
130-D Knowles Dr.
Los Gatos, CA 95030
Tel: (408) 378-3838  (800) 451-0900

Hardware features:

Stereo DACs - 8 bit
- Sound Blaster compatible in Mono mode
- ADPCM Decompression in hardware(2:1, 3:1, and 4:1)
- DMA transfer (shareable) on channel 0, 1, or 3 selectable by jumper
- Selectable sampling rates:  4K - 44.1KHz

Stereo ADCs - 8 bit
- Sound Blaster compatible in Mono mode
- DMA transfer (shareable) on channel 0, 1, or 3 selectable by jumper
- Selectable sampling rates:  4K - 44.1KHz
- Support recording from Microphone, Stereo Line-IN and CD-Audio

Stereo Digital/Analog Mixer
- Mixing of all audio sources: Stereo DAC, Stereo FM, Microphone, Stereo
  Line-In, CD-Audio and PC Internal Speaker
- Full software control of fade-in, fade-out, pan, volume, left/right
  steering and Mic mixing
- Multiple level volume controls on digitized sound:
  DAC            FM Music     Microphone
  CD-Audio       Line-In      Master Volume

Stereo FM Music Syntesizers
- Twin FM chips giving maximum 22 voices
- Power-on default to Mono mode for full compatibility with Sound Blaster
  and Adlib

MIDI Interface
- Sound Blaster Compatible
- MIDI time-stamp for Multimedia Extension
- 64-byte FIFO
- Sharing Joystick Port
- MIDI Adaptor and cables for standard MIDI cabling included

CD-ROM Interface
- 8-bit DMA transfer on channel 1 or 3 selectable by jumper
- Internal connector for CD-Audio
- Support internal and external CD-ROM drives

Joystick Port
- Standard PC Joystick Port for 1 or 2 joysticks(Y-cable Optional)

Microphone Automatic Gain Control (AGC) Amplifier
- Hardware AGC for optimum Microphone sensitivity
- Input Impedance 600 ohms
  Sensitivity: 10 - 100m V

Output Power Amplifier
- 4 watts per channel
- Load Impedance 4 ohms
- Mini stereo jack to RCA conversion cable included

Manual Volume Control
- Volume control knob to set output level
- Easily accessible and durable

Jumper Selections
- Interrupt selection        : IRQ 2, 5, 7, 10
- DMA selection              : channel 0, 1 or 3
- I/O address selection      : 220H or 240H

On-board Connector Pins
- PC Internal Speaker Input
- Line-Out
- Microphone Input
- CD-Audio Input
- CD-ROM Interface

Software Included:

Bundled Software 1: SB VOICE EDITOR
This is a powerful program that supports stereo recording, compression and
editing of voice file of unlimited size.  It displays the waveform with
zooming and allows cut-and-paste.  It creates echo and reverb.  It can also
insert marker and repeat commmands.  Playback of the voice files in
background is possible using the utilities.

Bundled Software 2: FM INTELLIGENT ORGAN
This powerful, easy to use organ software lets you play and learn to play
orchestra-like music using only ONE finger on your PC keyboard.  Background
accompaniments and rhythms are added automatically.  No music knowledge
required.  And now play from your MIDI keyboard too.

Bundled Software 3: SBTALKER
A high value memory resident module that makes your computer talk directly
from ASCII text supplied.  It speaks English from an unlimited vocabulary
dictionary.  SBTALKER comes with the insrutable DR SBAITSO AI software.
Consult DR SBAITSO about any of your problems and hear him reply you.
Loads of Fun.

Bundled Software 4: MIDI Sequencer Sp Pro
Sp Pro includes all of the essential features you'll need to create serious
music composition.  More importantly, it offers a wide range of options so
that you won't lose interest!  In fact, Sp Pro's extensive list of features
includes many of those found in the "Pro" versions of other programs.

Bundled Software 5: CD MUSIC PLAYER
Controls the playing of standard compact disc with CD-ROM drive.  Program
comes with a full feature control panel - Play, Next/Last Track, Pause,
Fast-Forward, Rewind and Stop.

Bundled Software 6: MMPLAY PRESENTATION
MMPlay integrates graphic animations with the sound capabilities of SB Pro:
FM Music, Digitized Voice and CD Audio.  THis utility supports
synchronisation, fading and mixing.


Suggested Retail Price : $299.95
Upgrade from Sound Blaster to Sound Blaster Pro : $199.95 + old Sound
Blaster
Release date: Late August - Early September


DOS software drivers and Windows DLL are included.
All specifications are subject to change without prior notice.