NWDOSODI.DOC           07/10/91
           Copyright 1991, Compaq Computer Corporation.
                                
  NETWARE DOS ODI WORKSTATION DRIVER INSTALLATION INSTRUCTIONS


CONTENTS

1. INTRODUCTION
2. FEATURES
3. FILES
4. SYSTEM REQUIREMENTS
5. INSTALLATION
6. INSTALLING NOVELL LAN WORKPLACE v4.0 FOR DOS
7. SOURCE ROUTING SUPPORT
8. NETWIRE


1. INTRODUCTION

   This file details the installation of the NetWare DOS ODI driver
for the Compaq 32-Bit DualSpeed Token Ring Controller.


2. FEATURES

     1. Provides improved performance over previous releases of the
        driver.

     2. Source Routing is supported.

     3. Microsoft Windows 3.0 is supported

     4. Compatable with Novell LAN Workplace 4.0 for DOS.


3. FILES

  NWDOSODI.DOC      - This file
  CPQTOKNW.COM      - NetWare DOS ODI workstation driver
  DOSNET.CFG        - Sample configuration file


4. SYSTEM REQUIREMENTS

  This device driver requires:
      *   Any COMPAQ EISA computer with the COMPAQ 32-bit DualSpeed 
          Token Ring controller installed. The system must have
          been configured using the COMPAQ EISA Configuration
          Utility.  

      *   NetWare DOS ODI software, included with the NetWare
          operating system.


5. INSTALLATION

The DOS ODI workstation driver allows operation of multiple
protocols on a single network board. This allows communication with
a variety of mainframes, workstations, and file servers, without
rebooting your workstation.

In the following procedure, refer to section of your manual on
installing the NetWare ODI Shell for DOS. You must fist create a
master workstation diskette the contains copies of the files
necessary to boot one type of workstation. Then you will either
make individual workstation boot diskettes for use with each
workstation or copy the files from the master workstation diskette
to the hard disk from which a workstation boots.

To install the device driver for the token ring controller,
following these steps:

     1.   Create a system diskette by using the MS-DOS
          FORMAT command with the /S parameter.

     2.   Copy the desired shell file (NET3.COM, for
          example) from the root directory of the DOS/DOS
          ODI WORKSTATION SERVICES diskette to the master
          workstation diskette (the diskette you created
          in step 1).

     3.   Copy the following files to the master
          workstation diskette: LSL.COM and the protocol
          stack file (IPXODI.COM, for example).

     4.   Copy the CPQTOKNW.COM file to the master
          workstation diskette.

     5.   Create the AUTOEXEC.BAT file to have the
          drivers in the order shown below.  The
          following is a sample AUTOEXEC.BAT file:

               LSL
               CPQTOKNW
               IPXODI
               NET3

Proceed to the follow steps if you network supports source routing.
Otherwise, you are finished with the installation procedure.

     6.   Copy the source routing driver (ROUTE.COM) from
          the root directory of the DOS/DOS ODI
          WORKSTATION SERVICES diskette to the master
          workstation diskette.

     7.   Create the AUTOEXEC.BAT file shown below if
          your network supports source routing.  Refer
          to the IBM Token-ring section of the NetWare
          386 Supplements manual for more information.

               LSL
               CPQTOKNW  
               ROUTE
               IPXODI
               NET3


The NET.CFG file is optional for loading the device driver on the
first controller in the system, but it is required for loading
drivers on additional controllers.  Refer to your NetWare
Installation manuals for more information.  The configuration
options used by the CPQTOKNW.COM device driver are as follows:

FRAME frame_type    The variable frame_type can be token-ring or
                    token-ring_snap.

NODE ADDRESS x      Burn-in node address override.  The variable
                    x must be 12 hexadecimal digits.

NO EARLYRELEASE     Disables early token release.

PROTOCOL name ID    Specifies which protocol is used with the
                    driver.

SEND RETRIES x      Maximum number of retries.

SLOT x              Slot override.


The following are the defaults if the keywords are not supplied:

     a. Use Burn-In Address. 
     b. Early token release feature will be enabled at 16Mbps.
     c. Protocol is IPX, protocol ID is e0. 
     d. Frame type is TOKEN-RING.
     e. Use the 1st COMPAQ 32-Bit DualSpeed Token Ring Controller
        found on the EISA bus.


6. INSTALLING LAN WORKPLACE v4.0 FOR DOS

     NET.CFG is an optional file then can be used when installing
     Novell DOS ODI Workstation.  To use the TCP/IP protocol stacks
     from Novell LAN Workplace v4.0 for DOS with the COMPAQ
     DualSpeed Token Ring Controller DOS ODI driver, the
     TOKEN-RING_SNAP frame type must be specified in the NET.CFG
     file.  The following are examples for using with TCP/IP
     protocol stack in the NET.CFG file.

     a. IPX/SPX using the TOKEN-RING frame type and TCP/IP using
        the TOKEN-RING_SNAP frame type.

      This is the recommended method of installing other protocol
      stacks other than IPX.

     Example:

        LINK DRIVER CPQTOKNW
           FRAME TOKEN-RING
           FRAME TOKEN-RING_SNAP

     b. Both IPX/SPX and TCP/IP using the TOKEN-RING_SNAP frame
     type.

     This method is interoperable with Netware 386 v3.x.  Netware
     286 v2.x  does not support the TOKEN-RING_SNAP frame type. 
     On Netware 386 v3.x, the TOKEN-RING_SNAP frame type must be
     loaded before to allow DOS ODI Workstation access to the
     server.

     Example:
                
        LINK DRIVER CPQTOKNW
           FRAME TOKEN-RING_SNAP


7. SOURCE ROUTING SUPPORT

     Source routing is a method of routing data across multiple
     networks through bridges. To enable the workstation to pass
     data through a source routing bridge, the workstation must be
     running the source routing program, route.com from Novell.
     This program is necessary only if external source routing
     bridges are present on the network. The source routing
     program, file route.com, is available on the Novell NetWare
     DOS Workstation Generation diskette. The Novell source routing
     program and installation instructions are also available on
     Compuserve NetWire under NOVA forum in library 8 (Novell
     Patch/Drv'r) in the TRN050.ZIP file.

     See the Novell NetWare documentation for more information on
     source routing.

     The following is an example of how to load source routing on
     the workstation. The following lines should be placed in the
     workstation autoexec.bat file.

     lsl
     cpqtoknw
     route
     ipxodi
     net3


8. NETWIRE

     The NetWare DOS ODI driver files for the COMPAQ 32-Bit
     DualSpeed Token Ring Controller reside on Compuserve NetWire
     under NOVA forum in library 11 (or library 17 for new uploads)
     in the CPQTR2.ZIP file.